## Slide 1
Mohammed Alser
Accelerating Genome Analysis A Primer on an Ongoing Journey
Senior Researcher and Lecturer
ETH Zurich
August 29 – September 1
Virtual
Monday, August 30 at 4:50 PM ET

## Slide 2: Accelerating Genome Analysis A Primer on an Ongoing Journey
Mohammed Alser
ETH Zurich
@mealser
RECOMB 2021 - Highlights
30 August 2021

## Slide 3: How to Analyze a Genome?
>CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCCAAGAGTTGCAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTAGCCAGAATGGTTGTGGGATGGGAGCCTCTGTGGACCGACCAGGTAGCTCTCTTTTCCACACTGTAGTCTCAAAGCTTCTTCATGTGGTTTCTCTGAGTGAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTTTTCATGTCAAGGACCTAATGTAGCTATACTGAACGTTATCTAGGGGAAAGATTGAAGGGGAGCTCTAAGGTCAACACACCACCACTTCCCAGAAAGCTTCTTCA……
  machine gives the complete sequence of genome as output
NO
Notes: Until today, there is no machine takes genomic sample and produces the full sequence of the donor.
Why? supercoiled structure, small cell’s size, sensitivity to 1 base, DNA length.

## Slide 4: Genome Analysis in Real Life
Current sequencing machine provides
small randomized fragments
of the original DNA sequence
Alser+, "Technology dictates algorithms: Recent developments in read alignment", Genome Biology, 2021
Read Mapping
Reads

## Slide 5: Good Luck in Solving the Puzzle
https://www.pacb.com/smrt-science/smrt-sequencing/hifi-reads-for-highly-accurate-long-read-sequencing/
Reads
Reference genome
Notes: Rhinoceros

## Slide 6: Analysis is Bottlenecked in Read Mapping!!
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGA
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Human whole
genomes
Human
1
Illumina NovaSeq 6000
48
at 30× coverage
in about 2 days
genome
32 CPU hours
on a 48-core processor
Chart: 
| Read Mapping | Others
Sales | 0.71 | 0.29
Goyal+, "Ultra-fast next generation human genome sequencing data processing using DRAGENTM bio-IT processor for precision medicine”, Open Journal of Genetics, 2017.
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 7
Need for Speed

## Slide 8: Personalized Medicine for Critically Ill Infants
Farnaes+, “Rapid whole-genome sequencing decreases infant morbidity and cost of hospitalization”, NPJ Genomic Medicine, 2018
rWGS can be performed in 2-day (costly) or 5-day time to interpretation.
Diagnostic rWGS for infants
  Avoids morbidity
  Reduces hospital stay length by 6%-69%
  Reduces inpatient cost by $800,000-$2,000,000.
Notes: There is also an urgent need for rapidly incorporating clinical sequencing into clinical practice for diagnosis of genetic disorders in critically ill infants [53, 54, 55, 56]. While early diagnosis in such infants shortens the clinical course and enables optimal outcomes [57, 58, 59], it is still challenging to deliver ecient clinical sequencing for tens to hundreds of thousands of hospitalized infants each year [60].

## Slide 9: Scalable Genome Analysis
“From 2019, all seriously ill children in UK will be offered whole genome sequencing as part of their care”

## Slide 10: Population-Scale Microbiome Profiling
Danko+, "A global metagenomic map of urban microbiomes and antimicrobial resistance", Cell, 2021

## Slide 11: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundances of microbes in a sample
Understanding genetic variations
Rapid surveillance of disease outbreaks
Developing personalized medicine
And many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 12
What makes
read mapping
a bottleneck?

## Slide 13: A Tsunami of Sequencing Data
A Tera-scale increase in sequencing production in the past 25 years

## Slide 14: Lack of Specialized Compute Capability
Specialized Machine
for Sequencing
General-Purpose Machine
for Analysis
FAST SLOW

## Slide 15: Data Movement Dominates Performance
Microprocessor
Main Memory
Storage (SSD/HDD)
Sequencing
Machine
Data movement dominates performance and is a major system energy bottleneck (accounting for 40%-62%)
✻ Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS 2018
★ Kestor et al., “Quantifying the Energy Cost of Data Movement in Scientific Applications,” IISWC 2013
☆ Pandiyan and Wu, “Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms,” IISWC 2014
Data Movement
Single memory request consumes >160x-800x more energy compared to performing an addition operation
Notes: generates a large amount of data movement between the CPU and main memory. The CPU accesses off-chip main memory through a pin-limited bus known as the memory channel, and a high amount of data movement across the memory channel is extremely costly in terms of both execution time and energy

## Slide 16: Read Mapping Execution Time
ONT FASTQ size: 103MB (151 reads), Mean length: 356,403 bp, std: 173,168 bp, longest length: 817,917 bp
Chart: 
| KSW2 | Seed Chaining | Sorting Seeds | Collect Matching Seeds | Collect Minimizers
Sales | 0.46 | 0.16 | 0.29 | 0.08 | 0.02
>60%
of the read mapper’s execution time is spent in sequence alignment
minimap2

## Slide 17: Large Search Space for Mapping Location
of candidate locations have high dissimilarity with a given read
98%
Cheng et al, BMC bioinformatics (2015)
Xin et al, BMC genomics (2013)
Notes: We also observe that an overwhelming majority of the candidate locations have high dissimilarity with a given read, which leads to waste the time verifying these locations.
H. Cheng, et al., "BitMapper: an efficient all-mapper based on bit-vector computing," BMC bioinformatics, vol. 16, p. 1, 2015.
H. Xin, et al., "Accelerating read mapping with FastHASH," BMC genomics, vol. 14, p. S13, 2013.

## Slide 18
We need intelligent algorithms and intelligent architectures
that handle data well
Notes: However,

## Slide 19: Accelerating Read Mapping
Alser+, “Accelerating Genome Analysis: A Primer on an Ongoing Journey”, IEEE Micro, 2020.

## Slide 20: Our Contributions
GateKeeper [Bioinformatics’17]
MAGNET [AACBB’18]
Shouji [Bioinformatics’19]
SneakySnake [Bioinformatics’20]
GenASM [MICRO 2020]
SneakySnake [IEEE Micro’21]
Specialized Pre-alignment Filtering Accelerators (GPU, FPGA)
GRIM-Filter [BMC Genomics’18]
GateKeeper-GPU [arXiv’21]
Near-memory/In-memory
Pre-alignment Filtering
Near-memory Sequence Alignment
Microprocessor
Main Memory
Storage (SSD/HDD)
Sequencing Machine
GenASM [MICRO 2020]

## Slide 21: Specialized Hardware for Pre-alignment Filtering
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 22: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Key idea:
  Approximate edit distance calculation is similar to Single Net Routing problem in VLSI chip
VLSI chip layout

## Slide 23: Key Results of SneakySnake
  SneakySnake is up to four orders of magnitude more accurate than Shouji (Bioinformatics’19) and GateKeeper (Bioinformatics’17)
  Using short reads, SneakySnake accelerates Edlib (Bioinformatics’17) and Parasail (BMC Bioinformatics’16) by
    up to 37.7× and 43.9× (>12× on average), on CPUs
    up to 413× and 689× (>400× on average) with FPGA/GPU acceleration
  Using long reads, SneakySnake accelerates Parasail and KSW2 by 140.1× and 17.1× on average, respectively, on CPUs

## Slide 24: Near-memory Pre-alignment Filtering
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 25: Near-memory SneakySnake
Problem: Read Mapping is heavily bottlenecked by data movement from main memory
Solution: Perform read mapping near where data resides (i.e., near-memory)
We carefully redesigned the accelerator logic of SneakySnake to exploit near-memory computation capability on modern FPGA boards with high-bandwidth memory
Xilinx Virtex UltraScale+ HBM VCU128 FPGA
FPGA + high-bandwidth memory on the same package substrate

## Slide 26: Key Results of Near-memory SneakySnake
Near-memory pre-alignment filtering improves performance and energy efficiency by 27.4× and 133×, respectively,
over a 16-core (64 hardware threads) IBM POWER9 CPU

## Slide 27: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lightning Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 28: Near-memory GenASM Framework
Our goal: Accelerate approximate string matching (ASM) by designing a fast and flexible framework, which can accelerate multiple steps of genome sequence analysis.
Key ideas: Exploit the high memory bandwidth and the logic layer of 3D-stacked memory to perform highly-parallel ASM in the DRAM chip itself.
Modify and extend Bitap1,2, ASM algorithm with fast and simple bitwise operations, such that it now:
  Supports long reads
  Supports traceback
  Is highly parallelizable
Co-design of our modified scalable and memory-efficient algorithms with low-power and area-efficient hardware accelerators
[1] R. A. Baeza-Yates and G. H. Gonnet. "A New Approach to Text Searching." CACM, 1992.
[2] S. Wu and U. Manber. "Fast Text Searching: Allowing Errors." CACM, 1992.

## Slide 29: Key Results of the GenASM Framework
Read Alignment
116× speedup, 37× less power than Minimap2 (state-of-the-art SW)
111× speedup, 33× less power than BWA-MEM (state-of-the-art SW)
3.9× better throughput, 2.7× less power than Darwin (state-of-the-art HW)
1.9× better throughput, 82% less logic power than GenAx (state-of-the-art HW)
Pre-Alignment Filtering
3.7× speedup, 1.7× less power than Shouji (state-of-the-art HW)
Edit Distance Calculation
22–12501× speedup, 548–582× less power than Edlib (state-of-the-art SW)
9.3–400× speedup, 67× less power than ASAP (state-of-the-art HW)
Notes: GenASM is flexible and can be used to accelerate multiple use cases.
In this work, we evaluate three use cases in detail: [CLICK] read alignment, [CLICK] pre-alignment filtering and [CLICK] edit distance calculation.
We find that, for all the three use cases [CLICK] [CLICK] [CLICK], GenASM is significantly more efficient in terms of both speed and power consumption than state-of-the-art software and hardware baselines

## Slide 30
Adoption of
hardware accelerators
in genome analysis

## Slide 31: Illumina DRAGEN Bio-IT Platform
Processes whole genome at 30x coverage in ~25 minutes with hardware support for data compression
FPGA board(s)
https://emea.illumina.com/products/by-type/informatics-products/dragen-bio-it-platform.html

## Slide 32: NVIDIA Clara Parabricks
https://developer.nvidia.com/clara-parabricks
GPU board(s)

## Slide 33
Computing
is Still Bottlenecked by
Data Movement

## Slide 34: Adoption Challenges of Hardware Accelerators
Accelerate the entire read mapping process rather than its individual steps (Amdahl’s law)
Reduce the high amount of data movement
  Working directly on compressed data
  Filter out unlikely-reused data at the very first component of the compute system
Develop flexible hardware architectures that do NOT conservatively limit the range of supported parameter values at design time
Adapt existing genomic data formats for hardware accelerators or develop more efficient file formats

## Slide 35: Adoption Challenges of Hardware Accelerators
Maintaining the same (or better) accuracy/sensitivity of the output results of the software version
  Using heuristic algorithms to gain speedup!
High hardware cost
Long development life-cycle for FPGA platforms

## Slide 36: Where is Read Mapping Going Next?
>CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCCAAGAGTTGCAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTAGCCAGAATGGTTGTGGGATGGGAGCCTCTGTGGACCGACCAGGTAGCTCTCTTTTCCACACTGTAGTCTCAAAGCTTCTTCATGTGGTTTCTCTGAGTGAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTTTTCATGTCAAGGACCTAATGTAGCTATACTGAACGTTATCTAGGGGAAAGATTGAAGGGGAGCTCTAAGGTCAACACACCACCACTTCCCAGAAAGCTTCTTCA……
  machine gives the complete sequence of genome as output
NO
What if we have such a machine?!
Think about comparing large genomes together as in whole-genome alignment, metagenomics, pangenomics, …
Notes: Will 100%-accurate genome-long reads alleviate/eliminate the need for read mapping?

## Slide 37: Open Questions
How and where to enable
fast, accurate, cheap,
privacy-preserving, and exabyte-scale analysis of genomic data?

## Slide 38: Processing Genomic Data Where it Makes Sense
(General Purpose) GPUs
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
FPGAs
Modern systems
?
Sequencing
Machine
Single memory request consumes >160x-800x more energy compared to performing a complex add operation

## Slide 39: Near-memory Pre-alignment Filtering
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.

## Slide 40: Read Mapping in 111 pages!
Mohammed Alser, Jeremy Rotman, Dhrithi Deshpande, Kodi Taraszka, Huwenbo Shi, Pelin Icer Baykal, Harry Taegyun Yang, Victor Xue, Sergey Knyazev, Benjamin D. Singer, Brunilda Balliu, David Koslicki, Pavel Skums, Alex Zelikovsky, Can Alkan, Onur Mutlu, Serghei Mangul
"Technology dictates algorithms: Recent developments in read alignment"
Genome Biology, 2021
[Source code]
In-depth analysis of 107 read mappers (1988-2020)

## Slide 41: More on Read Mapping
https://www.youtube.com/watch?v=ygmQpdDTL7o

## Slide 42: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 43: Prior Research on Genome Analysis (1/2)
Alser + "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs." to appear in Bioinformatics, 2020.
Senol Cali+, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis", MICRO 2020.
Alser+, "Technology dictates algorithms: Recent developments in read alignment", to appear in Genome Biology, 2021.
Kim+, "AirLift: A Fast and Comprehensive Technique for Translating Alignments between Reference Genomes", arXiv, 2020
Alser+, “Accelerating Genome Analysis: A Primer on an Ongoing Journey”, IEEE Micro, 2020.

## Slide 44: Prior Research on Genome Analysis (2/2)
Firtina+, “Apollo: a sequencing-technology-independent, scalable and accurate assembly polishing algorithm”, Bioinformatics, 2019.
Alser+, “Shouji: a fast and efficient pre-alignment filter for sequence alignment”, Bioinformatics 2019.
Kim+, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies”, BMC Genomics, 2018.
Alser+, "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping”, Bioinformatics, 2017.
Alser+, "MAGNET: understanding and improving the accuracy of genome pre-alignment filtering”, IPSI Transaction, 2017.

## Slide 45: Accelerating Genome Analysis A Primer on an Ongoing Journey
Mohammed Alser
ETH Zurich
@mealser
RECOMB 2021 - Highlights
30 August 2021

## Slide 46: Backup Slides

## Slide 47: The Effect of Pre-Alignment (Theoretically)
Chart: Pre-alignment rejected mapping percentage and speed compared to alignment step
| 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 2x | 4x | 8x | 16x | 32x | 64x | 128x | 256x
Total processing time without pre-alignment (sec) | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000
Chart: Pre-alignment rejected mapping percentage and speed compared to alignment step
| 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 2x | 4x | 8x | 16x | 32x | 64x | 128x | 256x
Total processing time without pre-alignment (sec) | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000
Total processing time with pre-alignment (sec) | 5000 | 7000 | 9000 | 11000 | 13000 | 2500 | 4500 | 6500 | 8500 | 10500 | 1250 | 3250 | 5250 | 7250 | 9250 | 625 | 2625 | 4625 | 6625 | 8625 | 312.5 | 2312.5 | 4312.5 | 6312.5 | 8312.5 | 156.25 | 2156.25 | 4156.25 | 6156.25 | 8156.25 | 78.125 | 2078.125 | 4078.125 | 6078.125 | 8078.125 | 39.0625 | 2039.0625 | 4039.0625 | 6039.0625 | 8039.0625
Ideal processing time for 90% pre-alignment rejection percentage | 6000 | 6000 | 6000 | 6000 | 6000 | 3500 | 3500 | 3500 | 3500 | 3500 | 2250 | 2250 | 2250 | 2250 | 2250 | 1625 | 1625 | 1625 | 1625 | 1625 | 1312.5 | 1312.5 | 1312.5 | 1312.5 | 1312.5 | 1156.25 | 1156.25 | 1156.25 | 1156.25 | 1156.25 | 1078.125 | 1078.125 | 1078.125 | 1078.125 | 1078.125 | 1039.0625 | 1039.0625 | 1039.0625 | 1039.0625 | 1039.0625
assuming alignment processes 100 Mappings/sec
Filter+
Alignment
Target
Pre-alignment saves more than
40% to 80%
of the total processing time
Notes: What effect pre-alignment has on overall execution time? Well, that depends on how much and how fast it can remove incorrect mappings
We make
two key observations. (1) The reduction in the end-to-end processing time of the
alignment step largely depends on the accuracy and the speed of the pre-alignment
lter. (2) Pre-alignment ltering can provide unsatisfactory performance (as
highlighted in red) if it can not reject more than about 30% of the potential
mappings while it's only 2x-4x faster than read alignment step.

## Slide 48: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches.
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout.
VLSI chip layout

## Slide 49: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches.
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout.
Key result:
  SneakySnake is up to four orders of magnitude more accurate than Shouji (Bioinformatics’19) and GateKeeper (Bioinformatics’17).
  SneakySnake greatly accelerates state-of-the-art CPU sequence aligners, Edlib (Bioinformatics’17) and Parasail (BMC Bioinformatics’16)
    by up to 37.7× and 43.9× (>12× on average), on CPUs
    by up to 413× and 689× (>400× on average) with FPGA acceleration

## Slide 50: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
E = 3
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 51: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
E = 3
ENTRANCE
EXIT
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 52: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
3
EXIT
2
1
0
0
0
4
0
2
0
0
ENTRANCE
0
0
0
4
1
0
1
0
1
1
0
1
0
0
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 53: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Routing Travel Path
Examining the Snake Survival
This is what you actually need to build and it can be done on-the-fly!
ENTRANCE
EXIT
3
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 54: FPGA Resource Analysis
FPGA resource usage for a single filtering unit of GateKeeper, Shouji, and Snake-on-Chip for a sequence length of 100 and under different edit distance thresholds (E).

## Slide 55: Filtering Accuracy
Alser, "Accelerating the Understanding of Life's Code Through Better Algorithms and Hardware Design”, arXiv preprint arXiv:1910.03936, 2019.

## Slide 56: Long Read Mapping (SneakySnake vs Parasail)
10K bp reads 100K bp reads

## Slide 57: Long Read Mapping (SneakySnake vs KSW2)
10K bp reads 100K bp reads

## Slide 58: Ongoing Directions
Seed Filtering Technique:
  Goal: Reducing the number of seed (k-mer) locations.
    Heuristic (limits the number of mapping locations for each seed).
    Supports exact matches only.
Pre-alignment Filtering Technique:
  Goal: Reducing the number of invalid mappings (>E).
    Supports both exact and inexact matches.
    Provides some falsely-accepted mappings.
Read Alignment Acceleration:
  Goal: Performing read alignment at scale.
    Limits the numeric range of each cell in the DP table and hence supports limited scoring function.
    May not support backtracking step due to random memory accesses.

## Slide 59: The Need for Speed
Alser+, "Technology dictates algorithms: Recent developments in read alignment", arXiv, 2020
Mapper
Did we realize the need for faster genome analysis?

## Slide 60: The Need for Speed

## Slide 61: Did we Achieve Our Goal?
Our goal is to significantly reduce the time spent on calculating the optimal alignment in genome analysis from hours to mere seconds using both new algorithms & hardware accelerators, given limited computational resources (i.e., personal computer or small hardware).
1997 2015

## Slide 62: What is Intelligent Genome Analysis?
Fast genome analysis
  Real-time analysis
Using intelligent architectures
  Specialized HW with less data movement
DNA is a valuable asset
  Controlled-access analysis
Population-scale genome analysis
  Sequence anywhere at large scale!
Avoiding erroneous analysis
  E.g., your father is not your father
Bandwidth
Energy-efficiency & Latency
Privacy
Scalability
Accuracy

## Slide 63: Where is Read Mapping Going Next?
Sherman+, “Assembly of a pan-genome from deep sequencing of 910 humans of African descent” Nature genetics, 2019.
African pan-genome contains ~10% more DNA than the current human reference genome.