## Slide 1: Bit-Exact ECC Recovery (BEER): Determining DRAM On-Die ECC Functions by Exploiting DRAM Data Retention Characteristics
Minesh Patel, Jeremie S. Kim
Taha Shahroodi, Hasan Hassan, Onur Mutlu
MICRO 2020 (Session 2C – Memory)
Notes: Hi, I’m Minesh, and today I will introduce BEER.
[CLICK]

## Slide 2
What are the DRAM chip’s
reliability characteristics?
Third-party
DRAM consumer
System Designer
Test/Validation Engineer
Research Scientist
Minimum viable operating timings?
Aggregate
failure rates?
‘Weak’ cell
locations?
Temperature dependence?
Inter-chip variation?
Statistical error distributions?
Notes: Third-party DRAM consumers often ask the question
[CLICK]
“What are a DRAM chip’s reliability characteristics?”
This includes things like
[CLICK] Aggregate failure rates
[CLICK] minimum viable operation timings
[CLICK] And many other reliability-related questions
[CLICK]

## Slide 3
Unknown &
Proprietary
DRAM Testing and
Error Characterization
Study observed bit flips
On-die ECC
No feedback to CPU upon error correction
Study observed bit flips
Bit flips obfuscated by on-die ECC
Notes: The way to answer these questions is with extensive DRAM testing and error characterization
[CLICK]
Given a DRAM chip
[CLICK]
We study the observed bit flips when errors occur
[CLICK]
However, modern DRAM chips include on-die ECC, which are
[CLICK] unknown and proprietary
[CLICK] and provide no feedback to the CPU upon error correction
[CLICK] Therefore, on-die ECC obfuscates the errors we wish to study
[CLICK]

## Slide 4
Unknown &
Proprietary
DRAM Testing and
Error Characterization
On-die ECC
No feedback to CPU
Study observed bit flips
Bit flips obfuscated by on-die ECC
On-die ECC complicates
third-party DRAM testing
Notes: This means that on-die ECC complicates third-party DRAM testing

## Slide 5: Overcoming Challenges of On-Die ECC
Our goal:
Determine exactly how on-die ECC
obfuscates errors (i.e., its parity-check matrix)
Data
I/O
ECC
Logic
DRAM Chip
Notes: To overcome these challenges
[CLICK]
our goal in this work is to determine exactly how on-die ECC obfuscates errors.
In other words, its parity-check matrix.
[CLICK]
In the context of a DRAM chip,
[CLICK]
we want to know exactly what happens within the ECC logic.
[CLICK]

## Slide 6
BEER Methodology
Induce uncorrectable errors
1
Aggregate unique error patterns
2
Solve for the parity-check matrix
3
BEER requires no special hardware or knowledge
https://github.com/CMU-SAFARI/BEER
Notes: To this end, we introduce BEER, a new three-step testing methodology that
[CLICK]
First induces uncorrectable errors in a DRAM chip
[CLICK]
Then aggregates unique error patterns observed
[CLICK]
And finally solves for the parity-check matrix given the unique patterns
[CLICK]
BEER requires no special hardware or knowledge
And we release our implementation as open-source on github

## Slide 7
Simulated correctness and practicality
Over 100,000 representative ECC codes
of varying word lengths (4 – 247 bits)
Two-Part Evaluation
Experimental demonstration
80 LPDDR4 DRAM chips
(3 major manufacturers)
Notes: We evaluate BEER in two ways.
[CLICK]
First, an experimental demonstration using real LPDDR4 DRAM
[CLICK]
Second, in simulation to show BEER’s correctness and practicality for various representative on-die ECC codes.

## Slide 8
Simulated correctness and practicality
Over 100,000 representative ECC codes
of varying word lengths (4 – 247 bits)
Two-Part Evaluation
Experimental demonstration
80 LPDDR4 DRAM chips
(3 major manufacturers)
Different manufacturers appear to use different parity-check matrices
Chips of the same model appear to use identical parity-check matrices
BEER works for all simulated test cases
BEER is practical in both runtime and memory usage
Notes: Our experiments show that:
different manufacturers appear to use different parity-check matrices
and chips of the same model appear to use identical matrices
[CLICK]
Our simulations show that
BEER works for all simulated test cases
And is practical in terms of both runtime and memory usage
[CLICK]

## Slide 9
Designing
Systems
System-level
error-mitigation
mechanisms
Improving
on-die ECC
Testing and Validation
Crafting worst-case
test patterns
Root-cause
failure
analysis
Characterizing Errors
Profiling for
error-prone
physical cells
Studying raw bit
error properties
BEER
Use Cases
Notes: To learn more about BEER and its use cases
[CLICK]
== OLD with anims ==
Finally, we show how knowing the parity-check matrix via BEER is useful in practice for
[CLICK]
Error characterization studies
[CLICK]
Efficient testing and validation
[CLICK]
And designing reliable systems
[CLICK]

## Slide 10: Bit-Exact ECC Recovery (BEER): Determining DRAM On-Die ECC Functions by Exploiting DRAM Data Retention Characteristics
Minesh Patel, Jeremie S. Kim
Taha Shahroodi, Hasan Hassan, Onur Mutlu
MICRO 2020 (Session 2C – Memory)
Notes: Please attend my talk at MICRO 2020.
[END]
== OLD ==
If you are interested in our work, please see our paper and the full presentation in MICRO 2020.