## Slide 1: Binary Star: Coordinated Reliability in Heterogeneous Memory Systems for High Performance and Scalability
Xiao Liu1, David Roberts, Rachata Ausavarungnirun2
Onur Mutlu3, Jishen Zhao1
52nd IEEE/ACM International Symposium on Microarchitecture®
October 12-16, 2019, Columbus, Ohio, USA
1UC San Diego, 2King Mongkut's University of Technology North Bangkok, 3ETH Zurich
Notes: Thanks for the introductions
Hybrid mem is a heterogeneous memory consists of 3D DRAM cache and main memory
This work collaborates with ETH Zurich and king mongkuts

## Slide 2: Large memory capacity is in demand
Chart: 
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Amazon EC2 | 0.0605 | 0.244 | 0.244 | 2 | 4
Microsoft Azure | 0.448 | 2 | 4
Scale-up Cloud Server
Memory Capacity (TB)
cr1.8x
r3.8x
X1
X1e
G5
S192
S192m
S960
20TB
X1e
16TB
[Ogleari+, HPCA’ 2019]
Notes: Application today
The major cloud service providers
The largest main memory capacity of a single node. Increase from less than 1 tb to more than 15 tb in less than three years.
[only talk about demand for memory capacity increases ]

## Slide 3: Decreasing reliability in future DRAM
Scaling: decrease cell size to increase capacity.
Increasing error rate:
  Vulnerability of ultra-thin dielectric material.
  Increased variance between cells on retention time.
Chart: 
| 28 | 25 | 20 | 1X | 1Y
 | 3e-08 | 4e-07 | 1.5e-06 | 8e-06 | 7e-05
Bit Error Rate
Technology nodes (nm)
[Cha+, HPCA’17]
10-3
10-4
10-5
10-5
10-6
10-7
10-8

## Slide 4: Benefit of hybrid memory
Core
L1 Cache
Shared SRAM Caches
3D DRAM LLC (Gigabytes)
Processor
…
…
Core
L1 Cache
Core
L1 Cache
Main Memory (Hundreds of GB ~ TB)
3D stacked DRAM
Izraelevitz, J., Yang, J., Zhang, L., Kim, J., Liu, X., Memaripour, A., Soh, Y.J., Wang, Z., Xu, Y., Dulloor, S.R., Zhao, J. and Swanson, S. 2019. Basic performance measurements of the intel optane DC persistent memory module. arXiv preprint arXiv:1903.05714.
Notes: On the other hand, numerous emerging memory device shows up.
DRAM evolves by itself.
NVRAM
In this work we look into a combination of both.
Add non-volatile memory for example optane DC, change order of animation, arxiv paper

## Slide 5: Reliability issues with traditional memory hierarchy scaling
Chart: 
| 1 | 1.05 | 0.94 | 0.97
 | 1 | 0.5 | 0.19 | 0.16
28nm RECC DRAM
Better Reliability
Better Performance
Notes: We statistically analyze the reliability and performance issue of traditional memory hierarchy.

## Slide 6: Reliability issues with traditional memory hierarchy scaling
Chart: 
| 1 | 1.05 | 0.94 | 0.97
 | 1 | 0.5 | 0.19 | 0.16
28nm RECC DRAM
Sub-20nm RECC+IECC DRAM
Better Reliability
Better Performance
Scales to <20nm

## Slide 7: Reliability issues with traditional memory hierarchy scaling
Chart: 
| 1 | 1.05 | 0.94 | 0.97
 | 1 | 0.5 | 0.19 | 0.16
28nm RECC DRAM with 3D DRAM Cache
28nm RECC DRAM
Sub-20nm RECC+IECC DRAM with 3D DRAM Cache
Sub-20nm RECC+IECC DRAM
Better Reliability
Better Performance
Add a 28nm
3D DRAM LLC
Add a sub-20nm 3D DRAM LLC

## Slide 8: Opportunity #1
Inefficiency of decoupled reliability schemes
On-chip 3D-stacked DRAM LLC
Off-chip Main Memory (Persistent)
ECC
ECC
Error
Ac
Am
log
Ap
Duplicated and unaware of each other

## Slide 9: Opportunity #2
Most cache lines are clean
Chart: 
YCSB | 0.92154 | 0.92208 | 0.92079 | 0.92189 | 0.92122 | 0.92124 | 0.92169 | 0.92254 | 0.92132 | 0.92277 | 0.92157 | 0.92231 | 0.92298 | 0.92135 | 0.92257 | 0.92159 | 0.92091 | 0.92333 | 0.92122 | 0.92124 | 0.92255 | 0.92217 | 0.92212 | 0.92084 | 0.92228 | 0.92164 | 0.92083 | 0.92089 | 0.92208 | 0.92229 | 0.92208 | 0.92141 | 0.92101 | 0.92191 | 0.92181 | 0.9224 | 0.92224 | 0.92163 | 0.92089 | 0.92128 | 0.92184 | 0.92049 | 0.92209 | 0.92159 | 0.9196 | 0.91927 | 0.92215 | 0.92036 | 0.92181
TPCC | 0.92525 | 0.92519 | 0.92514 | 0.92509 | 0.92505 | 0.92496 | 0.92448 | 0.92447 | 0.92445 | 0.92445 | 0.92438 | 0.92437 | 0.92437 | 0.92436 | 0.9247 | 0.92532 | 0.92527 | 0.92524 | 0.92519 | 0.92514 | 0.92508 | 0.92504 | 0.92497 | 0.9245 | 0.92447 | 0.92445 | 0.92444 | 0.92437 | 0.92437 | 0.92439 | 0.92437 | 0.92469 | 0.92532 | 0.92528 | 0.92523 | 0.9252 | 0.92514 | 0.92507 | 0.92505 | 0.92499 | 0.9245 | 0.92445 | 0.92445 | 0.92445 | 0.92437 | 0.92438 | 0.92438 | 0.92438 | 0.92469
Redis | 0.94506 | 0.94655 | 0.94718 | 0.94506 | 0.94569 | 0.94713 | 0.94642 | 0.94506 | 0.9464 | 0.94718 | 0.94506 | 0.94506 | 0.94666 | 0.94717 | 0.94506 | 0.946 | 0.94718 | 0.94508 | 0.94506 | 0.94652 | 0.94717 | 0.94506 | 0.94509 | 0.94685 | 0.94648 | 0.94506 | 0.94623 | 0.94717 | 0.94506 | 0.94506 | 0.94655 | 0.94717 | 0.94506 | 0.94566 | 0.94711 | 0.94648 | 0.94506 | 0.94641 | 0.94718 | 0.94506 | 0.94506 | 0.94666 | 0.94716 | 0.94506 | 0.94599 | 0.94718 | 0.94508 | 0.94506 | 0.94652
Memcached | 0.90146 | 0.90137 | 0.90127 | 0.90146 | 0.90127 | 0.90127 | 0.90146 | 0.90127 | 0.90127 | 0.90146 | 0.90127 | 0.90127 | 0.90146 | 0.90127 | 0.90146 | 0.90146 | 0.90127 | 0.90146 | 0.90146 | 0.90127 | 0.90146 | 0.90146 | 0.90127 | 0.90146 | 0.90146 | 0.90127 | 0.90146 | 0.90137 | 0.90127 | 0.90146 | 0.90137 | 0.90127 | 0.90146 | 0.90137 | 0.90127 | 0.90146 | 0.90137 | 0.90127 | 0.90146 | 0.90127 | 0.90127 | 0.90146 | 0.90127 | 0.90127 | 0.90146 | 0.90127 | 0.90146 | 0.90146 | 0.90127
mysql | 0.88902 | 0.89244 | 0.89559 | 0.89278 | 0.89637 | 0.8897 | 0.89215 | 0.89076 | 0.89606 | 0.89825 | 0.89009 | 0.89243 | 0.89115 | 0.89335 | 0.89721 | 0.89253 | 0.8932 | 0.88993 | 0.88858 | 0.89331 | 0.89219 | 0.89208 | 0.88977 | 0.89634 | 0.88915 | 0.88915 | 0.88858 | 0.89148 | 0.89434 | 0.89674 | 0.88896 | 0.89461 | 0.89119 | 0.89085 | 0.88891 | 0.89377 | 0.89372 | 0.8963 | 0.88905 | 0.89061 | 0.89339 | 0.88866 | 0.89127 | 0.89751 | 0.88898 | 0.89603 | 0.89668 | 0.88921 | 0.89304
facesim | 0.96272 | 0.96619 | 0.96735 | 0.96033 | 0.96827 | 0.96784 | 0.9656 | 0.96564 | 0.96754 | 0.96732 | 0.96088 | 0.96419 | 0.96135 | 0.96241 | 0.96334 | 0.96594 | 0.96272 | 0.96516 | 0.96409 | 0.96929 | 0.96053 | 0.96647 | 0.96477 | 0.96643 | 0.96579 | 0.96106 | 0.96412 | 0.96791 | 0.96128 | 0.9652 | 0.96212 | 0.96451 | 0.96418 | 0.96519 | 0.96477 | 0.96782 | 0.96785 | 0.96784 | 0.96795 | 0.96147 | 0.96546 | 0.96917 | 0.96835 | 0.96547 | 0.96665 | 0.96468 | 0.96047 | 0.96468 | 0.9638
fluidanimate | 0.93296 | 0.92709 | 0.92803 | 0.92546 | 0.93096 | 0.92575 | 0.92542 | 0.93317 | 0.93271 | 0.92958 | 0.93333 | 0.92644 | 0.93068 | 0.92692 | 0.93248 | 0.92727 | 0.92774 | 0.92565 | 0.93277 | 0.93276 | 0.92731 | 0.92804 | 0.93076 | 0.93266 | 0.933 | 0.92964 | 0.92995 | 0.92614 | 0.93366 | 0.93132 | 0.92804 | 0.92733 | 0.93264 | 0.92587 | 0.92897 | 0.93226 | 0.92887 | 0.9323 | 0.93154 | 0.9294 | 0.92862 | 0.927 | 0.93281 | 0.92769 | 0.92994 | 0.92952 | 0.9268 | 0.93398 | 0.92982
freqmine | 0.92436 | 0.91688 | 0.92498 | 0.92239 | 0.91873 | 0.92043 | 0.9153 | 0.92207 | 0.91921 | 0.91989 | 0.91936 | 0.91878 | 0.91739 | 0.91807 | 0.92488 | 0.92492 | 0.9164 | 0.92086 | 0.91797 | 0.92303 | 0.92388 | 0.92289 | 0.92433 | 0.92011 | 0.92321 | 0.91909 | 0.92298 | 0.91687 | 0.91934 | 0.91848 | 0.92216 | 0.92346 | 0.92228 | 0.91996 | 0.92194 | 0.92073 | 0.92023 | 0.92393 | 0.91522 | 0.91803 | 0.92484 | 0.91971 | 0.92245 | 0.92332 | 0.91859 | 0.92018 | 0.92367 | 0.91812 | 0.91767
vips | 0.90755 | 0.91197 | 0.90882 | 0.90874 | 0.90908 | 0.90858 | 0.91419 | 0.90717 | 0.91164 | 0.90931 | 0.90792 | 0.90976 | 0.91378 | 0.913 | 0.91003 | 0.90799 | 0.91334 | 0.90642 | 0.9096 | 0.91333 | 0.91314 | 0.91184 | 0.90722 | 0.90955 | 0.91072 | 0.91139 | 0.9089 | 0.90836 | 0.91276 | 0.90994 | 0.91196 | 0.91001 | 0.91427 | 0.90953 | 0.90998 | 0.90997 | 0.90581 | 0.90911 | 0.91064 | 0.91324 | 0.9107 | 0.91176 | 0.90705 | 0.90655 | 0.91075 | 0.91099 | 0.90564 | 0.90627 | 0.9087
x264 | 0.9468 | 0.95437 | 0.95133 | 0.95426 | 0.94844 | 0.9493 | 0.94979 | 0.94952 | 0.95097 | 0.95102 | 0.94787 | 0.94843 | 0.95086 | 0.95312 | 0.94777 | 0.95335 | 0.94745 | 0.95319 | 0.94818 | 0.95153 | 0.95444 | 0.95161 | 0.95337 | 0.95024 | 0.95107 | 0.94534 | 0.94964 | 0.94919 | 0.95468 | 0.95459 | 0.94937 | 0.95162 | 0.95382 | 0.95329 | 0.95456 | 0.94911 | 0.95293 | 0.94543 | 0.95026 | 0.95222 | 0.95029 | 0.95494 | 0.95054 | 0.94711 | 0.9535 | 0.95086 | 0.95289 | 0.94503 | 0.95156
Fraction of
Clean LLC Blocks
Time (Seconds)
0
5
10
Errors on the clean cache line can be corrected by data in NVRAM
Notes: Smooth talk

## Slide 10: Binary Star: design overview
On-chip Components
Shared SRAM Caches
On-chip 3D-stacked DRAM LLC (Gigabytes)
Off-chip NVRAM Main Memory
(Hundreds of Gigabytes ~ Terabytes)
On-chip Components
Off-chip Components
…
…
Core
L1 Cache
Last-level Cache
Main
Memory
Core
L1 Cache
Core
L1 Cache
Notes: Make all above 22

## Slide 11: Binary Star: design overview
On-chip Components
Coordinated Reliability Scheme Between 3D DRAM LLC and NVRAM
Shared SRAM Caches
On-chip 3D-stacked DRAM LLC (Gigabytes)
Off-chip NVRAM Main Memory
(Hundreds of Gigabytes ~ Terabytes)
On-chip Components
Off-chip Components
…
…
Core
L1 Cache
Core
L1 Cache
Core
L1 Cache

## Slide 12: Binary Star: design overview
On-chip Components
Coordinating Wear-Leveling with data consistency of the main memory
Shared SRAM Caches
On-chip 3D-stacked DRAM LLC (Gigabytes)
Off-chip NVRAM Main Memory
(Hundreds of Gigabytes ~ Terabytes)
On-chip Components
Off-chip Components
…
…
Core
L1 Cache
Core
L1 Cache
Core
L1 Cache

## Slide 13: Periodic forced writeback
Periodic forced writeback
(Infrequent, e.g., every 30 minutes)
ECC
On-chip 3D DRAM
LLC
Off-chip NVRAM
All SRAM caches
a
b
c
a
b
a
b
Consistent
NVRAM block
Inconsistent
NVRAM block
Observation 1: Errors in the LLC can be corrected by consistent data copies in NVRAM main memory.
CRC
Binary Star Daemon: conducts periodic forced writebacks
Stalls the application
Saves process state
Issues cache-line writeback instructions
Notes: About 30 minutes: we conduct sensity study and configure out. Trade-off

## Slide 14: Consistent cache writeback
a’
A’
CRC
On-chip 3D DRAM
LLC
a’
A
a’’
Off-chip NVRAM
a
b
b
c
a’’
Consistent
NVRAM block
Inconsistent
NVRAM block
Binary Star Triggered Wear-leveling
(once each periodic writeback interval)
Observation 2: NVRAM wear leveling naturally redirects and maintains the remapping of data updates to alternative memory locations.
Observation 1: Errors in the LLC can be corrected by consistent data copies in NVRAM main memory.
Notes: What if the cache line wants to evict a dirty cacheline?

## Slide 15: LLC error correction and recovery
A’
CRC
On-chip 3D DRAM
LLC
a’
A
a
Off-chip NVRAM
a
c
a
Consistent
NVRAM block
Inconsistent
NVRAM block
a
Dirty?
Error Correction:
Invalidate the Cache Line;
Serve a LLC Miss
No (Clean LLC Line)
Yes (Dirty LLC Line)
Error Recovery:
Application rolls back to execute from the last checkpoint
Error
Consistent Data
(A Checkpoint)
a
Notes: More smooth

## Slide 16: Experiment setup
Simulators: McSimA+ (Performance), FaultSim (Reliability)
Baselines:
  3D DRAM cache with DRAM main memory
  DRAM main memory only
  3D DRAM cache with NVRAM main memory (PCM)
  NVRAM main memory only (PCM)
Notes: Add animations for focus

## Slide 17: Experiment setup
Simulators: McSimA+ (Performance), FaultSim (Reliability)
Baselines:
  3D DRAM cache with DRAM main memory
  DRAM main memory only
  3D DRAM cache with NVRAM main memory (PCM)
  NVRAM main memory only (PCM)
Notes: Add animations for focus

## Slide 18: Experiment setup
Resilience schemes:
  Rank level ECC (RECC)
  In-DRAM ECC (IECC)
  Chipkill combined with IECC
  Binary Star
Workloads:
  In-memory/traditional databases workloads (Redis, Memcached, TPCC, YCSB, mysql)
  Memory intensive workloads from PARSEC
Notes: Add animations for focus

## Slide 19: Experiment setup
Resilience schemes:
  Rank level ECC (RECC)
  In-DRAM ECC (IECC)
  Chipkill combined with IECC
  Binary Star
Workloads:
  In-memory/traditional databases workloads (Redis, Memcached, TPCC, YCSB, mysql)
  Memory intensive workloads from PARSEC
Notes: Add animations for focus

## Slide 20: Evaluation: system reliability
System | FIT | Storage cost | 
 |  | DRAM LLC | Main memory
No-ECC 28nm DRAM | 44032-66150 | N/A | 0%
RECC 28nm DRAM | 8806-13230 | N/A | 12.50%
IECC+RECC sub-20nm 3D DRAM+DRAM | 78211-117912 | 18.75% | 18.75%
IECC+Chipkill sub-20nm 3D DRAM+DRAM | 37949-59518 | 18.75% | 18.75%
RECC sub-20nm 3D DRAM+PCM | 6352-9963 | 12.50% | 12.79%
Binary Star sub-20nm 3D DRAM+PCM |  |  | 
2637-3968
6.25%
12.79%
Better
Notes: Talk about the meaning of x/y axises
Add animations

## Slide 21: Evaluation: devices’ reliability
3D-DRAM device error rate (for sub20 nm)
  1016x reduction compares to RECC
  1012x reduction compares to Chipkill+IECC
Number of writes to NVRAM
  20% more writes when the periodic force writeback interval is 30 mins

## Slide 22: Evaluation: performance
Normalized Throughput
Chart: 
| YCSB | TPCC | Redis | Memcached | mysql | facesim | fluidanimate | freqmine | vips | x264 | Gmean
DRAM | 0.97353 | 0.9724 | 0.96872 | 0.96027 | 0.99511 | 0.90291 | 0.97483 | 0.9966 | 0.96589 | 0.96589 | 0.9673
PCM | 0.92745 | 0.94278 | 0.9329 | 0.84591 | 0.98371 | 0.71129 | 0.89435 | 0.97943 | 0.8532 | 0.8532 | 0.88887
3D DRAM+PCM | 0.98461 | 0.99646 | 0.9975 | 0.97392 | 0.99814 | 0.99107 | 0.99452 | 0.99236 | 0.99667 | 0.99667 | 0.99216
Binary Star | 0.98129 | 0.99558 | 0.99542 | 0.97002 | 0.99785 | 0.98971 | 0.99368 | 0.99119 | 0.99616 | 0.99616 | 0.99067
3D DRAM+DRAM
Better
Within 1%
Notes: Talk about the meaning of x/y axises
None of these baseline has any realibility
Animations

## Slide 23: Other results
NVRAM latency sensitivity study
Effect on varying the periodic forced writeback interval
  Performance
  Rollback rate
  Number of writes

## Slide 24: Summary
On-chip Components
Last-level Cache
Main
Memory
Binary Star
Shared SRAM Caches
On-chip 3D-stacked DRAM LLC (Gigabytes)
Off-chip NVRAM Main Memory
(Hundreds of Gigabytes ~ Terabytes)
…
…
Core
L1 Cache
Core
L1 Cache
Core
L1 Cache

## Slide 25: Summary
Chart: 
| 1 | 1.05 | 0.94 | 0.97
 | 1 | 0.5 | 0.19 | 0.16
Binary Star
28nm RECC DRAM with 3D DRAM Cache
28nm RECC DRAM
Sub-20nm RECC+IECC DRAM with 3D DRAM Cache
Sub-20nm RECC+IECC DRAM
Better Reliability
Better Performance

## Slide 26: Binary Star: Coordinated Reliability in Heterogeneous Memory Systems for High Performance and Scalability
Xiao Liu1, David Roberts, Rachata Ausavarungnirun2
Onur Mutlu3, Jishen Zhao1
52nd IEEE/ACM International Symposium on Microarchitecture®
October 12-16, 2019, Columbus, Ohio, USA
1UC San Diego, 2King Mongkut's University of Technology North Bangkok, 3ETH Zurich

## Slide 27: Summary
Binary Star utilizes state-of-art 3D DRAM and NVRAMs to provide large memory.
Binary coordinates resilience schemes to enable high reliability memory system.
Binary Star coordinates built in wear-leveling to enable high performance resilience guarantee.
Binary Star decreases the possibility of system failures by 92.9% compares to the state-of-the-art designs.
Binary Star achieves 99% performance of a conventional DRAM based system with no error correction.

## Slide 28: Binary Star triggered Wear-leveling
A’
A
Segment
number
Periodic forced
writeback
A
A’
A
B’
Consistent Cache
Writeback
B
B’
B
B
Free Segment
Consistent Segment
Inconsistent Segment

## Slide 29: Binary Star Daemon
Normal
application
execution
Identify
erroneous
processes
Rollback
Periodic forced writeback
Stall all
processes
Retrieve
data
with drst
Periodic forced writeback interval reached
Memory error signal
Resume
all the
processes
Retrieve
the ckpted
PCBs
1
Stall all
processes
Save all
processes’
PCB
Flush
all caches
with bclwb
5
6
7
8
9
2
3
4

## Slide 30: NVRAM latency sensitivity study
Chart: 
| 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | 0.5x | 1x | 2x | 4x | YCSB | TPCC | Redis | Memcached | mysql | facesim | fluidanimate | freqmine | vips | x264 | Gmean
Binary Star | 0.99293 | 0.98129 | 0.95881 | 0.9168 | 0.99829 | 0.99558 | 0.99022 | 0.97966 | 0.99819 | 0.99542 | 0.98289 | 0.95874 | 0.99185 | 0.97002 | 0.93912 | 0.90687 | 0.99943 | 0.99785 | 0.99472 | 0.98851 | 0.99724 | 0.98971 | 0.97498 | 0.9468 | 0.99831 | 0.99368 | 0.98455 | 0.96678 | 0.99764 | 0.99119 | 0.97853 | 0.95416 | 0.99898 | 0.99616 | 0.99057 | 0.97957 | 0.99898 | 0.99616 | 0.99057 | 0.97957 | 0.99754 | 0.99067 | 0.97731 | 0.95197
Throughput

## Slide 31: Effect on varying the periodic forced writeback interval
Chart: 
| 1 | 60 | 300 | 600 | 1800 | 3600
YCSB | 0.6479 | 0.80989 | 0.88492 | 0.93293 | 0.98129 | 0.98229
TPCC | 0.7767 | 0.87811 | 0.92681 | 0.96119 | 0.99558 | 0.99658
Redis | 0.77517 | 0.87733 | 0.92633 | 0.96087 | 0.99542 | 0.99642
Memcached | 0.5576 | 0.75883 | 0.85274 | 0.91094 | 0.97002 | 0.97102
mysql | 0.79874 | 0.88931 | 0.93357 | 0.96571 | 0.99785 | 0.99885
facesim | 0.72175 | 0.84961 | 0.90945 | 0.94953 | 0.98971 | 0.99071
fluidanimate | 0.75859 | 0.86881 | 0.92117 | 0.9574 | 0.99368 | 0.99468
freqmine | 0.73531 | 0.85672 | 0.9138 | 0.95246 | 0.99119 | 0.99219
vips | 0.78222 | 0.88093 | 0.92851 | 0.96233 | 0.99616 | 0.99716
x264 | 0.78222 | 0.88093 | 0.92851 | 0.96233 | 0.99616 | 0.99716
Gmean | 0.72969 | 0.85412 | 0.91226 | 0.95143 | 0.99067 | 0.99167
Normalized Throughput
Periodic Forced Writeback Interval (s)

## Slide 32: Effect on varying the periodic forced writeback interval
Chart: 
| 1 | 60 | 300 | 600 | 1800 | 3600
Uncorrectable errors | 5.76e-11 | 2.7475e-09 | 5.1552e-09 | 6.0653e-09 | 6.5491e-09 | 6.791e-09
Periodic Forced Writeback Interval (s)
8×10-9
6×10-9
4×10-9
2×10-9
0
Rollback rate

## Slide 33: Evaluation: 3D-DRAM reliability
Chart: 
| 1E-14 | 1E-13 | 9.9999999999999998E-13 | 9.9999999999999994E-12 | 1E-10 | 1.0000000000000001E-9 | 1E-8 | 9.9999999999999995E-8 | 9.9999999999999995E-7 | 1.0000000000000001E-5 | 1E-4 | 1E-3
RECC | 1.2902e-23 | 1.2902e-21 | 1.2902e-19 | 1.2902e-17 | 1.2902e-15 | 1.2902e-13 | 1.2902e-11 | 1.2902e-09 | 1.2902e-07 | 1.2902e-05 | 0.0012902 | 0.12902
RECC+IECC | 4.0005e-25 | 4.0005e-23 | 4.0005e-21 | 4.0005e-19 | 4.0005e-17 | 4.0005e-15 | 4.0005e-13 | 4.0005e-11 | 4.0005e-09 | 4.0005e-07 | 4.0005e-05 | 0.0040005
Chipkill+IECC | 8.3902e-47 | 8.3902e-43 | 8.3902e-39 | 8.3902e-35 | 8.3902e-31 | 8.3902e-27 | 8.3902e-23 | 8.3902e-19 | 8.3902e-15 | 8.3902e-11 | 8.3902e-07 | 0.0083902
Binary Star | 1.1086e-95 | 1.1086e-87 | 1.1086e-79 | 1.1086e-71 | 1.1086e-63 | 1.1086e-55 | 1.1086e-47 | 1.1086e-39 | 1.1086e-31 | 1.1086e-23 | 1.1086e-15 | 1.1086e-07
Single Cell BER
1016
1012
Sub-20 nm
28 nm
10-3
10-7
10-11
10-15
10-19
10-23
10-27
10-31
10-35
10-14
10-12
10-10
10-8
10-6
10-4
Device Failure Rate
Better
Notes: Talk about the meaning of x/y axises
Add animation

## Slide 34: Effect on varying the periodic forced writeback interval
Chart: 
| 1 | 60 | 300 | 600 | 1800 | 3600
YCSB | 16.8922 | 6.2136 | 2.2721 | 1.8967 | 1.2151 | 1.0827
TPCC | 16.2023 | 5.987 | 2.1735 | 1.8573 | 1.2053 | 1.0808
Redis | 16.5473 | 6.1003 | 2.2228 | 1.877 | 1.2102 | 1.0817
Memcached | 16.8922 | 6.2136 | 2.2721 | 1.8967 | 1.2151 | 1.0827
mysql | 17.0992 | 6.2815 | 2.3016 | 1.9085 | 1.218 | 1.0832
facesim | 17.9268 | 6.5534 | 2.4199 | 1.9557 | 1.2297 | 1.0855
fluidanimate | 15.9953 | 5.919 | 2.1439 | 1.8455 | 1.2024 | 1.0803
freqmine | 15.7883 | 5.851 | 2.1143 | 1.8337 | 1.1994 | 1.0797
vips | 24.4721 | 8.7034 | 3.355 | 2.3288 | 1.3223 | 1.1032
x264 | 15.9263 | 5.8963 | 2.134 | 1.8416 | 1.2014 | 1.0801
Gmean | 17.2317 | 6.3292 | 2.3195 | 1.9196 | 1.2214 | 1.084
Normalized writes
17.2x
3D DRAM+PCM
Periodic Forced Writeback Interval (s)

## Slide 35: Backup
Notes: Add results
1. Figure out question first, 2.hard question: do not had to , take offline,
3. Good question, 4. do not have strong jundgement