## Slide 1
Mayank Kabra
Rakesh Nadig, Harshita Gupta, Rahul Bera, Manos Frouzakis,
Vamanan Arulchelvan, Yu Liang, Haiyu Mao,
Mohammad Sadrosadati, and Onur Mutlu
Accelerating Homomorphic Encryption-Based
String Matching via Memory-Efficient Data Packing
and In-Flash Processing
CIPHERMATCH
Notes: Hello, everyone. I am Mayank Kabra and today I will be presenting our work ciphermatch, accelerating homomorphic encryption based string matching via efficient data packing and in flash processing

## Slide 2: Executive Summary
Problem: Secure exact string matching using homomorphic encryption (HE) lacks scalability
due to performance bottlenecks in two key areas:
a) Use of complex homomorphic multiplication resulting in high computation cost
b) Data movement bottleneck from large encrypted database stored in solid-state drive (SSD)
CIPHERMATCH: A new algorithm-hardware co-design
that significantly improves the performance of HE-based secure exact string matching by
a) using only homomorphic addition to reduce the high computation cost
b) optimizing the data packing scheme to reduce memory footprint
c) designing a new in-flash-processing (IFP) architecture to reduce data movement
Key Results:
CIPHERMATCH algorithm: 42.9x speedup & 39.4x energy savings than best software
CIPHERMATCH with IFP: 136.9x speedup & 256.4x energy savings over CM-SW
Key Idea: Use (a) only homomorphic addition and (b) perform in-flash processing by exploiting the operational principles of NAND-flash memory to accelerate secure exact string matching
Goal: Develop an algorithm-hardware co-design to provide scalable, parallelizable
and efficient HE-based secure exact string-matching
Notes: Let's 1st go into brief executive summary. So a secure string, matching, using homomorphic encryption face performance bottleneck in 2 key areas. 1st is the use of complex homomorphic multiplication operation, and second, the data movement bottleneck, which occurs from the because large encrypted databases are usually stored in ssds.
Our goal is to develop an algorithm hardware code design to provide scalable, parallelizable and efficient. He based secure exact string matching.
Our key idea is to use only homomorphic addition, operation and perform in flash processing by exploiting the operational principles of nand flash memory.
So to this end we propose cipher match and algorithm hardware code design that significantly improve the performance of he based secure exact string, matching
by using only homomorphic addition operation
by optimizing the existing data packing scheme and
by designing a new in flash processing architecture.
We observe that our cipher match algorithm provides 42.9 times speed up over state of the art and cipher match, when integrated within flash processing further provides 1 36.9 times speed up, and 256.4 times energy savings.

## Slide 3: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH System: Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results
Notes: This is my talk outine for today.

## Slide 4: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH System: Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results
Notes: so let's briefly go into background key problem and our goal.

## Slide 5: Exact String Matching
Exact string matching is used
in many security critical applications, such as
Databases
Bioinformatics
e.g., searching a query in sensitive databases
e.g., identifying similarities in DNA sequences
[Koudas+, VLDB 2003]
[Chen+, TIP 2013]
[Bhukya+, IJCA 2011]
[Cali+, MICRO 2020]
Notes: Exact string matching is used in many security critical applications, such as databases, for example, searching a query in sensitive databases or bioinformatics, for example, identifying variations in DNA sequences.

## Slide 6: Exact String Matching
Query
Server
Storage
(SSD)
Database
User
Notes: Let’s take a look, an example, assume a user has a query, and in a server with the database is stored in SSD.

## Slide 7: Exact String Matching
Query
Server
Storage
(SSD)
Database
User
010011100010101
010110100101010
10010
10010
10010
Notes: The user will send the query to the server and server will perform the string matches, and when the final match has happened the server will send the result back to user.

## Slide 8: Exact String Matching
Query
Server
Storage
(SSD)
Database
010011100010101
010110100101010
10010
Result
User
Performing computation on plaintext
can lead to data leakage
Notes: However, performing computations on this plain text data can lead to data leakage where the outsider can see the computation and can retrieve back the data.

## Slide 9: Exact String Matching
Query
Server
Storage
(SSD)
Database
010011100010101
010110100101010
10010
Result
User
Homomorphic encryption (HE) can be leveraged
to perform secure exact string matching
Notes: Now, homomorphic encryption can be leveraged to perform secure exact string matching.

## Slide 10: Secure Exact String Matching
Decrypt
Encrypt
Query
Server
Storage
(SSD)
Database
010011100010101
010110100101010
Result
User
Query
Enc(0100110101)
Enc(0101101001)
Homomorphic Operations
Allows users to compute on encrypted data without decrypting it
Result
Notes: Let's look at how secure exact string matching will work. So, 1st the user will encrypt the query, Send this encrypted query, and that the server will store the encrypted database. Now this we perform homomorphic operations, which allows users to compute on encrypted data without decrypting it on the server, and then we send the result back which is encrypted. Result where the user will decrypt these results so that he can see the final result.

## Slide 11: Approaches to HE-based String Matching
Secure string matching using HE can be performed using two key approaches
Boolean Approach
Arithmetic Approach
1) High memory footprint
1) Low memory footprint
2) High computation cost
2) Low computation cost
Encrypt individual bits and use
homomorphic XOR and AND operations
Encrypt multiple packed bits and use
homomorphic MUL and ADD operations
3) Supports flexible query size
3) Supports limited query size
More detailed analysis in the paper
Notes: Now secure string, matching, using homomorphic encryption can be used, performed using 2 key approaches. 1st is by Boolean approach, second is by arithmetic approach. In Boolean approach. We encrypt individual bits and use homomorphic ignore and and operation, whereas in arithmetic approach we encrypt multiple bits and use homomorphic multiplication and addition operations.
We analyzed these approaches and found some common characteristics. Boolean approach have high memory, footprint, and high computation cost, whereas arithmetic approach has lower memory, footprint, and lower computation cause as compared to Boolean approach. However, there exist a tradeoff in these two approaches as Boolean approach provides more flexibility in query size whereas arithmetic approach supports only limited query sizes because of the use of limited computation and noise margin challenges due to the use of homomorphic multiplication. WE provide more detailed analysis in our paper.

## Slide 12: Prior Works on HE-based String Matching
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
Boolean Approach [Pradel+, TrustCom 2021 ; Aziz+, Information 2024]
Notes: Now there are prior works in both arithmetic approach and Boolean approach. But we'll focus more into arithmetic approach

## Slide 13: Approaches to HE-based String Matching
Secure string matching using HE can be performed using two key approaches
Boolean Approach
Arithmetic Approach
1) High memory footprint
1) Low memory footprint
2) High computation cost
2) Low computation cost
Encrypt individual bits and use
homomorphic XOR and AND operations
Encrypt multiple packed bits and use
homomorphic MUL and ADD operations
3) Supports flexible query size
3) Supports limited query size
Notes: Now secure string, matching, using homomorphic encryption can be used, performed using 2 key approaches. 1st is by Boolean approach, second is by arithmetic approach. In Boolean approach. We encrypt individual bits and use homomorphic ignore and and operation, whereas in arithmetic approach we encrypt multiple bits and use homomorphic multiplication and addition operations.
We analyzed these approaches and found some common characteristics. Boolean approach have high memory, footprint, and high computation cost, whereas arithmetic approach has lower memory, footprint, and lower computation cause as compared to Boolean approach. However, there exist a tradeoff in these two approaches as Boolean approach provides more flexibility in query size whereas arithmetic approach supports only limited query sizes because of the use of limited computation and noise margin challenges due to the use of homomorphic multiplication. WE provide more detailed analysis in our paper.

## Slide 14: Arithmetic Approach
Arithmetic Approach
Encrypt multiple packed bits
Database = 1 1 … 0 1 0 … 1 . . . 1 1 … 0
1
…
0
1
1
…
1
0
…
32
…
21
67
1
…
1
0
44
…
97
68
41
…
52
94
…
1 bit
32 bits
1024 elements
2048 elements
Yasuda et al. “Secure Pattern Matching Using Somewhat Homomorphic Encryption,” in CCSW, 2013
Notes: Now we'll look more into details about arithmetic approach. So, let's assume a database in arithmetic approach. We take multiple bits of the data, and we place it into in each of the bits is placed into the elements of the plain text, vector and then we encrypt it to generate the encrypted data. For an example purpose, each plaintext element has 1 bit and 1024 elements and in encrypted ciphertext, each element can be of 32 bits with 2018 elements.

## Slide 15: Arithmetic Approach
Arithmetic Approach
Encrypt multiple packed bits
Database = 1 1 … 0 1 0 … 1 . . . 1 1 … 0
1
…
0
1
1
…
1
0
…
32
…
21
67
1
…
1
0
44
…
97
68
41
…
52
94
…
128 bytes
8 Kilobytes
Conventional database size
Encrypted database size
64x
Yasuda et al. “Secure Pattern Matching Using Somewhat Homomorphic Encryption,” in CCSW, 2013
Notes: Now assume a conventional database size of 128 bytes. We will pack this accordingly, and then generate an encrypted database with these approaches, and the database size will be 8 kB, which is 64 times increase in the database size.

## Slide 16: Arithmetic Approach
Encrypted Database
Arithmetic Approach
Encrypt multiple packed bits
Perform homomorphic MUL and ADD operations
1
…
0
1
1
…
1
0
…
32
…
21
67
1
…
1
0
44
…
97
68
41
…
52
94
…
Encrypted Query
21
…
23
57
21
…
23
57
21
…
23
57
…
Database = 1 1 … 0 1 0 … 1 . . . 1 1 … 0
Yasuda et al. “Secure Pattern Matching Using Somewhat Homomorphic Encryption,” in CCSW, 2013
Notes: Now we perform homomorphic multiplication and addition. Operation. Assume this has an encrypted database, as similarly, we will have an encrypted query. We'll perform homomorphic multiplication and addition operation to generate our final encrypted result

## Slide 17: Arithmetic Approach
Arithmetic Approach
32
…
21
67
44
…
97
68
41
…
52
94
…
…
21
…
23
57
21
…
23
57
21
…
23
57
…
Encrypted Result
49
…
51
49
32
…
65
28
81
…
56
63
...
Hom. Op.
Hom. Op.
Hom. Op.
Encrypt multiple packed bits
Perform homomorphic MUL and ADD operations
Yasuda et al. “Secure Pattern Matching Using Somewhat Homomorphic Encryption,” in CCSW, 2013

## Slide 18: Execution Time of Arithmetic Approach
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
Total execution time of [Yasuda+, CCSW 2013]
to perform secure string matching
0%
100%
98% of total time = homomorphic multiplication
98%
Homomorphic multiplication is 100x slower than homomorphic addition
on a CPU-system
Notes: We analyze total execution time of one of the prior arithmetic approach best in terms of performance that perform secure string, matching, and observe that 98% of the total time constitutes from homomorphic multiplication operation.
And this is because homomorphic multiplication is 100 times slower than homomorphic addition operation

## Slide 19: Key Problem (I): Homomorphic multiplication
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
Total execution time of [Yasuda+, CCSW 2013]
to perform secure string matching
0%
100%
98% of total time = homomorphic multiplication
98%
Homomorphic multiplication is 100x slower than homomorphic addition
Homomorphic multiplication limits scalability
of HE-based string matching algorithm
Notes: zthis brings us to our key problem, one that homomorphic multiplication limits the scalability of these achieve based string matching algorithm.

## Slide 20
Databases are large and stored in SSDs
Databases are Stored in Storage (SSD)
Solid-State Drive (SSD)
Database
Homomorphic encryption
further increases the database size
Solid-State Drive (SSD)
Encrypted
Database
Notes: Now, databases are large and they are stored in SSD. When you encrypt, they further increase the database size.

## Slide 21
Databases are large and stored in SSDs
Key Problem (II): Data Movement Bottleneck
Homomorphic encryption
further increases the database size
Solid-State Drive
(SSD)
Encrypted
Database
External I/O bandwidth of SSD
is the main bottleneck for reading large encrypted database
Main
Memory
(DRAM)
CPU/GPU
Notes: Now, this brings us to our second key problem of data movement bottleneck, because the external I/O bandwidth of these Ssds is limited. We need to read this data from the SSD to perform computations which which leads to a large data movement.

## Slide 22
Solid-State Drive
(SSD)
Prior Works on Reducing Data Movement
Encrypted
Database
Notes: However, HE significantly increases the database size after encryption and store them in SSDs.
[CLICK] Hence, our key problem two is the data movement because the external I/O bandwidth of SSD is the main bottleneck to read the encrypted database is limited.

## Slide 23
Prior Works on Reducing Data Movement
Solid-State Drive
(SSD)
SSD
Controller
Flash
Chip
Flash
Chip
Flash
Chip
Flash
Chip
…
…
Notes: Essentially data is stored in NAND-flash chips

## Slide 24
Prior Works on Reducing Data Movement
Solid-State Drive
(SSD)
SSD
Controller
Flash
Chip
Flash
Chip
Flash
Chip
Flash
Chip
…
…
In-Flash Processing (IFP) [Park+, MICRO 2022 ; Gao+, MICRO 2021]
enables computation inside SSD by exploiting
the operational principles of NAND-flash memory
Notes: Now prior works has shown that we can reduce the data movement by exploiting some techniques like in flash processing, which enables computations inside the SSD by exploiting the operational principles of 9 flash memory.

## Slide 25: Our Goal
Develop an
IFP-based algorithm-hardware co-designed system
that can perform scalable, parallelizable and efficient
secure exact string matching
Notes: And with this our goal is to develop an in- flash processing based algorithm hardware, co-design system that can perform scalable, parallelizable and efficient, secure, exact string matching.

## Slide 26: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH: System Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results
Notes: This is my talk outine for today.

## Slide 27: Key Observation
Database
0100111000101010101101
0101101001010101100010
Query
10010
01101
~
01101
01101
Perform addition
Observe a string of 1111’s, if query matches
01101
11111
Encrypted
Database
Enc(01001110001001…101)
Enc(01011010010100…010)
Enc(Query)
10010
~
01101
Enc(01101)
Perform homomorphic addition
Observe Enc(1111’s), if Enc(query) matches
Enc(01101)
Enc(11111)
Enc(01101)
Enc(01101)
In a conventional database,
we perform only addition to get a string match
This observation can be extended to perform
secure exact string matching
using only homomorphic addition
Notes: Let's move into our key idea. We make a key observation, assume a database and a query. First, st we if we negate the query and send this query to the database and perform addition operation. We'll observe that if the query matches we'll observe a string of ones. Now this observation can be extended to homomorphic encryption. Also, where you have encrypted database and encrypted query.
Now assume, let's take us again a query, and negate it, and then generate an encrypted query, and when we send this encrypted query and perform homomorphic addition, operation, if the encrypted query matches, we will observe an encrypted string of ones.

## Slide 28: Key Idea (1/2)
Database
0100111000101010101101
0101101001010101100010
Query
10010
01101
~
01101
01101
Perform addition
Observe a string of 1111’s
01101
11111
Encrypted
Database
Enc(01001110001001…101)
Enc(01011010010100…010)
Query
10010
01101
~
01101
Enc(01101)
Perform homomorphic addition
Observe a string of Enc(1111’s)
Enc(01101)
Enc(11111)
Enc(01101)
Use only homomorphic addition to perform
secure exact string matching
Notes: we can use only homomorphic addition to perform secure exact string matching.

## Slide 29: Key Observation
Homomorphic addition is highly parallelizable
Exploit inherent parallelism of NAND-flash memory
Improves the performance of secure string matching
Reduces data movement
Notes: we also observe that homomorphic addition is highly parallelizable. And for this we can exploit the inherent parallelism of Nand flash memory which can improve the performance and reduce the data movement. We'll discuss about this in later, when we present our cipher match algorithm.

## Slide 30: Key Idea (2/2)
Solid-State Drive (SSD)
Encrypted
Database
Main
Memory
(DRAM)
CPU/GPU
In-Flash Processing (IFP) [Park+, MICRO 2022 ; Gao+, MICRO 2021]
enables computation inside SSD by exploiting
the operational principles of NAND-flash memory
Performs computation
Use only homomorphic addition to perform
secure exact string matching
Use in-flash processing (IFP) to reduce data movement
and accelerate secure exact string matching
Notes: However, this gives a second key idea that we can use in flash processing to reduce data movement and accelerate secure exact string matching.

## Slide 31: CIPHERMATCH
An algorithm-hardware co-design
Improves the performance of
HE-based secure exact string matching
Eliminates costly homomorphic multiplication
- by designing secure string-matching algorithm using only homomorphic addition
Reduces memory footprint
- by optimizing the data packing scheme used before encryption
Reduces data movement
and leverages massive bit and array-level parallelism
by designing an in-flash processing architecture
Notes: With this we propose cipher match, an algorithm hardware code design that improves the performance of he based secure exact string matching cipher match reduces memory footprint by optimizing the data. Packing scheme eliminates costly homomorphic multiplication by using only homomorphic addition operation and reduces data movement and leverage parallelism by designing and in flash processing architecture.

## Slide 32: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH: System Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results
Notes: Let's move on into Ciphermatch system overview.

## Slide 33: CIPHERMATCH: System Overview
Client
Server
Database
Data Packing & Encryption
Storage
(SSD)
CPU
DRAM
Encrypted Database
Storage
(SSD)
Encrypted Database
Efficiently pack the database
to reduce the memory footprint after encryption
Notes: So assume you have a client and a server. 1st client has a database and wants to store in the server client will efficiently pack this database to reduce the memory footprint and send it and store it into the servers. Database. Now, client has a query which he wants to perform. A string match client will again efficiently pack the query and send it to the server. Now, at server. We load the data, encrypted database and then perform string matching operation and get the final result. Using only homomorphic addition operation
to accelerate this overall process we can perform string matching inside the inside. The SSD. By performing computations by exploiting the operational principles of Nand flash memory.

## Slide 34: CIPHERMATCH: System Overview
Client
Server
Query
Data Packing & Encryption
Storage
(SSD)
CPU
DRAM
Encrypted Query
Storage
(SSD)
Encrypted Database
Efficiently pack the database
to reduce the memory footprint after encryption
Efficiently pack the query
to perform parallel secure string matching on encrypted database

## Slide 35: CIPHERMATCH: System Overview
Client
Server
Query
Data Packing & Encryption
Storage
(SSD)
CPU
DRAM
Encrypted Query
Storage
(SSD)
Encrypted Database
Efficiently pack the database
to reduce the memory footprint after encryption
Efficiently pack the query
to perform parallel secure string matching on encrypted database
Perform secure exact string matching
using only homomorphic addition
CPU
Performs String Matching
Result
Matched Index

## Slide 36: CIPHERMATCH: System Overview
Client
Server
Query
Data Packing & Encryption
Storage
(SSD)
CPU
DRAM
Encrypted Query
Storage
(SSD)
Encrypted Database
Efficiently pack the database
to reduce the memory footprint after encryption
Efficiently pack the query
to perform parallel secure string matching on encrypted database
Perform secure exact string matching
using only homomorphic addition
Perform String Matching
Accelerate secure exact string matching by performing computations inside SSD
by exploiting operational principles of NAND-flash memory
Result
Matched Index

## Slide 37: CIPHERMATCH: Key Steps
Secure Exact String-Matching Algorithm
In-Flash Processing
1
2
3
Memory-Efficient Data Packing Scheme
Notes: Now, with this cipher match have 3 key steps. First, st to have a memory, efficient data packing scheme, second, to perform secure exact string, matching, algorithm, and 3, rd to use an in flash processing.

## Slide 38: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH: System Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results
Notes: This is my talk outine for today.

## Slide 39: CIPHERMATCH: Key Steps
Secure Exact String-Matching Algorithm
In-Flash Processing
1
2
3
Memory-Efficient Data Packing Scheme
Memory-Efficient Data Packing Scheme
- Efficiently pack the query and database
to reduce the memory footprint and enable parallel string matching
Notes: CIPHERMATCH algorithm consist of first two key steps and lets discuss them one by one.

## Slide 40: Memory-Efficient Data Packing Scheme
1
Database = 010110010100010…01001
01001110001001…101
01011010010100…010
Query (10010)
Database
01011
00101
00010
01001
Notes: 1st is the memory efficient data packing scheme. Now assume you have a database and a query in a conventional database, a conventional domain. Let's look at how we will encrypt it. 1st for database, we will take multiple bits and place it into the elements of the plain text, vector. And then we encrypt it to generate the encrypted database.

## Slide 41: Memory-Efficient Data Packing Scheme
Query (10010)
…
1
Database = 010110010100010…01001
01001110001001…101
01011010010100…010
Enc(Database)
32
…
21
48
67
Database
01011
00101
00010
01001
Encrypt
Encode database
by packing multiple bits
into a single plaintext vector
Increase in encrypted database size is only 4x (2KB -> 8KB)
16 bits
32 bits
Encode
1024 elements
2048 elements
Notes: Now we encoded databases encode our database by packing multiple bits into the single plain text, vector
and we observe that the increase in database size is only 4 times, so that you can take 2 kB of database and can pack it into and generate an encrypted database size of 8 kB. Only.

## Slide 42: Memory-Efficient Data Packing Scheme
Query (10010)
1
Enc(Database)
32
…
21
48
67
~Query (01101)
01101
01101
01101
01101
Notes: Now for query, we 1st negate the query. we replicate the query into the elements of this plain text vector and then encrypt it.

## Slide 43: Memory-Efficient Data Packing Scheme
…
Query (10010)
1
Enc(Database)
32
…
21
48
67
~Query (01101)
01101
01101
01101
01101
Encode query
by negating and replicating
into a single plaintext vector
Enc(~Query)
22
…
17
5
11
Encrypt
Encode
Notes: So essentially, we encode the query by negating and replicating it into the plain text vector which is used to perform parallel string matches. We will look at which we will look at in the next slide.

## Slide 44: Memory-Efficient Data Packing Scheme
1
Enc(Database)
32
…
21
48
67
Enc(~Query)
22
…
17
5
11
Notes: So, with this encrypted database and encrypted query, we want to perform string matches, and with this we let's look at our second key step of performing secure exact string matching.

## Slide 45: CIPHERMATCH: Key Steps
Secure Exact String-Matching Algorithm
- Uses only homomorphic addition and identifies the match
to eliminate costly homomomorphic multiplication
In-Flash Processing
1
2
3
Memory-Efficient Data Packing Scheme
- Efficiently pack the query and database
to reduce the memory footprint and enable parallel string matching

## Slide 46: Secure Exact String-Matching Algorithm
Enc(Database)
32
…
21
48
67
Enc(~Query)
22
…
17
5
11
2
Homomorphic addition
is inherently element-wise addition
+
+
+
+
Notes: Now we want to perform homomorphic addition between these 2. Now, homomorphic addition is inherently an element, wise addition, operation. So we perform an event wise addition and generate the final encrypted result.

## Slide 47
Enc(Database)
32
…
21
48
67
Enc(~Query)
22
17
5
11
2
+
+
+
+
Enc(Result)
54
…
38
53
78
…
Secure Exact String-Matching Algorithm
Notes: [CLICK] HE-based string matching can be performed using two key approaches:
[CLICK] By Boolean approach and an arithmetic approach.
[CLICK] In Boolean aproach,we encrypt individual bits
[CLICK] whereas in arithmetic approach, we take multiple bits,pack them together and generate polynomials
[CLICK] These polynomials are then encrypted to generate encrypted data

## Slide 48: Secure Exact String-Matching Algorithm
2
Enc(Result)
54
…
38
53
78
Decrypt
10110
…
11010
11111
10100
Match Found !!
However, we want to find the match
using Enc(Result) on the server
Notes: If we decrypt this result, we will observe that in one of the coefficient, we will find a string of one and with this the match is found. However, we want to find the match on the encrypted result on the server.

## Slide 49: Identify the Match
2
Enc(Result)
54
…
38
53
78
Decrypt
10110
…
11010
11111
10100
Match Found !!
11111
…
11111
11111
11111
Match Value
Encrypt
Enc(Match value)
35
…
64
53
29
Notes: So for this, what we want to do is to generate a new match value, which is basically it's every element contains a string of ones, we encrypt it, we generate an encrypted match value, and then, finally, we compare this encrypted result and encrypted match value to generate the index and send it back to the client.

## Slide 50: Identify the Match
2
Enc(Result)
54
…
38
53
78
Enc(Match value)
35
…
64
53
29
Compare
Generate Index
Compare and send the final index back to client

## Slide 51: CIPHERMATCH: Algorithm (Summary)
Negated, Replicated and Packed Encrypted Query
with an Encrypted Match Value
Client
Server
Query
Data Packing & Encryption
Storage
(SSD)
CPU
DRAM
Encrypted Query
Storage
(SSD)
Encrypted Database
CPU
Perform String Matching
Result
Matched Index
String Matching using
only Homomorphic Addition
Efficiently Packed Encrypted Database
using our Memory-Efficient Data Packing
1111..1
Encrypted Match Value
Notes: So, to summarize, we have an efficiently pack encrypted database using our data packing scheme. We negate the rep negate, replicate, and pack the encrypted query, and then we send it with an encrypted match value using the same encryption parameters to find that find us find the index, and then we perform string matching, using homomorphic addition operation.
This algorithm can be employed in software in real system and we will look at it later in the evaluation section.

## Slide 52: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH: System Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results

## Slide 53: CIPHERMATCH: Hardware Overview
Server
Storage
(SSD)
CPU
DRAM
Storage
(SSD)
Encrypted Database
Perform String Matching
Client
Query
Data Packing & Encryption
Encrypted Query
Result
Matched Index
1111..1
Encrypted Match Value
Perform secure exact string matching
inside SSD using in-flash processing (IFP)
Notes: Now with this, let's move on into our cipher match hardware design. So, we want to perform secure exact string matching inside our SSD using in-flash processing

## Slide 54: Overview of a Modern Solid State Drive (SSD)
Storage
(SSD)
Solid-State Drive (SSD)
(NAND Flash-Based SSD)

## Slide 55: Overview of a Modern Solid State Drive (SSD)
Solid-State Drive (SSD)
(NAND Flash-Based SSD)
Flash
Chip
Flash
Chip
Flash
Chip
Flash
Chip
SSD
Controller
(General-Purpose Core)
…
…
Internal DRAM
Notes: so let's look into more detail of our SSD, so SSD consists of an SSD controller running on a general purpose code and connected with the Nand flash chip so that we can communicate with them, and contains an internal dram with with which we can buffer the intermediate data.

## Slide 56: Overview of a Modern Solid State Drive (SSD)
Die#0
Die#1
…
NAND Flash Memory
Latching circuit
Data (A1)
Data (A2)
Data (An)
Bitlines (BLs)
…
Latching circuit
Data Latch 0
Data Latch 1
Data Latch 2
Sensing Latch
Solid-State Drive (SSD)
(NAND Flash-Based SSD)
Flash
Chip
Flash
Chip
Flash
Chip
Flash
Chip
SSD
Controller
(General-Purpose Core)
…
…
Internal DRAM
Notes: Now each flash chip, contain multiple dice, and then in each dice we have Nand Flash cell, which stores our data and consists of a latching circuit which which is used to perform, read and write operation. Now, this latching circuit consists of multiple data latches and sensing latches.

## Slide 57
Solid-State Drive (SSD)
(NAND Flash-Based SSD)
Flash
Chip
Flash
Chip
Flash
Chip
Flash
Chip
SSD
Controller
…
…
Internal DRAM
Die#0
Die#1
…
NAND Flash Memory
Latching circuit
Data (A1)
Data (A2)
Data (An)
Bitlines (BLs)
…
Latching circuit
Data Latch 0
Data Latch 1
Data Latch 2
Sensing Latch
Prior work [Gao+, MICRO 2021] uses latching circuit
to perform only bitwise operations
Limitations of Prior Work
Notes: however, prior works has shown that we can use this latching circuitry to perform competition, but are only restricted to perform bit wise operations.

## Slide 58: Advantages of Secure String Matching in SSD
Server
Storage
(SSD)
CPU
DRAM
Storage
(SSD)
Encrypted Database
Perform String Matching
Client
Query
Data Packing & Encryption
Encrypted Query
Result
Matched Index
1111..1
Encrypted Match Value
Homomorphic addition can be parallelized
Exploit bit-level and array-level parallelism
of NAND-flash memory
Notes: Now, there are advantages of performing this secure string matching inside SSD homomorphic addition can be parallelized, as we saw in our cipher match algorithm. And we can exploit the bit level and array level parallelism of Nand flash memory to perform the string matches.

## Slide 59: CIPHERMATCH: Hardware Overview
Matched Index
Encrypted Query
Server
Storage (SSD)
Index Generation
NAND Flash Memory
(Encrypted Data)
Perform homomorphic additions
inside NAND-flash memory
Generate the final index
by comparing it with match value
Encrypted Match Value
I
II
I
II
Notes: Now, essentially, let's look into more detail of how the how our hardware is designed. So we want to perform homomorphic addition inside the nand flash memory, and we want to generate the final index by comparing it with the match value.

## Slide 60: CIPHERMATCH: Hardware Overview
Matched Index
Encrypted Query
Server
Storage (SSD)
Perform homomorphic additions
inside NAND-flash memory
Encrypted Match Value
Perform element-wise addition inside NAND-flash memory
Index Generation
NAND Flash Memory
(Encrypted Data)
I
I
Notes: Now let's look at how can we perform homomorphic addition for this, we want to perform element wise addition inside the nand flash memory,

## Slide 61: CIPHERMATCH: Key Steps
Secure Exact String-Matching Algorithm
- Uses only homomorphic addition and identifies the match
to eliminate costly homomomorphic multiplication
In-Flash Processing
-Exploit the operational principles of NAND-flash memory
to perform homomorphic addition
1
2
3
Memory-Efficient Data Packing Scheme
- Efficiently pack the query and database
to reduce the memory footprint and enable parallel string matching
Notes: CIPHERMATCH algorithm consist of first two key steps and lets discuss them one by one.

## Slide 62
Solid-State Drive (SSD)
(NAND Flash-Based SSD)
Flash
Chip
Flash
Chip
Flash
Chip
Flash
Chip
SSD
Controller
…
…
Internal DRAM
Die#0
Die#1
…
Latching circuit
Data Latch 0
Data Latch 1
Data Latch 2
Sensing Latch
3
CIPHERMATCH: Element-Wise Addition
NAND Flash Memory
Bitlines (BLs)
…
Latching circuit
We use bit-serial addition
to avoid carry propagation across different bitlines
Notes: Now, with this, we want to, we use bit serial addition. So to avoid carry propagation across different bit lines.

## Slide 63: CIPHERMATCH: Bit-Serial Addition
Enc(Database)
…
Lay out the data vertically in NAND-flash memory
3
A2
An
A0
A1
X2
Xn
X1
Y2
Yn
Y0
Y1
A2
An
A0
A1
X2
Xn
X0
X1
Y2
Yn
Y0
Y1
NAND Flash Memory
Bitlines (BLs)
…
Latching circuit
…
…
…
Notes: Now let's look at in more details. How this how the bit serial addition is looks like assume as we have an encrypted database, and each element we have different bits of the data. we take these bits and we vertically lay out the data in the Nand flash memory, and in each bit line we perform a sequence of steps to perform bit serial addition.

## Slide 64: CIPHERMATCH: Bit-Serial Addition
Lay out the data vertically in NAND-flash memory
3
Bi
Ci
Bi⊕Ci
Ci
Bi.Ci
Bi⊕Ci
Bi.Ci
Ai⊕Bi⊕Ci
Ai
Bi.Ci
Sum
(Bi⊕Ci).Ai
Bi.Ci
Sum
Carry
Ai
Ai
Ai
Ai
Ai
Ai
Ai
Bi
Bi.Ci
Ai
(Bi⊕Ci).Ai
Carry
Sum
Bi
Ci
Ai
Bi
Latching circuit
NAND Flash Memory
Bitlines (BLs)
…
Latching circuit
A2
An
A0
A1
X2
Xn
X0
X1
Y2
Yn
Y0
Y1
…
…
…
Notes: Now, just to remind back in each latching circuit, we have multiple data latches and sensing latch so that we can store the intermediary data

## Slide 65: CIPHERMATCH: Bit-Serial Addition
Bi
Ci
Bi⊕Ci
Ci
Bi.Ci
Bi⊕Ci
Bi.Ci
Ai⊕Bi⊕Ci
Ai
Bi.Ci
Sum
(Bi⊕Ci).Ai
Bi.Ci
Sum
Carry
Ai
Ai
Ai
Ai
Ai
Ai
Ai
Bi
Bi.Ci
Ai
(Bi⊕Ci).Ai
Carry
Sum
Lay out the data vertically in NAND-flash memory
Send the query from SSD controller to the latches
Perform Steps 1-6 to perform bit-serial addition
Accumulate the sum bit and send the accumulated bit to the SSD controller
3
SSD Controller
Step 3
Step 4
Step 6
Step 1
Step 2
Step 5
Input Query Transferred from SSD Controller
Accumulated Bit Transferred to SSD Controller
Sum = Ai⊕Bi⊕Ci and Carry = (Bi⊕Ci).Ai + Bi.Ci
NAND Flash Memory
Bitlines (BLs)
…
Latching circuit
A2
An
A0
A1
X2
Xn
X0
X1
Y2
Yn
Y0
Y1
…
…
…
Notes: . First, we send the query which is from the SSD Controller to these latches we perform a sequence of steps from step one to 6, which constitute of bitwise Xor and An, or operation, and the data transfer between these latches to generate the final sum and carry bit.
Now we accumulate this sum bit and send the final accumulated bit back to the SSD controller.

## Slide 66: CIPHERMATCH: Hardware (Summary)
Matched Index
Encrypted Query
Server
Storage (SSD)
Index Generation
NAND Flash Memory
(Encrypted Data)
Perform homomorphic additions
inside NAND-flash memory
Generate the final index
by comparing it with match value
Encrypted Static Value
I
II
I
II
Notes: Now, with this we have performed homomorphic addition inside the land, flash memory. Finally, once the result is sent out, we want to generate the final index by comparing it with the match value, and with for this we use the general purpose course in a pipeline fashion to identify the final match.

## Slide 67: CIPHERMATCH: Hardware (Summary)
Matched Index
Encrypted Query
Server
Storage (SSD)
Index Generation
NAND Flash Memory
(Encrypted Data)
Encrypted Static Value
Use general purpose cores to identify the final match
General Purpose Core
Index Generation
Generate the final index
by comparing it with match value
II
I
II

## Slide 68: Talk Outline
Background, Problem & Goal
Key Idea
CIPHERMATCH: System Overview
CIPHERMATCH: Algorithm
CIPHERMATCH: Hardware
Evaluation Results

## Slide 69: Evaluation Methodology (1/2): Real System
Arithmetic (using SEAL): State-of-the-art arithmetic approach [Yasuda+, CCSW 2013]
Boolean (using TFHE-rs): State-of-the-art Boolean approach [Aziz+, Information 2024]
Intel Xeon, 6 cores, 3.2 GHz 32GB DDR4 DRAM 2TB PCIe 4.0 SSD
We evaluate software-based CIPHERMATCH implementation (CM-SW)
by modifying the Microsoft SEAL library
Our Implementation
Baselines
Varying query size (16-256 bits)* for encrypted database size of 128 GB
Varying encrypted database size (8-128 GB)* for 16-bit query and 1000 queries
* including all circular shifted queries
Workloads
Notes: Now let's move on into our evaluation result. We evaluate our software based cipher match implementation by modifying the Microsoft C library, and we evaluate against 2 baseline. 1st is the arithmetic approach, and second is the Boolean approach, and we evaluate for varying query, sizes for a fixed database size, and varying encrypted sizes, and we include all the circular shifted queries to find different variants of the queries.

## Slide 70: Speedup for Different Query Sizes
Query Size (in bits)
16 32 64 128 256 Avg
Boolean
Speedup
106
104
102
100
Notes: Let's look at the speed up for different query sizes where X-axis is the query size and Boolean approach is set at y equal to one.

## Slide 71: Speedup for Different Query Sizes (1/3)
Query Size (in bits)
106
104
102
100
16 32 64 128 256 Avg
Boolean
Speedup
Arithmetic
9.9x103x
Arithmetic technique outperforms Boolean technique
by orders of magnitude
Notes: We make 3 key observation. First, Arithmetic approaches outperform Boolean approaches by significant margins because they pack multiple bits and reduce the memory footprint and perform the faster operations.

## Slide 72: Speedup for Different Query Sizes (2/3)
Query Size (in bits)
106
104
102
100
16 32 64 128 256 Avg
Boolean
Speedup
Arithmetic
CM-SW
9.9x103x
42.9x
CM-SW outperforms the best prior arithmetic technique
by 42.9x
Notes: Second, ciphermatch software approach is further reduces outperforms. Arithmetic approaches by 42.9 times.

## Slide 73: Speedup for Different Query Sizes (3/3)
Query Size (in bits)
106
104
102
100
16 32 64 128 256 Avg
Boolean
Speedup
Arithmetic
CM-SW
9.9x103x
42.9x
20.7x
30.7x
44.1x
54.7x
62.2x
CM-SW speedup increases with query size
(due to the elimination of homomorphic multiplication)
Notes: Third, cipher match software speed up increases with the increasing query sizes. This is because we have eliminated the use of homomorphic multiplication, and with this increasing query, sizes, homomorphic additions are much more scalable.

## Slide 74: Evaluation Methodology (2/2): Simulation
CM-SW: CIPHERMATCH on compute-centric system [same as real system]
CM-PuM: CIPHERMATCH on memory-centric system [*, 32GB DDR4-2400]
CM-PuM-SSD: CIPHERMATCH on storage-centric system [*, SSD DRAM - 2GB LPDDR4-1866]
[*] - SIMDRAM framework [Hajinazar+ , ASPLOS 2021]
Baselines
We evaluate IFP-based CIPHERMATCH implementation (CM-IFP)
by modeling the characteristics of the NAND-flash memory
Our Implementation
Varying query size (16-256 bits)* for encrypted database size of 128 GB
Varying encrypted database size (8-128 GB)* for 16-bit query and 1000 queries
* including all circular shifted queries
Workloads

## Slide 75: Speedup for Different Query Sizes
Query Size (in bits)
16 32 64 128 256 Avg
Speedup
CM-SW
106
104
102
100

## Slide 76: Speedup for Different Query Sizes (1/3)
Query Size (in bits)
106
104
102
100
16 32 64 128 256 Avg
Speedup
CM-SW
CM-PuM
CM-PuM-SSD
CM-IFP
All three near-data processing systems
improve performance by reducing data movement

## Slide 77: Speedup for Different Query Sizes (2/3)
Query Size (in bits)
106
104
102
100
16 32 64 128 256 Avg
Speedup
CM-SW
CM-PuM
CM-PuM-SSD
CM-IFP
136.9x
CM-IFP outperforms other near-data processing systems
CM-IFP outperforms CM-SW by 136.9x

## Slide 78: Speedup for Different Query Sizes (3/3)
Query Size (in bits)
106
104
102
100
16 32 64 128 256 Avg
Speedup
CM-SW
CM-PuM
CM-PuM-SSD
CM-IFP
136.9x
216.0x
168.9x
122.7x
100.2x
76.6x
CM-IFP speedup decreases with query sizes
due to repeated flash read operations on same data
for circularly shifted queries

## Slide 79: Energy Consumption for Different Query Sizes
Query Size (in bits)
16 32 64 128 256 Avg
Norm. Energy Consumption
CM-SW
100
10-2
10-4
10-6

## Slide 80: Energy Consumption for Different Query Sizes
100
10-2
10-4
10-6
Norm. Energy Consumption
Query Size (in bits)
16 32 64 128 256 Avg
CM-SW
CM-PuM
CM-PuM-SSD
CM-IFP
256.4x
CM-IFP provides 256.4x energy savings over CM-SW
by largely reducing data movement
All three near-data processing systems
provide large energy savings over CM-SW

## Slide 81: More Details in Our Paper
More detailed observations from our evaluation
  Comparison between CM-PuM and CM-PuM-SSD
  Comparison with the Boolean approach
End-to-end system design
  Operations in vertical data layout
  Enabling CIPHERMATCH in commodity SSDs
Overhead analysis of CIPHERMATCH hardware
  Storage overhead (from end-to-end system design)
  Area overhead (~0.6% of baseline NAND-flash memory)
Bitwise operations using NAND-flash memory
  Enabling bitwise operations using latching circuitry
  Exploiting bit-level and array-level parallelism
https://arxiv.org/pdf/2503.08968

## Slide 82: To Summarize …

## Slide 83: Conclusion
A new algorithm-hardware codesign that significantly improves the performance of secure exact string matching algorithm
CIPHERMATCH-SW: 42.9x speedup & 39.4x lower energy than best software
CIPHERMATCH-IFP: 136.9x speedup & 256.4x lower energy than CM-SW
Pack multiple bits of database
and thus eliminate the use of
homomorphic multiplication
Use in-flash processing (IFP)
to accelerate secure exact
string-matching
CIPHERMATCH
Key Results
+ Reduces memory footprint
+ Provides scalable
secure exact string-matching
+ Reduces data movement
+ Leverages bit-level
and array-level parallelism
2
1

## Slide 84
Mayank Kabra
Rakesh Nadig, Harshita Gupta, Rahul Bera, Manos Frouzakis,
Vamanan Arulchelvan, Yu Liang, Haiyu Mao,
Mohammad Sadrosadati, and Onur Mutlu
Accelerating Homomorphic Encryption-Based
String Matching via Memory-Efficient Data Packing
and In-Flash Processing
CIPHERMATCH
arXiv

## Slide 85: Backup slides

## Slide 86: Summary
CM-SW provides 42.9x speedup
over the state-of-the-art approach in real systems
Due to our new memory-efficient data packing scheme
and use of only homomorphic additions
CM-IFP provides 136.9x speedup over CM-SW
and outperforms three near-data processing systems
Due to our new IFP design to perform in-flash operations
and exploiting large-scale bit-level parallelism

## Slide 87: Executive Summary
Problem: Secure exact string matching using homomorphic encryption (HE) operations face performance bottlenecks in two key areas:
High computation cost due to use of complex homomorphic operations (e.g., multiplication)
data movement bottleneck due to large homomorphically encrypted data
Motivation: Reducing memory expansion from HE and performing computation where the database resides can improve the performance of secure exact string matching algorithm
CIPHERMATCH: A novel algorithm-hardware co-design that significantly improves the performance of HE-based secure string matching by using only homomorphic addition and leveraging the operational principles of NAND-flash memory.
Key Results: (i) Software-based CIPHERMATCH implementation (CM-SW) achieves 42.9x speedup over state-of-the-art software approaches
(ii) CIPHERMATCH IFP implementation futher improves upon CM-SW, achieving 136.9x better performance and 256.4x lower energy consumption
Key Idea:
To pack multiple bits of data in the each coefficient of ciphertext
Use in-flash processing (IFP) to perform string matching inside NAND-flash memory
Key Benefits:
+ Reduce memory expansion after encryption
+ Eliminates the use of complex HE operations
+ Reduces data movement bottleneck
Opportunity: (a) Perform memory-efficient packing of the database to reduce the increase in memory footprint after encryption and (b) perform simple computations (e.g., HE addition) inside solid state drives (SSDs – i.e., where the database is stored) to reduce data movement

## Slide 88: Executive Summary
Problem: Secure exact string matching using homomorphic encryption (HE) operations face performance bottlenecks in two key areas:
High computation cost due to use of complex homomorphic operations (e.g., multiplication)
Data movement bottleneck due to large homomorphically encrypted data size
Motivation: Reducing memory expansion from HE and performing computation where the database resides can improve the performance of secure exact string matching algorithm
CIPHERMATCH: A novel algorithm-hardware co-design that significantly improves the performance of HE-based secure exact string matching (a) by using only homomorphic addition and (b) leveraging the operational principles of NAND-flash memory to perform secure exact string matching
Key Results:
(i) Software-based CIPHERMATCH (CM-SW): 42.9× speedup over existing state-of-the-art approaches
(ii) CIPHERMATCH with IFP: 136.9× faster and 256.4× lower energy consumption than CM-SW
Key Idea:
Pack multiple bits of data in the each coefficient of ciphertext
Use in-flash processing (IFP) to perform string matching inside NAND-flash memory
Key Benefits:
+ Reduce memory expansion after encryption
+ Eliminates the use of complex HE operations
+ Reduces data movement bottleneck
Opportunity: (a) Optimize memory usage by packing encrypted data efficiently and (b) perform secure string matching using simple HE operations (addition) inside SSDs, reducing data movement.
Notes: We will discuss with a brief executive summary
[CLICK]
Background is way too much and can be cut down.
Color coordination (Wierd colors)
Make the 1 and 2 and (a) and (b) consistent.
COlor code Key idea and key benefits to show more benefits

## Slide 89: NAND Flash Basics: A Flash Cell
A flash cell stores data by adjusting the amount of charge in the cell
Erased Cell
(Low Charge Level)
1
Programmed Cell
(High Charge Level)
0
Activation
Operates as a resistor
Operates as an open switch

## Slide 90: NAND Flash Basics: A NAND String
A set of flash cells are serially connected to form a NAND String
1
0
0
1
0
…
Bitline (BL)
NAND String

## Slide 91: NAND Flash Basics: A NAND Block
NAND strings connected to different bitlines comprise a NAND block
BL1
BL2
BL3
BL4
BL5
1
0
0
1
0
BLN
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
…
…
…
…
…
WL1
WL2
WL3
WL4
WLM
Block
A single wordline (WL) controls a large number of flash cells: High bit-level parallelism

## Slide 92: NAND Flash Basics: A NAND Plane
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Latches to store flash read data

## Slide 93: Speedup for Different Database Size
CM-SW shows average speedup of 68.1x over prior arithmetic approach
CM-SW speedup decreases as data size exceeds DRAM capacity, primarily due to increased data movement between storage and DRAM.
Query Size of 16 bits
1.2x103x
68.1x
72.1x
72.1x
72.1x
62.2x
62.2x
Encrypted Database Size (in GB)
106
104
102
100
Speedup
8GB 16GB 32GB 64GB 128GB Avg

## Slide 94: Speedup for Different Database Size
CM-IFP shows highest average speedup of 268.3x over CM-SW
CM-SW speedup decreases when data size goes beyond DRAM size due to frequent data movement between storage and DRAM
Query Size of 16 bits
Encrypted Database Size (in GB)
106
104
102
100
Speedup
250.1x
250.1x
250.1x
295.1x
295.1x
268.3x
226.3x
66.5x
8GB 16GB 32GB 64GB 128GB Avg

## Slide 95: Energy Consumption for Different Query Size
CM-IFP shows highest average energy savings of 256.4x over CM-SW
CM-IFP energy efficiency decreases with increasing query sizes due to expensive flash reads
Database Size of 128 GB
Query Size (in bits)
100
10-2
10-4
10-6
Norm. Energy
Consumption
454.5x
370.3x
294.1x
227.2x
156.2x
76.9x
83.3x
256.4x
16 32 64 128 256 Avg

## Slide 96: CIPHERMATCH: NAND-Flash Bitwise Operations
Die#0
Die#1
…
Internal DRAM
SSD Controller
(General Purpose Core)
Flash Controller
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash Controller
Flash Controller
Peripheral Circuitry
Plane#0
Blk#1
Plane#1
Blk#1
Blk#2
Blk#2
..
..
D-Latch
D-Latch
S-Latch
S-Latch
Storage (SSD)
NAND Flash Chip
NAND Flash Read Circuitry
Notes: We can provide it later. Lets breiefly discuss and provide background.

## Slide 97: CIPHERMATCH: NAND-Flash Bitwise Operations
Design proposed by prior work [Cho+, Patent 2022]
Notes: Show the tree structure why people should listen to NAND flash operations.

## Slide 98: CIPHERMATCH: NAND-Flash Bitwise Operations
Bitwise AND of A and B
Data (A) is read and stored in S- latch
Data (A) is transferred from S-latch to D-latch
Similarly data (B) is read and stored in S-latch
1
SO
OUT_D
OUT_S
OUT_S
OUT_D
2
RST_D
SET_D
3
SET_S
1
2
3

## Slide 99: CIPHERMATCH: NAND-Flash Bitwise Operations
Bitwise AND of A and B
SO
OUT_D
OUT_S
OUT_S
OUT_D
RST_D
SET_D
SET_S
D-latch (A) | S-latch (B) | Z
0
0
0 | 0
1
Retains Value
1
1->0
Precharge the bitline to logical 1
0
0 | 1
0
EN
1 | 0
1 | 1
0
1
Precharge the bitline to logical 1
EN
1
Notes: Show the tree structure why people should listen to NAND flash operations.

## Slide 100: Data Movement Bottleneck
Compute-centric systems: Move entire data from storage to CPU/GPU
Main
Memory
(DRAM)
CPU/GPU
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Notes: EXplain this better.
Explain the legends.
Too much gap
Write DRAM size 32GB on top.
Remove the DRAM size.
Remove the (can)

## Slide 101: Motivation (II) – Data Movement Bottleneck
Compute-centric systems: Move entire data from storage to CPU/GPU
Memory-centric systems: Perform computations in main memory
Main
Memory
(DRAM)
CPU/GPU
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Main
Memory
(DRAM)
CPU/GPU
Storage
(NAND Flash-Based SSD)
Storage I/O bandwidth: ~ 8 GB/s
External I/O bandwidth of storage systems
is the main bottleneck for memory intensive application
2
Notes: EXplain this better.
Explain the legends.
Too much gap
Write DRAM size 32GB on top.
Remove the DRAM size.
Remove the (can)

## Slide 102: Motivation (II) – Data Movement Bottleneck
Compute-centric systems: Perform computations in CPU/GPU
Memory-centric systems: Perform computations in main memory
Storage-centric systems: Perform computations inside storage system
Main
Memory
(DRAM)
CPU/GPU
Storage
(NAND Flash-Based SSD)
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
…
…
2
Notes: EXplain this better.
Explain the legends.
Too much gap
Write DRAM size 32GB on top.
Remove the DRAM size.
Remove the (can)

## Slide 103: Motivation (II) – Data Movement Bottleneck
Compute-centric systems: Perform computations in CPU/GPU
Memory-centric systems: Perform computations in main memory
Storage-centric systems: Perform computations inside storage system
Main
Memory
(DRAM)
CPU/GPU
Storage
(NAND Flash-Based SSD)
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
…
…
SSD-internal bandwidth
becomes the new bottleneck for computations
2
Notes: EXplain this better.
Explain the legends.
Too much gap
Write DRAM size 32GB on top.
Remove the DRAM size.
Remove the (can)

## Slide 104: In-Flash Processing (IFP)
Main
Memory
(DRAM)
CPU/GPU
Storage
(NAND Flash-Based SSD)
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
…
…
Perform computations inside NAND-flash chips
by using operational principles of NAND-flash memory
Notes: EXplain this better.
Explain the legends.
Too much gap
Write DRAM size 32GB on top.
Remove the DRAM size.
Remove the (can)

## Slide 105: In-Flash Processing (IFP)
NAND Flash Chip
Latching circuit
Operand O2
Operand O3
…
Operand O32
Bitlines (BLs)
Prior Works ([Gao+, MICRO 2021] , [Park+, MICRO 2022])
perform bitwise operations using the latching circuit
Operand O1
O1
Operand O1
Operand O2
O1 & O2
Notes: EXplain this better.
Explain the legends.
Too much gap
Write DRAM size 32GB on top.
Remove the DRAM size.
Remove the (can)

## Slide 106: Limitations of Prior Works
Boolean Approach [Pradel+, TrustCom 2021 ; Aziz+, Information 2024]
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
High memory footprint due to encryption of individual bits
Boolean
Approach
Low memory footprint due to data packing mechanism
Arithmetic
Approach
m = 1 1 0 1 0 1 1 . . . 1 1 0
m = 1 1 0 1 0 1 1 . . . 1 1 0
Enc(P1(x)) Enc(P2(x)) … Enc(Pn(x))
Enc(b0) Enc(b1) … Enc(bn)
Notes: [CLICK] Many prior works exist for performing secure string matching using both Boolean and arithmetic approaches
[CLICK] However, we analyze different characteristics of these prior works and observe that
[CLICK] Boolean approaches have high memory footprint because we need to encrypt individual bits, [CLICK] whereas in arithmetic approaches,we have lower memory footprint due to the use of data packing mechanisms.

## Slide 107: Limitations of Prior Works
Boolean Approach [Pradel+, TrustCom 2021 ; Aziz+, Information 2024]
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
High memory footprint due to encryption of individual bits
Boolean
Approach
Low memory footprint due to data packing mechanism
Arithmetic
Approach
High computation cost due to large number of HE operations
Low computation cost due to small number of HE operations
Enc(b0) ⊕ Enc(b1) ⊕ Enc(b2) .…. 1000x
Enc(P1(x)) Enc(P2(x)) .…. 10x
✖️ ✖️
Notes: [CLICK] Boolean approaches have overall high computation cost due to more number of HE operations required to perform string matching
[CLICK] Whereas in Boolean approaches, we perform lessnumber of HE operations and achieve lower computation cost as compared to Boolean appraoches

## Slide 108: Limitations of Prior Works
Boolean Approach [Pradel+, TrustCom 2021 ; Aziz+, Information 2024]
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
High memory footprint due to encryption of individual bits
Boolean
Approach
Low memory footprint due to data packing mechanism
Arithmetic
Approach
High computation cost due to large number of HE operations
Low computation cost due to small number of HE operations
Support flexible query sizes due to unlimited computations
Support limited query sizes due to limited computations
Notes: [CLICK] However, Boolean approaches support flexible query sizes because we can perform unlimited computations
[CLICK] Whereas arithmetic approaches can only support limited query sizes because these approaches can perform only limited computations which is defined by multiplicative depth of the algorithm as these algorithms use homomorphic multiplication operations.

## Slide 109: Approaches for HE-based String Matching
Secure string matching using HE can be performed using two key approaches
Boolean Approach
Arithmetic Approach
Encrypt individual bits
e.g., m = 1 1 0 1 0 1 1 . . . 1 1 0
Encrypt multiple packed bits
e.g., m = 1 1 0 1 0 1 1 . . . 1 1 0
P1= b2x2+b1x1+b0 P2(x)= b5x2+b4x1+b3 … Pn(x)
Enc(P1(x)) Enc(P2(x)) … Enc(Pn(x))
Enc(b0) Enc(b1) … Enc(bn)
Encrypt individual bits
Encrypt multiple packed bits
1
1

## Slide 110: Approaches for HE-based String Matching
Secure string matching using HE can be performed using two key approaches
Boolean Approach
Arithmetic Approach
Enc(P1(x)) Enc(P2(x)) … Enc(Pn(x))
1
Encrypt individual bits
Encrypt multiple packed bits
1
Perform homomorphic
XOR and AND operation
Perform homomorphic
multiplication and addition operation
2
2
Enc(b0) Enc(b1) … Enc(bn)
Enc(q0) Enc(q1) … Enc(qn)
Enc(Q1(x)) Enc(Q2(x)) … Enc(Qn(x))
⊕ ⊕ … ⊕
✖️ ✖️ … ✖️
Enc(r0) & Enc(r1) & … & Enc(rn)
Enc(R1(x)) + Enc(R2(x)) +… + Enc(Rn(x))
Result
Result
Notes: [CLICK] In Boolean Approach, [CLICK] we perform homomorphic XOR and [CLICK] AND operation and generate the final result
[CLICK] In arithmetic approach,[CLICK] we perform homomomorphic multiplication and addition operation.

## Slide 111: Prior Works on HE-based String Matching
Boolean Approach [Pradel+, TrustCom 2021 ; Aziz+, Information 2024]
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
High memory footprint due to encryption of individual bits
Boolean
Approach
Low memory footprint due to data packing mechanism
Arithmetic
Approach
m = 1 1 0 1 0 1 1 . . . 1 1 0
m = 1 1 0 1 0 1 1 . . . 1 1 0
Enc(P1(x)) Enc(P2(x)) … Enc(Pn(x))
Enc(b0) Enc(b1) … Enc(bn)
Notes: [CLICK] Many prior works exist for performing secure string matching using both Boolean and arithmetic approaches
[CLICK] However, we analyze different characteristics of these prior works and observe that
[CLICK] Boolean approaches have high memory footprint because we need to encrypt individual bits, [CLICK] whereas in arithmetic approaches,we have lower memory footprint due to the use of data packing mechanisms.

## Slide 112: Prior Works on HE-based String Matching
Boolean
Approach
Arithmetic
Approach
Support flexible query sizes due to unlimited computations
Support limited query sizes due to limited computations
High memory footprint due to encryption of individual bits
Low memory footprint due to data packing mechanism
Boolean Approach [Pradel+, TrustCom 2021 ; Aziz+, Information 2024]
Arithmetic Approach [Yasuda+, CCSW 2013 ; Kim+, TDSC 2017 ; Bonte+, CCS 2020 ]
Notes: [CLICK] However, Boolean approaches support flexible query sizes because we can perform unlimited computations
[CLICK] Whereas arithmetic approaches can only support limited query sizes because these approaches can perform only limited computations which is defined by multiplicative depth of the algorithm as these algorithms use homomorphic multiplication operations.

## Slide 113: Arithmetic Approach Performs Better
Execution Time (in s)
Query Size (in Bits)
Database Size
(64 bytes)
Database Size
(128 bytes)
Database Size
(256 bytes)
(Aziz +, Information 2024) (Yasuda+, CCSW 2013)
Arithmetic approach performs better
with larger database sizes due to fewer HE operations
Notes: Hence, arithmetic approaches scales better with larger database sizes because they use fewer HE operations.

## Slide 114: Latency Breakdown of Arithmetic Approach
Execution Time (in s)
Query Size (in Bits)
Database Size
(64 bytes)
Database Size
(128 bytes)
Database Size
(256 bytes)
(Aziz +, Information 2024) (Yasuda+, CCSW 2013)
Hom. Mult. (98.2%)
Hom.
Add.
(1.8%)
Latency
Breakdown (%)
Notes: We analyze the latency breakdown of arithmetic approach and found that most of the time is spent on performing homomorphic multiplications.

## Slide 115: Key Problem (I): Complex HE Operations
Execution Time (in s)
Query Size (in Bits)
Database Size
(64 bytes)
Database Size
(128 bytes)
Database Size
(256 bytes)
(Aziz +, Information 2024) (Yasuda+, CCSW 2013)
Hom. Mult. (98.2%)
Hom.
Add.
(1.8%)
Latency
Breakdown (%)
Prior arithmetic approaches
use costly homomorphic multiplication operations
which limits the scalabilty of HE-based string matching
Notes: [CLICK] Hence, key problem one is that prior arithmetic approaches use costly homomorphic multiplication operations which incur high computation cost and [CLICK] mitgating homomorphic operations can significanly improves the performance.

## Slide 116: Key Observation
String matching can be performed using addition operation
m = 0 1 0 1 0 0 1 0 1 0 0 1 0 1
+ ~m = 1 0 1 0 1 1 0 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1
Value which can be checked
If we negate the data, add it to the original data,
we get a string of 1 1 1 1’s
Notes: Conventional string matching can be performed using addition operation
[CLICK] e.g., if we negate the data and [CLICK] add it to the original data we receive a static value which can be checked

## Slide 117: Key Observation
Enc( m ) = (5 x1024 + 10 x1023 + …. + 19 , …)
+ Enc(~m ) = (6 x1024 + 11 x1023 + …. + 3 , …)
(11 x1024 + 21 x1023 + …. + 22 , …)
(1111…1x1024 + 1111…1 x1023 + …. + 1111…1)
Secure string matching can be performed using HE addition operation
Decrypt
m = 0 1 0 1 0 0 1 0 1 0 0 1 0 1
+ ~m = 1 0 1 0 1 1 0 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1
Value which can be checked
String matching can be performed using addition operation
Notes: Now this observation can be extended by using HE addition [CLICK], where the data is encrypted and we perform homomorphic addition. Once we decrypt the result we see that final result after decryption contains the static value of 1111

## Slide 118: Key Observation
Enc( m ) = (5 x1024 + 10 x1023 + …. + 19 , …)
+ Enc(~m ) = (6 x1024 + 11 x1023 + …. + 3 , …)
(11 x1024 + 21 x1023 + …. + 22 , …)
(1111…1x1024 + 1111…1 x1023 + …. + 1111…1)
Secure string matching can be performed using HE addition operation
Decrypt
m = 0 1 0 1 0 0 1 0 1 0 0 1 0 1
+ ~m = 1 0 1 0 1 1 0 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1
Value which can be checked
String matching can be performed using addition operation
This output after homomorphic addition
is an encrypted value of 1111’s
that can be used for matching
Notes: Now this observation can be extended by using HE addition [CLICK], where the data is encrypted and we perform homomorphic addition. Once we decrypt the result we see that final result after decryption contains the static value of 1111

## Slide 119: Memory-Efficient Data Packing Scheme
Encode database into multiple plaintext polynomials (P(x))
by packing multiple bits into a single polynomial coefficient
Assume, Database (d) =
e.g., P(x) = 1 0 1 0 1…1 x1024 + 1 0 0 1 0…1 x1023 + …. + 1 1...1 0 1 0 1
1 0 1 0 1 1 1
1 0 0 1 0 1 1
1 1 ... 1 0 1 0 1
1 0 1 0 1 1 1
1 0 0 1 0 1 1
1 1 ... 1 0 1 0 1
1
Client Machine
Server Machine
Result
Storage
(SSD)
CPU
DRAM
Perform String Matching
Matched Index
Encrypted Query
Encrypted Database
Encrypted Database
Query
Data Packing & Encryption
Notes: First, lets assume database d as string of binary values.
[CLICK] We distribute the database and place them into the multiple coefficients of the polynomial. Then we perform encryption to generate the encrypted database and store it in the SSD of server machine.

## Slide 120: CIPHERMATCH: Data Packing Scheme
1
Client Machine
Server Machine
Result
Storage
(SSD)
CPU
DRAM
Perform String Matching
Matched Index
Encrypted Database
0 0 0 1 1 0 0
0 0 0 1 1 0 0
0 0 0 1 1 0 0
Assume, Query (q) =
The query (q) is negated, replicated
and encoded into the plaintext polynomials (Q(x))
1 1 1 0 0 1 1
0 0 0 1 1 0 0
e.g., Q(x) = 0 0 0 1 1…0 x1024 + 0 0 0 1 1…0 x1023 + …. + 0 0 0 1 1…0
Encrypted
Query
Query
Data Packing & Encryption
Notes: Second, we assume a query (q). For query, we negate the query and replicate this query in coefficients of the polynomial. Then we encrypt this query and send this query from client to the server machine.

## Slide 121: CIPHERMATCH: Identify the Match
Secure string matching can be performed using HE addition operation
Decrypt
Enc( m ) = (5 x1024 + 10 x1023 + …. + 19 , …)
+ Enc(~m ) = (6 x1024 + 11 x1023 + …. + 3 , …)
(11 x1024 + 21 x1023 + …. + 22 , …)
(1111…1x1024 + 1111…1 x1023 + …. + 1111…1)
m = 0 1 0 1 0 0 1 0 1 0 0 1 0 1
+ ~m = 1 0 1 0 1 1 0 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1
Value which can be checked
String matching can be performed using addition operation
This output after homomorphic addition
is an encrypted value of 1111’s
that can be used for matching
2
Notes: Now this observation can be extended by using HE addition [CLICK], where the data is encrypted and we perform homomorphic addition. Once we decrypt the result we see that final result after decryption contains the static value of 1111

## Slide 122: CIPHERMATCH: Identify the Match
String matching can be performed using addition operation
m = 0 1 0 1 0 0 1 0 1 0 0 1 0 1
+ ~m = 1 0 1 0 1 1 0 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1 1 1 1 1 1 1
Value which can be checked
Secure String matching can be performed using HE addition operation
2
Enc( m ) = (5 x1024 + 10 x1023 + …. + 19 , …)
+ Enc(~m ) = (6 x1024 + 11 x1023 + …. + 3 , …)
(11 x1024 + 21 x1023 + …. + 22 , …)
(1010…1x1024 + 1111…1 x1023 + …. + 1001…0)
Decrypt
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 123: CIPHERMATCH: Identify the Match
2
Match polynomial = 111…11 x1024 + 111…11 x1023 + …. + 111…11
Encrypt
Match value = (91 x1024 + 24 x1023+ …. + 32 , …)
Enc( m ) = (5 x1024 + 10 x1023 + …. + 19 , …)
+Enc(~q ) = (2 x1024 + 14 x1023 + …. + 3 , …)
(1010…1x1024 + 1111…1 x1023 + …. + 1001…0)
Result = (7 x1024 + 24 x1023 + …. + 22 , …)
Encrypted Database
Encrypted Query
Decrypt
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 124: CIPHERMATCH: Identify the Match
2
Match polynomial = 111…11 x1024 + 111…11 x1023 + …. + 111…11
Encrypt
Match value = (91 x1024 + 24 x1023+ …. + 32 , …)
Enc( m ) = (5 x1024 + 10 x1023 + …. + 19 , …)
+Enc(~q ) = (2 x1024 + 14 x1023 + …. + 3 , …)
(1010…1x1024 + 1111…1 x1023 + …. + 1001…0)
Result = (7 x1024 + 24 x1023 + …. + 22 , …)
Encrypted Database
Encrypted Query
Decrypt
Result = (7 x1024 + 24 x1023 + …. + 22 , …)
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 125: CIPHERMATCH: Identify the Match
2
Compare
Generate Index
Compare the match value
Result = (7 x1024 + 24 x1023 + …. + 22 , …)
Match value = (91 x1024 + 24 x1023+ …. + 32 , …)
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 126: Qualitative Analysis of Prior Work
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 127: System-Level Overview of CIPHERMATCH
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 128: Evaluation Configuration
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation

## Slide 129: Evaluation Configuration
Notes: It should be observation
Say it in simple way ..
Too much text.
Rounded edges , fix the gaps
make it bold.
Entire slide think about it.
Key Observation