## Slide 1
PreLatPUF
CODIC-sig PUF
CODIC: A Low-cost Substrate for Enabling
Custom in-DRAM Functionalities and Optimizations
Lois Orosa1,2, Yaohua Wang3, Mohammad Sadrosadati1, Jeremie Kim1, Minesh Patel1,Ivan Puddu1,
Haocong Luo1, Kaveh Razavi1, Juan Gómez-Luna1, Hasan Hassan1,
Nika Mansouri Ghiasi1, Saugata Ghose4, and Onur Mutlu1
7: PUF Evaluation
2: Motivation
3: Goal
2
1
1: DRAM Background
  Enable new and enhance existing DRAM commands and optimizations by providing a low-cost substrate that enables fine-grained control over DRAM internal circuit timings.
  Design new security mechanisms that have strong security and high performance by using the CODIC substrate.
Limitations of fixed DRAM internal circuit timings
  Chosen at design time and cannot be modified
  Conservative internal circuit timings to ensure reliable operation
  Memory controller does not have any knowledge or control over the internal implementations of DRAM commands
Potential of controlling internal DRAM circuit timings
  Enables more aggressive performance, reliability, and energy optimizations
  Enables new functionalities
  May open new areas of research
Conclusion:
CODIC can be used for implementing very efficient security applications
CODIC Can enable new DRAM functionalities, and reliability, performance, and energy optimizations
Future Research Directions
Security applications
Accelerate Secure deallocation
Accurate control of failure mechanisms used in existing DRAM-based True Random Number Generators (TRGNs)
Reduce de effectiveness of RowHammer attacks
Custom DRAM latency/energy applications
- Adapt to environmental conditions
Mitigate process variation effects
Accurate DRAM characterization
3. Processing in Memory (PIM)
Enable the implementation of robust PIM approaches (e.g., RowClone, Ambit)
3
4
DRAM Chip
Bank
Chip I/O
DRAM Bank
bitline
wordline
…
…
DRAM Cell
Row Buffer
…
…
…
…
SA0
SA1
SAN-1
…
Sense Amplifiers (SAs)
DRAM Cell
ACTIVATE
CODIC substrate enables greater control over DRAM internal circuit timings
CODIC is an efficient and low-cost way to enable new functionalities and optimizations in DRAM
CODIC controls four key signals that orchestrate DRAM internal circuit timings
Activates the DRAM row containing the data
4: CODIC
PRECHARGE
Prepares all bitlines
for a subsequent
ACTIVATE command
to a different row
CODIC-sig generates digital signatures that depend on process variation
Key idea: Amplify a DRAM cell that we set to the precharge voltage (Vdd/2)
Mechanism:
Capacitor is initially set to 0 or Vdd
Raise the wordline signal ( )
Raise the precharge signal ( )
Result: the final value of the cell is the precharge voltage (Vdd/2)
Value = Vdd
Value = Vdd/2
5ns
7ns
CODIC-sig
CODIC-detz
CODIC-det generates deterministic values
Key idea: Activate and with a delay between them
Mechanism:
      Capacitor is initially set to 0 or Vdd
      Raise the wordline
  To generate 0, raise 1) , 2)
  To generate 1, raise 1) , 2)
Result: CODIC-det generates a 0 or 1 value deterministically
5ns
7ns
14ns
Value = 0
Value = Vdd
CODIC-det
5: Applications of CODIC
CODIC can be used in many applications:
Security
Custom Optimizations
Accurate DRAM Characterization
Processing-In-Memory (PIM)
We use CODIC to design two new applications in the security domain:
DRAM Organization
Internal DRAM Signals
DRAM Operations
sense_n controls the NMOS amplifier in the SA
EQ controls the unit that sets the bitline to Vdd/2
wl controls the transistor that connects the cell capacitor to the bitline
sense_p controls the PMOS amplifier in the SA
Application 1: PUF
CODIC-sig can generate signature values in DRAM that can be used as a Physical Unclonable Function (PUF)
  Signatures are unique to a device due to the unique physical variations of the device
  Typically used to authenticate or identify a device
Characteristics of CODIC-sig PUF:
  CODIC-sig has short evaluation latency
  Repeatable PUF responses without relying on a filtering mechanism
  CODIC-sig is resilient to temperature changes, i.e., changing the temperature does not influence much the repeatability of the PUF responses
  CODIG-sig responses do not depend on the content of DRAM
Application 2: Cold Boot Attacks
A cold boot attack is a physical attack on DRAM that involves hot-swapping a DRAM chip and reading out the contents of the DRAM chip on another system
The attacker first disables the power and then transfers the DRAM to another system
Cold boot attacks are possible because the data stored in DRAM is not immediately lost when the chip is powered-off
  Data in DRAM is stored in capacitors, and the data can remain in the cells long enough for it to be stolen
This data retention effect can be even more significant at low temperatures
Observation: It is possible to protect from cold boot attacks by deleting the entire memory content during DRAM power-on
Key Idea: A low cost in-DRAM mechanism based on CODIC that destroys all DRAM content during DRAM power-on
6: Experimental Setup
9: Future Work and Conclusion
Evaluation of 72 real DDR3L (low power) DRAM chips and 64 real DDR3 DRAM chips
SoftMC FPGA-based infrastructure
DRAM Latency PUF
PreLatPUF
w/(w/o) filter
CODIC-sig PUF
w/(w/o) filter
88.2 ms
7.95 (1.59) ms
4.41 (0.88) ms
CODIC Self-d
ChaCha-8
AES-128
~0%
~0%
~0%
Performance
Power
Processor Area
~0%
~0.0%
~17%
~0.9%
~12%
~1.3%
~1.1%
DRAM Area
~0.0%
~0.0%
~0%
~0%
~0%
~0%
~17%
~12%
~1.1%
~0.0%
~0.0%
~0.0%
~1.3%
~0.9%
Overhead
Similar responses to the same challenge
Uniqueness across responses
DRAM Latency PUF
CODIC-sig PUF is 1.8x faster than the best state-of-the-art DRAM PUF
We demonstrate and evaluate two CODIC variants:
Metric: Jaccard indices to measure similarity or uniqueness
8: Cold Boot Attack Evaluation
CODIC-sig PUF is very effective at very similar responses to the same challenge
CODIC-sig PUF maintains uniqueness across responses to different challenges
552.7x
2.5x
2.0x
CODIC-sig destroys the entire content
of DRAM at least 2x faster
than the state-of-the-art
CODIC vs. Full Memory encryption
CODIC has no performance and power overhead at runtime
CODIC has no processor area overhead, and 1.1% DRAM overhead