## Slide 1
CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators
Coherence For NDAs
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Rachata Ausavarungnirun, Kevin Hsieh, Nastaran Hajinazar, Krishna Malladi, Hongzhong Zheng, Onur Mutlu
Application Analysis
Analysis of Existing Coherence Mechanisms
Architecture Support
Evaluation
CoNDA consistently retains most of Ideal-NDA’s benefits, coming within 10.4% of the Ideal-NDA performance
CoNDA significantly reduces energy consumption and comes within 4.4% of Ideal-NDA
  Challenge: Coherence between NDAs and CPUs
DRAM
L2
L1
CPU
CPU
CPU
CPU
NDA
Compute Unit
(1) Large cost of off-chip communication
It is impractical to use traditional coherence protocols
(2) NDA applications generate a large amount of off-chip data movement
1st key observation: CPU threads often concurrently access the same region of data that NDA kernels are accessing which leads to significant data sharing
Graph Processing
Hybrid Databases (HTAP)
  We find not all portions of applications benefit from NDA
1
Memory-intensive portions benefit from NDA
2
Compute-intensive or cache friendly portions should remain on the CPU
Hybrid Database (HTAP)
Transactions
Analytics
Transactions
CPU
CPU
NDA
Analytics
Data Sharing
2nd key observation: CPU threads and NDA kernels typically do not concurrently access the same cache lines
  CPU threads rarely update the same data that an NDA is actively working on
  For Connected Components application, only 5.1% of the CPU accesses collide with NDA accesses
  Poor handling of coherence eliminates much of an NDA’s performance and energy benefits
Chart: Speedup
| CC | Radii | PageRank | CC | Radii | PageRank | arXiV | Gnutella
CPU-only | 1 | 1 | 1 | 1 | 1 | 1 | 1
NC | 0.94123 | 0.81872 | 0.70086 | 0.99483 | 0.75456 | 0.86561 | 0.94018
CG | 0.96362 | 0.76537 | 0.90958 | 1.1083 | 0.99235 | 1.0926 | 1.0091
FG | 1.4356 | 1.3635 | 1.2313 | 1.4923 | 1.3142 | 1.1915 | 1.3808
Ideal-NDA | 1.6953 | 1.7274 | 1.732 | 1.8673 | 1.7818 | 1.95 | 1.8461
GMEAN
Chart: Normalized Energy
| CC | Radii | PageRank | CC | Radii | PageRank | arXiV | Gnutella
CPU-only | 1 | 1 | 1 | 1 | 1 | 1 | 1
NC | 2.7065 | 2.2708 | 2.1343 | 2.1565 | 2.0632 | 2.1008 | 1.6446
CG | 0.84877 | 0.85235 | 0.49211 | 0.77022 | 0.82092 | 0.87097 | 0.70375
FG | 0.93538 | 0.8868 | 0.57887 | 0.83423 | 0.90309 | 0.96058 | 0.87325
Ideal-NDA | 0.65429 | 0.53872 | 0.35878 | 0.65573 | 0.58046 | 0.66718 | 0.55024
GMEAN
CoNDA
  We propose CoNDA, a mechanism that uses optimistic NDA execution to avoid unnecessary coherence traffic
Time
Optimistic-execution
CPU
NDA
Concurrent CPU + NDA Execution
Offload NDA kernel
Send signatures
  Coherence Resolution
Commit or Re-execute
No Coherence Request
Signature
Signature
CPU Thread Execution
Identifying Coherence Violations
Time
CPU
NDA
C1. Wr Z
C2. Rd A
C3. Wr B
N1. Rd X
N2. Wr Y
N3. Rd Z
  Any Coherence Violation?
N4. Rd X
N5. Wr Y
N6. Rd Z
  Any Coherence Violation?
C6. Wr X
C4. Wr Y
C5. Rd Y
  Yes. Flush Z to DRAM
  No. commit NDA operations
Effective Ordering
C1. Wr X
C2. Rd X
C3. Rd Y
C4. Wr Y
C5. Wr Y
C6. Rd Y
N4. Rd Z
N5. Wr Y
N6. Rd X
C7. Wr X
Non-Cacheable Approach
Hybrid Database (HTAP)
Transactions
Analytics
CPU
CPU
Transactions
NDA
Analytics
Data Sharing
  (1) Generates a large number of off-chip accesses
  (2) Significantly hurts CPU threads performance
  NC fails to provide any energy saving and perform 6.0% worse than CPU-only
  Mark the NDA data as non-cacheable
CPU
DRAM
CPU
CPUWriteSet
Shared LLC
Coherence Resolution
L1
NDA Core
L1
NDAReadSet
NDAWriteSet
High Level Architecture of CoNDA
CPU
CPUWriteSet
Shared LLC
Coherence Resolution
L1
NDA Core
NDAReadSet
NDAWriteSet
L1
Per-word dirty bit mask to mark all uncommitted data updates
The NDAReadSet and NDAWriteSet are used to track memory accesses from NDA
Optimistic Execution
Chart: Speedup
| CC | Radii | PR | CC | Radii | PR | CC | Radii | PR | 128 | 256 |  | arXiV | Gnutella | Enron | HTAP |
CPU-only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
NDA-only | 0.98 | 0.95 | 0.91 | 1.08 | 1.04 | 0.98 | 1.12 | 1.08 | 1.03 | 1.21 | 1.16 | 1.087
FG | 1.4356 | 1.3635 | 1.2313 | 1.4923 | 1.3142 | 1.1915 | 1.4984 | 1.4428 | 1.3267 | 1.4189 | 1.5174 | 1.3808
CoNDA | 1.5379 | 1.5265 | 1.4968 | 1.6931 | 1.4968 | 1.6658 | 1.6146 | 1.7593 | 1.8746 | 1.6785 | 1.8871 | 1.6521
Ideal-NDA | 1.6953 | 1.7274 | 1.732 | 1.8673 | 1.7818 | 1.95 | 1.7287 | 2.0488 | 2.1901 | 1.718 | 1.9359 | 1.8461
GMEAN
Chart: Normalized Energy
| CC | Radii | PR | CC | Radii | PR | CC | Radii | PR | 128 | 256 |  | arXiV | Gnutella | Enron | HTAP |
CPU-only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FG | 0.93538 | 0.8868 | 0.57887 | 0.83423 | 0.90309 | 0.96058 | 0.97241 | 0.86624 | 1.003 | 0.90661 | 0.84601 | 0.87325
CoNDA | 0.69544 | 0.57062 | 0.40155 | 0.68142 | 0.62119 | 0.80684 | 0.59502 | 0.58163 | 0.83249 | 0.32069 | 0.47677 | 0.57782
Ideal-NDA | 0.65429 | 0.53872 | 0.35878 | 0.65573 | 0.58046 | 0.76718 | 0.56841 | 0.54125 | 0.83217 | 0.31346 | 0.47235 | 0.55024
GMEAN
CPU
CPUWriteSet
Shared LLC
Coherence Resolution
L1
NDA Core
NDAReadSet
NDAWriteSet
L1
Address
…
1
1
0
0
0
1
1
1
0
0
0
1
hk-1
h1
h0
…
NDAReadSet
CPUWriteSet
Conflict
If conflicts happens:
The CPU flushes the dirty cache lines that match addresses in the NDAReadSet
NDA invalidates all uncommitted cache lines
Signatures are erased and NDA restarts execution
If no conflicts:
  Any clean cache lines in the CPU that match an address in the NDAWriteSet are invalidated
  NDA commits data updates
Coherence Resolution
Bloom filter based signature has two benefits:
Allows us to easily perform coherence resolution
Allows for a large number of addresses to be stored within a fixed-length register
Fine-Grained Coherence
CPU
CPU
NDA
High amount of off-chip coherence Traffic
  FG eliminates 71.8% of the energy benefits of an ideal NDA mechanism
  Using fine-grained coherence has two benefits:
1
Simplifies NDA programming model
2
Allows us to get permissions for only the pieces of data that are actually accessed
Coarse-Grained Coherence
CPU
CPU
NDA
  Get coherence permission for the NDA region
  Unnecessarily flushes a large amount of dirty data
  Use coarse-grained locks to provide exclusive access
Access to NDA data
CPU
NDA
Time
STALL
  Blocks CPU threads when they access NDA data regions
  CG fails to provide any performance benefit of NDA and perform 0.4% worse than CPU-only