## Slide 1: COSM: A Cooperative Scheduling Framework for Concurrent PIM and CPU Execution on Mobile Devices
ISCA’ 2026
Shanghai Jia Tong University | Shanghai Qi Zhi Institute ETH Zurich | Tsinghua University | Beihang University
ISCA 2026
June 27– July 1, 2026
Raleigh, USA
sjtuzyl@sjtu.edu.cn , liufangxin@sjtu.edu.cn, ljiang_cs@sjtu.edu.cn
August 2, 2026
Yilong Zhao(Speaker)*, Fangxin Liu*, Onur Mutlu, Mingyu Gao, Jian Liu, Haibing Guan, Li Jiang†
* Co-first Author
† Corresponding Author
Notes: Thank you for the introduction. hello everyone.
I am delighted to present our work COSM.

## Slide 2: Overview
Background: LLM inference with PIM on mobile devices
Notes: This is an overview of our work. We focus on large model inference with PIM on mobile devices.

## Slide 3: Overview
Background: LLM inference with PIM on mobile devices
Goal：Co-scheduling CPU & PIM to maximize overall bandwidth utilization
 Cooperative scheduling framework – Interface + Scheduling
Insight: Complementary Bandwidth Occupation
  CPU/PIM workload: High/Low External BDW; Low/High Internal BDW
Notes: Our key insight is that CPU and PIM workloads have complementary bandwidth occupation. Therefore, our goal is to co-schedule these two workloads to maximize overall bandwidth utilization.

## Slide 4: Overview
Background: LLM inference with PIM on mobile devices
Goal：Co-scheduling CPU & PIM to maximize overall bandwidth utilization
 Cooperative scheduling framework – Interface + Scheduling
Insight: Complementary Bandwidth Occupation
  CPU/PIM workload: High/Low External BDW; Low/High Internal BDW
Challenges → Solutions：
1 The dilemma of fixed-length PIM execution command Interface
2 PIM data transfers starve CPU access under conventional scheduling
3 Achieve high CPU & PIM performance
1 Low-interference Interface
  1.1 Preemptable PIM Execution
  1.2 Bandwidth-decoupled Data Transfer
2 Idleness-aware Memory Scheduling
2.1 Idle time window estimate
2.2 Scheduling strategy
Notes: To achieve this, we design a cooperative scheduling framework with both interface and scheduling policy optimizations. We address three key challenges on the interference of the interface and the scheduling policy, and give solutions in our framework.

## Slide 5: Overview
Background: LLM inference with PIM on mobile devices
Goal：Co-scheduling CPU & PIM to maximize overall bandwidth utilization
 Cooperative scheduling framework – Interface + Scheduling
Insight: Complementary Bandwidth Occupation
  CPU/PIM workload: High/Low External BDW; Low/High Internal BDW
Evaluation：Ramulator2 simulation | 2-Channel LPDDR5 | Mobile APP + LLM
Results：2.8x PIM Throughput with only 2% CPU Degradation.
Challenges → Solutions：
1 The dilemma of fixed-length PIM execution command Interface
2 PIM data transfers starve CPU access under conventional scheduling
3 Achieve high CPU & PIM performance
1 Low-interference Interface
  1.1 Preemptable PIM Execution
  1.2 Bandwidth-decoupled Data Transfer
2 Idleness-aware Memory Scheduling
2.1 Idle time window estimate
2.2 Scheduling strategy
Notes: We evaluate on the Ramulator2 simulator, our design achieves a 2.8x PIM speedup with only 2% CPU degradation.

## Slide 6: LLM Inference on Mobile
Privacy &
Data Sovereignty
Real-time Response
Cost Efficiency & Scalability
These Requirements Demand Mobile LLM Inference
Notes: Then I will go through our work, starting with the background. The requirement of Privacy, Latency, and Cost Requirements demand Mobile LLM Inference

## Slide 7: LLM Decoding is Memory Bound
LLM decoding is inefficient on NPU/GPU because of limited bandwidth!
Limited resource on mobile  Batch size =1  Decoding is memory bound
Memory Bound
>80% time
>70% energy
on data transfer
Samsung [HCS’23]
Notes: Due to the limited resources, the batch size of the inference always be one, so the the decoding phase is memory-bound.
Technique reports shows most of the time and energy are on data transfer

## Slide 8: DRAM-based Processing-in-Memory (PIM)
PIM: Integrate Computing Units in DRAM Banks
PIM achieve high bandwidth through parallel access
Serialized
Parallel
8~16x Bandwidth
Data source: Samsung
Notes: Processing-in-Memory, or PIM, provides a solution. Computing units are integrated into DRAM banks, so they can access banks in parallel. PIM have high memory bandwidth, and fit for large model inference.

## Slide 9: CPU-PIM Memory Contention
Mobile device faces limited resource  CPU & PIM should share memory
Notes: Due to the limited resources, CPU and PIM should share the DRAM memory on mobile device.

## Slide 10: CPU-PIM Memory Contention
Mobile device faces limited resource  CPU & PIM should share memory
CPU & PIM face memory access contention
DRAM Memory
Contention
Game (CPU APP)
Voice Assistant (PIM APP)
Significant performance degradation is unacceptable
Notes: So CPU and PIM will face memory access contention.
Under contention, any significant performance degradation is unacceptable, particularly for native CPU applications.

## Slide 11: CPU-PIM Memory Contention
Mobile device faces limited resource  CPU & PIM should share memory
How to maximize the utilization of available bandwidth resources?
CPU & PIM face memory access contention
DRAM Memory
Contention
Game (CPU APP)
Voice Assistant (PIM APP)
Significant performance degradation is unacceptable
Notes: So how can we maximize the utilization of bandwidth under this situation?

## Slide 12: PIM & CPU Workload: Inefficient Bandwidth Use
High External Bandwidth ↑
Low Internal Bandwidth ↓
Low External Bandwidth ↓
High Internal Bandwidth ↑
External bandwidth: memory bus bandwidth | Internal bandwidth: aggregated bank bandwidth
CPU Workload:
Only accesses
PIM Workload:
A few accesses + Massive executions
Notes: On the left, During CPU accesses, data from all banks goes serially through the external memory bus. So, even when the external memory bus bandwidth is saturated, internal bank bandwidth remains underutilized.
In contrast, on the right, PIM workload consumes more internal bandwidth. This indicate a complementary bandwidth occupation.

## Slide 13: PIM & CPU Workload: Inefficient Bandwidth Use
High External Bandwidth ↑
Low Internal Bandwidth ↓
Low External Bandwidth ↓
High Internal Bandwidth ↑
External bandwidth: memory bus bandwidth | Internal bandwidth: aggregated bank bandwidth
CPU Workload:
Only accesses
PIM Workload:
A few accesses + Massive executions
Goal: Co-scheduling CPU & PIM workloads to exploit both internal & external bandwidth
Notes: So we can co-schedule these two workloads to fully exploit both internal and external memory bandwidth

## Slide 14: PIM Command Support
PIM Execution
PIM Data Transfer (between Banks)
Vectors
Weights
Results
weight
Results
via extended DRAM command
via normal read/write command
PIM units can only access local bank
Notes: Since PIM can only access local bank, a PIM system needs two types of commands, PIM execution and PIM data transfer.
PIM execution is implemented via extended DRAM command, while PIM data transfer are normal read/write access.

## Slide 15
Interface Analysis I:
Interference between PIM Execution & CPU Access
Notes: To achieve our goal, we first made key observations to identify design constraints. We first analysis the interference between PIM Execution and CPU access.

## Slide 16: Observation 1
PIM interference on CPU access latency:
CPU access only:
Define Command Length: # Cycles of PIM Execution
Notes: When there is only CPU, CPU access is processed immediately when it comes.

## Slide 17: Observation 1
CPU access only:
With PIM execution:
Define Command Length: # Cycles of PIM Execution
PIM interference on CPU access latency:
Notes: However, with PIM in the system, if a PIM execution is still running when the access comes, there will be an additional read latency.

## Slide 18: Observation 1
CPU access only:
With PIM execution:
With a Shorter PIM Execution:
Define Command Length: # Cycles of PIM Execution
PIM interference on CPU access latency:
Notes: and, shorter PIM execution will lead to lower latency.

## Slide 19: Observation 1
CPU Workloads
Latency ↑
Performance ↓
CPU workload is sensitive to read latency
PIM execution should be Short
Experimental Setup:
Inject Additional Read Latency in Ramulator2 Simulator
Notes: To see how this latency affects CPU workload, we injected read latencies to see the CPU performance.
As shown in the right figure, Even a moderate 128-cycle delay severely degrades CPU performance. So, CPU workload is sensitive to read latency, PIM execution must be short

## Slide 20: Observation 2
PIM underutilization due to bus pressure:
Short PIM execution command:
Idle before rounded back
Notes: While the command length also affects PIM's performance.
The memory controller needs to sequentially issue PIM execution to each bank. As shown in this figure, if it is too short, a bank finishes and stay idle before the memory controller can round back to it.

## Slide 21: Observation 2
PIM underutilization due to bus pressure:
Short PIM execution command:
Notes: This creates a contention on the command bus, leaving internal bandwidth underutilized.

## Slide 22: Observation 2
PIM underutilization due to bus pressure:
Short PIM execution command:
Long PIM execution command:
Notes: In contrast, longer command is better: it keep the banks busy, and avoid bus contention.

## Slide 23: Challenge 1
Challenge 1: Dilemma of fixed-length commands
Command Length | CPU | PIM
Short | Low latency √ | Bus Contention×
Long | High Latency× | High Throughput√
Notes: In summary: CPU workloads prefer shorter PIM executions, while PIM workloads prefer longer ones. This is the dilemma of conventional, fixed-length PIM execution designs

## Slide 24
Interface Analysis II:
Interference between PIM Data Transfer & CPU Access
Notes: Our next observation focuses on interference between PIM data transfer and CPU access,

## Slide 25: Observation 3
Co-schedule PIM data transfer and CPU access:
CPU access:
Random, Sporadic
PIM data transfer:
Contiguous, Bursty
CPU Access v.s. PIM Transfer
Notes: So CPU accesses are usually random and sporadic. But PIM data transfers are typically contiguous and bursty, so it have a high row-hit rate.

## Slide 26: Observation 3
Co-schedule PIM data transfer and CPU access:
Co-schedule CPU & PIM
Only CPU
CPU access:
Random, Sporadic
PIM data transfer:
Contiguous, Bursty
CPU Access v.s. PIM Transfer
FR-FCFS:
(First-ready, First-Come First-Serve)
A conventional memory scheduling policy
Always Row Hit!
Starved!
Notes: So, if we co-schedule them using a conventional FR-FCFS scheduler, this high row-hit rate of PIM data transfers will starve CPU accesses. As shown in this figure, the CPU's read request, R3, is delayed compared to the CPU only case, because the memory controller prioritizes the row hit.

## Slide 27: Observation 3
Co-schedule PIM data transfer and CPU access:
Case2: Co-schedule
Case1: CPU Only
CPU access:
Random, Sporadic
PIM data transfer:
Contiguous, Bursty
CPU Access v.s. PIM Transfer
FR-FCFS:
(First-ready, First-Come First-Serve)
A conventional memory scheduling policy
Always Row Hit!
Starved!
Challenge 2: PIM Data transfers starve CPU access
Notes: So this is our second major challenge

## Slide 28
Scheduling Analysis III:
Unbalanced CPU Access & PIM Execution
Notes: Next, I will analyze two previous scheduling methods that fails to balance CPU and PIM performance.

## Slide 29: Previous Work 1
Row-hit-aware Scheduling:
Switch between CPU/PIM queue when row close
Notes: So this method is row-hit-aware scheduling. This method only switches between CPU and PIM queues only when row closed.

## Slide 30: Previous Work 1
Row-hit-aware Scheduling:
Switch between CPU/PIM queue when row close
Not Hit! Row Close
 Switch to PIM Queue
CPU Access:
Low row hit rate
Notes: In this case, If a access did not hit the row, then the row is closed and switch to PIM queue.

## Slide 31: Previous Work 1
Row-hit-aware Scheduling:
Switch between CPU/PIM queue when row close
PIM Execution:
High row hit rate
CPU Access:
Low row hit rate
CPU Stalled
Notes: But PIM execution also have high row-hit rate. So we always issues more PIM execution.

## Slide 32: Previous Work 1
Row-hit-aware Scheduling:
Switch between CPU/PIM queue when row close
Biased to PIM Performance
PIM Execution:
High row hit rate
CPU Access:
Low row hit rate
CPU Stalled
Notes: So this method is biased to PIM.

## Slide 33: Previous Work 2
CPU-first Scheduling:
Only switch to PIM queue when CPU queue is empty
Notes: On the other extreme is CPU-first scheduling. It only switches to PIM when the CPU queue is empty.

## Slide 34: Previous Work 2
CPU-first Scheduling:
Only switch to PIM queue when CPU queue is empty
Switch to CPU Queue
Notes: When a CPU access comes, it immediately switched to CPU Queue

## Slide 35: Previous Work 2
CPU-first Scheduling:
Only switch to PIM queue when CPU queue is empty
Processing earlier accesses from other banks
Underutilized
Notes: However, if the memory bus is still busy processing earlier accesses from other banks,
when switched to CPU, that CPU read is delayed anyway, and internal bandwidth is underutilized.

## Slide 36: Previous Work 2
CPU-first Scheduling:
Only switch to PIM queue when CPU queue is empty
Delayed Switch is Better
Issue more PIM executions
Notes: A better way is to delay the switch and issue more PIM commands.

## Slide 37: Previous Work 2
CPU-first Scheduling:
Only switch to PIM queue when CPU queue is empty
Biased to CPU Performance
Notes: So in summary, this method is too biased toward CPU.

## Slide 38: Challenge 3
Challenge 3: Simultaneously achieve high CPU & PIM performance
Row-hit-aware:
Biased to PIM
CPU-first:
Biased to CPU
Notes: This leads to our third challenge: how to achieve high performance for both CPU and PIM.

## Slide 39: COSM: A Cooperative Scheduling Framework
Co-optimize Interface & Scheduling
Solution
Challenge
Notes: In our proposed framework COSM, we co-optimize the interface and scheduling to solve the three challenges.

## Slide 40: COSM: A Cooperative Scheduling Framework
Co-optimize Interface & Scheduling
Solution
Challenge
 |  | Low-interference Interface
1 Dilemma of fixed-length commands |  | Preemptable PIM Execution
2 PIM data transfers starve CPU access |  | Bandwidth-decoupled Data Transfer
Notes: For the first two challenges, we design a low-interference interface.

## Slide 41: COSM: A Cooperative Scheduling Framework
Co-optimize Interface & Scheduling
Solution
Challenge
 |  | Low-interference Interface
1 Dilemma of fixed-length commands |  | Preemptable PIM Execution
2 PIM data transfers starve CPU access |  | Bandwidth-decoupled Data Transfer
3 Balance CPU & PIM performance |  | Idleness-aware Memory Scheduling
Notes: For the third challenge, we propose an idleness-aware memory scheduling to balance both CPU and PIM performance.

## Slide 42: Interface— 1.1 Preemptable PIM Execution (1)
Solution of Challenge 1: Fixed-length  Preemptable
Notes: This is our solution for Challenge 1. The challenge is due to the fixed-length, So our solution is to make it preemptable.

## Slide 43: Interface— 1.1 Preemptable PIM Execution (1)
Solution of Challenge 1: Fixed-length  Preemptable
Notes: This shows the current fix-length design, with short PIM execution, results in high bus occupation.

## Slide 44: Interface— 1.1 Preemptable PIM Execution (1)
Solution of Challenge 1: Fixed-length  Preemptable
New module in PIM:
PIM Exec Engine (PEE)
PEE take over and send PIM execution
Memory Bus is released
Notes: While in the preemptable PIM execution, we introduce a PIM Execution Engine inside the PIM. when a PIM task arrives, the engine takes over and automatically issues commands to the PIM units. And the memory bus is released.

## Slide 45: Interface— 1.1 Preemptable PIM Execution (2)
CPU access preempts PIM execution
1. Memory controller send a PIM_Pause to freeze PEE
PEE is frozen, stop issuing
Timely CPU Access
Notes: if a CPU access arrives for example at this tick at this red line, the memory controller sends a PIM pause command, The execution engine stops, allowing timely CPU access

## Slide 46: Interface— 1.1 Preemptable PIM Execution (2)
CPU access preempts PIM execution
1. Memory controller send a PIM_Pause to freeze PEE
After CPU accesses are done:
2. Memory controller resend PIM_Exec to resume PEE
Resume from the frozen counters
Notes: Once CPU access finished, the engine resumes and finish the execution.

## Slide 47: Interface— 1.2 Bandwidth-decoupled Data Transfer (1)
Should prioritize CPU access over PIM data transfer to avoid CPU access starving
Notes: Now for the 2nd, Challenge We should prioritize CPU accesses to avoid them starving

## Slide 48: Interface— 1.2 Bandwidth-decoupled Data Transfer (1)
But using normal access command for PIM data transfer is NOT efficient.
Because it requires strict timing synchronization:
1 The external bus must be idle
2 AND the target row of internal bank must be pre-opened
→ Missing any window leads to transfer failure.
Should prioritize CPU access over PIM data transfer to avoid CPU access starving
Notes: However, such a priority rule is inefficient because conventional PIM transfers requires strict timing synchronization. The bus should be idle and the target row of the internal bank must be pre-opened.

## Slide 49: Interface— 1.2 Bandwidth-decoupled Data Transfer (1)
But using normal access command for PIM data transfer is NOT efficient.
Because it requires strict timing synchronization:
1 The external bus must be idle
2 AND the target row of internal bank must be pre-opened
→ Missing any window leads to transfer failure.
Should prioritize CPU access over PIM data transfer to avoid CPU access starving
Numerous idle windows exist, but they are scarcely concurrent.
Notes: and like this figure shows, Numerous idle windows exist, but they are scarcely concurrent.

## Slide 50: Interface— 1.2 Bandwidth-decoupled Data Transfer (2)
Conventional (through normal access)
Occupy both external & internal
Solution: Decouple internal (bank) & external (bus) bandwidth occupation
Notes: Our solution is to eliminate this constraint by decoupling the internal and external bandwidth occupation.
In the conventional method, each data transfer command occupies both external and internal bandwidth

## Slide 51: Interface— 1.2 Bandwidth-decoupled Data Transfer (2)
Conventional (through normal access)
Bandwidth-decoupled Data Transfer
External only
Host <->PIM Buffer
Occupy both external & internal
Internal only
PIM Buffer<-> Bank
Solution: Decouple internal (bank) & external (bus) bandwidth occupation
Notes: Our design decouples these two stages: We first write data into a buffer, which only occupies external bandwidth.

## Slide 52: Interface— 1.2 Bandwidth-decoupled Data Transfer (2)
Conventional (through normal access)
Bandwidth-decoupled Data Transfer
External only
Host <->PIM Buffer
Occupy both external & internal
Internal only
PIM Buffer<-> Bank
Solution: Decouple internal (bank) & external (bus) bandwidth occupation
Notes: Then, data is transferred from the buffer to the bank, which only occupies internal bandwidth.

## Slide 53: Interface— 1.2 Bandwidth-decoupled Data Transfer (2)
Conventional (through normal access)
Bandwidth-decoupled Data Transfer
External only
Host <->PIM Buffer
Occupy both external & internal
Internal only
PIM Buffer<-> Bank
Solution: Decouple internal (bank) & external (bus) bandwidth occupation
Effect: Decouple external bus traffic from internal bank traffic,
enabling opportunistic scheduling
Notes: By decoupling them, we enable opportunistic scheduling: we transfer externally when the bus is idle, and internally when the bank is idle. This maximizes overall bandwidth utilization."

## Slide 54: 2 Idleness-aware Memory Scheduling (1)
Locate CPU access idle windows, insert PIM command into the windows
Notes: To achieve high CPU and PIM performance, we propose an idleness-aware memory scheduling policy. this policy estimates idle time windows between CPU accesses and insert PIM commands into them.

## Slide 55: 2 Idleness-aware Memory Scheduling (1)
Locate CPU access idle windows, insert PIM command into the windows
IWE: Analysis Mem Queue, estimate idle windows
Notes: The key component is the Idle Window Estimator. It analyzes the CPU queue to estimate upcoming idle windows

## Slide 56: Idle Window Estimator (IWE)
1
2
3
4
5
6
7
8
Notes: This shows how it works. Given a CPU queue, the IWE first predict the issue order of the current CPU accesses. Note that we do not need to really simulate the CPU scheduler, we only predict according to the feature of scheduler, for example, FR-FCFS prefers how hit and rank hit.

## Slide 57: Idle Window Estimator (IWE)
Notes: With the order, we can estimate the idle time window of memory bus and every bank.

## Slide 58: Idle Window Estimator (IWE)
If the window is larger than a threshold, scheduler will
Insert PIM commands exactly to the idle time window (Avoid bias to PIM)
Delay CPU Pre-charge and send more PIM Execution (Avoid bias to CPU)
Use these information
Notes: With this information ,the scheduler will insert PIM commands only to the idle time window to avoid bias to PIM, or delay CPU precharge and send more PIM execution to avoid bias to CPU

## Slide 59: More in the Paper
Extended analysis of related work (All-bank PIM interface)
In-depth details on idleness-aware scheduling, including:
  Algorithm for estimating idle time windows
  Overlapped execution phase to better utilize idle time windows
Discussion on the implications for the software stack
Notes: You can find these details in the paper, including extended analysis of more previous work, and more details on some tricks of memory scheduling.

## Slide 60: Experimental Setup
Benchmarks:
  PIM Benchmarks: BLOOM-1B1, DeepSeek-R1-1.5B, and Qwen2-0.5B.
  CPU Benchmarks: 6 mobile APPs, 3 PolyBench (contiguous access), 3 SPEC 2017
Baselines:
ASYNCDIMM [HPCA’25]:row-hit-aware scheduling
Chopim [ISCA’20]: CPU-first scheduling
System Configuration:
Simulation:
CPU model: collect trace on a mobile phone
DRAM model: Ramulator2
Proposed Scheduling Modules: Synopsys DC
System Configuration | 
CPU | 8 cores @2.1Hz on average (Follow Xiaomi 11 Pro)
DRAM | LPDDR5, 2 Channel*2 Ranks
PIM | 32GOPS, 64 per Rank (Follow Samsung LPDDR5-PIM)
Notes: This is the experimental setup. We use mobile appes and large language models as CPU and PIM benchmarks, and compare COSM against the two baseline scheduling method. We simulated with ramulator2 simulator and the system configuration follows a mobile phone,

## Slide 61: Result: CPU Performance
CPU Degradation:
LLM: BLOOM 1b1
More results in paper: Results on other LLM models
AsyncDIMM (Row-hit-aware): > 90%
COSM: 2.0%
Chopim(CPU-first): <3%
Notes: This is the CPU performance, the Row-hit-aware scheduling have more than 90% degradation on CPU performance. While CPU-first scheduling have only 3% degradation. Thanks to the scheduling framework, COSM have only 2% CPU degradation.

## Slide 62: Result: PIM Performance
PIM Performance:
LLM: BLOOM 1b1
More results in paper: Results on other LLM models
COSM achieves 2.8x PIM Throughput with only 2% CPU Degradation.
COSM
2.8x over Chopim
(CPU-first)
1.4x over AsyncDIMM
(Row-hit-aware)
Notes: For PIM performance, COSM achieve 2.8x over CPU-first scheduling. So COSM achieve a balance between CPU and PIM performance.

## Slide 63: Result: The Effect of Preemptable Execution
Fixed-length commands:
Length = 32:
0.7 x Max PIM Performance
CPU Degradation < 5%
Length = 64:
Max PIM Performance
CPU Degradation > 5%
-- Trade-off
PIM workload: KQV gen of DeepSeek (Exclude data transfer)
Degradation > 5%
(length=64)
0.7x Performance
(length=32)
Notes: This experiment compare the fixed-length command and our preemptable interface. For fixed-length commands, the PIM performance saturates when > 64, but CPU performance declines > 5% at this length.

## Slide 64: Result : The Effect of Preemptable Execution
Breaks the CPU-PIM trade-off
Preemptable commands:
Max PIM Performance
CPU Degradation < 5%
More results in paper: Results on other LLM models
PIM workload: KQV gen of DeepSeek (Exclude data transfer)
Max PIM Performance
Degradation < 5%
Notes: While our preemptable commands can achieve the maximized PIM performance, while CPU performance declines is smaller than 5%. So our, Preemptable Execution breaks the CPU-PIM trade-off.

## Slide 65: Result: Effect of Idleness-aware Scheduling
Unavailable bandwidth: too short to be utilized
Available bandwidth: usable idle time windows
Utilized bandwidth: utilized for PIM execution by scheduler
COSM can better utilize the idle time windows
Result:
COSM leaves < 1% available bandwidth unused
PIM workload: Attention of DeepSeek，only PIM Execution
Notes: This experiment plots the effectiveness of idleness-aware scheduling. The scheduling leaves only 1% available bandwidth unused.

## Slide 66: Area
Components | Area | Overhead
Original Memory Controller | ~0.93mm2 | -
PIM Scheduler | 0.014 mm2 | 
Idle Time Estimator | 0.0085 mm2 | 
Command Arbiter | 0.0054 mm2 | 
PIM Queues | 0.041 mm2 | 
Total | 0.069 mm2 | 7.4%
Synthesized with Synopsys Design Compiler; scaled to 5nm
Notes: The area overhead of the modules in memory controller is around 7.4%. which is moderate.

## Slide 67: Conclusion
A Cooperative Scheduling Framework for Concurrent PIM & CPU Execution on Mobile Devices.
Results： 2.8x PIM Throughput with only 2% CPU Degradation.
Critical contributions：
  Low-interference Interface
  Idleness-aware Memory Scheduling
Artifacts Available
Artifacts Evaluated - Functional
Results Reproduced
Notes: This is the summary We propose a cooperative scheduling framework for concurrent CPU and PIM execution. The framework co-optimize both interface and scheduling policy.
Results shows 2.8x PIM speedup with only 2% CPU performance degradation.

## Slide 68
Thank You!

## Slide 69: COSM: A Cooperative Scheduling Framework for Concurrent PIM and CPU Execution on Mobile Devices
ISCA’ 2026
Shanghai Jia Tong University | Shanghai Qi Zhi Institute ETH Zurich | Tsinghua University | Beihang University
ISCA 2026
June 27– July 1, 2026
Raleigh, USA
sjtuzyl@sjtu.edu.cn , liufangxin@sjtu.edu.cn, ljiang_cs@sjtu.edu.cn
August 2, 2026
Yilong Zhao(Speaker)*, Fangxin Liu*, Onur Mutlu, Mingyu Gao, Jian Liu, Haibing Guan, Li Jiang†
* Co-first Author
† Corresponding Author
Notes: Hello everyone, today I'm going to present COMET, a cooperative scheduling framework for concurrent PIM and CPU execution on mobile devices.