## Slide 1: CROW A Low-Cost Substrate for Improving DRAM Performance, Energy Efficiency, and Reliability
Hasan Hassan Minesh Patel Jeremie S. Kim A. Giray Yaglikci Nandita Vijaykumar Nika Mansouri Ghiasi Saugata Ghose Onur Mutlu
Session 2A: Memory and Storage (Monday 2:00 pm at North 221 ABC)
Notes: Hi, my name is Hasan and I am from ETH Zurich.
I will present a brief overview of our paper that appears at ISCA 2019, entitled
CROW: a low-cost substrate for improving DRAM performance, energy efficiency, and reliability.

## Slide 2: Challenges of DRAM Scaling
access latency
refresh overhead
exposure to vulnerabilities
1
2
3
Notes: DRAM offers high memory capacity at low cost.
However, process technology scaling introduces three key challenges to DRAM [CLICK]
First, high DRAM access latency is a bottleneck for improving system performance and energy efficiency. [CLICK]
Second, as the number of cells in a DRAM chip increases, DRAM refresh overheads incur more performance and energy overheads. [CLICK]
Third, as process technology shrinks, DRAM cells become smaller and get closer to each other. The increasing interference between cells exposes DRAM to vulnerabilities such as RowHammer, which reduce DRAM reliability.

## Slide 3: Conventional DRAM
DRAM Subarray
sense amplifier
Notes: A conventional DRAM chip is composed of multiple subarrays. DRAM cells in a subarray are organized as a two-dimensional array.
To access a cell, a DRAM row has to be activated. [CLICK] A row activation results in loading the row’s data into the sense amplifiers, where read and write operations can be performed.

## Slide 4: Copy Row DRAM (CROW)
Row copy
Multiple row activation
DRAM Subarray
sense amplifier
Notes: To address the scaling challenges of conventional DRAM, we propose a flexible substrate which we call CROW.
CROW slightly modifies the DRAM subarray by introducing copy rows in addition to the regular rows in conventional DRAM. The copy rows have their own address decoders and they can be activated independently from the regular rows.
The CROW substrate enables two key operations. [CLICK]
First, it enables duplicating an entire regular row to a copy row within the subarray. This operation is simply performed by following a regular row activation with a copy row activation. [CLICK]
Second, CROW enables simultaneously activating a regular row and a copy row. If the two rows contain the same data, this operation results in low latency activation. This is because two rows share more charge with the sense amplifiers and as a result the sense amplifiers operate faster.

## Slide 5: Use Cases of CROW
CROW-cache
  reduces access latency
CROW-ref
  reduces DRAM refresh overhead
A mechanism for protecting against RowHammer
weak
strong
Notes: The CROW substrate is flexible and can be used to enable a variety of mechanisms.
In this work, we discuss and evaluate two mechanisms. First, [CLICK] CROW-cache enables low-latency access to the most recently activated regular rows in every subarray. To do so, [CLICK] CROW-cache
makes a copy of the activated regular row into an available copy row. During a subsequent access to the same regular row, [CLICK] CROW-cache simultaneously activates both the regular and copy row to reduce activation latency.
[CLICK]
Second, CROW-ref mitigates DRAM refresh overhead by avoiding storing any data in retention-weak rows such that the entire DRAM chip can use a longer refresh interval. [CLICK] CROW-ref simply remaps weak regular DRAM rows to strong copy rows and the memory controller activates the corresponding copy row instead of the weak regular row.
Please come to my talk and see our paper to learn more about these mechanisms.
[CLICK]
In the talk, we will also briefly discuss a third mechanism that uses CROW to mitigate RowHammer errors.
We hope future work exploits CROW to devise more use cases.

## Slide 6: Key Results
  CROW-cache + CROW-ref
    20% speedup
    22% less DRAM energy
  Hardware Overhead
    0.5% DRAM chip area
    1.6% DRAM capacity
    11.3 KiB memory controller storage
Notes: CROW-cache and CROW-ref are complementary to each other. Averaged across 20 four-core memory intensive workloads, the combination of CROW-cache and CROW-ref improves performance by 20.0% and reduces DRAM energy by 22%.
[CLICK]
CROW provides such performance and energy benefits with a small hardware overhead in the DRAM chip and the memory controller.

## Slide 7: CROW A Low-Cost Substrate for Improving DRAM Performance, Energy Efficiency, and Reliability
Hasan Hassan Minesh Patel Jeremie S. Kim A. Giray Yaglikci Nandita Vijaykumar Nika Mansouri Ghiasi Saugata Ghose Onur Mutlu
Session 2A: Memory and Storage (Monday 2:00 pm at North 221 ABC)
Notes: Please attend my talk on Monday at 2.00 pm if you would like to learn more or ask questions. Thank you.