## Slide 1
Challenges of DRAM scaling:
  High access latency → bottleneck for improving system performance/energy
  Refresh overhead → reduces performance and consume high energy
  Exposure to vulnerabilities (e.g., RowHammer)
Copy-Row DRAM (CROW)
  Introduces copy rows into a subarray
  The benefits of a copy row:
    Efficiently duplicating data from regular row to a copy row
    Quick access to a duplicated row
    Remapping a regular row to a copy row
Use cases:
  CROW-cache & CROW-ref
  Mitigating RowHammer
  We hope CROW enables many other use cases going forward
SA
SA
SA
SA
SA
SA
CROW: A Low-Cost Substrate for Improving DRAM Performance, Energy Efficiency, and Reliability
1: Summary
2: DRAM Operation Basics
3: The Components of CROW
github.com/CMU-SAFARI/CROW
Hasan Hassan Minesh Patel Jeremie S. Kim A. Giray Yaglikci
Nandita Vijaykumar Nika Mansouri Ghiasi Saugata Ghose Onur Mutlu
CPU
Memory Controller
DRAM Row
Sense-Amplifier
Memory
Bus
DRAM Cell
Activate
Read/Write
Precharge
A row is opened
The sense amplifiers could be accessed
Many read/write commands can be issued to the open row
DRAM Module
Each cell stores a single-bit of data
Logic 0
Logic 1
Low Charge
High Charge
Ready to open (activate) a new row
(20% speedup and 22% less DRAM energy)
Memory Controller
CROW-table
DRAM Subarray
Copy-Row DRAM (CROW): a flexible in-DRAM substrate that can be used in multiple different ways to address the performance, energy efficiency, and reliability challenges of DRAM
1
2
4: CROW Operations
Memory Controller
DRAM Subarray
ACT-c
Row Copy
Two-Row Activation
Enables quickly copying a regular row into a copy row
Enables fast access to data that is duplicated across a regular row and a copy row
Memory Controller
DRAM Subarray
ACT-t
5: CROW-cache
Problem: High access latency
Key idea: Use copy rows to enable low-latency access to most-recently-activated regular rows in a subarray
CROW-cache combines:
  row copy → copy a newly activated regular row to a copy row
  Two-row activation → activate the regular row and copy row together on next access
Reduces activation latency by 38%
8: Evaluation
Simulator
  DRAM Simulator (Ramulator [Kim+, CAL’15])
    https://github.com/CMU-SAFARI/ramulator
Workloads
  44 single-core workloads
    SPEC CPU2006, TPC, STREAM, MediaBench
  160 multi-programmed four-core workloads
    By randomly choosing from single-core workloads
  Execute at least 200 million representative instructions per core
System Parameters
  1/4 core system with 8 MiB LLC
  LPDDR4 main memory
  8 copy rows per 512-row subarray
Problem: Refresh has high overheads. Weak rows lead to high refresh rate
  weak row: at least one of the row’s cells cannot retain data correctly when refresh interval is increased
Key idea: Avoid storing data in a weak regular row by remapping it to a strong copy row
CROW-ref uses:
  row copy → copy a weak regular row to a strong copy row
CROW-ref eliminates more than half of the refresh requests
6: CROW-ref
7: Mitigating RowHammer
victim
aggressor
victim
Key idea: remap victim rows to copy rows
Methodology
Chart: Speedup
| leslie3d | tpch2 | zeus | lbm | mcf | stream-cp | libq | h264-dec | AVERAGE (1-core) | HHHH | AVERAGE (4-core)
CROW-1 | 1.099 | 1.047 | 1.11 | 1.095 | 1.116 | 1.098 | 1.019 | 1.061 | 1.066 | 1.007 | 1.012
CROW-8 | 1.111 | 1.061 | 1.124 | 1.1 | 1.158 | 1.103 | 1.026 | 1.061 | 1.075 | 1.071 | 1.038
CROW-64 | 1.111 | 1.061 | 1.125 | 1.101 | 1.158 | 1.11 | 1.026 | 1.061 | 1.077 | 1.095 | 1.047
CROW-128 | 1.111 | 1.061 | 1.125 | 1.101 | 1.158 | 1.11 | 1.026 | 1.061 | 1.078 | 1.1 | 1.049
Ideal CROW-cache (100% Hit Rate) | 1.127 | 1.071 | 1.134 | 1.117 | 1.171 | 1.117 | 1.055 | 1.059 | 1.091 | 1.123 | 1.058
6.6%
1.2%
7.1%
single-core
four-core
CROW-cache Performance
CROW-cache improves single-/four-core system performance
Chart: Speedup
| mcf | milc | lbm | stream_cp | cactus | tpch17 | leslie3d | jp2-enc | libq | zeus | AVERAGE | HHHH
8 Gbit | 1.05 | 1.047 | 1.048 | 1.048 | 1.042 | 1.04 | 1.045 | 1.015 | 1.068 | 1.051 | 1.03 | 1.054
16 Gbit | 1.064 | 1.062 | 1.063 | 1.061 | 1.051 | 1.053 | 1.059 | 1.021 | 1.096 | 1.066 | 1.037 | 1.066
32 Gbit | 1.076 | 1.075 | 1.076 | 1.075 | 1.062 | 1.066 | 1.071 | 1.025 | 1.088 | 1.078 | 1.043 | 1.081
64 Gbit | 1.119 | 1.111 | 1.116 | 1.116 | 1.098 | 1.104 | 1.112 | 1.044 | 1.171 | 1.12 | 1.071 | 1.119
17%
7.1%
single-core
11.9%
four-core
single-core
four-core
CROW-ref Performance
CROW-ref significantly reduces the performance overhead of DRAM refresh
Chart: Speedup
| single-core | four-core
CROW-(cache+ref) | 1.17 | 1.2
Ideal CROW-cache + no refresh | 1.195 | 1.265
Chart: Normalized DRAM Energy
| single-core | four-core
CROW-(cache+ref) | 0.765 | 0.777
Ideal CROW-cache + no refresh | 0.751 | 0.767
17%
20%
23%
22%
CROW-(cache+ref) provides more performance and DRAM energy benefits than each mechanism alone
Combining CROW-cache and CROW-ref
Available in July:
For 8 copy rows:
  0.5% DRAM chip area
  1.6% DRAM capacity
  11.3 KiB memory controller storage
Hardware Overhead
Other Results in the Paper
3.8%
Sensitivity to:
  Number of copy-rows per subarray
  Chip density
  Last-level cache capacity
CROW-cache with prefetching
CROW-cache against other in-DRAM caching mechanisms:
  TL-DRAM [Lee+, HPCA’13]
  SALP [Kim+, ISCA’12]