## Slide 1: Chronus Understanding and Securing the Cutting-Edge Industry Solutions to DRAM Read Disturbance
Oğuzhan Canpolat
Giray Yağlıkçı Geraldo Oliveira Ataberk Olgun
Nisa Bostancı İsmail Emir Yüksel Haocong Luo
Oğuz Ergin Onur Mutlu
https://github.com/CMU-SAFARI/Chronus

## Slide 2: Executive Summary
Goal: Rigorously analyze, characterize, and improve the security and performance of the DDR5 standard PRAC mechanism
Problem:
DRAM continues to become more vulnerable to read disturbance
Latest update (April 2024) to DDR5 standard introduces Per Row Activation Counting (PRAC) to mitigate read disturbance
No prior work investigates PRAC’s security and performance
Mathematical analysis & extensive simulations show that: PRAC
Has significant (10%) performance overhead for modern DRAM chips because PRAC requires additional time to track read disturbance aggressors
Poorly scales to future DRAM chips that are more vulnerable to read disturbance because PRAC is vulnerable to an adversarial access pattern (i.e., the wave attack)
https://github.com/CMU-SAFARI/Chronus
Chronus: Solves PRAC’s two major weaknesses by
Concurrently tracking read disturbance aggressors while serving accesses
Securing PRAC against a potential wave attack
Key Results: Chronus provides high performance and low energy at low hardware complexity overhead and outperforms five state-of-the-art solutions

## Slide 3: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Performance Analysis of Industry Solutions
Chronus
Evaluation

## Slide 4: DRAM Organization
DRAM
Channel
DRAM Module
DRAM Chips
Processor
Notes: Processor <> DRAM Module

## Slide 5: DRAM Organization
Bitline
S
S
S
S
Sense amplifiers
(row buffer)
Wordline
DRAM Cell
Bank
DRAM Array
Off-chip channel
Notes: Several banks
2d grid
Dram cell
Rows
Row buffer

## Slide 6: DRAM Operations
ACTIVATE: Fetch the row into the row buffer
READ/WRITE: Retrieve or
update data
PRECHARGE: Prepare the bank for a new ACTIVATE
1
1
1
1
1
2
3
to I/O
ACTIVATION and PRECHARGE are time-consuming operations
Notes: 3 stages
Act, rd/wr/pre
Time consuming

## Slide 7: DRAM Access Latency
tRP
Command
Data
Duration
ACTIVATE
PRECHARGE
Next
ACT
row-cycle time (tRC)
tRAS
Notes: Predefined amount of time
To send a PRE after ACT we wait -> tRAS
To send an ACT after PRE we wait -> tRP

## Slide 8: RowHammer: A Prime Example of Read Disturbance
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
DRAM Subarray
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes read disturbance bitflips in nearby cells
Notes: victims EXPERIENCE bitflips

## Slide 9: Read Disturbance Vulnerabilities (I)
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 2
open
DRAM Subarray
The minimum number of activations that causes a bitflip is called the RowHammer threshold (NRH)
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row

## Slide 10: Read Disturbance Vulnerabilities (II)
DRAM chips are more vulnerable to read disturbance today
Read disturbance bitflips occur at much lower activation counts
(more than two orders of magnitude decrease in less than a decade):
It is critical to prevent read disturbance bitflips
effectively and efficiently for highly vulnerable systems
139K
[Kim+, ISCA’14]
9.6K
[Kim+, ISCA’20]
<1K (RowPress)
[Luo+, ISCA’23]

## Slide 11: Existing RowHammer Mitigations (I): Preventive Refresh
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Refreshing potential victim rows mitigates RowHammer bitflips
Aggressor Row

## Slide 12: Existing RowHammer Mitigations (II): DRAM Aggressor Row Tracking or Estimation
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 0
Row 1
Row 3
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
DRAM Subarray
Necessary to accurately track or estimate aggressor DRAM row activation counts to preventively refresh potential victim rows
Aggressor Row

## Slide 13: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Overhead Analysis of Industry Solutions
Chronus
Evaluation

## Slide 14: Industry Solutions to Read Disturbance: When To Refresh? (I)
REF
ACT
DRAM
Channel
DRAM Module
Preventive refresh operations are blocking and time consuming operations
Memory controller cannot access a memory bank
undergoing a preventive refresh
Notes: One problem is finding time to refresh
DRAM module CANNOT decide on its own

## Slide 15: Industry Solutions to Read Disturbance: When To Refresh? (II)
RFM
DRAM
Channel
DRAM Module
Earlier JEDEC DDR5 specifications introduce
Refresh Management (RFM) commands
Memory controller sends an RFM command
to allow time for preventive refreshes

## Slide 16: Industry Solutions to Read Disturbance
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands
Per Row Activation Counting and Back-Off (PRAC)
DRAM chip tracks row activations and requests RFMs by sending a back-off
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands
Notes: Industry has two solutions that use PRFM

## Slide 17: Industry Solutions to Read Disturbance: Periodic Refresh Management (PRFM)
0
0
0
1
2
3
ACT
RFM
0
0
0
Bank Activation Counters
ACT
ACT
ACT
RFM
DRAM Commands
RFM Threshold
PRFM tracks activations with low accuracy,
causing a high number of preventive refreshes,
leading to large performance and energy overheads
Notes: a counter PER DRAM bank

## Slide 18: Industry Solutions to Read Disturbance
Per Row Activation Counting and Back-Off (PRAC)
DRAM chip tracks row activations and requests RFMs by sending a back-off
Per Row Activation Counting and Back-Off (PRAC)
DRAM chip tracks row activations and requests RFMs by sending a back-off
Periodic Refresh Management (PRFM)
Memory controller periodically issues RFM commands

## Slide 19: Industry Solutions to Read Disturbance: Per Row Activation Counting
101010101010101010101010
0
0
1
2
3
4
101010101010101010101010
PRAC allows accurate tracking of aggressor row activations
Counters
DRAM Rows
…
…
Notes: Each row has a corresponding counter

## Slide 20: Industry Solutions to Read Disturbance: Per Row Activation Counting DRAM Timings
101010101010101010101010
0
0
101010101010101010101010
Counters
DRAM Rows
The activation counter of a row is updated
while the row is being closed
PRAC increases precharge duration (tRP) by 140%
PRE
ACT
precharge duration (tRP)
…
…
Notes: Be clear on what JEDEC published

## Slide 21: Industry Solutions to Read Disturbance: Per Row Activation Counting DRAM Timings
tRP
tRAS
tRTP
tWR
: +21ns
: -16ns
: -2.5ns
: -20ns
tRC
: +5ns
(+140%)
(-50%)
(-33%)
(-66%)
(+10%)
Timing parameter changes for DDR5-3200AN speed bin
[JEDEC JESD79-5C, April 2024]
Notes: The list of all affected timing parameters
Importantly, tRP and tRC increase

## Slide 22: Industry Solutions to Read Disturbance: Per Row Activation Counting (PRAC)
PRAC-N
Back-Off
ACT
RFM
No Back-Off
delay
(N ACTs)
0
1
2
3
4
0
0
Row Counters
ACT
ACT
RFM
ACT
ACT
RFM
DRAM Commands
Back-Off Threshold
normal traffic
(180 ns)
recovery
(N RFMs)
ACT
ACT
…
Notes: An execution example
Recovery predefined #RFMs
mechanism named after the number of RFMs
Delay predefined #ACTs
Same number with RFMs in recovery

## Slide 23: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Performance Analysis of Industry Solutions
Chronus
Evaluation

## Slide 24: Security Analysis of Industry Solutions: Mathematical Security Analysis Methodology
Wave attack [Yağlıkçı+, 2021] : worst-case access pattern
  maximizes hammer count by using decoy rows
  on a system with PRFM
  on a system with PRAC
Parameters:
  Starting row set size: # of rows that the wave attack hammers
  RFM threshold (PRFM)
  Back-Off threshold (PRAC)
Result: Worst possible (highest) activation count that an attacker can achieve to a row

## Slide 25: Security Analysis of Industry Solutions: Secure PRFM Configurations
Wave Attack Parameter
Highest activation count an attacker can achieve
Lower is better
Less frequent RFM commands

## Slide 26: Security Analysis of Industry Solutions: Secure PRFM Configurations
Wave Attack Parameter
Highest activation count an attacker can achieve
RowHammer Threshold = 1024
Safe
Unsafe
Lower is better
Less frequent RFM commands
Notes: We check by drawing a line
A system is secure if all attacker params are under the line
RFM 256 *not* safe against RH 1024

## Slide 27: Security Analysis of Industry Solutions: Secure PRFM Configurations
Highest activation count an attacker can achieve
Lower is better
Less frequent RFM commands
PRFM Security Analysis

## Slide 28: Security Analysis of Industry Solutions: Secure PRFM Configurations
PRFM must send RFM commands very frequently (every ~8 ACTs) to prevent bitflips at low read disturbance thresholds (below 128)
Highest activation count an attacker can achieve
Lower is better
Less frequent RFM commands
PRFM Security Analysis

## Slide 29: Security Analysis of Industry Solutions: Secure PRAC Configurations
Highest activation count an attacker can achieve
Lower is better
Less frequent back-off signals
PRAC Security Analysis

## Slide 30: Security Analysis of Industry Solutions: Secure PRAC Configurations
PRAC can be configured for secure operation
against RowHammer thresholds as low as 20
Less frequent back-off signals
Highest activation count an attacker can achieve
Lower is better
PRAC Security Analysis

## Slide 31: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Performance Analysis of Industry Solutions
Chronus
Evaluation
Notes: Using these secure configurations

## Slide 32: Performance Analysis of Industry Solutions: Evaluation Methodology
Performance evaluation: cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023]
System Configuration:
  Processor 4 cores, 4.2GHz clock frequency,
  4-wide issue, 128-entry instruction window
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 64K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4 Last-Level Cache 8 MiB (4-core)
Workloads: 60 4-core workload mixes
  SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, YCSB

## Slide 33: Performance Analysis of Industry Solutions: Industry Solution Variants
PRFM
Memory controller periodically issues RFM
1
PRAC-N
Memory controller issues N RFMs each with back-off
2
PRAC+PRFM
Memory controller issues RFM periodically and with back-offs
3
Notes: TAKE YOUR TIME

## Slide 34: Experimental Results: Performance Overhead and Its Scaling
Increasing RowHammer vulnerability
Higher is better

## Slide 35: Experimental Results: Performance Overhead and Its Scaling
Increasing RowHammer vulnerability
Higher is better
At high NRH values, PRAC has non-negligible (10%) performance overhead due to increased DRAM access latency
10%

## Slide 36: Experimental Results: Performance Overhead and Its Scaling
Lower is worse
Higher is better
Above NRH of 64, PRAC overhead only slightly increases due to timely preventive refreshes
Below NRH of 64, PRAC overhead significantly increases
due to conservative configuration against a potential wave attack

## Slide 37: PRAC’s Two Major Outstanding Problems
Increased critical
DRAM timing parameters
Wave attack vulnerability requires aggressive configuration
Large performance overhead even at high read disturbance thresholds
Poor scaling to low read disturbance thresholds
1
2

## Slide 38: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Performance Analysis of Industry Solutions
Chronus
Evaluation

## Slide 39: Chronus: Key Ideas
Concurrently update counters while serving
DRAM accesses
Prevent wave attacks by providing DRAM chip
more control over back-offs and preventive refreshes
No increase in critical
DRAM timing parameters
Better scaling to low read disturbance thresholds
1
2

## Slide 40: Chronus: Overview
Chronus Back-Off
Dynamically control the number of refreshes as needed
Concurrent Counter Update
Concurrently update counters while serving DRAM accesses

## Slide 41: Chronus: Concurrent Counter Update
Chronus concurrently updates counters while serving accesses
Counter 0
Counter 2N-1
Counter N+1
Counter N-1
Counter
Subarray
Row Decoder
Regular
Subarray
Row 2N-1
Row N
Row Decoder
Regular
Subarray
Row N-1
Row 0
Row Decoder
Row Buffer
Row Buffer
Row Buffer
Increment
DRAM Bank
Regular
Accesses
Counter
Updates
Subarray
Level
Parallelism
Notes: Chronus concurrently updates counters with a small change to the bank
Alongside the regular DRAM subarrays that store data, Chronus adds an additional Counter subarray to store counters
DRAM -> access, Counter -> updates
SALP

## Slide 42: Chronus: Concurrent Counter Update
Time
ACT 0
PRE
ACT N
Row 0
Row N
Row 0
Counter 0
Counter 2N-1
Counter N+1
Counter N-1
Counter
Subarray
Row Decoder
Regular
Subarray
Row 2N-1
Row N
Row Decoder
Regular
Subarray
Row N-1
Row 0
Row Decoder
Row Buffer
Row Buffer
Row Buffer
Increment
Chronus concurrently updates counters while serving accesses
Counter 0
Counter N-1
Row 0
Open Row
Open Row
Row N
Serves
Regular
Accesses
Updates
Counter

## Slide 43: Chronus: Concurrent Counter Update (More in the paper)
Counter Subarray
incurs 0.5% area overhead
per bank
Counter Subarray
induces 19% energy overhead
to opening and closing a row
https://arxiv.org/abs/2502.12650

## Slide 44: Chronus: Overview
Chronus Back-Off
Dynamically control the number of refreshes as needed
Concurrent Counter Update
Concurrently update counters while serving DRAM accesses

## Slide 45: Chronus: Chronus Back-Off
Chronus Back-Off prevents a potential wave attack
with two simple changes to PRAC Back-Off
Chronus Back-Off dynamically controls
the number of refreshes as needed
1)
Chronus Back-Off does not have a delay period
2)

## Slide 46: Chronus: Chronus Back-Off
Time
RFM
RFM
RFM
alert_n
refresh needed
no critical rows
Chronus refreshes all rows that exceed the back-off threshold
Row
Counter
R50
100
R0
100
R35
100
R60
99
!
!
!
no delay period
ACT
RFM
dynamic control of refreshes
-
-
-
-
-
-
R60
100
!
window of normal traffic
and refreshes continue
Aggressor Tracking Table
Tracks row counters
with most activations
Notes: Hypothetical scenario
Aggressor tracks counters with most activations, helps to know which rows to mitigate in RFM
When critical, assert alert_n
Memory controller sends RFMs as long as asserted
When done, deassert
If a new counter becomes critical, reassert without a delay
Execution continues…

## Slide 47: Chronus: Chronus Back-Off (More in the paper)
Aggressor Tracking Table
requires only 4 entries
Chronus Back-Off
security analysis
https://arxiv.org/abs/2502.12650
Notes: More in the paper:
The tracking table
Configuring table size
Security proof of Chronus back-off

## Slide 48: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Performance Analysis of Industry Solutions
Chronus
Evaluation

## Slide 49: Evaluation Methodology
Performance and energy consumption evaluation: cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 4 cores, 4.2GHz clock frequency,
  4-wide issue, 128-entry instruction window
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 64K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4 Last-Level Cache 8 MiB (4-core)
Workloads: 60 4-core workload mixes
  SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, YCSB

## Slide 50: Evaluation Methodology: Chronus Variants
Chronus
Concurrently updates counters while serving accesses
and uses Chronus Back-Off
1
Chronus-PB
Concurrently updates counters while serving accesses
but uses PRAC Back-Off
2
Notes: We only propose Chronus but evaluate Chronus-PB isolates the benefits of Chronus Back-Off

## Slide 51: Evaluation Methodology
Comparison Points: Two Chronus variants are compared against 5 state-of-the-art DRAM read disturbance mitigation mechanisms:
PARA [Kim+, ISCA 2014]
Graphene [Park+, MICRO 2020]
Hydra [Qureshi+, ISCA 2022]
PRAC [JEDEC 2024]
PRFM [JEDEC 2020]

## Slide 52: Evaluation: System Performance and Its Scaling
Increasing RowHammer vulnerability
Higher is better

## Slide 53: Evaluation: System Performance and Its Scaling
<0.1%
10%
At high NRH values, Chronus and Chronus-PB’s concurrent counter update mechanism prevents the high performance overhead of PRAC

## Slide 54: Evaluation: System Performance and Its Scaling
At low NRH values, Chronus Back-Off prevents
the high performance overhead due to aggressive PRAC configuration

## Slide 55: Evaluation: System Performance and Its Scaling
Chronus outperforms all evaluated mitigation mechanisms
at all evaluated RowHammer thresholds

## Slide 56: Evaluation: DRAM Energy and Its Scaling
Increasing RowHammer vulnerability
Lower is better

## Slide 57: Evaluation: DRAM Energy and Its Scaling
At high NRH values, Chronus reduces PRAC energy overhead by 44%
18%
10%

## Slide 58: Evaluation: DRAM Energy and Its Scaling
At low NRH values, Chronus Back-Off prevents
the high energy overhead due to aggressive PRAC configuration

## Slide 59: Evaluation Summary
Chronus significantly reduces
the negative performance and energy overheads of PRAC
Chronus concurrently updates counters
while serving DRAM accesses
1)
Chronus dynamically controls
the number of refreshes as needed
2)

## Slide 60: More in the Paper
Detailed Background on PRAC
  More information on PRAC and RFM
  Determining which rows to refresh during a back-off
Security Analysis of PRAC
  Threat Model
  Secure Configurations
Details on Chronus
  Preventing bitflips in the counter subarray
  Security proof
  Hardware complexity
Evaluation
  Chronus outperforms all mechanisms in single-core workloads
  Effect of workload memory intensity on system performance
System Performance Adversarial Workloads
  Chronus reduces PRAC’s system performance overhead under a system performance adversarial workload by 66%
https://arxiv.org/abs/2502.12650

## Slide 61: The Paper
https://arxiv.org/abs/2502.12650

## Slide 62: Outline
Background
Industry Solutions to Read Disturbance
Conclusion
Security Analysis of Industry Solutions
Performance Analysis of Industry Solutions
Chronus
Evaluation

## Slide 63: Conclusion
We rigorously analyzed and characterized the security and performance implications of recently introduced industry solutions to DRAM read disturbance
https://github.com/CMU-SAFARI/Chronus
Key Results: Chronus
Significantly reduces the negative performance and energy overheads of PRAC for both modern and future DRAM chips that are more vulnerable to read disturbance
Outperforms five state-of-the-art academic and industry solutions in terms of system performance and energy
Mathematical analysis & extensive simulations show that: PRAC
Has significant (10%) performance overhead for modern DRAM chips because PRAC requires additional time to update row activation counters
Poorly scales to future DRAM chips that are more vulnerable to read disturbance because PRAC is vulnerable to an adversarial access pattern (i.e., the wave attack)
Chronus: Solves PRAC’s two major weaknesses by
Concurrently updating counters while serving accesses
Securing PRAC against a potential wave attack

## Slide 64: Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/Chronus

## Slide 65: Chronus Understanding and Securing the Cutting-Edge Industry Solutions to DRAM Read Disturbance
Oğuzhan Canpolat
Giray Yağlıkçı Geraldo Oliveira Ataberk Olgun
Nisa Bostancı İsmail Emir Yüksel Haocong Luo
Oğuz Ergin Onur Mutlu
https://github.com/CMU-SAFARI/Chronus

## Slide 66: Chronus Understanding and Securing the Cutting-Edge Industry Solutions to DRAM Read Disturbance
Oğuzhan Canpolat
Giray Yağlıkçı Geraldo Oliveira Ataberk Olgun
Nisa Bostancı İsmail Emir Yüksel Haocong Luo
Oğuz Ergin Onur Mutlu
https://github.com/CMU-SAFARI/Chronus
BACKUP SLIDES

## Slide 67: PRAC Counter Update
Time
ACT 0
PRE
Row 0
Row N-1
Row 0
Row Decoder
Row Buffer
Row 0
Open Row
Time
ACT 0
PRE
iRD
iWR
iPRE
Row 0
Row N-1
Row 0
Row Decoder
Row Buffer
Row 0
Open Row
Counter N-1
Counter 0
Row Buffer
Counter 0
Open Row
start counter update
close the row
increment

## Slide 68: Evaluation: Singe-core System Performance

## Slide 69: Evaluation: Effect of Workload Memory Intensity (NRH=32)

## Slide 70: Evaluation: Storage Overhead

## Slide 71: Wave Attack Visualization

## Slide 72: Security Analysis: Wave Attack (I)
101010101010101010101010
0
101010101010101010101010
0
0
101010101010101010101010
0
101010101010101010101010
0
1
2
3
4
0
101010101010101010101010
101010101010101010101010
0
101010101010101010101010
0

## Slide 73: Security Analysis: Wave Attack (II)
0
101010101010101010101010
101010101010101010101010
101010101010101010101010
0
0
0
101010101010101010101010
0
101010101010101010101010
101010101010101010101010
1
1
1
2
0
2
2
3
3
0
0
0
0
4
5
101010101010100010101010
100010101010101010001010
6
101010101010100010100010
100010101010101010001000
7
100010001010100010100010
100010100000101010001000
101010101010101010101010
101010101010101010101010
101010101010101010101010
0
Secure configuration is not trivial