## Slide 1
Andreas Kosmas Kakolyris
F. Nisa Bostancı
Harsh Songara
Konstantinos Kanellopoulos
Ataberk Olgun
Konstantinos Marios Sgouras
A. Giray Yağlıkçı
İsmail Emir Yüksel
Umut Başer
Onur Mutlu
ColumnKeeper: Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems

## Slide 2: Executive Summary
Problem: DRAM chips are vulnerable to ColumnDisturb, a new, column-based read disturbance phenomenon. Naively mitigating ColumnDisturb incurs significant overheads.
Goal: Design mechanisms that mitigate ColumnDisturb bitflips with low performance, energy and area overheads
Key Idea: Track row activations at subarray granularity. Iteratively refresh all rows.
ColumnKeeper-D (Deterministic): Uses separate activation counters for odd and even bitlines of each subarray and issues a preventive refresh when either counter reaches a predetermined threshold
ColumnKeeper-P (Probabilistic): Probabilistically issues refreshes to one row in three consecutive subarrays upon a row activation in the middle subarray
Evaluation
ColumnKeeper mitigates ColumnDisturb bitflips with low overheads at current (1M) and “near-future” (128K) thresholds
ColumnKeeper can mitigate ColumnDisturb bitflips with low overheads even at low thresholds (16K) with changes to DRAM microarchitecture
https://github.com/CMU-SAFARI/ColumnKeeper

## Slide 3: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 4: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 5: DRAM Organization
CPU
DRAM Module
DRAM Chip
DRAM
Channel

## Slide 6: DRAM Organization
wordline
bitline
DRAM Cell
capacitor
DRAM Subarrays
…
…
SA
SA
SA
SA
SA
SA
DRAM
Chip
DRAM Column
…
…
DRAM Chip
Chip I/O
Bank
Bank
Bank
Bank
Bank
Bank
DRAM Bank
DRAM Subarray 0
Sense Amplifiers
DRAM Subarray 1
Sense Amplifiers
DRAM Subarray 2
Sense Amplifiers
DRAM Subarray N
Sense Amplifiers
…
DRAM Row

## Slide 7: DRAM Organization
SA
SA
SA
SA
1
0
1
1
1
0
1
1
ACTIVATE: Fetch the row into the sense amplifiers
1
READ/WRITE: Retrieve or
update data
2
PRECHARGE: Prepare the bank for a new ACTIVATE
3
to/from I/O

## Slide 8: DRAM Read Disturbance: RowHammer
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Victim Row
Victim Row
Aggressor Row

## Slide 9: DRAM Read Disturbance: RowHammer
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Victim Row
Victim Row
Aggressor Row
RowHammer causes bitflips in adjacent rows in the same subarray

## Slide 10: DRAM Read Disturbance: RowPress
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Another prominent example: RowPress
Victim Row
Victim Row
Aggressor Row
keep open

## Slide 11: DRAM Read Disturbance: RowPress
SA
SA
SA
SA
Read disturbance in DRAM breaks memory isolation
Another prominent example: RowPress
Victim Row
Victim Row
Aggressor Row
RowPress causes more bitflips in adjacent rows in the same subarray
keep open

## Slide 12: DRAM Read Disturbance: ColumnDisturb
ColumnDisturb: Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
Subarray
Subarray
Subarray
SA
SA
SA
SA
Open-bitline architecture: columns of a single row span multiple subarrays

## Slide 13: DRAM Read Disturbance: ColumnDisturb
ColumnDisturb: Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
Subarray
Subarray
Subarray
All cells
Cells on odd columns
Cells on even columns

## Slide 14: DRAM Read Disturbance: ColumnDisturb
ColumnDisturb: Repeatedly hammering or pressing a DRAM row disturbs many DRAM cells on the same DRAM column
Subarray
Subarray
Subarray
All cells
Cells on odd columns
Cells on even columns
ColumnDisturb affects DRAM cells across
three consecutive DRAM subarrays (up to 3072 DRAM rows)
ColumnDisturb induces bitflips within the DDR4 refresh window
The number of activations required to induce ColumnDisturb bitflips (NCD) is currently 1M
Scaling studies show ColumnDisturb is getting worse in newer chips

## Slide 15: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 16: Mitigating ColumnDisturb (I)
The easiest way of mitigating ColumnDisturb is to reduce the DRAM refresh window so that all rows are refreshed before bitflips can occur
Significant performance overheads at near-future ColumnDisturb thresholds:
More than 50% for workloads with high memory intensity
Significant DRAM energy overheads at near-future ColumnDisturb thresholds:
More than 6x increase in energy consumption
Mitigating ColumnDisturb by increasing the DRAM refresh rate
incurs prohibitive overheads

## Slide 17: Mitigating ColumnDisturb (II)
Alternative method: Modifying RowHammer mitigation mechanisms to protect against ColumnDisturb
RowHammer mitigations such as Per-Row Activation Counting (PRAC):
Track activations at the row granularity
Only refresh a few neighboring victim rows
Using PRAC to mitigate ColumnDisturb requires:
Aggressively configuring PRAC to fire at a low threshold
Refreshing all 3072 rows across three subarrays
Modified PRAC incurs prohibitive overheads

## Slide 18: Our Goal
Design mechanisms
that prevent ColumnDisturb bitflips
at low performance, energy, and area overheads

## Slide 19: Our Overarching Key Idea
Track activations at subarray granularity
Iteratively refresh all rows within each subarray

## Slide 20: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 21: Key Observation
Activations in one subarray affect all columns in that subarray but
either odd or even columns in neighboring subarrays

## Slide 22: Key Observation
SA
SA
SA
SA
Subarray A
Subarray B
Subarray C
Χ
Υ
Nodd = Χ
Neven = Χ
Nodd = Υ
Neven = Χ
Nodd = Υ
Neven = Υ
Total ACTs = Χ
Actual ACTs = Χ
Total ACTs = Υ
Actual ACTs = Υ
Total ACTs = Χ+Υ
Actual ACTs = max{Χ,Υ}
SA
SA
SA
SA
Activations in one subarray affect all columns in that subarray but
either odd or even columns in neighboring subarrays

## Slide 23: Key Observation
Activations in one subarray affect all columns in that subarray but
either odd or even columns in neighboring subarrays
Υ
Χ
SA
SA
SA
SA
Subarray A
Subarray B
Subarray C
Nodd = Χ
Neven = Χ
Nodd = Υ
Neven = Χ
Nodd = Υ
Neven = Υ
Total ACTs = Χ
Actual ACTs = Χ
Total ACTs = Υ
Actual ACTs = Υ
Total ACTs = Χ+Υ
Actual ACTs = max{Χ,Υ}
SA
SA
SA
SA
In the worst case when Χ = Υ Total ACTs = 2 Actual ACTs
Naively counting the activations affecting a subarray overestimates the activation count of cells and increases overheads

## Slide 24: ColumnKeeper-D Key Idea
Separately count activations in odd and even columns of each subarray to mitigate ColumnDisturb at low performance and energy overheads

## Slide 25: ColumnKeeper-D Overview
Memory Request Scheduler
5
8
4
…
CT-Even
ColumnKeeper-D consists of:
Counter Table – Even (CT-Even): Counts activations in even columns
Counter Table – Odd (CT-Odd): Counts activations in odd columns
Row Pointer Table (RPT): Points to the next row to be preventively refreshed in each subarray
3
2
9
…
CT-Odd
NSUBARRAYS
RPT
…

## Slide 26: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
5
8
4
…
CT-Even
Upon a row activation in subarray k, ColumnKeeper-D:
Increments both the CT-Even and CT-Odd entries for subarray k
Increments the CT-Even entry for the previous subarray
Increments the CT-Odd entry for the next subarray
3
2
9
…
CT-Odd
NSUBARRAYS
8
2
+1
+1
5
+1
9
+1
9
3
6
10

## Slide 27: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
Upon a row activation in subarray k, ColumnKeeper-D:
Calculates the maximum value of the two counters for the three subarrays
Compares the calculated value to a predetermined threshold (NPR)
NPR = 10

## Slide 28: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
Row activation in subarray k:
Calculates the maximum value of the two counters for the three subarrays
Compares the calculated value to a predetermined threshold (NPR)
NPR = 10
We set NPR to NCD divided by the subarray size
This ensures all rows are iteratively refreshed before reaching NCD

## Slide 29: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
Row activation in subarray k:
Calculates the maximum value of the two counters for the three subarrays
Compares the calculated value to a predetermined threshold (NPR)
If the maximum counter value for a subarray exceeds NPR ColumnKeeper-D decides to issue a preventive refresh for that subarray
NPR = 10
Y
N
N

## Slide 30: ColumnKeeper-D Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
ColumnKeeper-D:
Issues an ACT command followed by a PRE command to the Row Address pointed by the corresponding RPT entry
Increments the RPT entry to point to the next row in that subarray
Zeroes the CT-Even and CT-Odd entries for that subarray
NPR = 10
Y
N
N
Preventive Refresh
ACT+PRE
Row Address
6
+1
7
0
0

## Slide 31: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 32: ColumnKeeper-P Key Idea
Probabilistically issue preventive refreshes to avoid activation counting and mitigate ColumnDisturb at lower area overhead

## Slide 33: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
NSUBARRAYS
ColumnKeeper-P substitutes ColumnKeeper-D’s deterministic activation counting mechanism with a probabilistic one
Row Address
6
+1
7
4
…
CT-Even
3
…
CT-Odd
9
3
6
10
MAX
MAX
MAX
10
9
6
NPR = 10
Y
N
N
0
0
Preventive Refresh
ACT+PRE

## Slide 34: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
Upon a row activation in one subarray:
ColumnKeeper-P flips a coin that lands heads up with a predetermined probability (PPR)
Coin Flip w/ Probability PPR

## Slide 35: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
Upon a row activation in one subarray:
ColumnKeeper-P flips a coin that lands heads up with a predetermined probability (PPR)
Preventive Refreshes
ACT+PRE
$
Coin Flip w/ Probability PPR
PPR is calculated to upper bound the probability of a ColumnDisturb bitflip occurring during a year of continuous ColumnDisturb attack

## Slide 36: ColumnKeeper-P Overview
RPT
…
Memory Request Scheduler
Upon a row activation in one subarray:
ColumnKeeper-P flips a coin that lands heads up with a predetermined probability (PPR)
If the coin lands heads up, ColumnKeeper-P issues preventive refreshes for that subarray and its neighbors and increments all three RPT entries
Preventive Refreshes
ACT+PRE
2
7
9
2
7
9
+1
+1
+1
Y
Row Addresses
Heads up?
Coin Flip w/ Probability PPR

## Slide 37: More Details in the Paper
Detailed calculation of NPR for ColumnKeeper-D
Security analysis of ColumnKeeper-D
Detailed calculation of PPR for ColumnKeeper-P
Monte-Carlo security analysis of ColumnKeeper-P

## Slide 38: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 39: Methodology
Performance and energy consumption evaluation: cycle-level simulations using Ramulator2 [Luo+, CAL 2023] and DRAMPower [Chandrasekar+, DATE 2013]
System Configuration:
  Processor 1 or 4 cores, Last-Level Cache: 2 MiB/core
  DRAM 16GB DDR4, 1 channel, 2 rank/channel, 4 bank groups,
  4 banks/bank group, 64K rows/bank, 1K rows/subarray
  Mem. Ctrl. 64-entry read/write request queue,
  Scheduling policy: FR-FCFS, Open-Row Policy
  Address mapping: RoBaRaCoCh
  ColumnKeeper-D (Det) or ColumnKeeper-P w/ yearly failure probability of 10-3 (Pr-Perf) or 10-12 (Pr-Cons)
Workloads:
62 single-core workloads from SPEC CPU2006, SPEC CPU2017, TPC, MediaBench, and YCSB categorized by Row Buffer Misses per-kilo-instructions (RBMPKI)
60 quad-core workload mixes synthesized from the resulting RBMPKI categories

## Slide 40: Evaluation: Single-Core Performance

## Slide 41: Evaluation: Single-Core Performance
Higher is better
More memory-intensive

## Slide 42: Evaluation: Single-Core Performance
ColumnKeeper-D and –P incur low (<1%) average performance overheads for current ColumnDisturb thresholds (1M)

## Slide 43: Evaluation: Single-Core Performance

## Slide 44: Evaluation: Single-Core Performance
Performance overheads increase for more memory-intensive workloads

## Slide 45: Evaluation: Single-Core Performance
Performance overheads increase for more memory-intensive workloads
All ColumnKeeper mechanisms incur significant performance overheads at low ColumnDisturb thresholds of NCD=16K

## Slide 46: Evaluation: DRAM Energy (Single-Core)

## Slide 47: Evaluation: DRAM Energy (Single-Core)
Lower is better
More memory-intensive

## Slide 48: Evaluation: DRAM Energy (Single-Core)
Energy overheads increase for more memory-intensive workloads
Low energy overheads for current thresholds
Significant energy overheads for future low thresholds

## Slide 49: Evaluation: Multi-Core Performance

## Slide 50: Evaluation: Multi-Core Performance
Higher is better
More memory-intensive

## Slide 51: Evaluation: Multi-Core Performance

## Slide 52: Evaluation: Multi-Core Performance
Performance overheads increase for memory-intensive workload mixes
Low performance overheads for current thresholds
Significant performance overheads for future low thresholds

## Slide 53: Evaluation: Multi-Core Performance
1.5%
More pronounced difference between the deterministic and the probabilistic mechanisms than single-core

## Slide 54: Evaluation: Sensitivity to Subarray Size

## Slide 55: Evaluation: Sensitivity to Subarray Size
Higher is better
Smaller Subarrays

## Slide 56: Evaluation: Sensitivity to Subarray Size
Smaller subarrays (128 rows) eliminate the overheads of ColumnKeeper
for current ColumnDisturb thresholds (1M)

## Slide 57: Evaluation: Sensitivity to Subarray Size
Smaller subarrays reduce the overheads of ColumnKeeper
for all ColumnDisturb thresholds

## Slide 58: Evaluation: Sensitivity to Subarray Size

## Slide 59: Evaluation: Sensitivity to Subarray Size
Smaller subarrays reduce the overheads of ColumnKeeper
even at very low thresholds

## Slide 60: Evaluation: Area and Power Overheads
ColumnKeeper requires:
7.5 KB of SRAM for ColumnKeeper-D
2.5 KB of SRAM for ColumnKeeper-P
Hardware Implementation & Synthesis:
ColumnKeeper implemented in Verilog
OpenRoad + NanGate 45nm Open-Source Cell Library
Area Overheads:
0.1 mm2 for ColumnKeeper-D
0.03 mm2 for ColumnKeeper-P
Power Overheads:
50 mW for ColumnKeeper-D
15 mW for ColumnKeeper-P

## Slide 61: More in the Paper
Evaluation of ColumnKeeper with Subarray-level Parallelism [Kim+, ISCA 2012]
Impact of physical page allocation policy on the performance overheads of ColumnKeeper
Performance evaluation of ColumnKeeper integrated with RowHammer mitigation mechanisms
Performance evaluation under adversarial workloads
An in-DRAM implementation of our design

## Slide 62: Available on arXiv
https://arxiv.org/pdf/2606.22632

## Slide 63: Artifact Evaluated & Open-Source
https://github.com/CMU-SAFARI/ColumnKeeper

## Slide 64: Outline
Background
Motivation
ColumnKeeper-D (Deterministic)
Evaluation
Conclusion
ColumnKeeper-P (Probabilistic)

## Slide 65: Conclusion
Key Idea: Track row activations at subarray granularity and iteratively refresh all affected rows in a subarray
Goal: Mitigate ColumnDisturb bitflips at low overhead
Key Results:
ColumnKeeper prevents ColumnDisturb bitflips with low overheads for current and near-future thresholds
ColumnKeeper can prevent ColumnDisturb bitflips at low overheads for low thresholds with changes to DRAM microarchitecture
ColumnKeeper-D: Uses separate activation counters for odd and even columns of each subarray
ColumnKeeper-P: Probabilistically issues refreshes to one row in three consecutive subarrays upon a row activation in the middle subarray

## Slide 66
ColumnKeeper: Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems
Paper
Code

## Slide 67
ColumnKeeper: Efficient Solutions to the ColumnDisturb Vulnerability in DRAM-based Systems
F. Nisa Bostancı
Harsh Songara
Konstantinos Kanellopoulos
Ataberk Olgun
Konstantinos Marios Sgouras
A. Giray Yağlıkçı
İsmail Emir Yüksel
Umut Başer
Onur Mutlu
Andreas Kosmas Kakolyris
Backup Slides

## Slide 68: Evaluation: Detailed Single-Core Results

## Slide 69: Evaluation: Sensitivity to Page Allocation
No significant difference in performance between the two allocators

## Slide 70: Evaluation: In-DRAM Implementation
The in-DRAM implementation of ColumnKeeper-D reduces its overheads at low ColumnDisturb thresholds

## Slide 71: ColumnKeeper-P: PPR Calculation
Methodology
Similar to the one proposed in HiRA [Yaglikci+, MICRO 2022]
Considers the maximum number of attacks that can happen in a refresh window
At least one of these attacks has to succeed
To induce bitflips: The number of preventive issues issued to a subarray must be lower than the subarray size (S) when the ColumnDisturb threshold is reached
Total number of preventive refreshes issued after N activations (MN):
Sum of Bernoulli random variables
MN follows a binomial distribution

## Slide 72: ColumnKeeper-P: PPR Calculation
We substitute:
A single ColumnDisturb attack succeeds with probability P1:
Probability of a successful attack within a refresh window based on maximum number of attacks:
Probability of a successful attack within a year (PY):

## Slide 73: ColumnKeeper-P Configuration
Small increases in PPR significantly increase security for the same NCD

## Slide 74: ColumnKeeper-P: Monte-Carlo Simulation
Lower PY leads to more preventive refreshes and a lower HCmax

## Slide 75: Evaluation: Integration w/ RH Mitigations
ColumnKeeper issues ACT+PRE commands:
ACTs and PREs are transparent to RowHammer mitigation mechanisms
RowHammer mitigation mechanisms issue:
ACT + PRE commands
RFM commands
ColumnKeeper operates transparently to RowHammer mitigation mechanisms
RowHammer mitigation mechanisms operate transparently to ColumnKeeper
RFM commands accounted by incrementing all activation counters in affected banks

## Slide 76: Evaluation: Integration w/ RH Mitigations
No destructive interference between RowHammer mitigation mechanisms and ColumnKeeper
NCD = 128K, NRH = 128

## Slide 77: ColumnDisturb: Newer Chips are More Vulnerable
5.1x
1.3x
3x
2.5x
Newer chips tend to be more vulnerable to ColumnDisturb bitflips
This trend is consistent across all tested manufacturers

## Slide 78: Evaluation: Adversarial Workloads
Low performance overheads for current and near-future thresholds
Significant performance overheads for future low thresholds