## Slide 1: Conduit Programmer-Transparent Near-Data Processing Using Multiple Compute-Capable Resources in Solid State Drives
Rakesh Nadig, Vamanan Arulchelvan, Mayank Kabra, Harshita Gupta, Rahul Bera, Nika Mansouri Ghiasi,
Nanditha Rao, Qingcai Jiang, Andreas Kosmas Kakolyris, Yu Liang, Mohammad Sadrosadati, and Onur Mutlu
HPCA 2026

## Slide 2: Talk Outline
Background and Motivation
Conduit
Evaluation
Summary
2

## Slide 3: Talk Outline
Background and Motivation
Conduit
Evaluation
Summary
3

## Slide 4: Overview of a Modern SSD
4
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip

## Slide 5: Near Data Processing in an SSD (ISP)
5
In-Storage Processing (ISP) Processing using embedded cores in the SSD controller
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip

## Slide 6: Near Data Processing in an SSD (ISP)
6
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Many prior ISP works (e.g., Biscuit [Gu+, ISCA 2016], GenStore [Mansouri Ghiasi+, ASPLOS 2022], REIS [Chen+, ISCA 2025]) accelerate complex tasks including filtering, aggregation, encryption, and search

## Slide 7: Near Data Processing in an SSD (PuD-SSD)
7
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Processing-using-DRAM in SSD (PuD-SSD) Computation using SSD DRAM’s intrinsic operational principles

## Slide 8: Near Data Processing in an SSD (PuD-SSD)
8
PuD works (e.g., Ambit [Seshadri+, MICRO 2017], SIMDRAM [Hajinazar+, ASPLOS 2021], MIMDRAM [Oliveira+, HPCA 2024]) enable bulk-bitwise and complex arithmetic operations entirely within the DRAM chips
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip

## Slide 9: Near Data Processing in an SSD (IFP)
9
In-Flash Processing (IFP) Computation by exploiting the flash chip’s structure
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip

## Slide 10: Near Data Processing in an SSD (IFP)
10
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Several IFP techniques (e.g., Ares-Flash [Chen+, MICRO 2024]) enable arithmetic operations inside NAND flash chips by controlling the latching circuit of the page buffer

## Slide 11: Near Data Processing in an SSD (IFP)
11
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Flash-Cosmos [Park+, MICRO 2022] enables bulk-bitwise operations within NAND flash chips by simultaneously reading multiple pages

## Slide 12: Near Data Processing in an SSD: Tradeoffs
12
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip
NDP Paradigm |  | 
Supports general-purpose computations
Wimpy embedded cores provide limited performance
ISP
Computations in a highly parallel manner within the DRAM chips
Requires transferring operands from flash chips via bandwidth-limited flash channels
PuD-SSD
Eliminates data movement overhead and provides high computation parallelism
Limited operation set
IFP

## Slide 13: NDP in an SSD: Research Questions
13
SSD Controller
Flash Controller
Flash Controller
…
PCIe
Channel
Channel
…
Chip
Chip
Chip
DRAM
…
SSD
Host
Embedded Cores
Embedded Cores
Embedded Cores
Embedded Cores
…
Flash Chip
Flash Chip
Flash Chip
Flash Chip
Is a single NDP paradigm good for all workloads?
Which is the most suitable NDP paradigm for each computation?
Do we need to combine these NDP paradigms?

## Slide 14: Case Study on Combining NDP Paradigms (1/5)
We examine the performance bottlenecks by hand-mapping parts of the workload to multiple SSD computation resources
Evaluated Policies
  Host CPU
  In-storage processing (ISP)
  In-flash processing (IFP)
  Offloading to both ISP and IFP (ISP + IFP)
Evaluated Workloads
  Hybrid workloads: Workloads that involve both computation and data movement (e.g., aggregation, sorting)
  I/O-Intensive workloads: Workloads dominated by data movement (e.g., databases, bitmap indices)
  More in the paper
14

## Slide 15: Case Study on Combining NDP Paradigms (2/5)
15
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU

## Slide 16: Case Study on Combining NDP Paradigms (3/5)
16
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
Offloading to ISP and IFP improves performance by 40% over IFP by reducing data movement and mapping computations to the most suitable computation resource
40% performance improvement

## Slide 17: Case Study on Combining NDP Paradigms (4/5)
17
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
I/O-Intensive Workloads
Host CPU
ISP
IFP
IFP+ISP

## Slide 18: Case Study on Combining NDP Paradigms (5/5)
18
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
I/O-Intensive Workloads
Host CPU
ISP
IFP
IFP+ISP
15% performance reduction
Naively combining multiple computation resources in I/O-intensive workloads negates offloading benefits due to data movement between computation resources

## Slide 19: Case Study: Key Takeaways
19
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
I/O-Intensive Workloads
Host CPU
ISP
IFP
IFP+ISP
15% performance reduction
No single computation resource consistently performs well across different workloads
Performance bottlenecks are workload-dependent and vary across different execution phases of the same workload
Offloading to multiple SSD computation resources provides benefits, but only when done judiciously

## Slide 20: Limitations of Prior SSD-Based NDP Techniques
Prior SSD-based NDP techniques
Map computations only to one or two NDP paradigms and fail to exploit the SSD’s full computational potential
Lack generality across a wide range of applications
Are not programmer-transparent
20

## Slide 21: NDP Offloading Techniques For Main Memory
No prior work proposes application-transparent offloading of computations across multiple SSD computation resources
Several NDP offloading techniques explore partitioning and mapping application code segments between host and NDP units near main memory
We adapt these offloading models for SSD-based NDP
BW-Offloading: Makes offloading decisions based on bandwidth utilization of the host and NDP units
(e.g., TOM [Hsieh+, ISCA 2016], ƛ-IO [Yang+, FAST 2023])
DM-Offloading: Makes offloading decisions to minimize data movement between the host and NDP units
(e.g., ALP [Mansouri Ghiasi+, TETC 2023], PIMProf [Wei+, DATE 2022])
21

## Slide 22: Effectiveness of Prior Offloading Techniques
Speedup over CPU
DM-Offloading falls short of the Ideal’s performance by 2.5x due to its narrow offloading model
DM-Offloading prefers a single computation resource to reduce data movement, causing queueing delays and resource contention
22
Chart: 
| AES | XOR Filter | heat-3d | jacobi-1d | LlaMA2 Inference | LLM Training | GMEAN
BW-Offloading | 5.2772 | 4.7324 | 0.90177 | 1.2396 | 1.7703 | 1.8721 | 2.1267
DM-Offloading | 7.5849 | 5.6139 | 0.82558 | 1.1999 | 1.7494 | 2.2319 | 2.3413
Ideal | 7.6843 | 6.8309 | 3.7102 | 3.2149 | 7.9975 | 7.452 | 5.7807
8.0
2.5x

## Slide 23: Our Goal
To enable programmer-transparent NDP in an SSD that
effectively utilizes multiple SSD computation resources to perform computations
makes workload- and system-aware offloading decisions
improves performance and energy efficiency of a wide range of applications
23

## Slide 24: Talk Outline
Background and Motivation
Conduit
Evaluation
Summary
24

## Slide 25: Our Proposal
A general-purpose programmer-transparent NDP framework that dynamically offloads computations at instruction granularity to multiple heterogeneous SSD computation resources
25
Conduit

## Slide 26: Conduit: Key Steps
Compile-time pre-processing step to identify offloadable code regions in the application and transform them to wide vector operations
Runtime offloading of vectorized instructions to the most suitable SSD computation resource based on application and system characteristics
26

## Slide 27: Conduit: Key Steps
Compile-time pre-processing step to identify offloadable code regions in the application and transform them to wide vector operations
Runtime offloading of vectorized instructions to the most suitable SSD computation resource based on application and system characteristics
27

## Slide 28: Conduit: Compile-Time Preprocessing (1/3)
Embedded Core
Intermediate Representation (IR)
Host
for (j = 0; j < nb; ++j) {
….
if ((ret[1 + j * 4] >> 8) == 1) {
ret[1 + j * 4] ^= 283;
}
….
}
Application Code
…
%38 = load <4096 x i32>, ptr %37, align 4
%39 = xor <4096 x i32> %38, %34
%40 = xor <4096 x i32> %39, %21
%41 = xor <4096 x i32> %40, %22
%42 = and <4096 x i32> %20, <i32 283 … i32>
…
Loop Auto-Vectorization
Conduit runs a custom compiler (e.g., LLVM) pass to identify offloadable code regions
Loop auto-vectorization transforms scalar instructions into wide vector operations that match the SSD-internal parallelism
Conduit leverages partial vectorization so that partially vectorizable code regions benefit from parallel execution in an SSD
28

## Slide 29: Conduit: Compile-Time Preprocessing (2/3)
Embedded Core
"element_size": "i32",
"index": "%42",
"length": 4096,
"line": 387,
"load_addr": ["const"],
"operands": [ "%20", const"],
"operation": "and"
Metadata
Host
for (j = 0; j < nb; ++j) {
….
if ((ret[1 + j * 4] >> 8) == 1) {
ret[1 + j * 4] ^= 283;
}
….
}
Application Code
…
%38 = load <4096 x i32>, ptr %37, align 4
%39 = xor <4096 x i32> %38, %34
%40 = xor <4096 x i32> %39, %21
%41 = xor <4096 x i32> %40, %22
%42 = and <4096 x i32> %20, <i32 283 … i32>
…
Conduit extracts lightweight metadata (e.g., operation type, operand pointers, element sizes, vector length) for each vector operation
Loop Auto-Vectorization
Extract Metadata
Conduit embeds the metadata with IR to reduce runtime scheduling latency and preserve programmer transparency
29
Intermediate Representation (IR)

## Slide 30: Conduit: Compile-Time Preprocessing (3/3)
Embedded Core
"element_size": "i32",
"index": "%42",
"length": 4096,
"line": 387,
"load_addr": ["const"],
"operands": [ "%20", const"],
"operation": "and"
Metadata
Host
for (j = 0; j < nb; ++j) {
….
if ((ret[1 + j * 4] >> 8) == 1) {
ret[1 + j * 4] ^= 283;
}
….
}
Application Code
…
%38 = load <4096 x i32>, ptr %37, align 4
%39 = xor <4096 x i32> %38, %34
%40 = xor <4096 x i32> %39, %21
%41 = xor <4096 x i32> %40, %22
%42 = and <4096 x i32> %20, <i32 283 … i32>
…
Generate an ARM Executable
Transfer Executable to SSD
SSD
Conduit converts the IR with metadata to an executable capable of running on ARM cores
Conduit transfers the ARM executable to the SSD by repurposing existing NVMe admin commands for firmware update
30
Intermediate Representation (IR)

## Slide 31: Conduit: Key Steps
Compile-time pre-processing step to identify offloadable code regions in the application and transform them to wide vector operations
Runtime offloading of vectorized instructions to the most suitable SSD computation resource based on application and system characteristics
31

## Slide 32: Conduit: Runtime Offloading (1/3)
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Host
Transfer Binary to SSD
The SSD controller has real-time knowledge of the current state (e.g., resource utilization, contention in shared channels) of all SSD computation resources
Conduit performs runtime offloading in the SSD controller to preserve programmer transparency and avoid changes to the storage stack
Runtime Offloading
32

## Slide 33: Conduit: Runtime Offloading (2/3)
17
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Cost Function
SSD Offloader
Embedded Core
Conduit’s SSD offloader maps each vectorized instruction in the ARM executable to the most-suitable SSD computation resource based on a cost function
33

## Slide 34: Conduit: Runtime Offloading (3/3)
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Cost Function
SSD Offloader
Embedded Core
34
Conduit’s SSD offloader maps each vectorized instruction in the ARM executable to the most-suitable SSD computation resource based on a cost function

## Slide 35: Conduit: Cost Function
Cost Function
SSD Offloader
35
Cost Function
SSD Offloader

## Slide 36: Conduit: Cost Function
Cost Function
SSD Offloader
Data Movement Latency
Conduit tracks both application characteristics and current system conditions to evaluate the cost of offloading an instruction to each SSD computation resource
36
Data movement latencies if the operands are not in the target computation resource

## Slide 37: Conduit: Cost Function
Cost Function
SSD Offloader
Data Movement Latency
Conduit tracks both application characteristics and current system conditions to evaluate the cost of offloading an instruction to each SSD computation resource
37
Expected Computation Latency
Estimated instruction execution latency on a computation resource based on the operation type
+

## Slide 38: Conduit: Cost Function
Cost Function
SSD Offloader
Data Movement Latency
Conduit tracks both application characteristics and current system conditions to evaluate the cost of offloading an instruction to each SSD computation resource
38
Expected Computation Latency
+
Data Dependence Delay
Delay for operand availability
+

## Slide 39: Conduit: Cost Function
Cost Function
SSD Offloader
Data Movement Latency
Conduit tracks both application characteristics and current system conditions to evaluate the cost of offloading an instruction to each SSD computation resource
39
Expected Computation Latency
Resource Queueing Delay
Delay caused by pending instructions in a computation resource’s execution queue
Data Dependence Delay
+
+

## Slide 40: Conduit: Cost Function
Cost Function
SSD Offloader
Data Movement Latency
Conduit tracks both application characteristics and current system conditions to evaluate the cost of offloading an instruction to each SSD computation resource
40
Expected Computation Latency
max
Total Execution Latency Per Resource
Resource Queueing Delay
Data Dependence Delay
+
+

## Slide 41: Conduit: Cost Function
Cost Function
SSD Offloader
Total LatencyISP
Total LatencyPuD-SSD
Total LatencyIFP
min
Offloading Target
Conduit calculates the latency of executing each instruction on each computation resource, and selects the computation resource with the lowest execution latency
41

## Slide 42: Conduit: Instruction Transformation (1/4)
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Cost Function
SSD Offloader
Embedded Core
Instruction
Transformation
Conduit’s instruction transformation unit transforms each vectorized instruction to the native ISA of the chosen SSD computation resource
42

## Slide 43: Conduit: Instruction Transformation (2/4)
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Cost Function
SSD Offloader
Embedded Core
Instruction
Transformation
For ISP, Conduit transforms each vector operation to ARM Cortex ISA, and schedules the instruction for execution
ARM Cortex ISA
Offload to ISP
43

## Slide 44: Conduit: Instruction Transformation (3/4)
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Cost Function
SSD Offloader
Embedded Core
Instruction
Transformation
Conduit transforms each vector operation to ISA extensions (e.g., bbop_op for 2-input arithmetic) from prior PuD works (e.g., SIMDRAM [Hajinazar and Oliveira+, ASPLOS 2021])
PuD ISA
Offload to PuD-SSD
44

## Slide 45: Conduit: Instruction Transformation (4/4)
SSD
SSD Controller
Processing using DRAM
In-Flash Processing
…
Emb.
Core
Emb.
Core
Emb.
Core
Cost Function
SSD Offloader
Embedded Core
Instruction
Transformation
For IFP, Conduit leverages the MWS primitives from Flash-Cosmos [Park+, MICRO 2022] and arithmetic operations from Ares-Flash [Chen+, MICRO 2024] for instruction transformation
IFP ISA
Offload to IFP
45

## Slide 46: More in the paper
Data coherence across SSD computation resources
  Conduit employs a lazy coherence mechanism
Data mapping and SSD-internal data movement
Host-SSD communication
  Regular I/O mode
  Computation mode
Failure handling
Conduit’s extensibility
Limitations of auto-vectorization
Conduit’s applicability to irregular workloads
Detailed background on the three NDP paradigms
Detailed description of binary transfer from the host to the SSD
46

## Slide 47: More in the Paper
https://arxiv.org/pdf/2601.17633
47

## Slide 48: Talk Outline
Background and Motivation
Conduit
Evaluation
Summary
48

## Slide 49: Evaluation Methodology
Using an in-house event-driven SSD simulator that faithfully models:
  Core SSD functionalities (e.g., address translation, transaction scheduling) based on MQSim [Tavakkol+, FAST 2018]
  DRAM modeling based on Ramulator [Kim+, CAL 2015]
  Shared resource contention
  Performance models of three NDP paradigms
SSD configuration based on Samsung 980 Pro SSD
Six data-intensive workloads from
  AES, XOR Filter, heat-3d, jacobi-1d, LlaMA2 training and inference
Evaluated Policies
  Host CPU
  BW-Offloading: Offloading based on bandwidth utilization (based on TOM [Hsieh+, ISCA 2016], ƛ-IO [Yang+, FAST 2023])
  DM-Offloading: Offloading based on data movement cost (based on ALP [Mansouri Ghiasi+, TETC 2023], PIMProf [Wei+, DATE 2022])
  Conduit
  Ideal Offloading: No resource contention, resource selection based on lowest computation latency and zero data movement
49

## Slide 50: Results: Performance Analysis
Conduit outperforms the best-performing prior approach by 1.8x on average by making holistic offloading decisions
Conduit provides 62% of the Ideal offloading policy’s performance without the ideal approach’s unrealistic assumptions
Speedup over CPU
50
Chart: 
| AES | XOR Filter | heat-3d | jacobi-1d | LlaMA2 Inference | LLM Training | GMEAN
BW-Offloading | 5.2772 | 4.7324 | 0.90177 | 1.2396 | 1.7703 | 1.8721 | 2.1267
DM-Offloading | 7.5849 | 5.6139 | 0.82558 | 1.1999 | 1.7494 | 2.2319 | 2.3413
Conduit | 7.592 | 6.2052 | 3.7009 | 1.5863 | 4.2432 | 4.5677 | 4.1834
Ideal | 7.6843 | 6.8309 | 3.7102 | 3.2149 | 7.9975 | 7.452 | 5.7807
8.0
2.0x
1.8x
38%

## Slide 51: Results: Energy Consumption
Energy Consumption
Conduit reduces energy consumption by 46.8% on average compared to DM-Offloading by exploiting all SSD computation resources and reducing resource queueing delays
Conduit provides 68% of the energy efficiency of the Ideal approach
51
Chart: 
| AES | XOR Filter | heat-3d | jacobi-1d | LlaMA 2 Inference | LLM Training | AVG
BW-Offloading | 0.17935 | 0.1979 | 0.78439 | 0.60142 | 0.44363 | 0.41013 | 0.43614
DM-Offloading | 0.12334 | 0.15905 | 0.892 | 0.59327 | 0.42708 | 0.32591 | 0.42011
Conduit | 0.12335 | 0.15706 | 0.23723 | 0.46149 | 0.19975 | 0.18673 | 0.2276
Ideal | 0.091428 | 0.11309 | 0.23969 | 0.25049 | 0.12159 | 0.10913 | 0.15424
46.8%
32%

## Slide 52: Offloading Decisions
Chart: 
| BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal
PuD-SSD | 0.53825 | 0.30263 | 0.30383 | 0.30263 | 0.81476 | 0.5002 | 0.70318 | 0.98306 | 0.25876 | 1 | 0.40007 | 0.4 | 0.56284 | 0 | 0.0012295 | 0 | 0.84374 | 0 | 0.48698 | 0.48698 | 0.52256 | 0.16685 | 0.32982 | 0.2176
IFP | 0.42286 | 0.69389 | 0.69242 | 0.69737 | 0.16561 | 0.49718 | 0.29117 | 0.011296 | 0.53725 | 0 | 0.40007 | 0.2 | 0.43716 | 1 | 0.66544 | 0.66667 | 0.13482 | 1 | 0 | 0 | 0.38254 | 0.83315 | 0.54934 | 0.66154
ISP | 0.038893 | 0.0034811 | 0.0037505 | 0 | 0.019625 | 0.0026242 | 0.0056478 | 0.0056478 | 0.20398 | 0 | 0.19987 | 0.4 | 0 | 0 | 0.33333 | 0.33333 | 0.021434 | 0 | 0.51302 | 0.51302 | 0.0949 | 0 | 0.12085 | 0.12086
LLM Training
LlaMA 2 Inference
jacobi-1d
heat-3d
XOR Filter
AES

## Slide 53: Offloading Decisions
Chart: 
| BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal | BW-Offloading | DM-Offloading | Conduit | Ideal
PuD-SSD | 0.53825 | 0.30263 | 0.30383 | 0.30263 | 0.81476 | 0.5002 | 0.70318 | 0.98306 | 0.25876 | 1 | 0.40007 | 0.4 | 0.56284 | 0 | 0.0012295 | 0 | 0.84374 | 0 | 0.48698 | 0.48698 | 0.52256 | 0.16685 | 0.32982 | 0.2176
IFP | 0.42286 | 0.69389 | 0.69242 | 0.69737 | 0.16561 | 0.49718 | 0.29117 | 0.011296 | 0.53725 | 0 | 0.40007 | 0.2 | 0.43716 | 1 | 0.66544 | 0.66667 | 0.13482 | 1 | 0 | 0 | 0.38254 | 0.83315 | 0.54934 | 0.66154
ISP | 0.038893 | 0.0034811 | 0.0037505 | 0 | 0.019625 | 0.0026242 | 0.0056478 | 0.0056478 | 0.20398 | 0 | 0.19987 | 0.4 | 0 | 0 | 0.33333 | 0.33333 | 0.021434 | 0 | 0.51302 | 0.51302 | 0.0949 | 0 | 0.12085 | 0.12086
LLM Training
LlaMA 2 Inference
jacobi-1d
heat-3d
XOR Filter
AES
Conduit makes similar offloading decisions as the Ideal offloading approach without the Ideal’s unrealistic assumptions
53

## Slide 54: Overhead Analysis
Storage Overhead
Runtime Latency Overhead
Area Overhead
  17 bytes for storing cost function features in the SSD DRAM
  1.5 KiB for storing the instruction transformation mapping of vectorized instructions to the native ISA of all computation resources
  3.8 µs on average for cost function feature collection and instruction transformation for each instruction
54
  Conduit does not add any area overhead beyond that of the prior techniques it leverages

## Slide 55: More in the Paper
Tail latency evaluation
  In LlaMA2 inference, compared to DM-Offloading, Conduit reduces 99th percentile latency by 5.6x, and 99.99th percentile latency by 22.3x
Interaction between the workload and SSD computation resources
Detailed description of overhead analysis
Detailed workload description and characteristics
Detailed description of SSD modeling and NDP extensions
55

## Slide 56: More in the Paper
https://arxiv.org/pdf/2601.17633
56

## Slide 57: Talk Outline
Background and Motivation
Conduit
Evaluation
Summary
57

## Slide 58: Conduit: Summary
First general-purpose programmer-transparent NDP framework that enables fine-grained computation offloading across multiple SSD computation resources
Improves performance by 1.8x on average over the best-performing prior offloading approach
Reduces energy consumption by 46.8% on average over the most efficient prior work
Low latency and storage overheads
58

## Slide 59: Conduit Programmer-Transparent Near-Data Processing Using Multiple Compute-Capable Resources in Solid State Drives
Rakesh Nadig, Vamanan Arulchelvan, Mayank Kabra, Harshita Gupta, Rahul Bera, Nika Mansouri Ghiasi,
Nanditha Rao, Qingcai Jiang, Andreas Kosmas Kakolyris, Yu Liang, Mohammad Sadrosadati, and Onur Mutlu
HPCA 2026
Notes: Hello and Good afternoon. I am Rakesh Nadig, a Phd student from SAFARI Research group at ETH Zurich. I am going to present our work “Conduit: Programmer-Transparent Near-Data Processing Using Multiple Compute-Capable Resources in Solid-State Drives”.

## Slide 60: Backup Slides

## Slide 61: FAQ (1/2)
Executive Summary
PuD-SSD
IFP
Extended Case Study (With More Compute-Intensive Workloads)
Compile-Time Preprocessing
Runtime Offloading
System Integration

## Slide 62: FAQ (2/2)
Evaluated Configurations
Workload Characteristics
Results
  Extended Performance Results
  Extended Energy Consumption
  Tail Latency
  Workload-Computation Resource Interaction

## Slide 63: Executive Summary
Background: A solid-state drive enables three near-data processing paradigms: processing using embedded cores, processing using DRAM, and in-flash processing
Problem:
  Prior SSD-based NDP techniques (1) do not exploit the SSD’s full computational potential, (2) are application-specific, and (3) are not programmer-transparent
  Prior main-memory-based NDP offloading techniques provide limited benefits for an SSD because they optimize for limited factors (e.g., bandwidth utilization)
Goal: To enable a programmer-transparent NDP framework in SSDs that (1) offloads computations across multiple SSD computation resources, and (2) makes offloading decisions that are both workload- and system-aware
Conduit: A general-purpose programmer-transparent NDP framework that consists of:
  compile-time preprocessing to identify offloadable code regions and transform them to wide vector operations,
  runtime offloading that maps computations to the most suitable SSD computation resource based on workload and system factors
Key Results: We evaluate Conduit and two prior NDP offloading techniques using an in-house event-driven SSD simulator on six data-intensive workloads
  Compared to the best prior offloading policy, Conduit improves performance by 1.8x on average and reduces energy consumption by 46% on average

## Slide 64: In-Storage Processing (ISP)
The embedded cores in the SSD controller typically execute FTL firmware and handle host communication
The embedded cores can be repurposed to perform general-purpose computations
Many prior works show that ISP accelerates various tasks including filtering, aggregation, encryption, and search
Limited SIMD parallelism (e.g., 32-bit registers in ARM Cortex R5)
64

## Slide 65: Processing-Using-DRAM in SSD (PuD-SSD)
SSD-Internal DRAM
[1] Hajinazar+, “SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM," In ASPLOS, 2021
[2] Oliveira+, “MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing,” In HPCA, 2024
DRAM Bank
…
…
Bank
DRAM Chip
Bank
Bank
Bank
Bank
Bank
I/O Logic
…
…
PuD techniques leverage DRAM’s operational principles to perform computations within the memory array
Prior works (e.g., SIMDRAM[1], MIMDRAM[2]) enable bulk-bitwise and complex arithmetic operations entirely within the DRAM chips
65

## Slide 66: Processing-Using-DRAM in SSD (PuD-SSD)
SSD-Internal DRAM
[1] Hajinazar+, “SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM," In ASPLOS, 2021
[2] Oliveira+, “MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing,” In HPCA, 2024
DRAM Bank
…
…
Bank
DRAM Chip
Bank
Bank
Bank
Bank
Bank
I/O Logic
…
…
PuD-SSD requires transferring operands from flash chips to the DRAM via bandwidth-limited flash channels
These data transfers incur latency and energy overheads, and cause contention in flash channels
66

## Slide 67: In-Flash Processing (IFP) (1/2)
SSD Controller
Channel
Flash Chip
Flash Chip
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Bitlines (BLs)
Operand O1
67

## Slide 68: In-Flash Processing (IFP) (1/2)
SSD Controller
Channel
Flash Chip
Flash Chip
NAND Flash Chip
Page Buffer
Bitlines (BLs)
Several IFP techniques (e.g., Ares-Flash[3]) enable arithmetic operations inside NAND flash chips by controlling the latching circuit of the page buffer
Operand O2
Operand O3
…
Operand O32
Operand O1
Operand O1
Sensing
[3] Chen+, “Ares-Flash: Efficient Parallel Integer Arithmetic Operations Using NAND Flash Memory," In MICRO, 2024
Operand O1
68

## Slide 69: In-Flash Processing (IFP) (1/2)
SSD Controller
Channel
Flash Chip
Flash Chip
NAND Flash Chip
Page Buffer
Bitlines (BLs)
Operand O2
Operand O3
…
Operand O32
Operand O1
Operand O1
Sensing
Operand O2
O1 Add O2
[3] Chen+, “Ares-Flash: Efficient Parallel Integer Arithmetic Operations Using NAND Flash Memory," In MICRO, 2024
Several IFP techniques (e.g., Ares-Flash[3]) enable arithmetic operations inside NAND flash chips by controlling the latching circuit of the page buffer
69

## Slide 70: In-Flash Processing (IFP) (2/2)
SSD Controller
Channel
Flash Chip
Flash Chip
NAND Flash Chip
Page Buffer
Bitlines (BLs)
Operand O2
Operand O3
…
Operand O32
Operand O1
Operand O1
Single Sensing
Page Buffer
Flash-Cosmos[4] enables bulk-bitwise operations inside NAND flash chips by simultaneously reading multiple pages within the flash chips
[4] Park+, "Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory." In MICRO, 2022
Operand O32
…
Operand O3
Operand O2
Operand O1
O1 & O2 & O3 & …& O32
IFP techniques support limited set of operations and are less suitable for complex workloads
70

## Slide 71: Extended Case Study (1/5)
We examine the performance bottlenecks when offloading computations to multiple SSD computation resources
Evaluated Policies
  Host CPU
  In-storage processing (ISP)
  In-flash processing (IFP)
  Offloading to both ISP and IFP (ISP + IFP)
Evaluated Workloads
  I/O-Intensive workloads: Workloads dominated by data transfer (e.g., databases, bitmap indices)
  More compute-intensive workloads: Workloads dominated by computations (e.g., encryption, matrix multiplication)
  Hybrid workloads: Workloads that involve both computation and data movement (e.g., aggregation, sorting)
71

## Slide 72: Extended Case Study (2/5)
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
I/O-Intensive Workloads
ISP
IFP
IFP+ISP
Host CPU
ISP
IFP
IFP+ISP
More Compute-Intensive Workloads
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
Host CPU
72

## Slide 73: Extended Case Study (3/5)
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
I/O-Intensive Workloads
ISP
IFP
IFP+ISP
Host CPU
ISP
IFP
IFP+ISP
More Compute-Intensive Workloads
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
Host CPU
Offloading to ISP and IFP in I/O-intensive workloads reduces performance by 15% compared to IFP
Offloading to multiple computation resources incurs additional data movement between flash chips and SSD controller
73

## Slide 74: Extended Case Study (4/5)
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
I/O-Intensive Workloads
ISP
IFP
IFP+ISP
Host CPU
ISP
IFP
IFP+ISP
More Compute-Intensive Workloads
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
Host CPU
Offloading to ISP and IFP improves performance by 28% over IFP by mitigating the limitations of individual computation paradigms
74

## Slide 75: Extended Case Study (5/5)
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1
Series 2
Series 3
Computation
Host-SSD Data Movement
SSD-Internal Data Movement
Flash Read
I/O-Intensive Workloads
ISP
IFP
IFP+ISP
Host CPU
ISP
IFP
IFP+ISP
More Compute-Intensive Workloads
ISP
IFP
IFP+ISP
Hybrid Workloads
Overall Execution Time (Normalized to Host CPU)
Host CPU
Host CPU
Offloading to ISP and IFP improves performance by 40% over IFP by reducing data movement and mapping computations to the most suitable computation resource
75

## Slide 76: Compile-Time Preprocessing
Compiler Flags
  -O3 -g –mllvm -force-vector-width=4096 -force-vector-interleave=1 -Rpass-analysis=loop-vectorize -Rpass=loop-vectorize
-force-vector-width=4096 - Aligns each vector to a typical NAND flash page (vector width of 4096 for 32-bit operands)
  Simplifies data movement across computation resources
  Avoids misaligned accesses
  Matches L2P mapping granularity
-force-vector-interleave=1 flag controls loop unrolling to enable instruction-granularity offloading
76

## Slide 77: Runtime Offloading: Cost Function
77

## Slide 78: Runtime Offloading: Why do it in SSD?
SSD controller has real-time knowledge of all computation resources and shared resource contention
We explored offloading in the host CPU
Limitations of offloading in the host CPU
  No real-time status of the SSD internals in the host
  Significant traffic if the SSD needs to transfer information to the host frequently
  We need to think of a better way to do this in the future
78

## Slide 79: System Integration (1/4)
Transferring the binary
  Repurpose fw-download and fw-commit commands
  Extend these commands with a new flag to identify Conduit’s executable
Data mapping and SSD-internal data movement
  Conduit adheres to the data layout requirements of prior techniques
Host-SSD communication
  Regular I/O mode: Host I/O and FTL operations are executed
  Computation mode: Host I/O is suspended while performing maintenance tasks such as garbage collection and wear-leveling
79

## Slide 80: System Integration (2/4)
Data Coherence between SSD computation resources
  Conduit employs a lazy coherence mechanism
  Conduit synchronizes data across SSD computation resources only when
    Another computation resource requests data
    Computation result must be transferred to the host
    Data must be evicted from SSD DRAM, page buffers or SSD controller registers
    FTL initiates garbage collection
    SSD undergoes power cycle
80

## Slide 81: System Integration (3/4)
Data Coherence between SSD computation resources
  Conduit maintains coherence at page-granularity by extending the logical-to-physical mapping table to store:
    Owner - SSD computation resource that holds the latest version of the page
    State – page’s modification status (i.e., clean or dirty)
    Version – 1-byte monotonically-increasing counter to order updates and detect stale copies
81

## Slide 82: System Integration (4/4)
Failure Handling
  For transient failures (e.g., instruction abort, ECC correction failures), the SSD controller maintains completion and status flags, and replays the instruction in a different computation resource
  For permanent faults (e.g., bad blocks), Conduit relies on existing FTL recovery mechanisms such as bad-block remapping, garbage collection and wear-leveling
82

## Slide 83: Evaluated Configurations
83

## Slide 84: Workloads (1/3)
AES
  256-bit encryption and decryption algorithm with high data reuse and low-latency bitwise operations
XOR Filter
  A probabilistic data structure for fast membership tests
  Dominated by arithmetic and predication operations
heat-3d
  3D stencil computation that repeatedly updates each grid point using its neighbors
  Moderate-to-high arithmetic intensity with high data reuse
jacobi-1d
  1D stencil computation solver that updates each element using values from its immediate neighbors
  Moderate-to-high latency operations
84

## Slide 85: Workloads (2/3)
LlaMA2 Inference
  INT8 inference of a 7B-parameter LlaMA2 model
  High and medium latency operations
LLM Training
  Bandwidth-intensive INT8 training of 7B-parameter model characterized by frequent weight updates, data movement, and a combination of arithmetic and control-intensive operations
Quantization enables complete execution of all workloads within the SSD
Memory footprint of each workload exceeds the SSD capacity by 2x
  Induces resource contention and data movement scenarios
85

## Slide 86: Workloads (3/3)
86

## Slide 87: LLM Inference and Training Characteristics
LLM Inference
  Linear layers (Q, K, V, FFN)
    Matrix multiplications, high arithmetic intensity
  Attention-Score computation
    Dot products
  Element-wise operations: scaling, residual add…
  Layer normalization
    Accumulation, scale and shift
  Partially vectorizable – reduction, exponentiation, normalization
  Not vectorizable
    Token selection and sampling
      Branch-heavy, data-dependent
87

## Slide 88: LLM Inference and Training Characteristics
LLM Training
  Forward Pass
    Vectorizable
  Backpropagation
    Gradient computation: Dense matrix computations, high reuse, arithmetic-heavy
  Weight updates
    Element-wise arithmetic (SIMD friendly)
  Optimizer logic
    Conditionals, state updates and control flow
88

## Slide 89: Extended Results: Performance Analysis
Conduit outperforms the best-performing prior approach by 1.8x on average by making holistic offloading decisions
Conduit provides 62% of the Ideal offloading policy’s performance without the ideal approach’s unrealistic assumptions
Chart: 
| AES | XOR Filter | heat-3d | jacobi-1d | LlaMA2 Inference | LLM Training | GMEAN
GPU | 4.3866 | 5.6734 | 1.2601 | 1.5248 | 1.7684 | 2.1328 | 2.377
ISP | 1.5157 | 1.2933 | 1.032 | 1.2885 | 1.1261 | 1.444 | 1.2721
PuD-SSD | 3.8303 | 4.1971 | 0.75456 | 1.2232 | 1.7627 | 1.6422 | 1.8714
IFP | 3.0746 | 2.9981 | 0.82558 | 1.3087 | 1.7494 | 1.997 | 1.8068
BW-Offloading | 5.2772 | 4.7324 | 0.90177 | 1.2396 | 1.7703 | 1.8721 | 2.1267
DM-Offloading | 7.5849 | 5.6139 | 0.82558 | 1.1999 | 1.7494 | 2.2319 | 2.3413
Conduit | 7.592 | 6.2052 | 3.7009 | 1.5863 | 4.2432 | 4.5677 | 4.1834
Ideal | 7.6843 | 6.8309 | 3.7102 | 3.2149 | 7.9975 | 7.452 | 5.7807
Speedup over CPU
1.79x
3.3x
2.2x
2.3x
2.0x
1.8x
38%
89

## Slide 90: Extended Results: Energy Consumption
Energy Consumption
Conduit reduces energy consumption by 46.8% on average compared to DM-Offloading by reducing resource queueing delays and exploiting all SSD computation resources
Conduit provides 68% of the energy efficiency of the Ideal approach
Chart: 
| AES | XOR Filter | heat-3d | jacobi-1d | LlaMA 2 Inference | LLM Training | AVG
GPU | 0.34295 | 0.26401 | 0.82429 | 0.6913 | 0.60115 | 0.54551 | 0.54487
ISP | 0.45477 | 0.70416 | 0.85099 | 0.70752 | 0.84575 | 0.61325 | 0.69607
PuD-SSD | 0.25687 | 0.37727 | 0.8 | 0.7828 | 0.63361 | 0.61817 | 0.57812
IFP | 0.22681 | 0.3911 | 0.8 | 0.69782 | 0.61168 | 0.48121 | 0.53477
BW-Offloading | 0.17935 | 0.1979 | 0.78439 | 0.60142 | 0.44363 | 0.41013 | 0.43614
DM-Offloading | 0.12334 | 0.15905 | 0.892 | 0.59327 | 0.42708 | 0.32591 | 0.42011
Conduit | 0.12335 | 0.15706 | 0.23723 | 0.46149 | 0.19975 | 0.18673 | 0.2276
Ideal | 0.091428 | 0.11309 | 0.23969 | 0.25049 | 0.12159 | 0.10913 | 0.15424
46.8%
32%
90
58.2%
67.3%
60.6%
57.4%
47.8%

## Slide 91: Tail Latency Evaluation (1/2)
Chart: 
(b) 99.99th Percentile Access Latency
(a) 99th Percentile Access Latency
Chart: 
Chart: 
Chart: 
LlaMA 2 Inference
jacobi-1d
CDF
102
104
106
102
104
106
102
103
104
105
102
103
104
105
  In LlaMA2 inference, compared to DM-Offloading, Conduit reduces 99th percentile latency by 5.6x, and 99.99th percentile latency by 22.3x
91

## Slide 92: Tail Latency Evaluation (2/2)
Chart: 
(b) 99.99th Percentile Access Latency
(a) 99th Percentile Access Latency
Chart: 
Chart: 
Chart: 
LlaMA 2 Inference
jacobi-1d
CDF
102
104
106
102
104
106
102
103
104
105
102
103
104
105
  In jacobi-1d, compared to DM-Offloading, Conduit reduces 99th percentile latency by 1.1x, and 99.99th percentile latency by 1.3x
92

## Slide 93: Workload-Computation Resource Interaction
(a) Operations
(b) BW-Offloading
(c) DM-Offloading
(d) Conduit
0
2000
4000
6000
8000
10000
12000
Number of Instructions
93