## Slide 1: DRAM Bender An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips
Ataberk Olgun
Yahya Can Tugrul
Minesh Patel
Hasan Hassan
Lois Orosa
Oguz Ergin
A. Giray Yaglikci
Haocong Luo
Onur Mutlu

## Slide 2: Factors Affecting DRAM Reliability and Latency
We need to perform experimental studies
of real DRAM chips
DRAM timing violation
Inter-cell interference
Voltage
Temperature
Manufacturing process
Factors affecting DRAM reliability and latency cannot be properly modeled in simulation or analytically
Notes: HBM chips harbor new architectural characteristics that might affect the RowHammer vulnerability
[CLICK] Understanding RowHammer enables designing effective and efficient solutions
[CLICK] However, no rigorous study demonstrates the RowHammer vulnerability in HBM
[CLICK] Our goal is to experimentally analyze how vulnerable real HBM chips are to RowHammer
[CLICK] Therefore, we perform a detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip and we provide two main findings.
[CLICK] First, we show that there is substantial variation in RowHammer vulnerability in different physical locations of high bandwidth memory chips. Different channels in 3D-stacked HBM chips exhibit different vulnerability, and
[CLICK] DRAM rows near the end of a DRAM bank are more RowHammer resilient
[CLICK] Second, we show that a modern HBM chip implements undisclosed on-DRAM-die Rowhammer mitigation
[CLICK] We find that this particular mitigation refreshes a victim row after every 17 periodic refresh operations, resembling a mitigation prior work found in DDR4 chips

## Slide 3: DRAM Testing Infrastructure
Allow experimental studies of real DRAM chips
Open-source FPGA-based testing infrastructure
Publicly-available: Start using today
Relatively low cost: An FPGA board + DRAM modules
SoftMC
Litex Tester

## Slide 4: Limitations of Existing Infrastructure
Impose restrictions on the DDR4 interface.
Restrictions limit various characterization experiments.
Difficult to set up (based on discontinued HW/SW) and use (require developing HW)
Monolithic hardware design makes extensions (new standards, prototypes) relatively difficult
Notes: They have several limitations that make it difficult to use them as flexible, accessible, extensible platforms.

## Slide 5: DRAM Bender: Design Goals
Flexibility
  Ability to test any DRAM operation
  Ability to test any combination of DRAM operations and custom timing parameters
Ease of use
  Simple programming interface (C++)
  Minimal programming effort and time
  Accessible to a wide range of users
    who may lack experience in hardware design
Extensibility
  Modular design
  Well-defined interfaces between hardware modules
Notes: I would like to explain the two goals that we believe a DRAM characterization infrastructure should achieve.
[CLICK] First, a DRAM characterization infrastructure should be flexible so that it can support testing any DRAM operation. The infrastructure should enable issuing the DRAM commands in any order, with adjustable and precise timing between these commands.
[CLICK]
Second, the infrastructure should be easy to use. It should have simple and intuitive programming interface that minimizes programming effort and time. It also should be accessible to wide-range of users. Even users that lack experience of hardware design should be able to perform DRAM tests.
We designed our infrastructure to achieve these goals.

## Slide 6: DRAM Bender: Overview
Publicly-available FPGA-based DDR4/3 (and HBM2) characterization infrastructure
Easily programmable using the DRAM Bender C++ API
[Yaglikci+, DSN’22]

## Slide 7: DRAM Bender: Prototypes
Five out of the box FPGA-based prototypes

## Slide 8: DRAM Bender: Three Case Studies
RowHammer: Interleaving Pattern of Activations
  Interleaving pattern significantly affects the number of RowHammer bitflips
RowHammer: Random Data Patterns
  Use 512-bit random data patterns
  Uncover more bitflips than 8-bit SoftMC random patterns
In-DRAM Bitwise Operations
  Demonstrate in-DRAM bitwise AND/OR capability in real DDR4 chips
DRAM Bender is flexible: supports many different types of experiments

## Slide 9: DRAM Bender: Ease of Use
RowHammer: Interleaving Pattern of Activations
Easy to devise new experiments to uncover new insights.
one iteration of the RowHammer test
Easily programmable using the DRAM Bender C++ API

## Slide 10: More in the paper (II)
DRAM Bender design details
  DRAM Bender instruction set architecture
  Hardware & software modules
  Prototype design
  Temperature controller setup
DRAM Bender application programming interface
Detailed results for three case studies
Future work & improvements

## Slide 11: More in the paper (II)
https://arxiv.org/abs/2211.05838

## Slide 12: Research DRAM Bender Enabled
[DSN’24] Olgun+, “Read Disturbance in High Bandwidth Memory: A Detailed Experimental Study on HBM2 DRAM Chips”
[DSN’24] Yuksel+, “Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis”
[DSN’24 Disrupt] Luo+, “An Experimental Characterization of Combined RowHammer and RowPress Read Disturbance in Modern DRAM Chips”
[HPCA’24] Yaglikci+, ”Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[HPCA’24] Yuksel+, “Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis"
[ISCA’23] Luo+, “RowPress: Amplifying Read Disturbance in Modern DRAM Chips”
[DSN’23 Disrupt] Olgun+, ”An Experimental Analysis of RowHammer on HBM2 DRAM Chips”
[arXiv Preprint, 2023] Orosa+, ”SpyHammer: Using RowHammer to Remotely Spy on Temperature”
[MICRO’22] Yaglikci+, “HIRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips”
[DSN’22] Yaglikci+, “Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices”
[MICRO’21] Orosa+, “A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses”
[MICRO’21] Hassan+, “Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications”
[ISCA’21] Olgun+, “QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips”

## Slide 13: More Research DRAM Bender Enabled
[ISCA’21] Orosa+, “CODIC: A Low-Cost Substrate for Enabling Custom In-DRAM Functionalities and Optimizations”
[ISCA’20] Kim+, “Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques”
[S&P’20] Frigo+, “TRRespass: Exploiting the Many Sides of Target Row Refresh”
[HPCA’19] Kim+, “D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput”
[MICRO’19] Koppula+, “EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM”
[SIGMETRICS’18] Ghose+, “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study”
[SIGMETRICS’17] Chang+, “Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms”
[MICRO’17] Khan+, “Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content”
[SIGMETRICS’16] Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization”

## Slide 14: Even More Research DRAM Bender Enabled
[ISCA’24] Nam+, ”DRAMScope: Uncovering DRAM Microarchitecture and Characteristics by Issuing Memory Commands”
[DATE’24] Zhou+, “DRAM-Locker: A General-Purpose DRAM Protection Mechanism Against Adversarial DNN Weight Attacks”
[DRAMSec’23] Lang+, “BLASTER: Characterizing the Blast Radius of Rowhammer”
[IEEE CAL’23] Nam+ ”X-ray: Discovering DRAM Internal Structure and Error Characteristics by Issuing Memory Commands”
[MICRO’22] Gao+, “FracDRAM: Fractional Values in Off-the-Shelf DRAM”
[Applied Sciences’22] Bepary+, “DRAM Retention Behavior with Accelerated Aging in Commercial Chips”
[ETS’21] Farmani+, “RHAT: Efficient RowHammer-Aware Test for Modern DRAM Modules”
[HOST’20] Talukder+, “Towards the Avoidance of Counterfeit Memory: Identifying the DRAM Origin”
[MICRO’19] Gao+, “ComputeDRAM: In-Memory Compute Using Off-the-Shelf DRAMs”
[IEEE Access’19] Talukder+, “PreLatPUF: Exploiting DRAM Latency Variations for Generating Robust Device Signatures”
[ICCE’18] Talukder+, “Exploiting DRAM Latency Variations for Generating True Random Numbers”
Notes: SoftMC has also contributed to research from other research groups.

## Slide 15: A Highlight: RowPress
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
These bitflips do NOT require many row activations
Only one activation is enough in some cases!
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips

## Slide 16: RowPress Results & Source Code
Fully open source and artifact evaluated
https://github.com/CMU-SAFARI/RowPress
Notes: We have more results in the paper, and our work is fully open-source and artifact evaluated.

## Slide 17: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 18: Summary
DRAM Bender
The first publicly-available DDR4 characterization infrastructure
github.com/CMU-SAFARI/DRAMBender
[Yaglikci+, DSN’22]
Flexible and Easy to Use
Source code available:
DRAM Bender enables many studies, ideas, and methodologies in the design of future memory systems
Notes: [CLICK] In summary, SoftMC is the first publicly-available DRAM characterization infrastructure
[CLICK] It is flexible and easy to use
[CLICK] The source code of SoftMC is available on GitHub
[CLICK] SoftMC enables many new studies, ideas, and methodologies in the design of future memory systems

## Slide 19: DRAM Bender Paper, Slides, Videos, Code
https://github.com/CMU-SAFARI/DRAM-Bender
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]

## Slide 20: DRAM Bender An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips
Ataberk Olgun
Yahya Can Tugrul
Minesh Patel
Hasan Hassan
Lois Orosa
Oguz Ergin
A. Giray Yaglikci
Haocong Luo
Onur Mutlu