## Slide 1
Chart: Performance Delta Over Baseline
| Homo- geneous | Hetro- geneous | Homo- geneous | Hetro- geneous | DRR4-2133 | DDR4-2400
BOP | 0.13488 | 0.10895 | 0.15387 | 0.2002
SMS | 0.16084 | 0.11323 | 0.19207 | 0.24859
SPP | 0.15863 | 0.11981 | 0.18497 | 0.22301
DSPatch+SPP | 0.21761 | 0.19358 | 0.26385 | 0.37347
DSPatch: Dual Spatial Pattern Prefetcher
1. Motivation
Rahul Bera* Anant V. Nori* Onur Mutlu+ Sreenivas Subramoney*
Chart: Peak DRAM Bandwidth (GBps)
| 12.8 | 17.064 | 19.2 | 25.6 | 34.128 | 38.4
BOP | 0.12663 | 0.1546 | 0.16501 | 0.18965 | 0.20001 | 0.20307
SMS | 0.13554 | 0.16531 | 0.17708 | 0.20545 | 0.21466 | 0.21883
SPP | 0.16331 | 0.18633 | 0.19606 | 0.21523 | 0.2153 | 0.21768
eSPP | 0.16851 | 0.19462 | 0.20529 | 0.2281 | 0.23155 | 0.23516
eBOP | 0.11565 | 0.14499 | 0.15687 | 0.18866 | 0.2091 | 0.21683
BW | 12.8 | 17.064 | 19.2 | 25.6 | 34.128 | 38.4
A
C
Current state-of-the-art spatial prefetcher performance plateaus despite increasing memory bandwidth
Need to boost speculation and coverage to maximize utilization of memory bandwidth resource
Fundamental tradeoff in traditional prefetcher design between Coverage versus Accuracy
Limits ability to dynamically adapt to memory bandwidth headroom and significantly boost Coverage
New prefetcher design should include:
Pattern representations best suited to capture spatially co-located program accesses and boost Coverage
Mechanisms to simultaneously optimize for both Coverage and Accuracy
Ability to dynamically adjust aggressiveness (Coverage vs. Accuracy) based on available DRAM bandwidth
2. Challenge
3. Goal
4. DSPatch Key Insights
A bit-pattern representation, rotated and anchored to the first “triggering” access to a page, captures all spatially identical patterns subsuming any temporal variability.
Captures all “global deltas” from the trigger access
Bit-wise OR of rotated bit-patterns adds missing bits to the pattern, biasing it towards Coverage
Bit-wise AND of rotated bit-patterns keeps only repeating bits in the pattern, biasing it for Accuracy
A
C
Using dual modulated bit-patterns allows DSPatch to simultaneously optimize for both Coverage and Accuracy
5. DSPatch Design
Page Buffer (PB) [1.23 KB]
Signature Prediction Table
(SPT)
[2.375 KB]
Program Access
Bandwidth
utilization
CovP
AccP
1
2
3
4
5
PC Signature | CovP | AccP
0x7ffecca | 1100011001111100 | 1000001000011000
Program
1001011100010001
PC Signature | CovP | AccP
0x7ffecca | 1101111101111101 | 1000001000010000
Pattern Update
Pattern
Predict
OR
AND
MeasureCovP : Incr. if CovP Coverage < 50% || CovP Accuracy < 50%
MeasureAccP : Incr. if AccP Accuracy < 50%
BW>=75%?
Predict AccP
Vulnerable Fill
No prediction
Y
Y
N
BW>=50%?
N
MeasureCovP saturated?
Predict CovP
N
Y
Y
N
MeasureAccP saturated?
Y
DSPatch: Overall Flow
DSPatch: Pattern Update
DSPatch: Pattern Predict
5. DSPatch Results
DSPatch: Single Core Performance
DSPatch: Single Core DRAM B/W Scaling
DSPatch: Multi-Core Performance
Chart: Performance Delta over Baseline (%)
| Client | Server | HPC | FSPEC06 | ISPEC06 | FSPEC17 | ISPEC17 | Cloud | SYSmark | GEOMEAN
BOP | 0.24657 | 0.079647 | 0.066882 | 0.21979 | 0.076985 | 0.12938 | 0.2303 | 0.12134 | 0.17731 | 0.1546
SMS | 0.28571 | 0.15068 | 0.14103 | 0.19384 | 0.10966 | 0.13275 | 0.1855 | 0.12346 | 0.19993 | 0.16531
SPP | 0.35968 | 0.17658 | 0.15982 | 0.25087 | 0.14144 | 0.18554 | 0.18215 | 0.10235 | 0.17791 | 0.18633
DSPatch | 0.32005 | 0.16144 | 0.1572 | 0.22308 | 0.15916 | 0.16664 | 0.237 | 0.14665 | 0.20152 | 0.19593
DSPatch+SPP | 0.36742 | 0.189 | 0.20327 | 0.29068 | 0.21909 | 0.19859 | 0.29611 | 0.20294 | 0.28665 | 0.2526
6%
Chart: Peak DRAM Bandwidth (GBps)
| 12.8 | 17.064 | 19.2 | 25.6 | 34.128 | 38.4
BOP | 0.12663 | 0.1546 | 0.16501 | 0.18965 | 0.20001 | 0.20307
SMS | 0.13554 | 0.16531 | 0.17708 | 0.20545 | 0.21466 | 0.21883
SPP | 0.16331 | 0.18633 | 0.19606 | 0.21523 | 0.2153 | 0.21768
DSPatch+SPP | 0.2044 | 0.2526 | 0.27337 | 0.31324 | 0.33125 | 0.33941
1ch-2133
2ch-2400
6%
10%
7.4%
15.1%
*Processor Architecture Research Lab (PARL), Labs
+ ETH Zürich