## Slide 1: DSPatch: Dual Spatial pattern prefetcher
Rahul Bera1, Anant V. Nori1, Onur Mutlu2, Sreenivas Subramoney1
1Processor Architecture Research Lab, Intel Labs
2ETH Zürich

## Slide 2: Summary
Motivation:
  DRAM bandwidth increases with every generation
  Prefetchers need to adapt to effectively utilize this resource
  Challenge:
  Significantly boost Coverage AND
  Simultaneously optimize for Accuracy
  Dual Spatial Pattern Prefetcher (DSPatch)
  Simultaneously learn two spatial bit-pattern representations of program accesses per page
    Coverage-biased (CovP)
    Accuracy-biased (AccP)
  Predict one of the patterns based on current DRAM bandwidth headroom
6% average speedup over baseline with PC-stride @ L1 and SPP @ L2
10% average speedup when DRAM bandwidth is doubled
Only 3.6 KB of hardware storage
BW
utilization
CovP
AccP

## Slide 3: Outline
1. Motivation and Observations
2. Dual Spatial Pattern Prefetcher (DSPatch)
3. Evaluation
4. Conclusion

## Slide 4: Motivation: Current prefetchers’ performance scales poorly with increasing DRAM bandwidth
Chart: Peak DRAM Bandwidth (GBps)
| 12.8 | 17.064 | 19.2 | 25.6 | 34.128 | 38.4
BOP | 0.12663 | 0.1546 | 0.16501 | 0.18965 | 0.20001 | 0.20307
SMS | 0.13554 | 0.16531 | 0.17708 | 0.20545 | 0.21466 | 0.21883
SPP | 0.16331 | 0.18633 | 0.19606 | 0.21523 | 0.2153 | 0.21768
eSPP | 0.16851 | 0.19462 | 0.20529 | 0.2281 | 0.23155 | 0.23516
eBOP | 0.11565 | 0.14499 | 0.15687 | 0.18866 | 0.2091 | 0.21683
A
C
Traditional prefetcher design tradeoff between Coverage and Accuracy
Limits ability to significantly boost Coverage when needed

## Slide 5: Observation 1 Anchored spatial bit-patterns well suited to capture spatial access patterns
1001 1000 0011 0000
Anchored spatial
bit-pattern
Spatial bit-pattern
0010 0110 0000 1100
0100 1100 0001 1000
Cacheline offset seq.
within a page
A: [02]-[06]-[05]-[12]-[13]
B: [01]-[05]-[04]-[11]-[12]
C: [01]-[05]-[11]-[04]-[12]
D: [01]-[11]-[05]-[04]-[12]
E: [01]-[11]-[04]-[05]-[12]
F: [01]-[04]-[11]-[05]-[12]
G: [01]-[04]-[05]-[11]-[12]
“_” marks the first (triggering) access to the page
+4, -1,+7,+1
+4,+6,-7,+8
+10,-6,-1,+8
+10,-7,+1,+7
+3,+7,-6,+7
+3,+1,+6,+7
Cacheline delta seq.
within a page
Spatial bit-patterns subsume any small temporal variability in accesses
Anchored spatial bit-patterns capture all “global” deltas from the triggering access

## Slide 6: Observation 2 Anchored spatial bit-patterns allow modulation for Coverage versus Accuracy
Bit-wise OR modulation ⇒ Biased towards Coverage
Bit-wise AND modulation ⇒ Biased towards Accuracy
Cacheline delta seq. within a page
Anchored spatial bit-patterns
+4,-1,+7,+1
+4,+6,-7,+8
…
+10,-6,-1,+8
+5,-1,+6,+1
…
+11,-1,-6,+1
+3,+2,+4,+2
…
+9,+1,-5,-2
1001 1000 0011 0000
1000 1100 0011 0000
1001 0100 0110 0000
Modulated anchored spatial bit-patterns
1001 1100 0011 1000
Coverage biased : 100% Coverage
OR
1000 1000 0001 0000
Accuracy biased : 100% accuracy
AND

## Slide 7: Outline
1. Motivation and Observations
2. Dual Spatial Pattern Prefetcher (DSPatch)
3. Evaluation
4. Conclusion

## Slide 8: DSPatch: Key Idea
  Simultaneously learn two modulated spatial bit-pattern representations of program accesses
      Coverage-Biased (CovP)
      Accuracy-Biased (AccP)
  Predict one of the patterns based on current DRAM bandwidth headroom
BW
utilization
CovP
A
C
AccP
Optimize simultaneously for both:
Significantly higher Coverage
High Accuracy

## Slide 9: DSPatch: Overall Design
Page Buffer (PB)
Signature Prediction Table
(SPT)
Program Access
BW
utilization
CovP
AccP
1
2
3
4
5
Page | Trigger PC | Bit-pattern
0x65 | 0x7ffecca | 0010 1100 0001 0010
0x66 | 0x7ff8980 | 0001 0010 0011 0001
.
.
.
.
.
.
.
.
.
PC Signature | CovP | AccP
0x7ffecca | 1011 0011 1110 0011 | 0001 0000 0011 0010
.
.
.
.
.
.
.
.
.

## Slide 10: DSPatch: Quantify Coverage, Accuracy and Bandwidth
Page Buffer (PB)
Signature Prediction Table
(SPT)
Program Access
BW
utilization
CovP
AccP
1
2
3
4
5
Pattern | Value | PopCount
From Program | 1011 0100 0011 1100 | 8
From SPT | 1010 0110 0000 0001 | 5
Bitwise-AND | 1010 0100 0000 0000 | 3
Quantifying DRAM bandwidth utilization
Count DRAM accesses in 4 x tRC window
Compare to peak possible access count
Quantize to quartile buckets (25%,50,75%)
Quantifying Coverage and Accuracy
Identify good bits in SPT pattern(s)
PopCount compare to program pattern
Quantize to quartile buckets (25%,50,75%)
Coverage
[25%-50%]
Accuracy
[50%-75%]

## Slide 11: DSPatch: Pattern Update
5
PC Signature | CovP | AccP
0x7ffecca | 1100 0110 0111 1100 | 1000 0010 0001 1000
Program
1001 0111 0001 0001
OR
AND
PC Signature | CovP | AccP
0x7ffecca | 1101 1111 0111 1101 | 1000 0010 0001 0000
2b
2b
ORcount
Limit number of modulation operations
MeasureCovP
Incr if CovP coverage < 50% || CovP accuracy < 50%
MeasureAccP
Incr if AccP accuracy < 50%
2b

## Slide 12: DSPatch: Pattern Predict
BW utilization >=75%?
Prefetch using AccP
Vulnerable Fill
No prefetch
BW utilization >=50%?
MeasureCovP saturated?
Prefetch using CovP
MeasureAccP saturated?
PC Signature | CovP | AccP
0x7ffecca | 1101111101111101 | 1000001000010000
2b
2b
2b
BW Utilization
< 50%
Y
Y
Y
Y
N
N
N
N
Y

## Slide 13: Outline
1. Motivation and Observations
2. Dual Spatial Pattern Prefetcher (DSPatch)
3. Evaluation
4. Conclusion

## Slide 14: Evaluation Methodology
Configuration
  4 x86 cores @ 4 GHz, 4 wide OoO, 224 deep ROB entries
  32KB, 8 way Data and Code L1 caches
    PC-stride prefetcher into Data L1
  256 KB L2 Cache
    BOP, SPP, SMS, DSPatch evaluated @ L2
  2 MB LLC/Core
  Memory Configuration
    Single Core evaluations: 1Ch-DDR4-2133MHz
    Multi Core evaluations: 2Ch-DDR4-2133MHz
Workloads
  Single-Core: 75 workloads spanning Cloud, Client, Server, HPC, Sysmark, SPEC06 and SPEC17
  Multi-Core: 42 high-MPKI homogeneous mixes, 75 heterogeneous mixes

## Slide 15: DSPatch: Single-Core Performance
Chart: Performance Delta over Baseline (%)
| Client | Server | HPC | FSPEC06 | ISPEC06 | FSPEC17 | ISPEC17 | Cloud | SYSmark | GEOMEAN
BOP | 0.24657 | 0.079647 | 0.066882 | 0.21979 | 0.076985 | 0.12938 | 0.2303 | 0.12134 | 0.17731 | 0.1546
SMS | 0.28571 | 0.15068 | 0.14103 | 0.19384 | 0.10966 | 0.13275 | 0.1855 | 0.12346 | 0.19993 | 0.16531
SPP | 0.35968 | 0.17658 | 0.15982 | 0.25087 | 0.14144 | 0.18554 | 0.18215 | 0.10235 | 0.17791 | 0.18633
DSPatch | 0.32005 | 0.16144 | 0.1572 | 0.22308 | 0.15916 | 0.16664 | 0.237 | 0.14665 | 0.20152 | 0.19593
DSPatch+SPP | 0.36742 | 0.189 | 0.20327 | 0.29068 | 0.21909 | 0.19859 | 0.29611 | 0.20294 | 0.28665 | 0.2526
6%
Standalone DSPatch outperforms SPP and SMS by 1% and 3% respectively
DSPatch+SPP outperforms SPP by 6% on average

## Slide 16: DSPatch: Performance Scaling With Bandwidth
Chart: Peak DRAM Bandwidth (GBps)
| 12.8 | 17.064 | 19.2 | 25.6 | 34.128 | 38.4
BOP | 0.12663 | 0.1546 | 0.16501 | 0.18965 | 0.20001 | 0.20307
SMS | 0.13554 | 0.16531 | 0.17708 | 0.20545 | 0.21466 | 0.21883
SPP | 0.16331 | 0.18633 | 0.19606 | 0.21523 | 0.2153 | 0.21768
eBOP+SPP | 0.19666 | 0.23338 | 0.24835 | 0.2763 | 0.29358 | 0.29883
DSPatch+SPP | 0.2044 | 0.2526 | 0.27337 | 0.31324 | 0.33125 | 0.33941
1ch-1600
1ch-2133
1ch-2400
2ch-1600
2ch-2133
2ch-2400
6%
10%
DSPatch performance scales well with increase in memory bandwidth

## Slide 17: DSPatch: Multi-Core Performance
Chart: Performance Delta over Baseline
| Homogeneous | Hetrogeneous | Homogeneous | Hetrogeneous | DRR4-2133 | DDR4-2400
BOP | 0.13488 | 0.10895 | 0.15387 | 0.2002
SMS | 0.16084 | 0.11323 | 0.19207 | 0.24859
SPP | 0.15863 | 0.11981 | 0.18497 | 0.22301
DSPatch+SPP | 0.21761 | 0.19358 | 0.26385 | 0.37347
7.4%
15.1%
DSPatch performs well in bandwidth-constrained multi-core scenarios
5.9%
7.9%

## Slide 18: DSPatch: Hardware Storage
Structure | Size Per Entry (in bytes) | No. of Entries | Size (in KB)
PB | 19.75 B | 64 | 1.23 KB
SPT | 9.5 B | 256 | 2.375 KB
Total |  |  | 3.6 KB
DSPatch is an order of magnitude smaller than SMS
and takes only 2/3rd storage of SPP

## Slide 19: More In Paper
Design optimizations
  Bit-pattern compression (Reduce storage)
  Multiple triggers per 4KB page (Increase coverage)
Results
  Breakdown of coverage and accuracy of DSPatch
  Performance comparison of ISO-sized adjunct prefetchers
  Contribution of Coverage vs. Accuracy biased patterns

## Slide 20: Outline
1. Motivation and Observations
2. Dual Spatial Pattern Prefetcher (DSPatch)
3. Evaluation
4. Conclusion

## Slide 21: Summary
Motivation:
  DRAM bandwidth increases with every generation
  Prefetchers need to adapt to effectively utilize this resource
  Challenge:
  Significantly boost Coverage AND
  Simultaneously optimize for Accuracy
  Dual Spatial Pattern Prefetcher (DSPatch)
  Simultaneously learn two spatial bit-pattern representations of program accesses per page
    Coverage-biased (CovP)
    Accuracy-biased (AccP)
  Predict one of the patterns based on current DRAM bandwidth headroom
6% average speedup over baseline with PC-stride @ L1 and SPP @ L2
10% average speedup when DRAM bandwidth is doubled
Only 3.6 KB of hardware storage
BW
utilization
CovP
AccP

## Slide 22: DSPatch: Dual Spatial pattern prefetcher
Rahul Bera1, Anant V. Nori1, Onur Mutlu2, Sreenivas Subramoney1
1Processor Architecture Research Lab, Intel Labs
2ETH Zürich

## Slide 23: BACKUP

## Slide 24: Observation: Pollution
Chart: LLC Cache Sizes
| 8MB | 4MB | 2MB
NoReuse | 0.9167 | 0.8953 | 0.8366
PrefetchedBeforeUse | 0.0761 | 0.0922 | 0.1338
BadPollution | 0.0072 | 0.0125 | 0.0296

## Slide 25: Coverage and Accuracy
Chart: L2 accesses
| BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | BOP | SMS | SPP | DSPatch+SPP | Client | Server | HPC | FSPEC06 | ISPEC06 | FSPEC17 | ISPEC17 | Cloud | SYSmark | AVG
Sum of covered | 0.33975 | 0.2723 | 0.38832 | 0.4603 | 0.19276 | 0.27464 | 0.25207 | 0.35127 | 0.59207 | 0.58202 | 0.60569 | 0.71615 | 0.62477 | 0.44414 | 0.6177 | 0.72825 | 0.37031 | 0.2229 | 0.24139 | 0.43031 | 0.55847 | 0.44057 | 0.52098 | 0.65319 | 0.45564 | 0.39889 | 0.41234 | 0.55241 | 0.31164 | 0.29687 | 0.23313 | 0.47043 | 0.4394 | 0.41338 | 0.34444 | 0.60203 | 0.43165 | 0.37175 | 0.40179 | 0.55159
Sum of missed | 0.66025 | 0.7277 | 0.61168 | 0.5397 | 0.80724 | 0.72536 | 0.74793 | 0.64873 | 0.40793 | 0.41798 | 0.39431 | 0.28385 | 0.37523 | 0.55586 | 0.3823 | 0.27175 | 0.62969 | 0.7771 | 0.75861 | 0.56969 | 0.44153 | 0.55943 | 0.47902 | 0.34681 | 0.54436 | 0.60111 | 0.58766 | 0.44759 | 0.68836 | 0.70313 | 0.76687 | 0.52957 | 0.5606 | 0.58662 | 0.65556 | 0.39797 | 0.56835 | 0.62825 | 0.59821 | 0.44841
Sum of mispred | 0.17152 | 0.20267 | 0.15389 | 0.18406 | 0.43606 | 0.24512 | 0.34019 | 0.43596 | 0.19224 | 0.087758 | 0.11729 | 0.12371 | 0.14911 | 0.089225 | 0.14683 | 0.16435 | 0.34066 | 0.24166 | 0.2869 | 0.31884 | 0.16479 | 0.13727 | 0.16962 | 0.19614 | 0.35649 | 0.30138 | 0.2777 | 0.36821 | 0.42587 | 0.28213 | 0.29127 | 0.41374 | 0.40853 | 0.27227 | 0.18561 | 0.3644 | 0.29392 | 0.20661 | 0.21881 | 0.28549
Covered
Uncovered
Mispredicted
For DSPatch, every 2% increase in coverage comes at a cost of only 1% increase in misprediction