## Slide 1
DejaVu
Why You Should Write to Your DRAM Rows Twice, Carefully
Haocong Luo
İsmail Emir Yüksel Ataberk Olgun Nisa Bostanci Orhun Ecemiş Abdullah Giray Yaglikci Onur Mutlu

## Slide 2: High-Level Summary
We demonstrate and analyze DejaVu, a new phenomenon in DRAM where data previously written to a DRAM row affects
Tested 112 DDR4 chips from all 3 major manufacturers
Analyze two hypotheses on root causes
Implications on DRAM testing
Vulnerability to read disturbance
Vulnerability to retention failure
Reliability of Processing-Using-DRAM Operations

## Slide 3: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 4: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 5: DRAM Organization
High-Level Illustration of DRAM Cell and DRAM Row
A DRAM cell stores 1 bit of information in a capacitor
DRAM cells are organized into DRAM rows
…
DRAM Row
…
Wordline

## Slide 6: Key DRAM Operation
DRAM cells are accessed at row granularity
To read/write data in DRAM, the memory controller
  Sends an ACT (activate) command to open the DRAM row
  Sends RD/WR commands to read/write data
  Sends a PRE (precharge) command that closes the row
Commands need to respect timing constraints
Timeline of DRAM Commands
Time
tRCD
tRAS
PRE
RD/WR
ACT

## Slide 7: DRAM Robustness Issues (I) – Read Disturbance
Modern DRAM is vulnerable to read disturbance
RowHammer
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
RowPress
Keeping a DRAM row open for a long period of time causes RowPress bitflips in adjacent rows
Row 1
Row 2
Row 3
Row 2
DRAM
Victim Row
Victim Row
Aggressor Row
Row 2
Closed
Row 2
Opened

## Slide 8: DRAM Robustness Issues (I) – Read Disturbance
Modern DRAM is vulnerable to read disturbance
RowHammer
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
RowPress
Keeping a DRAM row open for a long period of time causes RowPress bitflips in adjacent rows
Row 1
Row 2
Row 3
Row 2
DRAM
Victim Row
Victim Row
Aggressor Row
Row 2
Opened

## Slide 9: DRAM Robustness Issues (II) – Retention Failure
The DRAM cell capacitor that stores data is leaky
DRAM needs frequent and periodic refresh to prevent data retention failure bitflips
  One of the main DRAM scaling challenges [Liu+, ISCA’13]
Illustration of DRAM Cell Leakage Paths [Wang+, TC’19]

## Slide 10: Processing-Using-DRAM
The analog operational principles of DRAM can be used to perform computation
Simultaneously activating X rows that share bitlines enables a majority-of-X operation (MAJ-X)
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
Assert three rows’ wordlines
Three rows of DRAM cells perturb bitlines simultaneously
Sense amplifiers sample the output of majority

## Slide 11: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 12: DejaVu - Summary
We demonstrate and analyze DejaVu, a new phenomenon in DRAM where data previously written to a DRAM row affects
Vulnerability to read disturbance
Vulnerability to retention failure
Reliability of Processing-Using-DRAM Operations

## Slide 13: DejaVu – Row Initialization Patterns
Different ways of initializing (writing to) a DRAM row
Baseline
DRAM row is written only once
ACT
PRE
WR X
×128 (Full row write)
OverWrite
DRAM row is first written with opposite data ~X, then overwritten with data X
ACT
PRE
WR ~X
×128 (Full row write)
ACT
PRE
WR X
×128 (Full row write)
then
SameWrite
DRAM row is written with data X twice
ACT
PRE
WR X
×128 (Full row write)
ACT
PRE
WR X
×128 (Full row write)
then
DejaVu Patterns

## Slide 14: DRAM Characterization Methodology (I)
FPGA-based real DDR4 DRAM testing infrastructure
  Developed from DRAM Bender
  Tests Commercial Off-The-Shelf (COTS) DDR4 modules
  Fine-grained control of DRAM commands, timings, and temperature
Photo of an instance of our testing infrastructure

## Slide 15: DRAM Characterization Methodology (I)
Photos of our laboratory for understanding DRAM

## Slide 16: DRAM Characterization Methodology (II)
112 DDR4 DRAM chips tested (14 modules)
  All three major DRAM manufacturers
  Variety of die density and revisions
Details of the tested DDR4 DRAM chips

## Slide 17: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 18: DejaVu on RowHammer (I) - Methodology
Double-sided RowHammer
Key vulnerability metric: ACmin
  The minimum aggressor row activation count to induce at least one bitflip in the victim row
  128 randomly sampled victim rows
  50 experiment repetitions
Illustrations of the double-sided RowHammer access pattern

## Slide 19: DejaVu on RowHammer (II) – Example
Double-sided RowHammer ACmin distribution from one example victim row across 50 test repetitions (0->1 bitflips)

## Slide 20: DejaVu on RowHammer (II) – Example
Double-sided RowHammer ACmin distribution from one example victim row across 50 test repetitions (1->0 bitflips)

## Slide 21: DejaVu on RowHammer (III) – Key Results
Distribution of minimum ACmin (y-axis) across all tested rows and repetitions for each module (x-axis)
DejaVu patterns (OverWrite and SameWrite) normalized to baseline (0->1 bitflips)
Less vulnerable to RowHammer
More vulnerable to RowHammer

## Slide 22: DejaVu on RowHammer (III) – Key Results
Distribution of minimum ACmin (y-axis) across all tested rows and repetitions for each module (x-axis)
DejaVu patterns (OverWrite and SameWrite) normalized to baseline (1->0 bitflips)
Less vulnerable to RowHammer
More vulnerable to RowHammer

## Slide 23: DejaVu on RowHammer (IV) - Summary
Takeaway 1
DejaVu causes consistent changes in RowHammer vulnerability on DRAM chips from all three manufacturers
Takeaway 2
Overwriting the victim row with opposite data makes DRAM more vulnerable to RowHammer
Writing the same data to the victim row twice makes DRAM less vulnerable to RowHammer

## Slide 24: DejaVu on RowPress (I) - Methodology
Double-sided RowPress
Key metric: ACmin at different tAggON values
  The minimum aggressor row activation count to induce at least one bitflip in the victim row
  128 randomly sampled victim rows
  50 experiment repetitions
Illustrations of the double-sided RowPress access pattern

## Slide 25: DejaVu on RowPress (II)
tAggON (ns)
Distribution of minimum ACmin (y-axis) across all tested rows and repetitions from all modules for different tAggON values (x-axis)
DejaVu patterns (OverWrite and SameWrite) normalized to baseline (1->0 bitflips)
Less vulnerable to RowPress
More vulnerable to RowPress

## Slide 26: DejaVu on RowPress (III)
Number of instances (y-axis) DejaVu patterns (OverWrite and SameWrite) can induce RowPress bitflips when the baseline cannot across all tested modules (x-axis)

## Slide 27: DejaVu on RowPress (IV) - Summary
Takeaway 3
DejaVu consistently makes DRAM less (SameWrite) or more (OverWrite) vulnerable to RowPress; similar to RowHammer
Takeaway 4
OverWrite significantly worsens DRAM’s vulnerability to RowPress by inducing bitflips the baseline pattern cannot

## Slide 28: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 29: DejaVu on Retention Failure (I) - Methodology
Retention failure characterization workflow
  Set DRAM temperature to 95°C
  Write “1” to the DRAM row under test using either SameWrite or OverWrite
  Pause DRAM auto-refresh for 4096 ms
  Read back data and check for bitflips
Key metric: Number of retention failure bitflips
  The same 128 tested rows as in read disturbance tests
  50 experiment repetitions

## Slide 30: DejaVu on Retention Failure (II)
Distribution of retention failure bitflip counts per row (y-axis) from 16 example rows (x-axis)
DejaVu patterns (OverWrite and SameWrite)

## Slide 31: DejaVu on Retention Failure (III)
Distribution of the average retention failure bitflip counts (y-axis) from all tested modules (x-axis)
OverWrite normalized to SameWrite
More vulnerable to retention failure
Avg: +10.4%, Max: +36.7%

## Slide 32: DejaVu on Retention Failure (IV) - Takeaway
Takeaway 5
OverWrite significantly worsens DRAM’s vulnerability to retention failures

## Slide 33: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 34: DejaVu on PuD Reliability (I) - Methodology
PuD Operations: 16- and 32-row MAJ-3 operations
Input Data: Random pattern
  Maximize inter-bitline interference during simultaneous multi-row activation
Reliability Metric: Bitline Failure Rate
  Fraction of DRAM cells (bitlines) that produce an incorrect output in at least 1 of 1000 repetitions
Tested Input Rows
  3 different subarrays
  100 row groups from each subarray that can perform simultaneous multi-row activation

## Slide 35: DejaVu on PuD Reliability (II) - Results
Failure rate reduction (y-axis) of DejaVu patterns (OverWrite and SameWrite) for 16- and 32-row MAJ-3 operations
5.8%
30.6%
10.7%
32.7%

## Slide 36: DejaVu on PuD Reliability (III) - Takeaway
Takeaway 6
Both OverWrite and SameWrite significantly improves the reliability of Processing-Using-DRAM operations

## Slide 37: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 38: Hypotheses (I)
Hypothesis 1
DejaVu is caused by the under-restoration of charge in the capacitors of DRAM cells
Hypothesis 2
DejaVu is caused by the change in charge-trap occupancy in the DRAM cell access transistor

## Slide 39: Hypotheses (II)
More investigations on the hypotheses in the paper
  Experiments to (partially) test the charge-under restoration hypothesis
  Analyses of the relationship between the trap occupancy hypothesis and PuD reliability results
Call for Contribution
We call for future works to fundamentally understand DRAM read disturbance and other robustness issues across the stack: from device to circuit and to chip to enable high-performance, safe, secure, and robust DRAM

## Slide 40: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 41: Implications (I)
Characterizing read disturbance threshold
Critical for configuring mitigation techniques
Overwriting data is legal and not uncommon (e.g., page zeroing)
Our results show OverWrite consistently reduces ACmin of RowHammer and RowPress
Implication 1
When characterizing DRAM to find the minimum ACmin
to configure read disturbance mitigation techniques, the victim row should always be initialized with OverWrite

## Slide 42: Implications (II)
Avoiding accidental interference from DejaVu
Without being aware of DejaVu, one may mistakenly attribute the DejaVu induced changes in ACmin to something else
Example case study: Does the data in rows beyond the two immediate neighboring rows of the victim row affects ACmin of RowHammer?
Victim Row
Aggr. Row
Aggr. Row
R
R+1
R-1
Far Row
R-k
Far Row
R+k
Any effect?

## Slide 43: Implications (II) – Cont’d
Avoiding accidental interference from DejaVu
It is natural to use a range-based loop to bulk-initialize many contiguous DRAM rows (i.e., from R-k to R+k), and then initialize row R to test different data patterns
for i in range(R-k, R+k):
write_row(i, data)
write_row(R, data)
for i in range(R-k, R+k):
write_row(i, data)
write_row(R, ~data)
Accidental SameWrite
Accidental OverWrite
Test Pattern A – Same Data
Test Pattern B – Opposite Data
ACmin difference!

## Slide 44: Implications (III) – Cont’d
Test Pseudocode A
Test Pseudocode B
Implication 2
Avoid accidentally comparing SameWrite to OverWrite by always writing the same data to the tested DRAM row twice (i.e., always do SameWrite)

## Slide 45: More in Our Paper
Paper (arXiv)

## Slide 46: Open-source Artifact
Artifact (Github)

## Slide 47: Outline
DRAM Background
Vulnerability to Read Disturbance
DejaVu
Hypotheses on Root Causes
Implications
Conclusion
Vulnerability to Retention Failure
Reliability of Processing-Using-DRAM Operations

## Slide 48: Conclusion
We demonstrate and analyze DejaVu, a new phenomenon in DRAM where data previously written to a DRAM row affects
Vulnerability to read disturbance
Vulnerability to retention failure
Reliability of Processing-Using-DRAM Operations
We call for future works to fundamentally understand DRAM read disturbance and other robustness issues across the stack: from device to circuit and to chip to enable high-performance, safe, secure, and robust DRAM
Call for Contribution

## Slide 49
DejaVu
Why You Should Write to Your DRAM Rows Twice, Carefully
Haocong Luo
İsmail Emir Yüksel Ataberk Olgun Nisa Bostanci Orhun Ecemiş Abdullah Giray Yaglikci Onur Mutlu