## Slide 1: Understanding and Modeling On-Die Error Correction in Modern DRAM: An Experimental Study Using Real Devices
Minesh Patel Jeremie S. Kim
Hasan Hassan Onur Mutlu
Notes: Thank you for the introduction.
Today I’m going to talk about our work: Understanding and Modeling On-Die Error Correction in Modern DRAM.
This work was done by researchers from the SAFARI group at ETH Zurich.
[END]

## Slide 2: Executive Summary
Motivation: Experimentally studying DRAM error mechanisms provides insights for improving performance, energy, and reliability
Problem: on-die error correction (ECC) makes studying errors difficult
  Distorts true error distributions with unstandardized, invisible ECC functions
  Post-correction errors lack the insights we seek from pre-correction errors
Goal: Recover the pre-correction information masked by on-die ECC
Key Contributions:
  Error INference (EIN): statistical inference methodology that:
      Infers the ECC scheme (i.e., type, word length, strength)
      Infers the pre-correction error characteristics beneath the on-die ECC mechanism
      Works without any hardware intrusion or insight into the ECC mechanism
  EINSim: open-source tool for using EIN with real DRAM devices
      Available at: https://github.com/CMU-SAFARI/EINSim
  Experimental demonstration: using 314 LPDDR4 devices
      EIN infers (i) the on-die ECC scheme and (ii) pre-correction error characteristics
  We hope EIN and EINSim enable many valuable studies going forward
Notes: First, I’ll give a high level overview of the talk.
…
[END]

## Slide 3: Presentation Outline
Error Characterization and On-Die ECC
EIN: Error INference
  The Inference Problem
  Formalization
  EIN in Practice: EINSim
Demonstration Using LPDDR4 Devices
Notes: I’ll start out by giving some background on error characterization and on-die ECC
…
[END]

## Slide 4: What is DRAM Error Characterization?
Studying how DRAM behaves
when we deliberately induce bit-flips
Error Mechanisms
& Technology Scaling
Environmental
Effects
+
-
System-Level
Interactions
CPU
Understanding
Exploitable Insights
+
Operating Timing Constraints
Notes: So what exactly is DRAM characterization?
In a nutshell, it's the process of studying how DRAM behaves when we deliberately induce bit-flips.
We might study things like:
operating timings across different values
error mechanisms and how they scale across different technologies
interactions between CPU and the DRAM
even environmental effects such as temperature and voltage
Our hope is that by studying all these different things we can gain some understanding as to how DRAM works and get exploitable insights we can use to improve the system

## Slide 5: How Do We Characterize DRAM?
DRAM Device
Error Distributions
Cell-to-cell Variation
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 0.068349 | 0.61046 | 0.90156 | 0.79788 | 0.5778 | 0.38287 | 0.24372 | 0.15261 | 0.095185 | 0.059531 | 0.037476 | 0.023794
Device Comparisons
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0.5 | 0.44125 | 0.3894 | 0.34364 | 0.30327 | 0.26763 | 0.23618 | 0.20843 | 0.18394 | 0.16233 | 0.14325 | 0.12642 | 0.11157
Y2 | 0.8 | 0.65498 | 0.53626 | 0.43905 | 0.35946 | 0.2943 | 0.24096 | 0.19728 | 0.16152 | 0.13224 | 0.10827 | 0.088643 | 0.072574
Y3 | 1.2 | 0.88898 | 0.65857 | 0.48788 | 0.36143 | 0.26776 | 0.19836 | 0.14695 | 0.10886 | 0.080647 | 0.059744 | 0.04426 | 0.032788
Spatial Distributions
Temporal Distributions
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 1.3222 | 1.6128 | 1.7853 | 1.9085 | 2.0043 | 2.0828 | 2.1492 | 2.2068 | 2.2577 | 2.3032 | 2.3444 | 2.382
Test Routine
Write data
Induce errors
Read data
Record errors
Tester
e.g., CPU, FPGA

## Slide 6: Why Study DRAM Errors?
Errors provide insight into how a DRAM device works
  Error mechanisms are based on physical phenomena
  Patterns in errors can indicate opportunity for improvement
  e.g., Reliably reducing
  conservative operating timings
Performance
  e.g., Efficiently profiling for
  and mitigating errors
Reliability
  e.g., Defending against
  vulnerabilities (e.g., RowHammer)
Security
  e.g., Reducing the cost
  of refresh and other operations
Energy
Characterization-Driven Insights

## Slide 7: Three Key Types of DRAM
No ECC
(Standard)
Data
Tester
Rank-Level ECC
(Server-style)
On-Die ECC
(or Integrated ECC)
Tester
Data
Corrected Data
Tester
ECC Data
Data
ECC Logic
Raw Data Is Unmodified
ECC Modifies Raw Data
ECC
Logic
Raw Data Is Unmodified
ECC Logic
Notes: Chips have internal logic that can correct a limited number of errors

## Slide 8: Three Key Types of DRAM
No ECC
(Standard)
Data
Tester
Rank-Level ECC
(Server-style)
On-Die ECC
(or Integrated ECC)
Tester
Data
Corrected Data
Tester
ECC Data
Data
ECC Logic
Raw Data Is Unmodified
ECC Modifies Raw Data
ECC
Logic
Raw Data Is Unmodified
ECC Logic
Unfortunately, the on-die ECC scheme:
    Cannot be bypassed
    Is unknown and proprietary
    Is completely invisible

## Slide 9: ECC Complicates Error Characterization
Encoder A
Encoder B
Encoder C
Scheme A
Scheme B
Scheme C
1111
Original Data
1 Error
0 Errors
2 Errors
1011
1111
1010
Decoder A (SEC)
Decoder B (SEC)
Decoder C (SEC)
0101110
1011011
0011001
0001100
1111001
0111011

## Slide 10: ECC Complicates Error Characterization
Encoder A
Encoder B
Encoder C
Scheme A
Scheme B
Scheme C
1111
Original Data
1 Error
0 Errors
2 Errors
1011
1111
1010
Decoder A (SEC)
Decoder B (SEC)
Decoder C (SEC)
0101110
1011011
0011001
0001100
1111001
0111011
Observed errors can change
depending on the ECC scheme

## Slide 11: ECC Makes Error Characterization Difficult
ECC causes two key problems:
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 0.068349 | 0.61046 | 0.90156 | 0.79788 | 0.5778 | 0.38287 | 0.24372 | 0.15261 | 0.095185 | 0.059531 | 0.037476 | 0.023794
Pre-ECC Error Distribution
Unknown
ECC Scheme A
Unknown
ECC Scheme B
Unknown
ECC Scheme C
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 0.69407 | 0.47806 | 0.34815 | 0.26596 | 0.21043 | 0.17095 | 0.14176 | 0.11951 | 0.10213 | 0.088278 | 0.077041 | 0.067798
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 2.9447e-10 | 0.009833 | 0.94523 | 1.9947 | 0.85637 | 0.17033 | 0.022738 | 0.0024582 | 0.00023865 | 2.2084e-05 | 2.0192e-06 | 1.8647e-07
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 0.009833 | 0.44445 | 1.0268 | 0.99736 | 0.68291 | 0.39777 | 0.21418 | 0.11111 | 0.056778 | 0.028936 | 0.014814 | 0.0076506
Post-ECC Error Distribution
Based on a physical
DRAM error mechanism
ECC-scheme specific;
Error mechanism influence lost
  Prevents comparing error characteristics between devices
  Obfuscates the well-studied error distributions we expect

## Slide 12: Example: Technology Scaling Study
Goal: study how errors evolve over technology generations
0.0
1.0
0.4
0.2
0.6
0.8
Test Parameter Value
(e.g., temperature, voltage)
Technology Generation
Distribution of
all bit-errors
Consistent with a physical phenomenon
(e.g., process scaling)
EIN
ECC artifact
Post-ECC error distributions
Pre-ECC error distributions

## Slide 13: Example: Technology Scaling Study
Goal: study how errors evolve over technology generations
0.0
1.0
0.4
0.2
0.6
0.8
Distribution of
all bit-errors
Consistent with a physical phenomenon
(e.g., process scaling)
EIN
ECC artifact
Post-ECC error distributions
Pre-ECC error distributions
Our goal:
Recover pre-correction error characteristics
obfuscated by on-die ECC
Notes: As researchers, EIN enables us to study the pre-correction error characteristics rather than being limited to just those observed post-correction. This allows us to propose better solutions from the bottom up rather than building solely upon what the manufacturer has decided to do for a particular device.

## Slide 14: Presentation Outline
Error Characterization and On-Die ECC
EIN: Error INference
  The Inference Problem
  Formalization
  EIN in Practice: EINSim
Demonstration Using LPDDR4 Devices
Notes: I’ll start out by giving some background on error characterization and on-die ECC
…
[END]

## Slide 15: Key Observation
DRAM error mechanisms have
predictable characteristics
that are intrinsic to DRAM technology

## Slide 16: Example: Data-Retention Errors
DRAM encodes data
in leaky capacitors
Leakage rates differ due to process variation
By disabling refresh, we induce data-retention errors
Well-studied and fundamental to DRAM technology
Errors exhibit predictable statistical characteristics
  Exponential bit-error rate (BER) with respect to temperature
  Uniform-random spatial distribution
Necessitates periodic refresh operations
Chart: Time
| 0 | 1 | 2 | 3 | 3.1 | 4 | 5 | 6 | 6.1 | 7 | 8 | 9 | 9.1 | 10 | 11
Y-Values | 4 | 2 | 1 | 1 | 4 | 2 | 1 | 1 | 4 | 2 | 1 | 1 | 4 | 2 | 1
REF

## Slide 17: Inferring the ECC Scheme
Exploit error characteristics to infer the ECC scheme
  Works for any DRAM susceptible to the error mechanism
  Independent of any particular device or manufacturer
Data Store
ECC Encoder
ECC Decoder
CPU
DRAM
Predictable
Inferable
Observable

## Slide 18: Inferring the ECC Scheme
Exploit error characteristics to infer the ECC scheme
  Works for any DRAM susceptible to the error mechanism
  Independent of any particular device or manufacturer
Data Store
ECC Encoder
ECC Decoder
CPU
DRAM
Predictable
Inferable
Observable
EIN’s key idea: use predictable
error characteristics to infer:
the ECC scheme
the pre-correction error rate

## Slide 19: Presentation Outline
Error Characterization and On-Die ECC
EIN: Error INference
  The Inference Problem
  Formalization
  EIN in Practice: EINSim
Demonstration Using LPDDR4 Devices

## Slide 20: Formalizing the Inference Problem
Model the entire DRAM transformation as a function:
Data Store
ECC Scheme
CPU
DRAM
Distribution
of outputs
We want to infer given observed
Distribution
of inputs
ECC Scheme
Error Distribution
Random variables

## Slide 21: Formalizing the Inference Problem
ECC encoding/decoding algorithms
Spatial distribution of errors (e.g., uniform-random)
Probability of each value (i.e., 0x0, 0x1, …)
  is typically defined by the data pattern we write
Data Store
ECC Scheme
CPU
DRAM

## Slide 22: Formalizing the Inference Problem
Unfortunately: is hard to measure
  64-bit → possible values
  Typical 8GiB DRAM only has ~ (<< 264)
  Hard to get a representative sample of even with all 8GiB
Probability that has [] errors
  Easy to experimentally measure: simply count errors
  Meaningful in the context of ECC (e.g., –error correction)
Data Store
ECC Scheme
CPU
DRAM

## Slide 23: Inferring the ECC Scheme
Want the most likely ECC scheme given an experiment
Experiment
error distribution
inputs/outputs
Likelihood
Are these results reasonable?
Prior
How likely is S?
This is a maximum-a-posteriori (MAP) estimation
We provide a rigorous derivation in the paper
  Full optimization objective function
  Extension for inferring error distribution characteristics
Bayes’
Theorem
ECC Scheme

## Slide 24: Error INference (EIN) Methodology
Define experimental inputs
(i.e., data pattern, error mechanism)
Identify candidate ECC Schemes
Compute MAP estimation
1
2
3
4
Run Experiments
Most likely ECC scheme

## Slide 25: Presentation Outline
Error Characterization and On-Die ECC
EIN: Error INference
  The Inference Problem
  Formalization
  EIN in Practice: EINSim
Demonstration Using LPDDR4 Devices

## Slide 26: MAP Estimation in Practice
Observations
(# errors per word)
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
Y-Values | 0 | 0.068349 | 0.61046 | 0.90156 | 0.79788 | 0.5778 | 0.38287 | 0.24372 | 0.15261 | 0.095185 | 0.059531 | 0.037476 | 0.023794
Experiment
Chart: 
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3
A | 0 | 0.068349 | 0.61046 | 0.90156 | 0.79788 | 0.5778 | 0.38287 | 0.24372 | 0.15261 | 0.095185 | 0.059531 | 0.037476 | 0.023794
B | 0 | 0.009833 | 0.44445 | 1.0268 | 0.99736 | 0.68291 | 0.39777 | 0.21418 | 0.11111 | 0.056778 | 0.028936 | 0.014814 | 0.0076506
C | 0 | 0.00012274 | 0.18433 | 1.1196 | 1.3298 | 0.80675 | 0.35566 | 0.1334 | 0.046084 | 0.01531 | 0.0050134 | 0.0016421 | 0.00054276
D | 0 | 2.9447e-10 | 0.009833 | 0.94523 | 1.9947 | 0.85637 | 0.17033 | 0.022738 | 0.0024582 | 0.00023865 | 2.2084e-05 | 2.0192e-06 | 1.8647e-07
Outputs
(# errors per word)
Calculation
Input
(i.e., data pattern,
error distribution)
1
Suspected
ECC Schemes
{A, B, C, D, …}
2
Device to Test
(unknown ECC scheme)
3
Chart: 
| A | B | C | D | …
Series 1 | 0.2 | 0.4 | 0.1 | 0.8
Likelihood per Scheme
4
Hard to calculate
analytically
Monte-Carlo
Simulation
(EINSim)
Most Likely
ECC Scheme

## Slide 27: EINSim: A Tool for Using EIN
Evaluates MAP estimation via Monte-Carlo simulation
  Simulates the life of a dataword through a real experiment
  Configuration knobs to replicate the experimental setup
Flexible and extensible to apply to a wide variety of:
  DRAM devices
  Error mechanisms
  ECC schemes
Open-source C++/Python project
https://github.com/CMU-SAFARI/EINSim
Example datasets provided (same as used in paper)

## Slide 28: EINSim: A Tool for Using EIN
Evaluates MAP estimation via Monte-Carlo simulation
  Simulates the life of a dataword through a real experiment
  Configuration knobs to replicate the experimental setup
Flexible and configurable to apply to a wide variety of:
  DRAM devices
  Error mechanisms
  ECC schemes
Open-source C++/Python project
https://github.com/CMU-SAFARI/EINSim
Example datasets provided (same as used in paper)
Give EINSim a try at:
https://github.com/CMU-SAFARI/EINSim

## Slide 29: Presentation Outline
Error Characterization and On-Die ECC
EIN: Error INference
  The Inference Problem
  Formalization
  EIN in Practice: EINSim
Demonstration Using LPDDR4 Devices

## Slide 30: Methodology
We experimentally test LPDDR4 DRAM devices
  232 with on-die ECC (one major manufacturer)
  82 without on-die ECC (three major manufacturers)
Thermally controlled testing chamber
  55oC - 70oC
  Tolerance of ±1oC
Precise control over the commands sent to DRAM
  Ability to enable/disable self-/auto-refresh
  Control over CAS (i.e., read/write) commands

## Slide 31: Experimental Design
Goal: infer which ECC scheme is used
in real LPDDR4 devices with on-die ECC
Parameter | Experiment | Simulation (EINSim)
ECC Schemes | Unknown | Hamming (32, 64, 128, 256) BCH-2EC (32, 64, 128, 256) BCH-3EC (32, 64, 128, 256) Repetition (3, 5, 7)
Data Pattern | RANDOM | RANDOM, 0xFF
Error Mechanism | Data-Retention | Data-Retention
Word Size | 256 bits | 256 bits

## Slide 32: MAP Estimation Methodology
Assume a uniform prior distribution
  Avoids biasing results towards our preconceptions
  Demonstrates EIN in the worst case
Simulate 106 256-bit words per ECC scheme
Error estimation using bootstrapping (104 samples)

## Slide 33: MAP Estimation Results
BCH(78, 64, 2)
BCH(144, 128, 2)
BCH(274, 256, 2)
Ham(38, 32, 1)
Ham(71, 64, 1)
Ham(136, 128, 1)
Ham(265, 256, 1)
BCH(44, 32, 2)
ECC Schemes
(#code bits, #data bits, #errors correctable)
Most Likely
ECC Scheme
Confidence interval is extremely tight
Lower is
MORE Likely

## Slide 34: MAP Estimation Results
BCH(78, 64, 2)
BCH(144, 128, 2)
BCH(274, 256, 2)
Ham(38, 32, 1)
Ham(71, 64, 1)
Ham(136, 128, 1)
Ham(265, 256, 1)
BCH(44, 32, 2)
ECC Schemes
(#code bits, #data bits, #errors correctable)
Most Likely
ECC Scheme
Less Likely Models
Confidence interval is extremely tight
Lower is
MORE Likely

## Slide 35: MAP Estimation Results
BCH(78, 64, 2)
BCH(144, 128, 2)
BCH(274, 256, 2)
Ham(38, 32, 1)
Ham(71, 64, 1)
Ham(136, 128, 1)
Ham(265, 256, 1)
BCH(44, 32, 2)
ECC Schemes
(#code bits, #data bits, #errors correctable)
Most Likely
ECC Scheme
Less Likely Models
Confidence interval is extremely tight
Lower is
MORE Likely
EIN effectively infers the ECC scheme in LPDDR4 devices with on-die ECC
to be a (128 + 8) Hamming Code
EIN infers the ECC scheme without:
  Visibility into the ECC mechanism
  Disabling ECC
  Tampering with the hardware

## Slide 36: EIN Applies Beyond On-Die ECC
EIN technically applies for any device for which:
  Communication channel protected by ECC
  Can induce uncorrectable errors
  Errors follow predictable statistical characteristics
Flash Memory ECC
NAND
Flash
DRAM Rank-Level ECC
CPU
ECC
Data
Normal
Data

## Slide 37: Other Contributions in our Paper
Two error-characterization studies showing EIN’s value
  EIN enables comparing BERs of the DRAM technology itself
  EIN recovers expected distributions that ECC obfuscates
Using EIN to infer additional information:
  The data pattern written to DRAM
  The pre-correction error characteristics (e.g., pre-ECC BER)
Formal derivation of EIN + discussion of its limitations
Verify uniform-randomly spaced data-retention errors
  Reverse-engineering DRAM design characteristics that affect uniformness (e.g., true-/anti-cell layout)

## Slide 38: Talk & Paper Recap
Motivation: Experimentally studying DRAM error mechanisms provides insights for improving performance, energy, and reliability
Problem: on-die error correction (ECC) makes studying errors difficult
  Distorts true error distributions with unstandardized, invisible ECC functions
  Post-correction errors lack the insights we seek from pre-correction errors
Goal: Recover the pre-correction information masked by on-die ECC
Key Contributions:
  Error INference (EIN): statistical inference methodology that:
      Infers the ECC scheme (i.e., type, word length, strength)
      Infers the pre-correction error characteristics beneath the on-die ECC mechanism
      Works without any hardware intrusion or insight into the ECC mechanism
  EINSim: open-source tool for using EIN with real DRAM devices
      Available at: https://github.com/CMU-SAFARI/EINSim
  Experimental demonstration: using 314 LPDDR4 devices
      EIN infers (i) the on-die ECC scheme and (ii) pre-correction error characteristics
  We hope EIN and EINSim enable many valuable studies going forward

## Slide 39: Understanding and Modeling On-Die Error Correction in Modern DRAM: An Experimental Study Using Real Devices
Minesh Patel Jeremie S. Kim
Hasan Hassan Onur Mutlu

## Slide 40: Backup Slides

## Slide 41: EIN: 3 Concrete Use Cases
Rapid error profiling using statistical distributions
  Use properties of the error mechanisms to model errors
  Use EIN to determine model parameters at runtime
  Replacement for laborious, per-device characterization
Comparison studies (e.g., technology scaling)
  Use EIN to compare pre-correction error rates
  Study + predict industry and future technology trends
Reverse-engineering proprietary ECC schemes
  Applies beyond just DRAM with on-die ECC
  Can be useful for security research
  E.g., vulnerability evaluation, patent infringement, competitive analysis, forensic analysis

## Slide 42: Observed BER Depends on ECC
Assume errors occur independently, uniform-randomly
  Fixed per-bit = “bit error rate” (BER)
BCH(64, 2)
BCH(128, 2)
BCH(256, 2)
Hamming(32, 1)
Hamming(64, 1)
Hamming(128, 1)
Hamming(256, 1)
3-Repetition
None

## Slide 43: A Closer Look at On-Die ECC
Primarily mitigates technology scaling issues [1]
  Transparently mitigates random single-bit errors (e.g., VRT)
  Fully backwards compatible (no changes to DDRx interface)
Unfortunately, has side-effects for error characterization
  Unspecified, black-box implementation
  Obfuscates errors in an ECC-specific manner
Input
(writes)
ECC Encoder
Data Storage
ECC Storage
ECC Decoder
Output
(reads)
DRAM with on-die ECC
[1] “ECC Brings Reliability and Power Efficiency to Mobile Devices,” Micron Technology, Inc, Whitepaper, 2017

## Slide 44: On-Die ECC in Literature
Two types of ECC mentioned
  (128 + 8) Hamming code
  (64 + 7) Hamming code
Paper contains references to both of these

## Slide 45: On-Die ECC Research Challenge
Good for DRAM manufacturers:
  ✓ Transparently improves reliability
  ✓ Decreases power required for data retention
  ✓ Low latency/power overhead
  ✓ No changes to DRAM interface (i.e., backwards compatible)
Bad for researchers studying DRAM errors:
✘ Hides errors in a black-box, device-specific way
✘ Distorts well-understood statistical distributions
✘ Prevents fairly comparing BER of the DRAM itself

## Slide 46: EINSim Functional Description
Simulates the dataflow through a real experiment
  Configuration parameters replicate experimental setup
  Simulate enough words to resolve the output distribution
Error Injector
ECC Encoder
ECC Decoder
Word Generator
Error Checker
Output Distribution
(i.e., )
Input Configuration
(i.e., )
Tester
DRAM

## Slide 47: EINSim Configuration + Features
Error Injector
ECC Encoder
ECC Decoder
Word Generator
Error Checker
Output Distribution
(i.e., )
Input Configuration
(i.e., )
Word Generator | Word length Data Pattern
ECC Encoder, ECC Decoder | ECC code {type, length, strength} code details (e.g., generator polynomial)
Error Injector | Spatial error distribution
Error Checker | Measurement (e.g., #errors per word)
Module | Parameters

## Slide 48: Word Generator
Creates an
  Commonly used data patterns (e.g., 0xFF, RANDOM)
  Effectively sampling the distribution
N may be multiple long
  Useful if we don’t know how are laid out
  Split into according to a configurable mapping
  More details about this in the paper
Error Injector
ECC Encoder
ECC Decoder
Word Generator
Error Checker

## Slide 49: ECC Encoder/Decoder
Error Injector
EINSim implements ECC algorithms
  Currently supports common codes (e.g., Hamming, BCH)
  Modularly designed and easily extensible to others
  Validated by hand + using unit tests (available on GitHub)
Configurable parameters for:
  Number of data bits, correction capability
  Details of implementation (e.g., generator polynomials)
ECC Encoder
ECC Decoder
Word Generator
Error Checker

## Slide 50: Error Injector
Error Injector
Injects errors according to a spatial error distribution
  Configurable parameters depend on particular distribution
  Extensible to many different error distributions
Uniform-random for data-retention errors
  We experimentally validate this using real LPDDR4 devices
  Experiment and analysis discussed in detail in the paper
ECC Encoder
ECC Decoder
Word Generator
Error Checker

## Slide 51: Error Checker
Error Injector
Computes a configurable output distribution
  Corresponds to the experimental measurement we make
  E.g., number of errors per (i.e., )
ECC Encoder
ECC Decoder
Word Generator
Error Checker

## Slide 52: Validating Uniform-Randomness
We model data-retention errors as uniform random
  Well-studied throughout prior work
  Error count per N-bit word follows a binomial distribution
We experimentally validate uniform-randomness
  82 LPDDR4 devices without on-die ECC
  Disable refresh operations for 20s @ 60oC

## Slide 53: Anatomy of a DRAM Bank
DRAM cells can encode data in two ways:
  Data ‘1’ as ‘charged’ -> “True-cell”
  Data ‘1’ as ‘discharged’ -> “Anti-cell”
Retention errors typically “charged” -> “discharged”

## Slide 54: Incidence of “Outlier Rows”
Some rows do not follow the true-/anti-cell layout
Appear to follow typical “remapped row” distributions
  Extra memory rows used for post-manufacturing repair

## Slide 55: MAP Estimation Shown Graphically
Low sample count
Non-uniformities (details in paper)

## Slide 56: Example Error-Characterization Studies
BER vs. refresh rates
  We compare devices with on-die ECC to those without it
  EIN infers the pre-correction BER beneath on-die ECC
  Enables comparing BER of the DRAM technology itself
BER vs. temperature
  On-die ECC distorts the expected exponential relationship
  EIN recovers the obfuscated statistical distribution
We provide two studies to demonstrate EIN’s value
  Measure data-retention error rates
  Have 314 LPDDR4 devices (with + without on-die ECC)

## Slide 57: Finding the “Right” Answer
MAP estimation selects between suspected models
  EIN cannot tell if the MAP estimate is “right”
  “Likelihood” is a relative measure
Techniques for gaining confidence in the answer:
  Using confidence intervals (e.g., statistical bootstrap)
  Testing across many different error conditions
Unlikely that the ECC scheme used is unknown
  ECC is a well-studied area
  Manufacturers are unlikely to a completely unknown code
Typically we may suspect some schemes already
  Academic/industry papers, datasheets, etc.

## Slide 58: Control of Errors
EIN requires knowledge and control of errors
  Understand the spatial distribution of errors
  Be able to induce uncorrectable errors
Not a limitation in practice for DRAM
  Many well-studied easily-controlled error mechanisms exist
    E.g., data retention
    E.g., access-latency reduction (i.e., tRCD, tRP, etc.)
    E.g., RowHammer

## Slide 59: Error Localization
EIN cannot identify bit-exact error locations
  ECC decoding function is lossy (i.e., many-to-one)
  We are unaware of a way to reverse the decoding function
Not a limitation in practice since we can still infer:
  The ECC scheme
  Pre-correction error rates