## Slide 1: FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives
Arash Tavakkol, Mohammad Sadrosadati, Saugata Ghose,
Jeremie S. Kim, Yixin Luo, Yaohua Wang, Nika Mansouri Ghiasi,
Lois Orosa, Juan Gómez-Luna, Onur Mutlu
June 5, 2018

## Slide 2: Executive Summary
Modern solid-state drives (SSDs) use new storage protocols (e.g., NVMe) that eliminate the OS software stack
  I/O requests are now scheduled inside the SSD
  Enables high throughput: millions of IOPS
OS software stack elimination removes existing fairness mechanisms
  We experimentally characterize fairness on four real state-of-the-art SSDs
  Highly unfair slowdowns: large difference across concurrently-running applications
We find and analyze four sources of inter-application interference that lead to slowdowns in state-of-the-art SSDs
FLIN: a new I/O request scheduler for modern SSDs designed to provide both fairness and high performance
  Mitigates all four sources of inter-application interference
  Implemented fully in the SSD controller firmware, uses < 0.06% of DRAM space
  FLIN improves fairness by 70% and performance by 47% compared to a state-of-the-art I/O scheduler

## Slide 3: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 4: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)

## Slide 5: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units

## Slide 6: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host

## Slide 7: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests

## Slide 8: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests
  Flash Channel Controllers (FCCs): sends commands to, transfers data with memory chips in back end

## Slide 9: Conventional Host–Interface Protocols for SSDs
SSDs initially adopted conventional host–interface protocols (e.g., SATA)
  Designed for magnetic hard disk drives
  Maximum of only thousands of IOPS per device
Process 1
Process 2
Process 3
OS Software Stack
SSD Device
Hardware dispatch queue
I/O Scheduler
In-DRAM
I/O Request
Queue

## Slide 10: Host–Interface Protocols in Modern SSDs
Modern SSDs use high-performance host–interface protocols (e.g., NVMe)
  Bypass OS intervention: SSD must perform scheduling
  Take advantage of SSD throughput: enables millions of IOPS per device
OS Software Stack
Hardware dispatch queue
Process 1
Process 2
Process 3
SSD Device
I/O Scheduler
In-DRAM
I/O Request
Queue
Fairness mechanisms in OS software stack are also eliminated
Do modern SSDs need to handle fairness control?

## Slide 11: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 12: Measuring Unfairness in Real, Modern SSDs
We measure fairness using four real state-of-the-art SSDs
  NVMe protocol
  Designed for datacenters
Flow: a series of I/O requests generated by an application
Slowdown = (lower is better)
Unfairness = (lower is better)
Fairness = (higher is better)
shared flow response time
alone flow response time
max slowdown
min slowdown
1
unfairness

## Slide 13: Representative Example: tpcc and tpce
average slowdown of tpce: 2x to 106x across our four real SSDs
tpce
tpcc
very low fairness
SSDs do not provide fairness among concurrently-running flows

## Slide 14: What Causes This Unfairness?
Interference among concurrently-running flows
We perform a detailed study of interference
  MQSim: detailed, open-source modern SSD simulator [FAST 2018] https://github.com/CMU-SAFARI/MQSim
  Run flows that are designed to demonstrate each source of interference
  Detailed experimental characterization results in the paper
We uncover four sources of interference among flows

## Slide 15: Source 1: Different I/O Intensities
The I/O intensity of a flow affects the average queue wait time of flash transactions
Similar to memory scheduling for bandwidth-sensitive threads vs. latency-sensitive threads
The average response time of a low-intensity flow substantially increases due to
interference from a high-intensity flow

## Slide 16: Source 2: Different Access Patterns
Some flows take advantage of chip-level parallelism in back end
Leads to a low queue wait time
Even distribution of transactions in chip-level queues

## Slide 17: Source 2: Different Request Access Patterns
Other flows have access patterns that do not exploit parallelism
Flows with parallelism-friendly access patterns are susceptible to interference from flows whose access patterns do not exploit parallelism

## Slide 18: Source 3: Different Read/Write Ratios
State-of-the-art SSD I/O schedulers prioritize reads over writes
Effect of read prioritization on fairness (vs. first-come, first-serve)
When flows have different read/write ratios, existing schedulers do not effectively provide fairness

## Slide 19: Source 4: Different Garbage Collection Demands
NAND flash memory performs writes out of place
  Erases can only happen on an entire flash block (hundreds of flash pages)
  Pages marked invalid during write
Garbage collection (GC)
  Selects a block with mostly-invalid pages
  Moves any remaining valid pages
  Erases blocks with mostly-invalid pages
High-GC flow: flows with a higher write intensity induce more garbage collection activities
The GC activities of a high-GC flow can
unfairly block flash transactions of a low-GC flow

## Slide 20: Summary: Source of Unfairness in SSDs
Four major sources of unfairness in modern SSDs
  I/O intensity
  Request access patterns
  Read/write ratio
  Garbage collection demands
OUR GOAL
Design an I/O request scheduler for SSDs that (1) provides fairness among flows by mitigating all four sources of interference, and (2) maximizes performance and throughput
Notes: New goal, link to sources

## Slide 21: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 22: FLIN: Flash-Level INterference-aware Scheduler
FLIN is a three-stage I/O request scheduler
  Replaces existing transaction scheduling unit
  Takes in flash transactions, reorders them, sends them to flash channel
Identical throughput to state-of-the-art schedulers
Fully implemented in the SSD controller firmware
  No hardware modifications
  Requires < 0.06% of the DRAM available within the SSD
Notes: Fix animation

## Slide 23: Three Stages of FLIN
Stage 1: Fairness-aware Queue Insertion relieves I/O intensity and access pattern interference
9
8
7
6
5
4
3
2
1
0
From high-intensity flows
From low-intensity flows
Head
Tail

## Slide 24: Three Stages of FLIN
Stage 1: Fairness-aware Queue Insertion relieves I/O intensity and access pattern interference
Stage 2: Priority-aware Queue Arbitration enforces priority levels that are assigned to each flow by the host

## Slide 25: Three Stages of FLIN
Stage 1: Fairness-aware Queue Insertion relieves I/O intensity and access pattern interference
Stage 2: Priority-aware Queue Arbitration enforces priority levels that are assigned to each flow by the host
Stage 3: Wait-balancing Transaction Selection relieves read/write ratio and garbage collection demand interference

## Slide 26: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 27: Evaluation Methodology
MQSim: https://github.com/CMU-SAFARI/MQSim [FAST 2018]
  Protocol: NVMe 1.2 over PCIe
  User capacity: 480GB
  Organization: 8 channels, 2 planes per die, 4096 blocks per plane, 256 pages per block, 8kB page size
40 workloads containing four randomly-selected storage traces
  Each storage trace is collected from real enterprise/datacenter applications: UMass, Microsoft production/enterprise
  Each application classified as low-interference or high-interference

## Slide 28: Two Baseline Schedulers
Sprinkler [Jung+ HPCA 2014] a state-of-the-art device-level high-performance scheduler
Sprinkler+Fairness [Jung+ HPCA 2014, Jun+ NVMSA 2015] we add a state-of-the-art fairness mechanism to Sprinkler that was previously proposed for OS-level I/O scheduling
  Does not have direct information about the internal resources and mechanisms of the SSD
  Does not mitigate all four sources of interference

## Slide 29: FLIN Improves Fairness Over the Baselines
Chart: Fraction of High-Intensity Traces in Workload
| 0.25 | 0.5 | 0.75 | 1
Sprinkler | 0.495 | 0.31 | 0.095 | 0.01
Sprinkler+Fairness | 0.7 | 0.49 | 0.225 | 0.13
FLIN | 0.91 | 0.88 | 0.53 | 0.39
FLIN improves fairness by an average of 70%, by mitigating all four major sources of interference

## Slide 30: FLIN Improves Performance Over the Baselines
Chart: Fraction of High-Intensity Traces in Workload
| 0.25 | 0.5 | 0.75 | 1
Sprinkler | 2.5 | 1.495 | 0.75 | 0.5
Sprinkler+Fairness | 2.8 | 1.9 | 1.2 | 0.7
FLIN | 3.45 | 2.6 | 1.7 | 1.3
FLIN improves performance by an average of 47%, by making use of idle resources in the SSD and improving the performance of low-interference flows

## Slide 31: Other Results in the Paper
Fairness and weighted speedup for each workload
  FLIN improves fairness and performance for all workloads
Maximum slowdown
  Sprinkler/Sprinkler+Fairness: several applications with maximum slowdown over 500x
  FLIN: no flow with a maximum slowdown over 80x
Effect of each stage of FLIN on fairness and performance
Sensitivity study to FLIN and SSD parameters
Effect of write caching

## Slide 32: Background: Modern SSD Design Unfairness Across Multiple Applications in Modern SSDs FLIN: Flash-Level INterference-aware SSD Scheduler Experimental Evaluation Conclusion
Outline

## Slide 33: Conclusion
Modern solid-state drives (SSDs) use new storage protocols (e.g., NVMe) that eliminate the OS software stack
  Enables high throughput: millions of IOPS
  OS software stack elimination removes existing fairness mechanisms
  Highly unfair slowdowns on real state-of-the-art SSDs
FLIN: a new I/O request scheduler for modern SSDs designed to provide both fairness and high performance
  Mitigates all four sources of inter-application interference
    Different I/O intensities
    Different request access patterns
    Different read/write ratios
    Different garbage collection demands
  Implemented fully in the SSD controller firmware, uses < 0.06% of DRAM
  FLIN improves fairness by 70% and performance by 47% compared to a state-of-the-art I/O scheduler (Sprinkler+Fairness)

## Slide 34: FLIN: Enabling Fairness and Enhancing Performance in Modern NVMe Solid State Drives
Arash Tavakkol, Mohammad Sadrosadati, Saugata Ghose,
Jeremie S. Kim, Yixin Luo, Yaohua Wang, Nika Mansouri Ghiasi,
Lois Orosa, Juan Gómez-Luna, Onur Mutlu
June 5, 2018

## Slide 35: Backup Slides

## Slide 36: Executive Summary
Modern NVMe solid-state drives (SSDs) eliminate the OS software stack to improve the performance of storage accesses
  Take advantage of SSD throughput: enables millions of IOPS per device
  The SSD device itself should provide fairness
Modern SSDs focus on providing high performance at the expense of large amounts of unfairness
  We perform experiments on four real state-of-the-art SSDs
  Large difference in the slowdown of concurrently-running flows
We comprehensively analyze the major sources of inter-application interference in state-of-the-art SSDs
  There are four major sources of interference
We propose FLIN, a new device-level I/O scheduler that protects against all sources of unfairness and provides fairness and high performance
  Compared to a state-of-the-art I/O scheduler, FLIN, on average, improves fairness and performance by 70% and 47%, respectively
  Implemented fully within the SSD controller firmware with a modest DRAM cost

## Slide 37: Enabling Higher SSD Performance and Capacity
Solid-state drives (SSDs) are widely used in today’s computer systems
  Data centers
  Enterprise servers
  Consumer devices
I/O demand of both enterprise and consumer applications continues to grow
SSDs are rapidly evolving to deliver improved performance
Host
Host Interface
SATA
NAND Flash
3D XPoint
New NVM

## Slide 38: Defining Slowdown and Fairness for I/O Flows
RTfi: response time of Flow fi
Sfi: slowdown of Flow fi
F: fairness of slowdowns across multiple flows
  0 < F < 1
  Higher F means that system is more fair
WS: weighted speedup

## Slide 39: Host–Interface Protocols in Modern SSDs
Modern SSDs use high-performance host–interface protocols (e.g., NVMe)
  Take advantage of SSD throughput: enables millions of IOPS per device
  Bypass OS intervention: SSD must perform scheduling, ensure fairness
Process 1
Process 2
Process 3
SSD Device
In-DRAM
I/O Request
Queue
Fairness should be provided by the SSD itself. Do modern SSDs provide fairness?

## Slide 40: FTL: Managing the SSD’s Resources
Flash writes can take place only to pages that are erased
  Perform out-of-place updates (i.e., write data to a different, free page), mark old page as invalid
  Update logical-to-physical mapping (makes use of cached mapping table)
  Some time later: garbage collection reclaims invalid physical pages off the critical path of latency

## Slide 41: FTL: Managing the SSD’s Resources
Flash writes can take place only to pages that are erased
  Perform out-of-place updates (i.e., write data to a different, free page), mark old page as invalid
  Update logical-to-physical mapping (makes use of cached mapping table)
  Some time later: garbage collection reclaims invalid physical pages off the critical path of latency
Transaction Scheduling Unit: resolves resource contention

## Slide 42: Motivation
The study experimental results on our four SSDs
  An example of two datacenter workloads running concurrently
tpce on average experiences 2x to 106x
higher slowdown compared to tpcc
SSD-A
SSD-B
SSD-C
SSD-D
tpce
tpcc

## Slide 43: Reason 1: Difference in the I/O Intensities
The I/O intensity of a flow affects the average queue wait time of flash transactions
The queue wait time
highly increases with I/O intensity

## Slide 44: Reason 1: Difference in the I/O Intensities
An experiment to analyze the effect of concurrently executing two flows with different I/O intensities on fairness
  Base flow: low intensity (16 MB/s) and low average chip-level queue length
  Interfering flow: varying I/O intensities from low to very high
Base flow experiences a drastic increase
in the average length of the chip-level queue
The average response time of a low-intensity flow substantially increases due to
interference from a high-intensity flow

## Slide 45: Reason 2: Difference in the Access Pattern
The access pattern of a flow determines how its transactions are distributed across the chip-level queues
The running flow benefits from parallelism in the back end
Leads to a low transaction queue wait time
Even distribution of transactions in chip-level queues

## Slide 46: Reason 2: Difference in the Access Pattern
The access pattern of a flow determines how its transactions are distributed across the chip-level queues
Higher transaction wait time in the chip-level queues
Uneven distribution of flash transactions

## Slide 47: Reason 2: Difference in the Access Pattern
An experiment to analyze the interference between concurrent flows with different access patterns
  Base flow: streaming access pattern (parallelism friendly)
  Interfering flow: mixed streaming and random access pattern
Flows with parallelism-friendly access patterns are susceptible to interference from flows
with access patterns that do not exploit parallelism

## Slide 48: Reason 3: Difference in the Read/Write Ratios
State-of-the-art SSD I/O schedulers tend to prioritize reads over writes
  Reads are 10-40x faster than writes
  Reads are more likely to fall on the critical path of program execution
The effect of read prioritization on fairness
  Compare a first-come first-serve scheduler with a read-prioritized scheduler
Existing scheduling policies are not effective
at providing fairness, when
concurrent flows have different read/write ratios

## Slide 49: Reason 4: Difference in the GC Demands
Garbage collection may block user I/O requests
  Primarily depends on the write intensity of the workload
An experiment with two 100%-write flows with different intensities
  Base flow: low intensity and moderate GC demand
  Interfering flow: different write intensities from low-GC to high-GC
Lower fairness
due to GC execution
Tries to
preempt GC
The GC activities of a high-GC flow can
unfairly block flash transactions of a low-GC flow

## Slide 50: Stage 1: Fairness-Aware Queue Insertion
Relieves the interference that occurs due to the intensity and access pattern of concurrently-running flows
In concurrent execution of two flows
  Flash transactions of one flow experience a higher increase in the chip-level queue wait time
Stage 1 performs reordering of transactions within the chip-level queues to reduce the queue wait
Intensity
Access pattern

## Slide 51: Stage 1: Fairness-Aware Queue Insertion
9
8
7
6
5
4
3
2
1
0
New transaction arrives
1. If source of the new transaction is high-intensity
9
8
7
6
5
4
3
2
1
0
If source of the new transaction is low-intensity
From high-intensity flows
From low-intensity flows
9
8
7
6
5
4
3
2
1
0
2a. Estimate slowdown of each transaction and reorder transactions to improve fairness in low-intensity part
2b. Estimate slowdown of each transaction and reorder transactions to improve fairness in high-intensity part
9
8
7
6
5
4
3
2
1
0
9
8
7
6
5
4
3
2
1
0
Head
Tail
Notes: Simplify to two queues

## Slide 52: Stage 2: Priority-Aware Queue Arbitration
Many host–interface protocols, such as NVMe, allow the host to assign different priority levels to each flow
FLIN maintains a read and a write queue for each priority level at Stage 1
  Totally 2×P read and write queues in DRAM for P priority classes
Stage 2
  Selects one ready read/write transaction from the transactions at the head of the P read/write queues and moves it to Stage 3
  It uses a weighted round-robin policy
An example
Read Slot
0
1
2
To stage 3
Notes: simpler

## Slide 53: Stage 3: Wait-Balancing Transaction Selection
Minimizes interference resulted from the read/write ratios and garbage collection demands of concurrently-running flows
Attempts to distribute stall times evenly across read and write transactions
Stage 3 considers proportional wait time of the transactions
  Reads are still prioritized over writes
  Reads are only prioritized when their proportional wait time is greater than write transaction’s proportional wait time
Smaller for reads
Waiting time before
the transaction is dispatched
to the flash controller
Notes: Fix completely, add estimation logic

## Slide 54: Stage 3: Wait-Balancing Transaction Selection
Read Slot
Write Slot
GC Read Queue
GC Write Queue
1. Estimate proportional wait times for the transactions in the read slot and write slot
2. If the read-slot transaction has a higher proportional wait time, then dispatch it to channel
3. If the write-slot transaction has a higher proportional wait time
3a. If GC queues are not empty then execute some GC requests ahead of write
3b. Dispatch the transaction in the write slot to the FCC
The number of GC activities is estimated
based on 1) relative write intensity, and
2) relative usage of the storage space

## Slide 55: Implementation Overheads and Cost
FLIN can be implemented in the firmware of a modern SSD, and does not require specialized hardware
FLIN has to keep track of
  flow intensities to classify flows into and low-intensity categories,
  slowdowns of individual flash transactions in the queues,
  the average slowdown of each flow, and
  the GC cost estimation data
Our worst-case estimation shows that the DRAM overhead of FLIN would be very modest (< 0.06%)
The maximum throughput of FLIN is identical to the baseline
  All the processings are performed off the critical path of transaction processing

## Slide 56: Methodology: SSD Configuration
MQSim, an open-source, accurate modern SSD simulator: https://github.com/CMU-SAFARI/MQSim [FAST’18]

## Slide 57: Methodology: Workloads
We categorize workloads as low-interference or high-interference
  A workload is high-interference if it keeps all of the flash chips busy for more than 8% of the total execution time
We form workloads using randomly-selected combinations of four low- and high-interference traces
Experiments are done in groups of workloads with 25%, 50%, 75%, and 100% high-intensity workloads

## Slide 58: Experimental Results: Fairness
For workload mixes 25%, 50%, 75%, and 100%, FLIN improves average fairness by
  1.8x, 2.5x, 5.6x, and 54x over Sprinkler, and
  1.3x, 1.6x, 2.4x, and 3.2x over Sprinkler+Fairness
1.0
0.8
0.6
0.4
0.2
0.0
Sprinkler+Fairness improves fairness over Sprinkler
  Due to its inclusion of fairness control
Sprinkler+Fairness does not consider all sources of interference, and therefore has a much lower fairness than FLIN
Notes: Keep heterogeneity
Backup slides – review questions

## Slide 59: Experimental Results: Weighted Speedup
Across the four workload categories, FLIN on average improves the weighted speedup by
  38%, 74%, 132%, 156% over Sprinkler, and
  21%, 32%, 41%, 76% over Sprinkler+Fairness
FLIN’s fairness control mechanism improves the performance of low-interference flows
Weighted-speedup remains low for Sprinkler+Fairness as its throughput control mechanism leaves many resources idle
4
3
2
1
0

## Slide 60: Effect of Different FLIN Stages
The individual stages of FLIN improve both fairness and performance over Sprinkler, as each stage works to reduce some sources of interference
The fairness and performance improvements of Stage 1 are much higher than those of Stage 3
  I/O intensity is the most dominant source of interference
Stage 3 reduces the maximum slowdown by a greater amount than Stage 1
  GC operations can significantly increase the stall time of transactions

## Slide 61: Fairness and Performance of FLIN

## Slide 62: Experimental Results: Maximum Slowdown
Across the four workload categories, FLIN reduces the average maximum slowdown by
  24x, 1400x, 3231x, and 1597x over Sprinkler, and
  2.3x, 5.5x, 12x, and 18x over Sprinkler+Fairness
Across all of the workloads, no flow has a maximum slowdown greater than 80x under FLIN
There are several flows that have maximum slowdowns over 500x with Sprinkler and Sprinkler+Fairness
100000
10000
1000
100
10
1

## Slide 63: Conclusion & Future Work
FLIN is a lightweight transaction scheduler for modern multi-queue SSDs (MQ-SSDs), which provides fairness among concurrently-running flows
FLIN uses a three-stage design to protect against all four major sources of interference that exist in real MQ-SSDs
FLIN effectively improves both fairness and system performance compared to state-of-the-art device-level schedulers
FLIN is implemented fully within the SSD firmware with a very modest DRAM overhead (<0.06%)
Future Work
  Coordinated OS/FLIN mechanisms