## Slide 1: Flash-Cosmos In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira,
Mohammad Sadrosadati, Rakesh Nadig, David Novo,
Juan Gómes Luna, Myungsuk Kim, and Onur Mutlu
Notes: Good afternoon. I am Jisung Park, an Assistant Professor at POSTECH.
Today, I am going to present our work, “Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory.” [Click]

## Slide 2: Talk Outline
Problem, Goals & Key Idea
Background
Flash-Cosmos: Computation with One-Shot Multi-Operand Sensing
Evaluation
Summary
Notes: This is the outline of my talk.
Let me start with the motivation and the problem in this work. [Click]

## Slide 3: Bulk Bitwise Operations
Widely-used computation primitive in data-intensive applications
Bulk
Bitwise
Operations
Databases
Graph Processing
Set Operations
Genome Analysis
Cryptography
Web Search
Hyper-Dimensional
Computing
…
Notes: Bulk bitwise operations are widely-used computation primitive in many important data-intensive applications, such as databases, genome analysis, graph processing, etc. [Click]

## Slide 4: Bulk Bitwise Operations
Widely-used computation primitive in data-intensive applications
Bulk
Bitwise
Operations
Databases
Graph Processing
Set Operations
Genome Analysis
Cryptography
Web Search
Hyper-Dimensional
Computing
…
Problem:
Data movement significantly bottlenecks
performance and energy efficiency
Notes: The problem is that the performance and energy efficiency of bulk bitwise operations can be significantly bottleneck by data movement in conventional systems. [Click]

## Slide 5: Data-Movement Bottleneck
Conventional systems: Outside-storage processing (OSP) that must move the entire data to CPUs/GPUs through the memory hierarchy
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
External I/O bandwidth of storage systems
is the main bottleneck in conventional systems (OSP)
Notes: This is a very high-level overview of computing systems that consist of three main components, compute units, main memory, and storage devices. [Click]
To perform just simple bitwise operations, conventional systems must first read the massive entire data to the compute units throughout the memory hierarch. [Click]
If the target data resides in the storgage device, [Click] the relatively slow storage bandwidth becomes the main bottleneck in conventional systems. [Click]

## Slide 6: Near-Data Processing for Bitwise Operations
Can effectively mitigate data movement by performing simple bitwise operations where the data resides
DRAM-Based
Main Memory
(e.g., Ambit2)
In-Storage
Processing Unit
(e.g., Biscuit4)
NVM-Based
Main Memory
(e.g., Pinatubo3)
SRAM-Based
Cache
(e.g., Compute Cache1)
NAND Flash-Based
Storage
(e.g., ParaBit5)
1Aga+, “Compute Caches," HPCA, 2017
2Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO, 2017
3Li+, “Pinatubo: A Processing-in-Memory Architecture for Bulk Bitwise Operations in Emerging Non-Volatile Memories,” DAC, 2016
4Gu+, “Biscuit: A Framework for Near-Data Processing of Big Data Workloads,” ISCA, 2016
5Gao+, “ParaBit: Processing Parallel Bitwise Operations in NAND Flash Memory Based SSDs,” MICRO, 2021
Near-Data
Processing (NDP)
Notes: Near-Data Processing, or NDP in short, can effectively mitigate the data-movement bottleneck by performing the simple computation where the target data resides. [Click]
Many prior works have proposed various NDP techniques for bulk bitwise operations at different levels in the memory herarchy. [Click]

## Slide 7: Near-Data Processing for Bitwise Operations
Can effectively mitigate data movement by performing simple bitwise operations where the data resides
SRAM-Based
Cache
(e.g., Compute Cache1)
DRAM-Based
Main Memory
(e.g., Ambit2)
NVM-Based
Main Memory
(e.g., Pinatubo3)
In-Storage
Processing Unit
(e.g., Biscuit4)
NAND Flash-Based
Storage
(e.g., ParaBit5)
Our focus:
Large data sets
that do not fit
in main memory
Near-Data
Processing (NDP)
1Aga+, “Compute Caches," HPCA, 2017
2Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO, 2017
3Li+, “Pinatubo: A Processing-in-Memory Architecture for Bulk Bitwise Operations in Emerging Non-Volatile Memories,” DAC, 2016
4Gu+, “Biscuit: A Framework for Near-Data Processing of Big Data Workloads,” ISCA, 2016
5Gao+, “ParaBit: Processing Parallel Bitwise Operations in NAND Flash Memory Based SSDs,” MICRO, 2021
Notes: In this work, we focus on in-storage and in-flash processing which are highly effective when the target data set does not fit into main memory. [Click]

## Slide 8: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Notes: In-storage processing leverages cute units inside the storage devices, [Clompick] such as …

## Slide 9: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
In-storage
processing
…
…
…
Notes: Such as embedded core or FPGA to perform computation inside the storage [Click] and sends …

## Slide 10: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
In-storage
processing
Results only
ISP can mitigate data movement overhead
by reducing SSD-external data movement
…
…
…
Notes: Sends only the computation results. [Click]
This way, in-storage processing can significatnly mitigate the data movement by reducing external I/Os between the host and the storage device. [Click]

## Slide 11: In-Storage Processing (ISP)
Uses in-storage compute units (embedded cores or FPGA) to send only the computation results
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Results only
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
In-storage
processing
SSD internal I/O bandwidth: ~ 10 GB/s
…
…
…
SSD-internal bandwidth
becomes the new bottleneck in ISP
Notes: However, in-storage processing also needs to read the massive data from underlying NAND flash chips, [Click] and SSD internal bandwidth is not that higher than the external bandwidth even in high-end NAND flash-based SSDs. [Click]
As a result, SSD internal I/Os become the new bottlenck in in-storage processing. [Click]

## Slide 12: In-Flash Processing (IFP)
Performs computation inside NAND flash chips
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Results only
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
SSD internal I/O bandwidth: ~ 10 GB/s
In-flash processing
…
…
…
Notes: If we can perform computation inside NAND flash chips, [Click] it can reduce …

## Slide 13: In-Flash Processing (IFP)
Performs computation inside NAND flash chips
Main
Memory
(DRAM)
CPU/GPU
$ (SRAM)
Storage
(NAND Flash-Based SSD)
Memory bandwidth: ~ 40 GB/s
Storage I/O bandwidth: ~ 8 GB/s
Results only
IFP fundamentally mitigates data movement
In-flash processing
NAND
Chip#1
NAND
Chip#4
NAND
Chip#31
NAND
Chip#32
In-Storage
Compute
Units
Results only
SSD internal I/O bandwidth: ~ 10 GB/s
…
…
…
Notes: It can reduce the internal data movement within the SSD by sending only the results to the flash controller and the host, [Click] thereby fundamentally mitigating the data movement from the storage device. [Click]

## Slide 14: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page#1
Page#2
Page#3
…
Page#32
Page Buffer
Bitlines (BLs)
Notes: To our knowledge, there is only one recent work for in-flash bulk bitwise operations, called ParaBit, which enables in-flash bulk bitwise operations by intelligently controlling the latch circuit of the page buffer in NAND flash chips. [Click]
This figure shows a high-level organization of a NANd flash chip that consists of a large number of pages to persistantly store data and the page buffer to temporalily store the data to read or writes [Click]

## Slide 15: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Bitlines (BLs)
Notes: Suppose that we want to perform bitwise AND operations on these thirty two operands, each of which is stored in a single page. [Click]

## Slide 16: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Operand O1
Bitlines (BLs)
Operand O1
Sensing
Notes: Then the parabit reads the operands sequentially, [Click] while accumulating …

## Slide 17: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Operand O1
Bitlines (BLs)
O1 & O2
Operand O2
Sensing
Notes: Accumulating the results of bitwise AND operation into the page buffer, [Click] by intelligently …

## Slide 18: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
…
Operand O32
Operand O1
Bitlines (BLs)
O1 & O2
Operand O3
O1 & O2 & O3
Sensing
Notes: By intelligently controlling the latching circuit of in the page buffer. [Click]

## Slide 19: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
…
Operand O1
Bitlines (BLs)
O1 & O2
O1 & O2 & O3 & …
Operand O32
Result only
O1 & O2 & O3 & … & O32
Sensing
Notes: After that, [Click] ParaBit transfers only the computation results out of the chip, [Click] which significantly …

## Slide 20: State-of-the-Art IFP for Bulk Bitwise Operations
ParaBit [Gao+, MICRO 2021]
  Performs bulk bitwise operations inside NAND flash chips by intelligently controlling the latching circuit of the page buffer
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
…
Operand O1
Bitlines (BLs)
O1 & O2
O1 & O2 & O3 & …
Operand O32
O1 & O2 & O3 & … & O32
Sensing
Result only
ParaBit significantly reduces data movement
out of NAND flash chips
Serial sensing operations
(e.g., 32 sensing operations for 32-operand AND)
bottleneck performance and energy in ParaBit
Notes: Which significantly reduces the data movement out of NAND flash chips. [Click]
However, when there are many operands to compute, the serial sensing operations for every operand become the new bottleneck in the state-of-the-art in-flash processing. [Click]

## Slide 21: State-of-the-Art IFP for Bulk Bitwise Operations
Limitations of ParaBit [Gao+, MICRO 2021]
  Serial sensing operations become the new bottleneck
  Erroneous computation results due to the high raw bit-error rate of NAND flash memory
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Bitlines (BLs)
Bit Error
Notes: Another issue is realiability, which is a general problem in in-flash processing. [Click]
It is well known that NAND flash memory is highly error prone and it is hard to leverage widely-used error-correcting codes in in-flash processing, because error correction is performed outside NAND flash chips, at the flash controller. [Click]

## Slide 22: State-of-the-Art IFP for Bulk Bitwise Operations
Limitations of ParaBit [Gao+, MICRO 2021]
  Serial sensing operations become the new bottleneck
  Erroneous computation results due to the high raw bit-error rate of NAND flash memory
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Operand O1
Bitlines (BLs)
Operand O1
Bit Error
Sensing
Notes: So, performing in-flash bulk bitwise operations would accumulate the raw bit errors of each operand into the results,

## Slide 23: State-of-the-Art IFP for Bulk Bitwise Operations
Limitations of ParaBit [Gao+, MICRO 2021]
  Serial sensing operations become the new bottleneck
  Erroneous computation results due to the high raw bit-error rate of NAND flash memory
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Operand O1
Bitlines (BLs)
O1 & O2
Operand O2
Sensing
Bit Error
Notes: So, performing in-flash bulk bitwise operations would accumulate the raw bit errors of each operand into the results,

## Slide 24: State-of-the-Art IFP for Bulk Bitwise Operations
Limitations of ParaBit [Gao+, MICRO 2021]
  Serial sensing operations become the new bottleneck
  Erroneous computation results due to the high raw bit-error rate of NAND flash memory
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
…
Operand O32
Operand O1
Bitlines (BLs)
O1 & O2
Operand O3
O1 & O2 & O3
Sensing
Bit Error
Notes: So, performing in-flash bulk bitwise operations would accumulate the raw bit errors of each operand into the results,

## Slide 25: State-of-the-Art IFP for Bulk Bitwise Operations
Limitations of ParaBit [Gao+, MICRO 2021]
  Serial sensing operations become the new bottleneck
  Erroneous computation results due to the high raw bit-error rate of NAND flash memory
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
…
Operand O1
Bitlines (BLs)
O1 & O2
Operand O32
O1 & O2 & O3 & …
O1 & O2 & O3 & … & O32
Sensing
Bit Error
Notes: So, performing in-flash bulk bitwise operations would accumulate the raw bit errors of each operand into the results, which limits the applicability of in-flash processing only to highly error-tolerant applications [Click]

## Slide 26: Our Goals
Address the new bottleneck of IFP
(serial sensing of operands)
Make IFP reliable
(provide accurate computation results)
Notes: So, our goal in this work is to address the new bottleneck of the state-of-the-art in-flash processing, [Click] while providing accurate computation results without errors. [Click]

## Slide 27: Our Proposal: Flash-Cosmos
Flash-Cosmos enables
  Computation on multiple operands with a single sensing operation
  Accurate computation results by eliminating raw bit errors in stored data
NAND Flash Chip
Page Buffer
Operand O1
Operand O2
Operand O3
…
Operand O32
Bitlines (BLs)
Operand O32
…
Operand O3
Operand O2
Operand O1
O1 & O2 & O3 & … & O32
Simultaneous sensing
Notes: At a very high level, Flash-Cosmos enables [Click] computation while sensing multiple operands at once and accurate computation results by zeroing raw bit errors in stored data. [Click]

## Slide 28: Talk Outline
Problem, Goals & Key Idea
Background
Flash-Cosmos: Computation with One-Shot Multi-Operand Sensing
Evaluation
Summary
Notes: Next, let me provide a brief background that is necessary to understand our key ideas. [Click]

## Slide 29: NAND Flash Basics: A Flash Cell
A flash cell stores data by adjusting the amount of charge in the cell
Erased Cell
(Low Charge Level)
1
Programmed Cell
(High Charge Level)
0
Activation
Operates as a resistor
Operates as an open switch
Notes: A flash cell stores data by adjusting the amount of charge in the cell. [Click]
A cell is considered to store bit data ‘1’ if its charge level is low, whereas it is considered to store ‘0’ if its charge level is high. [Click]
When activating a cell, a low-charge cell operates as a resistance, while a high-charge cell operates as as open switch. [Click]

## Slide 30: NAND Flash Basics: A NAND String
A set of flash cells are serially connected, forming a NAND string
1
0
0
1
0
Bitline (BL)
…
NAND String
Notes: A set of flash cells are serially connected, forming a NAND string, [Click] and to read …

## Slide 31: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Notes: To read only the target cell from a NAND string, NAND flash memory makes all non-target cells in the string operate as a resistance regardless of stored data. [Click]

## Slide 32: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
Bitline (BL)
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
Notes: If the cell stores ‘1’, it operates as a resistance, [Click] so the bitline current …

## Slide 33: NAND Flash Basics: Read Mechanism
NAND flash memory reads data by checking the bitline current
1
0
0
1
0
BLi
Non-Target Cells:
Operate as resistors regardless of stored data
…
NAND String
Target Cells:
Operate as resistors (1) or open switches (0)
0
1
1
0
1
BLj
…
Reads as ‘1’
if BL current
flows
Reads as ‘0’
if BL current
cannot flow
Notes: So the bitline current can flow through the NAND string, which reads as ‘1’ [Click]
If the cell stores ‘0’, [Click] the cell blocks the bitline current, which reads as ‘0’. [Click]

## Slide 34: NAND Flash Basics: A NAND Flash Block
NAND strings connected to different bitlines comprise a block
BL1
BL2
BL3
BL4
BL5
1
0
0
1
0
BLN
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
1
0
0
1
0
…
…
…
…
…
…
WL1
WL2
WL3
WL4
WLM
Block
A single wordline (WL) controls a large number of flash cells: High bit-level parallelism
Notes: There are a large number of bitlines in NAND flash memory, and NAND strings at the same vertical position comprise a NAND flash block. [Click]
A single wordline controls all the flash cells at the same vertical position, which enables the high bit-level parallelism of NAND flash memory [Click]

## Slide 35: NAND Flash Basics: Block Organization
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Notes: And more than a thounsand blocks share the same bitlines within the chip. [Click]

## Slide 36: Similarity to Digital Logic Gates
A large number of blocks share the same bitlines
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Cells in the same block are connected serially: Similar to digital AND
A
B
A•B
2-input AND
Notes: Our key observation is that NAND flash memory has similar organization to digital AND logic, as multiple cells are serially connected to the bitline, [Click] and

## Slide 37: Similarity to Digital Logic Gates
A large number of blocks share the same bitlines.
BL1
BL2
BL3
BL4
BL5
BLN
…
…
…
…
Block2
…
…
…
…
…
…
…
…
…
BlockK
…
…
…
…
…
…
…
…
…
Block1
…
…
…
…
…
…
…
…
…
…
…
Cells in the same block are connected serially: Similar to digital AND
A
B
A•B
2-input AND
Cells in different blocks
are connected in parallel: Similar to digital OR
2-input OR
A
B
A+B
Notes: It also similar to digital OR logic, in that multiple NAND strings are connected to the bitline in parallel. [Click]

## Slide 38: Talk Outline
Problem, Goals & Key Idea
Background
Flash-Cosmos: Computation with One-Shot Multi-Operand Sensing
Evaluation
Summary
Notes: Let’s dive into the key ideas of Flash-Cosmos. [Click]

## Slide 39: Key Ideas
Multi-Wordline Sensing (MWS)
to enable in-flash bulk bitwise operations via a single sensing operation
Enhanced SLC-Mode Programming (ESP)
to eliminate raw bit errors in stored data
(and thus in computation results)
Notes: We introduce two techniques, Multi-Wordline Sensing, or MWS in short, that enables in-flash bulk bitwise operations via a single sensing operation, [Click] and Enhanced SLC-Mode Programming, or ESP in short, to achieve zero raw bit errors in stored data and thus no errors in computation results. [Click]

## Slide 40: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Notes: The key observation is that, if we simultaneously activate multiple wordlines within a block, which we call intra-block MWS, it results in the bitwise AND of stored data in the wordlines. [Click]

## Slide 41: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Blocki
Non-Target Cells:
Operate
as resistors
Notes: As explained all the non-target cell would operate as a resistance, [Click] while …

## Slide 42: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cells:
Operate
as resistors
Target Cells:
Operate
as resistors (1) or open switches (0)
0
0
0
1
Result:
Notes: Target cells operate as either a resistance or an open switch depending the stored data. [Click]
In this example, only Bitline 4 can conduct flow, as the other bitlines have at least one cell that operates as an open switch. [Click]

## Slide 43: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Non-Target Cell:
Operate
as a resistance
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Notes: So, the sensing result would be ‘1’ only when all the target cells store bit data ‘1’, which is equivalent to the bitwise AND of all the target cells. [Click]

## Slide 44: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
Notes: This property also holds [Click] when we activate more than two wordlines at the same time, [Click], for example, …

## Slide 45: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
0
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
0
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Notes: The bitline current cannot flow through Bitline 4 any longer, as it has a cell that stores ‘0’ and blocks the bitline current. [Click]

## Slide 46: Multi-Wordline Sensing (MWS): Bitwise AND
Intra-Block MWS: Simultaneously activates multiple WLs in the same block  Bitwise AND of the stored data in the WLs
BL1
BL2
BL3
BL4
0
0
1
0
…
0
1
0
0
…
1
0
1
1
…
1
1
1
1
…
…
…
…
…
WL1
WL2
WL3
WL4
Target Cell:
Operate
as a resistance (1) or an open switch (0)
0
0
0
1
Result:
A bitline reads as ‘1’ only when all the target cells store ‘1’
 Equivalent to the bitwise AND of all the target cells
Flash-Cosmos (Intra-Block MWS) enables
bitwise AND of multiple pages in the same block
via a single sensing operation
Notes: This way, intra-block MWS enables bitwise AND operation on any pages in the same block via a single sensing operation. [Click]

## Slide 47: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
1
1
0
0
…
WLy in Blocki
…
…
…
…
Notes: Flash-Cosmos also enables bitwise OR operations by simultaneously activating multiple wordlines in different blocks, which we call inter-block MWS. [Click]

## Slide 48: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
Notes: In this example, only Bitline 4 cannot conduct current, as both the target NAND string have a cell that operates as an open switch. [Click]

## Slide 49: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
0
Result:
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
Notes: It means that the sensing result would read as ‘0’ only when all the target cells store bit data ‘0’, which is equivalent to the bitwise OR of all the target cells. [Click]

## Slide 50: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Notes: Like intra-block MWS, [Click] this property holds when we activate more than two wordlines in different blocks at the same time, [Click], as we can see …

## Slide 51: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
A bitline reads as ‘0’ only when all the target cells store ‘0’
 Equivalent to the bitwise OR of all the target cells
Notes: As we can see the current can flow through Bitline 4 as well, since there is a cell that operates as a resistance. [Click]

## Slide 52: Multi-Wordline Sensing (MWS): Bitwise OR
Inter-Block MWS: Simultaneously activates multiple WLs in different blocks  Bitwise OR of the stored data in the WLs
BL1
BL2
BL3
BL4
…
…
…
…
1
0
1
0
…
WLx in Block1
…
…
…
…
1
1
0
0
…
WLy in Blocki
1
1
1
1
Result:
1
0
0
1
…
WLz in Blockj
Flash-Cosmos (Inter-Block MWS) enables
bitwise OR of multiple pages in different blocks
via a single sensing operation
Notes: This way, inter-block MWS enables bitwise OR operations on any pages in different blocks via only a single sensing operation. [Click]

## Slide 53: Other Types of Bitwise Operations
Flash-Cosmos also enables other types of bitwise operations (NOT/NAND/NOR/XOR/XNOR)
leveraging existing features of NAND flash memory
https://arxiv.org/abs/2209.05566.pdf

## Slide 54: Key Ideas
Multi-Wordline Sensing (MWS)
to enable in-flash bulk bitwise operations via a single sensing operation
Enhanced SLC-Mode Programming (ESP)
to eliminate raw bit errors in stored data
(and thus in computation results)
Notes: Now let’s dive into the key ideas of Enhanced SLC-Mode Programming [Click] that elminiates …

## Slide 55: Enhanced SLC-Mode Programming (ESP)
Goal: eliminate raw bit errors in stored data (and computation results)
Key ideas
  Programs only a single bit per cell (SLC-mode programming)
    Trades storage density for reliable computation
  Performs more precise programming of the cells
    Trades programming latency for reliable computaion
Maximizes the reliability margin
between the different states of flash cells
Notes: Eliminates raw bit errors in stored data. [Click]
The key idea is to program only a single bit per cell for the target data of computation, meaning that ESP trades storage density, [Click] and use more precise program-voltage control, meaning that it also trades program latency, [Click] to maximize the reliability margin between the program and erased states of flash cells. [Click]

## Slide 56: Enhanced SLC-Mode Programming (ESP)
To eliminate raw bit errors in stored data (and computation results)
Key ideas
  Programs only a single bit per cell (SLC-mode programming)
    Trades storage density for reliable computation
  More precise program-voltage control
    Trades programming latency for reliable computaion
Maximizes the reliability margin
between the different states of flash cells
Flash-Cosmos (ESP) enables
reliable in-flash computation
by trading storage density & programming latency
Storage & latency overheads affect
only data used in in-flash computation
Notes: So, ESP enables reliable in-flash computation by trading storage density and program performance, [Click] but the overheads occur only for the target data of computation. [Click]

## Slide 57: Talk Outline
Problem, Goals & Key Idea
Background
Flash-Cosmos: Computation with One-Shot Multi-Operand Sensing
Evaluation
Summary
Notes: We evaluate Flash-Cosmos in two ways. [Click]

## Slide 58: Evaluation Methodology
Real-device characterization
  To validate the feasibility and reliability of Flash-Cosmos
  Using 160 48-WL-layer 3D Triple-Level Cell NAND flash chips
    3,686,400 tested wordlines
  Under worst-case operating conditions
    Under a 1-year retention time at 10K P/E cycles
    Worst-case data patterns
System-level evaluation
  Using the state-of-the-art SSD simulator (MQSim [Tavakkol+, FAST’18])
  Three real-world applications
    Bitmap Indices (BMI): Bitwise AND of up to ~1,000 operands
    Image Segmentation (IMS): Bitwise AND of 3 operands
    K-clique Star Listing (KCS): Bitwise OR of up to 32 operands
  Baselines
    Outside-Storage Processing (OSP): A multi-core CPU (Intel i7-11700K)
    In-Storage Processing (ISP): An in-storage hardware accelerator
    ParaBit [Gao+, MICRO’21]: State-of-the-art in-flash processing mechanism
Notes: First, we conducted rigorous real-device characterization to validate the feasibility and reliability of Flash-Cosmos, [Click] using 160 3D NAND flash chips, [Click] considering the worst-case operation conditions. [Click]
We also performed system-level evaluation using the state-of-the-art SSD simulator, [Click] for three real-world applications that perform bulk bitwise operations on different numbers of operands. [Click]
We compared Flash-Cosmos against three baselines, a conventional system that uses a multi-core CPU, an in-storage processing system with an in-storage hardware accelerator, and a system that adopts the state-of-the-art in-flash processing mechanism to perform bulk bitwise operations. [Click]

## Slide 59: Results: Real-Device Characterization
Both intra- and inter-block MWS operations
require no changes to the cell array
of commodity NAND flash chips
Both MWS operations can activate multiple WLs
(intra: up to 48, inter: up to 4) at the same time
with small increase in sensing latency (< 10%)
ESP significantly improves
the reliability of computation results
(no observed bit error in the tested flash cells)
Notes: Through our real-device characterization, we demnostrated that both MWS operations are possible without requiring any change ot the cell array of commodity NAND flash chips, [Click] and they can reliably activate multiple wordlines at the same time without significant increase in sensing latency. [Click]
We also observed no errors in the tested cells when we program data using ESP, which shows that Flash-Cosmos enables reliable in-flash bulk bitwise operations. [Click]

## Slide 60: Results: Performance & Energy
Speedup over OSP
Chart: 
| BMI | IMS | KCS | AVG
 | 1.3181 | 1.1935 | 1.3007 | 1.2794
 | 14.1649 | 2.9997 | 12.8867 | 9.2742
 | 198.4035 | 2.9998 | 25.8962 | 32.4204
ISP
ParaBit
Flash-Cosmos
Flash-Cosmos provides significant performance & energy benefits over all the baselines
The larger the number of operands,
the higher the performance & energy benefits
Chart: 
| BMI | IMS | KCS | AVG
ISP | 8.2558 | 5.4514 | 7.4777 | 7.1709
ParaBit | 49.449 | 8.7761 | 38.1762 | 29.1277
Flash-Cosmos | 582.8533 | 8.9811 | 76.5954 | 95.9386
Energy benefit over OSP
150×
14×
2.5×
20×
2×
70×
12×
1.6×
10×
2×
25×
3.5×
3.3×
13.4×
Notes: As system-level evaluation, [Click] we evaluate the speedup and [Click] energy benefit over the conventional system. [Click]
We observe that Flash-Cosmos provides significant performance and energy benefits over all the baselines, including the state-of-the-art in-flash bulk bitwise operation technique, [Click] and the larger the number of operands for bulk bitwise operations, the higher the performance and energy benefits that Flash-Cosmos can achieve over other computing platforms. [Click]

## Slide 61: More in the Paper
Support for other types of bitwise operations
  NOT/NAND/NOR/XOR/XNOR
More detailed real-device characterization results
Optimizations to improve bitwise operation performance
Flash-Cosmos command interface
System support
Overhead analysis

## Slide 62: More in the Paper
https://arxiv.org/abs/2209.05566.pdf

## Slide 63: Summary: Flash-Cosmos
The first work that enables in-flash multi-operand bulk bitwise operations with a single sensing operation and high reliability
Improves performance by 32x/25x/3.5x over OSP/ISP/ParaBit
Improves energy efficiency by 95x/13.4x/3.3x over OSP/ISP/ParaBit
$
Low-cost & requires no changes to flash cell arrays

## Slide 64: Flash-Cosmos In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory
Jisung Park, Roknoddin Azizi, Geraldo F. Oliveira,
Mohammad Sadrosadati, Rakesh Nadig, David Novo,
Juan Gómes Luna, Myungsuk Kim, and Onur Mutlu