## Slide 1
Jawad Haj-Yahya1 Mohammed Alser1 Jeremie S. Kim1 Lois Orosa1 Efraim Rotem2
Avi Mendelson3,4 Anupam Chattopadhyay 4 Onur Mutlu1
FlexWatts: A Power- and Workload-Aware Hybrid Power Delivery Network for
Energy-Efficient Microprocessors
1
1
2
3
4
MICRO 2020, session 6B Mobile & Embedded Architectures
Wednesday, October 21, 2020
Notes: My name is Jawad Haj-Yahya and I will present our work FlexWatts [END]

## Slide 2: The Power Delivery Network (PDN) Debate
2017
2013
2015
2019
https://semiengineering.com/power-delivery-affecting-performance-at-7nm/
Intel Haswell Uses IVR PDN (FIVR)
Intel Skylake Uses MBVR PDN
AMD Ryzen Uses LDO PDN
Intel Icelake Uses IVR PDN (FIVR)
Notes: In recent years there is a hot debate in industry and academia on power delivery networks. [CLICK]
PDN issues are becoming even worse as process technology scales down [END]

## Slide 3: Executive Summary
Problem: Client processors typically use one of three commonly-used power delivery network (PDN) architectures: 1) MBVR, 2) IVR, and 3) LDO. The energy-efficiency of each of these PDNs varies with the processor power and workload characteristics.
Goal: Provide high energy-efficiency and high performance PDN architecture by leveraging the advantages of each one of the three PDN architectures across the processor’s wide range of power consumption and workloads.
Mechanism: FlexWatts, a new hybrid adaptive PDN for client processors that introduces
  New hybrid voltage regulators (VRs) that are allocated for processor domains with a wide power consumption range (e.g., CPU cores and graphics engines) that dynamically switch between two modes: IVR-Mode and LDO-Mode.
  Static allocation of off-chip VRs, which have high energy-efficiency for low and narrow power ranges, for the rest of the domains (e.g., IO domain).
  A novel prediction algorithm that switches the hybrid PDN to the mode (IVR-Mode/LDO-Mode) that is the most beneficial based on processor power and workload characteristics.
Evaluation: We evaluate FlexWatts using our new architectural PDN model (PDNspot):
  Improves the average performance of the SPEC CPU2006 and 3DMark06 workloads by 22% and 25%, respectively, for 4W thermal design power (TDP) system.
  Reduces the average power consumption of video playback workload by 11% across all tested TDPs (4W-50W).
https://github.com/CMU-SAFARI/PDNspot
Notes: First, I will give a high-level overview of the talk [CLICK]
Client processors typically use one of three commonly-used power delivery network architectures: 1) Motherboard voltage regulators, 2) Integrated voltage regulators , and 3) Low dropout voltage regulators. The energy-efficiency of each of these PDNs varies with the processor power and workload characteristics. [CLICK]
Our goals is to provide high energy-efficiency and high performance PDN architecture by leveraging the advantages of each one of the three PDN architectures across the processor’s wide range of power consumption and workloads. [CLICK]
To this end we propose FlexWatts, a new hybrid adaptive PDN for client processors that introduces three mechanisms [CLICK]
First, New hybrid voltage regulators that are allocated for processor domains with a wide power consumption range that dynamically switches between two modes: IVR-Mode and LDO-Mode. [CLICK]
Secondly, Static allocation of off-chip VRs, which have high energy-efficiency for low and narrow power ranges, for the rest of the domains. [CLICK]
And finally, A novel prediction algorithm that switches the hybrid PDN to the mode that is the most beneficial based on processor power and workload characteristics. [CLICK]
We evaluate FlexWatts using our new architectural PDN model, PDNspot [CLICK]
FlexWatts Improves the average performance of the SPEC CPU2006 and 3DMark workloads by 22% and 25%, respectively, for 4W thermal design power system. [CLICK]
and FlexWatts Reduces the average power consumption of video playback workload by 11% across all tested TDPs
[END]

## Slide 4: Presentation Outline
Overview of Client Processor PDN Architectures
Motivation and Goal
FlexWatts
  Hybrid Adaptive PDN
  Voltage Noise-Free Mode-Switching
  Runtime Mode Prediction Algorithm
Evaluation
Conclusion
Notes: Here is the outline for the talk today
[END]

## Slide 5: Presentation Outline
Overview of Client Processor PDN Architectures
Motivation and Goal
FlexWatts
  Hybrid Adaptive PDN
  Voltage Noise-Free Mode-Switching
  Runtime Mode Prediction Algorithm
Evaluation
Conclusion
Notes: I will begin with a brief overview on Client Processor PDN Architectures [END]

## Slide 6: Overview of Modern Client PDN Architectures
The Power Delivery Network (PDN) is the electrical system that provides supply voltage to the processor’s domains
  A PDN consists of 1) a power supply, 2) voltage regulators (VRs), 3) network of interconnections, 4) decoupling capacitors (not graphed), and 5) power-gates
There are 3 different commonly-used PDNs
  Use Switching VRs (SVRs) and/or Low dropout VRs (LDO VRs)
  An SVR can be placed into the motherboard (MBVR) or integrated on-chip (IVR)
The PDNs perform differently based on the processor power and workload characteristics
  MBVR and LDO PDNs are more energy-efficient at low thermal design power (TDP) and light workloads compared to IVR
  IVR PDN is more energy-efficient at high TDP and heavy workloads than LDO and MBVR
  MBVR is more energy-efficient than LDO in graphics workloads
Motherboard voltage regulators (MBVR)
Integrated voltage regulators (IVR)
Low dropout voltage regulators (LDO)
MBVRs
IVRs
LDOs
Notes: [CLICK]
The Power Delivery Network is the electrical system that provides supply voltage to the processor’s domains [CLICK]
  A PDN consists of,
  a power supply,
  voltage regulators,
  network of interconnections,
  decoupling capacitors,
  and power-gates [CLICK]
There are 3 different commonly-used PDNs [CLICK]
These PDNs normally Use Switching VRs and/or Low dropout VRs [CLICK]
  An SVR can be placed into the motherboard, which called MBVR, or integrated on-chip, which known as IVR [CLICK]
The PDNs perform differently based on the processor power and workload characteristics [CLICK]
  MBVR and LDO PDNs are more energy-efficient at low thermal design power (TDP) and light workloads compared to IVR [CLICK]
  IVR PDN is more energy-efficient at high TDP and heavy workloads than LDO and MBVR [CLICK]
  MBVR is more energy-efficient than LDO in graphics workloads [END]

## Slide 7: Overview of Modern Client PDN Architectures
The Power Delivery Network (PDN) is the electrical system that provides supply voltage to the processor’s domains
  A PDN consists of 1) a power supply, 2) voltage regulators (VRs), 3) network of interconnections, 4) decoupling capacitors (not graphed), and 5) power-gates
There are 3 different commonly-used PDNs
  Use Switching VRs (SVRs) and/or Low dropout VRs (LDO VRs)
  An SVR can be placed into the motherboard (MBVR) or integrated on-chip (IVR).
The PDNs perform differently based on the processor power and workload characteristics
  MBVR and LDO PDNs are more energy-efficient at low thermal design power (TDP) and light workloads compared to IVR
  IVR PDN is more energy-efficient at high TDP and heavy workloads than LDO and MBVR
  MBVR is more energy-efficient than LDO in graphics workloads
Motherboard voltage regulators (MBVR)
Integrated voltage regulators (IVR)
Low dropout voltage regulators (LDO)
MBVRs
IVRs
LDOs
A single PDN architecture cannot provide high energy-efficiency across
a wide power consumption range and wide variety of workloads
Notes: We conclude that a single PDN architecture cannot provide high energy-efficiency across
a wide power consumption range and wide variety of workloads

## Slide 8: Presentation Outline
Overview of Client Processor PDN Architectures
Motivation and Goal
FlexWatts
  Hybrid Adaptive PDN
  Voltage Noise-Free Mode-Switching
  Runtime Mode Prediction Algorithm
Evaluation
Conclusion
Notes: I will now discuss the motivation and the goal of our work
[END]

## Slide 9: Motivational Experiment
We evaluate the potential benefits of the 3 PDNs (IVR, MBVR, LDO) across different TDPs, application ratios (ARs) and workloads
  AR is the switching rate of a component (e.g., CPU core) for a workload when compared to the highest possible power (power-virus)
We use our validated model, PDNspot, to evaluate the efficiency of the three PDNs
We use the Metric end-to-end power conversion efficiency (ETEE)
  ETEE of a PDN is the ratio between total output power consumption to total input power consumption of the PDN
We use multiple workload traces from SPEC CPU2006, 3DMark06, and video playback workloads
PDN
Loads
Output
power
Input
power
Power Supply
https://github.com/CMU-SAFARI/PDNspot
Notes: [CLICK]
We evaluate the potential benefits of the 3 PDNs :IVR, MBVR and LDO, across different TDPs, application ratios and workloads [CLICK]
  application ratio is the switching rate of a component for a workload when compared to the highest possible power (power-virus) [CLICK]
We use our validated model, PDNspot, to evaluate the efficiency of the three PDNs [CLICK]
We use the Metric end-to-end power conversion efficiency [CLICK]
  end-to-end efficiency of a PDN is the ratio between total output power consumption to total input power consumption of the PDN [CLICK]
We use multiple workload traces from SPEC CPU2006, 3DMark06, and video playback workloads [END]

## Slide 10: Observation 1: TDP Effect on PDN’s Efficiency
Executing CPU- and graphics-intensive workloads, with different ARs
  IVR PDN has a lower ETEE at the 4W TDP compared to MBVR and LDO PDNs
  IVR PDN has a higher ETEE at the 50W TDP compared to MBVR and LDO PDNs
The ETEE crossover point, at which the IVR ETEE becomes higher than the MBVR/LDO ETEE, exists at some TDP between 4W and 50W.
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74713 | 0.74724 | 0.74734 | 0.74743 | 0.74751 | 0.74758 | 0.74765 | 0.74771 | 0.74776 | 0.74781 | 0.74786 | 0.7479 | 0.74794 | 0.74798 | 0.74802 | 0.74805 | 0.74808
MBVR Measured | 0.79186 | 0.79202 | 0.79216 | 0.79228 | 0.7924 | 0.7925 | 0.79259 | 0.79268 | 0.79276 | 0.79283 | 0.7929 | 0.79296 | 0.79302 | 0.79307 | 0.79312 | 0.79316 | 0.79321
LDO Measured | 0.7945 | 0.79472 | 0.79492 | 0.7951 | 0.79527 | 0.79541 | 0.79554 | 0.79567 | 0.79578 | 0.79588 | 0.79597 | 0.79606 | 0.79614 | 0.79622 | 0.79629 | 0.79636 | 0.79642
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74731 | 0.74742 | 0.74752 | 0.74761 | 0.74769 | 0.74776 | 0.74783 | 0.74789 | 0.74794 | 0.74799 | 0.74804 | 0.74808 | 0.74812 | 0.74816 | 0.7482 | 0.74823 | 0.74826
MBVR Measured | 0.79858 | 0.79905 | 0.79947 | 0.79985 | 0.80018 | 0.80049 | 0.80077 | 0.80102 | 0.80125 | 0.80147 | 0.80166 | 0.80185 | 0.80202 | 0.80217 | 0.80232 | 0.80246 | 0.80259
LDO Measured | 0.79752 | 0.79784 | 0.79812 | 0.79837 | 0.79859 | 0.79879 | 0.79898 | 0.79915 | 0.7993 | 0.79945 | 0.79958 | 0.7997 | 0.79981 | 0.79992 | 0.80002 | 0.80011 | 0.80019
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762
MBVR Measured | 0.79266 | 0.79268 | 0.79269 | 0.79271 | 0.79272 | 0.79273 | 0.79274 | 0.79275 | 0.79276 | 0.79277 | 0.79278 | 0.79279 | 0.79279 | 0.7928 | 0.7928 | 0.79281 | 0.79281
LDO Measured | 0.79544 | 0.79546 | 0.79548 | 0.7955 | 0.79552 | 0.79554 | 0.79555 | 0.79556 | 0.79558 | 0.79559 | 0.7956 | 0.79561 | 0.79562 | 0.79563 | 0.79563 | 0.79564 | 0.79565
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.48452 | 0.50405 | 0.52224 | 0.53921 | 0.55508 | 0.56995 | 0.58389 | 0.597 | 0.60933 | 0.62096 | 0.63194 | 0.64232 | 0.65215 | 0.66147 | 0.67032 | 0.67874 | 0.68674
LDO Measured | 0.54818 | 0.56585 | 0.58216 | 0.59726 | 0.61128 | 0.62432 | 0.63649 | 0.64786 | 0.6585 | 0.66849 | 0.67789 | 0.68673 | 0.69508 | 0.70297 | 0.71043 | 0.7175 | 0.72421
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.55116 | 0.56636 | 0.58034 | 0.59324 | 0.60516 | 0.61622 | 0.6265 | 0.63609 | 0.64505 | 0.65343 | 0.6613 | 0.6687 | 0.67566 | 0.68223 | 0.68844 | 0.69431 | 0.69987
LDO Measured | 0.6178 | 0.63053 | 0.64212 | 0.65272 | 0.66246 | 0.67142 | 0.6797 | 0.68738 | 0.69451 | 0.70116 | 0.70737 | 0.71317 | 0.71862 | 0.72374 | 0.72856 | 0.73311 | 0.7374
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094
MBVR Measured | 0.71384 | 0.71543 | 0.71685 | 0.71812 | 0.71926 | 0.7203 | 0.72124 | 0.72211 | 0.7229 | 0.72363 | 0.72431 | 0.72493 | 0.72552 | 0.72606 | 0.72657 | 0.72704 | 0.72749
LDO Measured | 0.70404 | 0.70563 | 0.70705 | 0.70832 | 0.70947 | 0.71051 | 0.71145 | 0.71232 | 0.71312 | 0.71385 | 0.71453 | 0.71516 | 0.71574 | 0.71629 | 0.71679 | 0.71727 | 0.71772
4W
50W
Single-Thread
Multi-Thread
Graphics
Notes: Our first observation is about the TDP Effect on PDNs’ Efficiency [CLICK]
When Executing CPU- and graphics-intensive workloads, with different Ars [CLICK]
  We observe that IVR PDN has a lower end-to-end efficiency at the 4W TDP compared to MBVR and LDO PDNs [CLICK]
  And We observe that IVR PDN has a higher end-to-end efficiency at the 50W TDP compared to MBVR and LDO PDNs [CLICK]
The end-to-end efficiency crossover point, at which the IVR end-to-end efficiency becomes higher than the MBVR/LDO end-to-end efficiency, exists at some TDP between 4W and 50W [END]

## Slide 11: Observation 1: TDP Effect on PDN’s Efficiency
Executing CPU- and graphics-intensive workloads, with different ARs
  IVR PDN has a lower ETEE at the 4W TDP compared to MBVR and LDO PDNs
  IVR PDN has a higher ETEE at the 50W TDP compared to MBVR and LDO PDNs
The ETEE crossover point, at which the IVR ETEE becomes higher than the MBVR/LDO ETEE, exists at some TDP between 4W and 50W.
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74713 | 0.74724 | 0.74734 | 0.74743 | 0.74751 | 0.74758 | 0.74765 | 0.74771 | 0.74776 | 0.74781 | 0.74786 | 0.7479 | 0.74794 | 0.74798 | 0.74802 | 0.74805 | 0.74808
MBVR Measured | 0.79186 | 0.79202 | 0.79216 | 0.79228 | 0.7924 | 0.7925 | 0.79259 | 0.79268 | 0.79276 | 0.79283 | 0.7929 | 0.79296 | 0.79302 | 0.79307 | 0.79312 | 0.79316 | 0.79321
LDO Measured | 0.7945 | 0.79472 | 0.79492 | 0.7951 | 0.79527 | 0.79541 | 0.79554 | 0.79567 | 0.79578 | 0.79588 | 0.79597 | 0.79606 | 0.79614 | 0.79622 | 0.79629 | 0.79636 | 0.79642
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74731 | 0.74742 | 0.74752 | 0.74761 | 0.74769 | 0.74776 | 0.74783 | 0.74789 | 0.74794 | 0.74799 | 0.74804 | 0.74808 | 0.74812 | 0.74816 | 0.7482 | 0.74823 | 0.74826
MBVR Measured | 0.79858 | 0.79905 | 0.79947 | 0.79985 | 0.80018 | 0.80049 | 0.80077 | 0.80102 | 0.80125 | 0.80147 | 0.80166 | 0.80185 | 0.80202 | 0.80217 | 0.80232 | 0.80246 | 0.80259
LDO Measured | 0.79752 | 0.79784 | 0.79812 | 0.79837 | 0.79859 | 0.79879 | 0.79898 | 0.79915 | 0.7993 | 0.79945 | 0.79958 | 0.7997 | 0.79981 | 0.79992 | 0.80002 | 0.80011 | 0.80019
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762 | 0.74762
MBVR Measured | 0.79266 | 0.79268 | 0.79269 | 0.79271 | 0.79272 | 0.79273 | 0.79274 | 0.79275 | 0.79276 | 0.79277 | 0.79278 | 0.79279 | 0.79279 | 0.7928 | 0.7928 | 0.79281 | 0.79281
LDO Measured | 0.79544 | 0.79546 | 0.79548 | 0.7955 | 0.79552 | 0.79554 | 0.79555 | 0.79556 | 0.79558 | 0.79559 | 0.7956 | 0.79561 | 0.79562 | 0.79563 | 0.79563 | 0.79564 | 0.79565
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.48452 | 0.50405 | 0.52224 | 0.53921 | 0.55508 | 0.56995 | 0.58389 | 0.597 | 0.60933 | 0.62096 | 0.63194 | 0.64232 | 0.65215 | 0.66147 | 0.67032 | 0.67874 | 0.68674
LDO Measured | 0.54818 | 0.56585 | 0.58216 | 0.59726 | 0.61128 | 0.62432 | 0.63649 | 0.64786 | 0.6585 | 0.66849 | 0.67789 | 0.68673 | 0.69508 | 0.70297 | 0.71043 | 0.7175 | 0.72421
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.55116 | 0.56636 | 0.58034 | 0.59324 | 0.60516 | 0.61622 | 0.6265 | 0.63609 | 0.64505 | 0.65343 | 0.6613 | 0.6687 | 0.67566 | 0.68223 | 0.68844 | 0.69431 | 0.69987
LDO Measured | 0.6178 | 0.63053 | 0.64212 | 0.65272 | 0.66246 | 0.67142 | 0.6797 | 0.68738 | 0.69451 | 0.70116 | 0.70737 | 0.71317 | 0.71862 | 0.72374 | 0.72856 | 0.73311 | 0.7374
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094
MBVR Measured | 0.71384 | 0.71543 | 0.71685 | 0.71812 | 0.71926 | 0.7203 | 0.72124 | 0.72211 | 0.7229 | 0.72363 | 0.72431 | 0.72493 | 0.72552 | 0.72606 | 0.72657 | 0.72704 | 0.72749
LDO Measured | 0.70404 | 0.70563 | 0.70705 | 0.70832 | 0.70947 | 0.71051 | 0.71145 | 0.71232 | 0.71312 | 0.71385 | 0.71453 | 0.71516 | 0.71574 | 0.71629 | 0.71679 | 0.71727 | 0.71772
4W
50W
Single-Thread
Multi-Thread
Graphics
At low-TDP, the MBVR and LDO PDNs are more efficient.
TDP affects the ETEE of a PDN.
At high-TDP, the IVR PDN is more efficient.
Notes: We conclude that a TDP affects the end-to-end efficiency of a PDN. [CLICK]
At low-TDP, the MBVR and LDO PDNs are more efficient. [CLICK]
at high-TDP, the IVR PDN is more efficient. [END]

## Slide 12: Observation 2: Workload Effect on PDN’s Efficiency
Workload’s AR and the workload type (e.g., single-threaded, multi-threaded, graphics) affects PDN ETEE
The ETEEs of the MBVR & LDO PDNs increase with AR due to load-line effect
Different workload types have different ETEE curves
  The LDO ETEE is higher than the MBVR ETEE for CPU-intensive (single- and multi-threaded) workloads, but is lower than the MBVR ETEE for graphics-intensive workloads
  LDO inefficiency is more dominant in graphics workloads, due to the high voltage difference between the core and graphics domains (graphics’ voltage is significantly higher than cores’)
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.48452 | 0.50405 | 0.52224 | 0.53921 | 0.55508 | 0.56995 | 0.58389 | 0.597 | 0.60933 | 0.62096 | 0.63194 | 0.64232 | 0.65215 | 0.66147 | 0.67032 | 0.67874 | 0.68674
LDO Measured | 0.54818 | 0.56585 | 0.58216 | 0.59726 | 0.61128 | 0.62432 | 0.63649 | 0.64786 | 0.6585 | 0.66849 | 0.67789 | 0.68673 | 0.69508 | 0.70297 | 0.71043 | 0.7175 | 0.72421
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.55116 | 0.56636 | 0.58034 | 0.59324 | 0.60516 | 0.61622 | 0.6265 | 0.63609 | 0.64505 | 0.65343 | 0.6613 | 0.6687 | 0.67566 | 0.68223 | 0.68844 | 0.69431 | 0.69987
LDO Measured | 0.6178 | 0.63053 | 0.64212 | 0.65272 | 0.66246 | 0.67142 | 0.6797 | 0.68738 | 0.69451 | 0.70116 | 0.70737 | 0.71317 | 0.71862 | 0.72374 | 0.72856 | 0.73311 | 0.7374
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094
MBVR Measured | 0.71384 | 0.71543 | 0.71685 | 0.71812 | 0.71926 | 0.7203 | 0.72124 | 0.72211 | 0.7229 | 0.72363 | 0.72431 | 0.72493 | 0.72552 | 0.72606 | 0.72657 | 0.72704 | 0.72749
LDO Measured | 0.70404 | 0.70563 | 0.70705 | 0.70832 | 0.70947 | 0.71051 | 0.71145 | 0.71232 | 0.71312 | 0.71385 | 0.71453 | 0.71516 | 0.71574 | 0.71629 | 0.71679 | 0.71727 | 0.71772
50W
Single-Thread
Multi-Thread
Graphics
Notes: Our second observation is about the Workload Effect on PDN’s Efficiency [CLICK]
Workload’s application ratio and the workload type affects PDN end-to-end efficiency [CLICK]
The end-to-end efficiencies of the MBVR & LDO PDNs increase with AR due to load-line effect [CLICK]
Different workload types have different end-to-end efficiency curves [CLICK]
  For example: The LDO end-to-end efficiency is higher than the MBVR end-to-end efficiency for CPU-intensive workloads, but is lower than the MBVR end-to-end efficiency for graphics intensive workloads [CLICK]
  LDO inefficiency is more dominant in graphics workloads, due to the high voltage difference between the core and graphics domains [END]

## Slide 13: Observation 2: Workload Effect on PDN’s Efficiency
Workload’s AR and the workload type (e.g., single-threaded, multi-threaded, graphics) affects PDN ETEE
The ETEEs of the MBVR & LDO PDNs increase with AR due to load-line effect
Different workload types have different ETEE curves
  The LDO ETEE is higher than the MBVR ETEE for CPU-intensive (single- and multi-threaded) workloads, but is lower than the MBVR ETEE for graphics-intensive workloads
  LDO inefficiency is more dominant in graphics workloads, due to the high voltage difference between the core and graphics domains (graphics’ voltage is significantly higher than cores’)
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.48452 | 0.50405 | 0.52224 | 0.53921 | 0.55508 | 0.56995 | 0.58389 | 0.597 | 0.60933 | 0.62096 | 0.63194 | 0.64232 | 0.65215 | 0.66147 | 0.67032 | 0.67874 | 0.68674
LDO Measured | 0.54818 | 0.56585 | 0.58216 | 0.59726 | 0.61128 | 0.62432 | 0.63649 | 0.64786 | 0.6585 | 0.66849 | 0.67789 | 0.68673 | 0.69508 | 0.70297 | 0.71043 | 0.7175 | 0.72421
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.74609 | 0.74728 | 0.74835 | 0.74931 | 0.75017 | 0.75096 | 0.75167 | 0.75232 | 0.75292 | 0.75348 | 0.75399 | 0.75446 | 0.7549 | 0.75531 | 0.75569 | 0.75605 | 0.75639
MBVR Measured | 0.55116 | 0.56636 | 0.58034 | 0.59324 | 0.60516 | 0.61622 | 0.6265 | 0.63609 | 0.64505 | 0.65343 | 0.6613 | 0.6687 | 0.67566 | 0.68223 | 0.68844 | 0.69431 | 0.69987
LDO Measured | 0.6178 | 0.63053 | 0.64212 | 0.65272 | 0.66246 | 0.67142 | 0.6797 | 0.68738 | 0.69451 | 0.70116 | 0.70737 | 0.71317 | 0.71862 | 0.72374 | 0.72856 | 0.73311 | 0.7374
Chart: AR (%)
| 0.4 | 0.42500000000000004 | 0.45000000000000007 | 0.47500000000000009 | 0.50000000000000011 | 0.52500000000000013 | 0.55000000000000016 | 0.57500000000000018 | 0.6000000000000002 | 0.62500000000000022 | 0.65000000000000024 | 0.67500000000000027 | 0.70000000000000029 | 0.72500000000000031 | 0.75000000000000033 | 0.77500000000000036 | 0.80000000000000038
IVR Measured | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094 | 0.75094
MBVR Measured | 0.71384 | 0.71543 | 0.71685 | 0.71812 | 0.71926 | 0.7203 | 0.72124 | 0.72211 | 0.7229 | 0.72363 | 0.72431 | 0.72493 | 0.72552 | 0.72606 | 0.72657 | 0.72704 | 0.72749
LDO Measured | 0.70404 | 0.70563 | 0.70705 | 0.70832 | 0.70947 | 0.71051 | 0.71145 | 0.71232 | 0.71312 | 0.71385 | 0.71453 | 0.71516 | 0.71574 | 0.71629 | 0.71679 | 0.71727 | 0.71772
50W
Single-Thread
Multi-Thread
Graphics
Application ratio and workload type
have significant effects on each PDN’s ETEE.
MBVR and LDO PDNs have lower ETEE
with low application ratios.
LDO PDN has lower ETEE
on graphics workloads.
Notes: We conclude that Application ratio and workload type have significant effects on each PDN’s end-to-end efficiency [CLICK]
MBVR and LDO PDNs have lower ETEE with low application ratios [CLICK]
LDO PDN has lower ETEE on graphics workloads [CLICK]

## Slide 14: Observation 3: Power-State Effect on PDN’s Efficiency
The ETEE of the IVR PDN is lower than that of MBVR and LDO PDNs for computationally light workloads and low power states across all TDPs
A video playback workload spends 10%, and 90% of its execution time in light workload (C0MIN) and low power states (C2 and C8) respectively
MBVR and LDO PDNs have 12% and 11% lower average power consumption, respectively, than the IVR PDN due to the higher ETEE of MBVR and LDO PDNs
Chart: Power States
| C0min | C2 | C3 | C6 | C7 | C8
IVR | 0.73837 | 0.74717 | 0.73036 | 0.70961 | 0.69751 | 0.64222
MBVR | 0.79874 | 0.79709 | 0.79581 | 0.78234 | 0.78328 | 0.73404
LDO | 0.79719 | 0.79975 | 0.79581 | 0.78234 | 0.78328 | 0.73404
Chart: Norm. Average Power (%)
| Movie Playback
IVR | 1
MBVR | 0.88
LDO | 0.89
11%
12%
Notes: Our last observation is about the Power-state Effect on PDN’s Efficiency [CLICK]
The end-to-end efficiency of the IVR PDN is lower than that of MBVR and LDO PDNs for computationally light workloads and low power states across all TDPs [CLICK]
A video playback workload spends 10%, and 90% of its execution time in light workload and low power states respectively [CLICK]
MBVR and LDO PDNs have 12% and 11% lower average power consumption, respectively, than the IVR PDN due to the higher end-to-end efficiency of MBVR and LDO PDNs [END]

## Slide 15: Observation 3: Power-State Effect on PDN’s Efficiency
The ETEE of the IVR PDN is lower than that of MBVR and LDO PDNs for computationally light workloads and low power states across all TDPs
A video playback workload spends 10%, and 90% of its execution time in light workload (C0MIN) and low power states (C2 and C8) respectively
MBVR and LDO PDNs have 12% and 11% lower average power consumption, respectively, than the IVR PDN due to the higher ETEE of MBVR and LDO PDNs
Chart: Power States
| C0min | C2 | C3 | C6 | C7 | C8
IVR | 0.73837 | 0.74717 | 0.73036 | 0.70961 | 0.69751 | 0.64222
MBVR | 0.79874 | 0.79709 | 0.79581 | 0.78234 | 0.78328 | 0.73404
LDO | 0.79719 | 0.79975 | 0.79581 | 0.78234 | 0.78328 | 0.73404
Chart: Norm. Average Power (%)
| Movie Playback
IVR | 1
MBVR | 0.88
LDO | 0.89
11%
12%
The IVR PDN is energy-inefficient
for computationally-light workloads.
This negatively impacts both energy consumption and battery life.
Notes: We conclude that the IVR PDN is energy-inefficient for computationally-light workloads.
This negatively impacts both energy consumption and battery life [END]

## Slide 16: Our Goal: A Hybrid and Adaptive PDN
We conclude that there is no single PDN for modern client processors that provides a high ETEE across all TDPs, workload types and application ratios (ARs)
Notes: Based on our three key observations [CLICK]
We conclude that there is no single PDN for modern client processors that provides a high end-to-end efficiency across all TDPs, workload types and application ratios [CLICK]

## Slide 17: Our Goal: A Hybrid and Adaptive PDN
We conclude that there is no single PDN for modern client processors that provides a high ETEE across all TDPs, workload types and application ratios (ARs)
Our goal is to provide a PDN architecture that provides
high energy-efficiency across the wide range of
power consumption and variety of workloads.
Notes: Our goal is to provide a PDN architecture that provides
high energy-efficiency across the wide range of
power consumption and variety of workloads.

## Slide 18: Presentation Outline
Overview of Client Processor PDN Architectures
Motivation and Goal
FlexWatts
  Hybrid Adaptive PDN
  Voltage Noise-Free Mode-Switching
  Runtime Mode Prediction Algorithm
Evaluation
Conclusion
Notes: Now I will explain the technique to achieve our goal
[END]

## Slide 19: FlexWatts
FlexWatts is a new hybrid adaptive PDN that provides a high ETEE for the wide power consumption range and workload diversity of client processors
FlexWatts is based on three key ideas:
  New hybrid voltage regulators (VRs) that are allocated for processor domains with a wide power consumption range that dynamically switch between two modes (IVR-Mode and LDO-Mode) to maintain high energy-efficiency across the wide range
  Static allocation of off-chip VRs, which have high energy-efficiency for low and narrow power ranges, for the rest of the domains (e.g., IO domain)
  A novel prediction algorithm that switches the hybrid PDN to the mode (IVR-Mode/LDO-Mode) that is the most beneficial based on processor power and workload characteristics
Notes: We propose FlexWatts [CLICK] FlexWatts is a new hybrid adaptive PDN that provides a high ETEE for the wide power consumption range and workload diversity of client processors [CLICK]
FlexWatts is based on three key ideas: [CLICK]
  First, New hybrid voltage regulators (VRs) that are allocated for processor domains with a wide power consumption range that dynamically switch between two modes (IVR-Mode and LDO-Mode) to maintain high energy-efficiency across the wide range [CLICK]
  Secondly, Static allocation of off-chip VRs, which have high energy-efficiency for low and narrow power ranges, for the rest of the domains [CLICK]
  And Finaly, A novel prediction algorithm that switches the hybrid PDN to the mode that is the most beneficial based on processor power and workload characteristics [END]

## Slide 20: FlexWatts Architecture: 3 Components
Hybrid adaptive PDN: includes hybrid VRs and off-chip VRs
Voltage Noise-Free Mode-Switching: transitions the hybrid PDN between two modes (IVR-Mode and LDO-Mode)
A new mode prediction algorithm: automatically determines, which PDN mode would be the most beneficial based on system and workload characteristics
Notes: [CLICK] FlexWatts has three key components: [CLICK]
  A hybrid adaptive PDN that includes hybrid VRs and off-chip VRs [CLICK]
  A Voltage Noise-Free Mode-Switching that transitions the hybrid PDN between two modes, IVR-Mode and LDO-Mode
  A new mode prediction algorithm that automatically determines which PDN mode would be the most beneficial based on system and workload characteristics [END]

## Slide 21: Component 1: Hybrid Adaptive PDN
Off-chip VRs allocated to each system domain with a low and narrow power consumption range (i.e., SA and IO domains).
Hybrid VRs allocated to system domains with a wide power consumption range (e.g., CPU cores and graphics engines)
  This hybrid PDN can dynamically switch between two modes, IVR-Mode and LDO-Mode, based on the expected ETEE benefits of each mode for the current workload and power consumption
  The hybrid PDN shares multiple die, package, and board resources
Notes: Now I will talk about each component in more detail.
The first component is a Hybrid Adaptive PDN [CLICK] FlexWatts PDN consists of two key components:
Off-chip VRs allocated to each system domain with a low and narrow power consumption range [CLICK]
A hybrid VRs allocated to system domains with a wide power consumption range [CLICK]
  This hybrid PDN can dynamically switch between two modes, IVR-Mode and LDO-Mode, based on the expected ETEE benefits of each mode for the current workload and power consumption [CLICK]
  The hybrid PDN shares multiple die, package and board resources [END]

## Slide 22: Component 2: Voltage Noise-Free Mode-Switching
FlexWatts performs mode-switching using 3 steps, while the compute domains are idle to prevent any voltage noise
  Place the processor in an idle power-state for a short period of time
  Configure the hybrid PDN and update the on-chip and off-chip VR levels
  Exit the idle power-state and resume the processor with the new PDN mode
Notes: The second component is a Voltage Noise-free Mode-Switching mechanism [CLICK]
FlexWatts performs mode-switching using 3 steps, while the compute domains are idle to prevent any voltage noise
  First, We Place the processor in an idle power-state for a short period of time [CLICK]
  Secondly, We Configure the hybrid PDN and update the on-chip and off-chip VR levels, and [CLICK]
  And finally, We Exit the idle power-state and resume the processor with the new PDN mode [END]

## Slide 23: Component 3: Runtime Mode Prediction Algorithm
A new runtime mode-prediction algorithm predicts which PDN mode, among the two modes (IVR-Mode and LDO-Mode), provides the best end-to-end power conversion efficiency (ETEE). ETEE is a function of:
  The AR and the workload type (i.e., single-thread, multi-thread, and graphics)
  The TDP and the power-state of the system
We store two sets of ETEE curves inside the power management unit (PMU) firmware, one set for the IVR PDN and the other set for the LDO PDN
The PMU firmware estimates each of the input parameters at runtime
TDP
Application Ratio
Workload Type
Power state
Estimate IVR ETEE
Estimate LDO ETEE
IVR_ETEE> LDO_ETEE
LDO_Mode
IVR_Mode
Yes
No
Notes: The final component is Runtime Mode Prediction Algorithm [CLICK]
A new runtime mode-prediction algorithm predicts which PDN mode, among the two modes (IVR-Mode and LDO-Mode), provides the best end-to-end power conversion efficiency (ETEE). ETEE is a function:
  The AR and the workload type, i.e., single-thread, multi-thread, and graphics [CLICK]
  The TDP and the power-state of the system [CLICK]
We store two sets of ETEE curves inside the power management unit firmware, one set for the IVR PDN and the other set for the LDO PDN [CLICK]
The PMU firmware estimates each of the input parameters at runtime [END]

## Slide 24: Presentation Outline
Overview of Client Processor PDN Architectures
Motivation and Goal
FlexWatts
  Hybrid Adaptive PDN
  Voltage Noise-Free Mode-Switching
  Runtime Mode Prediction Algorithm
Evaluation
Conclusion
Notes: I will next present our evaluation of FlexWatts
[END]

## Slide 25: Methodology
Framework: We evaluate the PDNs using our new open-sourced PDNspot model
Workloads: We evaluate FlexWatts with three classes of workloads
  CPU: SPEC CPU2006 benchmarks
  Graphics: 3DMARK06 benchmarks
  Battery life: web browsing, light gaming, video conferencing, and video playback benchmarks
Comparison Points: We compare FlexWatts to the three commonly-used (IVR, MBVR, LDO) PDNs of client processors
https://github.com/CMU-SAFARI/PDNspot
Notes: First, I will present our methodology [CLICK]
We evaluate the PDNs using our new open-sourced PDNspot model [CLICK]
We evaluate FlexWatts with three classes of workloads [CLICK]
  For CPU:SPEC CPU2006 benchmarks [CLICK]
  For Graphics: 3DMARK06 benchmarks [CLICK]
  And For Battery life: web browsing, light gaming, video conferencing, and video playback benchmarks [CLICK]
We compare FlexWatts to the three commonly-used PDNs of client processors [END]

## Slide 26: Results – CPU Workloads (TDPs 4-50W)
At TDPs lower than 18W, FlexWatts provides up to 22% higher performance over the IVR PDN
  by operating mainly in LDO-Mode
At TDPs higher than 18W, FlexWatts provides up to 7%/4% higher performance over the MBVR/LDO PDNs
  by operating in IVR-Mode
Chart: Norm. Performance (%)
| 4W | 8W | 10W | 18W | 25W | 36W | 50W
IVR | 1 | 1 | 1 | 1 | 1 | 1 | 1
MBVR | 1.2321 | 1.1128 | 1.0552 | 0.95206 | 0.91539 | 0.92001 | 0.93165
LDO | 1.2246 | 1.145 | 1.0852 | 1.0159 | 0.97074 | 0.95947 | 0.9635
FlexWatts | 1.2196 | 1.14 | 1.0802 | 1.0109 | 0.991 | 0.9905 | 0.991
22%
7%
4%
Notes: Let me start with showing the result for the CPU workloads [CLICK]
[CLICK]
At TDPs lower than 18W, FlexWatts provides up to 22% higher performance over the IVR PDN
by operating mainly in LDO-Mode [CLICK]
At TDPs higher than 18W, FlexWatts provides up to 7%/4% higher performance over the MBVR/LDO PDNs
by operating in IVR-Mode [CLICK]

## Slide 27: Results – CPU Workloads (TDPs 4-50W)
At TDPs lower than 18W, FlexWatts provides up to 22% higher performance over the IVR PDN by operating mainly in LDO-Mode, which has a higher ETEE than the IVR PDN at low TDPs
At TDPs higher than 18W, FlexWatts provides up to 7%/4% higher performance over the MBVR/LDO PDNs by operating at IVR-Mode, which has a higher ETEE than the MBVR/LDO PDNs at high TDPs
Chart: Norm. Performance (%)
| 4W | 8W | 10W | 18W | 25W | 36W | 50W
IVR | 1 | 1 | 1 | 1 | 1 | 1 | 1
MBVR | 1.2321 | 1.1128 | 1.0552 | 0.95206 | 0.91539 | 0.92001 | 0.93165
LDO | 1.2246 | 1.145 | 1.0852 | 1.0159 | 0.97074 | 0.95947 | 0.9635
FlexWatts | 1.2196 | 1.14 | 1.0802 | 1.0109 | 0.991 | 0.9905 | 0.991
22%
7%
4%
FlexWatts significantly improves CPU performance compared to IVR at low TDPs by operating in LDO-Mode.
FlexWatts provides higher CPU performance compared
to MBVR/LDO at high TDPs by operating in IVR-Mode.
Notes: FlexWatts significantly improves CPU performance compared to IVR at low TDPs by operating in LDO-Mode. [CLICK]
FlexWatts provides higher CPU performance compared to MBVR/LDO at high TDPs by operating in IVR-Mode. [CLICK]

## Slide 28: Results – Graphics Workloads
At TDPs lower than 25W, FlexWatts provides up to 25% higher performance over the IVR PDN
  by operating mainly in LDO-Mode
At TDPs higher than 25W, FlexWatts provides up to 3%/6% higher performance over the MBVR/LDO PDNs
  by operating mainly in IVR-Mode
At TDPs lower than 25W, FlexWatts performs slightly worse (up to 2%) than MBVR/LDO PDNs due to
  The higher load-line of FlexWatts
  The large difference in operating voltages across the cores/LLC/graphics domains
Chart: Norm. Performance (%)
| 4W | 8W | 10W | 18W | 25W | 36W | 50W
IVR | 1 | 1 | 1 | 1 | 1 | 1 | 1
MBVR | 1.2735 | 1.2437 | 1.2034 | 1.0977 | 0.99997 | 0.97181 | 0.93954
LDO | 1.2615 | 1.2161 | 1.1738 | 1.0754 | 0.95058 | 0.9402 | 0.91848
FlexWatts | 1.2525 | 1.209 | 1.1658 | 1.0694 | 0.9909 | 0.9905 | 0.9901
25%
6%
2%
3%
Notes: Now let us see the result for the Graphics workloads [CLICK]
At TDPs lower than 25W, FlexWatts provides up to 25% higher performance over the IVR PDN
  by operating mainly in LDO-Mode
At TDPs higher than 25W, FlexWatts provides up to 3% and 6% higher performance over the MBVR and LDO PDNs
  by operating mainly in IVR-Mode
At TDPs lower than 25W, FlexWatts performs slightly worse (up to 2%) than MBVR/LDO PDNs due to
  The higher load-line of FlexWatts
  The large difference in operating voltages across the cores/LLC/graphics domains
[END]

## Slide 29: Results – Graphics Workloads
At TDPs lower than 25W, FlexWatts provides up to 25% higher performance over the IVR PDN
  by operating mainly in LDO-Mode
At TDPs higher than 25W, FlexWatts provides up to 3%/6% higher performance over the MBVR/LDO PDNs
  by operating mainly in IVR-Mode
At TDPs lower than 25W, FlexWatts performs slightly worse (up to 2%) than MBVR/LDO PDNs due to
  The higher load-line of FlexWatts
  The large difference in operating voltages across the cores/LLC/graphics domains
Chart: Norm. Performance (%)
| 4W | 8W | 10W | 18W | 25W | 36W | 50W
IVR | 1 | 1 | 1 | 1 | 1 | 1 | 1
MBVR | 1.2735 | 1.2437 | 1.2034 | 1.0977 | 0.99997 | 0.97181 | 0.93954
LDO | 1.2615 | 1.2161 | 1.1738 | 1.0754 | 0.95058 | 0.9402 | 0.91848
FlexWatts | 1.2525 | 1.209 | 1.1658 | 1.0694 | 0.9909 | 0.9905 | 0.9901
25%
7%
2%
3%
FlexWatts significantly improves graphics performance compared to IVR at low TDPs by operating in LDO-Mode.
FlexWatts provides higher graphics performance compared
to MBVR/LDO at high TDPs by operating in IVR-Mode.
Notes: We conclude that FlexWatts significantly improves graphics performance compared to IVR at low TDPs by operating in LDO-Mode. [CLICK]
FlexWatts provides higher graphics performance compared to MBVR/LDO at high TDPs by operating in IVR-Mode.

## Slide 30: Results – Battery Life Workloads
FlexWatts reduces average power consumption (8%-11%) on battery life workloads compared to IVR PDN
FlexWatts consumes up to 1% more power than MBVR PDN
Chart: Norm. Average Power (%)
| Movie Playback | Video Conf. | Web Browsing | Light Gaming
IVR | 1 | 1 | 1 | 1
MBVR | 0.88 | 0.89622 | 0.91048 | 0.9156
LDO | 0.89 | 0.90181 | 0.91639 | 0.92162
FlexWatts | 0.89 | 0.90743 | 0.92233 | 0.92769
11%
8%
1%
Battery life workloads have fixed performance requirements
  they consume the same power at all TDPs
Notes: Now I will present the results for Battery Life Workloads [CLICK]
Battery life workloads have fixed performance requirements
  they consumes the same power at all TDPs [CLICK]
FlexWatts reduces average power consumption between 8% to 11% on a battery life workloads compared to IVR PDN [CLICK]
FlexWatts consumes up to 1% more power than MBVR PDN [CLICK]

## Slide 31: Results – Battery Life Workloads
FlexWatts reduces average power consumption (8%-11%) on battery life workloads compared to IVR PDN
FlexWatts consumes up to 1% more power than MBVR PDN
Chart: Norm. Average Power (%)
| Movie Playback | Video Conf. | Web Browsing | Light Gaming
IVR | 1 | 1 | 1 | 1
MBVR | 0.88 | 0.89622 | 0.91048 | 0.9156
LDO | 0.89 | 0.90181 | 0.91639 | 0.92162
FlexWatts | 0.89 | 0.90743 | 0.92233 | 0.92769
11%
8%
1%
Battery life workloads have fixed performance requirements
  they consume the same power at all TDPs
FlexWatts is almost as energy-efficient as both MBVR and LDO
and up to 11% more energy-efficient than IVR.
Notes: We conclude that FlexWatts is almost as energy-efficient as both MBVR and LDO
and up to 11% more energy-efficient than IVR,
for battery life workloads.

## Slide 32: Other Results in the Paper
FlexWatts board area and bill of materials (BOM) compared to other PDNs:
  FlexWatts PDN has comparable BOM cost and board area to IVR PDN
  FlexWatts PDN has significantly lower BOM cost and board area compared to MBVR and LDO PDNs
Comparison to the PDN used in Intel Skylake-X processors that combines IVR and MBVR PDNs
  Intel Skylake-X PDN provides higher performance and lower energy consumption than the IVR PDN
  FlexWatts provides significantly higher performance and lower energy consumption than the Intel Skylake-X PDN
Notes: We have more results in the paper. For example [CLICK]
FlexWatts board area and bill of materials (BOM) compared to other PDNs:
  FlexWatts PDN has comparable BOM cost and board area to IVR PDN
  FlexWatts PDN has significantly lower BOM cost and board area compared to MBVR and LDO PDNs
Comparison to the PDN used in Intel Skylake-X processors that combines IVR and MBVR PDNs
  Intel Skylake-X PDN Provides higher performance and lower energy consumption than the IVR PDN
  FlexWatts provides significantly higher performance and lower energy consumption than the Intel Skylake-X PDN
[END]

## Slide 33: Presentation Outline
Overview of Client Processor PDN Architectures
Motivation and Goal
FlexWatts
  Hybrid Adaptive PDN
  Voltage Noise-Free Mode-Switching
  Runtime Mode Prediction Algorithm
Evaluation
Conclusion
Notes: Let me quickly conclude my talk.
[END]

## Slide 34: Conclusion
Problem: Client processors typically use one of three commonly-used power delivery network (PDN) architectures: 1) MBVR, 2) IVR, and 3) LDO. The energy-efficiency of each of these PDNs varies with the processor power and workload characteristics.
Goal: Provide high energy-efficiency and high performance PDN architecture by leveraging the advantages of each one of the three PDN architectures across the processor’s wide range of power consumption and workloads.
Mechanism: FlexWatts, a new hybrid adaptive PDN for client processors that introduces
  New hybrid voltage regulators (VRs) that are allocated for processor domains with a wide power consumption range (e.g., CPU cores and graphics engines) that dynamically switch between two modes: IVR-Mode and LDO-Mode.
  Static allocation of off-chip VRs, which have high energy-efficiency for low and narrow power ranges, for the rest of the domains (e.g., IO domain).
  A novel prediction algorithm that switches the hybrid PDN to the mode (IVR-Mode/LDO-Mode) that is the most beneficial based on processor power and workload characteristics.
Evaluation: We evaluate FlexWatts using our new architectural PDN model (PDNspot):
  Improves the average performance of the SPEC CPU2006 and 3DMark06 workloads by 22% and 25%, respectively, for 4W thermal design power (TDP) system.
  Reduces the average power consumption of video playback workload by 11% across all tested TDPs (4W-50W).
https://github.com/CMU-SAFARI/PDNspot
Notes: Client processors typically use one of three commonly-used power delivery network architectures: MBVR, IVR , and LDO.
The energy-efficiency of each of these PDNs varies with the processor power and workload characteristics. [CLICK]
Our goals is to provide high energy-efficiency and high performance PDN architecture by leveraging the advantages of each one of the three PDN architectures across the processor’s wide range of power consumption and workloads. [CLICK]
To this end we propose FlexWatts, a new hybrid adaptive PDN for client processors that introduces three mechanisms [CLICK]
First, New hybrid voltage regulators that are allocated for processor domains with a wide power consumption range that dynamically switches between two modes: IVR-Mode and LDO-Mode. [CLICK]
Secondly, Static allocation of off-chip VRs, which have high energy-efficiency for low and narrow power ranges, for the rest of the domains. [CLICK]
And finally, A novel prediction algorithm that switches the hybrid PDN to the mode that is the most beneficial based on processor power and workload characteristics. [CLICK]
We evaluate FlexWatts using our new architectural PDN model, PDNspot [CLICK]
FlexWatts Improves the average performance of the SPEC CPU2006 and 3DMark workloads by 22% and 25%, respectively, for 4W thermal design power system. [CLICK]
and FlexWatts Reduces the average power consumption of video playback workload by 11% across all tested TDPs
[END]

## Slide 35
Jawad Haj-Yahya1 Mohammed Alser1 Jeremie S. Kim1 Lois Orosa1 Efraim Rotem2
Avi Mendelson3,4 Anupam Chattopadhyay 4 Onur Mutlu1
FlexWatts: A Power- and Workload-Aware Hybrid Power Delivery Network for
Energy-Efficient Microprocessors
1
1
2
3
4
MICRO 2020, session 6B Mobile & Embedded Architectures
Wednesday, October 21, 2020
Notes: Thank you for your attention. For many more details, I invite you to read our MICRO 2020 paper. [END]