## Slide 1: A Compiler Framework for Optimizing Dynamic Parallelism on GPUs
Mhd Ghaith Olabi1, Juan Gómez Luna2, Onur Mutlu2, Wen-mei Hwu3,4, Izzat El Hajj1
1American University of Beirut 2ETH Zurich 3NVIDIA 4University of Illinois at Urbana-Champaign

## Slide 2: Organization of GPU Kernels
Grid
Thread
Thread block
Notes: Showcase BFS

## Slide 3: Dynamic Parallelism on GPUs
Dynamic parallelism enables executing GPU threads to launch other grids of threads
Useful for implementing computations with nested parallelism
Dynamic launch
Parameters and launch configurations
Parent threads
Child grids
Notes: Showcase BFS

## Slide 4: Dynamic Parallelism Overhead
Using dynamic parallelism may cause many small grids to be launched
Launching many small grids causes performance degradation due to:
  Congestion
    Limited number of grids can execute simultaneously (others need to wait)
  Hardware underutilization
    If grids are small, their may not be enough threads launched to fully utilize hardware resources
Solution: launch fewer grids of larger sizes
Notes: Showcase BFS

## Slide 5: Prior Work: Aggregation
Aggregation is an optimization where:
  Multiple child grids are consolidated into a single aggregated grid
  One parent thread launches the aggregated grid on behalf of the rest
I. El Hajj, J. Gomez-Luna, C. Li, L.-W. Chang, D. Milojicic, and W.-m. ´ Hwu, “KLAP: Kernel launch aggregation and promotion for optimizing dynamic parallelism,” in Microarchitecture (MICRO), 2016 49th Annual IEEE/ACM International Symposium on. IEEE, 2016, pp. 1–12
D. Li, H. Wu, and M. Becchi, “Exploiting dynamic parallelism to efficiently support irregular nested loops on GPUs,” in Proceedings of the 2015 International Workshop on Code Optimisation for Multi and Many Cores. ACM, 2015, p. 5.
Li, D., Wu, H., & Becchi, M., “Nested parallelism on GPU: Exploring parallelization templates for irregular loops and recursive computations,” in Parallel Processing (ICPP), 2015 44th International Conference on. IEEE, 2015, pp. 979– 988.
H. Wu, D. Li, and M. Becchi, “Compiler-assisted workload consolidation for efficient dynamic parallelism on GPU,” arXiv preprint arXiv:1606.08150, 2016.

## Slide 6: Prior Work: Aggregation
Aggregation is an optimization where:
  Multiple child grids are consolidated into a single aggregated grid
  One parent thread launches the aggregated grid on behalf of the rest
In memory
Memory access
Aggregated child grid
+ Reduces congestion by reducing the number of launched grids
+ Improves utilization because aggregated child grids have more threads then original ones

## Slide 7: Prior Work: Aggregation
Aggregates launches at different levels of granularity
Grid-Granularity
Block-Granularity
Original Kernel
Warp-Granularity

## Slide 8: Contributions
Thresholding (as a compiler optimization)
  Prior work relies on programmers to apply it manually
Coarsening of child thread blocks
  Prior work on compiler-based coarsening not specialized for dynamic parallelism
Aggregation of child grids at multi-block granularity
  Prior work only compiler-based aggregation only considers warp, block, and grid granularity
One compiler framework that combined the three optimizations

## Slide 9: Thresholding
Thresholding is an optimization where:
  A grid is launched dynamically only if the number of child threads exceeds a certain threshold
  Otherwise, work is executed sequentially by the parent thread

## Slide 10: Thresholding
Thresholding is an optimization where:
  A grid is launched dynamically only if the number of child threads exceeds a certain threshold
  Otherwise, work is executed sequentially by the parent thread
Child thread serialized in parent thread
+ Reduces congestion by reducing the number of launched grids
+ Improves utilization by only allowing grids with many threads to be launched

## Slide 11: Thresholding: Code Transformation
Create a serial device function executable by the parent
Heuristic to detect total number of threads to be compared with threshold
  Detect number of threads to be launched by observing commonly used grid dimension calculation expressions, such as ceiling divisions
Apply a conditional guard to either launch or serialize
09 __device__ child_serial(..., dim3 _gDim, dim3 _bDim) {
10 for(_bx = 0; _bx < _gDim.x; ++_bx) {
11 for(_tx = 0; _tx < _bDim.x; ++_tx) {
12 child body // Replace uses of blockIdx.x with _bx,
13 } // threadIdx.x with _tx, gridDim with
14 } // _gDim, and blockDim with _bDim
15 }
19 __global__ parent(...) {
20 ...
21 _threads = ...; // Extracted from gDim expression
22 if(_threads >= _THRESHOLD) {
23 child <<< gDim, bDim >>> (...);
24 } else {
25 child_serial (..., gDim, bDim);
26 }
27 ...
28 }
01 __global__ child(...) {
02 child body
03 }
04 __global__ parent(...) {
05 ...
06 child <<< gDim, bDim >>> (...);
07 ...
08 }

## Slide 12: Coarsening
Coarsening is a transformation where:
  The work of multiple child blocks is assigned to a single child block

## Slide 13: Coarsening
Coarsening is a transformation where:
  The work of multiple child blocks is assigned to a single child block
Coarsened child grids
Original thread block before coarsening
+ When applied before aggregation, amortizes the cost of disaggregation (incurred once per child blocks)

## Slide 14: Coarsening: Code Transformation
Coarsening child kernel
  Insert the coarsening loop around the child kernel body
Modify kernel parameters
  Add an extra parameter _gDim (being the original grid dimension) to be passed to the coarsened child kernel
Modify launch parameters
  Update grid dimension considering _CFACTOR
01 __global__ child(params, _gDim) {
02 for(_bx = blockIdx.x; _bx < _gDim.x; _bx += gridDim.x) {
03 child body // Replace uses of blockIdx.x with _bx
04 } // and gridDim with _gDim
05 }
06 __global__ parent(...) {
07 ...
08 _cgDim = _gDim = gDim ;
09 _cgDim.x = (_gDim.x + _CFACTOR – 1)/_CFACTOR;
10 child <<< _cgDim, bDim >>>(args, _gDim);
11 ...
12 }
01 __global__ child(...) {
02 child body
03 }
04 __global__ parent(...) {
05 ...
06 child <<< gDim, bDim >>> (...);
07 ...
08 }

## Slide 15: Multi-block Granularity Aggregation
Multi-block granularity aggregation is an optimization where:
  The child grids of multiple parent blocks are consolidated into a single aggregated grid

## Slide 16: Multi-block Granularity Aggregation
Multi-block granularity aggregation is an optimization where:
  The child grids of multiple parent blocks are consolidated into a single aggregated grid
+ Compared to block granularity, launches fewer and larger grids
+ Compared to grid granularity, launches child grids more eagerly

## Slide 17: Multi-block Aggregation: Code Transformation
See paper for detailed description of the code transformation
Key difference from other techniques:
  Every k blocks maintain a shared counter
  Each block atomically increments shared counter when reaching launch
  The kth block to increment the counter performs the launch
  Use thread fences to ensure that memory visibility semantics are preserved
01 __global__ child(_paramsArray, _gDimScannedArray, _bDimArray) {
02 _parentIdx = binary search in _gDimScannedArray
03 params = _paramsArray[_parentIdx]
04 _gDim = _gDimScannedArray[_parentIdx] - _gDimScannedArray[_parentIdx - 1]
05 _bx = blockIdx.x - _gDimScannedArray[_parentIdx - 1]
06 _bDim = _bDimArray[_parentIdx]
07 if(threadIdx < _bDim) {
08 child body // Replace uses of blockIdx.x with _bx
09 // and gridDim with _gDim
10 }
11 }
12 __global__ parent(...) {
13 ...
14 _gDim = gDim
15 _bDim = bDim
16 _groupIdx = blockIdx.x/_AGG_GRANULARITY
17 find group's memory segments in a pre-allocated buffer based on _groupIdx
18 if(_gDim > 0) {
19 (_parentIdx, _sumPrevGDim) =
20 atomicAdd(&(_numParents[_groupIdx], _sumGDim[_groupIdx]), (1, _gDim))
21 _argsArray[_parentIdx] = args
22 _gDimScannedArray[_parentIdx] = _sumPrevGDim + _gDim
23 _bDimArray[_parentIdx] = _bDim
24 atomicMax(&_maxBDim[_groupIdx], _bDim)
25 }
26 __threadfence()
27 __syncthreads()
28 if(threadIdx == launcher thread in block) {
29 _nFinishedBlocks = atomicAdd(&_numFinishedBlocks[_groupIdx], 1) + 1
30 _isLastBlockToFinish = (_nFinishedBlocks == _AGG_GRANULARITY)
31 if(_isLastBlockToFinish) {
32 child <<< _sumGDim[_groupIdx] , _maxBDim[_groupIdx] >>>
33 (_argsArray, _gDimScannedArray, _bDimArray);
34 }
35 }
36 ...
37 }

## Slide 18: Putting it all together
Thresholding
Coarsening
Aggregation
.cu
.cu
.cu
.cu

## Slide 19: Overall Speedup
We evaluate all combinations of optimizations for 7 benchmarks with 2 datasets each
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985

## Slide 20: Overall Speedup
We report speedup (higher is better) over the baseline that uses CUDA dynamic parallelism (CDP)
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985

## Slide 21: Overall Speedup
Observation #1: Not using CDP performs better than naïve CDP (same observation as prior work).
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985

## Slide 22: Overall Speedup
Observation #2: Aggregation improves performance of naïve CDP (same observation as prior work).
KLAP(CDP+A) is 12.1× faster than CDP on average (geomean).
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985

## Slide 23: Overall Speedup
Observation #3: Thresholding alone improves the performance over CDP.
CDP+T is 13.4× faster than CDP on average (geomean).
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985

## Slide 24: Overall Speedup
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985
Observation #4: Thresholding and Aggregation together improve the performance over CDP even more.
Despite both targeting the same source of inefficiency, one optimization does not obviate the other.

## Slide 25: Overall Speedup
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985
Observation #5: Coarsening alone does not improve performance substantially over CDP.
CDP+C is 1.01× faster than CDP.

## Slide 26: Overall Speedup
Chart: Speedup over CDP
| KRON | CNR | T32-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Geomean
No CDP | 6.5228 | 9.12 | 3.2117 | 1.0012 | 1.4106 | 2.3559 | 1.5304 | 6.2898 | 27.3969 | 0.14838 | 2.9487 | 10.5376 | 49.2928 | 138.7057 | 4.9488
CDP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
KLAP (CDP+A) | 13.382 | 22.3683 | 15.762 | 32.0761 | 8.0711 | 11.4359 | 10.3378 | 12.401 | 12.7678 | 9.6106 | 15.3985 | 24.0936 | 3.1464 | 5.3798 | 12.062
CDP+T | 15.5323 | 21.174 | 3.0975 | 1.03 | 8.9063 | 24.6794 | 116.192 | 65.7087 | 1.0093 | 1.0414 | 15.1 | 101.9115 | 15.586 | 131.246 | 13.369
CDP+C | 1.0028 | 1.0055 | 0.99977 | 1.029 | 1.0406 | 1.0097 | 1.0051 | 1.0019 | 1.0121 | 1.0239 | 0.99843 | 0.98922 | 1.0913 | 1.0037 | 1.0149
CDP+T+C | 15.7479 | 21.4267 | 3.0719 | 1.0491 | 10.0182 | 27.0858 | 116.4154 | 67.5061 | 1.0133 | 1.1173 | 18.0869 | 133.5322 | 19.996 | 147.5855 | 14.531
CDP+T+A | 17.7191 | 28.6653 | 16.206 | 42.5077 | 11.2256 | 30.2362 | 106.3237 | 100.6195 | 7.9523 | 7.6662 | 31.736 | 244.3081 | 23.4695 | 320.1842 | 35.2165
CDP+C+A | 26.3893 | 24.562 | 15.7794 | 41.8121 | 8.4034 | 10.2999 | 10.0278 | 11.5652 | 12.9332 | 15.5516 | 16.3337 | 21.8046 | 5.9153 | 5.8118 | 13.9502
CDP+T+C+A | 28.3823 | 30.3652 | 16.5295 | 43.3657 | 12.9355 | 34.4622 | 108.9033 | 111.742 | 8.0872 | 11.8754 | 40.6518 | 285.403 | 46.6433 | 422.1261 | 42.985
Observation #6: Coarsening does improve performance when combined with the other optimizations.
Recall: main benefit was amortizing overhead of aggregation. CDP+T+C+A is 1.22× faster than CDP+T+A.

## Slide 27: Execution Time Breakdown
Chart: Execution Time (normalized to CDP+A)
| KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A |  | KLAP (CDP+A) | CDP+T+A | CDP+T+C+A | KRON | CNR | T0032-C16 | T2048-C64 | KRON | CNR | KRON | CNR | RAND-3 | 5-SAT | KRON | CNR | KRON | CNR |  | BFS | BT | MSTF | MSTV | SP | SSSP | TC |  | Mean
Parent work | 0.046928 | 0.27097 | 0.10039 | 0.056746 | 0.23524 | 0.21871 | 0.82083 | 0.90241 | 0.88139 | 0.56047 | 0.69928 | 0.70783 | 0.012555 | 0.10637 | 0.10851 | 0.078909 | 0.11615 | 0.11504 | 0.015136 | 0.02488 | 0.019652 | 0.0075258 | 0.01882 | 0.018395 | 0.66646 | 1.4991 | 1.2775 | 0.15783 | 0.3425 | 0.55643 | 0.028085 | 0.2258 | 0.12435 | 0.01006 | 0.056202 | 0.05632 | 0.00079988 | 0.036768 | 0.036377 | 0.001582 | 0.0075965 | 0.0084563 | 0.17599 | 0.32443 | 0.3021
Child work | 0.23435 | 0.014831 | 0.035674 | 0.09711 | 0.029836 | 0.043825 | 0.045033 | 0.002092 | 0.00018351 | 0.065902 | 0.026877 | 0.021964 | 0.20694 | 0.090476 | 0.10546 | 0.18337 | 0.0095437 | 0.0097881 | 0.19792 | 0.011079 | 0.0030725 | 0.16117 | 0.0084281 | 0.012877 | 0.028413 | 0.10438 | 0.055997 | 0.29862 | 0.25911 | 0.25693 | 0.14576 | 0.065486 | 0.064957 | 0.13122 | 0.0074161 | 0.0087136 | 0.088665 | 0.0033202 | 0.0052571 | 0.048378 | 0.00041482 | 0.00028252 | 0.13806 | 0.045235 | 0.044642
Launch | 0.39967 | 0.020266 | 0.034421 | 0.45735 | 0.048502 | 0.013967 | 0.11748 | 0.023306 | 0.02448 | 0.22662 | 0.0051065 | 0.0022627 | 0.73293 | 0.23435 | 0.14543 | 0.70361 | 0.016713 | 0.0063521 | 0.72615 | 0.047052 | 0.045937 | 0.79048 | 0.020586 | 0.0077236 | 0.24058 | 0.046943 | 0.25427 | 0.38769 | 0.38485 | 0.039075 | 0.44755 | 0.14138 | 0.11396 | 0.44326 | 0.022071 | 0.013085 | 0.57657 | 0.050545 | 0.0049125 | 0.5979 | 0.0024587 | 0.00048595 | 0.48913 | 0.07601 | 0.050455
Aggregation | 0.0415 | 0.0056076 | 0.013548 | 0.06326 | 0.0076885 | 0.011949 | 0.0018592 | 0.013299 | 0.0086249 | 0.0028374 | 0.021276 | 0.0035776 | 0.001075 | 0.0049766 | 0.015091 | 0.00040414 | 0.0035281 | 0.0022168 | 0.0016809 | 0.00094564 | 0.00012497 | 0.0016345 | 0.00028807 | 0.00022107 | 0.030574 | 0.017902 | 0.07 | 0.0052389 | 0.012443 | 0.023795 | 0.026822 | 0.0034218 | 0.003248 | 0.031555 | 0.00017551 | 0.00016121 | 0.0024737 | 0.0025522 | 0.001606 | 0.0051404 | 0.00088455 | 3.7441e-05 | 0.015432 | 0.0067848 | 0.011014
Disaggregation | 0.27755 | 0.0067346 | 0.069609 | 0.32553 | 0.051663 | 0.021229 | 0.014791 | 0.0072669 | 0.015035 | 0.14416 | 0.0032564 | 0.024793 | 0.046498 | 0.034932 | 0.030725 | 0.033704 | 0.02056 | 0.0035673 | 0.059109 | 0.0015625 | 0.0016869 | 0.039187 | 0.010064 | 0.0017476 | 0.033972 | 0.066101 | 0.048381 | 0.15062 | 0.18468 | 0.0021809 | 0.35179 | 0.070959 | 0.083999 | 0.38391 | 0.011982 | 0.0069754 | 0.33149 | 0.005983 | 0.0029507 | 0.347 | 0.00071837 | 8.7377e-05 | 0.18138 | 0.034033 | 0.022355
Observation #1: Thresholding increases parent work and decreases child work
Observation #2: Thresholding decreases the overhead from launching, aggregation, and disaggregation
Observation #3: Coarsening decreases the overhead from launching and disaggregation

## Slide 28: Impact of Threshold and Aggregation Granularity
Observation #1: As the threshold increases initially, performance improves due to reduction in launches
Observation #2: For some benchmarks, increasing threshold too much degrades performance due to too much serialization
Observation #3: Different benchmarks perform best with different levels of aggregation granularity (including multi-block)

## Slide 29: Summary
We present a compiler framework for optimizing the use of dynamic parallelism on GPUs in applications with nested parallelism
The framework includes three key optimizations:
  Thresholding
  Coarsening
  Aggregation
Our evaluation shows that our compiler framework substantially improves performance of applications with nested parallelism that use dynamic parallelism
  43.0× faster than CDP.
  8.7× faster than No CDP
  3.6× faster than prior aggregation work (KLAP)

## Slide 30: Thank you! A Compiler Framework for Optimizing Dynamic Parallelism on GPUs
Mhd Ghaith Olabi1, Juan Gómez Luna2, Onur Mutlu2, Wen-mei Hwu3,4, Izzat El Hajj1
1American University of Beirut 2ETH Zurich 3NVIDIA 4University of Illinois at Urbana-Champaign
Contact: moo02@mail.aub.edu