## Slide 1
Jeremie S. Kim,
Damla Senol Cali, Hongyi Xin, Donghyuk Lee,
Saugata Ghose, Mohammed Alser, Hasan Hassan,
Oguz Ergin, Can Alkan, and Onur Mutlu
GRIM-Filter:
Fast seed location filtering in DNA read mapping
using processing-in-memory technologies
Notes: Hello, my name is Jeremie Kim and I will be presenting GRIM-Filter, fast seed location filtering in DNA read mapping using processing-in-memory technologies.
[CLICK]

## Slide 2
Genome Read Mapping is a very important problem and is the first step in genome analysis
Read Mapping is an approximate string matching problem
  Find the best fit of 100 character strings into a 3 billion character dictionary
  Alignment is currently the best method for determining the similarity between two strings, but is very expensive
We propose an algorithm called GRIM-Filter
  Accelerates read mapping by reducing the number of required alignments
  GRIM-Filter can be accelerated using processing-in-memory
    Adds simple logic into 3D-Stacked memory
    Uses high internal memory bandwidth to perform parallel filtering
GRIM-Filter with processing-in-memory delivers a 3.7x speedup
Executive Summary
Notes: Motivate filtering more

## Slide 3: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: Can skip this
[END]

## Slide 4: GRIM-Filter Outline
1. Motivation and Goal
2. Background Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 5: Motivation and Goal
Sequencing: determine the [A,C,G,T] series in DNA strand
Today’s machines sequence short strands (reads)
  Reads are on the order of 100 – 20k base pairs (bp)
  The human genome is approximately 3 billion bp
Therefore genomes are cut into reads, which are sequenced independently, and then reconstructed
  Read mapping is the first step in analyzing someone’s genome to detect predispositions to diseases, personalize medicine, etc.
Goal: We want to accelerate end-to-end performance of read mapping
Notes: [CLICK]
Sequencing refers to the process of determining the series of nucleotide base pairs in a DNA strand.
DNA is comprised of 4 different base pairs which are referred to as A,C,G, and T
[CLICK]
Today’s machines sequence short strands which are referred to as reads
[CLICK]
Reads are on the order of 100 – 20 THOUSAND base pairs long. The more commonly used sequencers result in 100-200 base pairs today, and sequencers that result in larger reads are expensive
[CLICK]
For some perspective, the human genome is approximately 3 billion base pairs long
[CLICK]
Therefore genomes are cut into reads, which are sequenced independently and then reconstructed.
[CLICK]
Read mapping is a very difficult and important problem
[CLICK]
It is the first step in analyzing someone’s genome to detect predispositions to diseases, personalize medicine, etc.
[CLICK]
Our goal is to accelerate end-to-end performance on read mapping
[END-CLICK]
##############################################################
//We present a case study of accelerating one of the most fundamental bioinformatics applications, read mapping, using 3D-stacked //DRAM, an emerging technology that enables processing-in-memory via a customizable logic layer embedded within the memory //arrays on top of extremely high bandwidth.
[CLICK]
Read mapping is a great candidate for acceleration using this emerging technology because it is compute and memory intensive.
[CLICK]
In this paper, we propose an implementation of read mapping using PIM for acceleration

## Slide 6: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 7: Background: Read Mappers
We now have sequenced reads and want a full genome
via Read Mapping
We map reads to a known reference genome (>99.9% similarity across humans) with some minor errors allowed
Because of high similarity, long sequences in reads
perfectly match in the reference genome
… G A C T G T G T C G A …
G A C T G T G T C A A
✔✔✔✔✔✔✔✔✔✘✔
We can use a hash table to help quickly map the reads!
Notes: [CLICK]
The purpose of a read mapper is to take a number of sequenced reads and reconstruct the full genome
[CLICK]
Thankfully we have a known reference genome that exhibits 99.9% similarity across humans (this is also generally true across any organisms of the same species). This enables us to map our reads to this known reference with some minor differences allowed, which then reduces read mapping to an approximate string matching problem. The differences are what makes each of us unique.
[CLICK]
Because the reference genome exhibits high similarity, long sequences in reads match the reference genome perfectly
[CLICK]
We see here that 9 sequential nucleotides, in the read of size 11, match perfectly to the reference genome
[CLICK]
This enables us to utilize a hash table to quickly reduce the search space for the read across the entire reference genome
[END-CLICK]

## Slide 8: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 9: Generating Hash Tables
To map any reads, generate a hash table per reference genome.
A A A A A
12 35 502 610 721 989
A A A A C
13 609 788
A A A A T
36 434
G G G G G
52 67 334 634 851
…
k-length sequences (k-mers)
Location list where k-mer occurs in the reference genome
@36: AAAAT
@434: AAAAT
We can query the table with substrings from reads
to quickly find a list of possible mapping locations
Notes: [CLICK]
Before mapping any reads, we generate a hash table once, which can be used to map any number of reads to the specific reference genome
[CLICK]
The keys in the hash table are k length sequences which are referred to as k-mers. And the values are lists of locations in the reference genome that the particular k-mer occurs. In this example, we see that the sequence of 5 A’s occurs in 6 locations
[CLICK]
We generate the key-value pair for every permutation of k-mers for the chosen value of k.
[CLICK]
To emphasize, we see that AAAAT occurs starting at the 36th and at the 434th base pairs of the reference genome
[CLICK]
we continue generating the hash table until all k-mer permutations are populated in the hash table
[CLICK]
We can query this hash table with substrings within the reads to quickly reduce the search space in the reference genome
[END-CLICK]

## Slide 10: Hash Tables in Read Mapping
Aligning
.
.
.
Mismatch
894
37
1564
140
1203
1564
894
1203
37
140
Hash Table
Read Sequence (100 bp)
✔
Reference Genome
140
1203
1564
We want to filter these out
so we do not waste time trying to align them
Aligning
.
.
.
Match!
Aligning
.
.
.
Mismatch
Aligning
.
.
.
Mismatch
Aligning
.
.
.
Mismatch
✘
✘
✘
✘
99.9% of locations
result in a mismatch
mrFAST spends 59% of its execution time performing sequence alignment on sequences that will be discarded
Notes: [CLICK]
Here I’ll show the process of using a hash table in read mapping for a single k-mer in a single read. Note that for every read, we must extract x+1 k-mers, where x is equal to the maximum number of allowable errors between a string match. This essentially guarantees that one of the k-mers WILL match perfectly in the reference genome.
[CLICK]
From any given read, we select k-mers and retrieve their location lists from the hash table
[CLICK]
We then retrieve the appropriate reference substring from the reference genome according to the location and the offset of the k-mer within the read
[CLICK]
We then compare each of these reference substrings against the read sequence using Alignment, an expensive dynamic programming algorithm. We note cases with clear mismatches should not waste compute resources via string comparison.
We also have to repeat this entire process for many many reads whose order can be approximated by dividing the genome length by the read sequence length. In the case of the human genome of length 3 billion and for 100 bp length read sequences, we will have at least 30 million reads
[CLICK]
Most locations we compare do not match the read. So, it is more efficient to build a filter that quickly identifies and discards such locations without doing the comparison to the reference genome
[END-CLICK]

## Slide 11: Location Filtering
Alignment is expensive and requires the use of O(n2) dynamic programming algorithm
  We need to align millions to billions of reads
  Modern read mappers reduce the time spent on alignment for increased performance. Can be done in two ways:
    Optimize the algorithm for alignment
    Reduce the number of alignments necessary by filtering out mismatches quickly
  Both methods are used by mappers today, but filtering has replaced alignment as the bottleneck [Xin+, BMC Genomics 2013]
Our goal is to accelerate read mapping
by improving the filtering step
Notes: [CLICK]
Alignment is the algorithm for determining a match between a read and a reference substring. This is very expensive and requires the use of an O(n2) dynamic programming algorithm.
[CLICK]
To give the scale of required computation, a single human can generate millions to billions of reads, and each read results in multiple locations
[CLICK]
Modern read mappers reduce the time spent on alignment for increased performance. This can be done in two ways:
[CLICK]
By further optimizing the alignment algorithm, which many prior works have done.. OR
[CLICK]
By reducing the number of alignments necessary by quickly discarding mismatches. We refer to this as filtering.
[CLICK]
Both methods are used by mappers today, but now filtering has replaced alignment as the bottleneck.
[CLICK]
Our goal is to improve the filtering step in read mappers
[END-CLICK]

## Slide 12: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 13: Hash Tables in Read Mapping
Filter
894
37
1564
140
1203
1564
894
1203
37
140
Hash Table
Read Sequence (100 bp)
✔
Reference Genome
140
1203
1564
Aligning
.
.
.
Match!
Aligning
.
.
.
Mismatch
✘
✘
✘
False Negative
✘
Notes: [CLICK]
Again, we split the read into k-mers of length 5 and query the hash table for their location lists
[CLICK]
We then pass the locations through the filter and attempt to efficiently discard as many locations as possible before having to run alignment. Here we see that locations that are obviously mismatches get discarded, before needing alignment.
[CLICK]
The read must then be aligned against the strings that pass the filter to determine location matches
[CLICK]
Any location that passes through the filter, but then fails the alignment is called a false negative. False negative rates and filtering speed are important metrics for analyzing a filter.
note that when the filter was added, we were able to forego 3 instances of alignment thus saving us execution time.
[END-CLICK]

## Slide 14: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 15: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 16: GRIM-Filter: Bins
We partition the genome into large sequences (bins).
… GGAAATACGTTCAGTCAGTTGGAAATACGTTTTGGGCGTTACTTCTCAGTACGTACAGTACAGTAAAAATGACAGTAAGAC …
Bin x - 3
Bin x - 2
Bin x - 1
Bin x
1
0
1
…
1
0
0
…
1
Bitvector
AAAAA
AAAAC
AAAAT
…
CCCCC
CCCCT
CCCCG
…
GGGGG
AAAAA exists in bin x
CCCCT doesn’t exist in bin x
  Represent each bin with a bitvector that holds the occurrence of all permutations of a small string (token) in the bin
  To account for matches that straddle bins, we employ overlapping bins
    A read will now always completely fall within a single bin
Notes: [CLICK]
We first partition the genome in large sequences that we refer to as bins
[CLICK]
[CLICK]
We show the genome with an arbitrary bin highlighted
[CLICK]
We then generate a bitvector that represents the bin and holds the occurrence of all permutations of a small string called a token in the bin
we see in the figure that tokens that exist in the bin are represented with a 1, and those not in the bin are a 0.
[CLICK]
so AAAAA exists in Bin x
and CCCCT does not exist in bin x
[CLICK]
to account for matches straddling two bins, we employ overlapping bins so that a read will now always fall within a single bin
[END-CLICK]

## Slide 17: GRIM-Filter: Bitvectors
  Reasonable memory footprint to hold pre-computed vectors which are generated per bin
    Only simple add/compare operations on vectors for likelihood
  At the cost of
    Lower approximate string matching accuracy
    Becoming a memory-bound process
… C G T G A G T C …
Bin x
0
…
…
…
…
…
Bin x Bitvector
AAAAA
…
CGTGA
…
TGAGT
…
GAGTC
…
GTGAG
…
C G T G A
G T G A G
T G A G T
G A G T C
1
0
0
0
0
1
1
1

## Slide 18: GRIM-Filter: Bitvectors
Storing all bitvectors
requires bits
in memory,
where t = number of bins.
For bin size ~200, and n = 5,
memory footprint
~3.8 GB
AAAAA
AAAAC
AAAAG
AAAAT
.
CCCCT
.
.
.
.
GCATG
.
TTGCA
.
TTTTT
1
1
0
0
.
1
.
.
.
.
1
.
1
.
0
0
1
0
.
1
.
1
.
1
.
1
.
.
.
0
AAAAA
AAAAC
AAAAG
.
AGAAA
.
GAAAA
.
GACAG
.
GCATG
.
.
.
TTTTT
  
b1
b2
tokens
Notes: We use bitvectors to quicly figure out existence within a bin
Don’t talk about top text
We see here a list of bit vectors that are associated with a particular bin. The memory required to store all bit vectors is found by multiplying the number of bins by 4^q bits (which is the size of the bit vectors)
For a bin size of 200 and a q of 5, the memory footprint comes to around 3.8 GB
[END-CLICK]

## Slide 19: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 20: GRIM-Filter: Checking a Bin
TTGGA
GAACT
AACTT
ACTTG
CTTGG
INPUT: Read Sequence r
GAACTTGGAGTCTA CGAG
...
Read bitvector for bin_num(x)
...
1
+
≥ Threshold?
Send to
Read Mapper for Sequence Alignment
tokens
Discard
NO
YES
Sum
How GRIM-Filter determines whether to discard potential match locations in a given bin prior to alignment
3
2
4
5
1
0
1
0
1
1
1
0
0
.
.
.
.
.
.
Get tokens
Match tokens to bitvector
Compare
Notes: Talk about why GRIM-Filter is faster than alignment. This is obviously faster than dynamic programming.
This threshold value changes error tolerance
In this example, we will use a token size of 5
We show how GRIM-Filter determines the need for alignment in a bin X. We use the read to generate a mask to selectively sum bit vectors.
[CLICK]
For the given read sequence in red, we find all indices corresponding to the q-grams found in the read.
[CLICK]
We then query and [CLICK] sum the bits of bin X’s pre-computed bit vector of the reference genome.
This final value is then compared to a threshold to determine the likelihood of this read’s existence in Bin X
These are all very simple operations and can be run in parallel across different bins
[END-CLICK]

## Slide 21: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 22: GRIM-Filter: Error Tolerance
one substitution error affects four tokens when n = 4
Threshold = read_length – (n–1) –
n × read_length × e
number of errors allowed per read
maximum number of tokens that could contain errors
total number of tokens in a read
tokens affected by the error
single substitution error
More details in the paper
GRIM-Filter can support different error tolerances by simply changing the threshold value
Notes: REWRITE
MOVE THIS TO BACKUP MAYBE
In this example, we will use a token size of 5
We show how GRIM-Filter determines the need for alignment in a bin X. We use the read to generate a mask to selectively sum bit vectors.
[CLICK]
For the given read sequence in red, we find all indices corresponding to the q-grams found in the read.
[CLICK]
We then query and [CLICK] sum the bits of bin X’s pre-computed bit vector of the reference genome.
This final value is then compared to a threshold to determine the likelihood of this read’s existence in Bin X
These are all very simple operations and can be run in parallel across different bins
[END-CLICK]

## Slide 23: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 24: Integrating GRIM-Filter into a Read Mapper
GRIM-Filter: Seed Location Checker
0001010 011010
...
...
...
GAACTTGCGAG GTATT
...
INPUT: Read Sequence
GRIM-Filter:
Filter Bitmask Generator
Seed Location Filter Bitmask
0001010 011010
...
...
...
020128
020131
414415
...
...
...
...
KEEP
x
DISCARD
KEEP
INPUT: All Potential Seed Locations
Read Mapper: Sequence Alignment
Reference Segment Storage
Edit-Distance Calculation
reference segment @ 020131
reference segment @ 414415
. . .
OUTPUT: Correct Mappings
1
2
4
3
Notes: REWRITE
In this example, we will use a token size of 5
We show how GRIM-Filter determines the need for alignment in a bin X. We use the read to generate a mask to selectively sum bit vectors.
[CLICK]
For the given read sequence in red, we find all indices corresponding to the q-grams found in the read.
[CLICK]
We then query and [CLICK] sum the bits of bin X’s pre-computed bit vector of the reference genome.
This final value is then compared to a threshold to determine the likelihood of this read’s existence in Bin X
These are all very simple operations and can be run in parallel across different bins
[END-CLICK]

## Slide 25: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 26: Key Properties of GRIM-Filter
Simple Operations:
  To check a given bin, find the sum of all bits corresponding to each token in the read
  Compare against threshold to determine whether to align
Highly Parallel: Each bin is operated on independently and there are many many bins
Memory Bound: Given the frequent accesses to the large bitvectors, we find that GRIM-Filter is memory bound
These properties together make GRIM-Filter a good algorithm to be run in 3D-Stacked DRAM
Notes: As a recap,
[CLICK]
GRIM-Filter is comprised of very simple addition/comparison operations
[CLICK]
To check a given bin, we sum the bits corresponding to each token in the read
[CLICK]
and then we compare the sum against a threshold to determine whether we need to align
[CLICK]
It is also highly parallel
each bin is operated on independently and there are many many bins
[CLICK]
These three properties together make it a suitable algorithm to be run in 3D stacked DRAM
[END-CLICK]

## Slide 27: 3D-Stacked Memory
3D-Stacked DRAM architecture has extremely high bandwidth as well as a stacked customizable logic layer
  Logic Layer enables Processing-in-Memory, offloading computation to this layer and alleviating the memory bus
  Embed GRIM-Filter operations into DRAM logic layer and appropriately distribute bitvectors throughout memory
Memory Array
Customized Logic
DRAM Layers
Logic Layer
TSVs
Notes: THICKEN TSV lines
[CLICK]
3D stacked memory stacks a logic layer and DRAM layers with vertical connections called TSVs. This vertical structure allows for a much higher number of connections increasing the available bandwidth. The customizable logic layer enables processing-in-memory, which avoids overloading the memory bus by offloading computation to this layer in the 3D stacked module.
We can design the simple operations required for GRIM-Filter into the customizable logic layer and appropriately distribute the bitvectors to enable an efficient filter
[CLICK]
Real 3D-stacked DRAM technologies are commercially available now such as high bandwidth memory
[CLICK]
And micron’s hybrid memory cube, among others
[END-CLICK]

## Slide 28: 3D-Stacked Memory
3D-Stacked DRAM architecture has extremely high bandwidth as well as a stacked customizable logic layer
  Logic Layer enables Processing in Memory, offloading computation to this layer and alleviating the memory bus
  Embed GRIM-Filter operations into DRAM logic layer and appropriately distribute bitvectors throughout memory
Memory Array
Customized Logic
http://i1-news.softpedia-static.com/images/news2/Micron-and-Samsung-Join-Force-to-Create-Next-Gen-Hybrid-Memory-2.png
Notes: [CLICK]
3D stacked memory stacks a logic layer and DRAM layers with vertical connections called TSVs. This vertical structure allows for a much higher number of connections increasing the available bandwidth. The customizable logic layer allows for processing-in-memory, which avoids overloading the memory bus by offloading computation to this layer in the 3D stacked module.
We can design the simple operations required for GRIM-Filter into the customizable logic layer and appropriately distribute the bit vectors to enable an efficient filter
[CLICK]
Real 3D-stacked DRAM technologies are commercially available now such as high bandwidth memory
[CLICK]
And micron’s hybrid memory cube, among others
[END-CLICK]

## Slide 29: 3D-Stacked Memory
3D-stacked DRAM architecture has extremely high bandwidth as well as a stacked customizable logic layer
  Logic Layer enables Processing in Memory, offloading computation to this layer and alleviating the memory bus
  Embed GRIM-Filter operations into DRAM logic layer and appropriately distribute bitvectors throughout memory
Memory Array
Customized Logic
http://i1-news.softpedia-static.com/images/news2/Micron-and-Samsung-Join-Force-to-Create-Next-Gen-Hybrid-Memory-2.png
http://images.anandtech.com/doci/9266/HBMCar_678x452.jpg
Notes: [CLICK]
3D stacked memory stacks a logic layer and DRAM layers with vertical connections called TSVs. This vertical structure allows for a much higher number of connections increasing the available bandwidth. The customizable logic layer allows for processing-in-memory, which avoids overloading the memory bus by offloading computation to this layer in the 3D stacked module.
We can design the simple operations required for GRIM-Filter into the customizable logic layer and appropriately distribute the bit vectors to enable an efficient filter
[CLICK]
Real 3D-stacked DRAM technologies are commercially available now such as high bandwidth memory
[CLICK]
And micron’s hybrid memory cube, among others
[END-CLICK]

## Slide 30: GRIM-Filter in 3D-Stacked DRAM
Each DRAM layer is organized as an array of banks
  A bank is an array of cells with a row buffer to transfer data
The layout of bitvectors in a bank enables filtering many bins in parallel
Notes: [CLICK]
Each DRAM layer is organized as an array of Banks
[CLICK]
and a bank is an array of cells with a row buffer. The row buffer holds one row at a time and uses this structure to transfer data with high bandwidth into the logic layer via TSVs
[CLICK]
We now show the distribution of bit vectors across the DRAM arrays to enable parallel processing of many bins.
[CLICK]
Each row represents a token's occurrence across many sequential bins. and the row of the appropriate token gets queried to find a vector showing the occurrence of the token across many bins.
These are the vectors are brought down into the logic layer to be operated on.
[CLICK]
[END-CLICK]

## Slide 31: GRIM-Filter in 3D-Stacked DRAM
Customized logic for accumulation and comparison per genome segment
  Low area overhead, simple implementation
  For HBM2, we use 4096 incrementer LUTs, 7-bit counters, and comparators in logic layer
Details are in the paper
Notes: [CLICK]
We now look at the implementation of logic in the logic layer
[CLICK]
GRIM-Filter only requires a very simple design for enabling the bitvector sum and threshold compare across many bins simultaneously. One comparator, incrementer, accumulator, and buffer for each bin that we are checking in parallel
[CLICK]
This results in a very low area overhead and ease of implementation
[END-CLICK]

## Slide 32: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 33: Methodology
Performance simulated using an in-house 3D-Stacked DRAM simulator
Evaluate 10 real read data sets (From the 1000 Genomes Project)
  Each data set consists of 4 million reads of length 100
Evaluate two key metrics
  Performance
  False negative rate
    The fraction of locations that pass the filter but result in a mismatch
  Compare against a state-of-the-art filter, FastHASH [Xin+, BMC Genomics 2013] when using mrFAST, but GRIM-Filter can be used with ANY read mapper

## Slide 34: GRIM-Filter Performance
2.1x average performance benefit
1.8x-3.7x performance benefit across real data sets
Chart: 
| ERR240726-1 | ERR240726-2 | ERR240727-1 | ERR240727-2 | ERR240728-1 | ERR240728-2 | ERR240729-1 | ERR240729-2 | ERR240730-1 | ERR240730-2 | Average
FastHASH | 37.7881 | 47.2858 | 26.4744 | 29.611 | 26.3053 | 28.5216 | 26.3319 | 27.6094 | 63.5181 | 27.748 | 34.1194
GRIM-3D | 15.2292 | 19.6862 | 14.5846 | 17.6976 | 14.573 | 17.0455 | 14.6994 | 15.4576 | 17.3955 | 15.7755 | 16.2144
e = 0.05
Sequence Alignment Error Tolerance (e)
Time (×1000 seconds)
FastHASH filter
GRIM-Filter
Benchmarks and their Execution Times
GRIM-Filter gets performance due to its hardware-software co-design
Notes: We ran 10 separate experiments with real read data sets, consisting of approximately 4 million reads each, and got the following results. Compared to the previous best filter, our filter enjoys a 2x average end-to-end read mapper performance gain across the data sets, and a 6x average lower false negative rate. Again, these are the locations that were not discarded by the filter, but were then later discarded after alignment

## Slide 35: GRIM-Filter False Negative Rate
6.0x average reduction in False Negative Rate
5.6x-6.4x False Negative reduction across real data sets
False Negative Rate
e = 0.05
FastHASH filter
GRIM-Filter
Chart: 
| ERR240726-1 | ERR240726-2 | ERR240727-1 | ERR240727-2 | ERR240728-1 | ERR240728-2 | ERR240729-1 | ERR240729-2 | ERR240730-1 | ERR240730-2 | Average
FastHASH | 0.40191 | 0.38648 | 0.40237 | 0.38943 | 0.40263 | 0.38846 | 0.40149 | 0.3892 | 0.40136 | 0.38925 | 0.39526
GRIM-3D | 0.066592 | 0.067988 | 0.063272 | 0.067891 | 0.064197 | 0.069488 | 0.066264 | 0.066911 | 0.062599 | 0.067789 | 0.066299
Benchmarks and their False Negative Rates
Sequence Alignment Error Tolerance (e)
GRIM-Filter utilizes more information available in the read to filter
Notes: We ran 10 separate experiments with real read data sets, consisting of approximately 4 million reads each, and got the following results. Compared to the previous best filter, our filter enjoys a 2x average end-to-end read mapper performance gain across the data sets, and a 6x average lower false negative rate. Again, these are the locations that were not discarded by the filter, but were then later discarded after alignment

## Slide 36: Other Results in the Paper
Sensitivity of execution time and false negative rates to error tolerance of string matching
Read mapper execution time breakdown
Sensitivity studies on the filter
  Token Size
  Bin Size
  Error Tolerance
Notes: Summarize these bullet points

## Slide 37: GRIM-Filter Outline
1. Motivation and Goal
2. Background: Read Mappers
4. Mapping GRIM-Filter to 3D-Stacked Memory
5. Results
3. Our Proposal: GRIM-Filter
6. Conclusion
a. Hash Table Based
b. Hash Table Based with Filter
Notes: [END]

## Slide 38: Conclusion
We propose an in-memory filtering algorithm to accelerate end-to-end read mapping by reducing the number of required alignments
Key ideas:
Introduce a new representation of coarse-grained segments of the reference genome
Use massively-parallel in-memory operations to identify read presence within each coarse-grained segment
Key contributions and results:
Customized filtering algorithm for 3D-Stacked DRAM
Compared to the previous best filter
  We observed 1.8x-3.7x read mapping speedup
  We observed 5.6x-6.4x fewer false negatives
GRIM-Filter is a universal filter that can be applied to any read mapper
Notes: [CLICK]
We propose an in-memory filter to accelerate read mapping
[CLICK]
Compared to the previous best filter we show up to 3.7x end-to-end speedup on the same mapper and
We also observe on average 6x fewer false negatives
[CLICK]
GRIM-Filter is a universal filter that can be applied to any read mapper and we hope these results encourage people to use processing in memory to improve other data intensive algorithms
[END-CLICK]

## Slide 39
Jeremie S. Kim,
Damla Senol Cali, Hongyi Xin, Donghyuk Lee,
Saugata Ghose, Mohammed Alser, Hasan Hassan,
Oguz Ergin, Can Alkan, and Onur Mutlu
GRIM-Filter:
Fast seed location filtering in DNA read mapping
using processing-in-memory technologies
Notes: Hello, my name is Jeremie Kim and I will be presenting GRIM-Filter, fast seed location filtering in DNA read mapping using processing-in-memory technologies.
[CLICK]
ANTICIPATE QUESTIONS
READ MAPPERS , FPGA, GPUs,
SHD? SIMD
Etc.
How PIM is working here. Quick summary of the steps

## Slide 45: GRIM-Filter: Error Tolerance
one substitution error affects four tokens when n = 4
Threshold = read_length – (n–1) –
n × read_length × e
number of errors allowed per read
maximum number of tokens that could contain errors
total number of tokens in a read
tokens affected by the error
single substitution error
More details in the paper
GRIM-Filter can support different error tolerances by simply changing the threshold value
Notes: REWRITE
MOVE THIS TO BACKUP MAYBE
In this example, we will use a token size of 5
We show how GRIM-Filter determines the need for alignment in a bin X. We use the read to generate a mask to selectively sum bit vectors.
[CLICK]
For the given read sequence in red, we find all indices corresponding to the q-grams found in the read.
[CLICK]
We then query and [CLICK] sum the bits of bin X’s pre-computed bit vector of the reference genome.
This final value is then compared to a threshold to determine the likelihood of this read’s existence in Bin X
These are all very simple operations and can be run in parallel across different bins
[END-CLICK]