## Slide 1
GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping
using Emerging Memory Technologies
Jeremie Kim1, Damla Senol1, Hongyi Xin1, Donghyuk Lee1, Saugata Ghose1, Mohammed Alser2, Hasan Hassan4,3,
Oguz Ergin3, Can Alkan2 and Onur Mutlu4,1
8: GRIM-Filter Walkthrough
9: Results & Conclusion
Baseline: mrFAST with FastHASH mapper code [Xin+, BMC Genomics 2013]. However, GRIM-Filter is fully complementary to other mappers, too.
Key Results of GRIM-Filter:
5.59x-6.41x less false negative locations, and
1.81x-3.65x end-to-end speedup over the state-of-the-art read mapper mrFAST with FastHASH.
We show the inherent parallelism of our filter and ease of implementation for 3D-stacked memory. There is great promise in adapting DNA read mapping algorithms to state-of-the-art and emerging memory and processing technologies.
Other Results:
Examined sensitivity to number of bins: 450x65536
Examined sensitivity to q-gram size: 5
Found to be the best tradeoff between memory consumption, filtering efficiency, and runtime.
*In the figures shown, smaller bars indicate better performance
5: 3D-Stacked Logic-in-Memory DRAM
Design and implement a new filter that rejects incorrect mappings before the alignment step
  Minimize the occurrences of unnecessary alignment
  Maintain high sensitivity and comprehensiveness
  Obtain low runtime and low false positive rate
  Accelerate read mapping by overcoming memory bottleneck with 3D-stacked memory and its PIM for data-intensive computation
  Very fast parallel operations on big data sets near memory
1: Read Mapping
Recent technology that tightly couples memory and logic vertically with very high bandwidth connectors.
Numerous Through Silicon Vias (TSVs) connecting layers, enable higher bandwidth and lower latency and energy consumption.
Customizable logic layer for application-specific accelerators.
Logic layer enables fast, massively parallel operations on large sets of data, and provides the ability to run these operations near memory to alleviate the memory bottleneck.
Processing in 3D-stacked memory is extremely good at accelerating embarrassingly parallel simple bit operations.
3: Problem
Read Mapping: Mapping billions of DNA fragments (reads) against a reference genome to identify genomic variants
Requires approximate string matching
Computationally expensive alignment using quadratic-time dynamic programming algorithm
Bottlenecked by memory bandwidth
Three general types of read mappers:
Suffix-array based mappers
Hash table based mappers
Hybrid
2: Hash Table Based Mappers
Seed-and-extend procedure to map reads against a reference genome allowing e indels. They have:
High sensitivity (can tolerate many errors)
High comprehensiveness (can find more mappings)
BUT
Low speed
The most recent fastest hash table based read mapper, mrFAST with FastHASH [Xin+, BMC Genomics 2013]
4: Our Goal
For lower runtimes, location filters can efficiently determine whether a candidate mapping location will result in an incorrect mapping before performing the computationally expensive incorrect verification by alignment. They should be fast.
6: GRIM-Filter Mechanism
GRIM-Filter is based on two key ideas:
Introduce parallelism to q-gram string matching
Utilize a 3D-stacked DRAM to alleviates the memory bandwidth issue of our algorithm and parallelizes most of the filter.
GRIM-Filter has two main steps:
Precomputation: Divide the reference genome into consecutive bins and generate existence bitvectors for each bin.
Filtering Algorithm: Filter locations by quickly determining whether a read can map to a specific segment of the genome.
Runtimes for GRIM-Filter as error threshold varies
7: Bins & Bitvectors
False Negative Rates for GRIM-Filter as error threshold varies
Existence bitvectors represent the existence of all possible permutations of q-length nucleotide sequences in each bin.
Bitvectors are distributed throughout the memory layers of 3D-stacked DRAM on top of the customized logic layer, which enables processing-in-memory and high parallelism.
Memory Array
Customized Logic
http://www.amd.com/en-us/innovations/software-technologies/hbm
1
2
3
4