## Slide 1: GenASM: A High Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis
Damla Senol Cali1
Carnegie Mellon University
(dsenol@andrew.cmu.edu)
Gurpreet S. Kalsi2, Zulal Bingol3, Can Firtina4, Lavanya Subramanian2,
Jeremie Kim1,4, Rachata Ausavarungnirun5,1, Mohammed Alser4,
Juan Gomez-Luna4, Amirali Boroumand1, Anant Nori2, Allison Scibisz1,
Sreenivas Subramoney2, Can Alkan3, Saugata Ghose6,1, and Onur Mutlu4,1,3
1 2 3 4
5 6 1,4
Notes: Hello I am Damla.
I will introduce GenASM

## Slide 2: Genome Sequence Analysis (GSA)
Read mapping: First key step in genome sequence analysis (GSA)
  Aligns reads to one or more possible locations within the reference genome, and
  Finds the matches and differences between the read and the reference genome segment at that location
Multiple steps of read mapping require approximate string matching
  Approximate string matching (ASM) enables read mapping to account for sequencing errors and genetic variations in the reads
Bottlenecked by the computational power and memory bandwidth limitations of existing systems
Notes: [CLICK] Read mapping is the first key step in genome sequence analysis, where we align each read to the reference genome.
[CLICK] Multiple steps of read mapping require approximate string matching (ASM) to account for the sequencing errors and genetic variations.
[CLICK] However, it is currently bottlenecked by the computational power and memory bandwidth limitations of existing systems.

## Slide 3: GenASM: ASM Framework for GSA
GenASM: First ASM acceleration framework for GSA
  Based upon the Bitap algorithm
    Uses fast and simple bitwise operations to perform ASM
  Modified and extended ASM algorithm
    Highly-parallel Bitap with long read support
    Bitvector-based novel algorithm to perform traceback
  Co-design of our modified scalable and memory-efficient algorithms with low-power and area-efficient hardware accelerators
Our Goal:
Accelerate approximate string matching
by designing a fast and flexible framework,
which can accelerate multiple steps of genome sequence analysis
Notes: [CLICK] our goal is to design a fast and flexible framework, which can accelerate multiple steps of genome sequence analysis (GSA).
[CLICK] We propose GenASM and
[CLICK] We base GenASM on Bitap, an ASM algorithm that uses only fast and simple bitwise operations, making it amenable to efficient hardware acceleration.
[CLICK] We modify Bitap to support long reads and to enable parallelization. We also develop a novel Bitap-compatible algorithm for traceback
[CLICK] And, we co-design specialized hardware for both algorithms.

## Slide 4: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC
Accelerator
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-TB
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Notes: Our co-designed hardware consists of two components: GenASM-DC and GenASM-TB.

## Slide 5: Use Cases of GenASM
Read Alignment Step of Read Mapping
  Find the optimal alignment of how reads map to candidate reference regions
Pre-Alignment Filtering for Short Reads
  Quickly identify and filter out the unlikely candidate reference regions for each read
Edit Distance Calculation
  Measure the similarity or distance between two sequences
We also discuss other possible use cases of GenASM in our paper:
  Read-to-read overlap finding, hash-table based indexing, whole genome alignment, generic text search
Notes: GenASM is flexible and can be used for a number of use cases.
In this work, we evaluate three use cases in detail: read alignment, pre-alignment filtering and edit distance calculation.
In our paper, we also briefly discuss several others.

## Slide 6: Key Results
Read Alignment
116× speedup, 37× less power than Minimap2 (state-of-the-art SW)
111× speedup, 33× less power than BWA-MEM (state-of-the-art SW)
3.9× better throughput, 2.7× less power than Darwin (state-of-the-art HW)
1.9× better throughput, 82% less logic power than GenAx (state-of-the-art HW)
Pre-Alignment Filtering
3.7× speedup, 1.7× less power than Shouji (state-of-the-art HW)
Edit Distance Calculation
22–12501× speedup, 548–582× less power than Edlib (state-of-the-art SW)
9.3–400× speedup, 67× less power than ASAP (state-of-the-art HW)
Notes: We find that, for all the three use cases, GenASM is significantly more efficient in terms of both speed and power consumption than state-of-the-art software and hardware baselines

## Slide 7: GenASM: A High Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis
Damla Senol Cali1
Carnegie Mellon University
(dsenol@andrew.cmu.edu)
Gurpreet S. Kalsi2, Zulal Bingol3, Can Firtina4, Lavanya Subramanian2,
Jeremie Kim1,4, Rachata Ausavarungnirun5,1, Mohammed Alser4,
Juan Gomez-Luna4, Amirali Boroumand1, Anant Nori2, Allison Scibisz1,
Sreenivas Subramoney2, Can Alkan3, Saugata Ghose6,1, and Onur Mutlu4,1,3
1 2 3 4
5 6 1,4
Notes: Thank you!