## Slide 1: GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis
Damla Senol Cali
Carnegie Mellon University
(dsenol@andrew.cmu.edu)
Gurpreet S. Kalsi2, Zulal Bingol3, Can Firtina4, Lavanya Subramanian5,
Jeremie Kim1,4, Rachata Ausavarungnirun6,1, Mohammed Alser4,
Juan Gomez-Luna4, Amirali Boroumand1, Anant Nori2, Allison Scibisz1,
Sreenivas Subramoney2, Can Alkan3, Saugata Ghose7,1, and Onur Mutlu4,1,3
1 2 3 4
5 6 7 1,4
Notes: Hello, I am Damla Senol Cali. Today, I'll be presenting our work "GenASM: A High Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis".

## Slide 2: Genome Sequencing
Genome sequencing: Enables us to determine the order of the DNA sequence in an organism’s genome
  Plays a pivotal role in:
    Personalized medicine
    Outbreak tracing
    Understanding of evolution
Modern genome sequencing machines extract smaller randomized fragments of the original DNA sequence, known as reads
  Short reads: a few hundred base pairs, error rate of ∼0.1%
  Long reads: thousands to millions of base pairs, error rate of 10–15%
Notes: [CLICK] Genome sequencing, which enables us to determine the DNA sequence of an organism, [CLICK] plays a pivotal role in areas such as personalized medicine, outbreak tracing (like COVID-19), and the understanding of evolution.
[CLICK] Modern genome sequencing machines extract small randomized fragments of the original DNA sequence, which we call reads.
[CLICK] State-of-the-art sequencing machines produce either short reads or long reads

## Slide 3: Genome Sequence Analysis
Read mapping: First key step in genome sequence analysis (GSA)
  Aligns reads to one or more possible locations within the reference genome, and
  Finds the matches and differences between the read and the reference genome segment at that location
Multiple steps of read mapping require approximate string matching
  Approximate string matching (ASM) enables read mapping to account for sequencing errors and genetic variations in the reads
Bottlenecked by the computational power and memory bandwidth limitations of existing systems
Notes: [CLICK] Read mapping is the first key step in genome sequence analysis, [CLICK] where we align each read to one or more possible locations within the reference genome, and find the matches and differences between the read and the reference genome segment at that location.
[CLICK] Multiple steps of read mapping must account for the sequencing errors, and for the differences caused by genetic variations. As a result, read mapping must perform approximate string matching (ASM).
[CLICK] However, it is currently bottlenecked by the computational power and memory bandwidth limitations of existing systems.

## Slide 4: GenASM: ASM Framework for GSA
GenASM: First ASM acceleration framework for GSA
  Based upon the Bitap algorithm
    Uses fast and simple bitwise operations to perform ASM
  Modified and extended ASM algorithm
    Highly-parallel Bitap with long read support
    Bitvector-based novel algorithm to perform traceback
  Co-design of our modified scalable and memory-efficient algorithms with low-power and area-efficient hardware accelerators
Our Goal:
Accelerate approximate string matching
by designing a fast and flexible framework,
which can accelerate multiple steps of genome sequence analysis
Notes: [CLICK] Our goal in this work is to design a fast and flexible framework for both short and long reads, which can accelerate multiple steps of genome sequence analysis (GSA).
[CLICK] To this end, we propose GenASM
[CLICK] We base GenASM on Bitap, an ASM algorithm that uses only fast and simple bitwise operations, making it amenable to efficient hardware acceleration. To our knowledge, GenASM is the first work that enhances and accelerates Bitap, and also it is the first ASM acceleration framework for genome sequence analysis.
[CLICK] We modify Bitap to support long reads and to enable parallelization.
We also develop a novel Bitap-compatible algorithm for traceback, which uses information collected during ASM about the different types of errors to identify the optimal alignment of reads.
[CLICK] And, we co-design specialized, low-power and area-efficient hardware for both algorithms.

## Slide 5: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-DC
Accelerator
GenASM-TB
Accelerator
GenASM-DC
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Notes: Our co-designed hardware consists of two components:
(1) GenASM-DC, which provides hardware support to efficiently execute our modified Bitap algorithm to perform distance calculation; and
(2) GenASM-TB, which provides hardware support to efficiently execute our novel traceback algorithm to find the optimal alignment.
GenASM also has two types of SRAM buffers:
DC-SRAM, and
TB-SRAMs

## Slide 6: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-DC
Accelerator
GenASM-TB
Accelerator
GenASM-DC
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Our specialized compute units and on-chip SRAMs help us to:
Match the rate of computation with memory capacity and bandwidth
Achieve high performance and power efficiency
Scale linearly in performance with the number of parallel compute units that we add to the system
Notes: Our specialized compute units and on-chip SRAMs help us to:
[CLICK] (1) Match the rate of computation with memory capacity and bandwidth
[CLICK] (2) Achieve high performance and power efficiency
[CLICK] (3) Scale linearly in performance with the number of parallel compute units that we add to the system

## Slide 7: GenASM-DC: Hardware Design
Linear cyclic systolic array based accelerator
  Designed to maximize parallelism and minimize memory bandwidth and memory footprint
Processing Block (PB)
Processing Core (PC)
Notes: [CLICK] We implement GenASM-DC as a linear cyclic systolic array based accelerator, using small and very simple logic components.
[CLICK] This design helps us to maximize parallelism and minimize memory BW and footprint.
[CLICK] Processing Core is the basic compute component which computes the intermediate bitvectors
[CLICK] and when we add the flip-flop-based storage logic around Processing Core, we define a Processing Element (PE)
[CLICK] Multiple PEs are concatenated to define a Processing Block
[CLICK] We also have DC-SRAM, which stores the reference text, the pattern bitmasks for the query read, and the intermediate data generated from PEs, and we also have
[CLICK] TB-SRAMs, which store the intermediate bitvectors generated by each PE of GenASM-DC for later use by GenASM-TB.

## Slide 8: GenASM-TB: Hardware Design
Bitwise Comparisons
CIGAR string
Last CIGAR
<<
match
CIGAR
out
1
2
.
.
64
192
insertion
deletion
subs
64
64
64
64
1
2
Next Rd Addr Compute
3
GenASM-TB
Very simple logic:
  ❶Reads the bitvectors from one of the TB-SRAMs using the computed address
  ❷Performs the required bitwise comparisons to find the traceback output for the current position
  ❸Computes the next TB-SRAM address to read the new set of bitvectors
Bitwise Comparisons
CIGAR string
Last CIGAR
<<
match
CIGAR
out
1
2
.
.
64
192
insertion
deletion
subs
64
64
64
64
to main
memory
1
2
Next Rd Addr Compute
3
1.5KB
TB-SRAM1
1.5KB
TB-SRAM2
1.5KB
TB-SRAM64
1
2
3
Notes: [CLICK] We implement GenASM-TB hardware using very simple logic, which
[CLICK] 1) reads the bitvectors from one of the TB-SRAMs using the computed address,
[CLICK] 2) performs the required bitwise comparisons to find the traceback output for the current position, and
[CLICK] 3) computes the next TB-SRAM address to read the new set of bitvectors.
After GenASM-TB finds the complete traceback output, [CLICK] it writes this output to main memory and completes its execution.

## Slide 9: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  Total (1 vault): 0.334 mm2 0.101 W
  Total (32 vaults): 10.69 mm2 3.23 W
  % of a Xeon CPU core: 1% 1%
Notes: [CLICK] We synthesize our DC and TB accelerator datapaths with a typical 28nm low-power process:
[CLICK] Both accelerators operates at 1GHz.
[CLICK] We find that for 32 GenASM accelerator (one for each HMC vault), total area overhead is ten point sixty nine millimeter square and total power consumption is three point twenty-three watts.
We observe that both area and power consumption of GenASM (at 1 vault) is around 1% of the area and power consumption of a single Xeon CPU core.

## Slide 10: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  GenASM has low area and power overheads
Notes: Thus, GenASM has low area and power overheads.

## Slide 11: Use Cases of GenASM
Indexing
Seeding
Pre-Alignment Filtering
Read Alignment
Reference genome
Hash table based index
Candidate mapping locations
Optimal alignment
Reads from sequenced genome
Remaining candidate mapping locations
Indexing
Seeding
Notes: GenASM is flexible and can be used for a number of use cases.
In this work, we evaluate three of them in detail and two of them are from the read mapping pipeline:
Pre-alignment filtering and read alignment

## Slide 12: Use Cases of GenASM (cont’d.)
Read Alignment Step of Read Mapping
  Find the optimal alignment of how reads map to candidate reference regions
Pre-Alignment Filtering for Short Reads
  Quickly identify and filter out the unlikely candidate reference regions for each read
Edit Distance Calculation
  Measure the similarity or distance between two sequences
We also discuss other possible use cases of GenASM in our paper:
  Read-to-read overlap finding, hash-table based indexing, whole genome alignment, generic text search
Notes: [CLICK] (1) read alignment
is the most time consuming step of read mapping that we align each read to all of its candidate reference regions and then find the optimal alignment.
[CLICK] (2) in pre-alignment filtering for short reads,
we aim to quickly identify and filter out the unlikely candidate reference regions of each read by approximating the edit distance between them and filter out if it is above a threshold.
[CLICK] And our third use case is edit distance calculation
Which is one of the fundamental operations in genomics that measures the similarity or distance btw two sequences
In our paper, we also briefly discuss several other use cases such as generic text search

## Slide 13: Key Results
Read Alignment
116× speedup, 37× less power than Minimap2 (state-of-the-art SW)
111× speedup, 33× less power than BWA-MEM (state-of-the-art SW)
3.9× better throughput, 2.7× less power than Darwin (state-of-the-art HW)
1.9× better throughput, 82% less logic power than GenAx (state-of-the-art HW)
Pre-Alignment Filtering
3.7× speedup, 1.7× less power than Shouji (state-of-the-art HW)
Edit Distance Calculation
22–12501× speedup, 548–582× less power than Edlib (state-of-the-art SW)
9.3–400× speedup, 67× less power than ASAP (state-of-the-art HW)
Notes: We find that, for all the three use cases, GenASM is significantly more efficient in terms of both speed and power consumption than state-of-the-art software and hardware baselines

## Slide 14: GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis
Damla Senol Cali
Carnegie Mellon University
(dsenol@andrew.cmu.edu)
Gurpreet S. Kalsi2, Zulal Bingol3, Can Firtina4, Lavanya Subramanian5,
Jeremie Kim1,4, Rachata Ausavarungnirun6,1, Mohammed Alser4,
Juan Gomez-Luna4, Amirali Boroumand1, Anant Nori2, Allison Scibisz1,
Sreenivas Subramoney2, Can Alkan3, Saugata Ghose7,1, and Onur Mutlu4,1,3
1 2 3 4
5 6 7 1,4
Notes: Thank you!