## Slide 1: GenPIP In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina,
Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, Onur Mutlu
Notes: Good Morning, everyone, I am Haiyu Mao, a postdoc researcher in SAFARI research group at ETH. Today, I am gonna present our work, GenPIP.

## Slide 2: Overview: Genome Analysis
Genome analysis: Enables us to determine the order of the DNA sequence in an organism’s genome
  Plays an important role in
    Personalized medicine
    Outbreak tracing
    Understanding of evolution
    …
ONT sequencing device [forbes.com]
Modern genome sequencing machines extract smaller randomized fragments of the original DNA sequence, known as reads
  Oxford Nanopore Technologies (ONT):
  A widely-used sequencing technology
    Portable sequencing devices
    High-throughput
    Cheap
Notes: [CLICK] Genome analysis enables us to determine the DNA sequence of an organism,
[CLICK] which plays an important role in
[CLICK] personalized medicine,
[CLICK] outbreak tracing (like COVID-19)
[CLICK] the understanding of evolution
[CLICK] and so on
[CLICK] Modern genome sequencing machines extract smaller randomized fragments of the original DNA sequence, which we call reads.
[CLICK] Oxford nanopore technologies is a widely-used sequencing technology
[CLICK] as it provides portable sequencing devices
[CLICK] it is high-throughput
[CLICK] and cheap

## Slide 3: Overview: Two Limitations
Multiple steps in genome analysis
Large data movement between multiple steps
A lot of
wasted computation done on data that is later discovered to be useless
Notes: [CLICK] There are multiple steps in the genome analysis
[CLICK] We observe there is large data movement between these steps
[CLICK] and a lot of wasted computation done on the data that later discovered to be useless

## Slide 4: Overview: GenPIP
GenPIP: A fast and energy-efficient in-memory acceleration system for the Genome analysis PIPeline via tight integration of genome analysis steps
GenPIP has two key techniques
GenPIP outperforms state-of-the-art software & hardware solutions using CPU, GPU, and optimistic PIM by 41.6×, 8.4x, and 1.4x, respectively.
  Early rejection (ER)
    Timely stops the execution on useless data by predicting which reads will not be useful
  Chunk-based pipeline (CP)
    Provides fine-grained collaboration of genome analysis steps
Notes: To overcome these two limitations, we propose GenPIP
[CLICK] GenPIP is A fast and energy-efficient in-memory acceleration system for the Genome analysis PIPeline via tight integration of genome analysis steps
[CLICK] GenPIP has two key techniques
    A chunk-based pipeline that provides fine-grained collaboration of genome analysis steps
    An early-rejection technique predicts which reads will not be useful and then stops the execution of basecalling and read mapping for such reads
[CLICK] GenPIP outperforms state-of-the-art software & hardware solutions.

## Slide 5: Outline
Background and Motivation
GenPIP: Tight Integration of Genome Analysis Steps
  Chunk-based Pipeline (CP)
  Early Rejection (ER)
GenPIP Implementation
Evaluation
Conclusion
Notes: Let’s have a look at the genome analysis pipeline and our motivation

## Slide 6: Genome Analysis Pipeline
High-quality
Read
G
G
A
C
Compute
Storage
Storage
1. Basecalling
Compute
2. Read Quality Control
Storage
Store
mapping results
Genome sequencing
A
T
G
C
G
T
T
C
T
C
A
A
A
G
Compute
3. Read Mapping
Reference genome
T
A
T
G
G
A
C
T
T
T
A
G
C
A
A
A
C
T
C
A
A
A
G
G
C
G
T
T
C
A
T
G
G
A
C
A
T
G
G
A
C
G
C
G
T
T
C
Mapped
Unmapped
Low-quality
Notes: After we get the raw signals from the nanopore sequencing machine, we store them
Then we execute the first step, basecalling. we read the raw signals chunk by chunk from the storage and basecall them one by one into chunk of bases.
Here, red means the base quality is low and green means the base quality is high
After basecalling all chunks in a sequence, we assemble them into a read.
After basecalling all raw signal sequences into reads, we store them
Then execute the second step, read quality control.
Read quality control filters out the low-quality reads
And stores the high-quality reads
After that, we execute the read mapping step to map the read to the reference genome
If the read cannot be mapped to the reference genome, we discard it
For the read can be mapped to the reference genome, we store the mapping results.

## Slide 7: Limitation 1: Large Data Movement
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Large data movement between genome analysis steps
3913 GB
546 GB
437 GB
382 GB
Using a human dataset in [NC’19] as an example:
[NC'19] Rory Bowden, Robert W Davies, Andreas Heger, Alistair T Pagnamenta, Mariateresa de Cesare, Laura E Oikkonen, Duncan Parkes, Colin Freeman, Fatima Dhalla, Smita Y Patel, et al. Sequencing of human genomes with nanopore technology. Nature Communications, 2019.
Notes: The genome analysis pipeline has two main limitations
The first one is large data movement
We use a human dataset as an example
We move the raw signals to the basecalling
Then store the reads
And move the reads to the machine that executes read quality control
Then move the high quality reads to machines executes read mapping
In the end, only mapped reads are reviewed by bio analysts.
We conclude that there is large data movement between these steps

## Slide 8: Limitation 2: Wasted Computation
Using a human dataset in [NC’19] as an example:
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Low-quality
reads
Unmapped
reads
A considerable amount of computation on useless data due to
Low-quality reads
Unmapped reads
100%
79.5%
69.5%
20.5%
10%
[NC'19] Rory Bowden, Robert W Davies, Andreas Heger, Alistair T Pagnamenta, Mariateresa de Cesare, Laura E Oikkonen, Duncan Parkes, Colin Freeman, Fatima Dhalla, Smita Y Patel, et al. Sequencing of human genomes with nanopore technology. Nature Communications, 2019.
Notes: Second, 100% of reads are basecalled but 20.5% low-quality reads are filtered
And 10% of unmapped reads are discarded.
We conclude that there is a considerable amount of computation on useless data due to low quality reads and unmapped reads

## Slide 9: State-of-the-art Works
NVM-based PIM is an efficient technique to reduce data movement by processing data using or near memory
  Reduce the data movement in a single genome analysis step
  Exacerbate the data movement overhead between analysis steps
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
No prior work tackles data movement between analysis steps and reduces useless computation
NVM-based PIM for dot-product operation [Helix, PACT’20]
NVM-based PIM for search and addition
[PARC, ASPDAC’20]
Notes: Previous works accelerate either basecalling or read mapping using processing in memory
A prior work uses NVM-based PIM for dot-product calculation to accelerate basecalling since dot-product is the main operation in basecalling
A prior work uses NVM-based CAM for search and addition operation to accelerate read mapping since these two operations are the dominant operations in read mapping
These PIM accelerators reduce the data movement in a single step
But exacerbate the data movement overhead between analysis steps
And there is no prior work tackles data movement problem between the steps and reduce useless computation

## Slide 10: Goal and Opportunities
Chart: Normalized Speedup
| System A | System B | System C
Normalized Speedup | 2.7 | 6.1 | 9
We perform a study to quantify potential performance benefits
  Results are normalized to the performance of GPU
Goal: Efficiently accelerate the entire genome analysis pipeline while minimizing data movement and useless computation
NVM-based PIM accelerators for separate basecalling and read mapping
no data movement
between the accelerators of analysis steps
no data movement
and
no useless reads
(ideal case)
Notes: Our goal in this work is to efficiently accelerate the entire genome analysis pipeline while minimizing data movement and useless computation
To quantify potential benefits of overcoming the two limitations, we compare performance of the three systems and results are normalized to the performance of GPU
First, Basecalling and read mapping are executed in two in-memory accelerators separately, which achieves 2.7 times speedup
Assume there is no data movement, which achieves 6.1 times speedup
Assume there is no data movement and no useless reads in the pipeline. Which achieves 9 times speedup

## Slide 11: Outline
Background and Motivation
GenPIP: Tight Integration of Genome Analysis Steps
  Chunk-based Pipeline (CP)
  Early Rejection (ER)
GenPIP Implementation
Evaluation
Conclusion
Notes: Let’s have a look at the detail of our proposal, GenPIP

## Slide 12: GenPIP
First holistic in-memory accelerator for the genome analysis pipeline, including basecalling, read quality control, and read mapping steps
  Chunk-based Pipeline (CP)
    Enables fine-grained pipelining of genome analysis steps
    Processes reads at chunk granularity (i.e., a subsequence; 300 bases)
  Early Rejection (ER)
GenPIP has two key techniques
Notes: GenPIP is the first holistic in-memory accelerator for the genome analysis pipeline, including basecalling, read quality control, and read mapping steps
[CLICK] GenPIP has two key techniques
[CLICK] Chunk-based pipeline (CP)
[CLICK] Early rejection (ER)
[CLICK] Enables fine-grained pipeline of genome analysis steps by processing reads at chunk granularity

## Slide 13: Chunk-based Pipeline (CP)
CP increases parallelism by overlapping the execution of different steps at chuck granularity
CP reduces intermediate data by computing on data as soon as data is generated
CP provides opportunities for ER by analyzing a read at chunk granularity
QC
Read
Read Mapping
Read
Conventional Pipeline
Basecalling
C1
Basecalling
C1
Basecalling
C2
Basecalling
C3
Basecalling
C4
Assemble
QC: Quality control
RM: Read mapping
Time
Chunk-based Pipeline
QC
C1
Basecalling
C2
RM
C1
QC
C2
Basecalling
C3
RM
C2
QC
C3
Basecalling
C4
RM
C3
QC
C4
RM
C4
RM
Read
Assemble
A read consists of four chunks: C1, C2, C3, C4
Saved cycles
Notes: CP increases parallelism by overlapping the execution of different steps at chuck granularity
CP reduces the intermediate data by computing on the data as soon as the data is generated
CP provides opportunities for ER by analyzing a read at chunk granularity
[CLICK] In the conventional pipeline, the basecaller basecalls chunks one by one and
[CLICK] assemble them into a read to
[CLICK] do quality check
[CLICK] and read mapping
[CLICK] in our chunk-based pipeline, once a chunk is basecalled, we do quality control and partial computation of read mapping on the basecalled chunk
[CLICK] in the end, we assemble the them and do the remaining computation on the read

## Slide 14: GenPIP
First holistic in-memory accelerator for the genome analysis pipeline, including basecalling, read quality control, and read mapping steps
  Chunk-based Pipeline (CP)
    Enables fine-grained collaboration of genome analysis steps by processing reads at chunk granularity (i.e., a subsequence of a read, e.g., 300 bases)
  Early Rejection (ER)
    Stops the execution on useless reads as early as possible by using a small number of chunks to predict the usefulness of a read
GenPIP has two key techniques
Notes: Another key technique of GenPIP is Early rejection (ER)
Which Timely stops the execution on useless reads by using a small number of chunks to predict the usefulness of a read

## Slide 15: Early Rejection (ER)
Predict and eliminate low-quality and unmapped reads from the genome analysis pipeline as early as possible
Pass
Fail
Pass
Basecall a small number of chunks
Check the average quality of these chunks
Execute the remaining computation in read mapping
Basecall more chunks
Stop
analysis
Basecall the remaining chunks
Fail
Check the mapping score
Early-Rejection based on chunk quality scores (ER-QSR)
  Predict low-quality reads using chunk quality scores
Early-Rejection based on chunk mapping scores (ER-CMR)
  Predict unmapped reads using chunk mapping scores
Map basecalled chunks so far
Notes: Our early rejection technique Predicts and eliminates low-quality and unmapped reads in the genome analysis pipeline as early as possible
[CLICK] First, it basecalls a small number of chunks,
[CLICK] then check the average quality score of these chunks.
[CLICK] if it fails, then it stops analysis;
[CLICK] if it passes, then it basecalls more chunks
[CLICK] and map the basecalled chunks to the reference genome
[CLICK] to check the mapping score
[CLICK] if it fails, then it stops analysis
[CLICK] otherwise, basecalling remaining chunks
[CLICK] and execute the remaining computation in read mapping
[CLICK] in conclusion, ER has two sub-techniques, ER based on chunk quality scores
[CLICK] and ER based on chunk mapping

## Slide 16: Implementation of CP and ER
CP and ER can be applied on
different systems, e.g., CPU, GPU, and PIM
We implement CP and ER using PIM since PIM is more efficient to reduce the data movement between genome analysis steps
We also apply CP and ER on CPU and GPU baselines and observe speedup and energy savings
Notes: It’s worth to mention that, CP and ER can be implemented in many systems, such as CPU and GPU
We implement CP and ER in the PIM system since it’s more efficient

## Slide 17: Outline
Background and Motivation
GenPIP: Tight Integration of Genome Analysis Steps
  Chunk-based Pipeline (CP)
  Early Rejection (ER)
GenPIP Implementation
Evaluation
Conclusion
Notes: Let’s look at GenPIP implementation

## Slide 18: GenPIP Implementation
GenPIP
Read Mapping Module
GenPIP Controller
Basecalling Module
eDRAM
In-memory
Read Mapping
[PARC, ASPDAC’20]
+ Our design
In-memory
Basecaller
[Helix, PACT’20]
PIM-CQS
PIM chunk quality score calculation
Raw signals from the sequencing machine
Signal
chunk
Base quality score
Chunk mapping score
To storage
Read mapping result
Average Calculator
ER
ER
Controller
Quality score
ER
Chunk
Read Mapping Controller
Basecalled
chunk
Chunk quality score
https://arxiv.org/pdf/2209.08600.pdf
Notes: GenPIP has three main modules, basecalling, read mapping and GenPIP controller
[CLICK]

## Slide 19: GenPIP Implementation
GenPIP
Read Mapping Module
GenPIP Controller
Basecalling Module
eDRAM
In-memory
Read Mapping
Our design +
[PARC, ASPDAC’20]
In-memory
Basecaller
[Helix, PACT’20]
PIM-CQS
PIM chunk quality score calculation
Raw signals from the sequencing machine
Signal
chunk
Base quality score
Chunk mapping score
To storage
Read mapping result
Average Calculator
ER
ER
Controller
Quality score
ER
Chunk
Read Mapping Controller
Basecalled
chunk
Chunk quality score
Tightly integrating the genome analysis steps
Reduces data movement
Eliminates useless computation
Notes: GenPIP has three main modules, basecalling, read mapping and GenPIP controller
[CLICK]

## Slide 20: Outline
Background and Motivation
GenPIP: Tight Integration of Genome Analysis Steps
  Chunk-based Pipeline (CP)
  Early Rejection (ER)
GenPIP Implementation
Evaluation
Conclusion
Notes: Let’s look at our evaluation

## Slide 21: Evaluation Methodology
Performance, Area and Power Analysis:
  Simulation via Verilog HDL, NVSim [TCAD’12], and CACTI 6.5 [MICRO’07]
  See methodology in the paper for more
Baselines:
  CPU (Intel Xeon Gold 5118 CPU)
  GPU (NVIDIA GeForce RTX 2080 Ti GPU)
  Optimistic integration of two PIM accelerators (Helix [PACT’20] and PARC [ASP-DAC’20])
    Assumes no data movement between steps
    Assumes intermediate data causes no overhead
Datasets:
  E. coli (http://lab.loman.net/2016/07/30/nano pore- r9- data- release/)
  Human (https://www.ebi.ac.uk/ena/browser/view/PRJEB30620)
Notes: We use several simulators for GenPIP and you can check the paper for more details
We compare GenPIP with cpu gpu and an optimistic integration of two PIM accelerators, where we assume there is no data movement between steps and enough on-chip memory for intermediate data
We evaluate on two datasets, Ecoli and human

## Slide 22: Key Results – Performance
GenPIP provides 41.6x, 8.4x, and 1.4x speedup over CPU, GPU, and optimistic PIM
Chart: Normalized Speedup
| E. coli | Human | GMEAN
CPU | 1 | 1 | 1
GPU | 4.9945 | 5.7397 | 4.9769
Optimistic PIM | 29.8134 | 28.5377 | 29.9223
GenPIP | 46.7861 | 36.3184 | 41.615
41.6x
8.4x
1.4x
Both CP and ER are critical to the speedup
Notes: Here are the results of performance.
On average, GenPIP provides 41.6x over CPU, 8.4x over GPU, and 1.4x speedup over optimistic PIM, , which is an ideal integration
More evaluation details in the paper show both CP and ER are critical to the speedup

## Slide 23: Key Results – Energy Efficiency
GenPIP provides 32.8x, 20.8x, and 1.37x energy savings
over CPU, GPU, and optimistic PIM
Chart: Normalized Energy Reduction
| E. coli | Human | GMEAN
CPU | 1 | 1 | 1
GPU | 1.5792 | 1.5841 | 1.5793
Optimistic PIM | 24.5291 | 23.1484 | 23.8783
GenPIP | 39.1191 | 26.4856 | 32.7831
32.8x
20.8x
1.37x
ER is especially critical to the energy efficiency
Notes: Here are the energy reduction results
On average, GenPIP provides 32.8, 20.8, and 1.37x energy savings compared to CPU, GPU, and optimistic PIM, which is an ideal integration
We also find that reducing data movement and useless data contribute a lot to the energy reduction

## Slide 24: More in the Paper
Details of CP and ER
Detailed GenPIP architecture and implementations
  GenPIP controller
  Timely early rejection implementation
  In-memory seeding accelerator
More comparison points
Sensitivity analysis of the chunks used for ER
Area and power analysis
https://arxiv.org/pdf/2209.08600.pdf
Notes: We have more details in the paper

## Slide 25: More in the Paper
Details of CP and ER
Detailed GenPIP implementation
  GenPIP controller
  Early rejection implementation
  In-memory seeding accelerator
Results of applying CP and ER in CPU and GPU
Sensitivity analysis on the number of sampled chunks used for ER
Area and power analysis
Notes: including
Details of cp and er
Detailed genpip implementation
Results of applying cp and er in cpu and gpu
Sensitivity analysis
Area and power analysis

## Slide 26: Outline
Background and Motivation
GenPIP: Tight Integration of Genome Analysis Steps
  Chunk-based Pipeline (CP)
  Early Rejection (ER)
GenPIP Implementation
Evaluation
Conclusion
Notes: To conclude our work

## Slide 27: Conclusion
Goal: Tightly integrate genome analysis steps to reduce the data movement between steps and eliminate computation on useless data
GenPIP outperforms state-of-the-art software & hardware solutions using CPU, GPU, and optimistic PIM by 41.6×, 8.4x, and 1.4x, respectively.
GenPIP: The first in-memory genome analysis accelerator that tightly integrates genome analysis steps
GenPIP has two key techniques
  A chunk-based pipeline
  A new early-rejection technique
Problem: The genome analysis pipeline has large data movement between genome analysis steps and a significant amount of wasted computation on useless data
Notes: we observe that the genome analysis pipeline has large data movement between steps and a significant amount of useless data
Our goal is to Tightly integrate genome analysis steps to reduce the data movement between steps and eliminate the computation on useless data
Therefore, we propose, GenPIP, the First in-memory genome analysis accelerator that tightly integrates basecalling and read mapping via two key techniques A chunk-based pipeline A new early-rejection technique
According to our evaluation, GenPIP outperforms state-of-the-art software & hardware solutions

## Slide 28: GenPIP In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina,
Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, Onur Mutlu
Notes: Thank you. I am happy to take any questions.

## Slide 29: Backup Slides
Genome Sequencing
  Sequencing Technologies
  Current State of Sequencing
Genome Analysis Pipeline
  Basecalling
  Read Quality Control
  Read Mapping
Early Rejection
  ER based on Quality Scores
  ER based on Chunk Mapping
GenPIP Architecture
  In-memory seeding
Number of chunks for ER

## Slide 30: Genome Sequencing
Sample Collection
Preparation
Sequencing
Genome Sequence Analysis
Large DNA
molecule
Chopped DNA
fragments
Sequenced reads

## Slide 31: Sequencing Technologies
Short reads: a few hundred base pairs and error rate of ∼0.1%
  Long reads: thousands to millions of base pairs and error rate of 5–10%
Oxford Nanopore (ONT)
PacBio
Illumina
Notes: ONT, PacBio, Illumina
[CLICK] Based on the sequencing device, we obtain either short reads or long reads.

## Slide 32: Current State of Sequencing
*From NIH (https://www.genome.gov/about-genomics/fact-sheets/DNA-Sequencing-Costs-Data)
Notes: However, the compute power doesn’t match up with this trend.
Modern sequencing machines generate read fragments at an exponentially higher rate than prior sequencing technologies, with their growth far outpacing the growth in computational power in recent years
For example, the Illumina NovaSeq 6000 system can sequence about 48 human whole genomes at 30× genome coverage (the av- erage number of times a genomic base is sequenced) in about two days. However, analyzing (performing mapping and variant calling) the sequencing data of a single human genome requires over 32 CPU hours on a 48-core Intel Xeon processor, 23 of which are spent on read mapping

## Slide 33: Current State of Sequencing
*From NIH (https://www.genome.gov/about-genomics/fact-sheets/DNA-Sequencing-Costs-Data)
Computation is a bottleneck!
Notes: However, the compute power doesn’t match up with this trend.
Modern sequencing machines generate read fragments at an exponentially higher rate than prior sequencing technologies, with their growth far outpacing the growth in computational power in recent years
For example, the Illumina NovaSeq 6000 system can sequence about 48 human whole genomes at 30× genome coverage (the av- erage number of times a genomic base is sequenced) in about two days. However, analyzing (performing mapping and variant calling) the sequencing data of a single human genome requires over 32 CPU hours on a 48-core Intel Xeon processor, 23 of which are spent on read mapping

## Slide 34: Basecalling
DNNs
Basecaller
Input
raw
signal
chunks
Assemble
chunks of bases into a long read
Long Reads
Raw Signals
A 0.1
C 0.6
G 0.2
T 0.1
Input: Raw signal chunks
Process: Translate raw signals to bases (i.e., A, C, G, T) and calculate each base quality
Output: Assemble chunks into a long read

## Slide 35: Read Quality Control
Input: Base quality scores of a read from the basecalling step
Process: Calculate the average of all base quality scores in a read as the read quality score, and compare the read quality score to the threshold to decide whether this read is low-quality or high-quality
Output: High-quality reads (discard low-quality reads)
A
A
C
T
G
3
5
4
2
7
Long read
Base quality score
Calculate the average
Compare the read quality score with the threshold
High-quality
Low-quality
lower
higher
Discard
Notes: [CLICK] The second step, read quality control, usually runs on the remote machines outside the lab
[CLICK] It receives the base quality scores of a read from the basecalling step
[CLICK] calculates the read quality score
[CLICK] compares the read quality score with the threshold
[CLICK] decides whether it’s low-quality or high-quality and
[CLICK] discards the low-quality reads

## Slide 36: Read Mapping
(c) Chaining
Possible substrings
Read
DP
(d) Alignment
c
d
Input: High-quality read passes the read quality control step
Process:
  Use subsequence in a read to query the hash table to get possible match locations
  Identify the candidate regions and output the chaining score
  Execute the alignment step if there is a chain
Output: Mapping information
High-quality Long Reads
(a) Indexing
Reference Genome
Subsequence
locations
a
Hash table
(b) Seeding
Query
Possible
locations
b
Read
Subsequence
Notes: [CLICK] The third step, read mapping.
[CLICK] It receives the high-quality long reads to execute the seeding step,
[CLICK] which uses the subsequences in the read to query the pre-created hash table of the reference genome and then gets the possible match locations
[CLICK] then it executes chaining to identify the candidate regions and output the chaining score
[CLICK] if the chaining score is acceptable, then it executes alignment to quantitatively identify the similarity between the read and each candidate region

## Slide 37: ER based on Chunk Quality Scores
Goal: Accurately estimate the quality of the entire read by checking the quality of a small number of sampled chunks
Observation 1: The range of quality scores for the chunks extracted from high-quality reads is greatly higher than that from low-quality reads
Observation 2: A single chunk’s quality score is not enough to predict the read quality score because there are many chunks whose quality scores are larger than 7
Observation 3: Consecutive chunks’ quality scores are usually close to each other, indicating that sampling consecutive chunks may not be representative enough to estimate the quality of an entire read
Threshold: 7
Low-quality read
High-quality read
High-quality
Low-quality
Sample a small number of non-consecutive chunks evenly in a read
to predict the read quality
Notes: The goal of ER based on the chunk quality scores is to accurately estimate the quality of the entire read by checking the quality of a small number of sampled chunks
To achieve the goal, we study the chunk quality score in both low-quality read and high-quality read. 7 is the threshold
We have 3 main observations.
[CLICK] First, The range of quality scores for the chunks extracted from high-quality reads is greatly higher than that from low-quality reads
[CLICK] Second, A single chunk’s quality score is not enough to predict the read quality score because there are many chunks whose quality scores are larger than 7
[CLICK] Third, Consecutive chunks’ quality scores are usually close to each other, indicating that sampling consecutive chunks may not be representative enough to estimate the quality of an entire read
[CLICK] Therefore, we conclude that ER based on chunk quality scores needs to Sample a small number of non-consecutive chunks evenly in a read to predict the read quality

## Slide 38: ER based on Chunk Mapping
Key insight of ER based on chunk mapping: A read probably cannot be mapped to the reference genome if enough consecutive chunks in this read cannot be mapped to the reference genome
1. Sample a small number of consecutive chunks in a read
2. Merge these small consecutive chunks into a big chunk
3. Map this big chunk to the reference genome to predict whether the read can be mapped or not
Mapping a small chunk provides too many possible mapping locations
Notes: The key insight of ER based on chunk mapping is that A read probably cannot be mapped to the reference genome if enough consecutive chunks in this read cannot be mapped to the reference genome
[CLICK] However, Mapping a small chunk provides too many possible mapping locations
[CLICK] Therefore, ER based on chunk mapping needs to Sample a small number of consecutive chunks in a read
[CLICK] Merge these small consecutive chunks into a big chunk
[CLICK] Map this big chunk to the reference genome to predict whether the read can be mapped or not

## Slide 39: Architecture of GenPIP
PIM Basecaller
Quality Score Calculation
for Each Base
b
Chunk Buffer
4
DP Units
(Dynamic Programming)
Read Queue
1
5
Global Buffer
PIM-CQS
PIM chunk quality score calculation
2
Basecalling Module
a
GenPIP Controller
Read Mapping Module
Read Mapping Controller
Raw signals from the sequencing machine
Signal
chunk
Base quality
scores
Chunk &
locations
Chunk/read
& locations
Mapping
result
Chaining score
ER-QSR
signal
In-memory
seeding
3
To storage
Sequence alignment result
ER-QSR
Controller
Average Quality Score Calculator
ER-CMR
signal
ER-CMR
Controller
Quality score
ER-CMR
signal
Chunk
Buffer
Basecalled
chunk
CQS
c
Notes: GenPIP has three main modules, basecalling, read mapping and GenPIP controller
[CLICK]

## Slide 40: In-memory Seeding
A list of possible locations to the read mapping controller
Possible locations
Chunk
QSG
ReRAM
CAM
(key)
Query
ReRAM
CAM
(key)
Query
Addr.
Addr.
eDRAM Buffer
Basecalled
chunk from the GenPIP controller
…
ReRAM-based RAM
(stores the possible locations
i.e., values in the hash table)
ReRAM-based RAM
(stores the possible locations
i.e., values in the hash table)
…
…
…
a
b
c
d
e
f
g
h
A substring from a chunk
Generated query string
QSG
Query String Generator (QSG)

## Slide 41: Key Results – Sensitivity Analysis
Early rejection based on the chunk quality scores technique uses two and five sampled chunks for the E. coli and human datasets, respectively.
Early rejection based on the chunk mapping technique uses five and three sampled chunks for the E. coli and human datasets, respectively.
Early rejection based on the chunk quality scores
Early rejection based on the chunk mapping
Notes: Early rejection based on the chunk quality scores technique uses two sampled chunks for the E. coli and five chunks for human dataset
Early rejection based on the chunk mapping technique uses five and three sampled chunks for the E. coli and human datasets