## Slide 1
Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Google Consumer Workloads
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback and Video Capture
Google’s video codec
Goals
Data Movement Cost
Data Movement
1st key observation: 62.7% of total system energy is spent on data movement
Processing-in-Memory (PIM)
SoC
DRAM
L2
L1
CPU
CPU
CPU
CPU
Compute Unit
  2nd key observation: a significant fraction of data movement often comes from simple functions
We look at widely-used Google workloads to identify major sources of energy consumption:
1
2
Understand the data movement related bottlenecks in modern consumer workloads
Analyze the benefits of processing-in-memory (PIM) to mitigate data movement cost
    Investigate the PIM logic that can maximize energy efficiency given the limited area and energy budget in consumer devices
3
Browser
Chart: Fraction of Total Energy
| Google Docs | Gmail | Google Calendar | WordPress | Twitter | Animation | AVG
Texture Tiling | 1.312e+13 | 3.058e+12 | 319593492076.364 | 5.4789e+12 | 738397531219.6801 | 12302893814262 | 5.8363e+12
Color Blitting | 7.9639e+12 | 2.5555e+12 | 214665611070.8 | 1.9954e+12 | 539179828060.68 | 10082397746853 | 3.8919e+12
Other | 2.0596e+13 | 1.3368e+13 | 881303971032.8361 | 1.3228e+13 | 2.3356e+12 | 27432841968845 | 1.2973e+13
Google Docs
Gmail
Google Calendar
Word- Press
Twitter
Ani- mation
AVG
41.9% of page scrolling energy is spent on texture tiling and color blitting
77% of total energy consumption goes to data movement
Chart: Total Energy (pJ)
| CPU | L1 | LLC | Inter- connect | Mem Ctrl | DRAM
Texture Tiling | 2.5516e+12 | 903728069139.29 | 687788466859.2 | 2521647969456 | 403463675112.96 | 6.052e+12
Color Blitting | 3.0259e+12 | 531329645419 | 909145674584 | 982460247840 | 157193639654.4 | 2357904594816
Other | 4.2213e+12 | 2.5668e+12 | 2.3559e+12 | 3045626768304 | 487300282928.64 | 7.3095e+12
49.1% of total data movement comes from texture tiling and color blitting
Chart: Fraction of Total Energy
| Texture Tiling | Color Blitting
Data Movement | 0.25733 | 0.12023
Compute | 0.062128 | 0.073675
HTML
CSS
HTML Parser
CSS Parser
Render Tree
Layout
Rasteriza-tion
Composit-ing
Texture Tiling
Color Blitting
Rasterization
Invoke
Compositing
idle
high
Conversion
Texture
Tiles
time
CPU
Memory
Rasterization
Read Bitmap
Conversion
Write Back
CPU
PIM
CPU + PIM
CPU-Only
Linear
Bitmap
Texture
Tiles
Invoke
Compositing
Texture Tiling
data movement
Linear
Bitmap
  Texture tiling is a good candidate for PIM execution
Requires simple primitives: memcopy, bitwise operations, and simple arithmetic operations
PIM Core
PIM Accelerator
Texture Tiling
Linear Bitmap
Tiled Texture
9.4% of the area available for PIM logic
7.1% of the area available for PIM logic
  PIM core and PIM accelerator are feasible to implement in-memory texture tiling
Chrome Process
…
Render Process (tab 1)
Render Process (tab 2)
Render Process (tab n)
Chrome uses compression to reduce each tab’s memory footprint
To study data movement during tab switching, we perform an experiment:
  A user opens 50 tabs (most-accessed websites)
  Scrolls through each for a few second
  Switches to the next tab
Compression and decompression contribute to 18.1% of the total system energy
19.6 GB of data move between CPU and ZRAM
TensorFlow Mobile
57.3% of the inference energy is spent on data movement
54.4% of the data movement energy comes from packing/unpacking and quantization
Inference
Prediction
Reorders elements of matrices to minimize cache misses
Up to 40% of the inference energy and 31% of inference execution time
Packing’s data movement accounts for up to 35.3% of the inference energy
Packing
Matrix
Packed Matrix
A simple data reorganization process that requires simple arithmetic
Converts 32-bit floating point to 8-bit integers
Up to 16.8% of the inference energy and 16.1% of inference execution time
Majority of quantization energy comes from data movement
Quantization
floating point
integer
A simple data conversion operation that requires shift, addition, and multiplication
Video Playback and Capture
63.5% of the system energy is spent on data movement
Compressed video
VP9 Decoder
Display
80.4% of the data movement energy comes from sub-pixel interpolation and deblocking filter
Deblocking filter: a simple low-pass filter that attempts to remove discontinuity in pixels
Sub-pixel interpolation: interpolates the value of pixels at non-integer location
59.1% of the system energy is spent on data movement
Captured video
VP9 Encoder
Compressed
Majority of the data movement energy comes from motion estimation
Motion estimation: compresses the frames using temporal redundancy between them
Evaluation
Chart: Normalized Energy
| Texture Tiling | Color Blitting | Com- pression | Decom- pression | Packing | Quantization | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.41638 | 0.531 | 0.59396 | 0.40527 | 0.5087 | 0.50462 | 0.50061 | 0.49893 | 0.59594
PIM-Acc | 0.36127 | 0.42335 | 0.47294 | 0.29851 | 0.47245 | 0.42913 | 0.34481 | 0.26459 | 0.3925
On average, energy consumption reduces by 49.1% using PIM core and 55.4% using PIM accelerator
Chart: Normalized Runtime
| Texture Tiling | Color Blitting | Comp- ression | Decomp- ression | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation | TensorFlow
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.43478 | 0.64516 | 0.76336 | 0.76923 | 0.72464 | 0.8 | 0.84746 | 0.63694
PIM-Acc | 0.4 | 0.57803 | 0.47619 | 0.5 | 0.5814 | 0.70423 | 0.47619 | 0.50505
Chrome Browser
Video Playback and Capture
TensorFlow Mobile
On average, energy consumption reduces by 44.6% using PIM core and 54.2% using PIM accelerator
  Chrome Rendering Pipeline
Scrolling
Tab Switching
Chrome employs a multi-process architecture
Main operations during tab switching:
  Context switch
  Load the new page
CPU
DRAM
ZRAM
Compressed Tab
1
2
CPU
CPU-Only
Memory
CPU
CPU + PIM
PIM
time
Swap out N pages
Read N Pages
Compress
Other tasks
Write back
compression
ZRAM
Swap out N pages
Other tasks
Compress
ZRAM
No off-chip data movement
data movement
high
Uncompressed
Pages
Uncompressed
Pages
  Both functions can benefit from PIM execution and can be implemented at PIM logic
Color blitting is a good candidate for PIM execution
Generates a large amount of data movement
Requires low-cost operations: Memset, simple arithmetic, and shift operations
  Accounts for 19.1% of the total system energy during scrolling
  Color Blitting
  Texture Tiling
  Color blitting is feasible to implement in PIM logic