## Slide 1
Chart: Execution time(ms)
| 32 Ciphertexts | 64 Ciphertexts
CPU | 9243236.848 | 16116650.33
PIM | 1238286.259 | 2476532.17
CPU-SEAL | 110852.6704 | 216799.532
GPU | 22426.9344 | 45094.9064
Chart: Execution time (ms)
| 640 USERS | 1280 USERS | 2560 USERS
CPU | 12769.858 | 25645.387 | 51290.774
PIM | 506.348 | 506.348 | 506.348
CPU-SEAL | 5948.177 | 12276.464 | 24552.928
GPU | 4955.483 | 8491.311 | 16982.622
Evaluating Homomorphic Operations
on a Real-World Processing-In-Memory System
Harshita Gupta* Mayank Kabra* Juan Gómez-Luna Konstantinos Kanellopoulos Onur Mutlu
(a)
(b)
(c)
For statistical operations, PIM achieves 30× to 300× improvement over CPU and 10× to 30× over GPU
KEY TAKEAWAY #1
UPMEM PIM excels in homomorphic addition with native 32-bit integer support, surpassing CPUs and GPUs.
Problem Statement
HE enables processing on encrypted data to facilitate secure computation
HE suffers from memory usage and data transfer bottlenecks on processor-centric chips, hampering scalability and performance
Acceleration efforts with GPUs, FPGAs, and ASICs face ongoing challenges related to resource limitations, data transfer, and practical ASIC implementation
Our Goal
Evaluate the suitability of real-world general-purpose processing-in-memory architectures to perform homomorphic operations
Evaluation Methodology
Homomorphic Vector Addition & Multiplication
We offload and evaluate homomorphic operations on UPMEM PIM, Intel i5-8250U CPU, and NVIDIA A100 GPU
Comparisons to custom CPU/GPU and optimized SEAL CPU libraries
Microbenchmarks cover addition/multiplication with varying ciphertexts (32, 64, 128 bits)
Statistical workloads: (i) mean (ii) variance (iii) linear regression
KEY TAKEAWAY #2
PIM performance for homomorphic multiplication
lags due to the absence of native 32-bit integer multiplication support, but future PIM systems may outperform CPUs and GPUs.
Statistical Workloads
KEY TAKEAWAY #3
PIM's computational power scales with memory capacity via more memory banks and cores.
PIM system is 50-100× faster than CPU and
2-15× faster than GPU in vector addition
PIM outperforms custom CPU library by 40-50× in vector multiplication but lags 10-15× behind GPU
Chart: Number of Ciphertexts
| 5120 | 10240 | 20480 | 40960 | 81920
CPU | 5473882.197 | 11005033.76 | 21970278.49 | 35266399.32 | 45957681.94
PIM | 131645.135 | 263991.946 | 527854.011 | 1055931.786 | 2137988.562
CPU-SEAL | 27889.706 | 55691.293 | 111695.209 | 224452.435 | 449237.07
GPU | 3462.7346 | 6530.458 | 13369.3576 | 27439.2448 | 55109.8277
Chart: Number of Ciphertexts
| 20480 | 40960 | 81920 | 163840 | 327680
CPU | 807.636 | 1627.494 | 3287.24 | 6505.403 | 12986.554
PIM | 37.71 | 58.86 | 123.84 | 258.79 | 536.33
CPU-SEAL | 565.438 | 1268.146 | 2156.795 | 5359.329 | 8609.573
GPU | 82.685 | 165.508 | 331.025 | 660.508 | 1309.579
Chart: Execution time (ms)
| 640 USERS | 1280 USERS | 2560 USERS
CPU | 5150594.752 | 10274890.69 | 20154639.25
PIM | 825630.9313 | 825630.9313 | 825630.9313
CPU-SEAL | 78684.453 | 141536.122 | 277067.911
GPU | 15170.605 | 30480.138 | 61179.058
Mean
Variance
Regression
CPU
(x86, ARM, RV…)
DDR
Data bus