## Slide 1: LTRF: Enabling High-Capacity Register Files for GPUs via Hardware/Software Cooperative Register Prefetching
Mohammad Sadrosadati | Amirhossein Mirhosseini
Seyed Borna Ehsani | Hamid Sarbazi-Azad
Mario Drumond | Babak Falsafi
Rachata Ausavarungnirun | Onur Mutlu

## Slide 2: Register file size limits GPU scalability
Register file already accounts for 60% of on-chip storage
But, there is still demand for more registers to achieve maximum performance and concurrency
Chart: 
| Available Register File | Average Required Register File | Maximum Required Register File
 | 256 | 588 | 1505
2.3x
5.9x
(KB)

## Slide 3: Register file size limits GPU scalability
Register file already accounts for 60% of on-chip storage
But, there is still demand for more registers to achieve maximum performance and concurrency
Chart: 
| Available Register File | Average Required Register File | Maximum Required Register File
 | 256 | 588 | 1505
2.3x
5.9x
(KB)
Unfortunately, all mechanisms to expand RF capacity without large area/power overheads significantly increase access latency
  Emerging technologies, register file compression/virtualization, etc.

## Slide 4: Register file size limits GPU scalability
Register file already accounts for 60% of on-chip storage
But, there is still demand for more registers to achieve maximum performance and concurrency
Chart: 
| Available Register File | Average Required Register File | Maximum Required Register File
 | 256 | 588 | 1505
2.3x
5.9x
(KB)
Goal: Tolerate register file latencies
Unfortunately, all mechanisms to expand RF capacity without large area/power overheads significantly increase access latency
  Emerging technologies, register file compression/virtualization, etc.

## Slide 5: Contributions (1)
Compiler-driven Register Prefetching
  Break control flow graph into “prefetch subgraphs”
  Prefetch registers at the beginning of each subgraph
  Interval analysis to identify prefetch subgraphs
P(R1,R2)
R1
P(R3)
R3
R2
P(R4)
R4
R1
R3
R2
R4

## Slide 6: Contributions (2)
Latency Tolerant Register File (LTRF)
  “2-level” main register file + register cache
  Performs prefetch ops while executing other warps
  Tolerates up to 6x higher RF access latencies
  Paves the way for various area/power optimizations

## Slide 7: Contributions (2)
Latency Tolerant Register File (LTRF)
  “2-level” main register file + register cache
  Performs prefetch ops while executing other warps
  Tolerates up to 6x higher RF access latencies
  Paves the way for various area/power optimizations
Example LTRF deployment enables 8× larger register file and 32% higher performance
Chart: Normalized IPC
| backprop | bfs | btree | kmeans | tpacf | lavaMD | lbm | leukocyte | myocyte | NN | sad | sgemm | STO | WP | GMEAN
TFET | 0.70925 | 0.73 | 0.71303 | 0.63905 | 0.61714 | 0.6649 | 0.6771 | 0.7015 | 0.6832 | 1.1895 | 0.9333 | 1.098 | 0.9943 | 0.7808 | 0.83818
TFET+RFC | 0.78378 | 0.81 | 0.78892 | 0.76892 | 0.76378 | 0.76463 | 0.77 | 0.8 | 0.77 | 1.37 | 1.06 | 1.26 | 1.13 | 0.88 | 0.95487
TFET+LTRF | 0.97927 | 0.98 | 0.97901 | 0.98901 | 0.99 | 1.07 | 1.09 | 1.14 | 1.1 | 1.92 | 1.485 | 1.76 | 1.6 | 1.2544 | 1.3483
Ideal | 1 | 1 | 1 | 1 | 1 | 1.09 | 1.11 | 1.15 | 1.12 | 1.95 | 1.53 | 1.8 | 1.63 | 1.28 | 1.3741

## Slide 8: LTRF: Enabling High-Capacity Register Files for GPUs via Hardware/Software Cooperative Register Prefetching
Mohammad Sadrosadati | Amirhossein Mirhosseini
Seyed Borna Ehsani | Hamid Sarbazi-Azad
Mario Drumond | Babak Falsafi
Rachata Ausavarungnirun | Onur Mutlu

## Slide 9: LTRF: Enabling High-Capacity Register Files for GPUs via Hardware/Software Cooperative Register Prefetching
Mohammad Sadrosadati | Amirhossein Mirhosseini
Seyed Borna Ehsani | Hamid Sarbazi-Azad
Mario Drumond | Babak Falsafi
Rachata Ausavarungnirun | Onur Mutlu
Please attend our talk at 2:00 in Virginia EF