## Slide 1: The Locality Descriptor A Holistic Cross-Layer Abstraction to Express Data Locality in GPUs
Nandita Vijaykumar
Eiman Ebrahimi, Kevin Hsieh, Phillip B. Gibbons, Onur Mutlu

## Slide 2: Executive Summary
Exploiting data locality in GPUs is a challenging task
Software
Hardware
Locality Descriptor
Cache Management
CTA Scheduling
Data Placement
Data Prefetching
…
Application
Flexible, architecture-agnostic interface
Access to program semantics
Performance Speedups:
26.6% (up to 46.6%) from cache locality
53.7% (up to 2.8x) from NUMA locality

## Slide 3: Outline
Why leveraging data locality is challenging?
Designing the Locality Descriptor
Evaluation

## Slide 4: Data locality is critical to GPU performance
Core
Core
L1
L2
Memory
Reuse-based (Cache Locality)
Two forms of data locality:
Reuse-based locality (cache locality)
NUMA locality
L1

## Slide 5: Data locality is critical to GPU performance
NUMA Locality
Memory
Memory
Memory
Memory
NUMA
Zone 2
NUMA
Zone 3
NUMA
Zone 1
NUMA
Zone 0
Two forms of data locality:
Reuse-based locality (cache locality)
NUMA locality
Cores
Cores
Cores
Cores

## Slide 6
The GPU execution and programming models are designed to explicitly express parallelism…
But there is no explicit way to express data locality
Exploiting data locality in GPUs is a challenging and elusive feat

## Slide 7: A case study in leveraging data locality: Histo
X dim
Y dim
Data Structure A
X dim
Y dim
Y dim
X dim
CTAs along the Y dim share the same data
CTA Compute Grid
Type of data locality:
Inter-CTA
CTAs

## Slide 8: Leveraging cache locality
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
Core
L1
Core
L1
Core
L1
Core
L1
CTA scheduling is required to leverage inter-CTA cache locality
CTA scheduling is insufficient: we also need other techniques

## Slide 9: Leveraging NUMA locality
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
Memory
Exploiting NUMA locality requires both
CTA scheduling and data placement
Memory
NUMA Zone 0
NUMA Zone 1
Memory
Memory
NUMA Zone 2
NUMA Zone 3
Cores
Cores
Cores
Cores

## Slide 10: Today, leveraging data locality is challenging
As a programmer:
No easy access to architectural techniques – CTA scheduling, cache management, data placement, etc.
Even when using work-arounds, optimization is tedious and not portable
As the architect:
Key program semantics are not available to the hardware
Where to place data?
Which CTAs to schedule together?

## Slide 11: To make things worse:
There are many different locality types: Inter-CTA, inter-warp, intra-thread, …
Each type requires a different set of architectural techniques:
  Inter-CTA locality requires CTA scheduling + prefetching
  Intra-thread locality requires cache management
  …

## Slide 12: The Locality Descriptor
Software
Hardware
A hardware-software abstraction to express and exploit data locality
Locality Descriptor
Cache Management
CTA Scheduling
Data Placement
Data Prefetching
…
Application
Connects locality semantics to the underlying
hardware techniques
New software interface
Access to key program semantics

## Slide 13: Goals in designing the Locality Descriptor
Software
Hardware
Locality Descriptor
Cache Management
CTA Scheduling
Data Placement
Data Prefetching
…
Application
2) Architecture-agnostic interface
3) Flexible and general
1) Supplemental and hint-based
Inter-CTA, inter-warp, intra-thread, …

## Slide 14: Designing the Locality Descriptor
LocalityDescriptor ldesc();
LocalityDescriptor ldesc(X, Y, Z);
Hardware
Cache Management
CTA Scheduling
Data Placement
Data Prefetching
…

## Slide 15: An Overview: The components of the Locality Descriptor
LocalityDescriptor ldesc(A, len,
INTER-THREAD,
tile,
loc);
1) Data Structure
2) Locality Type
3) Tile Semantics
4) Locality Semantics

## Slide 16: Outline
Why leveraging data locality is challenging?
Designing the Locality Descriptor
Evaluation

## Slide 17: 1. How to choose the basis of the abstraction?
Possibilities:
Hardware component: cache, core, NUMA zone, prefetcher,…
Not architecture agnostic
Thread model: grid, CTA, thread, …
Any computation has varying locality characteristics
Key Idea: Use the data structure as the basis to describe data locality

## Slide 18: 1. How to choose the basis of the abstraction?
LocalityDescriptor ldesc();
Architecture-agnostic
Each data structure is accessed the same way by all threads
A new instance is required for each important data structure
LocalityDescriptor ldesc(A);
Key Idea: Use the data structure as the basis to describe data locality
Data Structure

## Slide 19: 2. How to communicate with hardware?
Software
Hardware
Locality Descriptor
Cache Management
CTA Scheduling
Data Placement
Data Prefetching
…
Application
Architecture-agnostic interface
Inter-CTA, inter-warp, intra-thread, …
Architecture-specific optimizations
Locality type drives architecture mechanisms

## Slide 20: 2. How to communicate with hardware?
Key Idea: Use locality type to drive underlying architectural techniques
Origin of locality (or locality type) causes the challenges in exploiting it
E.g.:
Inter-CTA locality requires CTA scheduling as reuse is across threads
Intra-thread locality requires cache management to avoid thrashing
Locality type is application-specific and known to the programmer

## Slide 21: 2. How to communicate with hardware?
Key Idea: Use locality type to drive underlying architectural techniques
CTA Compute Grid
X dim
Y dim
Three fundamental types:
INTER-THREAD
INTRA-THREAD
NO-REUSE
LocalityDescriptor ldesc(A);
INTER-THREAD
LocalityDescriptor ldesc(A, INTER-THREAD);

## Slide 22: Driving underlying architectural techniques
Locality Type?
NO_REUSE
INTRA_THREAD
INTER_THREAD
Cache Bypassing
CTA Scheduling (if NUMA)
Memory Placement (if NUMA)
CTA Scheduling
Cache Soft Pinning
Memory Placement (if NUMA)
Determined based on more information

## Slide 23: 3. How to describe locality?
Data Structure A
X dim
Y dim
X dim
Y dim
Key Idea: Partition the data structure and compute grid into tiles
Basic unit of locality:
Data Tile
Compute Tile
Mapping between them
CTA Compute Grid
tile((X_tile, Y_len, 1), (1, GridSize.y, 1), (1, 0, 0));
Data Tile Dimensions
Compute Tile Dimensions
Compute-Data Map
Data Tile
Compute Tile
LocalityDescriptor ldesc(A, INTER-THREAD, tile);
LocalityDescriptor ldesc(A, INTER-THREAD);

## Slide 24: Additional features of the Locality Descriptor
Locality type insufficient to inform underlying architectural techniques
(INTER-THREAD, INTRA-THREAD, NO-REUSE)
LocalityDescriptor ldesc(A, INTER-THREAD, tile);
In addition, we also have Locality Semantics to include:
  - Sharing Type
  - Access Pattern
(COACCESSED, REGULAR, X_len)
LocalityDescriptor ldesc(A, INTER-THREAD, tile, loc);

## Slide 25: A decision tree to drive underlying techniques
Locality Type?
NO_REUSE
INTRA_THREAD
Sharing Type?
INTER_THREAD
NEARBY
Access Pattern?
COACCESSED
REGULAR
IRREGULAR
Cache Hard Pinning
CTA Scheduling (if NUMA)
Memory Placement (if NUMA)
Cache Bypassing
CTA Scheduling (if NUMA)
Memory Placement (if NUMA)
CTA Scheduling
Cache Soft Pinning
Memory Placement (if NUMA)
CTA Scheduling
Guided Stride Prefetching
Memory Placement (if NUMA)
CTA Scheduling
Next-line Stride Prefetching
Memory Placement (if NUMA)

## Slide 26: Leveraging the Locality Descriptor
LocalityDescriptor ldesc(A, INTER-THREAD, tile, loc);
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
Architectural techniques:
CTA Scheduling
Prefetching
Data Placement

## Slide 27: CTA Scheduling
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
Core 0
Core 1
L1D
L1D
Core 2
Core 3
L1D
L1D
Compute Tile 0
Compute Tile 1
Compute Tile 2
Compute Tile 3
Cluster 0
Cluster 1
Cluster 2
Cluster 3
Cluster 0
Cluster 1
Cluster 2
Cluster 3

## Slide 28: Leveraging the Locality Descriptor
LocalityDescriptor ldesc(A, INTER-THREAD, tile, loc);
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
Architectural techniques:
CTA Scheduling
Prefetching
Data Placement

## Slide 29: Data Placement
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
SM 0
SM 1
L1D
L1D
SM 2
SM 3
L1D
L1D
Clust 0
Cluster Queues
Clust 1
Clust 2
Clust 3
Memory
Memory
Memory
Memory
NUMA Zone 0
NUMA Zone 1
NUMA Zone 2
NUMA Zone 3
Cluster 0
Cluster 1
Cluster 2
Cluster 3
Cluster 0
Cluster 1
Cluster 2
Cluster 3

## Slide 30: Leveraging the Locality Descriptor
LocalityDescriptor ldesc(A, INTER-THREAD, tile, loc);
Data Structure A
CTA Compute Grid
X dim
Y dim
X dim
Y dim
Architectural techniques:
CTA Scheduling
Prefetching
Data Placement
All threads stall because they wait on the same data

## Slide 31: Outline
Why leveraging data locality is challenging?
The Locality Descriptor
Evaluation

## Slide 32: Methodology
Evaluation Infrastructure: GPGPUSim v3.2.2
Workloads: Parboil, Rodinia, CUDA SDK, Polybench
System Parameters:
Shader Core: 1.4 GHz; GTO scheduler [50]; 2 schedulers per SM, Round-robin CTA scheduler
SM Resources Registers: 32768; Scratchpad: 48KB, L1: 32KB, 4 ways
Memory Model: FR-FCFS scheduling [59, 60], 16 banks/channel
Single Chip System: 15 SMs; 6 memory channels; L2: 768KB, 16 ways
Multi-Chip System: 4 NUMA zones, 64 SMs (16 per zone); 32 memory channels;
L2: 4MB, 16 ways; Inter-GPM Interconnect: 192 GB/s;
DRAM Bandwidth: 768 GB/s (192 GB/s per module)

## Slide 33: Performance speedup: leveraging cache locality
Chart: Speedup
| SK | DT | HS | D2D | C2D | SPMV | LIB | LMD | INTER-THREAD (COACCESSED) | INTER-THREAD (NEARBY) | INTRA-THREAD | Geomean
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
LDesc-Sched | 1.0021 | 1.0237 | 1.0422 | 1.1434 | 1.1293 | 0.88133 | 1.0023 | 0.97481 | 1.0218
LDesc-Pref | 1.2465 | 1.2248 | 1.287 | 1.044 | 1.042 | 0.93547 | 1.0185 | 0.94907 | 1.0859
LDesc-Cache | 0.99742 | 1.0149 | 0.98413 | 0.87463 | 1 | 1.0926 | 1.1579 | 1.1956 | 1.0351
LDesc | 1.4663 | 1.3722 | 1.4036 | 1.227 | 1.2602 | 1.0926 | 1.1579 | 1.1956 | 1.2661
Locality descriptors are an effective means to leverage cache locality
26.6%
(up to 46.6%)
Different locality types require different optimizations
A single optimization is often insufficient

## Slide 34: Performance Impact: Leveraging NUMA Locality
Chart: Speedup
| ATX | SK | DT | SPMV | PT | LPS | MVT | LIB | C2D | PF | HS | SP | LMD | TRA | SC | Geomean
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
FirstTouch-Distrib | 0.74216 | 0.73475 | 1.4188 | 0.97485 | 1.352 | 0.94164 | 0.73932 | 0.96526 | 2.7485 | 1.3148 | 0.96072 | 1.9457 | 1.7077 | 1.378 | 1.148 | 1.1834
LDesc-Placement | 0.99916 | 1.1776 | 1.5041 | 1.0224 | 0.97888 | 0.93569 | 0.998 | 1.4627 | 0.86235 | 1.0297 | 0.96667 | 0.98755 | 0.96147 | 0.96711 | 1.0624 | 1.0482
LDesc | 1.5436 | 1.6666 | 1.5859 | 1.0224 | 1.1234 | 1.1515 | 1.5525 | 1.4635 | 2.7913 | 1.4632 | 1.2406 | 1.941 | 1.1644 | 2.4474 | 2.1419 | 1.5528
53.7%
(up to 2.8x)

## Slide 35: Conclusion
Problem:
  GPU programming models have no explicit abstraction to express data locality
  Leveraging data locality is a challenging task, as a result
Our Proposal: The Locality Descriptor
  A HW-SW abstraction to explicitly express data locality
  A architecture-agnostic and flexible SW interface to express data locality
  Enables HW to leverage key program semantics to optimize locality
Key Results:
  26.6% (up to 46.6%) performance speed up from leveraging cache locality
  53.7% (up to 2.8x) performance speed up from leveraging NUMA locality

## Slide 36: The Locality Descriptor A Holistic Cross-Layer Abstraction to Express Data Locality in GPUs
Nandita Vijaykumar
Eiman Ebrahimi, Kevin Hsieh, Phillip B. Gibbons, Onur Mutlu