## Slide 1: MARS Processing-In-Memory Acceleration of Raw Signal Genome Analysis Inside the Storage Subsystem
Melina Soysal
Mohammad Sadrosadati Onur Mutlu
Konstantina Koliogeorgi Can Firtina Nika Mansouri Ghiasi
Rakesh Nadig Haiyu Mao Geraldo F. Oliveira Yu Liang Klea Zambaku

## Slide 2: Outline
Conclusion
Background
Motivation and Goal
MARS
Evaluation

## Slide 3: Genome Sequence Analysis
Study of genome to understand genetic variation, species and evolution has led to groundbreaking advances:
Evolutionary biology
Outbreak tracing
Personalized medicine
Genome analysis typically starts with sequencing and mapping
Sequencing
generates small DNA fragments
Mapping
reference
mapping positions
aligns signals to reference genome
raw signals

## Slide 4: Raw Signal Genome Analysis (RSGA)
Hash
Raw Signal Genome Analysis (RSGA)
  novel approach that operates directly on raw electrical signals
  exploits high throughput of modern sequencing technologies
  enables real-time analysis
High Level Overview of RSGA Read Mapping
0x01
Indexing (offline)
store
query
0x00
Reference Genome
AAGCCT
AAGCCT
Sketching
Mapping (online)
Query Sequence
events
Sketching
Hash
Chaining
matches
x
x
x
Hash Table
0x00
0x01
0xFF
…
Hash
Positions
13,21
1,101,…
2,64,…
Deep Dive on mapping following

## Slide 5: Raw Signal Genome Analysis (RSGA)
Raw Signal Genome Analysis (RSGA)
  novel approach that operates directly on raw electrical signals
  exploits high throughput of modern sequencing technologies
  enables real-time analysis
High Level Overview of RSGA Read Mapping
EVENT DETECTION
SEEDING
hash and query
CHAINING
sorting and DP-based
query
0x00
Mapping (online)
Query Sequence
events
Sketching
Hash
Chaining
matches
x
x
x
Hash Table
0x00
0x01
0xFF
…
Hash
Positions
13,21
1,101,…
2,64,…
I
II
III

## Slide 6: Outline
Conclusion
Background
Motivation and Goal
MARS
Evaluation

## Slide 7: Motivation
Sequencing throughput is growing rapidly Modern sequencers can generate 100Ks of signal samples per second
RSGA struggles to keep up with increasing real-time requirements Software pipelines cannot keep up with the pace of raw signal generation
There is a critical need for acceleration
Goal: Identify key performance bottlenecks in the RSGA pipeline Target the most time- and energy-intensive steps for hardware acceleration
Chart: 
| D5 | D4 | D3 | D2 | D1
I/O | 0.44693 | 2.8113 | 14.2983 | 24.4228 | 40.8487
Event detection | 0.32219 | 0.78842 | 6.8819 | 15.2129 | 20.4808
Seeding | 4.3277 | 5.0721 | 8.0838 | 9.3213 | 5.1415
Chaining | 94.8976 | 91.312 | 70.5813 | 50.736 | 33.1082
Chaining & seeding consistently dominate runtime
Event detection & I/O overhead are also non-negligible

## Slide 8: Impact of I/O data movement
We model I/O data movement overhead when accelerating commonly targeted steps in the pipeline: seeding and chaining
Chart: Latency reduction of seeding and chaining %
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
D1 | 40.8487 | 42.4733 | 44.2325 | 46.1437 | 48.2275 | 50.5084 | 53.0158 | 55.7851 | 58.8597 | 62.2929 | 66.1515
D2 | 24.4228 | 25.9832 | 27.7567 | 29.7901 | 32.1449 | 34.9039 | 38.1811 | 42.1373 | 47.0083 | 53.1525 | 61.1445
D3 | 14.2983 | 15.5191 | 16.9678 | 18.7149 | 20.8631 | 23.5683 | 27.0796 | 31.8203 | 38.5732 | 48.9643 | 67.0182
D4 | 2.8113 | 3.1112 | 3.4827 | 3.9549 | 4.5753 | 5.4265 | 6.6668 | 8.642 | 12.2805 | 21.2107 | 77.7485
D5 | 0.44693 | 0.49616 | 0.55758 | 0.63636 | 0.74106 | 0.88699 | 1.1045 | 1.4633 | 2.1675 | 4.178 | 57.6885
I/O data movement from SSD becomes dominant overhead as compute steps are accelerated in RSGA
As compute latency is reduced, I/O becomes the dominant contributor to total execution time

## Slide 9: Our Goal
Design a high-performance and energy-efficient system for RSGA by addressing both the
I/O data movement and
computational bottlenecks

## Slide 10: Outline
Conclusion
Background
Motivation and Goal
MARS
Evaluation

## Slide 11: MARS: PIM Acceleration of RSGA Inside Storage
First In-Storage-Processing system for RSGA
Key Idea: Enable multiple Processing-In-Memory paradigms within the SSD and leverage high SSD-internal bandwidth to create a highly-parallel and energy-efficient system for RSGA
Co-design between targeted software modifications and dedicated hardware components within the storage system
Targeted software modifications to optimize RSGA for in-storage executions
Tailored to SSD parallelization capabilities and architecture
Processing-In-Memory within the SSD to accelerate RSGA steps
Processing using the SSD-internal DRAM
Processing near the SSD-internal DRAM

## Slide 12: MARS Genome Analysis Workflow
Software modifications to reduce computational workload and intermediate storage requirements
Filtering Techniques
  Discard candidates unlikely to result in valid mapping
  Includes frequency and vote-based filtering
Challenge: Preserve accuracy in the presence of raw signal noise
Requires careful placement of both techniques in the pipeline
Involves fine-tuning filter parameters
Arithmetic Conversion Techniques
  Convert floating-point to fixed-point representations (16 bits)
  Reduces memory footprint and computational cost

## Slide 13: Impact of SW Modification on Accuracy
Ground Truth
Basecalling (Dorado) and Read Mapping (minimap2)
Datasets: SARS-CoV-2, E.coli, Yeast, Green Algae, Human
Comparison points:
  RawHash2 (RH2) [Firtina+, Bioinformatics’24]: state-of-the-art RSGA algorithm
  MS-CPUFloat : RSGA + filtering techniques
  MS_CPUFixed : RSGA + filtering + arithmetic conversion techniques
We conduct an accuracy analysis to show the benefits of our SW improvements and evaluate the usage of fixed-point arithmetic

## Slide 14: Accuracy Evaluation
Key Observations

## Slide 15: Accuracy Evaluation
MS-CPU improves recall and F1-score over RH2
Our filtering techniques are effective in eliminating ambiguous and redundant candidate matches & allow pipeline to focus on more informative regions that are more likely to represent the correct match
Key Observations

## Slide 16: Accuracy Evaluation
MS-CPU improves recall and F1-score over RH2
Our filtering techniques are effective in eliminating ambiguous and redundant candidate matches & allow pipeline to focus on more informative regions that are more likely to represent the correct match
Using fixed-point arithmetic in MS-CPU only leads to minimal accuracy loss
We apply earlier normalization & quantization to ensure fixed-point arithmetic has no significant impact on our results
Key Observations

## Slide 17: MARS Architecture & System - Overview
In-Storage-Processing system for RSGA
Conventional Mode: SSD performs standard SSD storage operations
Accelerator Mode: SSD executes the full RSGA pipeline without host intervention
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
Flash Memory

## Slide 18: MARS Architecture & System (I/IV)
SSD Controller Components
MARS Control Unit
Finite State Machine that orchestrates pipeline execution, control and data flow
I
SSD Controller
Flash Memory
Cores
FTL
Flash Controller
Merger
Unit
III
Sorter
Unit
II
.
.
.
MARS
Control
Unit
I

## Slide 19: MARS Architecture & System (II/IV)
SSD Controller Components
MARS Control Unit
Finite State Machine that orchestrates pipeline execution, control and data flow
I
Merger Unit
Combines sorted subsequences into longer sorted ones
Sorter Unit
Performs parallel sorting of sequences using dedicated logic
II
III
SSD Controller
Flash Memory
Cores
FTL
Flash Controller
.
.
.
MARS
Control
Unit
I
Merger
Unit
III
Sorter
Unit
II
Paradigm: Implements Processing Near DRAM
1 Sorter-Merger pair per flash controller

## Slide 20: MARS Architecture & System (III/IV)
SSD-Internal DRAM Components
SSD-Internal DRAM
…
Bank
Bank
…
Subarrays
…
…
…
…
…
Querying Unit
V
Querying Unit
V
Arithmetic Unit
IV
Arithmetic Unit
Paradigm: Implements Processing Near DRAM
IV
Performs arithmetic and logical operations required for RSGA
Design: Based on the FULCRUM architecture for leveraging DRAM subarray proximity for low-latency parallel arithmetic operations
1 per two subarrays

## Slide 21: MARS Architecture & System (IV/IV)
SSD-Internal DRAM Components
SSD-Internal DRAM
…
Bank
Bank
…
Subarrays
…
…
…
…
…
Querying Unit
V
Querying Unit
V
Arithmetic Unit
IV
Querying Unit
Paradigm: Implements Processing Using DRAM
V
Performs efficient, in-memory hash table lookups for seeding
Design: Based on the PLUTO2 architecture leveraging DRAM row activation for massively parallel hash-table lookup operations
1 per subarray
Arithmetic Unit
Paradigm: Implements Processing Near DRAM
IV
Performs arithmetic and logical operations required for RSGA
Design: Based on the FULCRUM1 architecture for leveraging DRAM subarray proximity for low-latency parallel arithmetic operations
1 per two subarrays
1: [Lenjani, HPCA’20]; 2: [Ferreira+, MICRO’22]

## Slide 22: Mapping RSGA Workflow to MARS Architecture
Break down RSGA steps into fine-grained tasks
  Arithmetic, querying and sorting operations

## Slide 23: Mapping RSGA Workflow to MARS Architecture
Break down RSGA steps into fine-grained tasks
  Arithmetic, querying and sorting operations
Implement MARS as a pipeline
  Each task mapped to a dedicated compute unit
  e.g., multiplications mapped to arithmetic unit

## Slide 24: Mapping RSGA Workflow to MARS Architecture
Break down RSGA steps into fine-grained tasks
  Arithmetic, querying and sorting operations
Implement MARS as a pipeline
  Each task mapped to a dedicated compute unit
  e.g., multiplications mapped to arithmetic unit
MARS Control Unit encodes pipeline into a Finite State Machine
  Defines a fixed execution sequence
  Dynamically triggers tasks when input data is ready

## Slide 25: Control and Data Flow
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
Flash Memory

## Slide 26: Control and Data Flow (I/VI)
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
Flash Memory
raw input signals
1
Event Detection

## Slide 27: Control and Data Flow (II/VI)
Flash Memory
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
2
Seeding
(Hash-value generation & filtering)

## Slide 28: Control and Data Flow (III/VI)
Flash Memory
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
Arithmetic Unit
IV
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Seeding
(Hash-table querying)
2
…
Querying Unit
…
Querying Unit
V
V

## Slide 29: Control and Data Flow (IV/VI)
Flash Memory
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
Chaining
(Create batches of sequences)
3

## Slide 30: Control and Data Flow (V/VI)
Flash Memory
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Arithmetic Unit
IV
Chaining
(Sorting & Merging)
3
unsorted
sequences
in batches
Merger
Unit
Sorter
Unit
III
II

## Slide 31: Control and Data Flow (VI/VI)
Flash Memory
SSD Controller
SSD-Internal DRAM
Cores
FTL
Flash Controller
…
Bank
Bank
…
Subarrays
.
Merger
Unit
III
…
…
Arithmetic Unit
…
Querying Unit
…
Querying Unit
V
V
.
.
…
MARS
Control
Unit
I
Sorter
Unit
II
Arithmetic Unit
IV
Chaining
(Dynamic programming)
3
sorted
sequences

## Slide 32: Computational Units & System Integration
Arithmetic Unit
    Processing-Near-Memory
    Add Logic near the subarrays
    Column-Selection Latches
Querying Unit
  Processing-Using-Memory
  Add Custom Hash-key Match logic
  and Gated Sense Amplifiers
Sorter and Merger Unit
Inside the SSD controller
Processing-Near-Memory
Bitonic Sorter and Merger
More details on the Mechanism and System Integration
can be found in the paper

## Slide 33: Outline
Conclusion
Background
Motivation and Goal
MARS
Evaluation

## Slide 34: Evaluation Methodology (I/II)
We compare MARS against four systems for our performance and energy analysis
Conventional pipeline with GPU-based basecalling (dorado) and CPU-based read mapping (minimap2)
NVM-based hardware-accelerated pipeline for basecalling & read mapping
State-of the art CPU-based RSGA pipeline
Full MARS hardware-accelerated RSGA system inside the storage subsystem
BC
GenPIP
RH2
[MICRO’22]
MARS software-only RSGA pipeline executed on CPU
MARS-CPU
MARS
Basecalling-based pipeline
RSGA-based pipeline
[Bioinformatics’24]

## Slide 35: Evaluation Methodology (II/II)
We use the following hardware setup and simulate elements of our system setup
Hardware Components
CPU-based baseline
  state-of-the-art server with two AMD® EPYC® CPUs with 64 physical cores
  1-TB DDR4 DRAM
  NVIDIA RTX A6000 GPU (for the BC baseline)
SSD configurations
  8 channels with each 8 flash chips, PCIe 4.0 interface
  4GB LPDDR4 DRAM with 16 banks and 512 subarrays
Simulators Used
Synopsis Design Compiler - for accelerators
MQSim [Tavakkol+, FAST’18] - for SSD-internal operations
CACTI7 [Kim+, CAL’15] - for SSD-internal LPDDR4 DRAM

## Slide 36: Performance Evaluation
Key Observations
Chart: 
| D1 | D2 | D3 | D4 | D5 | GEOMEAN
BC | 0.01 | 0.6 | 0.1 | 0.70385 | 4.7 | 0.2881
GenPIP | 0.02 | 1.5 | 0.2 | 1.9 | 12.7 | 0.7
MARS-CPU2 | 1 | 1 | 1.2 | 10.2 | 1.2 | 1.7
RawGains-FULCRUM | 84.3 | 17.4 | 8 | 44.5 | 32 | 27.8
RawHash2
MARS
1
10
100
D1
D2
D3
D4
D5
GEOMEAN
0.1
BC
MS-CPU
GenPIP
Speedup
MARS outperforms all other baselines across all datasets
MARS outperforms GenPIP adopting PIM outside storage
MARS-CPU provide speedup of ∅1.7x over RH2
We fundamentally solve the I/O data movement overhead problem
Our SW modifications are effective in reducing the computational load
Basecalling-based pipeline
RSGA-based pipeline

## Slide 37: Energy Evaluation
1
10
102
0.1
Energy Reduction
Chart: 
| D1 | D2 | D3 | D4 | D5 | GEOMEAN
BC | 0.01 | 0.8 | 0.3 | 0.70385 | 0.3 | 0.2
GenPIP | 0.07 | 5.6 | 2.1 | 3.1 | 1.3 | 2.5
MARS-CPU | 1.1 | 2.1 | 4 | 7.2 | 1.2 | 3.12
MARS | 217.1 | 103.9 | 211.8 | 295.9 | 68.5 | 179.4
D1
D2
D3
D4
D5
GEOMEAN
RawHash2
MARS
BC
MS-CPU
GenPIP
Basecalling-based pipeline
RSGA-based pipeline
Key Observation
MARS reduces energy consumption over all other baselines across all datasets
Improvement stems from
reduced execution time
fundamentally addressing the I/O data movement overhead

## Slide 38: Outline
Conclusion
Background
Motivation and Goal
MARS
Evaluation

## Slide 39: Conclusion
The first in-storage processing system for end-to-end raw signal genome analysis enables through SW improvements and a HW system inside the storage system
MARS
Improves performance
93× over state-of-the-art software-based basecalling read mapping pipeline
40× over state-of-the-art hardware-accelerated basecalling read mapping pipeline
28× over state-of-the-art software-based RSGA read mapping pipeline
Reduces energy consumption
427× over state-of-the-art software-based read mapping pipeline
72× over state-of-the-art hardware-accelerated read mapping pipeline
180× over state-of-the-art software-based RSGA read mapping pipeline
High accuracy
matches basecalling-based pipelines
improves F1 scores over state-of-the-art RSGA pipeline

## Slide 40: MARS Processing-In-Memory Acceleration of Raw Signal Genome Analysis Inside the Storage Subsystem
Melina Soysal
Mohammad Sadrosadati Onur Mutlu
Konstantina Koliogeorgi Can Firtina Nika Mansouri Ghiasi
Rakesh Nadig Haiyu Mao Geraldo F. Oliveira Yu Liang Klea Zambaku

## Slide 41: BACKUP SLIDES
BACKUP SLIDES

## Slide 42: Ablation Study - Methodology
We conduct an ablation study to find the most suitable system setup of MARS
Full MARS hardware-accelerated RSGA system inside the storage subsystem
MARS with bit-serial PUM-based arithmetic units instead near-DRAM accelerators
MARS with conventional SSD, sorting on ASIC near CPU and external PIM-based DRAM
MARS
MARS-SIMDRAM
MARS with offloaded sorting using an external FPGA near the SSD, replacing in-SSD logic
SmartSSD
MARS-EXTERNAL
RSGA-based pipeline

## Slide 43: Ablation Study - Performance Evaluation
Chart: 
| D1 | D2 | D3 | D4 | D5 | GEOMEAN
RawGains-SIMDRAM | 1.4 | 0.9 | 0.5 | 4 | 1.3 | 1.3
RawGains-ext | 27.5 | 9 | 1.3 | 18.8 | 10.1 | 9.1
SmartSSD | 32.9 | 6.3 | 1.8 | 20.6 | 10.6 | 9.6
RawGains-FULCRUM2 | 84.3 | 17.4 | 8 | 44.5 | 32 | 27.8
1
10
100
D1
D2
D3
D4
D5
GEOMEAN
0.1
8.0
Speedup
RawHash2
MARS
MS-SIMDRAM
SmartSSD
MS-EXT
Key Observations
MARS outperforms all ablation variants across all datasets
MS-EXT lags behind due to high I/O data movement to storage-external compute
SmartSSD performs moderately, but is limited due to FPGA interface BW
MS-EXT is not able to fundamentally tackle the I/O data movement overhead
MARS as only system combining high compute with fundamentally addressing I/O data movement overhead

## Slide 44: Ablation Study - Energy Evaluation
Key Observation
Chart: 
| D1 | D2 | D3 | D4 | D5 | GEOMEAN
RawGains-SIMDRAM | 1739.7 | 166.6 | 466.3 | 507.3 | 269.6 | 629.9
RawGains-ext | 47.2 | 24.5 | 10.7 | 26.7 | 1.9 | 22.3
RG-SYTSEM | 217.1 | 103.9 | 211.8 | 295.9 | 68.5 | 179.4
1
10
102
D1
D2
D3
D4
D5
GEOMEAN
0.1
103
Energy Reduction
RawHash2
MARS
MS-SIMDRAM
MS-EXT
MS-SIMDRAM achieves highest energy reduction, but lowest performance among the ablation variants
Small bit-serial arithmetic unit trades off energy consumption for performance
MS-EXT incurs higher energy cost due to off-chip data movement and increased host involvement
MARS provides the best performance-energy trade-off

## Slide 45: Computational Units
Arithmetic Unit
    Processing-Near-Memory
    Add Logic near the subarrays
    Column-Selection Latches
Querying Unit
  Processing-Using-Memory
  Add Custom Hash-key Match logic
  and Gated Sense Amplifiers
Sorter and Merger Unit
Inside the SSD controller
Processing-Near-Memory
Bitonic Sorter and Merger

## Slide 46: MARS detailed workflow
Notes: Present workflow here?
Hardware acceleration?