## Slide 1
MASK: Redesigning the GPU Memory Hierarchy
to Support Multi-Application Concurrency
Rachata Ausavarungnirun, Vance Miller, Joshua Landgraf, Saugata Ghose, Jayneel Gandhi, Adwait Jog, Christopher J. Rossbach, Onur Mutlu
GPU Core
Private TLB
GPU Core
GPU Core
GPU Core
Shared TLB
Private TLB
Page Table Walkers
Page Table
Private TLB
Private TLB
High TLB Contention
High latency page walks
Data
Private
Shared
Performance Impact of Address Translation
Results
Address Translation Enables GPU Sharing
Methodology
GPGPU-Sim based model of GTX 750 Ti
Multiple GPGPU applications can concurrently execute
Models page walks and page tables
Models virtual-to-physical address mapping
Available at https://github.com/CMU-SAFARI/Mosaic
35 pairs of workloads
3 workload categories based on the TLB hit rate
Issues with State-of-the-Art Address Translation Designs
A page is shared by many threads, causing one translation miss to stall multiple warps
Parallel page walks further reduce the GPU’s latency hiding capability
Chart: Normalized Performance
| 3DS_BP | BLK_LPS | CFD_MM | CONS_LPS | HISTO_GUP | NW_LPS | RAY_GUP | RED_RAY | SCAN_CONS | SCP_HS | SC_FWT | SRAD_3DS | TRD_MUM | TRD_RAY | Average
PWCache | 0.43868 | 0.31185 | 0.53437 | 0.3557 | 0.26918 | 0.44451 | 0.48775 | 0.6844 | 0.62325 | 0.7115 | 0.63488 | 0.55322 | 0.31604 | 0.26119 | 0.544
SharedTLB | 0.55361 | 0.37859 | 0.6646 | 0.45219 | 0.32472 | 0.51551 | 0.62347 | 0.69262 | 0.62018 | 0.79882 | 0.72513 | 0.59066 | 0.39617 | 0.28077 | 0.62644
Ideal | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
MASK: A Translation-Aware Memory Hierarchy for GPUs
High Shared TLB Miss Rate
GPU Does Not Have Any Awareness
of Address Translation Data
Address Translation Data
Is Latency-Sensitive
Inefficient L2 Data Cache Design
Caches only part of the translation requests
Thrashing among multiple address translation requests
Thrashing from normal data demand requests
Translation-Oblivious Memory Scheduler
Address translation requests suffer from high DRAM latency
Chart: Normalized DRAM Bandwidth
| 3DS_BP | 3DS_HISTO | BLK_LPS | CFD_MM | CONS_LPS | CONS_LUH | FWT_BP | HISTO_GUP | HISTO_LPS | LUH_BFS2 | LUH_GUP | MM_CONS | MUM_HISTO | NW_HS | NW_LPS | RAY_GUP | RAY_HS | RED_BP | RED_GUP | RED_MM | RED_RAY | RED_SC | SCAN_CONS | SCAN_HISTO | SCAN_SAD | SCAN_SRAD | SCP_GUP | SCP_HS | SC_FWT | SRAD_3DS | TRD_HS | TRD_LPS | TRD_MUM | TRD_RAY | TRD_RED | Average
Data Demand Requests | 0.4109 | 0.1746 | 0.1959 | 0.1176 | 0.2024 | 0.21 | 0.5583 | 0.1147 | 0.2006 | 0.2103 | 0.2092 | 0.1187 | 0.114 | 0.1476 | 0.1734 | 0.2353 | 0.27 | 0.2247 | 0.074 | 0.07171 | 0.1727 | 0.09862 | 0.6118 | 0.5036 | 0.631 | 0.6362 | 0.5449 | 0.5869 | 0.2958 | 0.3176 | 0.2581 | 0.2872 | 0.2008 | 0.3341 | 0.1802 | 0.23168
Address Translation Requests | 0.04547 | 0.05329 | 0.07564 | 0.05596 | 0.04014 | 0.04526 | 0.03299 | 0.06315 | 0.0459 | 0.03442 | 0.08208 | 0.04407 | 0.0638 | 0.02627 | 0.05074 | 0.06187 | 0.02367 | 0.01361 | 0.06418 | 0.04605 | 0.02256 | 0.07185 | 0.01329 | 0.04016 | 0.01458 | 0.01636 | 0.07109 | 0.0306 | 0.07715 | 0.04678 | 0.02958 | 0.04554 | 0.06961 | 0.03514 | 0.02491 | 0.040258
Results
Chart: Weighted Speedup
Static | 1.6522 | 1.398 | 1.4209 | 1.4566
PWCache | 1.5206 | 1.2418 | 1.3177 | 1.3211
SharedTLB | 1.6649 | 1.489 | 1.5066 | 1.5316
MASK-TLB | 2.2195 | 2.0028 | 2.0287 | 2.057
MASK-Cache | 2.493 | 2.1758 | 2.0525 | 2.1983
MASK-DRAM | 2.0985 | 1.8483 | 1.7886 | 1.8798
MASK | 2.6431 | 2.4073 | 2.2895 | 2.4175
Ideal | 3.7614 | 3.1303 | 2.8272 | 3.1449
Chart: Unfairness
Static | 1.2932 | 1.5988 | 1.549 | 1.5025
PWCache | 1.3604 | 1.7625 | 1.6124 | 1.6694
SharedTLB | 1.2449 | 1.3694 | 1.3888 | 1.3446
MASK | 0.98717 | 1.0272 | 1.0861 | 1.0353
Chart: L2 TLB Miss Rate
| App 1 | App 2 | App 1 | App 2 | App 1 | App 2 | App 1 | App 2
Alone | 0.49324 | 0.39922 | 0.2974 | 0.034602 | 0.91176 | 0.39922 | 0.11742 | 0.64129
Shared | 0.6707 | 0.82203 | 0.42424 | 0.47649 | 0.9443 | 0.78015 | 0.41567 | 0.7585
Highly-parallel page walks lead to cache thrashing
Chart: Average Warp Stall per TLB Miss
| 3DS | BFS2 | BLK | BP | CFD | CONS | FFT | FWT | GUPS | HISTO | HS | JPEG | LIB | LPS | LUD | LUH | MM | MUM | NN | NW | QTC | RAY | RED | SAD | SC | SCAN | SCP | SPMV | SRAD | TRD
Warps Stalled Per TLB Entry | 4.9823 | 22.6714 | 2.0987 | 18.5 | 11.2548 | 8.4803 | 2.1604 | 20.1782 | 4.6016 | 2.7453 | 6.3464 | 2.918 | 2.2253 | 5.4585 | 4.4688 | 4.8093 | 8.7018 | 2.1074 | 5.426 | 1.3605 | 4.1473 | 3.6941 | 6.3519 | 1.2702 | 10.1084 | 17 | 4 | 2.184 | 33.2563 | 22.0693
Chart: Concurrent Page Walk
| 3DS | BFS2 | BLK | BP | CFD | CONS | FFT | FWT | GUPS | HISTO | HS | JPEG | LIB | LPS | LUD | LUH | MM | MUM | NN | NW | QTC | RAY | RED | SAD | SC | SCAN | SCP | SPMV | SRAD | TRD
Concurrent Page Walks | 4.127 | 26.153 | 1.7475 | 19.2579 | 17.6029 | 8.4803 | 2.9958 | 14.3853 | 4.1575 | 2.6093 | 6.2982 | 3.6873 | 1.798 | 4.8382 | 4.0156 | 6.605 | 10.3298 | 1.7541 | 5.3537 | 1.1946 | 6.4307 | 3.6941 | 6.6449 | 1.2017 | 11.2975 | 2 | 2 | 2.1134 | 22.1317 | 17.2586
GPU becomes unable to hide memory latency
45.6% Performance Degradation from Address Translation
3DS_HISTO
CONS_LPS
MUM_HISTO
RED_RAY