## Slide 1
MEMCON
Detecting and Mitigating
Data-Dependent DRAM Failures
by Exploiting Current Memory Content
Samira Khan
Chris Wilkerson, Zhe Wang, Alaa Alameldeen, Donghyuk Lee, Onur Mutlu
Session 1A at 11.20 am

## Slide 2: VISION: SYSTEM-LEVEL DETECTION AND MITIGATION
Unreliable
DRAM Cells
Detect
and
Mitigate
Reliable System
Detect and mitigate errors after
the system has become operational
ONLINE PROFILING

## Slide 3: BENEFITS OF ONLINE PROFILING
Unreliable
DRAM Cells
Reliable
DRAM Cells
Technology
Scaling
Improves yield, reduces cost, enables scaling
Vendors can make cells smaller without a strong reliability guarantee

## Slide 4: BENEFITS OF ONLINE PROFILING
Unreliable
DRAM Cells
LO-REF
HI-REF
HI-REF
LO-REF
LO-REF
2. Improves performance and energy efficiency
Reduce refresh rate, refresh faulty rows more frequently
Reduce refresh count by using a lower refresh rate,
but use higher refresh rate for faulty cells

## Slide 5: DETECTION IS HARD DUE TO INTERMITTENT FAILURES
DATA-DEPENDENT FAILURE
0
1
0
Some cells can fail depending on the
data stored in neighboring cells
FAILURE
1
1
1
NO
FAILURE

## Slide 6: HOW TO DETECT DATA-DEPENDENT FAILURES?
Test with specific data pattern in neighboring cells
LINEAR
MAPPING
X-1
X
X+1
L
D
R
0
1
0

## Slide 7: HOW TO DETECT DATA-DEPENDENT FAILURES?
LINEAR
MAPPING
X-1
X
X+1
L
D
R
0
1
0
Test with specific data pattern in neighboring cells

## Slide 8: HOW TO DETECT DATA-DEPENDENT FAILURES?
Test with specific data pattern in neighboring cells
LINEAR
MAPPING
X-1
X
X+1
L
D
R
0
1
0
SCRAMBLED
MAPPING
X
0
1
0
0
1
0
X-1
X+1

## Slide 9: HOW TO DETECT DATA-DEPENDENT FAILURES?
LINEAR
MAPPING
X-1
X
X+1
L
D
R
0
1
0
SCRAMBLED
MAPPING
X-4
X
X+2
0
1
0
0
1
0
NOT EXPOSED TO THE SYSTEM
Test with specific data pattern in neighboring cells

## Slide 10: MEMCON
SCRAMBLED
MAPPING
0
1
0
X-?
X
X+?
Detects data-dependent failures
without the knowledge of the
DRAM internal address mapping
65%-74%
Reduction in refresh count
40%-50%
Performance improvement using 32Gb DRAM

## Slide 11
MEMCON
Detecting and Mitigating
Data-Dependent DRAM Failures
by Exploiting Current Memory Content
Samira Khan
Chris Wilkerson, Zhe Wang, Alaa Alameldeen, Donghyuk Lee, Onur Mutlu
Session 1A at 11.20 am