## Slide 1
MEMCON
Detecting and Mitigating
Data-Dependent DRAM Failures
by Exploiting Current Memory Content
Samira Khan
Chris Wilkerson, Zhe Wang, Alaa Alameldeen, Donghyuk Lee, Onur Mutlu

## Slide 2: DRAM SCALING TREND
Chart: Year
| 1987.0 | 1990.0 | 1994.0 | 1996.0 | 1998.0 | 2000.0 | 2002.0 | 2005.0 | 2007.0 | 2010.0 | 2014.0
Y-Value 1 | 1 | 4 | 16 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
2X/1.5 YEARS
2X/3 YEARS
Source: Flash Memory Summit 2013, Memcon 2014
DRAM scaling is slowing down

## Slide 3: DRAM SCALING CHALLENGE
DRAM Cells
Technology
Scaling
DRAM Cells
Manufacturing reliable cells at low cost
is getting difficult

## Slide 4: TRADITIONAL APPROACH TO ENABLE DRAM SCALING
Manufacturing Time Testing
PASS
FAIL
1. Manufacturers perform exhaustive testing of DRAM chips
2. Chips failing the tests are discarded

## Slide 5: VISION: SYSTEM-LEVEL DETECTION AND MITIGATION
PASS
FAIL
Not fully tested during
manufacture-time
Ship modules
with possible failures
1
2
Detect and mitigate
failures online
3
Detect and mitigate errors after
the system has become operational
ONLINE PROFILING

## Slide 6: BENEFITS OF ONLINE PROFILING
Unreliable
DRAM Cells
Reliable
DRAM Cells
Technology
Scaling
Improves yield, reduces cost, enables scaling
Vendors can make cells smaller without a strong reliability guarantee

## Slide 7: BENEFITS OF ONLINE PROFILING
Unreliable
DRAM Cells
Improves yield, reduces cost, enables scaling
Vendors can make cells smaller without a strong reliability guarantee
2. Improves performance and energy efficiency
Reliable
DRAM Cells
Reduce
Refresh
HI-REF
LO-REF

## Slide 8
DRAM CELLS ARE NOT EQUAL
Real
Ideal
Smaller cells will fail to retain data at a lower refresh rate
Large variation in retention time
FAST
FAST
Most cells have high retention time 
can be refreshed at a lower rate without any failure
Smallest cell
Notes: Ideally, DRAM would have uniform cells which have same size, thereby having same access latency.
Unfortunately, due to process variation, each cell has different size, thereby having different access latency.
Therefore, DRAM shows large variation in both charge amount in its cell and access latency to its cell.

## Slide 9: BENEFITS OF ONLINE PROFILING
Unreliable
DRAM Cells
LO-REF
HI-REF
HI-REF
LO-REF
LO-REF
Improves yield, reduces cost, enables scaling
Vendors can make cells smaller without a strong reliability guarantee
2. Improves performance and energy efficiency
Reduce refresh rate, refresh faulty rows more frequently
Reduce refresh count by using a lower refresh rate,
but use higher refresh rate for faulty cells

## Slide 10
In order to enable these benefits,
we need to detect the failures
at the system level

## Slide 11: CHALLENGE IN SYSTEM-LEVEL DETECTION AND MITIGATION
Unreliable
DRAM Cells
Detect
and
Mitigate
Reliable System
Depends on accurately detecting DRAM failures
If failures were permanent,
a simple boot up test would have worked,
but there are intermittent failures

## Slide 12: DATA-DEPENDENT FAILURE
0
0
0
FAILURE
NO
FAILURE
1
1
INTERFERENCE
DUE TO
COUPLING
Some cells can fail depending on the
data stored in neighboring cells
JSSC’88, MDTD’02
How can we detect these failures at the system level?
Notes: Y. Nakagome, … Kiyoo Itoh, The Impact of Data-Line Interference Noise on DRAM Scaling, IJSSC’88
M. Redeker, B. F. Cockburn, and D. G. Elliott. An investigation into crosstalk noise in DRAM structures. MTDT, 2002 (Memory Technology, Design and Testing)
J. Liu et al. An experimental study of data retention behavior in modern DRAM devices: Implications for retention time profiling mechanisms, ISCA 2012

## Slide 13: DETECTING DATA-DEPENDENT FAILURES
Testing with specific patterns in neighboring addresses
LINEAR
MAPPING
X-1
X
X+1
L
D
R
0
1
0
SCRAMBLED
MAPPING
X-4
X
X+2
0
1
0
0
1
0
X-1
X+1
NOT EXPOSED TO THE SYSTEM

## Slide 14: CHALLENGE IN DETECTION
How to detect data-dependent failures
when we even do not know
which cells are neighbors?
SCRAMBLED
MAPPING
0
1
0
X-?
X
X+?

## Slide 15
DRAM
System-Level Detection and Mitigation of Failures
MEMCON: DRAM-Internal
Independent Detection
CAL’16, MICRO’17
GOAL
KEY IDEA
CHALLENGE
MECHANISM
PROBLEM:
SCRAMBLED ADDRESS MAPPING
RESULTS

## Slide 16: GOAL: MEMCON
SCRAMBLED
MAPPING
0
1
0
X-?
X
X+?
Detect data-dependent failures
without the knowledge of
the DRAM internal address mapping

## Slide 17: CURRENT DETECTION MECHANISM
Initial Failure Detection and Mitigation
Execution
of Applications
Detect and mitigate all failures with every possible content
Only after that start program execution
Detection is done with some initial testing
isolated from system execution
RAPID HPCA’06, Rethinking Refresh IEEE Micro’08 , RAIDR ISCA’12, SECRET ICCD’12, Dtail SC’14, ProactiveDRAM ICCD’14, REAPER ISCA’17

## Slide 18: CURRENT DETECTION MECHANISM
Unreliable
DRAM Cells
Initial Failure Detection and Mitigation
Detect every possible failure with all content before execution
(All possible
failing cell)
List of Failures

## Slide 19: CURRENT DETECTION MECHANISM
Unreliable
DRAM Cells
Initial Failure Detection and Mitigation
Detect every possible failure with all content before execution
Pattern x, Cell A
(All possible
failing cell)
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
List of Failures

## Slide 20: CURRENT DETECTION MECHANISM
Unreliable
DRAM Cells
Initial Failure Detection and Mitigation
Detect every possible failure with all content before execution
Pattern x, Cell A
Pattern y, Cell B
(All possible
failing cell)
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
List of Failures

## Slide 21: CURRENT DETECTION MECHANISM
Unreliable
DRAM Cells
Initial Failure Detection and Mitigation
Execution
of Applications
Detect every possible failure with all content before execution
Pattern x, Cell A
Pattern y, Cell B
Pattern z, Cell C
…
(All possible
failing cell)
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
List of Failures
Applications

## Slide 22: CURRENT DETECTION MECHANISM
Unreliable
DRAM Cells
Initial Failure Detection and Mitigation
Execution
of Applications
Detect every possible failure with all content before execution
??
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
List of Failures
Applications
The problem is cannot detect all failures
when we do not know the address mapping
No Reliability Guarantee

## Slide 23: MEMCON: MEMORY CONTENT-BASED DETECTION AND MITIGATION
Unreliable DRAM Cells
with Program Content
Simultaneous Detection and Execution
Based on current memory content of running applications
NO NEED TO DETECT EVERY POSSIBLE FAILURE
Current content, Cell A
0
1
0
1
0
0
1
0
0
0
1
0
0
1
0
0
0
0
0
1
Need to detect and mitigate
only with the current content
List of Failures
Application

## Slide 24: MEMCON: HIGH-LEVEL DESIGN
Simultaneous Detection and Execution
No initial detection and mitigation
Start running the application with a high refresh rate
Detect failures with the current memory content
  If no failure found, use a low refresh rate
Unreliable DRAM Cells
0
1
0
1
0
0
1
0
0
0
1
0
0
1
0
0
0
0
0
1
HI-REF
HI-REF
HI-REF
HI-REF
LO-REF
HI-REF
LO-REF
LO-REF
Application
Current content, Cell A

## Slide 25
MEMCON: DRAM-Internal
Independent Detection
CAL’16, MICRO’17
GOAL
KEY IDEA
CHALLENGE
MECHANISM
PROBLEM:
SCRAMBLED ADDRESS MAPPING
RESULTS

## Slide 26: CHALLENGE WITH MEMCON
Unreliable DRAM Cells
with Program Content
NEED TO DETECT FAILURE AT A WRITE
Current content, Cell ??
0
1
0
1
0
0
1
0
0
0
1
0
1
1
0
0
0
0
0
1
Testing at every write is expensive!!!
Write access
to row A

## Slide 27
MEMCON: COST-BENEFIT ANALYSIS
The cost of testing
Extra memory accesses to read and write rows
The benefit of testing
If no failure found, can reduce refresh rate

## Slide 28
MEMCON: COST-BENEFIT ANALYSIS
64 ms
LO-REF
Testing
Time
Cost
write1
write2
16 ms
HI-REF
Testing
Short write interval 
High average cost
Write Interval Length
Using HI-REF is better when write interval length is short
Avg cost
Avg cost
Frequent testing introduces high cost

## Slide 29
MEMCON: COST-BENEFIT ANALYSIS
The higher the write interval length,
the higher is the benefit
Can amortize the cost of testing with long intervals
16 ms
HI-REF
64 ms
LO-REF
Testing
Time
Cost
write1
write2
Testing
Write Interval Length
Write Interval Length
Benefit

## Slide 30
Chart: Time (ms)
| 16.0 | 64.0 | 112.0 | 160.0 | 208.0 | 256.0 | 304.0 | 352.0 | 400.0 | 448.0 | 496.0 | 544.0 | 592.0 | 640.0 | 688.0 | 736.0 | 784.0 | 832.0 | 880.0 | 928.0 | 976.0 | 1024.0 | 1072.0 | 1120.0 | 1168.0 | 1216.0 | 1264.0 | 1312.0 | 1360.0 | 1408.0 | 1456.0 | 1504.0 | 1552.0 | 1600.0 | 1648.0 | 1696.0 | 1744.0 | 1792.0 | 1840.0
Testing (64 ms) | 0 | 1602 | 1641 | 1680 | 1680 | 1719 | 1758 | 1797 | 1797 | 1836 | 1875 | 1914 | 1914 | 1953 | 1992 | 2031 | 2031 | 2070 | 2109 | 2148 | 2148 | 2187 | 2226 | 2265 | 2265 | 2304 | 2343 | 2382 | 2382 | 2421 | 2460 | 2499 | 2499 | 2538 | 2577 | 2616 | 2616 | 2655
HI-REF (16 ms) | 39 | 156 | 273 | 390 | 507 | 624 | 741 | 858 | 975 | 1092 | 1209 | 1326 | 1443 | 1560 | 1677 | 1794 | 1911 | 2028 | 2145 | 2262 | 2379 | 2496 | 2613 | 2730 | 2847 | 2964 | 3081 | 3198 | 3315 | 3432 | 3549 | 3666 | 3783 | 3900 | 4017 | 4134 | 4251 | 4368 | 4485
MEMCON: COST BENEFIT ANALYSIS
What is the write interval that can amortize the cost?
864 ms
MinWriteInterval

## Slide 31
MEMCON: MECHANISM
Time
How much longer??
Write Requests
How do we predict the interval on a write access?
MEMCON selectively initiates testing
when the write interval is long enough
to amortize the cost of testing

## Slide 32
MEMCON: DRAM-Internal
Independent Detection
CAL’16, MICRO’17
GOAL
KEY IDEA
CHALLENGE
MECHANISM
PROBLEM:
SCRAMBLED ADDRESS MAPPING
RESULTS

## Slide 33
32 seconds of execution on a real machine
Profiled with a custom FPGA-based infrastructure

## Slide 34
Chart: x (ms)
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32768.0
 | 0.049855 | 0.040637 | 0.03285 | 0.026697 | 0.023227 | 0.020037 | 0.014067 | 0.0025293 | 0.00080372 | 0.00038265 | 0.000278 | 0.00020603 | 0.00015434 | 0.00011346 | 7.9115e-05 | 6.1875e-05
ACBrotherhood
WRITE INTERVAL CHARACTERISTICS
The longer the elapsed time after a write
 The longer the write interval
Chart: x (ms)
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32768.0
 | 0.034186 | 0.03293 | 0.032054 | 0.027742 | 0.018466 | 0.0088843 | 0.0048625 | 0.0023542 | 0.00026849 | 0.000188 | 0.00014054 | 0.0001041 | 6.2711e-05 | 5.4556e-05 | 4.7643e-05 | 4.2502e-05
Write intervals follow a Pareto distribution
Netflix
Notes: Actually we find that write intervals follow a pareto distribution. According to pareto distribution, if we plot the probability of write intervals in a log log scale, it should be linear and we find that distributions closely matches to that, the R2 values are pretty high.
We actually leverage a property of the pareto distribution to predict the write intervals. The decrasing hazard rate property of pareto distribution says that the longer the elapsed time after a write, the longer the write interval

## Slide 35
Current
Interval
Length
(CIL)
Remaining
Interval
Length
(RIL)
Time
Write Interval Length
The longer the CIL
 It is expected that the longer the RIL
WRITE INTERVAL CHARACTERISTICS
Write Requests
T
Notes: So let’s define some terminology for write intervals. Current interval length is the elapsed time after a write and the RIL is remaining interval length. And pareto distrbtion says the the longer the CIL, it is expected that the longer the RIL

## Slide 36
WRITE INTERVAL CHARACTERISTICS
Chart: Current Interval Length (CIL) in ms
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32768.0
ACBrotherHood | 0.005572 | 0.006831 | 0.00844 | 0.010363 | 0.011875 | 0.013671 | 0.0193 | 0.10577 | 0.32323 | 0.62416 | 0.74113 | 0.84069 | 0.90304 | 0.94705 | 0.97119 | 0.9866
AdobePhotoshop | 0.17542 | 0.20995 | 0.28108 | 0.37299 | 0.45542 | 0.53918 | 0.60393 | 0.69187 | 0.77741 | 0.82771 | 0.8892 | 0.94567 | 0.92744 | 0.95662 | 0.93881 | 0.82904
AllSysMark | 0.16874 | 0.19341 | 0.21935 | 0.26602 | 0.31043 | 0.36591 | 0.42211 | 0.51624 | 0.63186 | 0.78628 | 0.84344 | 0.90704 | 0.94765 | 0.96296 | 0.98599 | 0.9865
AVCHD | 0.033405 | 0.036794 | 0.039417 | 0.042267 | 0.047878 | 0.058975 | 0.11042 | 0.27886 | 0.47748 | 0.61731 | 0.73664 | 0.8629 | 0.60954 | 0.91589 | 0.96685 | 0.96223
Blur | 0.029661 | 0.042756 | 0.056648 | 0.072632 | 0.096072 | 0.12808 | 0.2383 | 0.47821 | 0.57898 | 0.67756 | 0.70523 | 0.78672 | 0.90937 | 0.88985 | 0.67375 | 0.98344
FinalCutProPlayback | 0.047355 | 0.053885 | 0.060356 | 0.068851 | 0.080948 | 0.10063 | 0.15114 | 0.22293 | 0.34748 | 0.4521 | 0.51579 | 0.87627 | 0.865 | 0.94002 | 0.96932 | 0.97905
FinalMaster | 0.005665 | 0.005929 | 0.00611 | 0.006303 | 0.006596 | 0.010667 | 0.033796 | 0.0449 | 0.28236 | 0.63892 | 0.79526 | 0.84978 | 0.95568 | 0.98573 | 0.9975 | 0.99565
AdobePremierePro | 0.030306 | 0.034884 | 0.037727 | 0.039965 | 0.046026 | 0.057512 | 0.098325 | 0.23231 | 0.46111 | 0.53524 | 0.7386 | 0.93136 | 0.7557 | 0.87357 | 0.9871 | 0.97372
MotionPlayback | 0.020151 | 0.021192 | 0.022229 | 0.024221 | 0.025859 | 0.026107 | 0.026247 | 0.033487 | 0.087433 | 0.76363 | 0.79632 | 0.90063 | 0.34396 | 0.95976 | 0.95713 | 0.98727
Netflix | 0.004104 | 0.004253 | 0.004356 | 0.005001 | 0.007426 | 0.015123 | 0.026739 | 0.053524 | 0.45251 | 0.60686 | 0.74072 | 0.74815 | 0.95175 | 0.97988 | 0.99354 | 0.99534
SystemMgt | 0.17686 | 0.20707 | 0.24317 | 0.29331 | 0.35812 | 0.48317 | 0.58103 | 0.6495 | 0.71001 | 0.76993 | 0.86616 | 0.90013 | 0.98186 | 0.98697 | 0.98972 | 0.98568
VideoEncode | 0.17004 | 0.18966 | 0.20954 | 0.2312 | 0.25346 | 0.28506 | 0.41141 | 0.50122 | 0.55332 | 0.58436 | 0.70253 | 0.70975 | 0.96149 | 0.98221 | 0.9806 | 0.97665
If the interval is already 1024 ms long,
the probability that the remaining interval
is greater than 1024 ms is on average 76%
Notes: In order to see if this is true, here is plot the probability of RIL being greater than 1024 ms when we vary CIL
And we see that it is true that the probability increases as we increase CIL. Actually, if the CIL becomes 1024 ms, the probability that the remaining interval length is greater than becomes on average 76%

## Slide 37
How do we predict the interval on a write access?
Time
How much longer??
Write Requests
Notes: So remember that, we are trying to predict the write interval on a write and trying to decide if MEMCON should initiate the testing

## Slide 38
WRITE INTERVAL PREDICTION
Wait for
1024 ms
Expected
RIL > 1024 ms
Time
Write Interval Length
Write Requests
After a write, wait for a CIL, where P(RIL) > 1024 is high
If idle, predict the interval will last more than 1024 ms
Notes: So we just wait for 1024 ms and if there is no other write, we can predict the the RIL would be more than 1024 ms

## Slide 39
MEMCON: DRAM-Internal
Independent Detection
CAL’16, MICRO’17
GOAL
KEY IDEA
CHALLENGE
MECHANISM
PROBLEM:
SCRAMBLED ADDRESS MAPPING
RESULTS

## Slide 40: MEMCON: REDUCTION IN REFRESH COUNT
Chart: % Reduction in Refresh Over Baseline
| ACBrother | AdobePhoto | AllSysMark | AVCHD | BlurMotion | FinalCutPro | FinalMaster | AdobePrem | MotionPlay | Netflix | SystemMgt | VideoEnc
Column1 | 72.273 | 74.1767 | 74.4159 | 68.0876 | 74.4285 | 72.1889 | 72.6455 | 68.5998 | 64.745 | 69.1286 | 74.4353 | 72.1651
UPPER BOUND
71% average reduction in refresh count,
very close to the upper bound of 75%

## Slide 41: MEMCON: PERFORMANCE IMPROVEMENT DUE TO REDUCTION IN REFRESH COUNT
Chart: Speedup over Baseline (16 ms)
| 8Gb | 16Gb | 32Gb
60% Reduction | 1.1026 | 1.1764 | 1.4079
75% Reduction | 0.025571 | 0.044008 | 0.10114
Chart: Speedup over Baseline (16 ms)
| 8Gb | 16Gb | 32Gb
60% Reduction | 1.1013 | 1.2358 | 1.5215
75% Reduction | 0.040869 | 0.057572 | 0.13021
Four-Core
Single-Core
Refresh reduction leads to
significant performance improvement
50%
40%
65%
52%

## Slide 42
SCRAMBLED MAPPING
0
1
0
X-?
X
X+?
Goal: MEMCON detects and mitigates data-dependent failures without the knowledge of the DRAM internal address mapping
MEMCON: SUMMARY
Key Idea: Instead of detecting every possible failure, detects failure based on the current content
Problem:
Mechanism: Selective testing mechanism based on write interval length
Initiates a test only when can amortize the cost
Challenge: Content changes with writes, testing at every write is expensive
65%-74%
Reduction in refresh count
40%-50%
Performance improvement using 32Gb DRAM (1 core)
Results:

## Slide 43
MEMCON
Detecting and Mitigating
Data-Dependent DRAM Failures
by Exploiting Current Memory Content
Samira Khan
Chris Wilkerson, Zhe Wang, Alaa Alameldeen, Donghyuk Lee, Onur Mutlu

## Slide 44: DATA-DEPENDENT FAILURE

## Slide 45: DRAM Testing Infrastructure
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Notes: This is the photo of our infrastructure, that we built mostly from scratch.
For higher throughput, we employ eight FPGAs, all of which are enclosed in thermally-regulated environment.

## Slide 46: NUMBER OF FAILING ROWS WITH PROGRAM CONTENT
Chart: Percentage of Rows
| PERL | BZIP | GCC | MCF | ZEUSMP | CACTUS | NAMD | GOBMK | DEALII | SOPLEX | CALCULIX | HMMER | GEMS | LIBQUANT | H264REF | TONTO | LBM | OMNETPP | ASTAR | XALANC | ALL FAIL
 | 2.7139 | 2.7084 | 2.1233 | 3.2147 | 0.98412 | 2.478 | 3.8986 | 1.5263 | 1.9984 | 2.1173 | 2.784 | 5.621 | 4.9404 | 2.5926 | 1.8692 | 2.4544 | 4.7769 | 2.8009 | 0.38033 | 2.6367 | 13.4933
Tested with program content in real DRAM chips
Program content exhibits significantly less failures

## Slide 47
MEMCON: COST-BENEFIT ANALYSIS
Cost: Extra memory accesses to read and write rows
Benefit: If no failure found, can reduce refresh rate
Avg Cost
Avg Cost
16 ms
HI-REF
64 ms
LO-REF
Testing
Testing
Testing
Time
Cost
t1
t2
t3
16 ms
HI-REF
64 ms
LO-REF
Testing
16 ms
HI-REF
Time
Cost
t1
t2
t3
Initiate a test only when the cost can amortized
Frequent Testing
Selective Testing

## Slide 48: MEMCON: READ AND COMPARE
0
0
1
0
1
Benefit: If no failure found,
can reduce refresh rate
Aggressively refreshed before testing
Memory Controller
1. Read the entire row
16 ms
HI-REF
2. Wait for 64 ms
3. Read and compare
64 ms
LO-REF
00101

## Slide 49: MEMCON: COPY AND COMPARE
0
0
1
0
1
Benefit: If no failure found,
can reduce refresh rate
Aggressively refreshed before testing
Memory Controller
Copy the entire row
Keep ECC info in MC
16 ms
HI-REF
2. Wait for 64 ms
3. Read and compare
64 ms
LO-REF
0
0
1
0
1
0
0
1
0
1
01

## Slide 50
MEMCON: COST-BENEFIT ANALYSIS
Cost: Extra memory accesses
to read and write rows while testing
1. READ AND COMPARE
  Read in-test row in the memory controller
2. COPY AND COMPARE
  Copy in-test row in some other region in memory
Benefit: If no failure found,
can reduce refresh rate

## Slide 51
WRITE INTERVAL CHARACTERISTICS
Chart: Write Interval in ms
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32768.0
ACBrotherHood | 95.0145 | 0.92181 | 0.77866 | 0.6153 | 0.34707 | 0.31894 | 0.59707 | 1.1537 | 0.17256 | 0.042107 | 0.010465 | 0.0071965 | 0.0051696 | 0.0040879 | 0.0034343 | 0.0017239
Chart: Write Interval in ms
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0 | 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0 | 16384.0 | 32768.0
Netflix | 96.5814 | 0.12555 | 0.087605 | 0.43122 | 0.92758 | 0.95819 | 0.40218 | 0.25083 | 0.20857 | 0.0080489 | 0.0047465 | 0.0036438 | 0.0041388 | 0.00081552 | 0.00069128 | 0.00051408
ACBrotherhood
Netflix
Only a small fraction of the writes exhibit long intervals
but
Few long intervals
Few long intervals

## Slide 52
Chart: Percentage of Execution Time Spent on Write Intervals
| ACBrother | AdobePhoto | AllSysMark | AVCHD | BlurMotion | FinalCut | FinalMaster | AdobePrem | MotionPlay | Netflix | SystemMgt | VideoEnc
Write Interval < 1024 ms | 16.8732 | 0.9167 | 0.35843 | 12.7984 | 8.2422 | 14.1483 | 8.6266 | 10.2779 | 33.9498 | 17.6678 | 0.24588 | 1.1799
Write Interval >= 1024 ms | 83.1268 | 99.0833 | 99.6416 | 87.2016 | 91.7578 | 85.8517 | 91.3734 | 89.7221 | 66.0502 | 82.3322 | 99.7541 | 98.8201
WRITE INTERVAL CHARACTERISTICS
These long intervals constitute the majority of the time
spent on write intervals

## Slide 53
Quantum Length = CIL (e.g, 1024 ms)
Predicted to have a long write interval if
Receives a single write in quantum 1
And no write in quantum 2
PREDICTING WRITE INTERVAL
Time
Quantum 1
Write Requests
Quantum 2
Page X, Page Y
One Write
No Write
Page X, Page Y
Quantum 3
Notes: We use a simple mechanism to

## Slide 54: MEMCON: REDUCTION IN REFRESH COUNT
Chart: Current Interval Length (CIL)
| 512.0 | 1024.0 | 2048.0
Column1 | 71.6582 | 71.4408 | 71.0651
UPPER BOUND
On average 71% reduction in refresh count,
very close to the upper bound of 75%