## Slide 1
MIMDRAM An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing
Geraldo F. Oliveira |  | 
Ataberk Olgun | A. Giray Yağlıkçı | F. Nisa Bostancı
Saugata Ghose | Juan Gómez-Luna | Onur Mutlu
2024 International Symposium on High-Performance Computer Architecture
Notes: Hi, I am Geraldo, a PhD student at the SAFARI Research Group.
Today, I will talk about our work MIMDRAM: An End-to-End Processing-using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple Data Computing.
So, let’s get started.
[NEXT]

## Slide 2: Executive Summary
Key Mechanism: MIMDRAM, a hardware/software co-design PUD system
Key idea: leverage fine-grained DRAM for PUD operation
HW: - simple changes to the DRAM array, enabling concurrent PUD operations - low-cost interconnects at the DRAM peripherals for data reduction
SW: - compiler and OS support to generate and map PUD instructions
Goal: Design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
Key Results: MIMDRAM achieves
14.3x, 30.6x, and 6.8x the energy efficiency of state-of-the-art PUD systems, a high-end CPU and GPU, respectively
Small area cost to a DRAM chip (1.11%) and CPU die (0.6%)
https://github.com/CMU-SAFARI/MIMDRAM
Problem: Processing-Using-DRAM (PUD) suffers from three issues caused by DRAM’s large and rigid access granularity
Underutilization due to data parallelism variation in (and across) applications
Limited computation support due to a lack of interconnects
Challenging programming model due to a lack of compilers
Notes: Before we start, I will give a summary of OUR work.
Processing-in-memory architectures are emerging solutions to mitigate data movement bottlenecks by moving computation where the data resides. In particular, processing using DRAM is a PIM architecture that utilizes DRAM’s analog operating principles to implement bulk operations.
[CLICK] Even though processing-using-DRAM can often accelerate many application domains, they suffer from three issues caused by DRAM’s large and rigid access granularity
[CLICK] First, they suffer from under-utilization due to a mismatch in the data parallelism in applications and DRAM’s data parallelism
[CLICK] Second, they suffer from limited computation support, in particular for reduction operations, due to a lack of native interconnects for data movement within a DRAM array
[CLICK] Third, programming processing using-DRAM architectures is a challenging task due to a lack of automation tools
[CLICK] Therefore, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[CLICK] To this end, we propose MIMDRAM, a hardware/software co-designed PUD system
[CLICK] The key idea of MIMDRAM is to leverage fine-grained DRAM for PUD operation, which is, the ability to access only segments of a DRAM row. We leverage such key idea in both hardware and software
[CLICK] On the hardware-side, we implement simple modifications to the DRAM array to enable the allocation of only the resources required for a PUD operation. This also allows MIMDRAM to concurrently execute independent PUD operations in a single DRAM array.
We also implement low-cost interconnects at the DRAM peripheral logic, enabling native in-DRAM vector reduction.
[CLICK] On the software side, we implement compiler and operating system support to generate and map PUD operations to the underlying hardware substrate.
[CLICK[ We extensively evaluation MIMDRAM, and we observe that it achieves
[CLICK] significant performance and energy efficiency gains compared to state-of-the-art PUD systems, a high-end CPU and GPU
[CLICK] while incuring low area cost to a DRAM chip and CPU die.
[NEXT]

## Slide 3: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: So let’s get started.
[NEXT]

## Slide 4: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 5: Processing-in-Memory: Overview
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
…
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
Notes: In this work, we focus on processing-using-memory architectures. In particular, its implementation using DRAM.
Before I introduce processing-using-DRAM architectures, I will provide a short background on DRAM organization and operation.
[NEXT]

## Slide 6: Background: DRAM Hierarchical Organization
local sense amplifier
local row decoder
bitline
wordline
DRAM subarray
(e.g., 65,536 rows)
DRAM mat
(e.g., 512 rows/columns)
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: DRAM chips are hierarchically organized.
[CLICK] On the bottom level, we have a DRAM mat, which is a 2D array of DRAM cells
[CLICK] Rows in a DRAM mat share a wordline,
[CLICK] and columns share a bitline
[CLICK] Columns are connected to a set of local sense amplifiers
[CLICK] and rows are connected to a local row decoder
[CLICK] Multiple DRAM mats constitute a DRAM subarray
[NEXT]

## Slide 7: Background: DRAM Hierarchical Organization
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: The many mats in a DRAM subarray are indexed using a global row decoder, which propagates the target row address across all mats using the global wordline
[CLICK] To move data outside a mat, a DRAM subarray uses a global sense amplifier,
[CLICK] and to move data outside a DRAM subarray, a DRAM chip uses the I/O logic interface
[NEXT]

## Slide 8: Background: DRAM Operation – Row Access (ACTIVATE)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: To access data, the memory controller executes two main operations.
[CLICK] To access a DRAM row, the memory controller issues an ACTIVATE command to DRAM. On receiving an ACT, the global and local row decoder assess the wordline of the target row, connecting the DRAM cells to the bitlines
[CLICK] Then, the sense amplifier senses the perturbation caused in the bitline, amplifying and latching the data from the DRAM cells
[NEXT]

## Slide 9: Background: DRAM Operation – Column Access (READ)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
column
to memory channel
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
global wordline
Notes: Then, the memory controller issues a read command to read a column of data from the previously latched DRAM row.
[CLICK] The read command moves the target DRAM column from the local sense amplifiers to the global sense amplifier and finally to the memory channel via the I/O interface
[NEXT]

## Slide 10: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
← src
← dst
Notes: The operating principles of DRAM can be used to implement bulk-bitwise operations inside DRAM. For example, RowClone implements in-DRAM row copy operation by issuing back-to-back ACTIVATE commands to DRAM
[CLICK] The first activate copies the source row into the local sense amplifier
[NEXT]

## Slide 11: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
Notes: The second activate connects the destination row to the local sense amplifier.
[CLICK] which allows the previously-latched source row to be written back to the destination row.
[NEXT]

## Slide 12: Background: In-DRAM Majority Operations
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority is performed by simultaneously activating three DRAM rows
← src3
← src2
← src1
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 13: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 14: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 15: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← tmp
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
A
Sum
MAJ
Cout
MAJ
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 16: Background: Bulk Bitwise Arithmetic Operations
← A
← tmp
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 17: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 18: Background: Bulk Bitwise Arithmetic Operations
← Cin
← B
← A
← Sum
← Cout
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 19: Background: PUD in Commodity Off-the-Shelf DRAM
Commodity off-the-shelf DRAM chips can perform bulk bitwise operations without hardware modifications
https://arxiv.org/pdf/2402.18736.pdf
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 20: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Next, let’s look at the limitations of PUD systems
[NEXT]

## Slide 21: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Processing-using-DRAM architectures suffers from three main limitations due to the rigid and large DRAM access granularity
[CLICK] First, they suffer from SIMD underutilization
[CLICK] Second, they suffer from a limited computation support
[CLICK] Third, they have a challenging programming model
Let me elaborate on each limitation next
[NEXT]

## Slide 22: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Starting with the SIMD underutilization
[NEXT]

## Slide 23: Limitations of PUD Systems: Underutilization of SIMD Lanes (I)
Ideal maximum vectorization factor = # DRAM columns (e.g., 65,536)
Application Analysis: quantify the fraction of SIMD parallelism in real applications
Maximum Vectorization Factor:
maximum number of scalar operands that fit into a SIMD register
row decoder
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: In order to understand the amount of data parallelism a processing-using-DRAM architecture can leverage, we quantify the SIMD parallelism in real applications
[CLICK] To do so, we use the maximum vectorization factor metric, which is the maximum number of scalar operands that fit into a SIMD register a given loop
[CLICK] To achieve high SIMD utilization, the ideal maximum vectorization factor of a loop should match the number of DRAM columns in a DRAM subarray
[NEXT]

## Slide 24: Limitations of PUD Systems: Underutilization of SIMD Lanes (II)
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: In our application analysis, we collect the maximum vectorization of all vectorizable loops in twelve applications, and report their distribution using box plots, where whiskers extend to the maximum and minimum values, and a bubble depicts averages
[CLICK] As a reference, any value above the green line represents high SIMD utilization for a PUD system.
We draw two key observations.
[NEXT]

## Slide 25: Limitations of PUD Systems: Underutilization of SIMD Lanes (II)
SIMD parallelism significantly varies within a single application and across different applications
Takeaway
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: [CLICK] First, SIMD parallelism significantly varies within and across applications
[NEXT]

## Slide 26: Limitations of PUD Systems: Underutilization of SIMD Lanes (III)
A small fraction of vectorized loops have a large enough maximum vectorization factor to fully exploit the SIMD parallelism of PUD systems
Takeaway
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Application Analysis: quantify the fraction of SIMD parallelism in real applications
High Utilization
Low Utilization
Notes: Second, only very few loops have enough data parallelism to achieve high SIMD utilization of the processing-using-DRAM architecture.
[NEXT]

## Slide 27: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Let’s now look at the second issue.
[NEXT]

## Slide 28: Limitations of PUD Systems: Limited Computation Support
row decoder
PUD systems do not support vector reduction at low area cost since data movement is bounded to within a DRAM column
Directly connecting all DRAM columns
using a custom all-to-all interconnect
leads to large (i.e., 21%) area cost
Takeaway
no direct communication path across columns
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Processing-using-DRAM can only support parallel map operations. Unfortunally, this limits processing-using-DRAM applicability, since commonly used reduction operations cannot be implemented natively.
The limiting factor to implement in-DRAM vector reduction is the lack of direct communication path across the many DRAM columns in a subarray
[CLICK] directly connecting all DRAM columns using custom fabric leads to large area costs
[NEXT]

## Slide 29: Limitations of PUD Systems: Overview
1
SIMD Underutilization
due to data parallelism variation within and across applications
leads to throughput and energy waste
2
Limited Computation Support
due to a lack of low-cost interconnects across columns
limits PUD operations to only parallel map constructs
3
Challenging Programming Model
due to a lack of compiler support for PUD systems
creates a burden on programmers, limiting PUD adoption
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD systems suffer from three sources of inefficiency due to the large and rigid DRAM access granularity
Notes: Third, processing-using-DRAM suffers from a challenging programming model

## Slide 30: Limitations of PUD Systems: Challenging Programming Model
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
 |  |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Currently, processing-using-DRAM pototypes use assembly-like programming models, which leaves several key tasks for the programmer to manually handle. I will illustrate such tasks with a simple predicated addition/subtraction operation
[NEXT]

## Slide 31: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures |  |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: A programmer needs to map and align the data structures involved in the computation respecting DRAM’s organization.

## Slide 32: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries |  |  |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Identify the array boundaries of the target loops

## Slide 33: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions |  | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: Manually vectorize the target loop, while worrying to feed as many data operands to the DRAM array as possible, for high utilization
[NEXT]

## Slide 34: Limitations of PUD Systems: Challenging Programming Model
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions | Orchestrate data movement | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
for (int i = 0; i < size ; ++ i){
bool cond = A[i] > pred[i];
if (cond) C[i] = A[i] + B[i];
else C[i] = A[i] - B[i];
}
High-level code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: and manually orchestrate data movement across dependent operands.
[NEXT]

## Slide 35: Limitations of PUD Systems: Challenging Programming Model
bbop_trsp_init(A , size , elm_size);
bbop_trsp_init(B , size , elm_size);
bbop_trsp_init(C , size , elm_size);
bbop_add(D , A , B , size , elm_size);
bbop_sub(E , A , B , size , elm_size);
bbop_greater(F , A , pred , size , elm_size);
bbop_if_else(C , D , E , F , size , elm_size);
Map & align data structures | Identify array boundaries | Manually unroll loop | Map C to PUD instructions | Orchestrate data movement | Just write my kernel
Programmer’s Tasks:
Goal:
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
PUD’s assembly-like code for C[i] = (A[i] > pred[i])? A[i] + B[i] : A[i] – B[i]
Notes: As a result, the produced processing-using-DRAM code is often complicated and potentially inefficient
[NEXT]

## Slide 36: Problem & Goal
Processing-Using-DRAM’s large and rigid granularity limits its applicability and efficiency for different applications
Problem
Design a flexible PUD system that overcomes the three limitations caused by large and rigid DRAM access granularity
Goal
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: [CLICK] To summarize, PUD’s rigid granularity limits their applicability and efficiency for different applications
[CLICK] Thus, our goal in this work is to design a flexible PUD system that overcomes the three limitations caused by DRAM’s large and rigid access granularity
[NEXT]

## Slide 37: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: To this end, we propose MIMDRAM
[NEXT]

## Slide 38: MIMDRAM: Key Idea (I)
DRAM’s hierarchical organization can enable fine-grained access
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 39: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segments the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 40: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 41: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 42: MIMDRAM: Key Idea (III)
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 43: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 columns
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 44: MIMDRAM: Overview
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Based on that, we proposed MIMDRAM, a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and low programming effort
[CLICK] MIMDRAM constitutes of hardware and
[CLICK] software components, which I will elaborate on next.
[NEXT]

## Slide 45: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Let’s start with MIMDRAM’s hardware overview
[NEXT]

## Slide 46: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting from its DRAM array modifications for fine-grained PUD computation
[NEXT]

## Slide 47: MIMDRAM: DRAM Array Modifications
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
mat selector
mat range
isolation transistors
row decoder latch
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: We modify a DRAM array circuitry with four main components
[CLICK] First, the isolation transistors segment the global wordline, allowing a single mat to be activated
[CLICK] The row decoder latch stores the address of the currently activated row for a mat, allowing the row decoder to issue an request to a different row
[CLICK] The mat selector asserts the isolation transistors
[CLICK] based on a mat range specified by the PUD operation. The mat range addresses a physically contiguous set of DRAM mats
[NEXT]

## Slide 48: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Next, let’s talk about how to move data in a mat.
[NEXT]

## Slide 49: MIMDRAM: Background on DRAM Column Access
row decoder
IO interface
8 bits
global wordline
During a column access, data is locally and globally amplified to improve signal integrity
global
sense amplifier
helper FFs
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: But before, I need to provide further background on a DRAM column access
During a DRAM column access, data is locally and globally amplified to improve signal integrity
The data column is first latched in the local sense amplifier.
[NEXT]

## Slide 50: MIMDRAM: Background on DRAM Column Access
row decoder
IO interface
8 bits
global wordline
global
sense amplifier
helper FFs
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
During a column access, data is locally and globally amplified to improve signal integrity
Notes: And then latched and amplified using helper flip-flops at the peripheral logic mats
[NEXT]

## Slide 51: MIMDRAM: Background on DRAM Column Access
row decoder
IO interface
8 bits
global wordline
global
sense amplifier
helper FFs
column
column
column
column
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
During a column access, data is locally and globally amplified to improve signal integrity
Notes: Then, the data is moved from the helper flip-flops into the global sense amplifiers
[NEXT]

## Slide 52: MIMDRAM: Background on DRAM Column Access
During a column access, data is locally and globally amplified to improve signal integrity
row decoder
IO interface
8 bits
global wordline
global
sense amplifier
helper FFs
column
column
column
column
Leverage the shared local and global amplification paths to move data across and within DRAM mats
Key Idea
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Our key idea to move data within a DRAM subarray is to leverage the local and global amplification paths already present within a DRAM mat and subarray
[NEXT]

## Slide 53: MIMDRAM: Moving Data Across Mats
row decoder
global wordline
mat selector
mat range
isolation transistors
row decoder latch
IO interface
inter-mat
interconnect
global
sense amplifier
helper FFs
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: First, we implement an inter-mat interconnect at the DRAM peripheral to move data across mats.
The inter-mat interconnect creates a path between adjacent global sense amplifiers.
[NEXT]

## Slide 54: MIMDRAM: Moving Data Across Mats
row decoder
global wordline
mat selector
mat range
isolation transistors
row decoder latch
IO interface
inter-mat
interconnect
global
sense amplifier
helper FFs
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: This data path allows us to move data across adjacent DRAM mats
[NEXT]

## Slide 55: MIMDRAM: Moving Data Within a Mat
helper FFs
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: We leverage the helper flip-flops’ in a DRAM mat to move data within a DRAM mat.
First, we latch the source column into the helper flip-flop of the DRAM mat
[NEXT]

## Slide 56: MIMDRAM: Moving Data Within a Mat
helper FFs
Helper flip-flops latches and drives
source column into the destination column
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Second, we change the column address to that of the destination column without erasing the data previously stored in the helper flip-flop. This allows the helper-flip-flop to drive the source column into the destination column
[NEXT]

## Slide 57: MIMDRAM: In-DRAM Vector Reduction (I)
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: We leverage the inter-and intra-mat interconnects to implement in-DRAM vector reduction in three steps that implement a reduction three.
Let’s assume that we want to sum all elements of two vectors into a single element. We use two DRAM mats in this example.
[NEXT]

## Slide 58: MIMDRAM: In-DRAM Vector Reduction (II)
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
step 1: C = A + B
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
Notes: To do so, we first compute the target PUD operation using both data elements

## Slide 59: MIMDRAM: In-DRAM Vector Reduction (III)
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
step 2: inter-mat data movement
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
Notes: Then, we move the result of the first computation in the first DRAM mat to the second DRAM mat via the inter-mat network

## Slide 60: MIMDRAM: In-DRAM Vector Reduction (IV)
local
row buffer
global
row buffer
mat1
mat0
A[1]
B[1]
A[0]
B[0]
C[1]
C[0]
inter-mat interconnect
tmp
out
step 3: out = C[1] + tmp
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM leverages fine-grained DRAM access and inter-/intra-mat interconnects to implement in-DRAM vector reduction
Notes: Once the data from the first mat is in the second mat, we can once again compute the reduction step using only the second mat
[NEXT]

## Slide 61: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Finally, I will briefly discuss our control unit design
[NEXT]

## Slide 62: MIMDRAM: Control Unit
The control unit schedules and orchestrates the execution of multiple PUD operations transparently
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: The goal of MIMDRAM’s control unit, implemented at the memory controller, is to schedule and orchestrate the execution of multiple PUD operations transparently from the user. I highlight three main components of our control unit.
[CLICK] First, the mat scheduler is responsible for identifying which PUD operations can be dispatched based on the current mat utilization
[CLICK] Second, the mat scoreboard keeps track of the current utilized mats
[CLICK] and the uProgram processing engines dispatch DRAM access for a given running PUD operation
[NEXT]

## Slide 63: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Next, I’ll briefly discuss MIMDRAM’s software support
[NEXT]

## Slide 64: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Starting with our new compiler support for PUD applications
[NEXT]

## Slide 65: MIMDRAM: Compiler Support (I)
Transparently:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 66: MIMDRAM: Compiler Support (II)
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: The first pass is responsible for identifying SIMD parallelism in a code, using LLVM’s auto-vectorization engine, generate PUD instructions and set the best vectorization factor for such PUD instruction
[NEXT]

## Slide 67: MIMDRAM: Compiler Support (II)
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: The second pass is responsible for scheduling and mapping computation. Our pass uses metadata to mark independent PUD instructions that should be executed concurrently across mats
[NEXT]

## Slide 68: MIMDRAM: Compiler Support (III)
Generate the appropriate binary for data allocation and PUD instructions
Goal
Improve SIMD utilization by allowing the distribution of independent PUD instructions across DRAM mats
Goal
Identify SIMD parallelism, generate PUD instructions, and set the appropriate vectorization factor
Goal
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Finally, the third pass is responsible for code generation and data allocation for PUD instructions
[NEXT]

## Slide 69: MIMDRAM: Overview
  Main components of MIMDRAM:
1
Hardware-side
DRAM array modification to enable fine-grained PUD computation
inter- and intra-mat interconnects to enable PUD vector reduction
control unit design to orchestrate PUD execution
2
Software
new compiler support to transparently generate PUD instructions
system support to map and execute PUD instructions
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
MIMDRAM is a hardware/software co-designed PUD system that enables fine-grained PUD computation at low cost and programming effort
Notes: Our compiler pass relies on the system support we implement for PUD instructions
[NEXT]

## Slide 70: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Such system support includes ISA extensions, execution and data transposition, data coherence, address translation, data allocation and alignment, and metadata translation
[NEXT]

## Slide 71: MIMDRAM: System Support
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: I will brief discuss our data allocation & alignment routine
[NEXT]

## Slide 72: MIMDRAM: Data Allocation & Alignment
MIMDRAM’s memory allocator uses a pool of huge pages and reversed-engineered DRAM interleaving information for PUD memory objects
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: MIMDRAM requires data from PUD operations to map to the target DRAM mats correctly.
To allow the memory allocator to influence the physical data location for PUD operations, we implement a new memory allocator that leverages huge pages and reversed-engineered DRAM inter;eaving information for PUD memory objects.

## Slide 73: MIMDRAM: More in the Paper & GitHub
Instruction set architecture
Execution & data transposition
Data coherence
Address translation
Data allocation & alignment
Mat label translation
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
https://arxiv.org/pdf/2402.19080.pdf
https://github.com/CMU-SAFARI/MIMDRAM
Notes: For more details, please, check our paper
[NEXT]

## Slide 74: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: Next, I will give a brief overview of our evaluation results.
[NEXT]

## Slide 75: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU
  PUD: SIMDRAM [Oliveira+, 2021] and DRISA [Li+, 2017]
  PND: Fulcrum [Lenjani+, 2020]
  https://github.com/CMU-SAFARI/MIMDRAM
Workloads:
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  495 multi-programmed application mixes
Two-Level Analysis
  Single application → leverages intra-application data parallelism
  Multi-programmed workload → leverages inter-application data parallelism
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: We compared MIMDRAM to a high-end CPU and GPU, two state-of-the-art PUD systems that use large DRAM access for computation, and a processing-near-DRAM architecture.
[CLICK] In our analyses, we use 12 workloads from four benchmark suites and 495 application mixes from such workloads
[CLICK] We perform a two-level analysis. For single applications, MIMDRAM can leverage its intra-application data parallelism and for multiple applications, MIMDRAM leverages inter-application data parallelism
[NEXT]

## Slide 76: Evaluation: Single Application Analysis – Energy Efficiency
MIMDRAM significantly improves energy efficiency compared to CPU (30.6x), GPU (6.8x), and SIMDRAM (14.3x)
Takeaway
Chart: CPU-Normalized Performance/Watt
| 2mm | 3mm | cov | doitgen | fdtd | gemm | gs | hw | kmeans | bp | pca | x264 | GMean
CPU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
GPU | 0.134 | 0.138 | 0.036 | 0.063 | 0.163 | 0.012 | 0.009 | 0.015 | 0.04271
SIMDRAM | 2.346 | 2.328 | 8.195 | 0.343 | 2.626 | 2.35 | 2.994 | 0.041 | 5.189 | 62.814 | 0.153 | 15.696 | 2.1379
MIMDRAM | 30.754 | 36.108 | 199.081 | 13.408 | 2.689 | 26.765 | 35.272 | 1.429 | 123.361 | 2397.384 | 2.294 | 92.782 | 30.6103
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: [CLICK] First, we evaluate the energy efficiency of the CPU
[CLICK] GPU
[CLICK] SIMDRAM and
[CLICK] MIMDRAM for the twelve applications using a single DRAM subarray, which is conservative for PUD systems.
Values are normalized to the baseline CPU
[CLICK] We observe that MIMDRAM significantly improves energy efficiency compared to the CPU, GPU and SIMDRAM
[NEXT]

## Slide 77: Evaluation: Multi-Programmed Workload Analysis
Chart: Normalized Weighted Speedup (Higher is Better)
| SIMDRAM:1 | SIMDRAM:2 | SIMDRAM:4 | SIMDRAM:8 | MIMDRAM
ws_average | 1 | 1.2006 | 1.3094 | 1.3253 | 2.0209
MIMDRAM significantly improves system throughput (1.68x) compared to SIMDRAM
Takeaway
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: [CLICK] Next, we evaluate the system throughput of MIMDRAM and SIMDRAM using the weighted speedup metric. For fairness, we enable concurrent executions of PUD operations in SIMDRAM using bank-level parallelism of
[CLICK] One
[CLICK] Two
[CLICK] Fourth,
[CLICK] Eight simultaneous PUD operations
[CLICK]
[CLICK] We observe that MIMDRAM improves system throughput using a single DRAM bank for computation compared to SIMDRAM.
[NEXT]

## Slide 78: Evaluation: Comparison to Other PIM Architectures
MIMDRAM significantly improves performance/area compared to DRISA (1.18x) and Fulcrum (1.92x)
Takeaway
Chart: MIMDRAM-Normalized Performance/Area
| pca | hw | fdtd | doitgen | gemm | kmeans | 2mm | gs | 3mm | bp | cov | x264 | GMean
DRISA | 0.9 | 1.5 | 0.7 | 3.5 | 1 | 1.4 | 1 | 0.9 | 0.6 | 0.1 | 0.3 | 2.7 | 0.9
Fulcrum | 0.4 | 1.6 | 0.7 | 3.1 | 1 | 0.8 | 0.9 | 0.9 | 0.5 | 0.1 | 0.1 | 0.1 | 0.5
MIMDRAM | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: [CLICK] Finally, we compared MIMDRAM to other processing-in-memory architectures for our twelve workloads
For fairness, we report performance normalized area results, since such PIM architectures incur significant area costs to DRAM for computation
[CLICK] We evaluate the performance of DRISA
[CLICK] Fulcrum,
[CLICK] and MIMDRAM
Values are normalized to MIMDRAM
[CLICK] We observe that on average across all applications, MIMDRAM improves performance per area compared to both DRISA and Fulcrum
[NEXT]

## Slide 79: Evaluation: More in the Paper
MIMDRAM with subarray and bank-level parallelism
  MIMDRAM provides significant performance gains compared to the baseline CPU (13.2x) and GPU (2x)
Comparison to DRISA and Fulcrum for multi-programmed workloads
  MIMDRAM achieves system throughput on par with DRISA and Fulcrum
MIMDRAM’s SIMD utilization versus SIMDRAM
  MIMDRAM provides 15.6x the utilization of SIMDRAM
Area analysis
  MIMDRAM adds small area cost to a DRAM chip (1.11%) and CPU die (0.6%)
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: We have many more results in our paper, including.
[CLICK] Comparison to DRISA and Fulcrum for multi-applications
[CLICK] SIMDRAM utilization versus SIMDRAM
[CLICK] MIMDRAM’s performance with subarray and bank-level parallelism
[CLICK] and area analysis
[NEXT]

## Slide 80: Evaluation: More in the Paper
MIMDRAM with subarray and bank-level parallelism
  MIMDRAM provides significant performance gains compared to the baseline CPU (13.2x) and GPU (2x)
Comparison to DRISA and Fulcrum for multi-programmed workloads
  MIMDRAM achieves system throughput on par with DRISA and Fulcrum
MIMDRAM’s SIMD utilization versus SIMDRAM
  MIMDRAM provides 15.6x the utilization of SIMDRAM
Area analysis
  MIMDRAM adds small area cost to a DRAM chip (1.11%) and CPU die (0.6%)
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
https://arxiv.org/pdf/2402.19080.pdf
https://github.com/CMU-SAFARI/MIMDRAM
Notes: For all that, I invite you to check our paper
[NEXT]

## Slide 81: Outline
Introduction & Background
1
Limitations of PUD Systems
2
MIMDRAM
3
Hardware Overview
4
Software Support
5
Evaluation
6
Conclusion
7
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
Notes: To conclude
[NEXT]

## Slide 82: Conclusion
We introduced MIMDRAM, a hardware/software co-designed processing-using-DRAM system
Key idea: leverage fine-grained DRAM for processing-using-DRAM operation
HW: - simple changes to DRAM, enabling concurrent instruction execution - low-cost interconnects at the DRAM peripherals for data reduction
SW: - compiler and OS support to generate and map instructions
Our evaluation demonstrates that MIMDRAM
significantly improves performance, energy efficiency, and throughput compared to processor-centric (CPU and GPU) and memory-centric (SIMDRAM, DRISA, and Fulcrum) architectures
incurs small area cost to a DRAM chip and CPU die
Introduction & Background | Limitations of PUD | MIMDRAM | Hardware Overview | Software Support | Evaluation | Conclusion
● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● | ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● ● | ● ● ● ● ● | ●
https://github.com/CMU-SAFARI/MIMDRAM
Notes: [CLICK] In this paper, we proposed MIMDRAM, a hardware and software co-designed PUD system that leverages fine-grained DRAM access for energy efficiency and ease to program computation
[CLICK] We extensively evaluate MIMDRAM and observe that it significantly improves performance, energy efficiency and system throughput compared to processor-centric and memory-centric architectures while incurring small area overheads
We hope and believe that MIMDRAM’s ideas and results will help to enable more efficient and easy-to-program PUD systems. To aid with this effort, we open source all our infrastructure and programs at our GitHub.
[NEXT]

## Slide 83
MIMDRAM An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing
Geraldo F. Oliveira |  | 
Ataberk Olgun | A. Giray Yağlıkçı | F. Nisa Bostancı
Saugata Ghose | Juan Gómez-Luna | Onur Mutlu
2024 International Symposium on High-Performance Computer Architecture
Notes: Thanks for your attention.

## Slide 84
MIMDRAM An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Computing
Geraldo F. Oliveira |  | 
Ataberk Olgun | A. Giray Yağlıkçı | F. Nisa Bostancı
Saugata Ghose | Juan Gómez-Luna | Onur Mutlu
2024 International Symposium on High-Performance Computer Architecture
Backup Slides
Notes: Thanks for your attention.

## Slide 85: Bit-Serial PUD Addition

## Slide 86: Intra-Mat Interconnect

## Slide 87: Performance for Single Applications

## Slide 88: SIMD Utilization: MIMDRAM vs. SIMDRAM

## Slide 89: Weighted Speedup vs. CPU

## Slide 90: Multi-Applications: Full Data

## Slide 91: Multi-Applications: DRISA & Fulcrum

## Slide 92: BLP and SALP

## Slide 93: System Configuration

## Slide 94: Workload Characteristics