## Slide 1
MLWeaving: Software/Hardware Co-design
Our Approach (MLWwaving):
Experiment
(a) Time vs. Precision
Hardware: an Intel Broadwell CPU (14 cores, 35MB LLC, 60 GB/s memory bandwidth) and an Intel Arria 10 FPGA (directly access the CPU memory via one QPI and two PCIe, with memory bandwidth: 15GB/s.
Dataset: Epsilon (40,000 samples, 2000 features).
Hogwild (ModelAverage): state-of-the-art parallel implementations of SGD on CPUs, using 14 cores, AVX2 and 8-bit dataset.
MLWeaving:A One-Size-Fits-All
System for Any-precision Learning
Zeke Wang, Kaan Kara, Hantian Zhang, Gustavo Alonso, Onur Mutlu, Ce Zhang
Existing Approach:
MLWeaving memory layout (software)
(b) Memory traffic vs. Precision
One hardware design and one memory layout for any precision.
1, MLWeaving can roughly achieve linear speedup (time or memory traffic), when a lower number of bits is used, as shown in Figures a, b.
2, MLWeaving on an FPGA can achieve 11X speedup over its CPU rivals in Figure c.
Stochastic Gradient Decent (SGD):
For e = 1 to E do /*E epochs*/
For i = 1 to N do /*N samples (i,bi)*/
ax = Qs(i)* ; /*dot product*/
scale = γ*df(ax, bi); /*serial part*/
= scale*Qs(i); /*gradient comp*/
= - ; /*model update*/
Bit-level flexibility of precision from software side
A~Z (a~z ) is binary, 0 or 1.
MLWeaving arithmetic (hardware)
Directly consume the data from MLWeaving memory layout with bit-serial multipliers.
Problem:
Linear model training using low-precision SGD.
1, One hardware design for each precision.
2, One quantized dataset for each precision.
: model,
: gradient,
Γ: learning rate,
df: derivative of loss function
(c) MLWeaving vs. CPU rivals
Findings: