## Slide 1: The 3rd Ramulator & DRAM Bender Tutorial DRAM Bender Overview
Ataberk Olgun
ICS 2026
6 July 2026

## Slide 2: DRAM Bender An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips
Ataberk Olgun
Yahya Can Tugrul
Minesh Patel
Hasan Hassan
Lois Orosa
Oguz Ergin
A. Giray Yaglikci
Haocong Luo
Onur Mutlu

## Slide 3: Factors Affecting DRAM Reliability and Latency
We need to perform experimental studies
of real DRAM chips
DRAM timing violation
Inter-cell interference
Voltage
Temperature
Manufacturing process
Factors affecting DRAM reliability and latency cannot be properly modeled in simulation or analytically

## Slide 4: DRAM Testing Infrastructure
Allow experimental studies of real DRAM chips
Open-source FPGA-based testing infrastructure
Publicly-available: Start using today
Relatively low cost: An FPGA board + DRAM modules
SoftMC
Litex Tester

## Slide 5: Limitations of Existing Infrastructure
Impose restrictions on the DDR4 interface.
Restrictions limit various characterization experiments.
Difficult to set up (based on discontinued HW/SW) and use (require developing HW)
Monolithic hardware design makes extensions (new standards, prototypes) relatively difficult

## Slide 6: DRAM Bender: Design Goals
Flexibility
  Ability to test any DRAM operation
  Ability to test any combination of DRAM operations and custom timing parameters
Ease of use
  Simple programming interface (C++ and Python)
  Minimal programming effort and time
  Accessible to a wide range of users
    who may lack experience in hardware design
Extensibility
  Modular design
  Well-defined interfaces between hardware modules

## Slide 7: DRAM Bender: Overview
Publicly-available FPGA-based DDR4/3 and HBM2 characterization infrastructure
Easily programmable using the C++ and Python APIs
[Yaglikci+, DSN’22]

## Slide 8: DRAM Bender: Prototypes
Six
AMD Alveo U200 (DDR4)
Bittware XUPP3R (DDR4)
Bittware XUPVVH (DDR4 & HBM2)
Bittware XUSP3S (DDR4)
AMD ZC706 (DDR3)
Six out of the box FPGA-based prototypes
AMD Alveo U50 (HBM2)

## Slide 9: DRAM Bender: Coming Soon (I)
Support for AMD Alveo U55C HBM2 board
16 GB 2x8-HI HBM2
Enable HBM2 power measurement

## Slide 10: DRAM Bender: Coming Soon (II)
Enable DDR4 power measurement
Enable DDR4 over/undervolting studies

## Slide 11: Laboratory for Understanding Memory
Notes: And in our lab, we have many machines to test many DRAM modules and chips

## Slide 12: Laboratory for Understanding Memory
Notes: And in our lab, we have many machines to test many DRAM modules and chips

## Slide 13: Laboratory for Understanding Memory
https://arxiv.org/pdf/2606.13725

## Slide 14: People for Understanding Memory
Konstantinos Sgouras
Ismail E. Yuksel
Umut Baser

## Slide 15: Other People that Understand Memory
Haocong Luo
Jikun Wang
Spyridon Galanopoulos
Orhun Ecemis

## Slide 16: DRAM Bender: Ease of Use
RowHammer: Repeatedly activating two DRAM rows
Easy to devise new experiments to uncover new insights
one iteration of the RowHammer test
Easily programmable using the DRAM Bender C++ API
Notes: … the ease of use also comes with flexibility

## Slide 17: DRAM Bender: Three Case Studies
RowHammer: Interleaving Pattern of Activations
  Interleaving pattern significantly affects the number of RowHammer bitflips
RowHammer: Random Data Patterns
  Use 512-bit random data patterns
  Uncover more bitflips than 8-bit SoftMC random patterns
In-DRAM Bitwise Operations
  Demonstrate in-DRAM bitwise AND/OR capability in real DDR4 chips
DRAM Bender is flexible: supports many different types of experiments

## Slide 18: More in the Paper
DRAM Bender design details
  DRAM Bender instruction set architecture
  Hardware & software modules
  Prototype design
  Temperature controller setup
DRAM Bender application programming interface
Detailed results for three case studies
Future work & improvements

## Slide 19: More in the Paper
https://arxiv.org/abs/2211.05838

## Slide 20: Research DRAM Bender Enabled (I)
[ICS’26] Tokuda+, “Clutch: High Performance Vector-Scalar Comparison using DRAM via Chunked Temporal Coding”
[ISCA’26] Luo+, “DejaVu: Why You Should Write to Your DRAM Rows Twice”
[ISCA’26] Tokuda+, “Altering Processing-using-DRAM Operation Results Without Changing Operands: A Study of Real DRAM Chips and Implications for Future Systems”
[DSN’26] Wang+, “ScaleDisturb: Exploiting Temporal Asymmetry to Amplify Read Disturbance in Modern DRAM Chips”
[DSN Disrupt’26] Baser+, “In-DRAM Signature Generation Using Simultaneous Multiple-Row Activation: An Experimental Study of Off-The-Shelf DRAM Chips”
[ICCD’25] Yuksel+, “In-DRAM True Random Number Generation Using Simultaneous Multiple-Row Activation: An Experimental Study of Real DRAM Chips”
[MICRO’25] Yuksel+, “ColumnDisturb: Understanding Column-based Read Disturbance in Real DRAM Chips and Implications for Future Systems”
[ISCA’25] Yuksel+, “PuDHammer: Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips”
[DSN’25] Canpolat+, “EasyDRAM: An FPGA-based Infrastructure for Fast and Accurate End-to-End Evaluation of Emerging DRAM Techniques”
[VTS’25] Luo+, “Revisiting DRAM Read Disturbance: Identifying Inconsistencies Between Experimental Characterization and Device-Level Studies”
[HPCA’25] Olgun+, “Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance”
[HPCA’25] Tugrul+, “Understanding RowHammer Under Reduced Refresh Latency: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[DSN’24] Olgun+, “Read Disturbance in High Bandwidth Memory: A Detailed Experimental Study on HBM2 DRAM Chips”
[DSN’24] Yuksel+, “Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis”

## Slide 21: Research DRAM Bender Enabled (I)
[DSN’24 Disrupt] Luo+, “An Experimental Characterization of Combined RowHammer and RowPress Read Disturbance in Modern DRAM Chips”
[HPCA’24] Yaglikci+, ”Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[HPCA’24] Yuksel+, “Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis"
[ISCA’23] Luo+, “RowPress: Amplifying Read Disturbance in Modern DRAM Chips”
[DSN’23 Disrupt] Olgun+, ”An Experimental Analysis of RowHammer on HBM2 DRAM Chips”
[arXiv Preprint, 2023] Orosa+, ”SpyHammer: Using RowHammer to Remotely Spy on Temperature”
[MICRO’22] Yaglikci+, “HIRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips”
[DSN’22] Yaglikci+, “Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices”
[MICRO’21] Orosa+, “A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses”
[MICRO’21] Hassan+, “Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications”
[ISCA’21] Olgun+, “QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips”
[ISCA’21] Orosa+, “CODIC: A Low-Cost Substrate for Enabling Custom In-DRAM Functionalities and Optimizations”
[ISCA’20] Kim+, “Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques”
[S&P’20] Frigo+, “TRRespass: Exploiting the Many Sides of Target Row Refresh”
[HPCA’19] Kim+, “D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput”

## Slide 22: Research DRAM Bender Enabled (I)
[MICRO’19] Koppula+, “EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM”
[SIGMETRICS’18] Ghose+, “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study”
[SIGMETRICS’17] Chang+, “Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms”
[MICRO’17] Khan+, “Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content”
[SIGMETRICS’16] Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization”
[ISCA’14] Kim+, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors"
[SIGMETRICS’14] Khan+, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study”
[ISCA’13] Liu+, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms"

## Slide 23: Even More Research DRAM Bender Enabled
[IMW’26] Jiang+, “DRAM Operations under Cryogenic Temperatures: From Device Physics to DIMM Behavior”
[JSA’26] Garzon+, “CADM: Content addressable commodity off-the-shelf DRAM-based genome classifier”
[IEEE CAL’25] Kubo+, “PUDTune: Multi-Level Charging for High-Precision Calibration in Processing-Using-DRAM”
[arXiv’25] Zhou+, “EIM-TRNG: Obfuscating Deep Neural Network Weights with Encoding-in-Memory True Random Number Generator via RowHammer”
[ASPLOS’25] Baek+, “Marionette: A RowHammer Attack via Row Coupling”
[DATE’25] Zhou+, “Compromising the Intelligence of Modern DNNs: On the Effectiveness of Targeted RowPress”
[ISCA’24] Nam+, ”DRAMScope: Uncovering DRAM Microarchitecture and Characteristics by Issuing Memory Commands”
[DATE’24] Zhou+, “DRAM-Locker: A General-Purpose DRAM Protection Mechanism Against Adversarial DNN Weight Attacks”
[DRAMSec’23] Lang+, “BLASTER: Characterizing the Blast Radius of Rowhammer”
[IEEE CAL’23] Nam+ ”X-ray: Discovering DRAM Internal Structure and Error Characteristics by Issuing Memory Commands”
[MICRO’22] Gao+, “FracDRAM: Fractional Values in Off-the-Shelf DRAM”
[Applied Sciences’22] Bepary+, “DRAM Retention Behavior with Accelerated Aging in Commercial Chips”
[ETS’21] Farmani+, “RHAT: Efficient RowHammer-Aware Test for Modern DRAM Modules”
[HOST’20] Talukder+, “Towards the Avoidance of Counterfeit Memory: Identifying the DRAM Origin”
[MICRO’19] Gao+, “ComputeDRAM: In-Memory Compute Using Off-the-Shelf DRAMs”
[IEEE Access’19] Talukder+, “PreLatPUF: Exploiting DRAM Latency Variations for Generating Robust Device Signatures”
[ICCE’18] Talukder+, “Exploiting DRAM Latency Variations for Generating True Random Numbers”
Notes: SoftMC has also contributed to research from other research groups.

## Slide 24: DRAM Bender Paper, Slides, Videos, Code
https://github.com/CMU-SAFARI/DRAM-Bender
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]

## Slide 25: Summary
DRAM Bender
The first publicly-available DDR4/3 & HBM2 characterization infrastructure
github.com/CMU-SAFARI/DRAMBender
[Yaglikci+, DSN’22]
Flexible and Easy to Use
Source code available:
DRAM Bender enables many studies, ideas, and methodologies in the design of future memory systems
Notes: [CLICK] In summary, SoftMC is the first publicly-available DRAM characterization infrastructure
[CLICK] It is flexible and easy to use
[CLICK] The source code of SoftMC is available on GitHub
[CLICK] SoftMC enables many new studies, ideas, and methodologies in the design of future memory systems

## Slide 26: DRAM Bender An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips
Ataberk Olgun
Yahya Can Tugrul
Minesh Patel
Hasan Hassan
Lois Orosa
Oguz Ergin
A. Giray Yaglikci
Haocong Luo
Onur Mutlu

## Slide 27: The 3rd Ramulator & DRAM Bender Tutorial DRAM Bender Overview
Ataberk Olgun
ICS 2026
6 July 2026

## Slide 28: The 3rd Ramulator & DRAM Bender Tutorial DRAM Bender Research Highlights
Ataberk Olgun
ICS 2026
6 July 2026

## Slide 29: DRAM Bender is a Versatile Platform (I)
DRAM Bender is widely used for:
1
Understanding DRAM robustness problems
2
Uncovering new DRAM functionality
3
Learning DRAM internals
Notes: Point to Profs. Shaahin Angizi in NJIT and Jung Ho Ahn in SNU works and also Prof. Shinya Takamaeda-Yamazaki in the University of Tokyo
We have one speaker each from Shaahin Angizi and Jung Ho Ahn’s groups Ranyang Zhou and Hwayong Nam and we are excited to listen to them talk about their experience with DRAM Bender today

## Slide 30: Understanding DRAM Robustness Problems
[ISCA’26] Luo+, “DejaVu: Why You Should Write to Your DRAM Rows Twice”
[ISCA’26] Tokuda+, “Altering Processing-using-DRAM Operation Results Without Changing Operands: A Study of Real DRAM Chips and Implications for Future Systems”
[DSN’26] Wang+, “ScaleDisturb: Exploiting Temporal Asymmetry to Amplify Read Disturbance in Modern DRAM Chips”
[IMW’26] Jiang+, “DRAM Operations under Cryogenic Temperatures: From Device Physics to DIMM Behavior”
[MICRO’25] Yuksel+, “ColumnDisturb: Understanding Column-based Read Disturbance in Real DRAM Chips and Implications for Future Systems”
[ISCA’25] Yuksel+, “PuDHammer: Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips”
[VTS’25] Luo+, “Revisiting DRAM Read Disturbance: Identifying Inconsistencies Between Experimental Characterization and Device-Level Studies”
[HPCA’25] Olgun+, “Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance”
[HPCA’25] Tugrul+, “Understanding RowHammer Under Reduced Refresh Latency: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[DSN’24] Olgun+, “Read Disturbance in High Bandwidth Memory: A Detailed Experimental Study on HBM2 DRAM Chips”
DSN’24 Disrupt] Luo+, “An Experimental Characterization of Combined RowHammer and RowPress Read Disturbance in Modern DRAM Chips”
[HPCA’24] Yaglikci+, ”Spatial Variation-Aware Read Disturbance Defenses: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions”
[ISCA’23] Luo+, “RowPress: Amplifying Read Disturbance in Modern DRAM Chips”
[DSN’22] Yaglikci+, “Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices”
[MICRO’21] Orosa+, “A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses”
[ISCA’20] Kim+, “Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques”
[MICRO’19] Koppula+, “EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM”
[MICRO’17] Khan+, “Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content”
[ISCA’14] Kim+, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors"
[SIGMETRICS’14] Khan+, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study”
[ISCA’13] Liu+, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms"
[ASPLOS’25] Baek+, “Marionette: A RowHammer Attack via Row Coupling”
[DATE’25] Zhou+, “Compromising the Intelligence of Modern DNNs: On the Effectiveness of Targeted RowPress”
[DRAMSec’23] Lang+, “BLASTER: Characterizing the Blast Radius of Rowhammer”
[Applied Sciences’22] Bepary+, “DRAM Retention Behavior with Accelerated Aging in Commercial Chips”
[ETS’21] Farmani+, “RHAT: Efficient RowHammer-Aware Test for Modern DRAM Modules”

## Slide 31: Uncovering New DRAM Functionality
[ICS’26] Tokuda+, “Clutch: High Performance Vector-Scalar Comparison using DRAM via Chunked Temporal Coding”
[DSN Disrupt’26] Baser+, “In-DRAM Signature Generation Using Simultaneous Multiple-Row Activation: An Experimental Study of Off-The-Shelf DRAM Chips”
[ICCD’25] Yuksel+, “In-DRAM True Random Number Generation Using Simultaneous Multiple-Row Activation: An Experimental Study of Real DRAM Chips”
[DSN’24] Yuksel+, “Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips: Experimental Characterization and Analysis”
[HPCA’24] Yuksel+, “Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis"
[MICRO’22] Yaglikci+, “HIRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips”
[ISCA’21] Orosa+, “CODIC: A Low-Cost Substrate for Enabling Custom In-DRAM Functionalities and Optimizations”
[ISCA’21] Olgun+, “QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips”
[HPCA’19] Kim+, “D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput”
[JSA’26] Garzon+, “CADM: Content addressable commodity off-the-shelf DRAM-based genome classifier”
[IEEE CAL’25] Kubo+, “PUDTune: Multi-Level Charging for High-Precision Calibration in Processing-Using-DRAM”
[arXiv’25] Zhou+, “EIM-TRNG: Obfuscating Deep Neural Network Weights with Encoding-in-Memory True Random Number Generator via RowHammer”
[DATE’24] Zhou+, “DRAM-Locker: A General-Purpose DRAM Protection Mechanism Against Adversarial DNN Weight Attacks”
[MICRO’22] Gao+, “FracDRAM: Fractional Values in Off-the-Shelf DRAM”
[HOST’20] Talukder+, “Towards the Avoidance of Counterfeit Memory: Identifying the DRAM Origin”
[MICRO’19] Gao+, “ComputeDRAM: In-Memory Compute Using Off-the-Shelf DRAMs”
[IEEE Access’19] Talukder+, “PreLatPUF: Exploiting DRAM Latency Variations for Generating Robust Device Signatures”
[ICCE’18] Talukder+, “Exploiting DRAM Latency Variations for Generating True Random Numbers”

## Slide 32: Learning proprietary DRAM details
[ISCA’24] Nam+, ”DRAMScope: Uncovering DRAM Microarchitecture and Characteristics by Issuing Memory Commands”
[IEEE CAL’23] Nam+ ”X-ray: Discovering DRAM Internal Structure and Error Characteristics by Issuing Memory Commands”
[MICRO’21] Hassan+, “Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications”
[S&P’20] Frigo+, “TRRespass: Exploiting the Many Sides of Target Row Refresh”

## Slide 33: DRAM Bender is a Versatile Platform (II)
Other noteworthy use cases:
  Understanding DRAM voltage and latency sensitivity
    [SIGMETRICS’17] Chang+, “Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms”
    [SIGMETRICS’16] Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization”
  DRAM power characterization
    [SIGMETRICS’18] Ghose+, “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study”
  Reused in new FPGA-based evaluation infrastructures
    [DSN’25] Canpolat+, “EasyDRAM: An FPGA-based Infrastructure for Fast and Accurate End-to-End Evaluation of Emerging DRAM Techniques”

## Slide 34
DRAM Bender Enables Understanding DRAM Robustness Problems

## Slide 35: Variable Read Disturbance
Ataberk Olgun, Nisa Bostanci, Ismail Emir Yuksel, Abdullah Giray Yaglikci, Geraldo Francisco de Oliveira, Haocong Luo, Oguzhan Canpolat, Minesh Patel, and Onur Mutlu, "Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance" Proceedings of the 31st International Symposium on High-Performance Computer Architecture (HPCA), Las Vegas, NV, USA, March 2025. [Slides (pptx) (pdf)]

## Slide 36: A Typical DRAM-Based Computing System
CPU
DRAM Module
DRAM Chip
Notes: This is a typical DRAM-based computing system with a CPU [CLICK] and a DRAM module with multiple DRAM chips.

## Slide 37: DRAM Organization
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Row
Notes: Each DRAM chip contains multiple banks
Each bank is composed of many subarrays [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row buffer via bitlines [CLICK]
To access data in a row, you need to activate the row and too many repeated activations can lead to

## Slide 38: Read Disturbance in DRAM (I)
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
closed
DRAM Subarray
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
[Kim+, ISCA’14]
Notes: … read disturbance bitflips. Read disturbance bitflips have significant system-level implications because they break memory isolation.
[CLICK] A prominent example of read disturbance is RowHammer.
[CLICKx9] Repeatedly activating and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
We call the repeatedly activated row the aggressor row and the rows that have bitflips victim rows.
That’s RowHammer…

## Slide 39: Read Disturbance in DRAM (II)
Read disturbance in DRAM breaks memory isolation
A new read disturbance phenomenon: RowPress
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
keep open
Victim Row
Victim Row
Aggressor Row
[Luo+, ISCA’23]
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
DRAM Subarray
Notes: …, but there is also RowPress.
[Click]
RowPress induces bitflips by keeping the aggressor row open for a very long time.
Why do these bitflips occur?

## Slide 40: DRAM Cell Leakage
Each cell encodes information in leaky capacitors
wordline
capacitor
access
transistor
bitline
Stored data is corrupted if too much charge leaks (i.e., the capacitor voltage degrades too much)
charge
leakage
paths
[Patel+, ISCA’17]
Notes: Each cell encodes data in fundamentally leaky capacitors [CLICK] Here is a simplified diagram of a DRAM cell, where the capacitor in red stores the data and the access transistor gates access to the data
[CLICK]
There are a number of leakage paths by which charge can enter or exit the capacitor.
[CLICK]
The important thing to note is that stored data can be corrupted if too much charge leaks
Which is the same as saying if the capacitor voltage degrades too much
[END]

## Slide 41: DRAM Refresh
Periodic refresh operations preserve stored data
Capacitor voltage (Vdd)
100%
0%
Vmin
Refresh Window
Refresh Operations
time
REF
REF
REF
[Kim+, ISCA’20]
Notes: Here, we have a simplified diagram of the capacitor voltage over time
We see that the voltage decreases over time in an exponential decay.
There’s a threshold Vmin under which we can no longer guarantee that we will correctly read the data that was originally stored in the cell.
[CLICK]
As long as a cell’s voltage remains above this line, we consider this a retention success.
[CLICK]
However, as soon as the voltage drops below Vmin, we consider this a retention failure
In order to prevent charge leakage failures, also known as retention failures, [CLICK] we issue periodic refresh operations to restore the charge in the cell. [CLICK] The interval between refresh commands are referred to as the refresh window.

## Slide 42: Read Disturbance Bitflips
Capacitor voltage (Vdd)
100%
0%
Vmin
time
REF
REF
REF
Accesses to nearby row
Read Disturbance
Bitflip
[Kim+, ISCA’20]
Notes: Now lets take a look at this diagram in the context of a read disturbance access pattern.
[CLICK] If enough activations are issued to a nearby row within a refresh window, the charge leakage rate can be accelerated such that we end up with a bitflip.

## Slide 43: Read Disturbance Solutions
There are many solutions to mitigate read disturbance bitflips
More robust DRAM chips and/or error-correcting codes
Increased refresh rate
Physical isolation
Row remapping
Preventive refresh
Proactive throttling
Each solution offers a different system design point in reliability, performance, energy, and area tradeoff space
Notes: [CLICKx6 as you talk] Prior works proposed many techniques to mitigate read disturbance bitflips and maintain system robustness and security.
[CLICK] Many different techniques are valuable as each technique comes with a different reliability, performance, energy, and area tradeoff.

## Slide 44: The Read Disturbance Threshold (RDT)
Many secure read disturbance solutions take a preventive action before a bitflip manifests
  E.g., preventively refresh a victim row
Must accurately quantify the amount of disturbance that a row can withstand before experiencing a bitflip
  Typically identified by testing for read disturbance failures
Read Disturbance Threshold (RDT): The number of aggressor row activations needed to induce the first bitflip
Notes: Regardless, a *common* operation pattern across many different solutions is that they take *an action* before a bitflip manifests. For example, refreshing a victim row.
[CLICK] To do so, they *must accurately quantify* the amount of disturbance a row can withstand before it experiences a bitflip. [CLICK] This is typically quantified by time-intensive testing for read disturbance failures.
[CLICK] The read disturbance threshold, or RDT for short, quantifies the amount of disturbance a row can withstand before it experiences a bitflip. This metric is typically expressed in terms of an activation count.

## Slide 45: Accurate Identification of Read Disturbance Threshold is Critical for System Security and Performance
Configured RDT for the Mitigation Technique
Performance and Energy Overhead
RDT overestimated Insecure Low overhead (e.g., 10,000)
RDT underestimated High overhead Secure
(e.g., 20)
Ground truth RDT (e.g., 1,000)
To securely prevent bitflips at low overhead RDT must be accurately identified and carefully configured
Notes: Now I will try to illustrate [CLICK] why it is important to *accurately identify RDT*.
[CLICK] The x-axis shows increasing RDT values in arbitrary units
[CLICK] and the y-axis shows performance and energy overheads in arbitrary units.
[CLICK] This is a curve you’d expect to see: as the RDT becomes smaller, read disturbance solutions induce more performance and energy overheads, for example by more frequently performing time- and energy-intensive preventive refresh operations.
[CLICK] If you have this ground truth RDT value for the row, you want to configure your solution with that exact RDT value, why?
[CLICK] because if you configure it with a higher value you cannot mitigate bitflips and your system is no longer secure
[CLICK] and if you are overly conservative you incur unnecessary performance and energy overheads
[CLICK] In summary, we must accurately identify RDT to securely prevent bitflips at low overhead

## Slide 46: Motivation
Configured RDT for the Mitigation Technique
Performance and Energy Overhead
RDT overestimated Insecure Low overhead (e.g., 10,000)
RDT underestimated High overhead Secure
(e.g., 20)
Ground truth RDT (e.g., 1,000)
Prior works assume that the ground truth Read Disturbance Threshold (RDT) can be identified
Notes: Moreover [CLICKx2], prior works assume that the ground truth read disturbance threshold can be identified
In our work, we challenge this assumption…

## Slide 47: Our Goal
Answer two research questions:
Analyze implications for read disturbance solutions
1
Does RDT change over time?
2
How reliably and efficiently can RDT be measured?
Notes: Our goal is twofold:
First we’d like to answer two research questions: [CLICK] Does the read disturbance threshold change over time? [CLICK] If so, how reliably and efficiently can we measure it?
[CLICK] Second, we’d like to analyze implications of temporal variation of read disturbance threshold for read disturbance solutions.

## Slide 48: DDR4 DRAM Testing Infrastructure
  DRAM Bender on a Xilinx Virtex UltraScale+ XCU200
Xilinx Alveo U200 FPGA Board (programmed with DRAM Bender*)
DRAM Module with Heaters
MaxWell FT200 Temperature Controller
PCIe
Host Interface
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-Based Infrastructure to Easily Test State-of-the-Art DRAM Chips,” TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), and temperature (±0.5°C )
Notes: We use DRAM Bender to test DDR4 DRAM modules [CLICK]
This infrastructure provides us with fine-grained control over DRAM commands, timing parameters, and temperature

## Slide 49: HBM2 DRAM Testing Infrastructure
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-Based Infrastructure to Easily Test State-of-the-Art DRAM Chips,” TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
Fine-grained control over DRAM commands,
timing parameters (±1.67ns), and temperature (±0.5°C )
  DRAM Bender on a Bittware XUPVVH
Notes: This is another version of the same infrastructure we use to test HBM2 DRAM chips.

## Slide 50: Tested DRAM Chips
160 DDR4 and 4 HBM2 Chips from SK Hynix, Micron, Samsung
Notes: We test many DRAM chips from three major DRAM manufacturers spanning
[CLICK] various die density and die revisions and chip organizations.

## Slide 51: Foundational Results: Key Takeaway
The Read Disturbance Threshold (RDT) of a row changes randomly and unpredictably over time
Accurately identifying RDT is challenging
Key Takeaway
Notes: … starting with this takeaway message.
We find that the read disturbance threshold of a row changes randomly and unpredictably over time.
This makes accurately identifying RDT very challenging.

## Slide 52: Read Disturbance Threshold Changes Over Time
Chart: 
| 1
Y-Values | 37630
Measurement Number
Read Disturbance Threshold
37360 hammers
Notes: [CLICKx2] We plot the read disturbance threshold values observed
[CLICK] across many read disturbance threshold measurements (or samples, or observations) for one DRAM row
[CLICK] Here is an example point in the plot describing a measurement [CLICK] that yields a read disturbance threshold value of 37K hammers

## Slide 53: Read Disturbance Threshold Changes Over Time
Chart: 
| 1 | 2 | 3 | 4 | 5
Y-Values | 37630 | 38704 | 38346 | 37630 | 38704
Measurement Number
Read Disturbance Threshold
Notes: Here are the RDT values across 5 measurements

## Slide 54: Read Disturbance Threshold Changes Over Time
Chart: 
Measurement Number
Read Disturbance Threshold
Notes: Here is across 1000. To expand the x-axis further and still make sense out of the plot…

## Slide 55: Read Disturbance Threshold Changes Over Time
Chart: 
| 1
Y-Values | 37866.638
Measurement Number
Read Disturbance Threshold
Maximum
Minimum
Average
Notes: We “compress” a series of 1000 measurements into this form: circle shows the average across 1000 measurements and error bars show the range of values

## Slide 56: Read Disturbance Threshold Changes Over Time
Chart: 
Measurement Number
Read Disturbance Threshold
Notes: Now, here is RDT across one hundred thousand measurements for one DRAM row.

## Slide 57: Read Disturbance Threshold Changes Over Time
Chart: 
Measurement Number
Read Disturbance Threshold
Minimum RDT at 16926th measurement
Notes: We observe that for this series of RDT measurements, the minimum RDT appears at around 17 thousand measurements.

## Slide 58: Read Disturbance Threshold Changes Over Time
Chart: 
Read Disturbance Threshold
Read Disturbance Threshold of a DRAM row varies over time: Variable Read Disturbance (VRD)
Notes: This is a key result that demonstrates the variable read disturbance phenomenon

## Slide 59: Variable Read Disturbance Across DRAM Chips
Read Disturbance Threshold
# of Measurements
RDT consistently varies over time across all tested DRAM chips
Notes: Here we show data for one tested row each from 6 tested chips [CLICK].
This observation is consistent across all tested chips…

## Slide 60: Variable Read Disturbance Across DRAM Chips
RDT
# of Measurements
RDT consistently varies over time across all tested DRAM chips
https://arxiv.org/pdf/2502.13075
Notes: =

## Slide 61: VRD is (Likely) Unpredictable
The outcome of the next read disturbance threshold (RDT) measurement cannot be predicted given past measurements
1
RDT histograms well resemble* random probability distributions e.g., normal distribution
* Resemblance quantified using statistical tests in the paper
2
Analyze and find no repeating patterns in the series of consecutively measured RDT values using the autocorrelation function
Notes: We analyze the predictability of the next RDT value given past RDT measurements and we find that it is likely unpredictable.

## Slide 62: VRD is (Likely) Unpredictable
The outcome of the next RDT measurement cannot be predicted given past measurements
1
RDT histograms well resemble* random probability distributions e.g., normal distribution
2
Analyze and find no repeating patterns using the autocorrelation function
https://arxiv.org/pdf/2502.13075
Notes: For more details on our methodology, please check the paper

## Slide 63: In-Depth Analysis: Parameter Space
Four data patterns
Three temperature levels: 50°C, 65°C, 80°C
Three aggressor row on time values (RowPress):
  Minimum tRAS = ~35ns
  Interval between two periodic refresh commands tREFI = 7.8µs (DDR4)
  Maximum interval between two refresh 9 ⨉ tREFI = 70.2µs (DDR4)
Test 3750 rows and measure RDT 1000 times per row
  Aside: what would happen if we measure >1M times?
Notes: We perform a more in-depth analysis of VRD by varying many test parameters

## Slide 64: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: And this leads to 3 key takeaways

## Slide 65: Implications Summary
Security guarantees provided by mitigation techniques rely on accurately identified minimum read disturbance threshold (RDT)
Accurate identification of minimum RDT (for each row) is extremely challenging (even with 1000s measurements) because RDT unpredictably changes over time
We analyze the use of a guardband and ECC
  May prevent VRD-induced bitflips
  Large guardbands induce performance overhead
Call for future work on online RDT profiling and runtime configurable read disturbance mitigations
Notes: Security guarantees provided by read disturbance mitigation techniques or solutions rely on an accurately identified RDT
[CLICK] Our results show that accurate identification of RDT is extremely challenging
[CLICK] We evaluate a short-term solution: combining a guardband for RDT and error-correcting codes. [CLICK] Given our limited empirical bitflip dataset, we show that this combined solution could prevent VRD-induced bitflips at performance cost.
[CLICK] Our results call for future work on online read disturbance profiling and runtime configurable read disturbance mitigations

## Slide 66: Combining ECC and Guardbands (II)
RDT guardbands ≥20% yield 1 unique bitflip in a row
Given our limited measurement dataset (10K measurements) RDT guardbands ≥20% combined with ECC may prevent VRD-induced read disturbance bitflips
More detailed analysis (following a large-scale study) needed to make a definitive conclusion
Notes: We evaluate combining guardbands with ECC as a solution for VRD. We find that guardbands greater than or equal to 20% yield only 1 unique bitflip in a row
[CLICK] The bitflip patterns *we* observe could be prevented with larger than or equal to 20% guardband combined with widely-used ECC schemes.
[CLICK] But more detailed analysis likely following a large-scale study is needed to make a definitive conclusion about the effectiveness of guardbands and ECC.

## Slide 67: Extended Version on arXiv
https://arxiv.org/pdf/2502.13075
Notes: An extended version of our conference paper is on arXiv.

## Slide 68: Variable Read Disturbance
Ataberk Olgun, Nisa Bostanci, Ismail Emir Yuksel, Abdullah Giray Yaglikci, Geraldo Francisco de Oliveira, Haocong Luo, Oguzhan Canpolat, Minesh Patel, and Onur Mutlu, "Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance" Proceedings of the 31st International Symposium on High-Performance Computer Architecture (HPCA), Las Vegas, NV, USA, March 2025. [Slides (pptx) (pdf)]

## Slide 69: DiscoRD (Preprint)
How can we reliably identify RDT given VRD?
https://arxiv.org/pdf/2603.12435v1

## Slide 70: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023. One of the 12 computer architecture papers of 2023 selected as Top Picks by IEEE Micro.

## Slide 71: RowPress: Key Observation
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
These bitflips do NOT require many row activations
Only one activation is enough in some cases!
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips

## Slide 72: Real-System Demonstration (I)
Key Idea: A proof-of-concept RowPress program keeps a DRAM row open for a longer period by keeping on accessing different cache blocks in the row
Intel Core i5-10400 (Comet Lake)
Samsung DDR4 Module M378A2K43CB1-CTD
(Date Code: 20-10)
w/ TRR RowHammer Mitigation
// Sync with Refresh and Loop Below
for (k = 0; k < NUM_AGGR_ACTS; k++)
for (j = 0; j < NUM_READS; j++) ∗AGGRESSOR1[j];
for (j = 0; j < NUM_READS; j++) ∗AGGRESSOR2[j];
for (j = 0; j < NUM_READS; j++)
clflushopt(AGGRESSOR1[j]);
clflushopt(AGGRESSOR2[j]);
mfence();
activate_dummy_rows();
Number of Cache Blocks Accessed
Per Aggressor Row ACT
(NUM_READS=1 is Rowhammer)
Notes: We demonstrate RowPress on a real system with a recent Intel processor and a Samsung DDR4 module with TRR rowhammer mitigation. The key idea of our RowPress program is to keep a DRAM row open for a longer period by keeping accessing different cache blocks in the row.
Here is the key part of our program, where we can change the number of cache blocks read per aggressor row activation. If we only read 1 cache block, then the program does the same as RowHammer

## Slide 73: Real-System Demonstration (II)
Leveraging RowPress, our user-level program
induces bitflips when RowHammer cannot
On 1500 victim rows
Notes: We run the program on 1500 arbitrarily selected victim rows, and we show the total number of bitflips we observe on the left, and the number of rows with bitflips on the right.
Leveraging RowPress, our program induces bitflips when RowHammer cannot

## Slide 74: RowPress Results & Source Code
Fully open source and artifact evaluated
https://github.com/CMU-SAFARI/RowPress
Notes: We have more results in the paper, and our work is fully open-source and artifact evaluated.

## Slide 75: ColumnDisturb
Ismail Emir Yuksel, Ataberk Olgun, Nisa Bostanci, Haocong Luo, A. Giray Yaglikci, and Onur Mutlu, "ColumnDisturb: Understanding Column-based Read Disturbance in Real DRAM Chips and Implications for Future Systems" Proceedings of the 58th International Symposium on Microarchitecture (MICRO), Seoul, South Korea, October 2025. [Slides (pptx) (pdf)]

## Slide 76: Research Question
What if there is a much worse read disturbance phenomenon that affects thousands of DRAM rows through the bitlines?
Notes: In ColumnDisturb, we ask:
What if there is a much worse read disturbance phenomenon that affects thousands of rows, through the bitlines

## Slide 77
ColumnDisturb
By repeatedly opening or keeping a DRAM row open, it is possible to disturb many DRAM cells on the same DRAM column
With ColumnDisturb, the activation of a single row concurrently affects DRAM cells across as many as three DRAM subarrays (e.g., up to 3072 DRAM rows)
Victim Cell
Subarray
Subarray
Subarray
Notes: Turns out, there is one: which we call ColumnDisturb
[CLICK] We observe that by repeatedly opening or keeping a DRAM row open, it is possible to disturb many DRAM cells on the same DRAM column
[CLICK] With ColumnDisturb, the activation of a single row concurrently affects DRAM cells across as many as three DRAM subarrays: which translates to up to 3072 DRAM rows

## Slide 78: Key Takeaways from Major Characterization Experiments
ColumnDisturb is a widespread read disturbance phenomenon and becomes worse as DRAM technology scales down to smaller node sizes
Takeaway 1
ColumnDisturb induces bitflips in thousands of DRAM rows and is different from RowHammer, RowPress, and Retention failures
Takeaway 2
The bitflip directionalities of ColumnDisturb and RowHammer & RowPress
are significantly different
Takeaway 3
Significantly more rows are vulnerable to ColumnDisturb than retention failures
Takeaway 4
As temperature increases, DRAM chips become more vulnerable to ColumnDisturb
Takeaway 5
Notes: We have five key takeaways from major characterization experiments

## Slide 79: Key Takeaways from Major Characterization Experiments
ColumnDisturb is a widespread read disturbance phenomenon and becomes worse as DRAM technology scales down to smaller node sizes
Takeaway 1
ColumnDisturb induces bitflips in thousands of DRAM rows and is different from RowHammer, RowPress, and Retention failures
Takeaway 2
The bitflip directionalities of ColumnDisturb and RowHammer & RowPress
are significantly different
Takeaway 3
Significantly more rows are vulnerable to ColumnDisturb than retention failures
Takeaway 4
As temperature increases, DRAM chips become more vulnerable to ColumnDisturb
Takeaway 5
Notes: First, ColumnDisturb is a widespread read disturbance phenomenon and becomes worse as DRAM technology scales down to smaller node sizes

## Slide 80: Minimum Time to Induce First Bitflip
All tested 216 DDR4 chips are vulnerable to ColumnDisturb
Notes: Here we show the first result that lead us to first takeaway: y-axis shows the time to induce first bitflip in a subarray
[CLICK] X-axis shows the DRAM die revision and density and each subplot is dedicated to different manufacturer
[CLICK] Here is the result and as you can see all tested DRAM chips experience ColumnDisturb bitflips
[CLICK] We conclude that all tested 216 DDR4 chips are vulnerable to ColumnDisturb

## Slide 81: Minimum Time to Induce First Bitflip
Newer chips tend to be more vulnerable to ColumnDisturb bitflips
5.1x
1.3x
3x
2.5x
This trend is consistent across all tested manufacturers
Notes: For the second observation,
[CLICK] Let’s first focus on one manufacturer: Sk hynix
[CLICK] We observe that from A-die to D-die, the minimum time to observe first bitflips reduces by up to 5.1x, note that 8Gb D-die chips are newer than 8Gb A-die chips
And a similar reduction in 16Gb A-die to C-die
[CLICK] We conclude that newer chips tend to be more vulnerable to ColumnDisturb bitflips
[CLICK] And this observation is consistent across all tested manufacturers

## Slide 82: Minimum Time to Induce First Bitflip
Some real DRAM chips experience ColumnDisturb bitflips within the nominal refresh window (64ms) under nominal operating conditions
Notes: [CLICK] Another observation we made is based on the lowest time to induce the first bitflip in a subarray for each manufacturer, highlighted as red.
[CLICK] In some Micron chips, specifically 16Gb F-die chips experience ColumnDisturb bitflips within the nominal refresh window under nominal operating conditions, note that these 16Gb F-die chips are the newest one across all tested chips according to datasheet release date and manufacturing time.

## Slide 83: ColumnDisturb
Ismail Emir Yuksel, Ataberk Olgun, Nisa Bostanci, Haocong Luo, A. Giray Yaglikci, and Onur Mutlu, "ColumnDisturb: Understanding Column-based Read Disturbance in Real DRAM Chips and Implications for Future Systems" Proceedings of the 58th International Symposium on Microarchitecture (MICRO), Seoul, South Korea, October 2025. [Slides (pptx) (pdf)]

## Slide 84
DRAM Bender Enables Uncovering New DRAM Functionality

## Slide 85: QUAC-TRNG
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 86: Accessing a DRAM Cell
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline
[Seshadri+ MICRO’17]

## Slide 87: Accessing a DRAM Cell
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
½ VDD
VDD
enable wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell charge restored
Sense Amp
deviation in bitline voltage
½ VDD
0
bitline
[Seshadri+ MICRO’17]
1
2
3
4
5
6

## Slide 88: DRAM Operation
…
…
…
…
…
Sense Amplifiers
Sense Amplifiers
Cache line
READ
…
READ
READ
Wordline Drivers
Sense Amplifiers
READ
READ
READ
ACT R0
RD
PRE R0
RD
RD
ACT R1
RD
RD
RD
time
DRAM Command Sequence
tRAS (Activation Latency)
tRP (Precharge Latency)
[Kim+ HPCA’19]

## Slide 89: Quadruple Activation (QUAC)
New Observation
Carefully-engineered DRAM commands can activate four rows in real DRAM chips
Activate four rows with two ACT commands
ACT
PRE
ACT
<3ns
<3ns
35ns
14ns
Violated
Default

## Slide 90: Why Does QUAC Work?
Hypothetical circuit to explain QUAC
Hierarchical Wordlines
High density and performance requirements
Hierarchical organization of DRAM wordlines enable high-density and low-latency DRAM operation

## Slide 91: Hierarchical Wordlines
A master wordline drives multiple local wordlines
Select signals for rows 0-3

## Slide 92: Hypothetical Row Decoder
L
L
L
L
Address [0]
Address [1]
Latch
A0
A0
A1
A1
Predecode the least significant two bits
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Drive control signals
Notes: Made up of two stages

## Slide 93: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
0
0
First ACT command drives a single wordline

## Slide 94: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
0
0
PRE
Violate Timing
PRE command cannot disable latches

## Slide 95: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
0
0
PRE
Violate Timing
Violate Timing
ACT R3
1
1
Second ACT drives the remaining three wordlines

## Slide 96: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
PRE
Violate Timing
Violate Timing
ACT R3
1
1
Second ACT drives the remaining three wordlines
All four wordlines are enabled
Quadruple Activation
Notes: … and you can use Quadruple Activation for true random number generation

## Slide 97: Use Cases of True Random Numbers
High-quality true random numbers are critical to many applications
True random numbers can only be obtained by sampling random physical processes
Unfortunately, not all computing systems are equipped with TRNG hardware (e.g., dedicated circuitry)
Notes: These true random numbers are critical to many cryptographic applications, scientific simulations, and even machine learning applications

## Slide 98: Generating Random Values via QUAC
Vdd
-Vdd
Voltage Difference
Time
Ready to Sense
Voltage Level
VTH
-VTH
0
Sense Amplifier
VDD/2
VDD/2
Enable
Logic-1
R0
R1
R2
R3

## Slide 99: Generating Random Values via QUAC
Vdd
-Vdd
VDD/2
VDD/2
Enable
ACT R0
PRE
ACT R3
+
Voltage Difference
VTH
-VTH
0
Time
R0
R1
R2
R3
Sense Amplifier

## Slide 100: Generating Random Values via QUAC
Vdd
-Vdd
Voltage Difference
Time
VTH
-VTH
0
VDD/2
VDD/2
Enable
ACT R0
PRE
ACT R3
+
Enable Sense Amplifiers
Sense Amplifier
R0
R1
R2
R3
Random perturbation

## Slide 101: QUAC-TRNG vs State-Of-The-Art
Outperforms best prior DRAM-based TRNG (i) “base” by 15.08x at 2.4 GT/s
(ii) “enhanced” by 2.03x at 12 GT/s

## Slide 102: QUAC-TRNG
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 103: SiMRA-TRNG
Ismail Emir Yuksel, Ataberk Olgun, Nisa Bostancı, Oğuzhan Canpolat, Geraldo Francisco de Oliveira Junior, Mohammad Sadrosadati, Abdullah Giray Yağlıkçı, and Onur Mutlu, "In-DRAM True Random Number Generation Using Simultaneous Multiple-Row Activation: An Experimental Study of Real DRAM Chips" Proceedings of the 43rd IEEE International Conference on Computer Design (ICCD), Dallas, TX, USA, November 2025. [Slides (pptx) (pdf)]

## Slide 104: SiMRA-TRNG: Throughput
SiMRA-based TRNG designs outperform the state-of-the-art DRAM-based TRNG
State-of-the-art DRAM-based TRNG
1.15x
1.99x
1.82x
1.39x
Notes: Moving onto the throughput results
Here on the y-axis we have the TRNG throughput normalized to the state-of-the-art DRAM-based TRNG
[CLICK] which is four row activation
[CLICK] Here is the result
[CLICK] And we observe that SiMRA-TRNG achieves up to 2 times higher throughput than the state-of-the-art
[CLICK] We conclude that SiMRA-based TRNG designs outperforms the state-of-the-art DRAM-based TRNG

## Slide 105: SiMRA-TRNG
Ismail Emir Yuksel, Ataberk Olgun, Nisa Bostancı, Oğuzhan Canpolat, Geraldo Francisco de Oliveira Junior, Mohammad Sadrosadati, Abdullah Giray Yağlıkçı, and Onur Mutlu, "In-DRAM True Random Number Generation Using Simultaneous Multiple-Row Activation: An Experimental Study of Real DRAM Chips" Proceedings of the 43rd IEEE International Conference on Computer Design (ICCD), Dallas, TX, USA, November 2025. [Slides (pptx) (pdf)]

## Slide 106: SiMRA-PUF

## Slide 107: FC-DRAM
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, UK, March 2024. [Slides (pptx) (pdf)] [arXiv version] [FCDRAM Source Code]

## Slide 108: The Capability of COTS DRAM Chips
108
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 109: 48 Simultaneously Activated Rows
109
Exactly the same number of rows
in each subarray
are activated
Twice as many rows in one subarray
compared to its neighbor subarray are activated
COTS DRAM chips have two distinct sets of
activation patterns in neighboring subarrays
when two rows are activated with violated timings
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 16 rows
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 32 rows
A total of 32 rows
A total of 48 rows
Notes: We observe when Row A and B in neighboring subarrays are activated with violated timing parameters
[CLICK] Off-the-shelf DRAM chips have two distinct sets of simultaneous activation patterns in two neighboring subarrays
[CLICK] First pattern is exactly the same number rows in each subarray are activated.
[CLICK] We observe that we can activate up to 16 rows in neighboring subarrays, in other words a total of 32 rows
[CLICK] Second pattern is twice as many rows in one subarray compared to its neighbor subarray are activated
[CLICK] We observe that we can activate up to 16 rows in one subarray while activating up to 32 rows in its neighbor subarray, a total of 48 rows

## Slide 110: Bitwise NOT: Key Idea
110
Connect rows in neighboring subarrays
through a NOT gate by simultaneously activating rows
SA
A
src
dst
ACT src
ACT dst
SA
A
src
dst
SA
A
src
dst
~A
NOT gate
Notes: Our key idea is to leverage the connection between neighboring subarrays,
[CLICK] the NOT gate in the sense amplifier.
[CLICK] By simultaneously activating rows in neighboring subarrays, we can connect these rows through a NOT gate
[CLICK] As an example, source and destination in neighboring subarrays and if we first activate src
[CLICK] and then activate destination, this result in sense amplifier to drive the negated src value to the dst

## Slide 111: NOT Operation: A Walkthrough
½ VDD
src
dst
½ VDD
GND
GND
111
ACT src
connects src to bitline
Notes: Let’s see how we can perform NOT operation in real DRAM chips at a lower abstraction-level
[CLICK] As an example, we have source and destination cells, both store GROUND (low voltage) and bitlines are precharged to vdd over two
[CLICK] We first issue an activation to the source, which asserts the source wordline and starts charge sharing process between source and its bitline

## Slide 112: NOT Operation: A Walkthrough
GND
src
dst
GND
GND
VDD
112
ACT src
Nominal
drives bitline to GND
drives bitline to VDD
Notes: We wait for nominal timing parameters, which assures sense amplifier amplifies the difference and
[CLICK] drives ground to the source’s bitline and VDD to the destination’s bitline

## Slide 113: NOT Operation: A Walkthrough
src
dst
connects dst to bitline
113
ACT src
PRE
ACT dst
Nominal
<3ns
GND
VDD
sense amplifier is still enabled
dst’s bitline is still VDD
Notes: We then issue back-to-back precharge and activation commands with violated timing parameters. This operation leads to
[CLICK] connecting destination cell to its bitline
[CLICK] keeping the sense amplifier enabled
[CLICK] keeping the destination’s bitline to VDD

## Slide 114: NOT Operation: A Walkthrough
src
dst
negated value of src (VDD) is written to dst
114
ACT src
PRE
ACT dst
Nominal
<3ns
GND
VDD
Notes: Eventually, as sense amplifier is enabled and bitline is still VDD, the negated value of the source, which is VDD, is written to dst

## Slide 115: Performing NOT in COTS DRAM Chips
115
There is at least one DRAM cell that can
perform the NOT operation
with a 100% success rate
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Notes: This is a quite crowded picture but the key takeaway is that NOT in COTS DRAM chips can be done with very high success rates: most bitlines can reliably perform NOT operations

## Slide 116: 16-Input NAND/NOR/AND/OR
116
Manipulate the bitline voltage to express
a wide variety of functions using
multiple-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amp.
compares
V(A,B) and V(X,Y)
Notes: … and you can build on the phenomena that enables NOT across the sense amplifier to perform bitwise NAND, NOR, AND, and OR operations.

## Slide 117: Two-Input AND and NAND Operations
VDD=1 & GND = 0
117
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1

## Slide 118: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
118

## Slide 119: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
16-input AND, NAND, OR, and NOR operations
with very high success rate (>94%)
119

## Slide 120: FC-DRAM
Ismail Emir Yuksel, Yahya Can Tugrul, Ataberk Olgun, F. Nisa Bostanci, A. Giray Yaglikci, Geraldo F. Oliveira, Haocong Luo, Juan Gomez-Luna, Mohammad Sadrosadati, and Onur Mutlu, "Functionally-Complete Boolean Logic in Real DRAM Chips: Experimental Characterization and Analysis" Proceedings of the 30th International Symposium on High-Performance Computer Architecture (HPCA), Edinburgh, UK, March 2024. [Slides (pptx) (pdf)] [arXiv version] [FCDRAM Source Code]

## Slide 121
6th Workshop on Memory-Centric Computing Systems
A full-day workshop @ ISCA 2026
28th June 2026 (Sunday)
Organizers: Ismail Emir Yuksel, F. Nisa Bostanci, Ataberk Olgun, Prof. Onur Mutlu
Overview of PIM & PIM Taxonomy
PIM in Memory & Storage
Infrastructures for PIM Research
Real-World PnM Systems
PuM for Bulk Bitwise Operations
Programming Techniques & Tools
Research Challenges & Opportunities
MCCSys
https://events.safari.ethz.ch/isca26-mccsys/
More information &
call for papers:

## Slide 122
DRAM Bender Enables Learning DRAM Internals

## Slide 123: U-TRR
Hasan Hassan, Yahya Can Tugrul, Jeremie S. Kim, Victor van der Veen, Kaveh Razavi, and Onur Mutlu, "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [Lightning Talk Video (100 seconds)] [arXiv version]

## Slide 124: The RowHammer Vulnerability
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 2
open
Row 2
closed
DRAM Chip
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bit flips in nearby cells

## Slide 125: Target Row Refresh (TRR)
DRAM vendors equip their DRAM chips with a proprietary mitigation mechanisms known as Target Row Refresh (TRR)
Row 0
Row 1
Row 2
Row 3
Row 4
TRR-equipped DRAM Chip
TRR
Aggressor detected: Row 2
closed
open
Refresh neighbor rows
TRR-induced refreshes
Key Idea: TRR refreshes nearby rows upon detecting an aggressor row
Memory Controller
REF
Notes: To protect their DRAM chips against RowHammer, DRAM vendors currently implement proprietary RowHammer mitigation mechanisms typically called Target Row Refresh or (TRR)
[CLICK] The key idea of TRR is to refresh nearby rows upon detecting an aggressor row
[CLICK] We demonstrate how TRR operates at a high-level.
[CLICK] The TRR mechanism detects [CLICK] an aggressor row as a result of [CLICK] repeatedly activating and precharging the same row. [CLICK]
[CLICK] To protect the neighbor victim rows from experiencing RowHammer bit flips, [CLICK] TRR refreshes the victim rows by performing TRR-induced refresh operations. TRR refreshes victim rows by piggybacking TRR-induced refreshes to the REFRESH commands that the memory controller periodically issues.

## Slide 126: Goal
Study in-DRAM TRR mechanisms to
understand how they operate
1
secure DRAM completely against RowHammer
3
assess their security
2
Notes: Our goal is to study in-DRAM TRR mechanisms to [CLICK] understand how they operate, [CLICK] asses their security, [CLICK] and secure DRAM completely against RowHammer

## Slide 127: U-TRR: Key Idea
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by on-die mitigation
[Hassan+, MICRO’21, source code available at https://github.com/CMU-SAFARI/U-TRR]
Hassan et al., "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” in MICRO, 2021.

## Slide 128: Experimental Methodology
[Hassan+, MICRO’21]
Victim Row R
1. Identify a row (R) with T retention time
2. Wait for T/2
Aggressor Row R + 1
3. Hammer R+1 once
4. Issue a periodic REF command (trigger mitigation)
5. Wait for T/2, read out row R and check for bitflips
On-DRAM-die Mitigation
Sample as aggressor row
Timeline
Refresh R
time = 0
time = T/2
time = T
Read R
Refresh victim row
Mitigation refreshes R
Notes: Our experiment first
[CLICK] finds a DRAM row R with a retention time of T. This means that the row will harbor retention failures if we do not refresh its content for T units of time.
[CLICK] On the bottom we show a timeline of actions taken by us and the currently-hypothetical on-die mitigation mechanism. Initially, the row R is refreshed, so it can retain data correctly until time is T.
[CLICK] We wait for half T.
[CLICK] We activate and precharge R+1 (which is adjacent to R) once.
[CLICK] Let’s now look at what a hypothetical on-die mitigation would do
[CLICK] It will sample the hammering of R+1 as an aggressor row activation
[CLICK] after which we issue a periodic refresh command (to trigger the mitigation)
[CLICK] If the mitigation sampled R+1 as an aggressor row, it will refresh R as the victim row
[CLICK] We then wait for half T, read out row R and check for bitflips in row R.

## Slide 129: Experimental Methodology
[Hassan+, MICRO’21]
Victim Row R
1. Identify a row (R) with T retention time
2. Wait for T/2
Aggressor Row R + 1
3. Hammer R+1 once
4. Issue a periodic REF command (trigger mitigation)
5. Wait for T/2, read out row R and check for bitflips
On-DRAM-die Mitigation
Sample as aggressor row
Refresh victim row
Timeline
Refresh R
time = 0
time = T/2
time = T
Mitigation refreshes R
Row R experiences no bitflips only if on-DRAM-die mitigation exists
Read R
Notes: Row R will not experience any bitflips
Only if on-DRAM-die mitigation exists and has refreshed R at half T

## Slide 130: Experimental Methodology
[Hassan+, MICRO’21]
Victim Row R
1. Identify a row (R) with T retention time
2. Wait for T/2
Aggressor Row R + 1
3. Hammer R+1 once
4. Issue a periodic REF command (trigger mitigation)
5. Wait for T/2, read out row R and check for bitflips
On-DRAM-die Mitigation
Sample as aggressor row
Refresh victim row
Timeline
Refresh R
time = 0
time = T
retention bitflips
Row R experiences no bitflips only if on-DRAM-die mitigation exists
Read R
Row R experiences retention bitflips if not refreshed at T/2
time = T/2
Row R not refreshed
Notes: Otherwise, row R will experience retention bitflips because it was not refreshred for T units of time.

## Slide 131: DRAM Testing Infrastructure
We implement U-TRR using FPGA-based SoftMC [Hassan+, HPCA’17]
modified to support DDR4 DRAM
SoftMC provides fine-grained control over DRAM commands, timing parameters and temperature
15x Vendor A DDR4 modules
15x Vendor B DDR4 modules
15x Vendor C DDR4 modules
We analyze 45 DDR4 DRAM modules from three vendors
Table 1 in our paper provides more information about the analyzed modules
Notes: To implement U-TRR and conduct the DRAM experiments, we use SoftMC, an FPGA-based DRAM testing infrastructure.
We modified SoftMC to support DDR4 modules.
[CLICK] We used SoftMC because it provides fine-grained control over DRAM commands, timing parameters, and temperature.
[CLICK] In our study, we analyzed 15 DDR4 DRAM modules from each of the three major DRAM vendors.
[CLICK] In the paper, we have a table that provides detailed information about the tested modules and here is a glimpse of the table

## Slide 132: Bypassing TRR with New RowHammer Access Patterns
We craft new RowHammer access patterns that circumvent TRR of three major DRAM vendors
On the 45 DDR4 modules we test, the new access patterns cause a large number of RowHammer bit flips
Notes: Leveraging the understanding we develop using U-TRR, we craft new RowHammer access patterns that circumvent the TRR mechanisms of three major DRAM vendors.
[CLICK] We evaluate the effectiveness of these patterns on 45 DDR4 DRAM modules, and we find that the new RowHammer access patterns cause a large number of RowHammer bit flips.

## Slide 133: Effect on Individual Rows
Our RowHammer access patterns cause bit flips in more than 99.9% of the rows
Why are some modules less vulnerable?
Fundamentally less vulnerable to RowHammer
Different TRR mechanisms
Unique row organization
All 45 modules we tested are vulnerable to our new RowHammer access patterns
Notes: Let’s look at the effectiveness of our new RowHammer access patterns at DRAM row granularity.
[CLICK] The plot shows, for each of the 45 modules we test, the fraction of rows that experience at least one RowHammer bit flip compared to all rows in a DRAM bank.
[CLICK] We find that all 45 modules we tested are vulnerable to our new RowHammer access patterns
[CLICK] Further, in 20 of the modules, our RowHammer access patterns cause bit flips in almost all of the rows
[CLICK] But why are some modules less vulnerable? We find that it is because of three main reasons.
[CLICK] First, some modules are fundamentally less vulnerable to RowHammer, in the sense that rows in those modules can tolerate a higher number of hammers before experiencing RowHammer bit flips.
[CLICK] Second, some modules implement a different TRR mechanism that our custom access patterns are not as effective. We believe understanding more those different TRR mechanisms can help crafting more effective rowhammer access patterns.
[CLICK] Third, some modules of Vendor C implement a unique row organization that appears to mitigate RowHammer at DRAM circuit level.

## Slide 134: U-TRR
Hasan Hassan, Yahya Can Tugrul, Jeremie S. Kim, Victor van der Veen, Kaveh Razavi, and Onur Mutlu, "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [Lightning Talk Video (100 seconds)] [arXiv version]

## Slide 135: DRAMScope
Notes: I will not spoil it for you

## Slide 136: Research Highlights Conclusion
DRAM Bender enables many studies, ideas, and methodologies in the design of future memory systems
  Understanding DRAM robustness problems
  Uncovering new DRAM functionality
  Learning DRAM internals
  …
We attribute DRAM Bender’s widespread success in enabling research to its flexibility and ease of use
Research drives new DRAM Bender features & improvements
  DDR3  DDR4  HBM2
  Support for 6 FPGA boards out of the box

## Slide 137: The 3rd Ramulator & DRAM Bender Tutorial DRAM Bender Research Highlights
Ataberk Olgun
ICS 2026
6 July 2026

## Slide 138: The 3rd Ramulator & DRAM Bender Tutorial DRAM Bender Live Demo & Hardware/Software Overview
Ataberk Olgun
ICS 2026
6 July 2026

## Slide 139: RowHammer Using DRAM Bender
Connect to a DRAM Bender host machine via SSH
Execute a program to hammer a DRAM row
  Vary program parameters
Understand how the program gets executed

## Slide 140: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data

## Slide 141: Aside: Transferring Programs & Data
PCIe
Host to card (H2C) transfer: Write to a file
Card to host (C2H) transfer: Read from a file
DRAM Bender in FPGA
Host
Card
Program
Data

## Slide 142: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data
Notes: Lines 581-588

## Slide 143: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data

## Slide 144: DRAM Bender Programming Model
Assembly-like programming using C++/Python API
Two “types” of instructions
  DRAM command batch (ACT, READ, WRITE…)
  Regular (arithmetic, control-flow, load/store)
13 general purpose 32-bit registers
3 special-purpose DRAM address stride registers

## Slide 145: Regular DRAM Bender Instructions
Notes: We create our programs with these instructions

## Slide 146: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data
Notes: Go over the program now

## Slide 147: RowHammer Test Program
Create programs by appending instructions to a list
Initialize 8 rows surrounding the victim row
  Including the two aggressor rows
Initialize the victim row
Hammer the two aggressor rows
Read the victim row
Notes: - Lines 98-400

## Slide 148: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data

## Slide 149: DRAM Bender Hardware Overview
Notes: Do not describe in detail. I will show you what executing a program means.

## Slide 150: Life of a DRAM Bender Program
1
Host machine calls platform.execute(prog)
2
Frontend stores instructions in instruction memory

## Slide 151: Life of a DRAM Bender Program
3
Regular instructions take the exe pipeline path

## Slide 152: Life of a DRAM Bender Program
3
Regular instructions take the exe pipeline path
4
DRAM command batches take the dram pipeline path

## Slide 153: Life of a DRAM Bender Program
5
READ commands in the program fill up the Readback FIFO

## Slide 154: Life of a DRAM Bender Program
5
READ commands in the program fill up the Readback FIFO
6
The END instruction flushes the Readback FIFO

## Slide 155: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data

## Slide 156: Aside: DRAM Bender Instruction Encoding
https://docs.google.com/spreadsheets/d/18mPiKa1HBoO0OmzAbWRvo5OnIguL6A9tLEIwNeVfOe8

## Slide 157: Typical DRAM Bender Test Workflow
In a C++ or a Python executable:
1
Initialize DRAM Bender platform
2
Create DRAM Bender test program
3
Execute DRAM Bender test program
4
Read & analyze experimental data

## Slide 158: The 3rd Ramulator & DRAM Bender Tutorial DRAM Bender Live Demo & Hardware/Software Overview
Ataberk Olgun
ICS 2026
6 July 2026

## Slide 159: Summary
DRAM Bender
The first publicly-available DDR4/3 & HBM2 characterization infrastructure
github.com/CMU-SAFARI/DRAMBender
[Yaglikci+, DSN’22]
Flexible and Easy to Use
Source code available:
DRAM Bender enables many studies, ideas, and methodologies in the design of future memory systems
Notes: [CLICK] In summary, SoftMC is the first publicly-available DRAM characterization infrastructure
[CLICK] It is flexible and easy to use
[CLICK] The source code of SoftMC is available on GitHub
[CLICK] SoftMC enables many new studies, ideas, and methodologies in the design of future memory systems

## Slide 160: The 3rd Ramulator & DRAM Bender Tutorial Realistic DRAM Timing for HLS: Closing the Memory Fidelity Gap with Ramulator-Backed Co-Simulation
Dr. Antonino Tumeo
ICS 2026
6 July 2026

## Slide 161: A Highlight: RowPress
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
These bitflips do NOT require many row activations
Only one activation is enough in some cases!
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips

## Slide 162: RowPress Results & Source Code
Fully open source and artifact evaluated
https://github.com/CMU-SAFARI/RowPress
Notes: We have more results in the paper, and our work is fully open-source and artifact evaluated.

## Slide 163: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023.

## Slide 164: Variable Read Disturbance (VRD) Summary
Research Question
How accurately and efficiently can we measure the read disturbance threshold (RDT) of each DRAM row?
Experimental Characterization
Record >100M RDT measurements across 3750 rows and many test parameters (e.g., temperature, data pattern) in 160 DDR4 and 4 HBM2 chips
Key Observations
RDT changes significantly and unpredictably over time: VRD
Maximum observed RDT is 3.5X higher than minimum (for a row)
Smallest RDT (for a row) may appear after 94,467 measurements
Implications for System Security and Robustness
RDT cannot be accurately identified quickly
Given our limited dataset, guardbands (>10%) and ECC (SECDED or Chipkill) may prevent VRD-induced bitflips at significant performance cost
  More data and analyses needed to make definitive conclusion
Call for future work on understanding and efficiently mitigating VRD
Notes: [CLICK] Our work tries to answer a key question about the read disturbance threshold: “How accurately and efficiently can we measure the read disturbance threshold of each DRAM row?”
[CLICK] We record more than a hundred million read disturbance threshold measurements across many rows in many DRAM chips
[CLICK] We find that the read disturbance threshold of a DRAM row varies significantly and unpredictably over time.
[CLICK] The largest RDT observed for a DRAM row can be 3.5 times the smallest observed for the same row, and
[CLICK] a row’s smallest RDT may appear after 94 thousand measurements We call this new phenomenon Variable Read Disturbance.
[CLICK] Variable read disturbance has implications for system security and robustness because the RDT of a row cannot be quickly and accurately identified.
[CLICK] We evaluate using guardbands for RDT and error-correcting codes as a solution for VRD-induced bitflips: **Given our limited dataset of bitflip locations** we find that relatively large guardbands and ECC could prevent VRD-induced bitflips at significant performance cost.
[CLICK] But more data and analyses are needed to make a definitive conclusion
[CLICK] Our results call for future work on understanding and efficiently mitigating VRD.

## Slide 165: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: Here is the outline for the rest of the talk

## Slide 166: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: I will continue by motivating our study

## Slide 167: Motivation
DRAM chips are increasingly more vulnerable to read disturbance with technology scaling
Technology Scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2020 | 9.6
2014 | 139.2
[Yaglikci+, HPCA’24]
Notes: Read disturbance bitflips happen in more DRAM cells with fewer activations as DRAM technology scales to smaller sizes to satisfy our memory requirements.
[CLICK] We see more than 10X reduction in the read disturbance threshold between chips manufactured approximately 7 years apart.
[CLICK] Thus, DRAM chips become more vulnerable to read disturbance with technology scaling.

## Slide 168: Motivation
DRAM read disturbance worsens as DRAM chip density increases
Existing solutions become more aggressive
Aggressive preventive actions make existing solutions prohibitively expensive
Notes: Reducing read disturbance thresholds, or, worsening read disturbance [CLICK] causes existing mitigations to become more aggressive, [CLICK] and in turn, induce higher overheads

## Slide 169: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: First, all tested DRAM rows exhibit variable read disturbance, to *varying* degrees

## Slide 170: VRD Across DRAM Rows
DRAM Rows Sorted by Increasing Coefficient of Variation of RDT
Across 1000 RDT Measurements
Coefficient of Variation
A row with small variance in RDT distribution across 1000 measurements
Notes: Here we show the coefficient of variation in the distribution of 1000 read disturbance threshold measurements for each tested row.
[CLICK] The circled tiny pink dot stands for the DRAM row with the smallest coefficient of variation in its RDT distribution. Another way to look at this is that this row’s RDT values are very close to each other.
[CLICK] We show the rows sorted in increasing coefficient of variation on the x-axis

## Slide 171: VRD Across DRAM Rows
DRAM Rows Sorted by Increasing Coefficient of Variation of RDT
Across 1000 RDT Measurements
Coefficient of Variation
Median row
Row with the greatest variance in RDT distribution
All tested rows exhibit VRD
Notes: We observe that all tested rows exhibit VRD: no row has 0 variation in its RDT measurements
[CLICKx2] We highlight two points in this plot: the median row, and the row with the greatest variance in its read disturbance threshold distribution

## Slide 172: VRD in Two Example Rows
1.2⨉
3.5⨉
Variation in read disturbance threshold can reach 3.5⨉
Notes: Here is a look at those two rows. We see their RDT values across 1000 successive measurements on the x-axis
[CLICK] For the median row, we see that the maximum observed RDT is 1.2 times higher than the minimum
[CLICK] and we observe that the variation in RDT can reach a high factor: it is 3.5 times for the row with the greatest RDT variation

## Slide 173: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: Now moving onto the second takeaway: Relatively few measurements are unlikely to yield the minimum read disturbance threshold of a row

## Slide 174: Probability of Identifying the Minimum RDT
How likely is it that N < 1000 measurements yield the minimum RDT value across 1000 measurements?
N = 1, 3, 5, 10, 50, and 500
Monte Carlo simulations for 10K iterations
Notes: We try to answer this question: how likely is it for us to find the minimum observed RDT across 1000 measurements, using
[CLICK] only N measurements where N is smaller than 1000? [CLICK]
We use monte carlo simulations and [CLICK] plot the probability of identifying the minimum RDT value over varying N [CLICK] for all tested rows

## Slide 175: Probability of Identifying the Minimum RDT
Very unlikely to find the minimum RDT of a DRAM row with N = 1 measurement
only 0.2% for the median row
Notes: [CLICK] N = 1 measurement has a very low probability of yielding the minimum RDT across 1000 measurements, only 0.2%... and

## Slide 176: Probability of Identifying the Minimum RDT
Probability of finding the minimum read disturbance threshold increases with N (i.e., with more and more testing)
0.2%
0.7%
1.1%
2.1%
10.0%
75.3%
Probability values for the median row
Notes: (SLOWLY) we observe that the probability increases with N
goes up to 75% for the median row - but does not reach 100% -, for N = 500 measurements
====
TODO: spend more time here

## Slide 177: Expected Value of the Minimum RDT
With only N < 1000 RDT measurements how far are we from the minimum RDT across 1000 measurements
Chart: 
Measurement Number
Read Disturbance Threshold
Minimum across 1000 measurements
Notes: To gain more insight into VRD, we devise another metric called the expected value of the minimum RDT to quantify how higher of an RDT value we expect to find with N smaller than 1000 measurements.
[CLICK] I’ll describe this pictorially. [CLICK] This line depicts the minimum RDT value across 1000 measurements

## Slide 178: Expected Value of the Minimum RDT
With only N < 1000 RDT measurements how far are we from the minimum RDT across 1000 measurements
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159 | 160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175 | 176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191 | 192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223 | 224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239 | 240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255 | 256 | 257 | 258 | 259 | 260 | 261 | 262 | 263 | 264 | 265 | 266 | 267 | 268 | 269 | 270 | 271 | 272 | 273 | 274 | 275 | 276 | 277 | 278 | 279 | 280 | 281 | 282 | 283 | 284 | 285 | 286 | 287 | 288 | 289 | 290 | 291 | 292 | 293 | 294 | 295 | 296 | 297 | 298 | 299 | 300 | 301 | 302 | 303 | 304 | 305 | 306 | 307 | 308 | 309 | 310 | 311 | 312 | 313 | 314 | 315 | 316 | 317 | 318 | 319 | 320 | 321 | 322 | 323 | 324 | 325 | 326 | 327 | 328 | 329 | 330 | 331 | 332 | 333 | 334 | 335 | 336 | 337 | 338 | 339 | 340 | 341 | 342 | 343 | 344 | 345 | 346 | 347 | 348 | 349 | 350 | 351 | 352 | 353 | 354 | 355 | 356 | 357 | 358 | 359 | 360 | 361 | 362 | 363 | 364 | 365 | 366 | 367 | 368 | 369 | 370 | 371 | 372 | 373 | 374 | 375 | 376 | 377 | 378 | 379 | 380 | 381 | 382 | 383 | 384 | 385 | 386 | 387 | 388 | 389 | 390 | 391 | 392 | 393 | 394 | 395 | 396 | 397 | 398 | 399 | 400 | 401 | 402 | 403 | 404 | 405 | 406 | 407 | 408 | 409 | 410 | 411 | 412 | 413 | 414 | 415 | 416 | 417 | 418 | 419 | 420 | 421 | 422 | 423 | 424 | 425 | 426 | 427 | 428 | 429 | 430 | 431 | 432 | 433 | 434 | 435 | 436 | 437 | 438 | 439 | 440 | 441 | 442 | 443 | 444 | 445 | 446 | 447 | 448 | 449 | 450 | 451 | 452 | 453 | 454 | 455 | 456 | 457 | 458 | 459 | 460 | 461 | 462 | 463 | 464 | 465 | 466 | 467 | 468 | 469 | 470 | 471 | 472 | 473 | 474 | 475 | 476 | 477 | 478 | 479 | 480 | 481 | 482 | 483 | 484 | 485 | 486 | 487 | 488 | 489 | 490 | 491 | 492 | 493 | 494 | 495 | 496 | 497 | 498 | 499 | 500 | 501 | 502 | 503 | 504 | 505 | 506 | 507 | 508 | 509 | 510 | 511 | 512 | 513 | 514 | 515 | 516 | 517 | 518 | 519 | 520 | 521 | 522 | 523 | 524 | 525 | 526 | 527 | 528 | 529 | 530 | 531 | 532 | 533 | 534 | 535 | 536 | 537 | 538 | 539 | 540 | 541 | 542 | 543 | 544 | 545 | 546 | 547 | 548 | 549 | 550 | 551 | 552 | 553 | 554 | 555 | 556 | 557 | 558 | 559 | 560 | 561 | 562 | 563 | 564 | 565 | 566 | 567 | 568 | 569 | 570 | 571 | 572 | 573 | 574 | 575 | 576 | 577 | 578 | 579 | 580 | 581 | 582 | 583 | 584 | 585 | 586 | 587 | 588 | 589 | 590 | 591 | 592 | 593 | 594 | 595 | 596 | 597 | 598 | 599 | 600 | 601 | 602 | 603 | 604 | 605 | 606 | 607 | 608 | 609 | 610 | 611 | 612 | 613 | 614 | 615 | 616 | 617 | 618 | 619 | 620 | 621 | 622 | 623 | 624 | 625 | 626 | 627 | 628 | 629 | 630 | 631 | 632 | 633 | 634 | 635 | 636 | 637 | 638 | 639 | 640 | 641 | 642 | 643 | 644 | 645 | 646 | 647 | 648 | 649 | 650 | 651 | 652 | 653 | 654 | 655 | 656 | 657 | 658 | 659 | 660 | 661 | 662 | 663 | 664 | 665 | 666 | 667 | 668 | 669 | 670 | 671 | 672 | 673 | 674 | 675 | 676 | 677 | 678 | 679 | 680 | 681 | 682 | 683 | 684 | 685 | 686 | 687 | 688 | 689 | 690 | 691 | 692 | 693 | 694 | 695 | 696 | 697 | 698 | 699 | 700 | 701 | 702 | 703 | 704 | 705 | 706 | 707 | 708 | 709 | 710 | 711 | 712 | 713 | 714 | 715 | 716 | 717 | 718 | 719 | 720 | 721 | 722 | 723 | 724 | 725 | 726 | 727 | 728 | 729 | 730 | 731 | 732 | 733 | 734 | 735 | 736 | 737 | 738 | 739 | 740 | 741 | 742 | 743 | 744 | 745 | 746 | 747 | 748 | 749 | 750 | 751 | 752 | 753 | 754 | 755 | 756 | 757 | 758 | 759 | 760 | 761 | 762 | 763 | 764 | 765 | 766 | 767 | 768 | 769 | 770 | 771 | 772 | 773 | 774 | 775 | 776 | 777 | 778 | 779 | 780 | 781 | 782 | 783 | 784 | 785 | 786 | 787 | 788 | 789 | 790 | 791 | 792 | 793 | 794 | 795 | 796 | 797 | 798 | 799 | 800 | 801 | 802 | 803 | 804 | 805 | 806 | 807 | 808 | 809 | 810 | 811 | 812 | 813 | 814 | 815 | 816 | 817 | 818 | 819 | 820 | 821 | 822 | 823 | 824 | 825 | 826 | 827 | 828 | 829 | 830 | 831 | 832 | 833 | 834 | 835 | 836 | 837 | 838 | 839 | 840 | 841 | 842 | 843 | 844 | 845 | 846 | 847 | 848 | 849 | 850 | 851 | 852 | 853 | 854 | 855 | 856 | 857 | 858 | 859 | 860 | 861 | 862 | 863 | 864 | 865 | 866 | 867 | 868 | 869 | 870 | 871 | 872 | 873 | 874 | 875 | 876 | 877 | 878 | 879 | 880 | 881 | 882 | 883 | 884 | 885 | 886 | 887 | 888 | 889 | 890 | 891 | 892 | 893 | 894 | 895 | 896 | 897 | 898 | 899 | 900 | 901 | 902 | 903 | 904 | 905 | 906 | 907 | 908 | 909 | 910 | 911 | 912 | 913 | 914 | 915 | 916 | 917 | 918 | 919 | 920 | 921 | 922 | 923 | 924 | 925 | 926 | 927 | 928 | 929 | 930 | 931 | 932 | 933 | 934 | 935 | 936 | 937 | 938 | 939 | 940 | 941 | 942 | 943 | 944 | 945 | 946 | 947 | 948 | 949 | 950 | 951 | 952 | 953 | 954 | 955 | 956 | 957 | 958 | 959 | 960 | 961 | 962 | 963 | 964 | 965 | 966 | 967 | 968 | 969 | 970 | 971 | 972 | 973 | 974 | 975 | 976 | 977 | 978 | 979 | 980 | 981 | 982 | 983 | 984 | 985 | 986 | 987 | 988 | 989 | 990 | 991 | 992 | 993 | 994 | 995 | 996 | 997 | 998 | 999 | 1000
Y-Values | 38346 | 37272 | 37988 | 36198 | 37272
Measurement Number
Read Disturbance Threshold
Minimum across 1000 measurements
5 random samples
Minimum across 5 samples
Expected value of the minimum RDT
Notes: Here are 5 random samples from the set of 1000 measurements
[CLICK] and the minimum across those 5 samples
[CLICK] this metric quantifies the distance between the two minimums

## Slide 179: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
Notes: We plot the new metric on the [CLICK] y-axis and the probability of finding the minimum RDT on x-axis.

## Slide 180: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
RDT found by 1 measurement 3.21⨉ greater than minimum RDT across 1000 measurements
Notes: Each point on this plot stands for one row [CLICK]. [CLICK] This point shows you that there is a row where we expect to find an RDT value using one measurement 3.21 times greater than the one we would find if we were to test for 1000 times

## Slide 181: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
“Better” for testing
Plot interpretation
“Better” for testing == as tight an RDT distribution as possible
tight RDT distribution
Notes: A good way to interpret this plot is that we want to have small y-axis values. Small y-axis values indicate *tighter* RDT distributions and you want RDT distributions as tight as possible.

## Slide 182: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
The minimum RDT is significantly smaller than the one expected to be found with N = 1 measurement
RDT expected to be found by 1 measurement is 1.9⨉ greater than minimum RDT across 1000 measurements
Notes: This is the full plot.
[CLICK] Now we highlight the rows with smaller than 0.1% probability of finding the minimum RDT: for these rows the minimum RDT appears only once in the series of 1000 measurements
[CLICK] They can have up to 1.9 times expected normalized value of the minimum RDT
[CLICK] We conclude that the minimum RDT across 1000 measurements is significantly smaller than the one expected to be found by N = 1 measurement

## Slide 183: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
With increasing N (number of measurements) we expect to identify an RDT value closer to the minimum across 1000 measurements
Notes: With increasing N, we expect to identify an RDT value closer to the minimum value across 1000 measurements

## Slide 184: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: Finally, data patterns, temperature, and aggressor row on time all affect VRD and you can find the detailed analyses in the paper, but I am not going to cover these details in the presentation.

## Slide 185: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: The observations I presented have implications for system security and robustness

## Slide 186: Important Caveat
VRD solution analysis based on 1K or 10K read disturbance threshold measurements per row
More measurements could yield worse results
  Read disturbance threshold distribution tail could expand
What results would millions or billions of RDT measurements yield?
Notes: I’d like to stress an important caveat. The results I presented in the last slide and that I am going to present next are based on only a limited number of read disturbance threshold measurements.
[CLICK] More RDT measurements could yield worse results
[CLICK] and it is good to think about what millions of or billions of or more RDT measurements would yield.

## Slide 187: Challenges of Accurately Identifying RDT
Variation in read disturbance threshold across 1000 measurements can reach 3.5⨉ and may not be bounded
3.5⨉
RDT
Measurement Number
VRD is affected by data pattern, temperature, aggressor row on time
Comprehensive RDT profiling is time-intensive
Measuring RDT of each row only once with 8000 hammers using four data patterns, at three temperature levels takes 39 minutes in a bank of 256K rows
Notes: That, was a summary. I will do a deep dive by explaining why it’s challenging to accurately identify the minimum RDT
[CLICK] The variation in RDT can reach 3.5X and it may not be bounded.
[CLICK] RDT distribution is affected by many parameters and comprehensive RDT testing is time intensive
[CLICK] Measuring the RDT of each row in a bank of 256K rows *only once* can take 39 minutes

## Slide 188: RDT Profiling is Time-Intensive
Comprehensive RDT testing can take tens of hours (only 1000 measurements, one data pattern, one temperature level, one aggressor row on time)
Notes: In fact, we show that comprehensive read disturbance threshold testing for a DRAM chip can take tens of hours to complete if you want to measure RDT multiple times

## Slide 189: RDT Profiling is Time-Intensive
Comprehensive RDT testing can take hours (1000 measurements, one data pattern, one temperature level, one aggressor row on time)
https://arxiv.org/pdf/2502.13075
Notes: I refer you to our paper for more details on that

## Slide 190: Making Do With Few RDT Measurements
A system designer might measure RDT a few times and apply a safety margin (guardband) to the minimum observed value
Notes: Because it is so time consuming to comprehensively test for read disturbance bitflips, a system designer might measure RDT a few times, take the minimum across those few measurements, and apply a guardband to it with the hope of covering a not yet observed minimum RDT value
[CLICK] This plot shows you the probability that N measurements displayed on the x-axis + the guardband shown above will cover the minimum RDT value across 1,000 measurements.

## Slide 191: Making Do With Few RDT Measurements
A system designer might measure RDT a few times and apply a safety margin (guardband) to the minimum observed value
Average across all tested rows
Minimum across all tested rows
Notes: We show both the average value across all tested rows using circles and the minimum across all tested rows using bars.
What that pink bar means is there is a row where you *don’t* expect to find the minimum read disturbance threshold across 1K measurements with 100% probability, even with 500 measurements.
[CLICK] Here is the full plot.

## Slide 192: Making Do With Few RDT Measurements
A large guardband does not guarantee that the minimum RDT is always identified
Using guardbands alone is likely not effective
Notes: We observe that a large guardband does not guarantee that the minimum RDT is always identified and conclude that guardbands alone are likely not effective.

## Slide 193: RDT Guardband Increases Performance Overheads
50% RDT safety margin can induce 45% additional overhead (over no margin)
Relying solely on guardbands not recommended
45%
35%
Notes: Moreover, large guardbands can [CLICK] introduce significant performance overhead.
[CLICK] Thereby we do not recommend relying solely on guardbands.

## Slide 194: Combining ECC and Guardbands (I)
Single-error correcting double-error detecting (SECDED) or Chipkill ECC combined with guardbands could mitigate VRD-induced bitflips
Unique bitflips when 10% RDT guardband applied
10% guardband combined w/ ECC is likely unsafe
Notes: We evaluate error-correcting codes as a complementary technique to using a guardband for RDT
[CLICK] The plot shows you a histogram of the number of unique bitflips in a row when we use a 10% RDT guardband.
[CLICK] The bitflip rate we observe suggests that widely-used ECC schemes combined with 10% guardband for RDT is likely unsafe, depending on how the bitflips are located.

## Slide 195: More in the Paper
Hypothetical explanation for VRD
Effect of True- and Anti-Cell Layout
  Presence of true- and anti-cells in the victim row does not significantly affect the RDT distribution
Read disturbance mitigation evaluation methodology
Probability of errors at the worst observed bitflip rate for 10% RDT guardband
  SEC, SECDED, and Chipkill-like (SSC)
Read disturbance testing time and energy consumption
Detailed information on tested modules and chips
Notes: There are many more things in the paper that I cannot talk about now
In the interest of time, I’ll refer you to…

## Slide 196: More in the Paper
Hypothetical explanation for VRD
Effect of True- and Anti-Cell Layout
  Presence of true- and anti-cells in the victim row does not significantly affect the RDT distribution
Read disturbance mitigation evaluation methodology
Probability of errors at the worst observed bitflip rate for 10% safety margin
  SEC, SECDED, and Chipkill-like (SSC)
Read disturbance testing time and energy consumption
Detailed information on tested modules and chips
https://arxiv.org/pdf/2502.13075
Notes: … our paper for those details

## Slide 197: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: I’ll quickly conclude my talk

## Slide 198: Variable Read Disturbance Backup Slides

## Slide 199: Is this Experiment Noise?
Short answer: no
Hypothetical explanation for VRD: Randomly changing charge trap state in the active region
Long answer: We cannot identify any independent variables within our control that allow reliably predicting the minimum RDT despite extensive testing
Device-level studies should confirm our hypotheses

## Slide 200: Hypothetical Explanation for VRD
No device-level study shows temporal variations in read disturbance vulnerability
Electron migration and injection into victim cell is a major read disturbance failure mechanism
This mechanism is assisted by charge traps in the shared active region of the victim and aggr. cell
Temporal variation attributed to randomly changing occupied/unoccupied states of charge traps

## Slide 201: RDT Distribution Across Chips

## Slide 202: # of Consecutive Measurements That Yield the Same RDT Value

## Slide 203: Autocorrelation Function Tests

## Slide 204: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT

## Slide 205: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
Min. RDT found by 1 measurement 3.21⨉ greater than min. RDT found by 1000 measurements

## Slide 206: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT

## Slide 207: Effect of Die Density and Die Revision (I)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
RDT distribution worsens with increasing die density and with advanced DRAM technology
Notes: We plot the expected normalized value of the minimum RDT [CLICK] for three die revision and die density combinations
[CLICK] We observe that the RDT distribution worsens: that is, we expect to find a larger RDT with N < 1000 measurements, with increasing die density

## Slide 208: Effect of Die Density and Die Revision (II)
The effect of die density and die revision is consistent across all tested modules
Notes: [CLICK] We consistently make this observation across all tested modules

## Slide 209: Effect of Data Pattern (I)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
Notes: Here we show the expected normalized value of the minimum RDT for four tested data patterns

## Slide 210: Effect of Data Pattern (I)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
RDT distribution changes with data pattern
1.04⨉
1.06⨉
expected normalized value for the median row
Notes: We observe that the RDT distribution [CLICK] changes with the data pattern. Here we show the y-axis values for the median rows to quantify the change.

## Slide 211: Effect of Data Pattern (II)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
No single data pattern causes the worst RDT distribution across all tested DRAM chips
Notes: We look at the effect of data pattern across all tested modules. We observe that [CLICK] no single data pattern causes the worst RDT distribution across all tested DRAM chips

## Slide 212: Effect of Aggressor Row On Time
Expected Normalized Value of the Minimum RDT
RDT distribution changes with aggressor row on time
RDT distribution can become better or worse with increasing row on time
Notes: This shows the effect of aggressor row on time.
[CLICK] We see that the RDT distribution changes with aggressor row on time
[CLICK] It can become better or worse with increasing row on time

## Slide 213: Effect of Temperature
Expected Normalized Value of the Minimum RDT
RDT distribution tends to change with temperature
Number of Measurements (N) = 1
Notes: We look at the effect of temperature
[CLICK] and we see that the RDT distribution tends to change with temperature

## Slide 214: Effect of True- and Anti-Cell Layout
The presence of true- and anti-cells in the victim row does not significantly affect the RDT distribution

## Slide 215: Error Probability Analysis

## Slide 216: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Row 1
Access data in Row 1
Row 1 is closed
DRAM Subarray
Notes: To access a cell we use activate and precharge operations.
[CLICK] If we want to access data in Row 1, [CLICK] we must first activate Row 1, or open it

## Slide 217: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Activate command
Row 1
Access data in Row 1
Row 1 is open
Row 1 is closed
DRAM Subarray
Notes: We do that [CLICK] using an ACTIVATE [CLICK] command.

## Slide 218: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Row 1
Precharge command
Access data in Row 3
Row 3 is closed
DRAM Subarray
Notes: If, in this opened state, we [CLICK] want to access data in Row 3, [CLICK] we close the open row [CLICK] using the PREcharge command.

## Slide 219: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Activate command
Access data in Row 3
Row 3
Row 3 is open
Row 3 is closed
DRAM Subarray
Notes: [CLICK] Now we can activate Row 3 and access data in Row 3.
Repeatedly performing activate and precharge operations can lead to…