## Slide 1: MetaSys A Practical Open-source Metadata Management System to Implement and Evaluate Cross-layer Optimizations
Nandita Vijaykumar, Ataberk Olgun, Konstantinos Kanellopoulos, F. Nisa Bostancı, Hasan Hassan, Mehrshad Lotfi, Phillip B. Gibbons, Onur Mutlu

## Slide 2: Executive Summary
Motivation: Hardware-software cooperative (cross-layer) techniques improve performance, quality of service, and security
Problem: Cross-layer techniques are challenging to implement and evaluate in real hardware because they require modifications across the stack
Our Goal is twofold:
1) Enable rapid implementation and evaluation of cross-layer techniques in real hardware
2) Quantify the overheads associated with a general metadata management system
Key Idea:
Develop a metadata management system (MetaSys) with hardware and software components that are reusable across cross-layer techniques to minimize programmer effort
Prototype: Xilinx Zedboard prototype using RISC-V Rocket Chip:
Low on-chip storage (0.2%) and memory storage (0.2%) overhead metadata management
Evaluation: Graph prefetching and memory protection case studies, extensive overhead characterization
MetaSys-based graph prefetcher performs similar to state-of-the-art specialized prefetcher
Low-overhead bounds-checking (14%) and return address protection (1.2%)
Single general metadata management system scales well
MetaSys Source Code: https://github.com/CMU-SAFARI/MetaSys

## Slide 3: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 4: Hardware Performance Optimizations
Caches
Memory Controllers
Prefetchers
Today
Optimize for performance by designing hardware that infers and predicts program behavior
Notes: Start by looking at what is done in processors today
[CLICK] We design hardware structures such as caches, prefetchers and memory controllers and we make them specialize in
[CLICK] predicting program behavior. These components try to infer how a program behaves even sometimes the programmer intention by observing program execution.

## Slide 5: Cross-Layer Techniques
Future: Cross-Layer
Software can provide information (metadata) that the hardware is trying to infer
Data Structures
Access Patterns
Integer
Float
Char
Data Type/Layout
Hardware
Software
Notes: Cross-layer techniques envision a future where software provides useful information (or metadata) that the hardware is trying to infer and that the hardware can use to perform better
[CLICK] For example, the software can provide data structures used and access patterns present in an application. Different parts of the application may work on different data types and software can provide this information
[CLICK] to hardware [CLICK] that today tries to infer and does so with some accuracy. Cross-layer interaction between software and hardware can more accurately provide program metadata to hardware such that hardware performs better.

## Slide 6: Example: Locality Descriptor (I)
[Vijaykumar+, ISCA’18a]
The programmer or the compiler
describes key semantics
using a software interface
Data Structure
Float
Char
Metadata
Locality Descriptor [Vijaykumar+, ISCA’18a]
Express data locality (from software)
Exploit data locality (in hardware) in GPUs

## Slide 7: Example: Locality Descriptor (II)
[Vijaykumar+, ISCA’18a]
Hardware optimizations leverage key program semantics to improve performance significantly (e.g., >50%)
Notes: To conclude, cross layer techniques
[CLICK] allow hardware to improve performance or enhance system security
and [CLICK] software to provide better programmability and portability
[CLICK] To provide these benefits, cross-layer techniques communicate metadata between software and hardware over a cross-layer interface

## Slide 8: Benefits of Cross-Layer Techniques
Hardware
Software
Performance optimizations
Security enhancements
Quality of service improvements
Better programmability
Better portability
Hardware
Software
Cross-Layer Interface
[Vijaykumar+, ISCA’18a]
[Vijaykumar+, ISCA’18b]
[Koo+, ISCA’17]
[Mukkara+, ASPLOS’16]
[Ma+, ASPLOS’15]
[Yu+, CARVV’17]
Example prior work
…

## Slide 9: Cross-Layer Evaluation Infrastructure
Evaluating cross-layer techniques is non-trivial
Need a new infrastructure to evaluate a new cross-layer technique
Difficult given complexity (changes across the stack)
FPGA prototypes
Cycle-accurate simulators

## Slide 10: General Metadata Management System
A single general system can support multiple techniques
Key Benefit: Amortize the cost to implement each new technique
[Vijaykumar+, ISCA’18b]

## Slide 11: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System
Notes: Reduce to four bullets

## Slide 12: MetaSys: Overview
Goal: Enable rapid implementation and evaluation of cross-layer techniques in real hardware
MetaSys: Open-source infrastructure to evaluate cross-layer techniques end-to-end
MetaSys Source Code: https://github.com/CMU-SAFARI/MetaSys

## Slide 13: MetaSys: Components
Tagged memory-based metadata management Efficient metadata querying in hardware
1

## Slide 14: MetaSys: Tagged Memory (I)
Tag memory addresses with metadata IDs
Optimization Client
Metadata ID
Metadata
Is <address> accessed frequently?
metadata ID
Metadata Store
YES
Example

## Slide 15: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB

## Slide 16: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Metadata Mapping Table
Pointer
Metadata ID
Map memory addresses to metadata IDs
Metadata
Mapping Table
Notes: By default MMT resides in virtual address space, it exists per workload

## Slide 17: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Metadata Mapping Table
Pointer
Metadata ID
Map memory addresses to metadata IDs
Metadata
Mapping Table
64 B
4 KiB
64 B
4 KiB
Mapping Granularity
. . .
. . .
. . .
ID == 0
ID == 1
Notes: By default MMT resides in virtual address space, it exists per workload

## Slide 18: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Mapping Management Unit
MetaSys Instructions
Access & Manipulate Metadata Table
Metadata
Mapping Table

## Slide 19: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Mapping Management Unit
MetaSys Instructions
Metadata Lookup Unit
Address Translation
Retrieve Metadata ID
Metadata
Mapping Table
Metadata ID

## Slide 20: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Mapping Management Unit
MetaSys Instructions
Metadata Lookup Unit
Address Translation
Retrieve Metadata ID
Metadata
Mapping Table
Metadata ID

## Slide 21: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Mapping Management Unit
MetaSys Instructions
Metadata Lookup Unit
Address Translation
Retrieve Metadata ID
Metadata Mapping Cache
Metadata
Mapping Table
Metadata ID

## Slide 22: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Mapping Management Unit
MetaSys Instructions
Metadata Lookup Unit
Address Translation
Retrieve Metadata ID
Metadata Mapping Cache
Metadata
Mapping Table
Metadata ID

## Slide 23: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Metadata
Mapping Table
Mapping Management Unit
MetaSys Instructions
Metadata Lookup Unit
Address Translation
Retrieve Metadata ID
Metadata Mapping Cache
Optimization Client
Metadata Table
Map metadata IDs to metadata
Metadata Table
Metadata ID
Metadata

## Slide 24: MetaSys: Tagged Memory (II)
Processor
Main Memory
Core
TLB
Metadata
Mapping Table
Mapping Management Unit
Metadata Lookup Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
Retrieve metadata IDs
Initialize with metadata

## Slide 25: MetaSys: Components
Tagged memory-based metadata management Efficient metadata querying in hardware
1
Rich cross-layer interface Communicate metadata from SW to HW
2

## Slide 26: MetaSys: Cross-Layer Interface
Processor
Main Memory
Core
TLB
Metadata
Mapping Table
Mapping Management Unit
Metadata Lookup Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
MetaSys Instructions

## Slide 27: MetaSys: Cross-Layer Interface
Mapping Management Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
Main Memory
Metadata
Mapping Table
Notes: Refer to paper for more

## Slide 28: MetaSys: Cross-Layer Interface
Notes: Refer to paper for more

## Slide 29: MetaSys: Components
Tagged memory-based metadata management Efficient metadata querying in hardware
1
Rich cross-layer interface Communicate metadata from SW to HW
2
Flexible hardware and software modules Facilitate implementing new HW optimizations
3

## Slide 30: MetaSys: Hardware Modules (I)
Processor
Main Memory
Core
TLB
Metadata
Mapping Table
Mapping Management Unit
Metadata Lookup Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
Caches
Prefetchers
Bounds Checker
Memory Controller
Notes: Mention that this list can be expanded easily by developers. They just need to replicate what we have done.

## Slide 31: MetaSys: Hardware Modules (II)
Processor
Main Memory
Core
TLB
Metadata
Mapping Table
Mapping Management Unit
Metadata Lookup Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
commonly used across cross-layer techniques

## Slide 32: MetaSys: Software Modules
Processor
Main Memory
Core
TLB
Metadata
Mapping Table
Mapping Management Unit
Metadata Lookup Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
Operating System
MetaSys Library
Notes: Simple easy to modify operating system for adding new cross-layer optimizations
Metasys library exposes metasys instructions to the programmer in an organized way

## Slide 33: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 34: MetaSys: Operation (MAP)
Core
Mapping Management Unit
1
Map metadata ID (to memory location)
MAP Instruction
Metadata ID “0”
Start Address “0”
Size “1 Unit”
Main Memory
Metadata
Mapping Table
64 B
128 B
4 KiB
…
Notes: NEEDS WORK

## Slide 35: MetaSys: Operation (CREATE)
Prefetcher
Metadata Table
2
Associate metadata (with metadata ID)
CREATE Instruction
Cache
Metadata Table
Core
Mapping Management Unit
Main Memory
Metadata
Mapping Table
Metadata ID “0”
Client ID “Cache”
Metadata “Hot”
Notes: MAKE CLIENT MORE CONCRETE == CLIENT 0 PREFETCHER, CLIENT 1 CACHE

## Slide 36: MetaSys: Operation (CREATE)
Prefetcher
Metadata Table
Cache
Metadata Table
Core
Mapping Management Unit
Main Memory
Metadata
Mapping Table
2
Associate metadata (with metadata ID)
Metadata ID “0”
Metadata “Hot”

## Slide 37: MetaSys: Operation (LOOKUP)
Prefetcher
Metadata Table
3
Lookup metadata (with address)
Cache
Metadata Table
Core
Mapping Management Unit
Main Memory
Metadata
Mapping Table
Should I evict my cached word at address 0?

## Slide 38: MetaSys: Operation (LOOKUP)
Prefetcher
Metadata Table
Cache
Metadata Table
Core
Mapping Management Unit
Main Memory
Metadata
Mapping Table
Metadata Lookup Unit
Address “0”
Metadata ID “0”
4
Check metadata table (with metadata id)
It is used frequently (hot) I will not evict address 0
Metadata “Hot”
3
Lookup metadata (with address)

## Slide 39: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 40: FPGA Prototype (I)
Accurately evaluate feasibility of the metadata management system
  Implement all components (e.g., ports, wires, buffers)
Quickly run experiments
  Run workloads fast compared to simulation
Develop RTL as a basis for future work
  E.g., accurately measure area and power using synthesis tools
FPGA prototypes
Cycle-accurate simulators
Notes: Why we implement in FPGA, here are the reasons slide

## Slide 41: FPGA Prototype (II)
Zedboard Zynq FPGA board
RISC-V Rocket Chip
In-order Rocket
Core
TLB
Mapping Management Unit
Metadata Lookup Unit
Metadata Mapping Cache
Optimization Client
Metadata Table
DDR4 Chips
Metadata
Mapping Table

## Slide 42: MetaSys is Open Source
https://github.com/CMU-SAFARI/MetaSys
Link to Source Code

## Slide 43: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 44: Cross-Layer Prefetching Techniques
Handle challenging access patterns
Graph processing
Pointer chasing
Linear algebra
…
Case Study #1
New cross-layer prefetching technique for graph applications
Leverage graph data structure semantics
  Instead of relying on program context or memory access history
Example Prior Work
[Ainsworth+, ICS‘16] [Talati+, HPCA’21]

## Slide 45: Graph Representation
0
2
1
3
4
0
2
0
3
4
3
4
4
0
2
7
0
1
2
3
4
3
4
Work List
  Offsets List
  Edges List
  Properties
0
1
3
4
2
Compressed sparse row (CSR) format

## Slide 46: Traversing the Graph
0
2
1
3
4
0
2
0
3
4
3
4
4
0
2
7
0
1
2
3
4
3
4
Work List
  Offsets List
  Edges List
  Properties
Two types of indirection:
1
2
Using a single value
Using a range of values
Metadata required for prefetching:
Type of indirection
Base address of the next list
Size of elements in both lists

## Slide 47: Graph Prefetching Using MetaSys
1
Map metadata IDs to work, offset, and edges lists
2
CREATE metadata to express the characteristics {type, base, base_next, size, size_next} of each list
find what the application will access next using metadata
3
Load/store instruction triggers metadata lookup in prefetcher
Initialize metadata
Prefetch
Example
3
4
4
0
2
3
4
  Edges List
  Properties
base_properties + (size_properties * )
4

## Slide 48: Evaluation Methodology
CPU | 25 MHz, in-order Rocket core
TLB | 16 entry data TLB, LRU policy
L1 D&I$ | 16 KiB, 4-way, 4 cycle, 64 B cache line, LRU, 2 MSHRs
DRAM | DDR3 1066 MT/s
Metadata Cache | NMRU policy, 128 entries, 38 bits/entry, 512 B granularity
Metadata Table | 256 entries, 64 B entry
Workloads from the Ligra benchmark (graph applications):
PageRank (PR), Shortest Path (SSSP), Collaborative Filtering (CF), Teenage Follower (TF), Triangle Counting (TC), Breadth-First Search (BFS), Radius Estimation (Radii), Connected Components (CC)
Evaluated configurations:
Stride: Baseline system + a hardware stride prefetcher
GraphPref: Specialized graph prefetcher
MetaSys: Graph prefetching using MetaSys

## Slide 49: Results
MetaSys improves performance by 11.2% on average
Performs similar to the specialized prefetcher GraphPref (within 0.2%)

## Slide 50: Outline
Background
  Cross-Layer Techniques
  Infrastructure for Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 51: Memory Safety
Certain programming models are vulnerable to:
Buffer overflows cause unintentional memory modifications
Memory-unsafe: When there is no bounds checking for pointers
Software bounds checking: Computationally expensive
Hardware bounds checking: Too specialized
MetaSys allows bounds checking without additional hardware
char buffer[6];
string copy (buffer, “buffer overflow”)
b
u
f
f
e
r
o
v
e
r
f
l
o
w

## Slide 52: Bounds Checking with MetaSys (I)
MAP(Metadata ID M, Array A);
Array A = malloc (16 KB);
for (i = 0 ; i < 17 KB ; i++)
STORE A[i], 1337;
CREATE(M);
1
Allocate 16 KB of memory
2
Loop exceeds allocated memory range
3
Eventually, will cause buffer overflow
Map Metadata ID M != 0 to Array A
Execute a CREATE instruction with ID = M before each STORE
Metadata Lookup Unit
Array A
Out-of-bounds
Bounds Check Unit
Notes: DESCRIBE THIS OVER CODE

## Slide 53: Bounds Checking with MetaSys (I)
MAP(Metadata ID M, Array A);
Array A = malloc (16 KB);
for (i = 0 ; i < 17 KB ; i++)
STORE A[i], 1337;
CREATE(M);
1
Allocate 16 KB of memory
2
Loop exceeds allocated memory range
3
Eventually, will cause buffer overflow
Map Metadata ID M != 0 to Array A
Execute a CREATE instruction with ID = M before each STORE
Metadata Lookup Unit
Array A
Out-of-bounds
Bounds Check Unit
M
M
=
Notes: DESCRIBE THIS OVER CODE

## Slide 54: Bounds Checking with MetaSys (I)
MAP(Metadata ID M, Array A);
Array A = malloc (16 KB);
for (i = 0 ; i < 17 KB ; i++)
STORE A[i], 1337;
CREATE(M);
1
Allocate 16 KB of memory
2
Loop exceeds allocated memory range
3
Eventually, will cause buffer overflow
Map Metadata ID M != 0 to Array A
Execute a CREATE instruction with ID = M before each STORE
Metadata Lookup Unit
Array A
Out-of-bounds
Bounds Check Unit
0
M
!=
Fail bounds check
Notes: DESCRIBE THIS OVER CODE

## Slide 55: Bounds Checking with MetaSys (II)
Evaluation Methodology
Mapping granularity of 64 B
  Each 64 B non-contiguous memory location has an ID
Evaluate Olden benchmarks
Compare against a software bounds checker
(I) MetaSys bounds checking incurs 14% performance overhead on average (II) Performs better than the software bounds checker
Notes: Dashed line

## Slide 56: Return Address Protection with MetaSys
https://arxiv.org/pdf/2105.08123v2

## Slide 57: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 58: Characterizing MetaSys
Sources of system overhead:
Handling dynamic metadata
  Communicating metadata SW  HW at runtime
Metadata management and lookups
  Components retrieve metadata IDs
Scaling to multiple components
  Multiple components access shared metadata support
Conduct detailed characterization study to understand the overheads

## Slide 59: Methodology
Multiple workloads
  Polybench, Ligra, and memory-intensive microbenchmarks
Baseline MetaSys configuration (reminder)
  512 B mapping granularity
  128 entry metadata mapping cache
  256 entry metadata table
  64 B metadata
Stress the metadata management system
  Perform metadata lookups for every memory access

## Slide 60: Overhead of Accessing Metadata
Average real workload lookup overhead is low: 2.7% (~0% min, ~14% max)
Low spatial & temporal locality workloads have high overheads
(Random: 27%)
Miss-only and all-access are similar in performance (0.05% difference)
Notes: Miss-only is sometimes slower due to additional TLB misses. Frequent metadata accesses (in the all-access config) keep the translations inside the TLB whereas infrequent accesses cause them to be evicted from the TLB more often. Inducing additional delay on the critical path.

## Slide 61: Effect of Mapping Granularity
Mapping Granularity
Most workloads have small performance overhead even at the smallest mapping granularity
Some workloads experience high overhead even at the largest mapping granularity

## Slide 62: Effect of Multiple Clients
Client 0: Lookup on all memory accesses
Client 1: Lookup on all page table walk requests
Average real workload overhead is 0.3% (over one client)
Microbenchmarks experience higher overhead with more clients In the paper: Investigate mechanisms to alleviate their overheads

## Slide 63: Outline
Background
  Cross-Layer Techniques
  Evaluating Cross-Layer Techniques
MetaSys
  Overview
  Components
  Operation
  FPGA Prototype
Case Studies
  Prefetching
  Memory Safety and Protection
Characterizing a General Metadata Management System

## Slide 64: More in the Paper
More details on MetaSys Design
  OS Support
  Coherence/Consistency
  Timing Sensitivity of Metadata Lookups
  Software Library
  Area overhead (@ 22nm): 0.03 mm2
    0.02% of an Intel Ivy Bridge CPU core
In-depth characterization analysis
  Effects of address translation
  Effects of Metadata Mapping Cache size
  Performance overhead of MAP/CREATE instructions

## Slide 65: MetaSys Paper
https://dl.acm.org/doi/full/10.1145/3505250

## Slide 66: Executive Summary
Motivation: Hardware-software cooperative (cross-layer) techniques improve performance, quality of service, and security
Problem: Cross-layer techniques are challenging to implement and evaluate in real hardware because they require modifications across the stack
Our Goal is twofold:
1) Enable rapid implementation and evaluation of cross-layer techniques in real hardware
2) Quantify the overheads associated with a general metadata management system
Key Idea:
Develop a metadata management system (MetaSys) with hardware and software components that are reusable across cross-layer techniques to minimize programmer effort
Prototype: Xilinx Zedboard prototype using RISC-V Rocket Chip:
Low on-chip storage (0.2%) and memory storage (0.2%) overhead metadata management
Evaluation: Graph prefetching and memory protection case studies, extensive overhead characterization
MetaSys-based graph prefetcher performs similar to state-of-the-art specialized prefetcher
Low-overhead bounds-checking (14%) and return address protection (1.2%)
Single general metadata management system scales well

## Slide 67: MetaSys is Open Source
https://github.com/CMU-SAFARI/MetaSys
Link to Source Code

## Slide 68: Updated Version on ArXiv
https://arxiv.org/abs/2111.00082
Notes: An extended version of our conference paper is available on arXiv on this link where we discuss our framework in more detail.

## Slide 69: MetaSys is Open Source
https://github.com/CMU-SAFARI/MetaSys
Link to Source Code

## Slide 70: MetaSys A Practical Open-source Metadata Management System to Implement and Evaluate Cross-layer Optimizations
Nandita Vijaykumar, Ataberk Olgun, Konstantinos Kanellopoulos, F. Nisa Bostancı, Hasan Hassan, Mehrshad Lotfi, Phillip B. Gibbons, Onur Mutlu

## Slide 71: Backup Slides

## Slide 72: OS Support
Support for:
managing MMT in physical address space
flushing PMTs on context switch
updating MMT tags and invalidating MMC on page swaps
trap into OS to perform checks (e.g., on bounds check failure)

## Slide 73: Coherence/Consistency
Private metadata tables of private components (e.g., L1 cache) are not coherent
Private metadata tables of shared components are coherent automatically
  Updates in PMTs due to CREATEs are visible to all threads immediately
  Guaranteeing consistency requires use of barriers and fences
Metadata mapping table shared across threads of the same process
  Point of coherence is the mapping table, on a MAP, MMC entries in other cores are invalidated
  Consistency still requires barriers and fences

## Slide 74: Timing Sensitivity of Metadata
3 modes on how to handle a lookup:
Force stall: Memory instruction that triggered a lookup cannot commit until the optimization is complete
  Security use cases
No stall: Metadata lookups never stall the core, but they are always resolved
  E.g., in page placement, cache replacement
Best effort: Lookups may be dropped before they complete
  E.g., prefetcher training

## Slide 75: Software Library

## Slide 76: MetaSys vs XMem
Key difference:
The whole system is open-sourced
Differences in interfaces:

## Slide 77: Existing Cross-Layer Infrastructure
PARD: Enable quality-of-service techniques
Tag programs with an ID
Propagate program ID with memory requests
Hardware enforces QoS requirements on memory requests
Cheri: Fine-grained memory protection
Capability registers replace address operands
Tag capabilities with an ID
Propagate capability IDs with memory requests
Hardware enforces bounds checking, pointer integrity, etc.
[Huang+, CARRV’17] [Woodruf+, ISCA’14]

## Slide 78: MetaSys: Return Address Protection
Map return addresses to metadata id 1
Return address protection client performs metadata lookup on every store
If a store modifies a non-zero metadata tag, cause exception
1.2% average performance overhead (in contrast to software canary’s 5.5%)

## Slide 79: Additional Memory Accesses

## Slide 80: Metadata Mapping Cache Hit Rate

## Slide 81: Effect of Metadata Mapping Cache Size

## Slide 82: Tagging Granularity vs TLB Misses

## Slide 83: Effect of Address Translation

## Slide 84: Alleviating Metadata Mapping Cache Contention

## Slide 85: MAP/CREATE Instruction Overhead

## Slide 86
This work introduces MetaSys:
1) A general metadata management system
2) Various hardware and software components
in a real prototype to minimize developer effort
[Vijaykumar+, ISCA’18b]
Notes: Add a picture of the prototype