## Slide 1: NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira,
Stefano Corda, Sander Stuijk, Onur Mutlu, Henk Corporaal
56th Design Automation Conference (DAC), Las Vegas
4th-June-2019
Funded by the Horizon 2020 Framework Programme of the European Union
MSCA-ITN-EID

## Slide 2: Executive Summary
Motivation: A promising paradigm to alleviate data movement bottleneck is near-memory computing (NMC), which consists of placing compute units close to the memory subsystem
Problem: Simulation times are extremely slow, imposing long run-time especially in the early-stage design space exploration
Goal: A quick high-level performance and energy estimation framework for NMC architectures
Our contribution: NAPEL
  Fast and accurate performance and energy prediction for previously-unseen applications using ensemble learning
  Use intelligent statistical techniques and micro-architecture-independent application features to minimize experimental runs
Evaluation
  NAPEL is, on average, 220x faster than state-of-the-art NMC simulator
  Error rates (average) of 8.5% and 11.5% for performance and energy estimation
We open source Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 3
searches on
98PB
uploads on
180PB
15PB
15PB
3PB
SKA
300PB
Michael Wise, ASTRON, ”Science data Centre challenges”, DOME Symposium, 18 May, 2017

## Slide 4
searches on
98PB
uploads on
180PB
15PB
15PB
3PB
SKA
300PB
Michael Wise, ASTRON, ”Science data Centre challenges”, DOME Symposium, 18 May, 2017
Massive amounts of data

## Slide 5: Compute Centric Approach
DDR I/O
DDR chip
* R. Nair et al., “Active memory cube: A processing-in memory architecture for exascale systems”, IBM J. Research Develop., vol. 59, no. 2/3, 2015
System-level power break down*
Data Movement
Data Access
Processor
Memory hierarchies take advantage of locality
  Spatial locality
  Temporal locality
Not suitable for all workloads
  Graph processing
  Neural networks
Data access consumes a major part
  Applications are increasingly data hungry
Data movement energy dominates compute
  Especially true for off-chip movement
Integer core
link

## Slide 6: Compute Centric Approach
DDR I/O
DDR chip
System-level power break down*
Data Movement
Data Access
Processor
Memory hierarchies take advantage of locality
  Spatial locality
  Temporal locality
Not suitable for all workloads
  Graph processing
  Neural networks
Data access consumes a major part
  Applications are increasingly data hungry
Data movement energy dominates compute
  Especially true for off-chip movement
Data movement bottleneck
Integer core
link
* R. Nair et al., “Active memory cube: A processing-in memory architecture for exascale systems”, IBM J. Research Develop., vol. 59, no. 2/3, 2015

## Slide 7: Paradigm Shift - NMC
Compute-centric to a data-centric approach
Biggest enabler – stacking technology

## Slide 8: NMC Simulators
Simulation for:
  Design space exploration (DSE)
  Workload suitability analysis
NMC Simulators:
  Sinuca, 2015
  HMC-SIM, 2016
  CasHMC, 2016
  Smart Memory Cube (SMC), 2016
  CLAPPS, 2017
  Gem5+HMC, 2017
  Ramulator-PIM1, 2019
1Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 9: NMC Simulators
Simulation for:
  Design space exploration (DSE)
  Workload suitability analysis
NMC Simulators:
  Sinuca, 2015
  HMC-SIM, 2016
  CasHMC, 2016
  Smart Memory Cube (SMC), 2016
  CLAPPS, 2017
  Gem5+HMC, 2017
  Ramulator-PIM1, 2019
Simulation of real workloads can be 10000x slower than native-execution!!!
1Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 10: NMC Simulators
Simulation for:
  Design space exploration (DSE)
  Workload suitability analysis
NMC Simulators:
  Sinuca, 2015
  HMC-SIM, 2016
  CasHMC, 2016
  Smart Memory Cube (SMC), 2016
  CLAPPS, 2017
  Gem5+HMC, 2017
  Ramulator-PIM1, 2019
Idea: Leverage ML with statistical techniques for quick NMC performance/energy prediction
1Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 11: NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning
NAPEL Model Training

## Slide 12: Phase 1: LLVM Analyzer

## Slide 13: Phase 2: Microarchitecture Simulation
Central composite design of experiments technique to minimize the number of experiments while data collection

## Slide 14: Phase 3: Ensemble ML Training
Application Features
Instruction Mix
ILP
Reuse distance
Memory traffic
Register traffic
Memory footprint
Architecture Features
Core type
#PEs
Core frequency
Cache line size
DRAM layers
Cache access fraction
DRAM access fraction

## Slide 15: NAPEL Framework

## Slide 16: NAPEL Prediction

## Slide 17: Experimental Setup
Host System
  IBM POWER9
  Power: AMESTER
NMC Subsystem
  Ramulator-PIM1
Workloads
  PolyBench and Rodinia
  Heterogeneous workloads such as image processing, machine learning, graph processing etc.
Accuracy in terms of mean relative error (MRE)
1https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 18: NAPEL Accuracy: Performance and Energy Estimates
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 18 | 49 | 64.4 | 17.5 | 27 | 54.5 | 45 | 79 | 19.5 | 89 | 12 | 10 | 40.4083
ANN | 19 | 22 | 24 | 13.52 | 15.5 | 27.15 | 15.47 | 26 | 6 | 15.2 | 6.18 | 6.05 | 16.3392
NAPEL | 10.1 | 15 | 17 | 5 | 17 | 12 | 15 | 14.5 | 12 | 8.1 | 3.62 | 10.1 | 11.6183
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 16.5 | 60 | 37.65 | 10.92 | 32.5 | 41 | 19.2 | 14.74 | 23.16 | 32 | 25 | 13.14 | 27.1508
ANN | 13.44 | 26 | 21 | 12 | 11.29 | 19.78 | 9.97 | 8.83 | 10.05 | 22.24 | 11.27 | 11 | 14.7392
NAPEL | 5.86 | 19 | 14 | 5 | 9.28 | 6.6 | 5.68 | 12.36 | 5.67 | 4.63 | 6.23 | 8.05 | 8.53
(a) Performance prediction
(b) Energy prediction

## Slide 19: NAPEL Accuracy: Performance and Energy Estimates
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 18 | 49 | 64.4 | 17.5 | 27 | 54.5 | 45 | 79 | 19.5 | 89 | 12 | 10 | 40.4083
ANN | 19 | 22 | 24 | 13.52 | 15.5 | 27.15 | 15.47 | 26 | 6 | 15.2 | 6.18 | 6.05 | 16.3392
NAPEL | 10.1 | 15 | 17 | 5 | 17 | 12 | 15 | 14.5 | 12 | 8.1 | 3.62 | 10.1 | 11.6183
Chart: Mean Relative Error (%)
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm | gmean
Decision tree | 16.5 | 60 | 37.65 | 10.92 | 32.5 | 41 | 19.2 | 14.74 | 23.16 | 32 | 25 | 13.14 | 27.1508
ANN | 13.44 | 26 | 21 | 12 | 11.29 | 19.78 | 9.97 | 8.83 | 10.05 | 22.24 | 11.27 | 11 | 14.7392
NAPEL | 5.86 | 19 | 14 | 5 | 9.28 | 6.6 | 5.68 | 12.36 | 5.67 | 4.63 | 6.23 | 8.05 | 8.53
(a) Performance prediction
(b) Energy prediction
MRE of 8.5% and 11.6% for performance and energy

## Slide 20: Speed of Evaluation
Chart: DoE configurations
256 DoE configurations for 12 evaluated applications
256
1

## Slide 21: Speed of Evaluation
Chart: DoE configurations
256 DoE configurations for 12 evaluated applications
256
1
220x (up to 1039x) faster than NMC simulator

## Slide 22: Use Case: NMC Suitability Analysis
Chart: EDP Reduction
| atax | bfs | bp | chol | gemv | gesu | gram | kme | lu | mvt | syrk | trmm
Actual | 1.2825 | 4.5336 | 5.1644 | 4.9851 | 0.61146 | 0.2095 | 2.5023 | 2.1933 | 0.66969 | 0.16452 | 0.08306 | 0.029039
NAPEL | 1.5154 | 4.5901 | 3.8068 | 4.5216 | 0.48655 | 0.24709 | 2.0589 | 1.7048 | 0.63388 | 0.1711 | 0.091906 | 0.02441
Assess the potential of offloading a workload to NMC
NAPEL provides accurate prediction of NMC suitability
MRE between 1.3% to 26.3% (average 14.1%)

## Slide 23: Conclusion and Summary
Motivation: A promising paradigm to alleviate data movement bottleneck is near-memory computing (NMC), which consists of placing compute units close to the memory subsystem
Problem: Simulation times are extremely slow, imposing long run-time especially in the early-stage design space exploration
Goal: A quick high-level performance and energy estimation framework for NMC architectures
Our contribution: NAPEL
  Fast and accurate performance and energy prediction for previously-unseen applications using ensemble learning
  Use intelligent statistical techniques and micro-architecture-independent application features to minimize experimental runs
Evaluation
  NAPEL is, on average, 220x faster than state-of-the-art NMC simulator
  Error rates (average) of 8.5% and 11.5% for performance and energy estimation
We open source Ramulator-PIM: https://github.com/CMU-SAFARI/ramulator-pim/

## Slide 24: NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira,
Stefano Corda, Sander Stuijk, Onur Mutlu, Henk Corporaal
56th Design Automation Conference (DAC), Las Vegas
4th-June-2019
Funded by the Horizon 2020 Framework Programme of the European Union
MSCA-ITN-EID