## Slide 1: Understanding RowHammer Under Reduced Refresh Latency: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Yahya Can Tuğrul
A. Giray Yağlıkçı İsmail Emir Yüksel
Ataberk Olgun Oğuzhan Canpolat Nisa Bostancı
Mohammad Sadrosadati Oğuz Ergin Onur Mutlu

## Slide 2: Executive Summary
Evaluation: By reducing the existing solutions’ performance and energy overheads, improves system performance and energy efficiency with small additional area cost
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Reduces the latency of preventive refreshes issued by the existing solution
Adjusts the aggressiveness of the existing solution
Experimental Characterization: 388 DDR4 DRAM chips from three major vendors
The latency of a vast majority of preventive refresh can be significantly reduced without jeopardizing the data integrity of a DRAM chip
Goal:
To understand the impact of preventive refresh latency on RowHammer
To leverage this understanding to reduce the overheads of existing solutions
Problem:
Read disturbance in DRAM (e.g. RowHammer) worsens with technology node scaling
Existing solutions perform preventive refresh, inducing significant overheads
Motivation: Reducing preventive refresh latency to reduce its overheads.
No prior work studies i) the effect of preventive refresh latency on RowHammer or ii) the implications of reducing preventive refresh latency on existing solutions

## Slide 3: Outline
Evaluation
Background
Problem and Motivation
Experimental Characterization of Real DRAM Chips
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Conclusion

## Slide 4: DRAM Organization
CPU
Memory Controller
Memory
Channel
Sense Amplifier
DRAM Bank
DRAM Cell
DRAM Row

## Slide 5: DRAM Access
Sense Amplifier
DRAM Cell
Activate
Precharge
Read/Write
DRAM Bank

## Slide 6: DRAM Cell Leakage
Each cell encodes information in leaky capacitors
Stored data is corrupted if too much charge leaks (i.e., the capacitor voltage degrades too much)
wordline
capacitor
access
transistor
bitline
charge
leakage
paths

## Slide 7: DRAM Refresh
Refresh Window
Periodic refreshes preserve stored data
Capacitor voltage (VDD)
100%
0%
Vmin
time
REF
REF
REF
Periodic Refreshes

## Slide 8: RowHammer Vulnerability
Row 0
Row 1
Row 2
Row 3
Row 4
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
DRAM Bank
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bitflips in nearby cells

## Slide 9: RowHammer Bitflips
Capacitor voltage (VDD)
100%
0%
Vmin
time
RowHammer
Bitflip
RowHammer Attack

## Slide 10: RowHammer-Preventive Refresh
Capacitor voltage (VDD)
100%
0%
Vmin
time
REF
REF
REF
Preventive Refreshes
Preventively refreshing potential victim rows mitigates RowHammer bitflips
RowHammer Attack

## Slide 11: A Closer Look
Capacitor voltage (VDD)
100%
0%
time
50%
Preventive Refresh
Vmin
Charge Sharing
Charge Restoration
Preventive Refresh has a non-negligible latency
Precharge
Preventive Refresh Latency

## Slide 12: Outline
Evaluation
Background
Problem and Motivation
Experimental Characterization of Real DRAM Chips
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Conclusion

## Slide 13: Problem
RowHammer worsens as DRAM chip density increases
RowHammer bitflips occur at much lower activation counts
139K
[Kim+, ISCA’14]
9.6K
[Kim+, ISCA’20]
<1K
[Luo+, ISCA’23]
Mitigation mechanisms against RowHammer attacks induce higher overheads as RowHammer worsens
The minimum activation count needed to induce the first bitflip (NRH)

## Slide 14: Reducing Mitigation Overhead
Reduced Charge Restoration Latency
Reduced Preventive Refresh Latency
Reduced Preventive Refresh Overhead

## Slide 15: Reducing Charge Restoration Latency
Capacitor voltage (VDD)
100%
0%
time
50%
Preventive Refresh
Vmin
Charge Sharing
Charge Restoration
Precharge
time
<100%
The charge of the cell are partially restored

## Slide 16: Partial Charge Restoration
Partial charge restoration might affect the voltage level of the cell and thus affect the RowHammer vulnerability
To robustly perform partial charge restoration, we need to understand the DRAM chip’s limit with rigorous characterization

## Slide 17: Our Goal
To understand the impact of charge restoration latency on RowHammer
To leverage this understanding to reduce the overheads of existing solutions

## Slide 18: Outline
Evaluation
Background
Problem and Motivation
Experimental Characterization of Real DRAM Chips
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Conclusion

## Slide 19: DRAM Testing Infrastructure
DRAM Bender* on a Xilinx Alveo U200
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), and temperature (±0.5°C )

## Slide 20: Tested DRAM Chips
388 DDR4 DRAM chips from SK Hynix, Micron, and Samsung

## Slide 21: Key Takeaway from Real Chip Experiments
Charge restoration latency can be significantly reduced
for a vast majority of preventive refreshes

## Slide 22: Experiment Algorithm
time
Initialize
Refresh
Window
Partial Charge Restoration
Check Bitflips
RowHammer

## Slide 23: RowHammer Vulnerability Metric
Normalized RowHammer Threshold

## Slide 24: Effect of Partial Charge Restoration
Charge Restoration Latency
lower latency
Normalized RowHammer Threshold
NRH reduces more (becomes more vulnerable)
Data Retention Bitflip

## Slide 25: Effect of Partial Charge Restoration
Charge Restoration Latency
Normalized RowHammer Threshold
Data Retention Bitflips
64%
82%
36%
Charge restoration latency can be significantly reduced

## Slide 26: Repeated Partial Charge Restorations
Partial Charge Restoration causes cells to be partially restored
Repeated Partial Charge Restorations might induce bitflips
N  15K
time
Initialize
Refresh
Window
N Partial Charge Restorations
Check Bitflips
RowHammer

## Slide 27: Repeated Partial Charge Restorations
Charge Restoration Latency
Normalized RowHammer Threshold
Number of Restorations

## Slide 28: Repeated Partial Charge Restorations
Charge Restoration Latency
Normalized RowHammer Threshold
Numbers of Restorations
Partial charge restoration can be consecutively performed many times

## Slide 29: Repeated Partial Charge Restorations
Number of Restorations
Normalized RowHammer Threshold
After 15K/15K/1K partial charge restoration,
a single full charge restoration is needed
Data Retention Bitflips

## Slide 30: Key Takeaway from Real Chip Experiments
Charge restoration latency can be significantly reduced
for a vast majority of preventive refreshes

## Slide 31: Outline
Evaluation
Background
Problem and Motivation
Experimental Characterization of Real DRAM Chips
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Conclusion

## Slide 32: PaCRAM:
Key Experimental Takeaway: Charge restoration latency can be significantly reduced for a vast majority of preventive refreshes
Key Idea: Reduce preventive refresh overhead by reducing charge restoration latency of preventive refreshes
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
  Reduces the latency of preventive refreshes issued by the existing solution
  Configures the existing solution with the reduced RowHammer threshold
  Guarantees that any victim is not refreshed by more than a safe number of consecutive partial charge restorations
Partial Charge Restoration for Aggressive Mitigation
PaCRAM significantly reduces the performance and energy overhead of existing solutions

## Slide 33: PaCRAM:
PaCRAM is implemented in the memory controller
Partial Charge Restoration for Aggressive Mitigation
Memory Controller
DRAM
Chip (or module)
DRAM Commands, Address
Memory Request Scheduler
Activated Row Address
Activated Row Address
Preventive Refresh
Preventive Refresh Latency
Existing RowHammer Mitigation Solution
PaCRAM
NRH
Reduced
Preventive Refresh

## Slide 34: Outline
Evaluation
Background
Problem and Motivation
Experimental Characterization of Real DRAM Chips
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Conclusion

## Slide 35: Evaluation Methodology
Cycle-level simulations using Ramulator 2.0 [Luo+, CAL 2023]
System Configuration:
Workloads: 62 single-core and 60 four-core multiprogrammed workloads from 5 benchmark suites
NRH: {1K, 512, 256, 128, 64, 32} hammers The minimum hammer count needed to induce the first bitflip

## Slide 36: Configurations
Paired with 5 state-of-the-art solutions
  PARA [Kim+, ISCA’14]
  RFM [JEDEC 2020]
  PRAC [JEDEC 2024]
  Hydra [Qureshi+, ISCA’22]
  Graphene [Park+, MICRO’20]
Configured using experimental characterization data
Mfr. S |  | PaCRAM-S
Mfr. H |  | PaCRAM-H
Mfr. M |  | PaCRAM-M

## Slide 37: Configurations
Paired with 5 state-of-the-art solutions
  PARA [Kim+, ISCA’14]
  RFM [JEDEC 2020]
  PRAC [JEDEC 2024]
  Hydra [Qureshi+, ISCA’22]
  Graphene [Park+, MICRO’20]
Configured using experimental characterization data
Mfr. S |  | PaCRAM-S
Mfr. H |  | PaCRAM-H
Mfr. M |  | PaCRAM-M
55%
64%
82%

## Slide 38: Implication on Future Solutions
RowHammer Threshold
more vulnerable
System Performance (Norm. to No PaCRAM)
lower overhead
Reduction in mitigation overhead 25.43% Speedup
PaCRAM’s benefits increase as NRH reduces

## Slide 39: Implication on Future Solutions
RowHammer Threshold
System Performance (Norm. to No PaCRAM)
16.28% Speedup
2.87% Speedup
6.77% Speedup
3.16% Speedup
PaCRAM significantly reduces (11% on average) the performance overhead of existing solutions

## Slide 40: Implication on Future Solutions
RowHammer Threshold
Energy Consumption (Norm. to No PaCRAM)
18.10% Reduction
14.71% Reduction
1.96% Reduction
2.66% Reduction
5.55% Reduction
PaCRAM significantly reduces (9% on average) the energy overhead of existing solutions

## Slide 41: More in the Extended Version
Effect of partial charge restoration on
  Lowest observed NRH of DRAM modules
  RowHammer Bit-Error-Rate
  Half-Double access pattern
  Data retention time
Combined effect of partial charge restoration and temperature
Algorithms and details of our experiments
Detailed implementation of PaCRAM
  Hardware complexity analysis (0.09% area overhead on a high-end Intel Xeon Processer)
  Profiling cost analysis
Reducing charge restoration latency for periodic refreshes

## Slide 42: More in the Extended Version
https://arxiv.org/pdf/2502.11745

## Slide 43: PaCRAM is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/PaCRAM

## Slide 44: Outline
Evaluation
Background
Problem and Motivation
Experimental Characterization of Real DRAM Chips
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Conclusion

## Slide 45: Conclusion
The first rigorous experimental characterization on the effect of preventive refresh latency on RowHammer
388 DDR4 DRAM chips from three major vendors
PaCRAM: Partial Charge Restoration for Aggressive Mitigation
Reduces the latency of preventive refreshes issued by the existing solution
Adjusts the aggressiveness of the existing solution
The latency of a vast majority of preventive refresh can be significantly reduced without jeopardizing the data integrity of a DRAM chip
PaCRAM significantly reduces the performance and energy overheads of existing solutions

## Slide 46: Understanding RowHammer Under Reduced Refresh Latency: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Yahya Can Tuğrul
A. Giray Yağlıkçı İsmail Emir Yüksel
Ataberk Olgun Oğuzhan Canpolat Nisa Bostancı
Mohammad Sadrosadati Oğuz Ergin Onur Mutlu

## Slide 47: Backup Slides
Yahya Can Tuğrul
A. Giray Yağlıkçı İsmail Emir Yüksel
Ataberk Olgun Oğuzhan Canpolat Nisa Bostancı
Mohammad Sadrosadati Oğuz Ergin Onur Mutlu

## Slide 48: Preventive Refresh Overhead
RowHammer Threshold
more vulnerable
Fraction of Exec. Time Spent on Preventive Refresh (%)
higher overhead
Mitigation mechanisms against RowHammer attacks induce higher overheads as RowHammer worsens

## Slide 49: Effect of Partial Charge Restoration on Lowest Observed NRH of DRAM Modules
Charge Restoration Latency
Normalized RowHammer Threshold
Charge restoration latency can be reduced without significantly affecting the Lowest Observed NRH of DRAM Modules

## Slide 50: NRH Reduction Distribution
Rows that are highly vulnerable with full charge restoration do not exhibit the largest NRH reductions with partial charge restoration
RowHammer Threshold with Full Charge Restoration
Normalized RowHammer Threshold

## Slide 51: Effect of Partial Charge Restoration on RowHammer Bit-Error-Rate (BER)
Charge Restoration Latency
Normalized RowHammer BER
Charge restoration latency can be reduced without significantly affecting RowHammer Bit-Error-Rate

## Slide 52: Combined Effect of Partial Charge Restoration and Temperature
Charge Restoration Latency
Normalized RowHammer Threshold
No significant impact of temperature on the effect of charge restoration latency on RowHammer vulnerability

## Slide 53: Effect of Partial Charge Restoration on Data Retention Time
Charge Restoration Latency
Fraction of Rows with Data Retention Bitflips
Charge restoration latency can be significantly reduced to a safe minimum value without causing data retention failures

## Slide 54: Effect of Partial Charge Restoration on Half-Double Access Pattern
Charge Restoration Latency
Fraction of Rows with Half-Double Bitflips (%)
Charge restoration latency can be significantly reduced

## Slide 55: Detailed Implementation of PaCRAM
Memory Controller
DRAM
Chip (or module)
DRAM Commands, Address
Memory Request Scheduler
Activated Row Address
Activated Row Address
Preventive Refresh
Preventive Refresh Latency
Existing RowHammer Mitigation Solution
PaCRAM
NRH

## Slide 56: Detailed Implementation of PaCRAM
F State: the row has to be refreshed using full charge restoration
P State: the row can be refreshed using partial charge restoration
PaCRAM
Fully Restored Bit Vector (FR)
F | P | P | F | P | F | … | F | F | P
Number of Rows

## Slide 57: Determining Preventive Refresh Latency
PaCRAM
Fully Restored Bit Vector (FR)
F | P | P | F | P | F | … | F | F | P
Activated Row Address
F  Full Charge Restoration Latency P  Partial Charge Restoration Latency

## Slide 58: PaCRAM’s Row State Transition
F State  P State
  When the row is refreshed using full charge restoration
  After fully restoring a row, PaCRAM uses partial charge restoration
P State  F State
  PaCRAM periodically resets each rows state to F state
  Full Charge Restoration Interval

## Slide 59: Full Charge Restoration Interval
To Guarantee that any victim is not refreshed by more than a safe number (NPCR) of consecutive partial charge restorations
PaCRAM assumes the worst case where a DRAM row is accessed as frequently as possible
The smallest time window that can contain NPCR preventive refreshes
Attack Time
Preventive Refresh Latency
Time to Receive One Preventive Refresh

## Slide 60: Hardware Complexity Analysis of PaCRAM
Chip area and access latency analysis using CACTI
PaCRAM requires 1 bit for each DRAM row (Fully Restored Bit Vector)
For a DRAM module with 32 banks and 64K row/bank,
  256 KB of SRAM
  0.09% of a high-end Intel Xeon processor
  1.35% of the memory controller area
  Access latency of 0.27ns (<< row activation latency)
PaCRAM introduces a small additional area overhead

## Slide 61: PaCRAM with on-DRAM-die RowHammer Mitigation Mechanisms
On-DRAM-die mitigation mechanism
  PRAC
  Chronus
  …
PaCRAM can be implemented inside DRAM chip
  On-DRAM-die mitigation mechanism inserts a Back-Off signal to request a preventive refresh
  PaCRAM stores the preventive refresh latency in the mode register (MR)
  Memory controller checks the latency value in MR and issues a preventive refresh with the latency provided by PaCRAM

## Slide 62: Profiling Cost Analysis
For PaCRAM to work robustly,
  How much charge restoration latency can be reduced
  How RowHammer threshold changes with partial charge restoration
  How many partial charge restorations we can perform consecutively
Profiling
  The system perform profiling the very first time DRAM is initialized
  DRAM manufacturers perform profiling and store metadata in SPD
  The system can perform online profiling

## Slide 63: Effect of Charge Restoration Latency on System Performance
Charge Restoration Latency
System Performance (Norm. to No PaCRAM)
System performance first increases, then decreases as charge restoration latency decreases

## Slide 64: Effect of Charge Restoration Latency on System Performance
Charge Restoration Latency
System Performance (Norm. to No PaCRAM)

## Slide 65: Reducing Periodic Refresh Latency
PaCRAM improves the system performance and energy efficiency by reducing periodic refresh overhead

## Slide 66: Understanding RowHammer Under Reduced Refresh Latency: Experimental Analysis of Real DRAM Chips and Implications on Future Solutions
Yahya Can Tuğrul
A. Giray Yağlıkçı İsmail Emir Yüksel
Ataberk Olgun Oğuzhan Canpolat Nisa Bostancı
Mohammad Sadrosadati Oğuz Ergin Onur Mutlu

## Slide 67: BANNERS
AAAAAAA
AAAAAAA
AAAAAAA
AAAAAAA
AAAAAAA
AAAAAAA
AAAAAAA