## Slide 1: Project PBerry: FPGA Acceleration for Remote Memory
Irina Calciu, Ivan Puddu, Aasheesh Kolli
Andreas Nowatzyk, Jayneel Gandhi, Onur Mutlu
Pratap Subrahmanyam
HotOS 2019

## Slide 2: Recent remote memory systems
Systems: Infiniswap, HotPot, Remote regions
Same goal: pool remote memory
Different interfaces: swapping, dspm, file system
Same mechanism: page faults

## Slide 3
Remote memory systems use page faults
Overheads:
1. Page faults overheads
2. Page granularity
Use cache coherence (w/ FPGA)
Implications:
1. Reduce page faults
2. Cache line granularity
1. Remote memory
2. Live migration
3. Code analysis
4. Security
5. …
Problem
Solution
Impact
Use cache coherence traffic to track application memory accesses

## Slide 4: Remote memory
OS
Memory
Application host
(Local)
Memory
Memory host
(Remote)
1
Microsecond network
APP1
2
3
4
1
2
3
4
APP2
APP3
OS
1. Demand paging (fetch pages)
2. Evict pages
Local
Remote
X
X
2’. Dirty data tracking

## Slide 5: How to track dirty data?
Current solution:
1. Write-protect page
2. On page fault: mark page dirty
OS
Memory
Application host
APP1
1
2
3
4
X

## Slide 6: Overheads in current remote memory systems
1. Dirty data amplification (4KB, 2MB, 1GB)
  Breaking large pages to 4KB pages
[Smarduch et al., CloudOpen-Japan 2015]
Application | Amplification (4KB pages) | Amplification (2MB pages) | Amplification (64B cache-line)
Redis-random | 96.82 % (3.87 KB) | 99.99 % (1.99 MB) | 31.70 % (20.29 B)
Redis-seq | 82.91 % (3.32 KB) | 99.83 % (1.99 MB) | 17.18 % (10.99 B)

## Slide 7: Overheads in current remote memory systems
1. Dirty data amplification (4KB, 2MB, 1GB)
  Breaking large pages to 4KB pages
2. Application slowdown due to (write) page faults
3. Cost of write-protecting pages
[Smarduch et al., CloudOpen-Japan 2015]

## Slide 8
Remote memory systems use page faults
Overheads:
1. Page faults overheads
2. Page granularity
Use cache coherence (w/ FPGA)
Implications:
1. Reduce page faults
2. Cache line granularity
1. Remote memory
2. Live migration
3. Code analysis
4. Security
5. …
Problem
Solution
Impact
Use cache coherence traffic to track application memory accesses

## Slide 9: Key idea: use cache coherence for tracking memory accesses
Memory
CPU Caches
Modified
Exclusive
Shared
Invalid
Write
Write
Write
FlushX
M
Flush
MESI protocol
Read
Read

## Slide 10: Field Programmable Gate Array (FPGA)
Integrated circuit
Reconfigured after manufacturing
“Program the hardware”

## Slide 11: Key idea: use cache coherence for tracking memory accesses
CPU Caches
Memory
S
Memory
Coherent
interconnect
FPGA
CPU

## Slide 12: Key idea: use cache coherence for tracking memory accesses
CPU Caches
Memory
M
Memory
Coherent
interconnect
FPGA
CPU

## Slide 13: FPGA primitives
Read and write tracking using cache coherence
  Data pages
  Code pages
  OS pages (page tables)
Local and remote copy
In-place transform

## Slide 14: Remote memory using a cache coherent FPGA
Application host
Memory
Memory host
Microsecond network
Memory
Memory
OS
APP1
OS
DRAM cache for remote memory
1. Demand paging (fetch pages)
2. Evict pages
Local
Remote
2’. Dirty data tracking

## Slide 15: 1. “Demand paging” using a cache coherent FPGA
Application host
Memory
Memory host
Microsecond network
Memory
Memory
1
1
OS
APP1
OS
Fake physical address space
1

## Slide 16: 1. “Demand paging” optimization: translation triggered prefetching
Application host
Memory
Memory host
Microsecond network
Memory
Memory
1
1
OS
APP1
OS
Fake physical address space
1

## Slide 17
Remote memory systems use page faults
Overheads:
1. Page faults overheads
2. Page granularity
Use cache coherence (w/ FPGA)
Implications:
1. Reduce page faults
2. Cache line granularity
1. Remote memory
2. Live migration
3. Code analysis
4. Security
5. …
Problem
Solution
Impact
Use cache coherence traffic to track application memory accesses

## Slide 18: Benefits
Reduce (write) page faults
Reduce dirty data amplification (cache-line)
Determine access pattern, smart prefetching
Downside: FPGA memory slower than CPU memory

## Slide 19: Preliminary results (emulated)
Redis-random:
  89% less dirty data (cache-line vs. page granularity)
  27% faster than WP
Redis-seq:
  50% less dirty data (cache-line vs. page granularity)
  4% faster than WP
1. Demand paging (fetch pages)
2. Evict pages
Local
Remote
2’. Dirty data tracking

## Slide 20: Other use cases
Use case | Page type | Primitive
Live migration | Data, page tables | Read/write tracking, remote copy
Compression, Encryption | Data | Read/write tracking, in-place transform
Replication, Checkpointing | Data | Write tracking, local/remote copy
Near-memory compute | Data | Read/write tracking, in-place transform
Code analysis | Code | Read tracking
Security | Data | Read/write tracking

## Slide 21
Remote memory systems use page faults
Use cache coherence (w/ FPGA)
Other use cases
Problem
Solution
Impact
Use cache coherence traffic to track application memory accesses
Contact: icalciu@vmware.com
Thank you!