## Slide 1: 7th Workshop on Memory-Centric Computing Processing-Using-Memory in Real DRAM Chips
İsmail Emir Yüksel
ICS 2026
6 July 2026

## Slide 2: Brief Self Introduction
Ismail Emir Yuksel
    Researcher @ SAFARI Research Group since September 2022
      PhD @ ETH Zurich (Feb 2024 – ongoing)
    ismail.yuksel@safari.ethz.ch
Research interests:
    Computer architecture
    Processing-in-Memory (specifically Processing-using-DRAM)
    DRAM Safety, Security and Reliability
    Hardware security, safety, reliability, performance, availability, fairness, energy efficiency
    ...

## Slide 3: Problem
Computing
is Bottlenecked by Data

## Slide 4: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
    We can generate more than we can process
    We need to perform more sophisticated analyses on more data

## Slide 5: Huge Demand for Performance & Efficiency
Source: https://youtu.be/Bh13Idwcb0Q?t=283
~4 orders of magnitude increase in memory requirement
in just a few years!

## Slide 6: Huge Demand for Performance & Efficiency
development of new
sequencing technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Oxford Nanopore MinION
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 7: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 8: Data Movement Bottleneck
Today’s computing systems are processor centric
All data is processed in the processor  at great system cost
Memory
Channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
More than 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018

## Slide 9: Processor-Centric System Performance
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 10: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 11: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.

## Slide 12: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
6400X
A memory access consumes 6400X
the energy of a simple integer addition

## Slide 13: Energy Waste in Accelerators
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 14: Energy Waste in Accelerators
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]
> 90% of the total system energy
is spent on memory in large ML models

## Slide 15: Fundamental Problem
Processing of data
is performed
far away from the data

## Slide 16: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 17: Process Data Where It Makes Sense
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
SRAM
Storage
Storage
Sensors

## Slide 18: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 19: Goal: Processing Inside Memory/Storage
Many questions … How do we design the:
    compute-capable memory & controllers?
    processors & communication units?
    software & hardware interfaces?
    system software, compilers, languages?
    algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory/Storage
Database
Graphs
Media
ML Model
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 20: Processing in/near Memory: An Old Idea
Kautz, “Cellular Logic-in-Memory Arrays”, IEEE TC 1969.
https://doi.org/10.1109/T-C.1969.222754

## Slide 21: Processing in/near Memory: An Old Idea
Stone, “A Logic-in-Memory Computer,” IEEE TC 1970.
https://safari.ethz.ch/architecture/fall2020/lib/exe/fetch.php?media=stone_logic_in_memory_1970.pdf

## Slide 22: Processing-in-Memory: Two Types
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
1
Processing-Near-Memory: Computation logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells & circuitry to perform computation
Processing-
Using-DRAM
…
…
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 23: Focus: Processing-using-DRAM
We can natively support
    Bulk bitwise COPY and INIT/ZERO
    Bulk bitwise AND, OR, NOT, MAJ, NOR, NAND
    True Random Number Generation; Physical Unclonable Functions
    More complex computation using Lookup Tables
At low cost
Using analog computation capability of DRAM
    Idea: activating (multiple) rows performs computation
      Even in commodity off-the-shelf DRAM chips!
30X-257X performance and energy improvements
    Seshadri+“RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
    Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.
    Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
    Hajinazar+, “SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM,” ASPLOS 2021.
    Oliveira+, “MIMDRAM: An End-to-End Processing-Using-DRAM System for High-Throughput, Energy-Efficient and Programmer-Transparent Multiple-Instruction Multiple-Data Processing,” HPCA 2024.

## Slide 24: DRAM Organization
DRAM Module
DRAM
Chip
DRAM Chip
…
…
Chip I/O
Bank
DRAM Bank
Subarray
Sense Amplifiers
DRAM Cell
DRAM Row
Wordline
Bitline
Sense Amps.
Notes: DRAM is used as the main memory in many computing systems. [CLICK]
a DRAM module consists of multiple DRAM chips [CLICK]
Each chip contains multiple banks [CLICK]
Each bank is composed of multiple subarrays and sense amplifiers [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row of sense amplifiers via bitlines [CLICK]

## Slide 25: Major DRAM Operations
DRAM Subarray
Sense
Amplifiers
I/O Circuitry
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the bank for a new ACTIVATE
1
2
3
Notes: Data is internally accessed in a row granularity. To access data,
[CLICK] the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers
[CLICK] Then, column accesses are serviced from the sense amplifiers
[CLICK] Finally, the subarray needs to be precharged to get ready for the next row activation

## Slide 26: Closer Look to a DRAM Cell
Sense Amp
enable
bitline
wordline
capacitor
access transistor

## Slide 27: DRAM Cell Operation upon ACT
½ VDD + δ
0
½ VDD
0
1
1
VDD
raise wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell regains charge
Sense Amp
deviation in bitline voltage
½ VDD
0
enable
bitline
wordline
capacitor
access transistor

## Slide 28: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 29: Current Systems: Data Copy
Memory
MC
L3
L2
L1
CPU

## Slide 30: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 31: In-DRAM Row-Copy (RowClone)
[Seshadri+ MICRO’13]
d
s
t
r
c
s
d
s
t
s
r
c
Copying the source (src) row’s content to the destination (dst) row
s
r
c
Notes: In this study, we focus on two prior in-DRAM operations. First one is in-DRAM Row-Copy, which is also called RowClone
[CLICK] The RowClone operation copies the source row’s content to the destination row. Now let’s see how we perform RowClone

## Slide 32: RowClone: In-DRAM Bulk Data Copy
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
0
1
activate
source
activate
destination
data gets copied source to destination
Sense Amp
Source Cell
Destination Cell

## Slide 33: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013

## Slide 34: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 35: Triple-Row Activation: Majority Function
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
activate
all three rows simultaneously
0
1
0
1

## Slide 36: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C

## Slide 37: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C
Output = MAJ(A, B, C)
= C (A OR B) +
~C (A AND B)
Control the value of C to perform bitwise OR or AND

## Slide 38: In-DRAM Acceleration of Database Queries
>4-12X Performance Improvement

## Slide 39: More on Ambit
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 40: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 41: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program

## Slide 42: SIMDRAM Key Results
Large improvements over CPU & high-end GPU:
Throughput: 88× and 5.8×
(16 complex operations)
Energy: 257× and 31×
(16 complex operations)
Application Performance: 21× and 2.1×
(seven common real-world applications)

## Slide 43: More on SIMDRAM
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 44: MIMDRAM: More Flexible Processing using DRAM
Appears at HPCA 2024
https://arxiv.org/pdf/2402.19080.pdf

## Slide 45: MIMDRAM: Key Idea (I)
Enable narrower-width operations than a DRAM row
row decoder
global wordline
DRAM mat
Key Issue:
on a DRAM access, the global wordline propagates across all DRAM mats
Fine-Grained DRAM: segment the global wordline to access individual DRAM mats
global sense amplifier
Notes: MIMDRAM’s key idea is to leverage fine-grained DRAM access for processing-using-DRAM operation
[CLICK] In traditional architectures, on every DRAM access, all rows in a DRAM mat are asserted even if only portion of that row will be accessed, since the global wordline propagates across all DRAM MATS.
[CLICK] Fine-Grained DRAM architectures segments the global wordline to access individual DRAM mats on an DRAM access.
[NEXT]

## Slide 46: MIMDRAM: Key Idea (II)
row decoder
Fine-Grained DRAM: segment the global wordline to access individual DRAM mats
segmented global wordline
  Fine-grained DRAM for energy-efficient DRAM access:
[Cooper-Balis+, 2010]: Fine-Grained Activation for Power Reduction in DRAM [Udipi+, 2010]: Rethinking DRAM Design and Organization for Energy-Constrained Multi-Cores
[Zhang+, 2014]: Half-DRAM [Ha+, 2016]: Improving Energy Efficiency of DRAM by Exploiting Half Page Row Access
[O’Connor+, 2017]: Fine-Grained DRAM
[Olgun+, 2024]: Sectored DRAM
global sense amplifier
Notes: [CLICK] Fine-grained DRAM has been previously proposed for energy-efficient DRAM access
[NEXT]

## Slide 47: Sectored DRAM
Ataberk Olgun, F. Nisa Bostanci, Geraldo F. Oliveira, Yahya Can Tugrul, Rahul Bera, A. Giray Yaglikci, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "Sectored DRAM: A Practical Energy-Efficient and High-Performance Fine-Grained DRAM Architecture" ACM Transactions on Architecture and Code Optimization (TACO), [online] June 2024. [arXiv version] [ACM Digital Library version]
https://arxiv.org/pdf/2207.13795

## Slide 48: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Use fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently
global sense amplifier
Notes: In the context of processing-using-DRAM, fine-grained DRAM provides three benefits
[CLICK] First, it improves SIMD utilization for a single PUD operations, by accessing only the DRAM mats with the target input operands
[NEXT]

## Slide 49: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Use fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
Notes: Also, we can leverage the unused DRAM mats to concurrently execute independent PUD operations, in a multiple instruction, multiple data execution model
[NEXT]

## Slide 50: MIMDRAM: Key Idea (III)
segmented global wordline
  Use fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
global sense amplifier
row decoder
Notes: Second, we can leverage the global and local data buses that connect DRAM mats to move data within a DRAM subarray, allowing for the implementation of vector reduction operations
[NEXT]

## Slide 51: MIMDRAM: Key Idea (III)
row decoder
segmented global wordline
  Use fine-grained DRAM for processing-using-DRAM:
1
Improves SIMD utilization
for a single PUD operation, only access the DRAM mats with target data
for multiple PUD operations, execute independent operations concurrently → multiple instruction, multiple data (MIMD) execution model
global sense amplifier
2
Enables low-cost interconnects for vector reduction
global and local data buses can be used for inter-/intra-mat communication
3
Eases programmability
SIMD parallelism in a DRAM mat is on par with vector ISAs’ SIMD width
512 columns
Notes: Third, since the number of DRAM rows in a single DRAM mat are on par with the number of SIMD lanes in vector ISAs, we can ease PUD’s programmability by leveraging current compiler infrastructure for such ISAs
[NEXT]

## Slide 52: MIMDRAM: Compiler Support
Transparently to programmer:
extract SIMD parallelism from an application, and
schedule PUD instructions while maximizing utilization
Goal
Three new LLVM-based passes targeting PUD execution
Notes: Our goal is to transparently from the user, extract SIMD parallelism from an application and schedule PUD instructions while maximizing SIMD utilization
[CLICK] To this end, we implemented three LLVM passed targeting PUD execution
[NEXT]

## Slide 53: MIMDRAM Perf, Energy, Perf/Watt
582X and 13,612X the energy efficiency of CPU and GPU, respectively
Notes: We evaluate MIMDRAM using twelve real-world applications
and 495 multi-programmed application mixes.
When using 64 DRAM subarrays per bank and 16
banks for PuD computation in a DRAM chip, MIMDRAM
provides 1) 13.2Å~/0.22Å~/173Å~ the performance,
2) 0.0017Å~/0.00007Å~/0.004Å~ the energy consumption, 3)
582.4Å~/13612Å~/272Å~ the performance per Watt of the
CPU [215]/GPU [216]/SIMDRAM [174] baseline (Fig. 5) and
4) when using a single DRAM subarray, 15.6°ø the SIMD
utilization (i.e., SIMD efficiency) of the prior state-of-the-art
PuD framework, SIMDRAM [174].

## Slide 54: Capabilities of Off-The-Shelf Memory
Existing DRAM Chips
Are Already Quite Capable

## Slide 55: RowClone and MAJ3 in Real DRAM Chips
Key Idea: Violate DRAM timing parameters to mimic RowClone and Ambit’s MAJ3 operation

## Slide 56: Real Processing Using Memory Prototype
End-to-end RowClone & TRNG using off-the-shelf DRAM chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 57: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s
Host Machine
FPGA Board
RISC-V System
PiM-Enabled DIMM

## Slide 58: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 59: More on PiDRAM
Ataberk Olgun, Juan Gomez Luna, Konstantinos Kanellopoulos, Behzad Salami, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "PiDRAM: A Holistic End-to-end FPGA-based Framework for Processing-in-DRAM" ACM Transactions on Architecture and Code Optimization (TACO), March 2023. [arXiv version] Presented at the 18th HiPEAC Conference, Toulouse, France, January 2023. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (40 minutes)] [PiDRAM Source Code]

## Slide 60: Focus on Recent Real DRAM Chip-based PuD Works
HPCA 2024
DSN 2024
ISCA 2025

## Slide 61: Functionally-Complete Boolean Logic in Real DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
Ismail Emir Yüksel
Yahya C. Tugrul Ataberk Olgun F. Nisa Bostancı
A. Giray Yaglıkçı Geraldo F. Oliveira Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Functionally-Complete Boolean Logic in Real DRAM Chips

## Slide 62: Executive Summary
Motivation: Processing-using-DRAM can alleviate the performance and energy bottlenecks caused by data movement
  Prior works show that existing DRAM chips can perform three-input majority and two-input AND and OR operations
Problem: Proof-of-concept demonstrations on commercial off-the-shelf (COTS) DRAM chips do not provide
  functionally-complete operations (e.g., NAND or NOR)
  NOT operation
  AND and OR operations with more than two inputs
Experimental Study: 256 DDR4 chips from two major manufacturers
Key Results:
  COTS DRAM chips can perform NOT and {2, 4, 8, 16}-input AND, NAND, OR, and NOR operations with very high reliability (>94% success rate)
  Data pattern and temperature only slightly affect the reliability of these operations (<1.98% decrease in success rate)
Notes: Let’s start with an executive summary.
[CLICK] Processing-Using-DRAM is a promising paradigm that can alleviate the performance and energy bottlenecks caused by frequent data movement between main memory and processing units.
[CLICK] Proof-of-concept demonstrations on commercial-off-the-shelf DRAM chips do not provide
[CLICK]Functionally-complete operations, such as NAND or NOR
[CLICK] NOT operation
[CLICK] More than two-input AND and OR operations
[CLICK]In this study, we test 256 off-the-shelf DDR4 DRAM chips from two major manufacturers
[CLICK] Based on our analyses, we highlight that
[CLICK] We can perform NOT and up to 16-input AND, NAND, OR, and NOR operations with very high reliability
[CLICK] The impact of data patterns and the temperature on the reliability of these operations are small.
our work demonstrates the capability of performing functionally-complete Boolean logic in COTS DRAM chips. We believe these empirical results demonstrate
the promising potential of using DRAM as a computation substrate. Now let’s delve in ..

## Slide 63: DRAM Organization
DRAM Module
DRAM
Chip
DRAM Chip
…
…
Chip I/O
Bank
DRAM Bank
Subarray
Sense Amplifiers
DRAM Cell
DRAM Row
Wordline
Bitline
Sense Amps.
Notes: DRAM is used as the main memory in many computing systems. [CLICK]
a DRAM module consists of multiple DRAM chips [CLICK]
Each chip contains multiple banks [CLICK]
Each bank is composed of multiple subarrays and sense amplifiers [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row of sense amplifiers via bitlines [CLICK]

## Slide 64: DRAM Open Bitline Architecture
SA
SA
SA
SA
SA
SA
DRAM Bank
Subarray
SA
bitline
bitline
Sense
Amplifier
Notes: To achieve high-density DRAM chips, open-bitline architecture is widely adopted in modern DRAM modules.
[CLICK]
In this architecture each subarray’s bitlines are connected to two rows of sense amplifiers one above and one below the subarray,
This results in neighboring subarrays share common sense amplifiers.

## Slide 65: DRAM Open Bitline Architecture
Sense
Amplifier
SA
SA
SA
SA
SA
SA
DRAM Bank
Subarray
bitline
bitline
Serves as the reference for the SA
Activated
Not
Activated
NOT
Gate
Notes: [Click] During an activation, another bitline in a neighboring subarray is also involved to serve as the reference of the sense amplifier, which is bitline-bar in this example.
After a successful activation, the bitline and bitline-bar have a complementary voltage
[CLICK] as the sense amplifier consists of two back-to-back inverters.

## Slide 66: DRAM Operation
DRAM Subarray
Sense
Amplifiers
I/O Circuitry
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the bank for a new ACTIVATE
1
2
3
Notes: Data is internally accessed in a row granularity. To access data,
[CLICK] the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers
[CLICK] Then, column accesses are serviced from the sense amplifiers
[CLICK] Finally, the subarray needs to be precharged to get ready for the next row activation

## Slide 67: The Capability of COTS DRAM Chips
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 68: DRAM Testing Infrastructure
Developed from DRAM Bender [Olgun+, TCAD’23]*
Fine-grained control over DRAM commands, timings, and temperature
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure
to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Notes: [CLICK] We use a FPGA based DDR4 testing infrastructure developed from DRAM bender that
[CLICK] enables fine-grained control over DRAM commands, timings, and temperature

## Slide 69: Laboratory for Understanding Memory
Notes: And in our lab, we have many machines to test many DRAM modules and chips

## Slide 70: Laboratory for Understanding Memory
Notes: And in our lab, we have many machines to test many DRAM modules and chips

## Slide 71: DRAM Chips Tested
256 DDR4 chips from two major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK]We test 256 DDR4 chips from two major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 72: The Capability of COTS DRAM Chips
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 73: Key Observation
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
Activating two rows in quick succession
can simultaneously activate
multiple rows in neighboring subarrays
Neighboring Subarrays
Subarray X
Subarray Y
Row A
Row B
DRAM Bank
Shared Sense Amplifiers
14ns
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate multiple rows in neighboring subarrays
[CLICK] You may remember this pictorial example where Subarray X and Subarray Y are neighbor subarrays and Row A is in Subarray X and Row B is in Subarray Y.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT, we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate multiple rows at once in neighboring subarrays

## Slide 74: Hypothesis: Row Decoder Circuitry
Simultaneous many-row activation is possible due to the hierarchical DRAM row decoder design
Row Decoder
Row Address
Wordline
DRAM Subarray
Row Address (RA)
2x4
Stage 1 Decoder
Stage 2 Decoder
Stage 3 Decoder
Stage 4 Decoder
Stage 5 Decoder
Notes: We hypothesize that simultaneous many-row activation is possible due to the hierarchical DRAM row decoder design
[CLICK] Let’s recall a DRAM subarray where we have rows, sense amplifiers and row decoder circuitry
[CLICK] Row decoder circuitry decodes the row address that is sent with activate command and assert the corresponding wordline
[CLICK] As we mentioned, row decoder circuitry is hierarchical and has multiple stages of decoders
[CLICK] Each decoder stage takes some parts of the row address and asserts intermediate signals that are essentially drives the wordline using such intermediate signals

## Slide 75: Row Decoder: A Tree Example
We can visualize the hierarchical row decoder circuitry as a tree
Wordline A
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Wordline B
...
...
Stage 1
Decoder
Stage 5
Decoder
Decoder Output
2x4
Notes: To explain it in a higher abstraction level,
[CLICK] We can visualize the row decoder as a tree which
[CLICK] Each level of the tree represents a decoder stage
[CLICK] each node represents a decoder output

## Slide 76: Activating a Single Row
Wordline B
Wordline A
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Wordline A
ACT Row A
PRE
36ns
1. Decode Row A address
2. Assert corresponding signals
3. Follow asserted nodes path from root to leaf
4. Assert wordline
Notes: Let’s see an example when we activate a single row
[CLICK] Assume that we issue ACT Row A command, which will essentially assert the Wordline A signal
[CLICK] After issuing the activation command, the row decoder circuitry decodes Row A address
[CLICK] And assert corresponding signals in the tree
[CLICK] After the decoding completed, row decoder follows the asserted nodes path from root to leaf
[CLICK] As a result, it asserts wordline, in this it is Wordline A
[CLICK] After a successful activation we can issue PRE command which deasserts every asserted signals in the row decoder circuitry including the wordline

## Slide 77: Activating Many Rows: A Walkthrough
Wordline A
...
...
...
...
...
...
...
...
...
...
...
...
...
...
Wordline B
...
...
Wordline B
Wordline A
Back-to-back ACT commands with violated timings asserts many more signals in the row decoder
ACT Row A
PRE
36ns
ACT Row B
14ns
<3ns
<3ns
1. Keep the previously asserted signals active
2. Decode Row B & assert corresponding signals
3. Follow newly asserted nodes’ path
4. Simultaneously activate many rows
Notes: So that was an activation of a single row, now let’s see a simultaneous activation of many rows.
[CLICK] Our hypothesis is back-to-back ACT commands with violated timings asserts many more signals in the circuitry

## Slide 78: Hypothesis: Row Decoder Circuitry
(More discussions & hypotheses in the paper)
https://arxiv.org/pdf/2405.06081
Notes: As our time limited, I would like to refer you to our paper for more detailed circuitry and discussions about row decoder circuitry

## Slide 79: Key Results
Exactly the same number of rows
in each subarray
are activated
Twice as many rows in one subarray
compared to its neighbor subarray are activated
COTS DRAM chips have two distinct sets of
activation patterns in neighboring subarrays
when two rows are activated with violated timings
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 16 rows
Subarray X
Subarray Y
Shared Sense Amplifiers
Up to 16 rows
Up to 32 rows
A total of 32 rows
A total of 48 rows
Notes: We observe when Row A and B in neighboring subarrays are activated with violated timing parameters
[CLICK] Off-the-shelf DRAM chips have two distinct sets of simultaneous activation patterns in two neighboring subarrays
[CLICK] First pattern is exactly the same number rows in each subarray are activated.
[CLICK] We observe that we can activate up to 16 rows in neighboring subarrays, in other words a total of 32 rows
[CLICK] Second pattern is twice as many rows in one subarray compared to its neighbor subarray are activated
[CLICK] We observe that we can activate up to 16 rows in one subarray while activating up to 32 rows in its neighbor subarray, a total of 48 rows

## Slide 80: The Capability of COTS DRAM Chips
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 81: Key Idea
Connect rows in neighboring subarrays
through a NOT gate by simultaneously activating rows
SA
A
src
dst
ACT src
ACT dst
SA
A
src
dst
SA
A
src
dst
~A
NOT gate
Notes: Our key idea is to leverage the connection between neighboring subarrays,
[CLICK] the NOT gate in the sense amplifier.
[CLICK] By simultaneously activating rows in neighboring subarrays, we can connect these rows through a NOT gate
[CLICK] As an example, source and destination in neighboring subarrays and if we first activate src
[CLICK] and then activate destination, this result in sense amplifier to drive the negated src value to the dst

## Slide 82: NOT Operation: A Walkthrough
½ VDD
src
dst
½ VDD
GND
GND
ACT src
connects src to bitline
Notes: Let’s see how we can perform NOT operation in real DRAM chips at a lower abstraction-level
[CLICK] As an example, we have source and destination cells, both store GROUND (low voltage) and bitlines are precharged to vdd over two
[CLICK] We first issue an activation to the source, which asserts the source wordline and starts charge sharing process between source and its bitline

## Slide 83: NOT Operation: A Walkthrough
GND
src
dst
GND
GND
VDD
ACT src
Nominal
drives bitline to GND
drives bitline to VDD
Notes: We wait for nominal timing parameters, which assures sense amplifier amplifies the difference and
[CLICK] drives ground to the source’s bitline and VDD to the destination’s bitline

## Slide 84: NOT Operation: A Walkthrough
src
dst
connects dst to bitline
ACT src
PRE
ACT dst
Nominal
<3ns
GND
VDD
sense amplifier is still enabled
dst’s bitline is still VDD
Notes: We then issue back-to-back precharge and activation commands with violated timing parameters. This operation leads to
[CLICK] connecting destination cell to its bitline
[CLICK] keeping the sense amplifier enabled
[CLICK] keeping the destination’s bitline to VDD

## Slide 85: NOT Operation: A Walkthrough
src
dst
negated value of src (VDD) is written to dst
ACT src
PRE
ACT dst
Nominal
<3ns
GND
VDD
Notes: Eventually, as sense amplifier is enabled and bitline is still VDD, the negated value of the source, which is VDD, is written to dst

## Slide 86: Reliability Metric
Success Rate (for a DRAM cell)
Percentage of trials where the correct output of
a tested operation is stored in the cell
Total of 10000 trials
GND
src
dst
GND
…
Success rate for this cell: 50%
Notes: To evaluate the reliability of NOT Operation,
[CLICK]we define a metric called success rate
[CLICK] Success rate for a DRAM cell refers to percentage of correct trials
[CLICK] We test total of 10000 trials and record the success rate for each tested cell

## Slide 87: Key Takeaways from In-DRAM NOT Operation
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Key Takeaway 1
Temperature has a small effect on
the reliability of NOT operations
Key Takeaway 2
Notes: This analysis provides two key takeaway lessons: [CLICK]
[CLICK] First, off-the-shelf DRAM chips can perform NOT operations with up to 32 destination rows
[CLICK] Second, temperature has a small effect on the reliability of NOT operations

## Slide 88: Performing NOT in COTS DRAM Chips
There is at least one DRAM cell that can
perform the NOT operation
with a 100% success rate
COTS DRAM chips can perform NOT operations
with up to 32 destination rows
Notes: Let’s take a look at our first results
[CLICK] In the x-axis you see the number of destination rows and y-axis shows the success rate distributions across tested DRAM cells
[CLICK] We observe that there is at least one DRAM cell that can perform the NOT operation with a 100% success rate in every tested number of destination rows
[CLICK] Our takeaway from this experiment is off-the-shelf DRAM chips are capable of performing NOT operations with up to 32 destination rows

## Slide 89: The Capability of COTS DRAM Chips
We demonstrate that COTS DRAM chips:
Can simultaneously activate up to
48 rows in two neighboring subarrays
1
Can perform NOT operation
with up to 32 output operands
2
Can perform up to 16-input
AND, NAND, OR, and NOR operations
3
Notes: [CLICK]In this study, we experimentally demonstrate that off-the-shelf DRAM chips
[CLICK] Can simultaneously activating up to 48 DRAM rows in two neighboring subarrays
[CLICK] Can performing NOT operation with up to 32 output operands
[CLICK] Can performing up to 16-input AND, NAND, OR, and NOR operations

## Slide 90: Key Idea
Manipulate the bitline voltage to express
a wide variety of functions using
multiple-row activation in neighboring subarrays
Multiple Row ACT
V(A,B)
SA
B
X
Y
V(X,Y)
X
SA
B
Y
VREF
VREF
A
A
sense amp.
compares
V(A,B) and V(X,Y)
Notes: [CLICK] Let me give the key idea by showing four cells: X,Y,A, and B, two from each neighboring subarrays.
[CLICK] Now if we activate these four cells simultaneously,
[CLICK] the bitline at the bottom subarray becomes the function of voltages in X and Y and the bitline at the top subarray becomes the function of voltages in A and B
[CLICK] Sense amplifier will compare voltage at the bottom bitline to the voltage at the top bitline and figure out which one is higher

## Slide 91: Two-Input AND and NAND Operations
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
VDD
VDD/2*
Notes: Now let me show you the basic intuition to perform two-input AND and NAND operations.
[CLICK] For this example, we have two subarrays: reference and compute subarrays, each of which consists of two cells.
[CLICK] Reference subarray’s cells store VDD and VDD/2 as a side note we store VDD/2,using FracDRAM’s technique.
[CLICK] and in the compute subarray we have X and Y.
With this setup, if we activate all these four cells
[CLICK] using ACT-PRE-ACT sequence, we will get AND of X and Y in the compute subarray and NAND of X and Y in the reference subarray.
[CLICK] To simplify things assume bitlines will have the average value of their corresponding cell’s voltage values. Such as, Reference bitline will be the average of VDD and VDD half.
Now let me prove that that is the case. I am going to cover all combinations of X and Y values.

## Slide 92: Two-Input AND and NAND Operations
VDD=1 & GND = 0
X
Y
COM
0
0
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
GND
sense amp.
compares
the voltages on the bitlines
VDD
GND
0
1
Notes: In the first row of truth table, X and Y are GND.
[CLICK] This results in bitline in the compute subarray to be GND and the reference bitline is 3 vdd over 4.
[CLICK] Sense amplifier will amplify the voltage difference and since 3 vdd over 4 is greater than GND, reference cells store VDD and compute cells store GND

## Slide 93: Two-Input AND and NAND Operations
VDD=1 & GND = 0
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD/2
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
sense amp.
compares
the voltages on the bitlines
VDD
GND
0
1
0
1
0
0
0
1
Notes: In the second row of truth table, X is GND and Y is VDD
[CLICK] As the bitline voltage in compute subarray is lower than reference subarray’s bitline voltage
[CLICK] reference cells store VDD and compute cells store GND

## Slide 94: Two-Input AND and NAND Operations
VDD=1 & GND = 0
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD/2
sense amp.
compares
the voltages on the bitlines
VDD
GND
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
1
0
0
1
0
0
0
1
0
1
0
1
Notes: In the third row of truth table, X is VDD and Y is GND
[CLICK] This results in bitline in the compute subarray to be VDD half and the reference bitline is 3 vdd over 4.
[CLICK] Again, the sense amplifier will amplify the voltage difference and since 3 vdd over 4 is greater than vdd half, reference cells store VDD and compute cells store GND

## Slide 95: Two-Input AND and NAND Operations
VDD=1 & GND = 0
ACT
PRE
ACT
<3ns
<3ns
3VDD/4
VDD
X
Y
COM
0
0
1
0
1
0
0
1
1
1
REF
1
1
1
0
sense amp.
compares
the voltages on the bitlines
GND
VDD
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1
Notes: In the last row of truth table, X and Y are both VDD
[CLICK] This results in bitline in the compute subarray to be VDD and the reference bitline is 3 vdd over 4.
[CLICK] Again, the sense amplifier will amplify the voltage difference. However, this time compute subarray’s bitline is greater than. As a results reference cells store GND and compute cells store VDD
Consequently, this example shows compute subarray stores the result of the and operation of X and Y. and reference subarray cells store the result of the nand of operation of X and Y.

## Slide 96: Two-Input AND and NAND Operations
VDD=1 & GND = 0
Reference Subarray (REF)
Compute Subarray (COM)
X
Y
ACT
PRE
ACT
<3ns
<3ns
AVG(VDD,VDD/2)
AVG(X,Y)
*Gao et al., "FracDRAM: Fractional Values in Off-the-Shelf DRAM," in MICRO, 2022.
AND
NAND
VDD
VDD/2*
X
Y
COM
REF
1
1
1
0
0
1
0
1
1
0
0
1
0
0
0
1

## Slide 97: Key Takeaways from In-DRAM Operations
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
Key Takeaway 1
Data pattern slightly affects
the reliability of AND, NAND, OR, and NOR operations
Key Takeaway 3
COTS DRAM chips can perform
AND, NAND, OR, and NOR operations
with very high reliability
Key Takeaway 2

## Slide 98: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
{2, 4, 8, 16}-input AND, NAND, OR, and NOR operations
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 99: Performing AND, NAND, OR, and NOR
COTS DRAM chips can perform
16-input AND, NAND, OR, and NOR operations
with very high success rate (>94%)
Notes: Let’s see our first results
[CLICK] Here is the plot, in the x-axis we have the number of input operands and y-axis shows the success rate distribution across dram cells and the hue shows the type of operation
[CLICK] Our key takeaway from this experiment is off-the-shelf DRAM chips can perform 2, 4, 8, 16 input AND, NAND, OR, and NOR operations

## Slide 100: Available on arXiv
https://arxiv.org/pdf/2402.18736.pdf
Notes: The extended version of our study is available on arxiv

## Slide 101: FCDRAM is Open Source

## Slide 102: Functionally-Complete Boolean Logic in Real DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
Ismail Emir Yüksel
Yahya C. Tugrul Ataberk Olgun F. Nisa Bostancı
A. Giray Yaglıkçı Geraldo F. Oliveira Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Functionally-Complete Boolean Logic in Real DRAM Chips

## Slide 103: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 104: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: By leveraging simultaneous many-row activation, we can
[CLICK] Perform majority operations with more than three inputs
[CLICK] We can increase the robustness of majority operations
[CLICK] And we can copy one row’s content to multiple rows

## Slide 105: In-DRAM Majority-of-X (MAJX)
b
b
b
d
s
t
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
a
a
a
MAJ5(a, b, b, b, a) = b
MAJ7(a, b, b, a, a, b, b) = b
Simultaneously activate many rows to perform MAJX (where X>3) operations
b
b
b
b
b
b
b
b
b
a
a
a
a
a
a
a
a
a
b
b
b
b
b
b
Notes: Our key idea is to simultaneously activate many rows to perform MAJX operations where X is greater than 3
[CLICK] For example, if we can activate 5 rows at once
[CLICK] we can perform MAJ5 operations
[CLICK] Or if we simultaneously activate seven rows,
[CLICK] we can perform MAJ7

## Slide 106: MAJX in Real DRAM Chips
For MAJX, we need to activate X rows simultaneously
We can only simultaneously activate 2, 4, 8, 16, and 32 rows
Question
  How do we perform MAJX while simultaneously activating more than X rows?
Answer
  Making some rows neutral during the MAJX operation using the Frac operation*
b
b
a
b
b
a
b
b
a
b
b
a
N
N
N
3x Neutral Rows
=
MAJ5
w/ 5-row activation
MAJ5
w/ 8-row activation
*[Gao+MICRO’22]
Notes: So, let’s see how we can perform majority operations in real chips
[CLICK] For MAJX, we need to activate X rows simultaneously
[CLICK] However, we can simultaneously activate 2, 4, 8, 16, and 32 rows
[CLICK] The question is straightforward: How do we perform MAJX by simultaneously activating more than X rows? For example MAJ5 with 8-row activation
[CLICK] The answer is we prevent some rows from contributing to charge using the Frac operation, which is demonstrated in the prior work. Basically, these rows will be neutral rows, as if they are not activated
[CLICK] For example, MAJ5 with 5-row activation will be the same as MAJ5 with 8-row activation where three of these rows are neutral rows

## Slide 107: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: Now we are done with performing MAJX operations, let’s see how we can increase the robustness of these operations

## Slide 108: Improving the Robustness (Input Replication)
b
b
b
d
s
t
MAJ6(a, b, b, a, b, b) = b
MAJ3(a, b, b) = b
Storing multiple copies of MAJX input operands can increase the robustness of MAJX operations
a
b
b
d
s
t
d
s
t
d
s
t
d
s
t
b
a
a
a
b
b
b
b
b
b
b
b
a
a
a
b
b
b
Incorrect result
b
b
b
a
a
a
b
b
b
b
b
b
a
a
a
b
b
b
b
b
b
a
a
a
b
b
b
Correct result
Notes: Our key idea is to store multiple copies of majority operations’ input operands, which we call Input Replication
[CLICK] For example, we can increase the success rate of MAJ3 operation by activating 6 rows and replicating input operands two times

## Slide 109: Characterization Methodology
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Temperature (◦C): 50, 60, 70, 80, and 90
    Wordline Voltage (V): 2.5, 2.4, 2.3, 2.2, and 2.1
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
All rows in Subarray X
Row A
Row B
Temperature
50 ◦C
90 ◦C
Wordline Voltage
2.5V
2.1V
Notes: As we mentioned previously; we carefully sweep
[CLICK] Row Addresses and timing parameters
[CLICK] Temperature and wordline voltage

## Slide 110: Key Takeaways from MAJX Operation
COTS DRAM chips are capable of performing MAJ5, MAJ7, and MAJ9 operations
Key Takeaway 1
Storing multiple copies of MAJX’s input operands significantly increases the MAJX’s success rate
Key Takeaway 2
Voltage and temperature slightly affect the success rate, whereas data pattern affects significantly
Key Takeaway 3
Notes: Our analysis provides three key takeaway lessons:
[CLICK] First, off-the-shelf DRAM chips are capable of performing MAJ5, MAJ7, MAJ9 operations
[CLICK] Second, storing multiple copies of MAJX’s input operands significantly increases the MAJX’s success rate
[CLICK] Voltage and temperature slightly affects the success rate whereas data pattern affects significantly

## Slide 111: Robustness of MAJX Operations
COTS DRAM chips are capable of performing MAJ5, MAJ7, and MAJ9 operations
Notes: Now let me show you the first result the robustness of tested majority operations. In this figure, each subplot shows a different majority operation, from left to right the number of input operand in majority operation increases.
[CLICK] x-axis shows the number simultaneously activated rows
[CLICK] For this analysis, we will first focus on one data pattern: all ones or zeros
[CLICK] Let’s take look at the MAJ3 results where we use boxplot to show the success rate distributions
[CLICK] To simplify things, we focus on one distribution point that achieves highest success rate
[CLICK] From this figure we conclude that off-the-shelf DRAM chips are capable of performing up to nine-input majority operations

## Slide 112: Impact of Input Replication
Storing multiple copies of MAJ’s input operands increases the success rate of MAJ3, MAJ5, MAJ7, and MAJ9 operations
30.81% increase
Similar trend in success rate increase in all tested MAJX operations
56.27% increase
35.15% increase
13.11% increase
Final average success rate MAJ3 (MAJ5): 99.68% (93.49%)
Notes: Now let’s see how input replication affects the success rate
[CLICK] Again, here, let’s first focus on MAJ3 operation
[CLICK] We observe that when we increase the number of input operand copies in majority-of-three operation, we observe a drastic 30.81% increase in average success rate
[CLICK] And this increasing trend in success rate is consistent across all tested majority operations
[CLICK] Hence, we conclude that storing multiple copies of input operands increases the success rate of MAJ3, 5, 7, and 9 operations

## Slide 113: Leveraging Simultaneous Many-Row Activation
Perform MAJX (where X>3) operations
1
Increase the robustness of MAJX operations
2
Copy one row’s content to multiple rows
3
Notes: Next, I will show how we can copy one row’s content to multiple rows

## Slide 114: In-DRAM Multiple Row Copy (Multi-RowCopy)
d
s
t
r
c
s
Simultaneously activate many rows to copy one row’s content to multiple destination rows
d
s
t
s
r
c
RowClone
s
r
c
r
c
s
s
r
c
d
s
t
d
s
t
d
s
t
Multi-RowCopy
s
r
c
s
r
c
s
r
c
[Seshadri+ MICRO’13]
Notes: [CLICK] Our key idea is since we can activate many rows simultaneously, we can copy one row’s content to other simultaneously activated rows
[CLICK] Let’s recall the RowClone example where we copy source to destination
[CLICK] In RowClone, we first activate the source row which will copy its content to sense amplifiers
[CLICK] And then, we activate destination row to drive the sense amplifier’s content to destination row
[CLICK] In our mechanism, which we call Multi-RowCopy, we have several destination rows
[CLICK] Here we activate many destination rows simultaneously
[CLICK] and thus sense amplifier drives its content to these destination rows.

## Slide 115: Robustness of Multi-RowCopy
COTS DRAM chips can copy one row’s content to up to 31 rows with a very high success rate
Average: >99.98%
Notes: Now let me show you the first result
[CLICK] In this plot, y-axis shows the success rate
[CLICK] x-axis shows the number of destination rows from 1 to 31
[CLICK] And we plot the success rate distribution as a box-and-whiskers plot
[CLICK] We observe that the average success rate is higher than 99.98% across all tested number of destination rows
[CLICK] Hence, we conclude that off-the-shelf DRAM chips can copy one row’s content to up to 31 rows with a very high success rate

## Slide 116: Available on arXiv
https://arxiv.org/pdf/2405.06081
Notes: The extended version of our study is available on arxiv

## Slide 117: Our Work is Open Source and Artifact Evaluated
https://github.com/CMU-SAFARI/SiMRA-DRAM
Notes: And our work is artifact evaluated and got every badges
[CLICK] You can download our code from github and start testing right away!

## Slide 118: Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips Experimental Characterization and Analysis
Paper
GitHub
Juan Gómez–Luna Mohammad Sadr Onur Mutlu
İsmail Emir Yüksel
Yahya C. Tuğrul F. Nisa Bostancı Geraldo F. Oliveira
A. Giray Yağlıkçı Ataberk Olgun Melina Soysal Haocong Luo
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 119: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, PuDHammer [..]

## Slide 120: Executive Summary
Experimental Study: 316 COTS DDR4 chips from four major manufacturers to study read disturbance effects of multiple-row activation, which we call PuDHammer
PuDHammer significantly exacerbates DRAM read disturbance, causing up to 158.58x reduction in min. hammer count to induce first bitflip
PuDHammer bypasses in-DRAM RowHammer mitigation in DDR4 and induces 11340x more bitflips than RowHammer
Motivation: Processing-using-DRAM (PuD) alleviates data movement bottlenecks
DRAM can perform many PuD operations by activating multiple DRAM rows in quick succession or simultaneously (i.e., multiple-row activation)
Modern DRAM is subject to read disturbance (e.g., RowHammer)
    Repeatedly activating even a single row induces bitflips in unaccessed rows
Problem: No prior work studies the read disturbance effects of multiple-row activation
Goal: Understand and analyze read disturbance effects of multiple-row activation
Mitigation: We adapt Per Row Activation Counting (PRAC) for PuDHammer
Adapted PRAC solution incurs an average system performance overhead of 48.26%

## Slide 121: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-
Using-DRAM
…
…
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations
1. Consecutive Multiple-Row Activation (CoMRA)
2. Simultaneous Multiple-Row Activation (SiMRA)
Multiple-row activation is a key technique to realize many PuD operations
Notes: We categorize multiple-row activation into two categories
First, consecutive multiple-row activation, CoMRA
Second, simultaneous multiple-row activatio,, SiMRA
Now, let me dive deeper into these two and give their key ideas

## Slide 122: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
Violating timing of PRE command greatly in COTS DRAM chips activates two rows consecutively
Notes: However, if we violate the timing between PRE and ACT dst
[CLICK] We can activate destination row without deactivating sense amplifier and keeping the bitlines at source voltage level
[CLICK] As a result of this, we can perform in-dram row copy operation: source row can be copied to destination row

## Slide 123: Simultaneous Multiple-Row Activation
Activating two rows in quick succession
in COTS DRAM chips simultaneously activates multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Now let’s see how SiMRA works
[CLICK] The key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] In this pictorial example Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we can activate many rows at once in the same subarray

## Slide 124: Read Disturbance in DRAM
Unfortunately, even activating a single DRAM row disturbs the data integrity of other unaccessed DRAM rows
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
DRAM Subarray
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
[Kim+, ISCA’14]
Notes: Read disturbance bitflips have significant system-level implications because they break memory isolation.
[CLICK] Even activating a single DRAM row disturbs the data integrity of ther unaccessed DRAM rows.
[CLICK] A prominent example of read disturbance is RowHammer.
[CLICKx9] Repeatedly activating and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
We call the repeatedly activated row the aggressor row and the rows that have bitflips victim rows.

## Slide 125: Problem & Goal
Problem
No prior work investigates the read disturbance effects of multiple-row activation
Goal
Understand how multiple-row activation affects read disturbance vulnerability in DRAM

## Slide 126: DRAM Chips Tested
316 DDR4 chips from four major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK] We test 316 DDR4 chips from four major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 127: Hammering with CoMRA
DRAM Subarray
.
.
.
.
.
.
Double-Sided
Single-Sided
.
.
.
DRAM Subarray
src
dst
dst
src
ACT src
ACT dst
PRE
7.5ns
36ns
victim
victim
victim
victim
victim
aggressor
aggressor
aggressor
aggressor
Notes: To hammer using CoMRA access pattern, we use two versions of hammering:
[CLICK] First, double-sided where we sandwich a victim row
[CLICK] We adapt CoMRA to perform copy operation to sandwich a victim row for double-sided
[CLICK] Second, single-sided where a single aggressor row disturbs its neighboring victim rows
[CLICK] To perform single-sided CoMRA, we perform the copy operation between two rows that are far away from each other

## Slide 128: Read Disturbance Vulnerability Metric: HCfirst
The minimum hammer count required to induce the first bitflip
Lower is worse
Record bitflips in victim
Victim Row
Aggressor Row (src)
Aggressor Row (dst)
1 Hammer
ACT src
ACT dst
PRE
PRE
Notes: To evaluate the read disturbance vulnerability of DRAM chips, we use widely-adopted metric called Hcfirst
[CLICK] which is the minimum hammer count required to induce the first bitflip and lower the Hcfirst worse the read disturbance is
[CLICK] Here we have a double sided scenario where we sandwich a victim row
[CLICK] We count one CoMRa operation, ACT-PRE-ACT as 1 Hammer and we record bitflips in victim

## Slide 129: Double-Sided CoMRA vs. RowHammer (I)
13.98x
Double-sided CoMRA decreases lowest HCfirst by 13.98x compared to double-sided RowHammer
Lowest HCfirst reduction trend consistent across all four manufacturer
1.18x
3.28x
1.58x

## Slide 130: Double-Sided CoMRA vs. RowHammer (II)
Represents 99% of tested victim rows
Represents 50% of tested victim rows
HCfirst reduction of 50%
RowHammer HCfirst = 100
CoMRA HCfirst = 50
DRAM Rows (sorted by reducing HCfirst changes)
CoMRA reduces HCfirst
Notes: In this experiment,
[CLICK]
we investigate how much Hcfirst changes when we perform CoMRA compared to RowHammer
[CLICK] across all the tested DRAM rows sorted by reducing Hcfirst changes value on the x-axis.
[CLICK] Each curve in this plot represents a different DRAM vendor
Now let me walk through what this plot represents
[CLICK] X-axis from P1 to P100 shows 99% of the tested rows
[CLICK] Similarly, from P50 to P100 represents 50% of the tested rows
[CLICK] Hcfirst change of -50 means Hcfirst reduction of 50%
For example, a victim row has Hcfirst of 100 for RowHammer while having 50 for CoMRA

## Slide 131: Double-Sided CoMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
Double-sided CoMRA decreases HCfirst for a large fraction of rows compared to double-sided RowHammer

## Slide 132: Recall: SiMRA
Activating two rows in quick succession
in COTS DRAM chips simultaneously activates multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] You may remember this pictorial example where Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate many rows at once in the same subarray

## Slide 133: Double-Sided SiMRA vs. RowHammer (I)
159x
Double-sided SiMRA decreases lowest HCfirst by 159x compared to double-sided RowHammer
51x
86x
125x
Lowest HCfirst reduction trend consistent across all tested number of simultaneously activated rows
Min. hammer count to induce first bitflip
#Simultaneously Activated Rows

## Slide 134: Double-Sided SiMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
at least 25.19% of tested victim rows experience >99% HCfirst reduction

## Slide 135: Double-Sided SiMRA vs. RowHammer (II)
Double-sided SiMRA significantly decreases HCfirst for a majority of rows compared to double-sided RowHammer

## Slide 136: Mitigating PuDHammer
2
Adapt RowHammer mitigations to account for PuDHammer
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 137: Mitigating PuDHammer
2
Adapt RowHammer mitigations to account for PuDHammer
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 138: Target Row Refresh (TRR)
Row 0
Row 1
Row 2
Row 3
Row 4
TRR-equipped DRAM Chip
TRR
Memory Controller
DRAM vendors equip their DRAM chips with a proprietary mitigation mechanisms known as Target Row Refresh (TRR)
Aggressor detected: Row 2
Refresh neighbor rows
TRR-induced refreshes
Key Idea: TRR refreshes nearby rows upon detecting an aggressor row
REF
aggressor
Notes: To protect their DRAM chips against RowHammer, DRAM vendors currently implement proprietary RowHammer mitigation mechanisms typically called Target Row Refresh or (TRR)
[CLICK] The key idea of TRR is to refresh nearby rows upon detecting an aggressor row
[CLICK] We demonstrate how TRR operates at a high-level.
[CLICK] The TRR mechanism detects [CLICK] an aggressor row as a result of [CLICK] repeatedly activating and precharging the same row. [CLICK]
[CLICK] To protect the neighbor victim rows from experiencing RowHammer bit flips, [CLICK] TRR refreshes the victim rows by performing TRR-induced refresh operations. TRR refreshes victim rows by piggybacking TRR-induced refreshes to the REFRESH commands that the memory controller periodically issues.

## Slide 139: Real DRAM Chip Results
>10K bitflips
<60 bitflips
>10K bitflips
~60 bitflips
CoMRA induces 1.10x more bitflips than RowHammer on average in the presence of TRR

## Slide 140: Real DRAM Chip Results
>10K bitflips
<60 bitflips
~240K bitflips
~180K bitflips
SiMRA induces 11340x more bitflips than RowHammer on average in the presence of TRR

## Slide 141: Mitigating PuDHammer
2
Adapt RowHammer mitigations to account for PuDHammer
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 142: Adapting PRAC for PuDHammer
A Naïve Approach (PRAC-Naïve)
Reducing RowHammer threshold to SiMRA’s lowest observed HCfirst
Weighted Counting (PRAC-WC)
Increase counters based on the vulnerability caused by the operation (RH, CoMRA, and SiMRA)

## Slide 143: Methodology
Environment: Cycle-level DRAM simulator Ramulator2 [Kim+ CAL'15, Luo+ CAL'23]
System Configuration:
  Processor 4-core, out-of-order, 4.2GHz clock frequency
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 128K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4
  PRAC 4 RFMs per Back-off
  PIM Unit 1-core, issues CoMRA & SiMRA operations with a fixed invertal
Workloads:
    60 five-core multiprogrammed workload mixes.
    Each mix is composed of
      four workloads from five major benchmark suites and
      one synthetic workload that periodically performs back-to-back one SiMRA with 32-row activation and one CoMRA operation

## Slide 144: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-Naïve
PRAC-WC
DRAM performs PuD operations in every 125ns
Normalized to no RH mitigation

## Slide 145: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-WC greatly outperforms PRAC-Naïve until 2us
PRAC-WC incurs an average (maximum) performance overhead of 48.26% (98.83%)

## Slide 146: More in the Paper
More characterization results
    Temperature, spatial variation, timing parameters, access pattern, data pattern, aggressor row on time analyses for CoMRA and SiMRA
    Combined Read Disturbance Effect of RowHammer with PuD
      Combined pattern is more effective than RowHammer alone (e.g., 1.66x reduction in HCfirst on average)
Details and analyses on mitigating PuDHammer
    Discussion on how modifying DRAM chips could help mitigating PuDHammer
    More details on PRAC adaptation
      Challenges on adapting for PuDHammer
      An area-efficient PRAC solution
      ..
Notes: We have more content in the paper, including
…

## Slide 147: Available on arXiv
https://arxiv.org/pdf/2506.12947
Notes: The extended version of our study is available on arxiv

## Slide 148: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 149: 7th Workshop on Memory-Centric Computing Processing-Using-Memory in Real DRAM Chips
İsmail Emir Yüksel
ICS 2026
6 July 2026