## Slide 1
PyGim: An Efficient Graph Neural Network Library for Real Processing-In-Memory Architectures
Christina Giannoula, Peiming Yang, Ivan Fernandez, Jiacheng Yang, Sankeerth Durvasula, Yu Xin Li, Mohammad Sadrosadati, Juan Gomez Luna, Onur Mutlu, Gennady Pekhimenko

## Slide 2
Key Results: PyGim improves (i) performance and energy efficiency by 3.7× and 2.3× over state-of-the-art schemes, and (ii) core utilization on PIM system by 11.6× over PyTorch on GPUs
Executive Summary
Problem: The memory-intensive kernels of Graph Neural Networks (GNNs) dominate execution time (~91%) and are significantly bottlenecked by memory bandwidth in procesor-centric systems (CPUs/GPUs)
PyGim: An efficient and easy-to-use GNN library for real Processing-In-Memory (PIM) systems
Key Ideas & Benefits:
Cost Effectiveness: Heteregenous GNN kernels are executed in the best-fit hardware
High Performance: (i) Enabling three levels of parallelism with various strategies in the PIM side and (ii) adapting best-performing parallelization strategy to the graph’s unique characteristics
High Programming Ease: (i) Providing a handy Python API and (ii) automatically tuning the best-fit parallelization strategy without programmer intervention
github.com/CMU-SAFARI/PyGim
Motivation: PIM provide significantly high memory bandwidth by enabling computation to be performed close to the application data

## Slide 3
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 4
GNNs Are Widely Used in Real-World Applications
GNNs are state-of-the-art ML models for analyzing graph-structure data
GNN has a lot of applications:
Drug Discovery
Recommendation Systems
Fraud Detection

## Slide 5
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Each GNN layer has two execution steps:
1
2
5
4
6
Adjacency (Sparse) Matrix
Input Feature
Notes: Full matrix of results.

## Slide 6
Input Feature
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Each GNN layer has two execution steps:
Input Feature
1
2
5
4
6
Adjacency (Sparse) Matrix
1
2
5
4
6
Notes: Full matrix of results.

## Slide 7
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Each GNN layer has two execution steps:
1
2
5
4
6
Adjacency (Sparse) Matrix
Input Feature
1
2
5
4
6
1
2
5
4
6
Output Feature
Aggregation Result
Neural Network (NN)
Notes: Full matrix of results.

## Slide 8
Execution Steps of GNN Layers
GNNs comprise a few layers (e.g., 3-5 layers)
Each GNN layer has two execution steps:
Aggregation
Combination
Aggregate neighbor’s feature, corresponds to Sparse Matrix Matrix Multiplication (SpMM)
Combine features by NN. Typically comprises compute-intensive kernels (e.g., GEMMs)
1
2
5
4
6
Adjacency (Sparse) Matrix
Input Feature
Neural Network (NN)
1
2
5
4
6
1
2
5
4
6
Output Feature
Aggregation Result
Notes: sparse V V mul

## Slide 9
GNN Aggregation Is Memory-Bandwidth-Bound In GPUs
Using a RTX 3090 GPU with ~900 GB/s bandwidth, we find that GNN Aggregation
takes ~91% of the inference time
achieves less than 2% core utilization
Roofline Analysis
Bandwidth-Bound

## Slide 10
PIM Alleviates The Data Movement Bottleneck
Near-bank PIM: each PIM core is tightly coupled with one (or a few) DRAM banks
Near-bank PIM cores have significantly higher memory bandwidth than Host cores
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
PIM Provides A Promising Solution for GNN Aggregation
Notes: - Here I changed the title of the slide!
- Here you need to animate a banner: I added a draft banner please fix the text

## Slide 11
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 12
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Run heterogeneous kernels in the best-fit hardware
Strives a balance between computation and data transfer
Automatically tunes the best-performing PaF strategy
Integrates a handy Python (PyTorch) API
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Strives a balance between computation and data transfer
Automatically tunes the best-performing PaF strategy
Integrates a handy Python (PyTorch) API

## Slide 13
1. Cooperative Acceleration (CoA)
Heterogeneous kernels are running in the best-fit underlying hardware
Combination runs on Host cores
Aggregation runs on PIM cores
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
GNN Combination

## Slide 14
Challenge 1: Expensive Data Transfer Costs
Alleviate the overheads of passing the output data of the one step as input data to the next step
A Near-Bank PIM System
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host Processor
(e.g., CPU/GPU)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
PIM-Enabled Memory
Standard Memory Modules
Bus
GNN Aggregation
GNN Combination
data

## Slide 15
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
challenge
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)

## Slide 16
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
challenge
solution

## Slide 17
2. Parallelism Fusion (PaF)
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
Within PIM Cluster
PIM Core
Threads
Within PIM Core
Reduces data transfer costs
Reduce computation costs
Notes: - This slide is a bit crowded and dense. Probably if we make the images a bit smaller it might look better

## Slide 18
An Aggregation Example
E.g., a graph with 8 vertices and 14 edges
  SPMM is used for aggregation
1
2
3
4
5
8
6
7
SPMM
Adjacency (Sparse) Matrix
Input Feature Matrix
Aggregation Results
1
2
3
4
5
8
6
7
Notes: This is an example of aggregation, …..

## Slide 19
2.1 PaF Parallelism Across PIM Clusters
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Across PIM Clusters
PIM Core
Threads
Notes: - This slide is a bit crowded and dense. Probably if we make the images a bit smaller it might look better

## Slide 20
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
1
2
3
4
5
8
6
7
Edge-level partition
Clusters 1,2
Clusters 3,4
Clusters 1,2
Clusters 3,4
Notes: 4 features for each cluster
Add host core merge
Show “cluster” under graph in next click

## Slide 21
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
1
2
3
4
5
8
6
7
Clusters 1,2
1
2
3
4
5
8
6
7
Clusters 3,4
Edge-level partition
Feature-level partition
Clusters 1,2
Clusters 3,4
Cluster
1
Cluster
3
Cluster
4
Cluster
2
Clusters 1,2
Clusters 3,4
Notes: 4 features for each cluster
Add host core merge
Show “cluster” under graph in next click

## Slide 22
Across PIM Clusters: Edge- & Feature-Level Parallelism
E.g., creating 4 PIM clusters with 2 Edge partitions and 2 Feature partitions
Adjacency (Sparse) Matrix
Input Feature Matrix
Partial Results for Output
Cluster 1
Cluster 3
Cluster 2
Cluster 4
1
2
3
4
5
8
6
7
Cluster 1
1
2
3
4
5
8
6
7
Cluster 2
1
2
3
4
5
8
6
7
Cluster 3
1
2
3
4
5
8
6
7
Cluster 4
Edge-level partition
Feature-level partition
Clusters 1,2
Clusters 3,4
Cluster
1
Cluster
3
Cluster
4
Cluster
2
Merged by Host cores
Notes: 4 features for each cluster
Add host core merge
Show “cluster” under graph in next click

## Slide 23
2.2 PaF Parallelism Within PIM Cluster
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
Within PIM Cluster
PIM Core
Threads
Notes: Title, another color
- This slide is a bit crowded and dense. Probably if we make the images a bit smaller it might look better

## Slide 24
Within a PIM Cluster: Vertex- or Edge-Level Parallelism
E.g., balancing vertices or balancing edges across PIM cores within the cluster
Adjacency (Sparse) Matrix
Core 1
Balance Vertices Across PIM Cores
Balance Edges Across PIM Cores
Adjacency (Sparse) Matrix
Core 2
Core 1
Core 2
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1 has 2 PIM Cores
Cluster 2

## Slide 25
2.3 PaF Parallelism Within PIM Core
PaF (i) strives a balance between computation and data transfer costs and
(ii) covers various graphs with diverse characteristics
PaF enables 3 levels of parallelism:
  Across PIM Clusters: Edge- and Feature-level parallelism
  Within PIM Cluster: Vertex- or Edge-level parallelism
  Within PIM Core: Vertex- or Edge-level parallelism
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Cluster 1
Cluster 2
Cluster 3
Cluster 4
PIM Core
Threads
Within PIM Core
Notes: Titile
- This slide is a bit crowded and dense. Probably if we make the images a bit smaller it might look better

## Slide 26
Within a PIM Core: Vertex- or Edge-Level Parallelism
E.g., balancing vertices or balancing edges across threads within a PIM core
Adjacency (Sparse) Matrix
Thread 1
Balance Vertices Across Threads
Balance Edges Across Threads
Adjacency (Sparse) Matrix
PIM Core
Threads
PIM Core supports 4 threads
Thread 2
Thread 3
Thread 4
Thread 1
Thread 2
Thread 3
Thread 4
Synchronization is implement
with lock-free or fine-grained locking schemes

## Slide 27
PaF supports a wide variety of parallelization strategies:
  Typically there is no one-size-fits-all solution
Challenge = manually tuning the parallelization strategy poses significant burdens for developers
  Unique graph's characteristics need different tuning
Challenge 2: Programmability in Real-World Graphs
Real-world graphs exhibit diverse characteristics
regular graph
power-law graph
diagonal graph
Notes: - Real-world graphs exhibit diverse characteristics, e.g., the average, min or max vertex neighboring degrees vary across different graphs. Therefore, as discussed in prior works [39, 62, 77, 122, 138], the execution behavior of sparse kernels, such as the SpMV/SpMM, depends on the particular characteristics of the input given, and there is no typically one-size-fits-all parallelization solution that performs best across various inputs
- Programming a real near-bank PIM system is hard task. manually tuning the best-performing parallelization strategy for each unique graph's characteristics poses significant challenges for developers

## Slide 28
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
Programmability in
Real-World Graphs
challenge

## Slide 29
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface
Expensive Data Transfer Costs
Programmability in
Real-World Graphs
challenge
solution

## Slide 30
PyGim Tuner predicts the best-performing PaF strategy without manual programmer intervention
  Hardware profiler generate a group of performance measurements
  Performance predictor predict the execution of potential PaF strategy
  PaF selector apply the best-performing PaF strategy
3. Lightweight Tuning
PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Real PIM System
Real-world Graph
Best-performing
PaF Strategy
Tunes
PyGim Tuner
PaF Selector
Performance Predictor
Host->PIM
PIM->Host
PIM Kernel
Host Kernel
Hardware Profiler
PaF Generator
Notes:   Graph’s characteristics (i.e., non-zero patterns)
  PIM system’s characteristics (i.e., compute capabilities, available memory bandwidth…)

## Slide 31
PyGim Overview
An efficient and easy-to-use GNN library for real PIM systems
PyGim incorporates 4 key components:
Cooperative Acceleration (CoA)
Parallelism Fusion (PaF)
Lightweight Tuning
Handy Programming Interface

## Slide 32
PyGim integrates a handy Python API (currently integrated with PyTorch)
4. Handy Programming Interface
import torch, pygim as gyn
class GCNConv(torch.nn.Module):
def __init__(self, hidden_size):
self.linear = torch.nn.Linear(feature_size, features_size)
def forward(self, graph_pim, in_dense):
# Execute memory-intensive operator in PIM devices
dense_parts = col_split(in_dense)
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute compute-intensive operator in Host (e.g., CPU/GPU)
out = self.linear(out_dense)
return out
gyn.pim_init_devices(num_pim_devices) # Initialize PIM devices
data = load_dataset() # Load graph
# Tune the PaF strategy
graph_parts, config = gyn.tune(data.graph, feature_size, device_info)
graph_pim = gyn.load_graph_pim(graph_parts) # Partition graph to PIM
# Create GNN model
model = torch.nn.Sequential([Linear(in_channels, feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
model.forward(graph_pim, data.features) # GCN inference
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
# Create GNN model model=torch.nn.Sequential([Linear(in_channels,feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
import … pygim as gyn
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute memory-intensive kernel in real PIM devices
graph_pim= gyn.tune(data.graph, feature_size, device_info)
# Tune the PaF strategy

## Slide 33
Deploy Your GNNs Effortlessly with PyGim and Enjoy the PIM Benefits!
import torch, pygim as gyn
class GCNConv(torch.nn.Module):
def __init__(self, hidden_size):
self.linear = torch.nn.Linear(feature_size, features_size)
def forward(self, graph_pim, in_dense):
# Execute memory-intensive operator in PIM devices
dense_parts = col_split(in_dense)
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute compute-intensive operator in Host (e.g., CPU/GPU)
out = self.linear(out_dense)
return out
gyn.pim_init_devices(num_pim_devices) # Initialize PIM devices
data = load_dataset() # Load graph
# Tune the PaF strategy
graph_parts, config = gyn.tune(data.graph, feature_size, device_info)
graph_pim = gyn.load_graph_pim(graph_parts) # Partition graph to PIM
# Create GNN model
model = torch.nn.Sequential([Linear(in_channels, feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
model.forward(graph_pim, data.features) # GCN inference
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
# Create GNN model model=torch.nn.Sequential([Linear(in_channels,feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
GCNConv(feature_size),
Linear(feature_size, out_channels)])
import … pygim as gyn
out_dense = gyn.pim_run_aggr(graph_pim, dense_parts)
# Execute memory-intensive kernel in real PIM devices
graph_pim= gyn.tune(data.graph, feature_size, device_info)
# Tune the PaF strategy
UPMEM PIM
fast-forwarded
Memory
small cores
Computation is performed inside real PIM devices!

## Slide 34
Talk Outline
Background & Motivation
PyGim Design
Evaluation

## Slide 35
Evaluation Methodology
UPMEM PIM server: 16 PIM DIMMs with 1992 PIM Cores (24 threads per core) in total
GNN models: GCN, GIN, SAGE
Datasets: OGBN-Proteins, Reddit, AmazonProducts
Comparison points:
  PyTorch running on host CPU
  SparseP [Sigmetrics’22] (2×) running SpMM as multiple SpMV kernels on PIM cores
  GraNDe [IEEE Trans. Comput.’23]: optimizes GNN aggregation on near-rank PIM systems
UPMEM PIM System
PIM-Enabled Memory
PIM-Enabled Memory
124 GB PIM-Enabled Memory
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
DRAM Bank
PIM Core
Host CPU (2-socket Intel Xeon)
Host Cores
Shared Cache
Bus
PIM-Enabled Memory
PIM-Enabled Memory
128 GB Main Memory
Bus

## Slide 36
Performance Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SparseP1 | 1.104 | 1.3051 | 1.2104 | 1.3998 | 1.347 | 1.341 | 1.143 | 1.1836 | 1.217
SparseP2 | 1.0987 | 1.2522 | 1.1822 | 1.3804 | 1.319 | 1.2894 | 1.1353 | 1.162 | 1.1845
GraNDe | 0.47434 | 0.53453 | 0.50797 | 0.56132 | 0.51479 | 0.52287 | 0.40931 | 0.4062 | 0.42852
PyGim_CSR | 2.7667 | 3.2756 | 3.0324 | 3.3892 | 3.4308 | 3.3225 | 2.6124 | 2.8215 | 2.9016
PyGim_COO | 2.6776 | 3.3551 | 3.0108 | 3.4015 | 3.4393 | 3.3107 | 2.6037 | 2.8016 | 2.6584
ogbn-proteins
reddit
amazonProducts

## Slide 37
Performance Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SparseP1 | 1.104 | 1.3051 | 1.2104 | 1.3998 | 1.347 | 1.341 | 1.143 | 1.1836 | 1.217
SparseP2 | 1.0987 | 1.2522 | 1.1822 | 1.3804 | 1.319 | 1.2894 | 1.1353 | 1.162 | 1.1845
GraNDe | 0.47434 | 0.53453 | 0.50797 | 0.56132 | 0.51479 | 0.52287 | 0.40931 | 0.4062 | 0.42852
PyGim_CSR | 2.7667 | 3.2756 | 3.0324 | 3.3892 | 3.4308 | 3.3225 | 2.6124 | 2.8215 | 2.9016
PyGim_COO | 2.6776 | 3.3551 | 3.0108 | 3.4015 | 3.4393 | 3.3107 | 2.6037 | 2.8016 | 2.6584
ogbn-proteins
reddit
amazonProducts
PyGim significantly outperforms PyTorch (CPU) and prior PIM-based schemes by 3.1× and 4.4× respectively

## Slide 38
Energy Efficiency Evaluation in GNN Inference
Chart: INT32
| GIN | GCN | SAGE | GIN | GCN | SAGE | GIN | GCN | SAGE
PyTorch (CPU) | 2564.2726 | 2587.1552 | 2442.4522 | 4433.7424 | 4279.762 | 4359.3713 | 5852.4966 | 5620.9367 | 5704.5425
SparseP1 | 4946.4061 | 4897.4054 | 4944.507 | 7214.2204 | 7086.3536 | 7154.5176 | 10135.5761 | 9977.7677 | 10039.4813
SparseP2 | 4487.6501 | 4451.2338 | 4496.3087 | 6478.7246 | 6381.0069 | 6422.2122 | 9143.2736 | 9046.1845 | 9065.546
GraNDe | 6149.8183 | 5918.9864 | 6105.7194 | 8200.6406 | 7889.4481 | 7882.9551 | 13149.1481 | 13064.0146 | 13328.4552
PyGim_CSR | 1856.5666 | 1765.8154 | 1798.3173 | 2555.2897 | 2450.003 | 2473.5083 | 3737.752 | 3570.6333 | 3628.2915
PyGim_COO | 1912.043 | 1882.2876 | 1899.8371 | 2572.9546 | 2496.2467 | 2576.2211 | 3735.719 | 3580.2291 | 3671.5764
ogbn-proteins
reddit
amazonProducts
PyGim improves energy efficiency by 2.7× and 3.3× compared to PyTorch (CPU) and prior PIM-based schemes respectively

## Slide 39
Characteristics of CPU, PIM and GPU Systems
System | INT32 Peak Performance | FP32 Peak Performance | Total Bandwidth | Technology Node
CPU Xeon 4215 | 0.64 TOPS | 1.28 TFLOPS | 23.1 GB/s | 14nm
UPMEM PIM | 0.12 TOPS | 0.025 TFLOPS | 1390 GB/s | at least 20nm
GPU GTX 1080 Ti | 13.25 TOPS | 13.25 TFLOPS | 359.9 GB/s | 16nm
GPU RTX 2080 Ti | 16.94 TOPS | 16.94 TFLOPS | 558.1 GB/s | 12nm
GPU RTX 3090 | 17.79 TOPS | 35.58 TFLOPS | 936.2 GB/s | 8nm
Across last GPU generations:
memory bandwidth has tripled (~3×)
(last two generations) compute throughput has been doubled (~2×)

## Slide 40
Core Utilization in GNN Aggregation
Dataset & data type/ Software library | Reddit INT32 | Reddit FP32
Intel MKL (CPU Intel Xeon 4215) | 0.63% | 0.22%
CUDA (GPU GTX 1080 Ti) | 0.62% | 0.62%
CUDA (GPU RTX 2080 Ti) | 0.68% | 0.67%
CUDA (GPU RTX 3090) | 1.56% | 0.78%
PyGim (UPMEM PIM) | 13.86% | 9.13%
Core utilization in GNN aggregation remains similarly low across GPU generations
PyGim running on a real PIM system achieves
significantly higher core utilization(11.6x on average) than the PyTorch on GPUs
Notes: (at least a 5× increase)

## Slide 41
More in the Paper
Analysis within a PIM core
Analysis within a PIM cluster
Analysis across PIM clusters
PyGim tuning efficiency
Scalability analysis
Analysis on different data types
Analysis on different compression formats
Performance evaluation in GNN training
Recommendations
https://arxiv.org/pdf/2402.16731

## Slide 42
Conclusion
We present PyGim, a handy ML library that significantly improves performance, energy efficiency and cost effectiveness in GNNs through real PIM devices
Key Ideas & Benefits:
balances computation and data transfer costs via configurable parallelization strategies for diverse real-world graphs
automatically tunes the best-fit strategy without programmer intervention
Key Results:
performance and energy efficiency by 3.7× and 2.3× over SOTA schemes
core utilization on PIM system by 11.6× over PyTorch on GPUs
PyGim

## Slide 43
PyGim: An Efficient Graph Neural Network Library for Real Processing-In-Memory Architectures
Christina Giannoula, Peiming Yang, Ivan Fernandez, Jiacheng Yang, Sankeerth Durvasula, Yu Xin Li, Mohammad Sadrosadati, Juan Gomez Luna, Onur Mutlu, Gennady Pekhimenko