## Slide 1: QUAC-TRNG High-Throughput True Random Number Generation Using Quadruple Row Activation in Real DRAM Chips
Ataberk Olgun
Minesh Patel A. Giray Yağlıkçı Haocong Luo
Jeremie S. Kim F. Nisa Bostancı Nandita Vijaykumar
Oğuz Ergin Onur Mutlu

## Slide 2: Executive Summary
Motivation: DRAM-based true random number generators (TRNGs) provide true random numbers at low cost on a wide range of computing systems
Problem: Prior DRAM-based TRNGs are slow:
Based on fundamentally slow processes  high latency
Cannot effectively harness entropy from DRAM rows  low throughput
Goal: Develop a high-throughput and low-latency TRNG that uses commodity DRAM devices
Key Observation: Carefully engineered sequence of DRAM commands can activate four DRAM rows  QUadruple ACtivation (QUAC)
Key Idea: Use QUAC to activate DRAM rows that are initialized with conflicting data (e.g., two ‘1’s and two ‘0’s) to generate random values
QUAC-TRNG: DRAM-based TRNG that generates true random numbers at high-throughput and low-latency by repeatedly performing QUAC operations
Results: We evaluate QUAC-TRNG using 136 real DDR4 chips
5.4 Gb/s maximum (3.4 Gb/s average) TRNG throughput per DRAM channel
Outperforms existing DRAM-based TRNGs by 15.08x (base), and 1.41x (enhanced)
Low TRNG latency: 256-bit RN in 274 ns
Passes all 15 NIST randomness tests

## Slide 3: Outline
True Random Numbers in DRAM
DRAM Organization and Operation
QUadruple ACtivation (QUAC)
QUAC-TRNG
Evaluation

## Slide 4: Use Cases of True Random Numbers
High-quality true random numbers are critical to many applications
True random numbers can only be obtained by sampling random physical processes
Unfortunately, not all computing systems are equipped with TRNG hardware (e.g., dedicated circuitry)

## Slide 5: DRAM-Based TRNGs
DRAM chips are ubiquitous in modern computing platforms
DRAM-based TRNGs enable true random number generation within DRAM chips
Low-cost: No specialized circuitry for RNG
  Beneficial for constrained systems
High-throughput: > Gb/s throughput
  Open application space that require high-throughput TRNG

## Slide 6: Synergy with Processing-in-Memory
Processing-in-Memory (PIM) Systems
Perform computation directly within a memory chip
Improve system performance by avoiding off-chip data movement
True random number generation within DRAM
Enables PIM workloads to sample true random numbers directly within the memory chip
Avoids inefficient communication to other possible off-chip TRNG sources, enhances security & privacy
[UPMEM]
[Samsung]

## Slide 7: Outline
True Random Numbers in DRAM
DRAM Organization and Operation
QUadruple ACtivation (QUAC)
QUAC-TRNG
Evaluation

## Slide 8: DRAM Organization
…
…
…

## Slide 9: Accessing a DRAM Cell
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline
[Seshadri+ MICRO’17]

## Slide 10: Accessing a DRAM Cell
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
½ VDD
VDD
enable wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell charge restored
Sense Amp
deviation in bitline voltage
½ VDD
0
bitline
[Seshadri+ MICRO’17]
1
2
3
4
5
6

## Slide 11: DRAM Operation
…
…
…
…
…
Sense Amplifiers
Sense Amplifiers
Cache line
READ
…
READ
READ
Wordline Drivers
Sense Amplifiers
READ
READ
READ
ACT R0
RD
PRE R0
RD
RD
ACT R1
RD
RD
RD
time
DRAM Command Sequence
tRAS (Activation Latency)
tRP (Precharge Latency)
[Kim+ HPCA’19]

## Slide 12: Outline
True Random Numbers in DRAM
DRAM Organization and Operation
QUadruple ACtivation (QUAC)
QUAC-TRNG
Evaluation

## Slide 13: Quadruple Activation (QUAC)
New Observation
Carefully-engineered DRAM commands can activate four rows in real DRAM chips
Activate four rows with two ACT commands
ACT
PRE
ACT
<3ns
<3ns
35ns
14ns
Violated
Default

## Slide 14: Quadruple Activation (QUAC)
Characteristic 1
Activates a set of four DRAM rows whose addresses differ only in their two LSBs

## Slide 15: Quadruple Activation (QUAC)
Characteristic 2
First and second ACT’s addresses must have their two LSBs inverted
ACT 000
PRE
ACT 011
ACT 010
PRE
ACT 001
1
2
1
2

## Slide 16: QUAC on Real DRAM Chips
Valid QUAC behavior on 136 DDR4 chips

## Slide 17: Why Does QUAC Work?
Hypothetical circuit to explain QUAC
Hierarchical Wordlines
High density and performance requirements
Hierarchical organization of DRAM wordlines enable high-density and low-latency DRAM operation

## Slide 18: Hierarchical Wordlines
A master wordline drives multiple local wordlines
…
…
…

## Slide 19: Hierarchical Wordlines
A master wordline drives multiple local wordlines
Select signals for rows 0-3

## Slide 20: Hypothetical Row Decoder
L
L
L
L
Address [0]
Address [1]
Latch
A0
A0
A1
A1
Predecode the least significant two bits
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Drive control signals

## Slide 21: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
0
0
First ACT command drives a single wordline

## Slide 22: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
0
0
PRE
Violate Timing
PRE command cannot disable latches

## Slide 23: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
0
0
PRE
Violate Timing
Violate Timing
ACT R3
1
1
Second ACT drives the remaining three wordlines

## Slide 24: Hypothetical Row Decoder
L
L
L
L
A0
A0
A1
A1
A0
A1
A0
A1
A0
A1
A1
A0
S0
S1
S2
S3
Command
ACT R0
PRE
Violate Timing
Violate Timing
ACT R3
1
1
Second ACT drives the remaining three wordlines
All four wordlines are enabled
Quadruple Activation

## Slide 25: Outline
True Random Numbers in DRAM
DRAM Organization and Operation
QUadruple ACtivation (QUAC)
QUAC-TRNG
Evaluation

## Slide 26: Generating Random Values via QUAC
Vdd
-Vdd
Voltage Difference
Time
Ready to Sense
Voltage Level
VTH
-VTH
0
Sense Amplifier
VDD/2
VDD/2
Enable
Logic-1
R0
R1
R2
R3

## Slide 27: Generating Random Values via QUAC
Vdd
-Vdd
VDD/2
VDD/2
Enable
ACT R0
PRE
ACT R3
+
Voltage Difference
VTH
-VTH
0
Time
R0
R1
R2
R3
Sense Amplifier

## Slide 28: Generating Random Values via QUAC
Vdd
-Vdd
Voltage Difference
Time
VTH
-VTH
0
VDD/2
VDD/2
Enable
ACT R0
PRE
ACT R3
+
Enable Sense Amplifiers
Sense Amplifier
R0
R1
R2
R3
Random perturbation

## Slide 29: QUAC-TRNG
Key Idea: Leverage random values on sense amplifiers generated by QUAC operations as source of entropy
R0
R1
R2
R3
DRAM Segment
Step 1 Initialize
Step 2 QUAC
Sense Amplifiers
Random Values
Logic-1
Logic-0

## Slide 30: QUAC-TRNG
Key Idea: Leverage random values on sense amplifiers generated by QUAC operations as source of entropy
Step 1 Initialize
Step 2 QUAC
Sense Amplifiers
Step 3 Read
SHA-256
Memory Controller
256-bit Shannon Entropy Blocks
Step 4 Post-process
256-bit TRN

## Slide 31: QUAC-TRNG
Key Idea: Leverage random values on sense amplifiers generated by QUAC operations as source of entropy
Step 1 Initialize
Step 2 QUAC
Sense Amplifiers
Step 3 Read
SHA-256
Memory Controller
Step 4 Post-process
256-bit TRN
Generates a 256-bit random number for every 256-bit Shannon Entropy block

## Slide 32: Outline
True Random Numbers in DRAM
DRAM Organization and Operation
QUadruple ACtivation (QUAC)
QUAC-TRNG
Evaluation

## Slide 33: Real Chip Characterization
Experimentally study QUAC and QUAC-TRNG using 136 real DDR4 chips from SK Hynix
DDR4 SoftMC  DRAM Testing Infrastructure
https://github.com/CMU-SAFARI/SoftMC
[Hassan+ HPCA’17]

## Slide 34: Real Chip Characterization
Measure randomness of bitstreams using Shannon Entropy
Sample each bitline following QUAC 1000 times and calculate the bitline’s Shannon Entropy
SE(1111…111) = 0
0 < SE(1001…010) < 1
Calculating probabilities:
Proportion of logic-1 and logic-0 values in the random bitstream

## Slide 35: Real Chip Characterization
At 50°C and nominal voltage:
Repeatedly perform QUAC 1000 times and measure the Shannon Entropy of each bitline in
8K DRAM Segments (32K DRAM Rows),
using all 16 different four-bit data patterns
Data pattern: 1111 (four ones)
Data pattern: 1000
R0
R1
R2
R3
R0
R1
R2
R3
1000
1111

## Slide 36: Data Pattern Dependence
Calculate cache block entropy (CBE)
Metrics based on CBE:
Average CBE: Average entropy across all cache blocks in a module
Maximum CBE: Maximum of the cache block entropies in a module

## Slide 37: Data Pattern Dependence
Entropy varies with data pattern
Highest average entropy with pattern “0111”

## Slide 38: Spatial Distribution
Segment entropy behavior is different for different modules

## Slide 39: Spatial Distribution
Entropy significantly increases towards the end of the DRAM bank

## Slide 40: Takeaways: QUAC Entropy
We observe that entropy resulting from QUAC operations changes according to the
data pattern used in initialization
physical location of DRAM segments
attributed to:
systematic manufacturing process variation
design-induced variation

## Slide 41: QUAC-TRNG’s Quality
Two experiments:
Collect bitstreams by repeatedly sampling bitlines after QUAC operations
  1 Mb bitstreams
  Post-processing: Von Neumann Corrector
Collect bitstreams using QUAC-TRNG
  1 Gb bitstreams
  Post-processing: SHA-256

## Slide 42: QUAC-TRNG’s Quality
Two experiments:
Collect bitstreams by repeatedly sampling bitlines after QUAC operations
  1 Mb bitstreams
  Post-processing: Von Neumann Corrector
Collect bitstreams using QUAC-TRNG
  1 Gb bitstreams
  Post-processing: SHA-256
QUAC and QUAC-TRNG bitstreams pass all 15 NIST randomness tests

## Slide 43: QUAC-TRNG Throughput Estimation
Estimate QUAC-TRNG’s throughput according to:
SIB: # of SHA Input Blocks in the highest-entropy segment
L: Latency of one QUAC operation in nanoseconds
bps

## Slide 44: QUAC-TRNG Throughput Estimation
Estimate QUAC-TRNG’s throughput according to:
SIB: # of SHA Input Blocks in the highest-entropy segment
L: Latency of one QUAC operation in nanoseconds
4
256-bit Entropy Blocks
3
2
1
bps
4
3
2
1

## Slide 45: QUAC-TRNG Throughput Estimation
Estimate QUAC-TRNG’s throughput according to:
SIB: # of SHA Input Blocks in the highest-entropy segment
L: Latency of one QUAC operation in nanoseconds
bps

## Slide 46: QUAC-TRNG Throughput Estimation
Estimate QUAC-TRNG’s throughput according to:
SIB: # of SHA Input Blocks in the highest-entropy segment
L: Latency of one QUAC operation in nanoseconds
bps

## Slide 47: QUAC-TRNG Configurations
One Bank
BGP
Use a single DRAM bank
Use four banks from different bank groups
Bank Group-Level Parallelism
1
2
RC + BGP
Use in-DRAM copy to initialize DRAM rows and
use four banks from different bank groups
RowClone + BGP
3
DRAM Subarray
Source Row
Destination Row
[Seshadri+ MICRO’13]
[Gao+ MICRO’19]
Activate Source
Precharge
Activate Destination

## Slide 48: QUAC-TRNG Throughput
4.6X
Achieves 3.44 Gb/s throughput per DRAM channel on average across all modules
In-DRAM initialization greatly improves throughput

## Slide 49: QUAC-TRNG vs State-Of-The-Art
High-throughput DRAM-based TRNGs:
D-RaNGe: Activation latency failures
Talukder et. al: Precharge latency failures
Calculate throughput by tightly scheduling the DDR4 commands required to induce failures
Evaluate two versions of these past two works:
Base: As proposed
Enhanced (Fair): Throughput-optimized (SHA-256)
Assume four-channel DDR4 memory
[Kim+, HPCA’19]
[Talukder+, IEEE Access 2019]

## Slide 50: QUAC-TRNG vs State-Of-The-Art
Outperforms best prior DRAM-based TRNG (i) “base” by 15.08x at 2.4 GT/s
(ii) “enhanced” by 2.03x at 12 GT/s

## Slide 51: More in the Paper
NIST randomness tests results
Throughput & latency comparison against four other DRAM-based TRNGs
System Integration
  How QUAC-TRNG can be implemented in real systems
  System performance study
    QUAC-TRNG’s throughput with concurrently running applications
  Area overhead: 0.04% of a contemporary CPU (7 nm)
  Memory overhead: 0.002% of an 8 GiB DRAM module
Sensitivity Analysis
  Effect of temperature on QUAC’s entropy
    Entropy changes with temperature
  Time dependence study
    Entropy remains stable for at least up to a month

## Slide 52: Executive Summary
Motivation: DRAM-based true random number generators (TRNGs) provide true random numbers at low cost on a wide range of computing systems
Problem: Prior DRAM-based TRNGs are slow:
Based on fundamentally slow processes  high latency
Cannot effectively harness entropy from DRAM rows  low throughput
Goal: Develop a high-throughput and low-latency TRNG that uses commodity DRAM devices
Key Observation: Carefully engineered sequence of DRAM commands can activate four DRAM rows  QUadruple ACtivation (QUAC)
Key Idea: Use QUAC to activate DRAM rows that are initialized with conflicting data (e.g., two ‘1’s and two ‘0’s) to generate random values
QUAC-TRNG: DRAM-based TRNG that generates true random numbers at high-throughput and low-latency by repeatedly performing QUAC operations
Results: We evaluate QUAC-TRNG using 136 real DDR4 chips
5.4 Gb/s maximum (3.4 Gb/s average) TRNG throughput per DRAM channel
QUAC-TRNG has low TRNG latency: 256-bit RN in 274 ns
Outperforms existing DRAM-based TRNGs by 15.08x (base), and 1.41x (enhanced)
QUAC-TRNG passes all 15 NIST randomness tests

## Slide 53: QUAC-TRNG High-Throughput True Random Number Generation Using Quadruple Row Activation in Real DRAM Chips
Ataberk Olgun
Minesh Patel A. Giray Yağlıkçı Haocong Luo
Jeremie S. Kim F. Nisa Bostancı Nandita Vijaykumar
Oğuz Ergin Onur Mutlu

## Slide 54: BACKUP SLIDES

## Slide 55: Spatial Distribution
Cache block entropy is the highest around the middle of the DRAM segment

## Slide 56: NIST Results

## Slide 57: System Performance Study
The maximum throughput QUAC-TRNG provides without reducing the total off-chip memory bandwidth
Ramulator: 3.2 GHz core, four-channel DDR4 memory
QUAC-TRNG achieves 74.13% of the empirical average throughput

## Slide 58: Throughput & Latency Comparison

## Slide 59: Temperature Dependence

## Slide 60: DDR4 Modules