## Slide 1: REIS A High-Performance and Energy-Efficient Retrieval System with In-Storage Processing
Kangqi Chen
Nika Mansouri Ghiasi
Jisung Park
Rakesh Nadig
Yu Liang
Mohammad Sadrosadati
Manos Frouzakis
Haiyu Mao
Onur Mutlu
Presented by: Andreas Kosmas Kakolyris

## Slide 2: Executive Summary
Goal: Alleviate the I/O data movement overheads of RAG by accelerating both Nearest Neighbor Search and document retrieval without modifications to storage
Problem:
Retrieval Augmented Generation (RAG) pipelines incur data movement overheads between the host and the storage system
Existing In-Storage Processing (ISP) solutions only accelerate the Nearest Neighbor Search stage of RAG and introduce significant area and power overheads
Key Results:
Improves throughput (energy efficiency) by 15x (55x) over CPU
Reduces the I/O data movement overheads of RAG to <0.2% of total runtime
Outperforms an ISP-based ANNS accelerator by up to 2.5x
REIS introduces:
A lightweight scheme that links embeddings to documents
An ISP-tailored data-placement algorithm
An Approximate Nearest Neighbor Search (ANNS) engine that uses the existing components within the storage system

## Slide 3: Outline
Background
Motivation
REIS
Evaluation
Conclusion
Notes: This is an outline of my talk

## Slide 4: Typical LLM Inference Pipeline
Large Language Model
Query
Response
Limits their effectiveness in real-time and
domain-specific applications
Large Language Models:
Can only generate responses from data in their training sets
Require expensive retraining to memorize new data

## Slide 5: Retrieval Augmented Generation (RAG)
Doc. #N
Doc. #2
Document Database
Doc. #0
Doc. #1
Doc. #3
Large Language Model
RAG identifies the most relevant documents to the query to generate a high-quality response.
RAG combines:
Text generation capabilities of Large Language Models
Information retrieval techniques from document databases

## Slide 6: Retrieval Augmented Generation (RAG)
Doc. #N
Doc. #2
Document Database
Doc. #0
Doc. #1
Doc. #3
Query
Doc. #0
Doc. #1
Doc. #2
Doc. #N
Vector Database
Emb. #0
Emb. #1
Emb. #2
Emb. #N
Doc. #3
Emb. #3
Embedding
3
4
1
2
8
2
9
7
Embedding Model
Notes: To achieve this, RAG first uses an embedding model to generate embeddings for both the query and the document database.
Embeddings are multidimensional vectors representing the information contained in query and the documents.
Unfortunately they can be quite large [CLICK] reaching 8K dimensions.
As a result the Document database has to be stored in the storage system and usually in Flash memory
The next step is to then identify relevant documents using a process called nearest neighbor search

## Slide 7: Nearest Neighbor Search
Response
Distance
Doc. #0
Doc. #1
Doc. #2
Doc. #N
Vector Database
Emb. #0
Emb. #1
Emb. #2
Emb. #N
Doc. #3
Emb. #3
Query
Query Embedding
Query Embedding
6
Emb. #0
7
Emb. #1
18
Emb. #2
10
Emb. #3
4
Emb. #N
Doc. #N
Doc. #0
Doc. #1
Query
Large Language Model
Large embeddings lead to expensive distance calculations
Nearest Neighbor Search creates significant data movement
Notes: Nearest Neighbor Search involves calculating the distances [3x CLICK] between the query and the database embeddings and identifying those with the smallest distance to the query embedding.
To generate the response RAG then combines the documents that correspond to these embeddings with the Query, feedings them to the LLM to generate a response.
The problem here is that [CLICK] Nearest Neighbor Search creates significant data movement and
that Large embeddings lead to expensive distance calculations

## Slide 8: Accelerating Nearest Neighbor Search
Multiple approaches reduce Nearest Neighbor Search overheads
Quantization:
Integer Quantization
Binary Quantization
Product Quantization
In-Storage Processing:
Employs the computational resources within storage
Takes advantage of the large internal bandwidth of SSDs
Notes: To address these issues researchers have proposed multiple approaches

## Slide 9: Outline
Background
Motivation
REIS
Evaluation
Conclusion
Notes: In our motivation section we analyze both of these approaches

## Slide 10: Latency Breakdown of RAG
Quantization does not alleviate data movement overheads
Chart: Fraction of Execution Time, Nearest Neighbor Search with Binary Quantization
| wiki_en
Embedding Model Loading | 0.01005
Encoding | 0.0017831
Dataset Loading | 0.67256
Search | 0.019938
Generation Model Loading | 0.012806
Generation | 0.28287
Dataset Loading dominates total latency for large datasets
x
Notes: First, we perform a latency breakdown of all the stages in the RAG pipeline when using binary quantization
As you can see from the plot, Dataset loading comprises[CLLLLL] almost 70 percent of the total latency of RAG and [CLICK] dominates the total runtime for large datasets.
We thus deduce [CLICK] that Quantization on its own is not enough to alleviate the data movement overheads of the RAG pipeline

## Slide 11: In-Storage Nearest Neighbor Search Accelerators
Chart: Fraction of Execution Time, Nearest Neighbor Search with Binary Quantization
| wiki_en
Embedding Model Loading | 0.01005
Encoding | 0.0017831
Dataset Loading | 0.67256
Search | 0.019938
Generation Model Loading | 0.012806
Generation | 0.28287
Prior works introduce significant modifications to the SSDs
Existing designs only accelerate the search process
x
Notes: Second we explain why existing In-Storage Nearest Neighbor Search accelerator designs are not suitable for accelerating RAG pipelines.
Specifically, existing designs mainly [CLI?K] accelerate the search process, [CLICK]
which comprises only a small part of the total latency but do not provide support for accelerating retrieving the documents from storage.
In addition they introduce significant modifications to the design of the SSD and often incur power and area overheads which hinders their adoption

## Slide 12: Our Goal
Fundamentally alleviate the I/O data movement bottlenecks of RAG through an ISP design that does not require modifications to perform computation inside the storage system.
Notes: Our goal in this work is to

## Slide 13: Outline
Background
Motivation
REIS
Evaluation
Conclusion
Notes: To this end we propose REIS, which stands for

## Slide 14: REIS: Retrieval System with In-Storage Processing
Host System
CPU
DRAM
Accelerators
Query Embedding
REIS
Embedded Processor
Flash Controller
Flash Chip
Flash Controller
Flash Chip
Document Chunks
REIS employs three key mechanisms:
An Efficient ISP-tailored implementation of the Inverted File algorithm
A low-cost embedding-to-document linkage mechanism
An ANNS Engine that uses existing computational resources within SSDs
Key Idea: Leverage both In-Storage and In-Flash Processing to exploit the computational parallelism of Flash storage and conserve precious flash channel bandwidth.
Notes: Retrieval System with In storage procesing
The key idea of REIS is to …
When REIS is deployed,the Host system offloads RAG retrieval to the storage, by sending the query embedding and then receiving relevant document chunks
To achieve this REIS employs three key mechanisms

## Slide 15: Challenges of In-Storage Processing
SSD
Embedded Processor
Flash Controller
Flash Chip
Flash Chip
Flash Controller
Flash Chip
Flash Chip
Embedded Processor
Flash Controller
Flash Chip
Flash Chip
The design of the storage system creates unique limitations:
Limited performance and functionality in the embedded cores
Computation inside flash chips limited to bit-wise and bit-counting operations
Error-correction limits ISP performance due to data movement overheads
Notes: However, the design of the storage system creates unique limitations.
For example,
… such as lack of support from floating point operations
Computation inside flash chips is
Error correction limits … data movement overheads between the flash chips that store data embedded processors of the SSD that perform the error correction

## Slide 16: REIS: Overview
SSD Controller
Embedded
Processor
…
Flash Controller
Flash Chip
Flash Chip
…
Flash Controller
Flash Chip
Flash Chip
…
Channel
Flash Die
Flash Die
Flash Die
…
Flash Die
DRAM
Page
Plane #0
Plane #1
Page Buffer
Page Buffer
Peripheral Logic
Page
Page
Page
User Data
Out-of-Band
Notes: Despite these challenges, we base REIS’s design on the existing design of the SSD which is comprised of
Multiple processors, a small amount of dram
Multiple flash channels with multiple flash chips each, that are then composed of multiple flash dies
Each flash die contains multiple planes and pages, a Page buffer for each plane and peripheral circuitry ,
which all contain logic that can be used for computation. [CLICK]
In modern systems, the flash pages store the data and they also contain
a small amount of reserved capacity which stores error correction metadata called the out of band area.

## Slide 17: REIS: Database Layout
Page
Plane #0
Plane #1
Page Buffer
Page Buffer
Peripheral Logic
Page
Page
Page
Page – 16KB
Doc. Chunk #0
Doc. Chunk #1
Doc. Chunk #N
Page – 16KB
Emb #0
Emb #1
Emb #N
Addr
Addr
Addr
Embedding Reg.
Document Reg.
REIS’ Database Layout:
Creates separate regions for storing embeddings and documents.
Stores Embeddings using Enhanced SLC Programming for robust ISP operations.
Stores Documents in TLC to provide high storage density.
Stores Embeddings and Documents contiguously to avoid address translation.
Links Embeddings to Documents via the Out-of-Band (OOB) area in Flash pages.
Embedding Reg.
Document Reg.
Page – 16KB
Doc. Chunk #0
Doc. Chunk #1
Doc. Chunk #N
Page – 16KB
Emb #0
Emb #1
Emb #N
OOB
OOB
OOB
SLC
TLC
Park et al, “Flash-Cosmos: In-Flash Bulk Bitwise Operations Using Inherent Computation Capability of NAND Flash Memory”, in MICRO 2022
Notes: Let’s now move on to the database layout of our proposed design.
Robust ISP operations without error correction, eliminating thus any data movement overheads stemming from ECC
.
.
Links Embeddings to Documents by storing the Physical address of the Document chunk in the OOB area of the embedding pages
This again reduces the overheads of address translation because once an embedding is selected in the search process, the relevant document chunk can be directly retrieved without translation

## Slide 18: REIS: Inverted File Algorithm (IVF)
We thus design an In-Storage ANNS engine that accelerates IVF
REIS employs the Inverted File Algorithm (IVF) with Binary Quantization to accelerate Approximate Nearest Neighbor Search with In-Storage and In-Flash processing.
IVF:
Organizes embeddings into clusters
Performs a coarse-grained search to identify the nearest clusters
Performs a fine-grained search within the identified clusters to find the nearest embeddings
The Inverted File Algorithm:
Provides high performance and accuracy with Binary Quantization
Features characteristics that make it suitable to the storage system
Notes: While this database layout can be used to facilitate exact Nearest Neighbor Search, REIS goes a step further and also provides support for Approximate Nearest Neighbor Search, which provides higher performance.
Specifically, REIS employs the Inverted File algorithm or IVF with Binary Quantization, to accelerate Nearest Neighbor Search.
IVF: …
The reason that we chose IVF is that it:
Provides a favorable performance and accuracy tradeoff when combined with binary quantization
Features distinct characteristics that make it particularly suitable for in storage processing.
We thus design our In-Storage ANNS engine to support and accelerate IVF.

## Slide 19: REIS: In-Storage ANNS Engine
Flash Die
Plane #1
Page Buffer
Peripheral Logic
DRAM
Plane #0
Page Buffer
Page
Page
Query Embedding
Query Embedding
Query Embedding
Document Embedding
Document Embedding
Distances
For the coarse- and fine-grained stages of IVF, the ANNS engine:
Copies the Query Embeddings to the Page Buffer
Moves the Document Embeddings to the Page Buffer
Calculates distances using logic in the page buffer and the peripheral circuitry
Transfers the distances back to the SSD’s DRAM
Notes: For both the coarse and
Using the XOR logic and the bitcounting logic inside
At this point the embedded cores take over the execution

## Slide 20: REIS: In-Storage ANNS Engine
Flash Die
Plane #1
Page Buffer
DRAM
Plane #0
Page Buffer
Page
Page
Peripheral Logic
Distances
SSD Controller
Embedded
Processor
QuickSelect
Reranking
QuickSort
The Embedded Processor:
Performs QuickSelect to identify the Nearest Clusters and embeddings
Performs Reranking and QuickSort to refine the search results.
Query Embedding
Notes: …
And for the fine-grained search

## Slide 21: REIS: In-Storage ANNS Engine
Flash Die
Plane #1
Page Buffer
Peripheral Logic
DRAM
Plane #0
Page Buffer
Page
Page
SSD Controller
Embedded
Processor
Document Chunks
The ANNS Engine:
Moves the identified document chunks to the SSD’s DRAM
Transfers them to the host
Notes: Hide the top part , hide a lot of things

## Slide 22: REIS: Optimizations
We improve the In-Storage ANNS engine with the following optimizations:
Distance Filtering (DF)
  Quickly filters out embeddings with large distances without transferring them to the embedded processor.
Multi-Plane Input Broadcasting (MPIBC)
  Parallelly transfers the query embedding to multiple planes.
Pipelining (PL)
  Overlaps flash page reads with distance computations.
Notes: We further improve our design by proposing the following three optimizations

## Slide 23: Outline
Background
Motivation
REIS
Evaluation
Conclusion
Notes: I will now move on the the evaluation section

## Slide 24: Evaluated System Configurations & Baselines
Baselines
Evaluated Metrics
Datasets
SSD Configurations
Algorithms
CPU-Real: A CPU-based RAG retrieval system running IVF
No-I/O: The same CPU-based system without I/O overheads
NDSearch: A state-of-the-art ISP-based ANNS accelerator
Exact Nearest Neighbor Search (BF)
Inverted File Algorithm (IVF)
Throughput: Queries-per-second (QPS)
Energy Efficiency: QPS/ Watt
End-to-end Retrieval Performance
Wikipedia (Full)
Wikipedia (English subset)
Natural Questions (NQ)
HotpotQA
SIFT-1B
DEEP-1B
SSD-C: Cost-oriented
SSD-P: Performance-oriented
Notes: For the evaluation of REIS we use multiple baselines

## Slide 25: Performance Evaluation
Chart: Norm. QPS
| 0.98 | 0.94 | 0.90 | BF | IVF (Recall@10) | wiki_full
No-I/O | 1.1397 | 3.1759 | 16.1692 | 48.4078
REIS-SSD-C | 1.7505 | 4.7971 | 21.5811 | 45.9162
REIS-SSD-P | 3.5032 | 9.7446 | 47.0479 | 112.4616
We compare the throughput of No-I/O and REIS on SSD-C and SSD-P
Throughput is normalized to that of CPU-Real
We evaluate performance on BF and IVF across different recall values
REIS outperforms No-I/O due to the parallelism of the SSD
Performance improvements increase at higher recall values
3.33x
2.3x
112
10
47
3
48
22
16
5
46
1
2
4
Notes: For the performance evaluation [CLICK and read]
In the Y axis throughput …
From the data we observe that []
Due to the massive parallelism of the SSD
We also observe higher improvements at higher recall values, due to the increasde computational requirements that
further highlight the computational capabilities of the SSD.

## Slide 26: Energy Efficiency Evaluation
Chart: Norm. QPS/W
| 0.98 | 0.94 | 0.90 | BF | IVF (Recall@10) | wiki_full
REIS-SSD-C | 46.348 | 45.5765 | 40.2732 | 28.6207
REIS-SSD-P | 90.4327 | 90.2664 | 85.6016 | 68.3468
Energy efficiency normalized to that of CPU-Real
Improvements in energy efficiency increase at higher recall values
45.6x
28.6x
Notes: We perform a similar experiment for Energy Efficiency [CLICK]
This time the Y axis represents QPS/W normalized to the same metric for CPU real [CLICK]
We again make a similar conclusion ,which is that …
[CLICK ]As you can see

## Slide 27: Evaluation Across Multiple Datasets
Chart: Norm. QPS
| 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | NQ | HotpotQA | wiki_en | wiki_full
No-I/O | 1.2327 | 2.1174 | 6.1372 | 9.0728 | 1.249 | 2.2867 | 4.2167 | 6.3242 | 1.1634 | 1.6627 | 3.1515 | 6.7297 | 1.1397 | 3.1759 | 16.1692 | 48.4078
REIS-SSD-C | 1.001 | 1.5837 | 1.3098 | 1.2322 | 1.0061 | 1.7405 | 2.2449 | 2.2598 | 1.7105 | 4.2796 | 7.3696 | 11.6214 | 1.7505 | 4.7971 | 21.5811 | 45.9162
REIS-SSD-P | 2.1306 | 4.9629 | 4.4567 | 4.1926 | 2.0806 | 4.4469 | 6.7005 | 7.1343 | 3.4333 | 8.8854 | 16.8388 | 30.7936 | 3.5032 | 9.7446 | 47.0479 | 112.4616
Similar trends across all datasets
Performance benefits increase with larger datasets
Notes: n the paper we evaluate these on multiple different datasets
and we (i) observe the the patterns are largely the same
(ii) Performance benefits increase with larger datasets, again due to the parallelism of the SSD.

## Slide 28: More Datasets in the Paper
Chart: Norm. QPS/W
| 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | NQ | HotpotQA | wiki_en | wiki_full
REIS-SSD-C | 24.5037 | 22.5683 | 6.4396 | 4.0979 | 24.306 | 22.9663 | 16.0642 | 10.7817 | 44.3609 | 77.6645 | 70.5597 | 52.1065 | 46.348 | 45.5765 | 40.2732 | 28.6207
REIS-SSD-P | 50.8497 | 68.9532 | 21.3634 | 13.5949 | 49.0045 | 57.2105 | 46.7479 | 33.1875 | 86.8161 | 157.2163 | 157.1885 | 134.615 | 90.4327 | 90.2664 | 85.6016 | 68.3468
Energy Efficiency gains increase with higher target recall values

## Slide 29: End-to-End Performance: Latency Breakdown
Chart: Fraction of Execution Time, REIS
| wiki_en
Embedding Model Loading | 0.032634
Encoding | 0.0057899
In-Storage Retrieval | 0.0015136
Generation Model Loading | 0.041582
Generation | 0.91848
Chart: Fraction of Execution Time, Nearest Neighbor Search with Binary Quantization
| wiki_en
Embedding Model Loading | 0.01005
Encoding | 0.0017831
Dataset Loading | 0.67256
Search | 0.019938
Generation Model Loading | 0.012806
Generation | 0.28287
CPU Retrieval
REIS
Notes: Let’s now move on to evaluating end to end performance
We repeat the latency breakdown experiment from the motivation section, this time also performing document retrieval with REIS. [click]
As can be seen from the plot the once almost 70% [CLICK] of latency stemming from dataset loading and search is now combined into a single In-Storage retrieval step that comprises just 0.15% of the total latency
We thus conclude that REIS eliminates the data movement overheads from the RAG pipeline.

## Slide 30: Sensitivity Study
Chart: REIS-SSD-C
| 0.98 | 0.96 | 0.94 | 0.92 | 0.9
NO-OPT | 0.27924 | 0.88394 | 1.6593 | 3.0822 | 5.7073
+DF | 1.4274 | 4.3873 | 7.9382 | 13.8275 | 22.9706
+PL | 1.8944 | 5.7436 | 10.2242 | 17.3436 | 27.6886
+MPIBC | 5.5425 | 15.7675 | 26.1728 | 40.0935 | 56.1144
Chart: REIS-SSD-P
| 0.98 | 0.96 | 0.94 | 0.92 | 0.9
NO-OPT | 0.90136 | 2.8506 | 5.2586 | 9.9042 | 17.2659
+DF | 5.9019 | 17.2766 | 29.1666 | 47.2175 | 67.3082
+PL | 10.8935 | 29.6848 | 46.7051 | 68.5475 | 88.4923
+MPIBC | 11.2588 | 33.3611 | 57.0581 | 94.2395 | 137.4401
Distance Filtering provides a 5x throughput increase across all configurations
Pipelining further improves performance by 1.4x on average
Multi-Plane Input Broadcasting improves performance on SSD-P by 26% on average on top of Pipelining
These optimizations offer a combined performance improvement of 12.9x over the NO-OPT baseline.
Notes: In the paper, we also perform a sensitivity study which quantifies the speedups provided by our optimizations on top of our basic design, which we call No-OPT
[CLICK] In the x axis, we sweep different target recall values for recall @ 10
[CLICK] In the y-axis, we measure QPS, normalized to the throughput of the CPU-Real baseline
[CLICK] and the different lines correspond to different configurations, each adding another optimization on top of the previous ones
We perform this experiment both for the [CLICK] cost-oriented and the [CLICK] performance oriented SSD and we see that
[CLICK] On average DF provides a 5x improvement in throughput across all configuration
[CLICK] Pipelining further improves performance by 1.4x times
And that [CLICK] MPIBC improves performance on SSD-P by 26% on average on top of Pipelining
[CLICK] When combined, these optimization offer a combined performance improvement of 12.9x on average on top of the basic NO-OPT design.

## Slide 31: Performance Comparison to NDSearch
Chart: Norm. QPS
| SIFT-1B (Recall@10=0.94) | DEEP-1B (Recall@10=0.93)
Speedup over ND-HNSW | 2.5545 | 1.7554
Speedup over ND-DiskANN | 1.0534 | 1.3604
REIS with IVF features streaming access patterns that
exploit the internal bandwidth of the storage system
REIS improves performance by:
2.5x and 1.8x over NDSearch with HNSW
1.05x and 1.36x over NDSearch with DiskANN
We normalize the throughput of REIS to that of NDSearch running HNSW and DiskANN
We evaluate both REIS and NDSearch on SIFT-1B and DEEP-1B
Wang et al, “NDSEARCH: Accelerating Graph-Traversal-Based Approximate Nearest Neighbor Search through Near Data Processing”, in ISCA 2024
Notes: For my final evaluation slide for today we have a comparison to Ndsearch, a state of the art ANNS accelerator design.
For this comparison [CLICK]

## Slide 32: Available on arXiv
https://arxiv.org/abs/2506.16444
Notes: Our paper is available

## Slide 33: More in the Paper
Chart: Norm. QPS
| 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | NQ | HotpotQA | wiki_en | wiki_full
No-I/O | 1.2327 | 2.1174 | 6.1372 | 9.0728 | 1.249 | 2.2867 | 4.2167 | 6.3242 | 1.1634 | 1.6627 | 3.1515 | 6.7297 | 1.1397 | 3.1759 | 16.1692 | 48.4078
REIS-SSD-C | 1.001 | 1.5837 | 1.3098 | 1.2322 | 1.0061 | 1.7405 | 2.2449 | 2.2598 | 1.7105 | 4.2796 | 7.3696 | 11.6214 | 1.7505 | 4.7971 | 21.5811 | 45.9162
REIS-SSD-P | 2.1306 | 4.9629 | 4.4567 | 4.1926 | 2.0806 | 4.4469 | 6.7005 | 7.1343 | 3.4333 | 8.8854 | 16.8388 | 30.7936 | 3.5032 | 9.7446 | 47.0479 | 112.4616
Chart: Norm. QPS/W
| 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | 0.98 | 0.94 | 0.90 | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | BF | IVF (Recall@10) | NQ | HotpotQA | wiki_en | wiki_full
REIS-SSD-C | 24.5037 | 22.5683 | 6.4396 | 4.0979 | 24.306 | 22.9663 | 16.0642 | 10.7817 | 44.3609 | 77.6645 | 70.5597 | 52.1065 | 46.348 | 45.5765 | 40.2732 | 28.6207
REIS-SSD-P | 50.8497 | 68.9532 | 21.3634 | 13.5949 | 49.0045 | 57.2105 | 46.7479 | 33.1875 | 86.8161 | 157.2163 | 157.1885 | 134.615 | 90.4327 | 90.2664 | 85.6016 | 68.3468
Performance Evaluation on More Datasets
Energy Efficiency Evaluation on More Datasets
Notes: For my final evaluation slide for today

## Slide 34: More in the Paper
Performance Analysis of different ANNS algorithms
Notes: For my final evaluation slide for today

## Slide 35: Outline
Background
Motivation
REIS
Evaluation
Conclusion

## Slide 36: Conclusion
RAG retrieval is bottlenecked by I/O data transfer overheads between the host and the storage system
The first system for RAG retrieval that leverages
In-Storage Processing using the existing computational resources within the storage system
Outperforms CPU search by 15x on average
Improves energy efficiency by 55x on average
Reduces document retrieval latency to < 0.2%
Outperforms NDSearch by up to 2.5x
Key Results
REIS
Notes: RAG retrieval currently is bottlenecked
We propose reis
REIS:
Outperforms

## Slide 37: REIS: A High-Performance and Energy-Efficient Retrieval System with In-Storage Processing
Kangqi Chen
Nika Mansouri Ghiasi
Jisung Park
Rakesh Nadig
Yu Liang
Mohammad Sadrosadati
Manos Frouzakis
Haiyu Mao
Onur Mutlu
Presented by: Andreas Kosmas Kakolyris

## Slide 38: REIS: A High-Performance and Energy-Efficient Retrieval System with In-Storage Processing
Kangqi Chen
Nika Mansouri Ghiasi
Jisung Park
Rakesh Nadig
Yu Liang
Mohammad Sadrosadati
Manos Frouzakis
Haiyu Mao
Onur Mutlu
Presented by: Andreas Kosmas Kakolyris
Backup Slides

## Slide 39: SSDs & NAND Flash Memory
DRAM
SSD Controller
Embedded
Processor
…
Flash Controller
Flash Chip
Flash Chip
…
Flash Die
Flash Die
Flash Die
…
Flash Controller
Flash Chip
Flash Chip
…
Channel
Flash Die
Page
Plane #0
Plane #1
Page Buffer
Page Buffer
Peripheral Logic
Page
User Data
Sensing Buffer
Cache
Buffer
Data Buffer
Out-of-Band
Pass-Fail Checker
Fail-Bit Counter

## Slide 40: SSDs & NAND Flash Memory
DRAM
SSD Controller
Embedded
Processor
…
Flash Controller
Flash Chip
Flash Chip
…
Flash Die
Flash Die
Flash Die
…
Flash Controller
Flash Chip
Flash Chip
…
Channel
Flash Die
Page
Plane #0
Plane #1
Page Buffer
Page Buffer
Peripheral Logic
Page
User Data
Sensing Buffer
Cache
Buffer
Data Buffer
Out-of-Band
Pass-Fail Checker
Fail-Bit Counter

## Slide 41: REIS: In-Storage ANNS Engine
Page
Plane #0
Plane #1
Page Buffer
Page Buffer
Peripheral Logic
Page
SSD Controller
Embedded
Processor
…
Flash Controller
Flash Chip
Flash Chip
…
Flash Controller
Flash Chip
Flash Chip
…
Channel
Flash Die
Flash Die
Flash Die
…
Flash Die
DRAM
User Data
Out-of-Band
Pass-Fail Checker
Fail-Bit Counter
Sensing Buffer
Cache
Buffer
Data Buffer
Query Embedding
Database Embeddings
Data Buffer
Distance
Notes: Hide the top part , hide a lot of things