## Slide 1
Revelator
Rapid Data Fetching
via System-Software-Guided Hash-based
Speculative Address Translation
Konstantinos Kanellopoulos Konstantinos Sgouras
Harsh Songara Andreas Kosmas Kakolyris Vlad-Petru Nitu
Spiros Galanopoulos Rahul Bera Konstantina Koliogeorgi
Rakesh Kumar Onur Mutlu

## Slide 2
Background

## Slide 3
Virtual Memory is a Cornerstone
of Modern Computing Systems
GPUs
NICs
CPUs
Mobile/ Embedded SoCs
AI Accelerators
Notes: Virtual memory is the cornerstone abstraction underpinning every modern computing system.
From CPUs to GPUs and NICs— they all rely on it.

## Slide 4
Databases
Genomics
Graph
Analytics
Emerging Workloads
Performance bottleneck: 10-30%
of cycles spent on address translation
Zao et al. “Contiguitas: The Pursuit of Physical Memory Contiguity in Datacenters” ISCA 2023
Sparse
Machine
Learning
Notes: What happens when modern workloads meet this old contract?
[CLICK] Databases, genomics, graph analytics [CLICK] introduce address translation overheads

## Slide 5
Address Translation Overheads
Irregular Memory
Accesses
Large Data
Footprints
Notes: These workloads exhibit:
[CLICK] — irregular memory accesses
[CLICK] — large data footprints

## Slide 6
Low Spatial and Temporal Locality
0x54277457
0x54277457
0x51428887
0x54277457
0x54277457
0x56477457
0xA4266459
0x940F5498
TLB
0xA4266459
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
PMLE4
PDP
PD
PT
Level 4
Level 3
Level 2
Level 1
Frequent
TLB Misses
Frequent High-Latency Page Table Walks
Notes: Thus, experience low spatial/temporal locality causing:
[CLICK] frequent TLB misses
[CLICK]→ frequent high-latency page table walks

## Slide 7
address
The
Wall
tRANSLATION
Notes: Transition slide — 'Virtual Memory'. Pause.

## Slide 8
address
The
Wall
tRANSLATION
Speculation
Notes: Transition slide — 'Virtual Memory'. Pause.

## Slide 9
address
The
Wall
tRANSLATION
Speculation
Notes: Transition slide — 'Virtual Memory'. Pause.

## Slide 10
Notes: Transition slide — 'Virtual Memory'. Pause.

## Slide 11: Speculative Address Translation
  Conventional Address Translation
TLB Miss
Page Table Walk
Data Fetch
Likely DRAM access
Physical address
is known
Notes: [CLICK] Compared to regular translation
[CLICK] The idea of speculative translation is this:
[CLICK] instead of waiting for the page-table walk to complete,
[CLICK] predict the physical address and start the data fetch immediately. [CLICK] If the prediction is right, we overlap translation latency with data fetch and
[CLICK] gain performance

## Slide 12: Speculative Address Translation
TLB Miss
Page Table Walk
Data Fetch
  Speculative Address Translation
TLB Miss
Page Table Walk
Predict Physical
Address
Speculative Data Fetch
Data Fetch
Likely
cache hit
  Conventional Address Translation
Notes: [CLICK] Compared to regular translation
[CLICK] The idea of speculative translation is this:
[CLICK] instead of waiting for the page-table walk to complete,
[CLICK] predict the physical address and start the data fetch immediately. [CLICK] If the prediction is right, we overlap translation latency with data fetch and
[CLICK] gain performance

## Slide 13: Speculative Address Translation
TLB Miss
Page Table Walk
Data Fetch
  Speculative Address Translation
TLB Miss
Page Table Walk
Predict Physical
Address
Speculative Data Fetch
Data Fetch
Likely
cache hit
Saved
Cycles
  Conventional Address Translation
Notes: [CLICK] Compared to regular translation
[CLICK] The idea of speculative translation is this:
[CLICK] instead of waiting for the page-table walk to complete,
[CLICK] predict the physical address and start the data fetch immediately. [CLICK] If the prediction is right, we overlap translation latency with data fetch and
[CLICK] gain performance

## Slide 14: Predicting the PA is Challenging
Virtual-to-physical mapping depends
on unpredictable runtime conditions
and system-level factors
Scheduling Decisions
Memory Utilization
Memory Fragmentation
Co-running Applications
1
3
2
4
Notes: But predicting the physical address is hard. The OS allocates pages based on many system-level factors, so the VA-to-PA mapping looks essentially random.

## Slide 15: Example: Same Process, Different Instances
Virtual Address Space
Physical Address Space
Notes: But predicting the physical address is hard. The OS allocates pages based on many system-level factors, so the VA-to-PA mapping looks essentially random.

## Slide 16: Example: Same Process, Different Instances
Virtual Address Space
Physical Address Space
Process A – Instance 1
Notes: But predicting the physical address is hard. The OS allocates pages based on many system-level factors, so the VA-to-PA mapping looks essentially random.

## Slide 17: Example: Same Process, Different Instances
Virtual Address Space
Process A – Instance 2
Physical Address Space
Notes: But predicting the physical address is hard. The OS allocates pages based on many system-level factors, so the VA-to-PA mapping looks essentially random.

## Slide 18: Example: Same Process, Different Instances
Virtual Address Space
Process A – Instance 3
Physical Address Space
Takeaway: VA-to-PA mapping is established by modern OSes in an unpredictable manner
Notes: But predicting the physical address is hard. The OS allocates pages based on many system-level factors, so the VA-to-PA mapping looks essentially random.

## Slide 19: Motivation: Shortcomings of Prior Works
To improve VA-to-PA predictability,
prior speculative translation schemes require:
Free large pages and/or VA-to-PA contiguity
Costly hardware changes for speculation metadata
1
2
Notes: Prior speculative translation schemes work around this by making strong assumptions —
[CLICK] they require free large pages or contiguity,
[CLICK] and they use costly hardware for metadata.

## Slide 20: Prior Work: Contiguity-based Speculation1
As memory fragmentation increases, reduction
of translation latency drops significantly
Memory Fragmentation
1Alverti et al. “Enhancing and Exploiting Contiguity for Fast Memory Virtualization”, ISCA 2020
Reduction of
Translation
Latency (%)
Notes: Prior speculative translation schemes work around this by making strong assumptions —
[CLICK] they require free large pages or contiguity,
[CLICK] and they use costly hardware for metadata.

## Slide 21: Our Goal
Large page availability
VA-to-PA contiguity
Costly hardware for metadata
Enable highly-accurate speculative address translation without requiring:
Notes: Our goal for Revelator is to
[CLICK] enable highly accurate speculative translation
[CLICK] without relying on large pages,
[CLICK] without relying on contiguity, and
[CLICK] without costly metadata hardware.

## Slide 22
Revelator

## Slide 23: Revelator: Key Approach
Co-design hardware and OS to perform
highly accurate speculative translation
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 24: Revelator: Key Idea
Predictable
Physical Location
Tiered Hash-based Allocation
Operating System
Speculation
Engine
Hardware
Establish
Leverage
Data + Page Table
Employ hashing to enable highly accurate speculative
address translation with small system modifications
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 25
Revelator:
Overview

## Slide 26: Revelator: Overview
Page Table Walk
Speculative Data Fetch
Virtual Address
Hash Function
Parallel Operations
Data is found in the cache
TLB Miss
Data Fetch
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 27: Revelator: Overview
Speculative Data Fetch
Parallel Operations
Page Table Walk
L4
L3
L2
PTE
Speculatively Fetch PTE
Parallel Operations
Virtual Address
Hash Function
2
1
Data is found in the cache
PTE is
found in
the cache
TLB Miss
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 28: Revelator: Key Benefit
Co-design hardware and OS to perform
highly accurate speculative translation
Predictable
Physical Location
Tiered Hash-based Allocation
Operating System
Speculation
Engine
Hardware
Establish
Leverage
Data + Page Table
Hides & reduces address translation latency
without depending on memory fragmentation
(i.e., large pages, contiguity)
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 29: Revelator: Key Components
Predictable
Physical Location
Tiered Hash-based Allocation
Operating System
Establish
Data + Page Table
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 30: Revelator: OS Side
Tiered Hash-based Allocation
Hash()
PPN0
PPNi
PPNM
Virtual Page
M Different allocation tiers
(i.e., allocation attempts)
Predictable
Physical Location
Operating System
Establish
Data + Page Table
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 31: Revelator: OS Side
Hardware
Virtual Page
PPN0
PPNi
PPNM
M Candidate
Physical Locations
..
..
Predictable
Physical Location
Hash Circuit
Small OS modifications with
low impact on allocation latency
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 32: Revelator: Key Components
Predictable
Physical Location
Speculation
Engine
Hardware
Leverage
Data + Page Table
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 33: Revelator: Hardware Side
Hardware
Virtual Page
PPN0
PPNi
PPNM
M Candidate
Physical Locations
..
..
Predictable
Physical Location
Hash Circuit
Data + Page Table
Leverage
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 34: Revelator: Hardware Side
Tiered Hash-based Allocation
Hash()
PPN0
PPNi
PPNM
Virtual Page
M Different Tiers
(i.e., Hash Attempts)
Predictable
Physical Location
Operating System
Establish
Low-cost hardware
to generate candidate PAs
without the need for extra metadata
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 35
Revelator:
Detailed Design

## Slide 36: Revelator: Key Components
Predictable
Physical Location
Tiered Hash-based Allocation
Operating System
Speculation
Engine
Hardware
Establish
Leverage
Data + Page Table
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 37: Revelator: Key Components
Predictable
Physical Location
Tiered Hash-based Allocation
Operating System
Establish
Data + Page Table
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 38: OS: Tiered Hash-based Allocation
Hash Function
PPN0
PPN1
..
PPNi
..
PPNM
Virtual Page
Seed0
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 39: OS: Tiered Hash-based Allocation
Hash Function
PPN1
..
PPNi
..
PPNM
Virtual Page
Seed0
Seed1
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 40: OS: Tiered Hash-based Allocation
Hash Function
PPN1
..
PPNi
..
PPNM
Virtual Page
Seed0
Seed1
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 41: OS: Tiered Hash-based Allocation
Hash Function
..
PPNi
..
PPNM
Virtual Page
Seed0
Seed1
Seedn
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 42: OS: Tiered Hash-based Allocation
Hash Function
..
..
PPNM
Virtual Page
Seed0
Seed1
SeedM
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 43: OS: Tiered Hash-based Allocation
Hash Function
..
..
Virtual Page
Seed0
Seed1
SeedM
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 44: OS: Tiered Hash-based Allocation
If all M hash attempts fail
Revelator falls back
to the conventional allocator
Buddy Allocator
Tiered
Hash-based Allocation
Fallback
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 45: OS: Tiered Hash-based Allocation
If all N hash attempts fail
Revelator falls back
to the conventional allocator
Buddy Allocator
Tiered
Hash-based Allocation
Fallback
Does tiered hash-based allocation work well?
Notes: If that slot is taken, we try the next candidate using a new seed

## Slide 46: OS: Tiered Hash-based Allocation
Each allocation attempt is a Bernoulli trial: a slot is free with probability P = L / N
Each request makes k independent hash attempts
Allocation fails only if all k attempts land on taken slots
P(success) = 1 − (L / N)ᵏ
Probability data is allocated with a hash function
L = Number of occupied pages
N = Total number of pages
Notes: And we conclude that Revelator’s effectiveness..

## Slide 47: Revelator: Allocation Properties
Each allocation attempt is a Bernoulli trial: a slot is free with probability P = L / N
Each request makes k independent hash attempts
Allocation fails only if all k attempts land on taken slots
Probability data is allocated with a hash function
L = Number of occupied pages
N = Total number of pages
Number of hash-based allocation attempts
1
Notes: And we conclude that Revelator’s effectiveness..

## Slide 48: Number of Hash-based Alloc. Attempts
Chart: Number of hash-based allocation attempts
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
P(success) | 0.5 | 0.75 | 0.875 | 0.9375 | 0.9688 | 0.9844 | 0.9922 | 0.9961
  Increasing the number of hash-based allocation attempts exponentially increases the probability of successul allocation
P (Success. alloc.)
Memory Utilization: 50%
High Fragmentation
Notes: And we conclude that Revelator’s effectiveness..

## Slide 49: Revelator: Allocation Properties
Each allocation attempt is a Bernoulli trial: a slot is free with probability P = L / N
Each request makes k independent hash attempts
Allocation fails only if all k attempts land on taken slots
Probability data is allocated with a hash function
L = Number of occupied pages
N = Total number of pages
Number of hash-based allocation attempts
Allocation success is independent
from memory fragmentation
1
2
Notes: And we conclude that Revelator’s effectiveness..

## Slide 50: Allocation Success is Independent from Memory Fragmentation
Chart: Number of hash-based allocation attempts
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
P(success) | 0.5 | 0.75 | 0.875 | 0.9375 | 0.9688 | 0.9844 | 0.9922 | 0.9961
  Even at high fragmentation, using 4 hash
  attempts leads to >90% successful allocation
P (Success. alloc.)
Memory Utilization: 50%
High Fragmentation
Notes: And we conclude that Revelator’s effectiveness..

## Slide 51: Revelator: Key Components
Predictable
Physical Location
Speculation
Engine
Hardware
Leverage
Data + Page Table
Notes: The Revelator key idea:
[CLICK] co-design the hardware and the OS.
[CLICK] The OS uses a tiered hash-based allocation policy so that
[CLICK] the physical location of a page
[CLICK] is predictable from its virtual address at the hardware level using a speculation engine

## Slide 52: Hardware: Speculation Engine
Hash
Circuit
PPN0
PPN1
..
PPNi
..
PPNM
Memory Management Unit
Memory Hierarchy
Generate Candidate PAs
Notes: If confidence is high, the MMU dispatches the data fetch to the memory hierarchy in parallel with the real page-table walk.

## Slide 53: Revelator: Speculation Engine
Hash
Circuit
PPN0
PPN1
..
PPNi
..
PPNM
Memory Management Unit
Memory Hierarchy
Filter
Notes: If confidence is high, the MMU dispatches the data fetch to the memory hierarchy in parallel with the real page-table walk.

## Slide 54: Speculation Degree Filter
Filter
Hash-Based Allocation Statistics
Hash0
HashM
Hash1
.
.
.
0.6
0.2
0.1
1
1
0
Speculation
degree up to
1 is allowed
0
1
2
3
4
Bandwidth Consumption Monitor
Two-level Degree Filtering

## Slide 55: Revelator: Speculation Engine
Hash
Circuit
PPN0
PPN1
..
PPNi
..
PPNM
Memory Management Unit
Memory Hierarchy
Filter
Data stored in PPN0 is fetched into the cache before PTW completes
Notes: If confidence is high, the MMU dispatches the data fetch to the memory hierarchy in parallel with the real page-table walk.

## Slide 56
Extensions of Revelator

## Slide 57: Revelator: Extensions
Synergy with large pages
Virtualized environments
NUMA/CXL-like systems
1
2
3

## Slide 58: Revelator: Extensions
Synergy with large pages
Virtualized environments
NUMA/CXL-like systems
1
2
3

## Slide 59: Synergy with Large Pages
Try tiered hash-based allocation for 2MB pages
1
2MB
Virtual Page
PPN0
..
PFN511
PPN512
..
PPN1023
Hash Function

## Slide 60: Synergy with Large Pages
Try tiered hash-based allocation for 2MB pages
1
2MB
Virtual Page
PPN0
..
PFN511
PPN512
..
PPN1023
Hash Function
Hide address translation
latency of 2MB pages

## Slide 61: Synergy with Large Pages
Try tiered hash-based allocation for 2MB pages
1
Try to allocate with conventional THP
Use large pages when
fragmentation levels allow it
2

## Slide 62: Synergy with Large Pages
Try tiered hash-based allocation for 2MB pages
1
Try to allocate with conventional THP
2
Try 4KB hash-based data allocation
3
Maintain fast address translation
when large pages are not available

## Slide 63: Synergy with Large Pages
Try tiered hash-based allocation for 2MB pages
1
Try to allocate with conventional THP
2
Try 4KB hash-based data allocation
3
Fallback to conventional allocation
4

## Slide 64: Synergy with Large Pages
Try tiered hash-based allocation for 2MB pages
1
Try to allocate with conventional THP
2
Try 4KB hash-based data allocation
3
Fallback to conventional allocation
4
Revelator uses large pages
when possible while being effective
even when they are not available

## Slide 65: Revelator: Extensions
Synergy with large pages
1
2
3
Virtualized environments
NUMA/CXL-like systems

## Slide 66: Revelator: Extensions
Synergy with large pages
Revelator in virtualized environments
Revelator in NUMA/CXL-like systems
1
2
3
https://arxiv.org/abs/2508.02007

## Slide 67
Evaluation
Results

## Slide 68: Evaluation Methodology
Prototyped the SW component of Revelator in Linux 6.10.8
  Modifications in the buddy allocator
  Extensions on top of THP
Evaluation using Virtuoso [Kanellopoulos+ ASPLOS’25] ported on top of Sniper [Carlson+ SC’11]
Workloads: Executed for 300M instructions
  GraphBIG: PR, BFS, BC, GC, CC
  HPCC: Randacc
  XSBench: Particle Simulation
  DLRM: Sparse-Length Sum
  GenomicsBench: k-mer count
  Google DPC-4 mixes in multicore systems
Open source: https://github.com/CMU-SAFARI/Virtuoso
Single-core systems
Notes: [CLICK] We rototyped Revelator in Linux and
[CLICK] evaluated with Virtuoso
[CLICK] Same workloads as Utopia/Victima

## Slide 69: Evaluated Systems
THP: Baseline with THP enabled
ReserveTHP: System with reservation-based THP
SpecTLB [Barr+ ISCA’11]: Speculative translation scheme for reserved large pages
POM-TLB [Ryoo+ ISCA’17]: Large software-managed 64K-entry L3 TLB
64K-entry L2 TLB: L2 TLB with optimistic 12-cycle access latency
ASAP [Margaritov+ MICRO’19]: Intra-page table walk prefetching
DMT [Zhang+ ASPLOS’24]: Direct memory translation via VA-to-PTE mappings
ECHT [Skarlatos+ ASPLOS’20]: State of the art page table design
Mosaic Pages [Gosakan+ ASPLOS’24]: Large TLB reach via hash-based allocation
SpOT [Alverti+ ISCA’20]: Speculative translation via contiguous allocation
Revelator: Tiered hash-based allocation + speculation engine
Revelator+THP
Notes: Evaluated Revelator against 10 diverse techniques

## Slide 70: Single-Core: Performance Speedup
Revelator outperforms the best-performing scheme
by 17% on average when memory is highly fragmented
Speedup over THP
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
Reserve-THP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SpecTLB | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
POM-TLB | 0.99079 | 0.98992 | 0.99369 | 0.98992 | 0.99939 | 0.99939 | 0.98978 | 0.99287 | 0.99371 | 0.99629 | 0.99448 | 0.99365
64K-entry L2 TLB | 1.0319 | 1.0357 | 1.0164 | 1.0357 | 1.046 | 1.046 | 1.0366 | 1.0015 | 1.0274 | 1.0307 | 1.0582 | 1.0332
ASAP | 1.0645 | 1.0337 | 1.0311 | 1.0337 | 1.1195 | 1.1195 | 1.0254 | 1.0481 | 1.128 | 1.023 | 1.0267 | 1.0586
DMT | 1.0681 | 1.0382 | 1.0341 | 1.0382 | 1.1321 | 1.1321 | 1.0294 | 1.0461 | 1.1289 | 1.0254 | 1.03 | 1.0631
ECH | 1.0638 | 1.0275 | 1.0288 | 1.0275 | 1.1253 | 1.1253 | 1.0201 | 1.0298 | 1.1229 | 1.0184 | 0.98698 | 1.0514
Mosaic Pages | 1.0932 | 1.0924 | 1.0415 | 1.0924 | 1.0854 | 1.0854 | 1.0861 | 1.0079 | 1.0734 | 1.0848 | 1.1921 | 1.0842
SpOT | 1.0432 | 1.131 | 1.0902 | 1.131 | 1.0498 | 1.0498 | 1.0891 | 1.1242 | 1.072 | 1.0911 | 1.075 | 1.0856
Revelator | 1.322 | 1.245 | 1.1475 | 1.245 | 1.3263 | 1.3263 | 1.2132 | 1.2257 | 1.3978 | 1.188 | 1.1572 | 1.2517
Revelator+THP | 1.3395 | 1.2489 | 1.15 | 1.2489 | 1.3423 | 1.3423 | 1.217 | 1.1837 | 1.4258 | 1.1906 | 1.1594 | 1.256
Notes: In this plots, [CLICK] we show thatRevelator outperforms the state-of-the-art speculative scheme by 17% on average when memory is highly fragmented.

## Slide 71: Multi-Core: Performance Speedup
Revelator achieves increasing performance speedups (up to 1.5x) against THP with increasing core counts
Notes: In this plots, [CLICK] we show thatRevelator outperforms the state-of-the-art speculative scheme by 17% on average when memory is highly fragmented.

## Slide 72: Area and Power Overhead
We implement the speculation engine in Chisel
and synthesize it with Yosys using
the NanGate 45nm open-source cell library
0.02%
Additional Area
0.0149 mm²
0.03%
Additional Power
14.723 mW static power
Compared with a high-performance
Intel Cascade Lake core
Notes: In this plots, [CLICK] we show thatRevelator outperforms the state-of-the-art speculative scheme by 17% on average when memory is highly fragmented.

## Slide 73: More in the Paper
Analysis on the shortcomings of prior works
Deep dive into Revelator’s performance
Evaluation in NUMA and virtualized systems
Revelator combined with other schemes
Energy reduction achieved by Revelator
Sensitivity to the number of allocation attempts
Cache pollution caused by Revelator
Security implications

## Slide 74: More in the Paper
Synergy with large pages
Revelator in virtualized environments
Revelator in NUMA/CXL-like systems
1
2
3
https://arxiv.org/abs/2508.02007

## Slide 75: Revelator is Open-Source
https://github.com/CMU-SAFARI/Virtuoso
Notes: In this plots, [CLICK] we show thatRevelator outperforms the state-of-the-art speculative scheme by 17% on average when memory is highly fragmented.

## Slide 76
Conclusion

## Slide 77: Revelator: HW/OS Cooperation
Predictable
Physical Location
Tiered Hash-based Allocation
Operating System
Speculation
Engine
Hardware
Hides & reduces address translation latency without depending on memory fragmentation (i.e., large pages, contiguity)
Outperforms all state-of-the-art schemes
in both single-core and multi-core systems
Employ hashing to enable highly accurate speculative
address translation with small system modifications

## Slide 78
Revelator
Rapid Data Fetching
via System-Software-Guided Hash-based
Speculative Address Translation
Konstantinos Kanellopoulos Konstantinos Sgouras
Harsh Songara Andreas Kosmas Kakolyris Vlad-Petru Nitu
Spiros Galanopoulos Rahul Bera Konstantina Koliogeorgi
Rakesh Kumar Onur Mutlu

## Slide 79: Revelator: Allocation Properties
Each allocation attempt is a Bernoulli trial: a slot is free with probability P = L / N
Each request makes k independent hash attempts
Allocation fails only if all k attempts land on taken slots
P(success) = 1 − (L / N)ᵏ
Probability data is allocated with a hash function
L = Number of occupied pages
N = Total number of pages
Number of hash-based allocation attempts
Dependence on memory fragmentation
Allocation bias
1
2
3
Notes: And we conclude that Revelator’s effectiveness..

## Slide 80: Allocation Bias
Chart: Number of Hash-based Allocation Attempts
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
P(success) | 0.5 | 0.75 | 0.875 | 0.9375 | 0.9688 | 0.9844 | 0.9922 | 0.9961
  Sequential hashing biases allocations to succeed toward earlier hash functions
P (Success. alloc.)
Memory Utilization: 50%
High Fragmentation
3
50%
+25%
+12.5%
+6.25%
Notes: And we conclude that Revelator’s effectiveness..

## Slide 81: Example Scenarios of Allocation
VPN
VPN
Low Fragmentation
High Fragmentation
Allocated Early
Allocated Late
VPN
VPN
1
2
3
4

## Slide 82: SpOT [Alverti et al. ISCA 2020]
VMA1
VMA2
VMA3
Physical Memory
Contiguous
Segment
Contiguous
Segment
Contiguous
Segment
Offset
Offset
Offset
VMA1
VMA2
VMA3
Offset1
Offset2
Offset3
Hardware Table
Speculate PA assuming
VMA-Offset mapping is stable

## Slide 83: Limitations of SpOT (1)
SpOT is sensitive to the amount of fragmentation in the system

## Slide 84: Limitations of SpOT (2)
SpOT is sensitive to the number
of allocation contexts

## Slide 85: Limitations of Prior Work (3)
SpOT is sensitive to allocation interference

## Slide 86: Our Goal
Hide address translation latency in modern systems
Without relying on large pages
Without relying on VA-to-PA contiguity
Without costly hardware for metadata

## Slide 87: Revelator: Key Idea
Co-design hardware and OS to perform
highly accurate speculative translation
VPN
OS
HW
Hash Function #1
Hash Function #2
Hash-based allocation limits the potential
PA locations
Translation
Calculate hash-function result, form PA and fetch data
Translation
is resolved
Saved cycles
Hash Function-aware

## Slide 88: OS: Page Allocation Algorithm
PPN
VPN
Hash #1
Direct Mapped
Page is free

## Slide 89: OS: Page Allocation Algorithm
PPN
VPN
Hash #1
Direct Mapped
Page is not free

## Slide 90: OS: Page Allocation Algorithm
PPN
PPN
VPN
Hash #2
Change the seed and try again

## Slide 91: OS: Page Allocation Algorithm
VPN
Hash #N
Change the seed up to N times

## Slide 92: OS: Page Allocation Algorithm
VPN
Hash #N
Change the seed up to N times

## Slide 93: OS: Page Allocation Algorithm
VPN
Hash #N
Change the seed up to N times

## Slide 94: OS: Page Allocation Algorithm
PPN
VPN
Place
Anywhere
Fallback to conventional allocation

## Slide 95: OS: Page Allocation Algorithm
PPN
PPN
PPN
PPN
VPN
Page is not free
Fallback to conventional fault mechanism before N+1
Place at any
free location
Can we allocate the page table in the same way to enable faster pointer-chasing?

## Slide 96: OS: Allocating the Page Table
Null
3rd Level
Page Table
Frame
Hash Function
4th Level
Physical Memory

## Slide 97: OS: Allocating the Page Table
PD
Y
Z
PT
Z
W
Hash(VPN >> 9) = Z
OffsetPT
OffsetPD
Allocate PT
Frame
VPN
… … .
Try the following PPN
Enables overlapping the access to 3rd and 4th level of the walk

## Slide 98: Probability of Successful Allocation
Setup: each VPN allocation attempt = a Bernoulli trial
Trial outcome: success (slot is free) with probability p, failure (collision) with probability 1 − p
Per-slot occupancy: p = L / N, where L = active VPNs, N = total available slots
Trials are independent across the k hash probes (speculation degree)
Probability of successful allocation
All k probes fail (allocation rejected): P(fail) = pᵏ
At least one probe succeeds: P(success) = 1 − pᵏ = 1 − (L / N)ᵏ
Implication: increasing k drives P(success) → 1 exponentially, at the cost of bandwidth contention

## Slide 99: Probability of Successful Allocation

## Slide 100: Revelator: Hardware Side
Hash Function Circuit
Speculation Engine
Seed Generator
.
.
.
Hash1(VPN)
Hash2(VPN)
HashN(VPN)
PID
Memory Hierarchy
Bandwidth consumption is going to explode if N is large

## Slide 101: Speculation Degree Filter
Bandwidth Contention
Hash-Based Allocation Statistics
Hash1
HashN
Hash2
.
.
.
0.6
0.2
0.1
1
1
0
Speculate?
Speculation
degree up to
4 is allowed
Contention Zones
0
1
2
3
4

## Slide 102: Revelator with Large Pages
Try tiered hash-based allocation for 2MB pages
1
Try 2MB allocation via THP
2
Try tiered hash-based allocation for 4KB page
3
Fallback to conventional allocation
4

## Slide 103: Revelator with Large Pages
Try tiered hash-based allocation for 2MB pages
1
Try 2MB allocation via THP
2
Try tiered hash-based allocation for 4KB page
3
Fallback to conventional allocation
4
Leverages available contiguity when possible while maintaining the benefits of hash-based allocation
in the absence of contiguity

## Slide 104: Security Analysis
We do not introduce more vulnerabilities than existing data-dependent prefetchers used in modern processors
Hash1
HashN
Hash2
.
.
.
Correct
Mis-speculation
Mis-speculation
Mis-speculated data can not be used by the CPU as an index
to another data structure -> no new Meltdown/Spectre variants
However, mis-speculated data remain in the caches
-> an attacker can try to leak data

## Slide 105: Security Analysis
# Victim code # The programmer believes the bounds check prevents illegal access. array1 = public_array array2 = probe_array secret = sensitive_data function victim(index): if index < length(array1): value = array1[index] # Use value to touch a location in another array
touch(array2[value])
# This creates a microarchitectural trace, such as a cache effect.

## Slide 106: Security Analysis
touch(array2[value])
Hash1
HashN
Hash2
.
.
.
Threat Model:
Attacker knows the key of the victim and somehow the defender keeps all cache lines of array2 hot but not the TLB ones
Hash1
HashN
Hash2
Side-
Channel
L2 Cache
Iterate over
all values

## Slide 107: Security Analysis
1
Cleanup mis-speculated fetches
If the PTW completes before all data fetches complete, we can cancel them from the MSHRs so that they are not installed in the L2 cache
MMU
log
PTW confirms correct PA
MSHRs
Cancel mis-speculated fetches

## Slide 108: Security Analysis
1
Cleanup mis-speculated fetches
We can cancel 67% of mis-speculated fetches

## Slide 109: Security Analysis
2
What happens with the rest that remain in the caches until they are invalidated?

## Slide 110: Revelator in Virtualized Systems

## Slide 111: Revelator in NUMA

## Slide 112: Bloom-Filter-based Radix Table

## Slide 113: Succesful Allocations
Chart: 
| 10 | 20 | 40 | 80
Hash #1 | 0.704 | 0.64592 | 0.68426 | 0.68352 | 0.68531 | 0.6742 | 0.69997 | 0.68047 | 0.67469 | 0.65803 | 0.62475 | 0.65108 | 0.65175 | 0.61854 | 0.60289 | 0.5862 | 0.59189 | 0.58436 | 0.53641 | 0.46487 | 0.45331 | 0.43179 | 0.41795 | 0.42818
#2 | 0 | 0.23306 | 0.22184 | 0.22448 | 0.22702 | 0.22702 | 0 | 0.22074 | 0.22301 | 0.22906 | 0.23677 | 0.22956 | 0 | 0.23232 | 0.23437 | 0.23584 | 0.23553 | 0.23525 | 0 | 0.2207 | 0.21659 | 0.21017 | 0.20475 | 0.20892
#3 | 0 | 0 | 0.063978 | 0.06418 | 0.062528 | 0.067101 | 0 | 0 | 0.067539 | 0.073831 | 0.08611 | 0.077019 | 0 | 0 | 0.091414 | 0.096526 | 0.094965 | 0.096702 | 0 | 0 | 0.11399 | 0.11405 | 0.11066 | 0.11251
#4 | 0 | 0 | 0 | 0.016079 | 0.016674 | 0.018674 | 0 | 0 | 0 | 0.023494 | 0.031045 | 0.024883 | 0 | 0 | 0 | 0.041372 | 0.039937 | 0.042084 | 0 | 0 | 0 | 0.067342 | 0.067565 | 0.067108
#5 | 0 | 0 | 0 | 0 | 0.0044607 | 0.0051124 | 0 | 0 | 0 | 0 | 0.010865 | 0.0083377 | 0 | 0 | 0 | 0 | 0.017821 | 0.019182 | 0 | 0 | 0 | 0 | 0.045161 | 0.043828
#6 | 0 | 0 | 0 | 0 | 0 | 0.0015843 | 0 | 0 | 0 | 0 | 0 | 0.0031623 | 0 | 0 | 0 | 0 | 0 | 0.0098667 | 0 | 0 | 0 | 0 | 0 | 0.030746
10%
20%
40%
80%
Memory Pressure

## Slide 114: Effect on Allocation Latency

## Slide 115: Effect on Allocation Latency

## Slide 116: Performance Speedup over THP
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
Reserve-THP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SpecTLB | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
POM-TLB | 0.99079 | 0.98992 | 0.99369 | 0.98992 | 0.99939 | 0.99939 | 0.98978 | 0.99287 | 0.99371 | 0.99629 | 0.99448 | 0.99365
64K-entry L2 TLB | 1.0319 | 1.0357 | 1.0164 | 1.0357 | 1.046 | 1.046 | 1.0366 | 1.0015 | 1.0274 | 1.0307 | 1.0582 | 1.0332
ASAP | 1.0645 | 1.0337 | 1.0311 | 1.0337 | 1.1195 | 1.1195 | 1.0254 | 1.0481 | 1.128 | 1.023 | 1.0267 | 1.0586
DMT | 1.0681 | 1.0382 | 1.0341 | 1.0382 | 1.1321 | 1.1321 | 1.0294 | 1.0461 | 1.1289 | 1.0254 | 1.03 | 1.0631
ECH | 1.0638 | 1.0275 | 1.0288 | 1.0275 | 1.1253 | 1.1253 | 1.0201 | 1.0298 | 1.1229 | 1.0184 | 0.98698 | 1.0514
Mosaic Pages | 1.0932 | 1.0924 | 1.0415 | 1.0924 | 1.0854 | 1.0854 | 1.0861 | 1.0079 | 1.0734 | 1.0848 | 1.1921 | 1.0842
SpOT | 1.0432 | 1.131 | 1.0902 | 1.131 | 1.0498 | 1.0498 | 1.0891 | 1.1242 | 1.072 | 1.0911 | 1.075 | 1.0856
Revelator | 1.322 | 1.245 | 1.1475 | 1.245 | 1.3263 | 1.3263 | 1.2132 | 1.2257 | 1.3978 | 1.188 | 1.1572 | 1.2517
Revelator+THP | 1.3395 | 1.2489 | 1.15 | 1.2489 | 1.3423 | 1.3423 | 1.217 | 1.1837 | 1.4258 | 1.1906 | 1.1594 | 1.256
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
 | 0.99745 | 0.99934 | 0.99923 | 0.99934 | 0.99613 | 0.99613 | 0.9998 | 0.99915 | 0.99795 | 0.98944 | 0.99489 | 0.99716
 | 0.99884 | 0.99959 | 0.99936 | 0.99959 | 0.99747 | 0.99747 | 0.99992 | 0.99917 | 0.99852 | 0.99406 | 0.99813 | 0.99837
 | 1.0037 | 0.9982 | 0.99728 | 0.9982 | 1.0036 | 1.0036 | 0.98886 | 0.99246 | 0.99426 | 0.99962 | 0.99968 | 0.99812
 | 1.0374 | 1.0147 | 1.006 | 1.0147 | 1.0442 | 1.0442 | 1.0371 | 1.0013 | 1.0276 | 1.0156 | 1.0007 | 1.022
 | 1.0639 | 1.0286 | 1.0278 | 1.0286 | 1.1169 | 1.1169 | 1.0228 | 1.0479 | 1.1274 | 1.0169 | 1.0165 | 1.055
 | 1.0673 | 1.0287 | 1.0293 | 1.0287 | 1.1272 | 1.1272 | 1.0259 | 1.046 | 1.1281 | 1.0172 | 1.0177 | 1.0576
 | 1.0658 | 1.0264 | 1.0283 | 1.0264 | 1.1222 | 1.1222 | 1.0183 | 1.0298 | 1.1219 | 1.015 | 1.0175 | 1.0531
 | 1.0566 | 1.0055 | 0.99842 | 1.0055 | 1.0552 | 1.0552 | 1.0525 | 1.0012 | 1.0706 | 0.99881 | 1.0139 | 1.0281
 | 1.0668 | 0.92335 | 1.1184 | 0.92335 | 1.0751 | 1.0751 | 1.2156 | 1.5085 | 1.3473 | 0.92563 | 0.99454 | 1.0935
 | 1.2778 | 1.1459 | 1.1 | 1.1459 | 1.2894 | 1.2894 | 1.1758 | 1.2176 | 1.3942 | 1.0938 | 0.98421 | 1.187
 | 1.3575 | 1.2351 | 1.1484 | 1.2351 | 1.4184 | 1.4184 | 1.247 | 1.4047 | 1.5332 | 1.1328 | 0.99996 | 1.2757
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
 | 0.72614 | 0.97513 | 0.95792 | 0.97513 | 0.77515 | 0.77515 | 0.99644 | 0.94664 | 0.74442 | 0.88881 | 0.97066 | 0.87858
 | 0.79853 | 0.9773 | 0.96358 | 0.9773 | 0.77636 | 0.77636 | 0.99932 | 0.94688 | 0.76589 | 0.89409 | 0.97402 | 0.89059
 | 0.99313 | 0.98957 | 1.0038 | 0.98957 | 1.0022 | 1.0022 | 0.98165 | 0.97063 | 0.99961 | 0.98379 | 0.99746 | 0.9921
 | 1.0451 | 1.0232 | 1.0239 | 1.0232 | 1.0844 | 1.0844 | 1.0148 | 1.0496 | 1.0954 | 1.0099 | 1.0142 | 1.0421
 | 1.0012 | 1.0001 | 1.0002 | 1.0001 | 1.0074 | 1.0074 | 1.0001 | 1.0005 | 1.0055 | 1.0001 | 1 | 1.0021
 | 1.0011 | 1 | 1 | 1 | 1.0102 | 1.0102 | 1 | 1 | 1.0024 | 1 | 0.99999 | 1.0022
 | 0.99898 | 0.99978 | 0.99975 | 0.99978 | 1.0071 | 1.0071 | 0.99994 | 0.99965 | 0.99834 | 0.99996 | 0.99993 | 1.0009
 | 0.7702 | 0.81153 | 0.86817 | 0.81153 | 0.79291 | 0.79291 | 0.8239 | 0.59108 | 0.74936 | 0.85893 | 0.98928 | 0.79996
 | 1.1538 | 0.99451 | 1.1419 | 1.1245 | 1.1284 | 1.1836 | 1.0951 | 1.0897 | 1.1289 | 1.1582 | 1.0321 | 1.1106
 | 1.0127 | 0.98283 | 0.9924 | 1.1383 | 1.0506 | 1.0506 | 0.97265 | 1.0649 | 1.0799 | 0.98546 | 1.005 | 0.99669
 | 1.11 | 1.129 | 1.075 | 1.129 | 1.2005 | 1.2005 | 1.1026 | 1.0385 | 1.1855 | 1.0703 | 1.0166 | 1.1127
High Memory Fragmentation (Scarce contiguity)
Medium Memory Fragmentation (Medium availability of contiguity)
Very Low Fragmentation (Maximum contiguity)

## Slide 117: Deep dive into Revelator’s benefits
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
SpOT | 0.8588 | 0.74777 | 0.74158 | 0.74777 | 0.81481 | 0.81481 | 0.90289 | 0.95497 | 0.992 | 0.71271 | 0.20163 | 0.72494
Revelator | 0.92593 | 0.79273 | 0.79059 | 0.79273 | 0.94465 | 0.94465 | 0.929 | 0.98805 | 1.1334 | 0.73989 | 0.18979 | 0.77429
Revelator+THP | 1.1506 | 1.1264 | 1.1279 | 1.1264 | 1.2696 | 1.2696 | 1.0711 | 1.1007 | 1.2255 | 1.0711 | 1 | 1.137
Translation Speedup over THP
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
SpOT | 1.1122 | 0.99269 | 1.4023 | 0.99269 | 1.0996 | 1.0996 | 1.156 | 4.5577 | 1.3599 | 0.96867 | 1.244 | 1.287
Revelator | 1.0835 | 1.3077 | 1.3168 | 1.3077 | 1.2698 | 1.2698 | 1.1013 | 2.6377 | 1.3509 | 1.1368 | 1.2074 | 1.32
Revelator+THP | 1.0978 | 1.3084 | 1.3223 | 1.3084 | 1.3106 | 1.3106 | 1.1272 | 3.0804 | 1.4593 | 1.1251 | 1 | 1.3367
Data Fetching Speedup over THP
Medium Fragmentation
Medium Fragmentation

## Slide 118: Sweeping Memory Utilization
Chart: 
| 0 | 0.2 | 0.4 | 0.6 | 0.8
1 | 1.281 | 1.187 | 1.1132 | 1.0501 | 0.99437
2 | 1.2423 | 1.2167 | 1.1607 | 1.0809 | 0.98789
3 | 1.1851 | 1.1753 | 1.1426 | 1.0763 | 0.97444
4 | 1.1482 | 1.1432 | 1.1235 | 1.0712 | 0.96839
5 | 1.121 | 1.1176 | 1.1052 | 1.0639 | 0.96516
Speedup over THP
Number of Hash Functions:
Memory Utilization

## Slide 119: Ablation Study
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
Revelator-OnlyData | 1.2542 | 1.2191 | 1.1229 | 1.2191 | 1.1984 | 1.1984 | 1.1966 | 1.2036 | 1.249 | 1.1725 | 1.1438 | 1.1973
Revelator-OnlyPT | 1.0405 | 1.018 | 1.0151 | 1.018 | 1.0777 | 1.0777 | 1.0107 | 1.0177 | 1.0828 | 1.0102 | 0.97287 | 1.0305
Revelator-Data+PT | 1.322 | 1.245 | 1.1475 | 1.245 | 1.3263 | 1.3263 | 1.2132 | 1.2257 | 1.3978 | 1.188 | 1.1572 | 1.2517
Speedup over THP

## Slide 120: Bandwidth Filter

## Slide 121: L2 Cache Pollution

## Slide 122: Energy Reduction

## Slide 123: Multicore Environments

## Slide 124: Virtualized Environments

## Slide 125: NUMA

## Slide 126: NUMA Details

## Slide 127: Revelator + ECHT
Chart: 
| BC | BFS | CC | DLRM | GC | GEN | PR | RND | SSSP | TC | XS | GMEAN
ECH | 1.0658 | 1.0264 | 1.0283 | 1.0264 | 1.1222 | 1.1222 | 1.0183 | 1.0298 | 1.1219 | 1.015 | 1.0175 | 1.0531
Revelator | 1.2778 | 1.1459 | 1.1 | 1.1459 | 1.2894 | 1.2894 | 1.1758 | 1.2176 | 1.3942 | 1.0938 | 0.98421 | 1.187
Revelator+ECH | 1.3126 | 1.1561 | 1.1079 | 1.1561 | 1.3371 | 1.3371 | 1.1839 | 1.2291 | 1.4558 | 1.101 | 0.98146 | 1.2075
Speedup over THP

## Slide 128: WayCast: Utopia vs Revelator

## Slide 129: Modularity and Composability
V = Victima T = Trail R = Revelator U = Utopia
Notes: We evaluated different combinations of all schemes