## Slide 1
Revisiting RowHammer: An Experimental Analysis
of Modern DRAM Devices and Mitigation Techniques
Jeremie Kim1,2, Minesh Patel1, A. Giray Yağlıkçı1,
Hasan Hassan1, Roknoddin Azizi1, Lois Orosa1, and Onur Mutlu1,2
6: Characterization Results
7: Evaluation of Mitigation Mechanisms
5: Experimental Methodology
2: The RowHammer Phenomenon
3: Motivation
4: Our Goal
2
1
1: DRAM Background
8: Future Work and Conclusion
  Experimentally demonstrate how vulnerable modern DRAM chips are to RowHammer and predict how this vulnerability will scale going forward
  Examine the viability of current mitigation mechanisms on more vulnerable chips
Denser DRAM chips are more vulnerable to RowHammer
No comprehensive experimental study demonstrating how vulnerability scales across DRAM types and tech node sizes
Unclear whether current mitigation mechanisms will remain viable for future DRAM chips that are likely to be more vulnerable to RowHammer
1580 total chips tested from 300 modules
  Experimental Testing Infrastructures
  DDR3: SoftMC [Hassan+, HPCA’17]
    (Xilinx ML605)
  DDR4: SoftMC [Hassan+, HPCA’17]
    (Xilinx Virtex UltraScale 95)
  LPDDR4: In-house testing hardware
Prevent sources of interference during core test loop
  We disable:
    DRAM refresh: to avoid refreshing victim row
    DRAM calibration events: to minimize variation in test timing
    RowHammer mitigation mechanisms: to observe circuit-level effects
  Test for less than refresh window (32ms) to avoid retention failures
Worst-case access sequence
  We use worst-case access sequence based on prior works’ observations
  For each row, repeatedly access the two directly physically-adjacent rows as fast as possible
Row 0
Row 1
Row 2
Row
Row X-1
Aggressor Row
Row X+1
Aggressor Row
Row X
Victim Row
Conclusion: It is critical to research more effective solutions to RowHammer for future DRAM chips that will likely be even more vulnerable to RowHammer
Future Research Directions
DRAM-system cooperation
A DRAM-based or system-level mechanism alone ignores potential benefits of a holistic solution
2. Profile-guided
Accurately profiling RowHammer-susceptible cells in DRAM provides a powerful substrate for building targeted RowHammer solutions e.g.:
  - Increasing refresh rate: increase refresh rate for rows with RowHammer-susceptible cell
  - Access counters: only count accesses to rows containing RowHammer-susceptible cells
A fast and accurate profiling mechanism is a key research challenge for developing low-overhead and scalable RowHammer solutions
DRAM Bank
Row 1
Row 2
Row 3
Stored data is corrupted if too much charge leaks
(i.e., the capacitor voltage degrades too much)
DRAM cells are refreshed periodically to maintain data correctness
Access
Repeatedly opening (ACT) and closing (PRE)
a DRAM row causes failures in nearby rows
If a nearby row is activated enough times within a refresh window, the charge leakage rate can be accelerated to the point of failure. Some cells require more hammers to fail.
RowHammer bit flip
Increased Refresh Rate: Substantial overhead for high HCfirst values. Prohibitively high refresh rates required for HCfirst < 32k.
PARA: Scales to low HCfirst values, but significantly high performance overheads (e.g., 80% performance loss when HCfirst = 128).
ProHIT
MRLoc: Models for scaling ProHIT and MRLoc for HCfirst < 2k are not provided and how to do so is not intuitive.
TWiCe: Does not support HCfirst < 32k, but we evaluate an ideal version ignoring two critical issues. Ideal performs better than PARA.
Ideal: ideal refresh-based mechanism provides reasonably high normalized system performance across all tested HCfirst values.
Key Takeaways
1. PARA, ProHIT, and MRLoc mitigate RowHammer bit flips in worst chips with reasonable performance (92%, 100%, 100%)
2. Only PARA scales to low HCfirst but has low normalized system performance
3. Ideal mechanism is significantly better
than existing mechanisms for HCfirst < 1024
4. Significant opportunity for developing a scalable and low overhead solution
HCfirst
f) First RowHammer Failure per Chip
In a DRAM type, HCfirst reduces significantly from old to new chips, i.e., DDR3: 69.2k to 22.4k, DDR4: 17.5k to 10k, LPDDR4: 16.8k to 4.8k
In LPDDR4-1y chips from manufacturer A, there are chips whose weakest cells fail after only 4800 hammers
a) RowHammer Vulnerability
Newer DRAM chips are more vulnerable to RowHammer
b) Data Pattern Dependence
Worst-case data pattern is same for chips of same mfg. and type-node cfg
c) Hammer Count Effects
RowHammer bit flip rates increase with technology node generation
e) Spatial Effects
The number of RowHammer bit flips that occur in a given row decreases as the distance from the victim row (row 0) increases
Chips of newer DRAM technology nodes can exhibit RowHammer bit flips 1) in more rows and 2) farther away from the victim row
d) Hammer Count Effects
The distribution of RowHammer bit flip density per word changes in LPDDR4 chips from other DRAM types likely due to on-die ECC
At a bit flip rate of 10-6, a 64-bit word can contain up to 4 bit flips. Even at this very low bit flip rate, a very strong ECC is required to prevent failures
https://www.youtube.com/watch?v=Lqxc4_ToMUw
https://people.inf.ethz.ch/omutlu/pub/Revisiting-RowHammer_isca20.pdf
Full Paper
Full Talk Video
Fraction of 64-bit words containing X bit flips over all 64-bit words containing bit flips
Number of RowHammer bit flips per 64-bit word
Distance from victim row (Row 0)