## Slide 1: SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM
Nastaran Hajinazar* Geraldo F. Oliveira*
Sven Gregorio Joao Ferreira Nika Mansouri Ghiasi
Minesh Patel Mohammed Alser Saugata Ghose
Juan Gómez–Luna Onur Mutlu

## Slide 2: Data Movement Bottleneck
Memory
channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Data movement is a major bottleneck
Bandwidth-limited and power-hungry memory channel
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
More than 60% of the total system energy
is spent on data movement1
2

## Slide 3: Processing-in-Memory (PIM)
Processing-in-Memory: moves computation closer to where the data resides
  Reduces/eliminates the need to move data between processor and DRAM
Memory
channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
3

## Slide 4: Processing-using-Memory (PuM)
PuM: Exploits analog operation principles of the memory circuitry to perform computation
  Leverages the large internal bandwidth and parallelism available inside the memory arrays
A common approach for PuM architectures is to perform bulk bitwise operations
  Simple logical operations (e.g., AND, OR, XOR)
  More complex operations (e.g., addition, multiplication)
4

## Slide 5: Motivation, Goal, and Key Idea
Existing PuM mechanisms are not widely applicable
  Support only a limited and mainly basic set of operations
  Lack the flexibility to support new operations
  Require significant changes to the DRAM subarray
Goal: Design a PuM framework that
  Efficiently implements complex operations
  Provides the flexibility to support new desired operations
  Minimally changes the DRAM architecture
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
5

## Slide 6: SIMDRAM: PuM Substrate
SIMDRAM framework is built around a DRAM substrate that enables two techniques:
(1) Vertical data layout
4-bit element size
Row Decoder
most significant bit (MSB)
least significant bit (LSB)
A
B
Cout
Cin
MAJ
(2) Majority-based computation
Pros compared to the conventional horizontal layout:
Implicit shift operation
Massive parallelism
Cout= AB + ACin + BCin
Pros compared to AND/OR/NOT-based computation:
Higher performance
Higher throughput
Lower energy consumption
6

## Slide 7: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
7

## Slide 8: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
Program
MAJ/NOT logic
Step 1: Generate
MAJ logic
8
Step 1:
Builds an efficient MAJ/NOT representation of a given desired operation from its AND/OR/NOT-based implementation

## Slide 9: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Step 2: Generate
sequence of DRAM
commands
Program
9
Step 2:
Allocates DRAM rows to the operation’s inputs and outputs
Generates the sequence of DRAM commands (Program) to execute the desired operation

## Slide 10: SIMDRAM Framework: Overview
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
Step 3: Execution according to Program
Memory Controller
10
Step 3:
Executes the μProgram to perform the operation
Uses a control unit in the memory controller

## Slide 11: SIMDRAM Framework: Overview
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
New SIMDRAM Program
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of DRAM
commands
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
11

## Slide 12: Key Results
Evaluated on:
  16 complex in-DRAM operations
  7 commonly-used real-world applications
SIMDRAM provides:
88× and 5.8× the throughput of a CPU and a high-end GPU, respectively, over 16 operations
257× and 31× the energy efficiency of a CPU and a high-end GPU, respectively, over 16 operations
21× and 2.1× the performance of a CPU an a high-end GPU, over seven real-world applications
12

## Slide 13: Conclusion
SIMDRAM:
  Enables efficient computation of a flexible set and wide range of operations in a PuM massively parallel SIMD substrate
  Provides the hardware, programming, and ISA support, to:
    Address key system integration challenges
    Allow programmers to define and employ new operations without hardware changes
More in the paper:
  Efficiently transposing data
  Programming interface
  Handling page faults, address translation, coherence, and interrupts
  Security implications
  Reliability evaluation
  Comparison to in-cache computing
  And more …
13
  SIMDRAM is a promising PuM framework
  Can ease the adoption of processing-using-DRAM architectures
  Improve the performance and efficiency of processing-using-DRAM architectures

## Slide 14: SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM
Nastaran Hajinazar* Geraldo F. Oliveira*
Sven Gregorio Joao Ferreira Nika Mansouri Ghiasi
Minesh Patel Mohammed Alser Saugata Ghose
Juan Gómez–Luna Onur Mutlu