## Slide 1: SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM
Nastaran Hajinazar* Geraldo F. Oliveira*
Sven Gregorio Joao Ferreira Nika Mansouri Ghiasi
Minesh Patel Mohammed Alser Saugata Ghose
Juan Gómez–Luna Onur Mutlu

## Slide 2
Motivation: Processing-using-Memory (PuM) architectures can efficiently perform bulk bitwise computation
Problem: Existing PuM architectures are not widely applicable
  Support only a limited and specific set of operations
  Lack the flexibility to support new operations
  Require significant changes to the DRAM subarray
Goals: Design a processing-using-DRAM framework that:
  Efficiently implements complex operations
  Provides the flexibility to support new desired operations
  Minimally changes the DRAM architecture
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations
  Providing the ability to implement arbitrary operations as required
  Using a massively-parallel in-DRAM SIMD substrate that requires minimal changes to DRAM
Key Results: SIMDRAM provides:
  88x and 5.8x the throughput and 257x and 31x the energy efficiency of a baseline CPU and a high-end GPU, respectively, for 16 in-DRAM operations
  21x and 2.1x the performance of the CPU and GPU for seven real-world applications
Executive Summary
2

## Slide 3: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 4: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 5: Data Movement Bottleneck
Memory
channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Data movement is a major bottleneck
Bandwidth-limited and power-hungry memory channel
5
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
More than 60% of the total system energy
is spent on data movement1

## Slide 6: Processing-in-Memory (PIM)
Processing-in-Memory: moves computation closer to where the data resides
  Reduces/eliminates the need to move data between processor and DRAM
Memory
channel
DRAM
Computing Unit
(CPU, GPU, FPGA, Accelerators)
6

## Slide 7: Processing-using-Memory (PuM)
PuM: Exploits analog operation principles of the memory circuitry to perform computation
  Leverages the large internal bandwidth and parallelism available inside the memory arrays
A common approach for PuM architectures is to perform bulk bitwise operations
  Simple logical operations (e.g., AND, OR, XOR)
  More complex operations (e.g., addition, multiplication)
7

## Slide 8: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 9: Inside a DRAM Chip
Access
Transistor
Storage
Capacitor
Bitline
Wordline
Wordline
Bitline
Subarray
(2D Array of DRAM Cells)
Sense Amplifiers
DRAM Module
DRAM Chips
DRAM Bank
DRAM Cells
8
Row Buffer

## Slide 10: DRAM Cell Operation
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
9

## Slide 11: DRAM Cell Operation - ACTIVATE
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
½ VDD
1. Raise wordline
2. Capacitor shares charge with bitline
4. Amplify deviation
in the bitline
+ δ
3. Enable
sense amplifier
VDD
5. Capacitor charge is restored
10
6. Row buffer stores the cell value

## Slide 12: DRAM Cell Operation – READ/WRITE
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
Read/Write the value
latched in sense amplifier
11
VDD

## Slide 13: DRAM Cell Operation - PRECHARGE
1. ACTIVATE (ACT)
2. READ/WRITE
3. PRECHARGE (PRE)
wordline
bitline
sense
amplifier
enable
storage
capacitor
access
transistor
VDD
½ VDD
2. Precharge bitline for next access
1. Lower
wordline
3. Disable
sense amplifier
12

## Slide 14: In-DRAM Row Copy
sense
amplifier
enable
½ VDD
Source row A
Destination row B
13
1. ACT
2. ACT
3. PRE
Row copy
command sequence2:
2 V. Seshadri et al., “RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization", MICRO, 2013
bitline

## Slide 15: In-DRAM Row Copy: RowClone
bitline
½ VDD
1. ACTIVATE source row A
Bitline pulled
to value of row A
VDD
2. ACTIVATE destination row B
Charge level of source row A copied to destination row B
14
3. PRECHARGE bitline
for next access
½ VDD
2 V. Seshadri et al., “RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization", MICRO, 2013
1. ACT
2. ACT
3. PRE
Row copy
command sequence2:
sense
amplifier
enable
Source row A
Destination row B

## Slide 16: Triple-Row Activation
bitline
sense
amplifier
enable
½ VDD
A
B
C
15
1. ACT
2. PRE
Majority function
command sequence3:
3 V. Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology", MICRO, 2017

## Slide 17: Majority Function
bitline
sense
amplifier
enable
½ VDD
A
B
C
1. ACTIVATE three rows simultaneously
→ triple-row activation
Bitline will be pulled
to VDD
VDD
Values in cells A, B, C overwritten with
the majority output
16
1. ACT
2. PRE
Majority function
command sequence3:
3 V. Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology", MICRO, 2017
2. PRECHARGE bitline
for next access
½ VDD
MAJ(A, B, C ) = MAJ(VDD, VDD, 0) = VDD

## Slide 18: Ambit: In-DRAM Bulk Bitwise AND/OR
bitline
sense
amplifier
enable
A
B
C
½ VDD
17
V. Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology", MICRO, 2017
MAJ (A, B, 0) = AND (A, B)
MAJ (A, B, 1) = OR (A, B)

## Slide 19: Ambit: Subarray Organization
Sense amplifiers
Compute rows
Control rows
Data rows
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Regular
row decoder
Compute
row decoder
Address A
18
V. Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology", MICRO, 2017
DRAM subarray

## Slide 20: Ambit: Subarray Organization
Sense amplifiers
Compute rows
Control rows
Data rows
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Regular
row decoder
Bitwise decoder
Address A
18
V. Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology", MICRO, 2017
DRAM subarray
Less than 1% of overhead
in existing DRAM chips

## Slide 21: PuM: Prior Works
19
DRAM and other memory technologies that are capable of performing computation using memory
Shortcomings:
Support only basic operations (e.g., Boolean operations, addition)
  Not widely applicable
Support a limited set of operations
  Lack the flexibility to support new operations
Require significant changes to the DRAM
  Costly (e.g., area, power)

## Slide 22: PuM: Prior Works
20
DRAM and other memory technologies that are capable of performing computation using memory
Shortcomings:
Support only basic operations (e.g., Boolean operations, addition)
  Not widely applicable
Support a limited set of operations
  Lack the flexibility to support new operations
Require significant changes to the DRAM
  Costly (e.g., area, power)
Need a framework that aids general adoption of PuM, by:
- Efficiently implementing complex operations
- Providing flexibility to support new operations

## Slide 23: Our Goal
Goal: Design a PuM framework that
  Efficiently implements complex operations
  Provides the flexibility to support new desired operations
  Minimally changes the DRAM architecture
21

## Slide 24: Outline
  SIMDRAM Framework
  Processing-using-DRAM Substrate
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion

## Slide 25: Key Idea
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
23

## Slide 26: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 27: SIMDRAM: PuM Substrate
SIMDRAM framework is built around a DRAM substrate that enables two techniques:
(1) Vertical data layout
4-bit element size
Row Decoder
most significant bit (MSB)
least significant bit (LSB)
A
B
Cout
Cin
MAJ
(2) Majority-based computation
Pros compared to the conventional horizontal layout:
Implicit shift operation
Massive parallelism
Cout= AB + ACin + BCin
Pros compared to AND/OR/NOT-based computation:
Higher performance
Higher throughput
Lower energy consumption
25

## Slide 28: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 29: SIMDRAM Framework
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
27
New SIMDRAM Program
Program

## Slide 30: SIMDRAM Framework: Step 1
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
28
New SIMDRAM Program
Program

## Slide 31
Step 1: Naïve MAJ/NOT Implementation
A
B
Cin
Cout
Part 1
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
A
B
C
A
B
C
output is “1” only when A = B = “1”
  output is “0” only when A = B = “0”
Naïvely converting AND/OR/NOT-implementation to MAJ/NOT-implementation leads to an unoptimized circuit
29
MAJ
A
B
C
0
MAJ
A
B
C
1

## Slide 32
Step 1: Efficient MAJ/NOT Implementation
Part 2
Step 1 generates an optimized
MAJ/NOT-implementation of the desired operation
A
B
Cout
Cin
MAJ
Greedy
optimization
algorithm4
4 L. Amarù et al, “Majority-Inverter Graph: A Novel Data-Structure and Algorithms for Efficient Logic Optimization”, DAC, 2014.
30
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1

## Slide 33: SIMDRAM Framework: Step 2
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
31
New SIMDRAM Program
Program

## Slide 34: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
32

## Slide 35: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
33

## Slide 36: Task 1: Allocating DRAM Rows to Operands
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
regular
row decoder
Compute
Row decoder
subarray organization
Constraint 1:
Limited number of rows reserved for computation
34
Allocation algorithm considers two constraints specific to processing-using-DRAM
Compute
rows

## Slide 37: Task 1: Allocating DRAM Rows to Operands
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
regular
row decoder
Compute
Row decoder
subarray organization
Constraint 2:
Destructive behavior
of triple-row activation
35
Overwritten with MAJ output
Allocation algorithm considers two constraints specific to processing-using-DRAM

## Slide 38: Task 1: Allocating DRAM Rows to Operands
A
B
Cout
Cin
MAJ
Allocation
algorithm
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
36
Allocation algorithm:
Triple-row activation
Cout
Cout
Cout
Assigns as many inputs as the number of free compute rows
All three input rows contain the MAJ output and can be reused

## Slide 39: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
Task 1: Allocate DRAM rows to the operands
Task 2: Generate µProgram
37

## Slide 40: Task 2: Generate an initial µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
38
Initial µProgram

## Slide 41: Task 2: Optimize the µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
39
Initial µProgram
2. Optimize

## Slide 42: Task 2: Optimize the µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
40
Coalesce
row copies
Initial µProgram
2. Optimize

## Slide 43: Task 2: Optimize the µProgram
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
41
Merge
MAJ + row copy
Initial µProgram
2. Optimize

## Slide 44: Task 2: Optimize the µProgram
1. Copy A to reserved row (ACT/ACT/PRE)
2. Copy B to reserved row (ACT/ACT/PRE)
3. Copy Cin to reserved row
(ACT/ACT/PRE)
4. Execute MAJ
(ACT/PRE)
5. Copy Cout to destination row (ACT/PRE)
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
42
Initial µProgram
Coalesce
row copies
Merge
MAJ + row copy
Optimized µProgram
2. Optimize

## Slide 45: Task 2: Generate N-bit Computation
A
B
Cout
Cin
MAJ
A
B
Cout
Cin
MAJ
1. Generate
µProgram
3. Generate N-bit
computation
43
Repeat N times:
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Final µProgram
Repeat N times:
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Final µProgram is optimized and computes the desired operation for operands of N-bit size in a bit-serial fashion
2. Optimize
Optimized µProgram

## Slide 46: Task 2: Generate µProgram
44
Repeat N times:
Copy A, B, Cin
to reserved rows
(ACT/ACT/PRE)
2. Execute MAJ and
copy Cout to destination row
(ACT/ACT/PRE)
Stored in a reserved DRAM region
for future use
A new SIMDRAM instruction (called bbop_new)
added to CPU ISA
Final µProgram
Final µProgram is optimized and computes the desired operation for operands of N-bit size in a bit-serial fashion

## Slide 47: SIMDRAM Framework: Step 3
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
45
New SIMDRAM Program
Program

## Slide 48: Step 3: µProgram Execution
SIMDRAM control unit: handles the execution of the µProgram at runtime
Upon receiving a bbop instruction, the control unit:
  Loads the µProgram corresponding to SIMDRAM operation
  Issues the sequence of DRAM commands (ACT/PRE) stored in the µProgram to SIMDRAM subarrays to perform the in-DRAM operation
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
46

## Slide 49: More in the Paper
Detailed reference implementation and microarchitecture of the SIMDRAM control unit
…
…
Op 0
Op 63
Op 62
1024
Program
Scratchpad
+1
bbop_op
/
…
Op 0
Op 1
Op 63
PC
16
Op Proccessing
FSM
branch
target
AAP/AP
Op Memory
shift
amount
1
size
dst, src_1, src_2, n
Program
Op
decrement
is_zero
reg dst.
reg src.
1024
Loop
Counter
bbop
FIFO
Register
Addressing Unit
Register File
…
Op 0
Op 63
Op 62
…
Op 0
Op 63
Op 62
From Program
Memory
From
CPU
To Memory
Controller
2
3
4
5
6
7
47

## Slide 50: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 51: System Integration
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework
49

## Slide 52: System Integration
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework
50

## Slide 53: Transposing Data
51
SIMDRAM operates on vertically-laid-out data
Other system components expect data to be laid out horizontally
Challenging to share data between SIMDRAM and CPU

## Slide 54: Transposition Unit
Last–Level Cache
Transposition Unit
Memory Controller
Object Tracker (OT)
Fetch Unit
Vertical → Horizontal
Transpose
Transpose Buffer
Store Unit
Horizontal → Vertical
Transpose
Transpose Buffer
52
Transforms the data layout from horizontal to vertical, and vice versa

## Slide 55: Efficiently Transposing Data
Last–Level Cache
Transposition Unit
Memory Controller
Object Tracker (OT)
Fetch Unit
Vertical → Horizontal
Transpose
Transpose Buffer
Store Unit
Horizontal → Vertical
Transpose
Transpose Buffer
Low impact on the throughput of
SIMDRAM operations
Low area cost (0.06 mm2 in 22nm tech. node)
53

## Slide 56: More in the Paper
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework
54

## Slide 57: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 58: Methodology: Experimental Setup
Simulator: gem5
Baselines:
  A multi-core CPU (Intel Skylake)
  A high-end GPU (NVidia Titan V)
  Ambit: a state-of-the-art in-memory computing mechanism
Evaluated SIMDRAM configurations (all using a DDR4_2400_x64 device):
  1-bank: SIMDRAM exploits 65’536 SIMD lanes (an 8 kB row buffer)
  4-banks: SIMDRAM exploits 262’144 SIMD lanes
  16-banks: SIMDRAM exploits 1’048’576 SIMD lanes
56

## Slide 59: Methodology: Workloads
Evaluated:
16 complex in-DRAM operations:
  Absolute - Predication
  Addition/Subtraction - ReLU
  BitCount - AND-/OR-/XOR-Reduction
  Equality/ Greater/Greater Equal - Division/Multiplication
7 real-world applications
  BitWeaving (databases) - LeNET (neural networks)
  TPH-H (databases) - VGG-13/VGG-16 (neural networks)
  kNN (machine learning) - Brightness (graphics)
57

## Slide 60: Throughput Analysis
Chart: Average Normalized Throughput (GOPS/s) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 5.5 | 0.36 | 1.98
SIMDRAM - 4 Banks | 22 | 1.5 | 7.9
SIMDRAM - 16 Banks | 88.01 | 5.82 | 31.61
SIMDRAM significantly outperforms
all state-of-the-art baselines for a wide range of operations
58
Average normalized throughput across all 16 SIMDRAM operations

## Slide 61: Energy Analysis
Average normalized energy efficiency across all 16 SIMDRAM operations
Chart: Average Energy Efficiency (GOPS/s/Watt) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 257 | 31 | 2.6
SIMDRAM - 4 Banks | 257 | 31 | 2.6
SIMDRAM - 16 Banks | 257 | 31 | 2.6
SIMDRAM is more energy-efficient than
all state-of-the-art baselines for a wide range of operations
59

## Slide 62: Real-World Applications
Chart: Average Speedup -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 3 | 0.30612 | 2.5
SIMDRAM - 4 Banks | 8.7 | 0.88776 | 7.25
SIMDRAM - 16 Banks | 21 | 2.1429 | 17.5
SIMDRAM effectively and efficiently accelerates
many commonly-used real-world applications
60
Average speedup across 7 real-world applications

## Slide 63: More in the Paper
Evaluation:
  Reliability
  Data transposition overhead
  Area overhead
  Comparison to in-cache computing
  And more …
61

## Slide 64: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 65
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations
  Providing the ability to implement arbitrary operations as required
  Using a massively-parallel in-DRAM SIMD substrate
Key Results: SIMDRAM provides:
  88x and 5.8x the throughput and 257x and 31x the energy efficiency of a baseline CPU and a high-end GPU, respectively, for 16 in-DRAM operations
  21x and 2.1x the performance of the CPU and GPU for seven real-world applications
Conclusion: SIMDRAM is a promising PuM framework
  Can ease the adoption of processing-using-DRAM architectures
  Improve the performance and efficiency of processing-using-DRAM architectures
Conclusion
63

## Slide 66: SIMDRAM: A Framework for Bit-Serial SIMD Processing using DRAM
Nastaran Hajinazar* Geraldo F. Oliveira*
Sven Gregorio Joao Ferreira Nika Mansouri Ghiasi
Minesh Patel Mohammed Alser Saugata Ghose
Juan Gómez–Luna Onur Mutlu