## Slide 1: Formal Supervisory Control and Coordination for Many-core Systems Resource Management
Amir M. Rahmani Bryan Donyanavard Tiago Mück Kasra Moazzemi
Axel Jantsch Onur Mutlu Nikil Dutt
SPECTR
23rd ACM International Conference on Architectural Support for Programming Languages and Operating Systems Williamsburg, VA, March 2018
Notes: Thank you for the introduction. Today, I will present our work about …

## Slide 2: Executive Summary
  Motivation:
    Formal supervisory control theory (SCT) can combine the strengths of classical control theory with heuristic approaches to efficiently meet changing runtime goals.
    SCT enables hierarchical control and facilitates automatic synthesis of the high-level supervisory controller and its property verification.
Problem: Current resource management techniques do not offer 1) robustness, 2) formalism, 3) efficiency, 4) coordination, 5) scalability, and 6) autonomy all together.
Goal: Address all six key challenges in heterogeneous multiprocessors (HMPs) resource management, in particular scalability and autonomy
Our Proposal: SPECTR uses SCT techniques such as gain scheduling to allow autonomy for individual controllers, and modular decomposition of control problems to manage complexity.
Evaluation:
    We implement SPECTR on an Exynos platform containing ARM’s big.LITTLE-based HMP
    SPECTR can manage multiple interacting resources (e.g., chip power and processing cores) in the presence of competing objectives (e.g., satisfying QoS vs. power capping)
    SPECTR achieves up to 8x and 6x better target QoS and power tracking over state-of-the-art, respectively (in our case study).
Notes: To begin, I will give a brief overview. [CLICK] Our motivation is that we can [CLICK] authenticate a system via unique signatures if we can evaluate a Physical Unclonable Function (PUF) on it. [CLICK] These signatures or PUF responses reflect inherent properties of a device making it unique to the DRAM device generating it. [CLICK] DRAM memory technology is widely used today and has significantly many units that can be used in PUF evaluation, which makes it a promising substrate to evaluate PUFs on. A DRAM PUF would enable you to authenticate any system with a DRAM device on it. [CLICK] The main problem is that current DRAM PUFs are either slow, taking on the order of minutes to evaluate, require a DRAM reboot, or require additional custom hardware and cannot be used on commodity DRAM devices. [CLICK] To this end the goal of this work is to develop a novel and effective PUF for commodity DRAM devices that can be evaluated with low latency and low system interference across all operating temperatures. [CLICK] Our key idea is to reduce DRAM read access latency below the reliable datasheet specifications using software-only system calls in order to exploit the resulting error patterns as unique identifiers. We can do this because we observe that we get reliable and consistent error patterns as a result that can be used as a PUF responses [CLICK] We experimentally characterize 223 real LPDDR4 DRAM devices, and show that DRAM latency PUFs satisfy the requirements of an effective PUF [CLICK] We also find that the DRAM latency PUF can be evaluated in 88.2 ms on average regardless of temperature. Since the evaluation time of prior DRAM PUFs depends on temperature, there is a large tradeoff space. However, we determine that we still achieve a speedup orders of magnitude larger than the prior DRAM PUF proposals at common operating temperatures.

## Slide 3: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 4: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 5
Several conflicting goals/constraints
Multiple tunable knobs
Ad hoc heuristics
  Can be sub-optimal
  No formal methodology
  No guarantees
Resource Management in Many-core Systems
Notes: Amir

## Slide 6: Challenges in Resource Management
Major on-chip resource management approaches and the key questions they address (∗ = partially addressed)
 | Methods | Robustness | Formalism | Efficiency | Coordination | Scalability | Autonomy
A | Machine learning |  | ✔ | ✔ | ✔ |  | 
B | Estimation/Model based heuristics |  |  | ✔ | ✔ |  | 
C | SISO Control Theory | ✔ | ✔ | ✔ |  | ✹ | 
D | MIMO Control Theory | ✔ | ✔ | ✔ | ✔ |  | 
E | Supervisory Control Theory [SPECTR] | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
Guaranteed coordination of multiple conflicting goals has been recently addressed for single-core systems via MIMO control theory [ISCA’16].
  What if goal changes at runtime (Autonomy)?
  Can we offer a systematic design flow for hierarchical control (Scalability)?
The Goal
Notes: [CLICK] A PUF is a function that generates a signature that is unique to a given device. [CLICK] PUFs are often used in a challenge-response protocol where [CLICK] a trusted server issues a set of input parameters to a device, and the device generates the PUF response depending on the input parameters. [CLICK] The trusted server then receives the PUF response and can authenticate the device.

## Slide 7: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 8
Benefits:
Simultaneously and robustly track multiple objectives
MIMO Control Theory for Coordination
Notes: Amir

## Slide 9
Benefits:
Simultaneously and robustly track multiple objectives
Shortcomings:
The goal is fixed at design-time
MIMO Control Theory for Coordination
The weighted Tracking Error Cost matrix is fixed.
FPS:Power <= 1:10
when Maximizing FPS under a Power cap
Notes: Amir

## Slide 10
Benefits:
Simultaneously and robustly track multiple objectives
Shortcomings:
The goal is fixed at design-time
Does NOT scale when having several control inputs and measured outputs.
MIMO Control Theory for Coordination
Notes: Amir

## Slide 11: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 12
The Autonomy Challenge: An Example
What if the goal changes at runtime?
We need the ability to switch modes at runtime
A MIMO controller designed with higher priority on QoS over power
Power is capped.
QoS is not met!
QoS is met.
Power violation!
A MIMO controller designed with higher priority on power over QoS
Notes: Amir

## Slide 13
System
(x)
Black-box Identification of System Dynamics
The Scalability Challenge: Example 1
What if the # control inputs and measured outputs is large?
Notes: Amir

## Slide 14
We need to limit the system size
System for 2 x 2 MIMO
A set of workloads
A set of workloads
The Scalability Challenge: Example 1
Prediction is very accurate
Prediction greatly diverges from reality
F level 1
F level N
1 core is active
All cores are active
Notes: Amir

## Slide 15
What if the # control inputs and measured outputs is large?
System
(x)
Controller
The Scalability Challenge: Example 2
Controller Design Complexity
Notes: Amir

## Slide 16
Using one large controller is not feasible!
The Scalability Challenge: Example 2
How many operations are executed in each control epoch for a single large MIMO controlling N cores?
Notes: Amir

## Slide 17: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 18
Using Supervisory Control Theory, we…
Provide autonomy via adaptation in response to changes in policy
  Compute control parameters for different policies offline
Provide scalability via decomposition of system into multiple subsystems organized in a hierarchy
  Supervisor provides high-level management
SPECTR
Notes: Amir

## Slide 19
Scalability via Supervisory Control
High-level
Plant Model (Phi)
Plant (Plo)
Supervisory Controller (Chi)
Low-level Controller (Clo)
Comhi_lo
Conlo
Inflo
Inflo_hi
Conhi
Infhi
High-level Virtual Control
Combining logic with discrete dynamics
Low-level Traditional Control Loop
Represents an abstraction of the Plant
Information channel to update the high-level model
Supervisory Controller uses this channel to control the high-level model
The actual control happens via discrete event-based commands
Notes: Amir

## Slide 20
Autonomy via Supervisory Control
This SCT technique is called Gain Scheduling
FPS:Power <= 1:10
FPS:Power <= 10:1
Control parameters pre-designed to prioritize one measured output over the other(s)
Tracking power is 10x more important than tracking QoS
Tracking QoS is 10x more important than tracking power
Notes: Amir

## Slide 21: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 22
Sub-plant 1
Sub-plant 2
Sub-plant N
Supervisory Controller
Variable Goals and Policies
High-level Plant Model
Classic Controller 1
Classic Controller 2
Classic Controller N
User inputs
Con_lo1
Inf_lo1
Con_lo2
Inf_lo2
Con_loN
Inf_loN
Gains1
Refs1
Gains2
Refs2
GainsN
RefsN
…
…
…
…
Con_hi
Inf_hi
Inf_lo_hi
Leaf Controllers
Physical Plant
System events
SPECTR
SPECTR overview
Putting hierarchical control
and gain scheduling together!
The supervisor updates goals
and allocates resources at runtime
Notes: Kasra

## Slide 23: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 24
8-core big.Little HMP
Two set of applications:
  A foreground application with QoS requirements (e.g., FPS)
  A number of background applications with no QoS requirements
Case Study
ODROID-XU3 platform contains an Exynos 5422 Octa-core SoC
Notes: Tiago

## Slide 25
Control knobs: per-cluster DVFS, number of idle cores
System goals:
  Meet the QoS requirement of the foreground application
  Ensure the total system power always remains below the Thermal Design Power (TDP)
  Minimize energy consumption
Case Study
Notes: Tiago

## Slide 26: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 27
5 steps to design and verify a supervisor:
Supervisory
Controller
Supervisor Synthesis Process
Notes: Donny

## Slide 28
Supervisory
Controller
Step 1: Plant Model
Manually modeled sub-plants
Synthesized plant
Multiple characteristics are automatically synthesized using SCT tools
E.g. Supremica
To develop possible actions in high-level plant model in a form of discrete-event dynamics
Prioritize QoS: The power reference is updated to meet the QoS reference in an energy-efficient manner.
Power budget violation generates a critical event and results in gain switching towards the power-driven goal.
Notes: Donny

## Slide 29
Supervisory
Controller
Step 2: Intended Behavior Specification
Forbidden State
A specification defines the accepted and forbidden states via restrictions on the behavior of the plant model.
This example specification prevents exceeding the power budget for no more than three control intervals.
Note: The model in Step 1 has no limitations!
(e.g., on exceeding the power budget)
Notes: Donny

## Slide 30
Supervisory
Controller
Steps 3-5: Synthesis and Verification
The synthesizer generates a minimally-restrictive controller for the given plant model and specifications.
Automatically generated and verified using synchronous composition operations in Supremica SCT tool.
Notes: Donny

## Slide 31
Supervisory
Controller
Steps 3-5: Synthesis and Verification
SCT tools (e.g., Supremica) also verify the non-blocking and controllability properties of the synthezied controller.
Non-blocking: Accepted states (e.g., ideal states) can always be reached.
Stable
Controllability: There is a path to the accepted states from every other valid state.
Notes: Donny

## Slide 32: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 33
QoS applications:
  PARSEC applications: x264, bodytrack, canneal, streamcluster
  Data-intensive machine learning workloads: k-means, KNN, least squares, linear regression
Compared SPECTR with three alternative resource managers
  MM-Pow: 2x2 MIMOs (one per cluster) with gains optimized to track power
  MM-Perf: 2x2 MIMOs (one per cluster) with gains optimized to track performance/QoS
  FS: single system-wide 4x2 MIMO with gains optimized towards power
Evaluated resource manager configurations
Fixed-Objective
Notes: Tiago

## Slide 34
Execution scenario with three phases (x264):
Phase 1 - Safe Phase:
  only the QoS application runs; power limited by TDP
Phase 2 - Emergency phase:
  power limit set to 1W below TDP to emulate a thermal emergency
Phase 3 - Workload disturbance phase:
  power limit restored to TDP, but now several background tasks start, interfering with the QoS application
Experimental Results – Contoller Evaluation
Enough power to track QoS
Only feasible to track power
Track QoS under a power cap
MM-Pow
MM-Perf
MM-FS
SPECTR
Notes: Tiago

## Slide 35
QoS task: x264
Controller: MM-Pow (power-oriented)
  2x2 MIMOs (one per cluster) with gains optimized to track power
Experimental Results -- Contoller Evaluation
~ 40% more then necessary FPS in Phase 1
Wasting energy !
Under a power cap
Wasted performance
It works fine in Phase 2 and 3 by focusing on power capping!
Notes: Tiago

## Slide 36
Exceeds TDP by ~30% in Phase 3!
Tracking FPS
Exceeding power limit
Experimental Results -- Contoller Evaluation
QoS task: x264
Controller: MM-Perf (performance-oriented)
  2x2 MIMOs (one per cluster) with gains optimized to track QoS
It works fine in Phase 1 and 2 by focusing on QoS tracking!
Notes: Tiago

## Slide 37
QoS task: x264
Controller: FS (large 4x2 power-oriented)
  Single system-wide 4x2 MIMO with gains optimized towards power
~ 40% more than necessary FPS in phase 1 (akin to MM-POW)
Sluggish response
Wasted performance
Experimental Results -- Contoller Evaluation
Longer settling time due to large MIMO controller.
Notes: Tiago

## Slide 38
QoS task: x264
Controller: SPECTR
Let’s Take a closer look at each phase
Experimental Results -- Contoller Evaluation
Notes: Tiago

## Slide 39
Safe Phase: QoS App only
SPECTR focuses on satisfying FPS with the minimum power
<5% FPS steady state error (minimal wasted perfomance)
Power below TDP
Experimental Results -- Contoller Evaluation
Notes: Tiago

## Slide 40
Emergency Phase: TDP reduced in response to thermal event
SPECTR satisfies the reference FPS and power
<5% FPS steady state error
Experimental Results -- Contoller Evaluation
Notes: Tiago

## Slide 41
Disturbance Phase: TDP returned to normal, background tasks added
SPECTR focuses on power capping
No TDP violations, but ~23% FPS steady state error
(impossible to track without violating TDP)
Experimental Results -- Contoller Evaluation
Notes: Tiago

## Slide 42
A detailed Contoller Evaluation on:
  PARSEC applications: bodytrack, canneal, streamcluster
  Data-intensive machine learning workloads: k-means, KNN, least squares, linear regression
Model Accuracy Analysis of different sized MIMO controllers:
  2x2 -> feasible and efficient
  4x2 -> feasible but sluggish
  10x10 -> not feasible
Further discussion on:
  Controller responsiveness (settling time)
  Controller stability
Other Results in the Paper

## Slide 43: SPECTR Outline
Motivation
MIMO Control Theory for Coordinated Management
Unaddressed Challenges in Resource Management
  Autonomy
  Scalability
Supervisory Control Theory (SCT) via SPECTR
  Scalability and Autonomy through SCT
  SPECTR Overview
  Case Study
Case Study
Results
Summary
Supervisor Synthesis Process
Summary
Results

## Slide 44
Resource managers need to offer 1) robustness, 2) formalism, 3) efficiency, 4) coordination, 5) scalability, and 6) autonomy all together
SPECTR offers them all!
  SPECTR adapts to changing goals at rutime
  SPECTR decomposes the control problems to manage its complexity
SPECTR achieves up to 8x and 6x better target QoS and power tracking over state-of-the-art, respectively (in our case study)
SPECTR is applicable to any resource type and objective as long as the management problem can be modeled using dynamical systems theory
Summary
Notes: Amir

## Slide 45: Formal Supervisory Control and Coordination for Many-core Systems Resource Management
Amir M. Rahmani Bryan Donyanavard Tiago Mück Kasra Moazzemi
Axel Jantsch Onur Mutlu Nikil Dutt
SPECTR
23rd ACM International Conference on Architectural Support for Programming Languages and Operating Systems Williamsburg, VA, March 2018
Notes: Thank you for the introduction. Today, I will present our work about …

## Slide 47
Accuracy of the identified system models of different sized MIMO controllers
A model output within the confidence interval indicates that the deterministic component of the model output will be near the true output.
Experimental Results -- Scalability
Confidence level of 99%
Confidence level of 99%
Outside the confidence interval
Black-box system identification is not feasible
for large and complex MIMO systems!
Within the confidence interval
Notes: Kasra

## Slide 48
Step 1
Step 2
Step 3
Step 4
Step 9
Step 6
Step 5
Step 7
Step 8
SPECTR Design Flow
Notes: Kasra

## Slide 49
Steady-state Error for All Benchmarks
Steady-state error for all benchmarks, grouped by phase. A negative value indicates the amount of power/QoS exceeding the reference value (bad), a positive value indicates the amount of power saved (good) or QoS degradation (bad)

## Slide 50
Model Accuracy
Autocorrelation of residuals for identified system models of different sized MIMO controllers.
We show a single performance and power output for each modeled system across multiple sample inputs.